## Slide 1: Greening Hydrogen
Friedrich Sayn-Wittgenstein, Grace Frascati, Hoshi Ogawa, Nadine Palmowski, Ellie Valencia, Linfei Zhang, Hyae Ryung Kim, and Gernot Wagner
12 December 2024

## Slide 2: H2 Sector Overview

## Slide 3
For hydrogen using renewable energy to be truly green, electricity generation needs to be additional, localized, and time aligned to effectively reduce emissions.
Hydrogen (H2) is a gaseous energy molecule that functions as a fuel source to produce electricity and heat. It also serves as an input for chemical processes―for example, in refining.
Global H2 demand today remains low at ~100 Mt in 2022, accounting for less than 1% of the global energy mix. And while there are three types of H2, most of this demand is met by grey H2, the most carbon-intensive option.
            Grey H2 is produced using natural gas and therefore produces significant greenhouse gas emissions. It accounts for ~98% of current global H2 production.
            Blue H2 is also generated using natural gas, incorporating carbon capture, utilization, and storage to cut emissions. It consists of <1% of current global H2 production.
            Green H2 is produced by electrolysis using water and renewable energy and has the potential to be a zero-carbon fuel. It makes up <1% of the global H2 supply.
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Green hydrogen holds significant potential as a low-carbon energy source for the heat and power sector and for decarbonization of difficult-to-abate sectors, including steel, cement, chemicals, and potentially transportation.
However, it currently faces large-scale infrastructure and investment hurdles.
Key messages H2 Sector Overview

## Slide 4: Green H2 targets industry, power, and transport with an estimated emission abatement of ~3 billion tonnes by 2050
Sources: Scope 1 emissions from Rhodium Group ClimateDeck (September 2024); Scope 2 iron and steel estimate from IEA (2023); abatement estimates from IEA Net Zero Roadmap (2023);
BNEF Energy Outlook (2024); other industry sources *2024 emissions based on projections Credit: Theo Moers, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
0%
40%
60%
20%
80%
100%
Chemicals 10%
Remaining industry 17%
Iron and steel 16%
Cement 17%
Cement <1%
Oil and gas 21%
Industry
Oil 3%
Natural gas 20%
Natural Gas 3-4%
Coal 74%
Power and heat
Agricultural fuel combustion 4%
Land use, land use change
and forestry
17%
Waste 21%
Crops 27%
Agriculture, land use, and waste
Aviation 8%
Aviation 2-3%
Marine 3%
Marine 7-8%
Chemicals 3-4%
Road 62%
Road 13-14%
Livestock 32%
Transport
Commercial
combustion
20%
Refining 3%
HFCs from
refrigeration
and A/C
27%
Residential
combustion
53%
Buildings
28%
28%
21%
16%
7%
Coal mining 7%
Abatement in International Energy Agency (IEA) net-zero scenario
1-2% in iron and steel
<1% in cement
3-4% in chemicals
1-2% in refining
13-14% in road
3-4% in natural gas
7-8% in marine
2-3% in aviation
CO2e emissions in 2024*: ~50 billion tonnes

## Slide 5: Almost all existing H2 production today uses fossil fuels, leaving green H2 with <1% market share
 | Grey hydrogen | Blue hydrogen | Green hydrogen
Production process | Produced from natural gas steam methane reforming (SMR), where CO2 emissions generated during the production are released. | Produced through SMR of natural gas, but the carbon emissions are captured, utilized, or stored (CCUS). | Produced by electrolyzing water (electrolysis) using electricity generated from renewable energy sources.
Main inputs |  |  | 
CO2e per kg of H2 (Scope 1) | 11.0 – 13.7 kg | 0.2 – 3.2 kg | ~0.0 kg
Energy input per kg of H2 | ~ 60 kWh | ~ 60 kWh | ~ 50 kWh
Current market share | ~98% (all fossil fuels) | <1% | <1%
Production cost per kg of H2 | ~$1-3/kg | ~$2-5/kg | ~$4-12/kg (High variation due to early-stage technologies and global differences in cost of renewable energy.)
Observations | Demand for grey hydrogen is expected to decline as demand for green hydrogen becomes cost competitive. | Some question the effectiveness of blue hydrogen for a net-zero economy, as carbon capture does not abate all carbon emissions. | Potential challenges currently include high costs, inability to scale, and large ranges of demand forecasts.
Hydrogen ‘colors’ represent production method and indicate carbon intensity*
*Other types of hydrogen include pink (electrolysis with nuclear electricity), yellow (electrolysis with mixed electricity, e.g. from grid) and turquoise (produced via pyrolysis of natural gas).
Sources: S&P Global Commodity Insights, Atlas of Energy Transition (2023); World Economic Forum, Grey, blue, green—why are there so many colours of hydrogen? (2021); IEA, Global Hydrogen Review 2022 (2023); McKinsey, Global Energy Perspective 2023: Hydrogen Outlook; various industry sources
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
CH4 +
Methane Steam
Methane Steam CCUS
Water Renewable power
CH4 + +
H2O +
Chart: 
 | 98 | 2
Chart: 
 | 1 | 99
Chart: 
 | 1 | 99

## Slide 6: H2 dubbed Swiss Army knife of decarbonization, but application potential varies significantly across sectors
Varying levels of technical and economic potential
1 Long-haul overseas shipping using ammonia or synthetic e-fuels as a clean energy source; 2 uninterruptible power supply
Sources: Liebreich & Associates (with concept credit to Paul Martin), The Clean Hydrogen Ladder (2021); Redefining Energy, Hydrogen…it’s complicated! (2021)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
Some refer to hydrogen as the Swiss Army knife of decarbonization for its extensive applications across sectors.
While the feasibility of theoretical technology has been proved for many H2 applications, the true potential varies significantly between sectors.
  Some technologies are more in prototype stage and have not yet been tested on large-scale applications.
  Despite its many theoretical applications, hydrogen can fall short on cost advantages and efficiency.
Hydrogen is best utilized in hard-to-abate sectors, e.g., in industry or certain subsectors of transportation, where applications come with a large potential for future growth.
High application potential
Mid application potential
Low application potential
1
2
1
1

## Slide 7: True potential for green and blue H2 determined by viability of use cases as well as economic feasibility
Economic feasibility
Technology scalability
Evaluation of selected H2 technology use cases
Source: IEA, Net Zero Roadmap (2023); Liebreich & Associates (with concept credit to Paul Martin), The Clean Hydrogen Ladder (2021); various industry sources
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
Beyond theoretical technological feasibility, two main factors determine whether blue and green H2 are a realistic decarbonization solution for a specific use case
  Technological scalability: Is the technology sufficiently mature, scalable and viable for commercial application?
  Economic feasibility: Is H2 the best available decarbonization technology? Are there other technologies that are more (cost-) efficient?
Evaluation among the two metrics shows how use case viability is in many cases driven by economic feasibility; i.e., the availability of better or cheaper alternative technologies (electric vehicles for cars, heat pumps for heating)
High application potential
Mid application potential
Low application potential
Steel
Fertilizer
Long-duration grid balancing
Regional trucks
Commercially scalable; economic feasibility dependent on weight and distance
Short-duration grid balancing
Currently moving from pilot stage to first large-scale commercial demonstration plants
Domestic heating
Shipping
Metro trains and buses
Cars
Scalability more difficult than for long-duration storage as short-duration more distributed, resulting in higher infrastructure needs; lithium-ion batteries more cost-competitive for short-term storage.
Aviation (jet fuel)
Not yet at a commercially viable production level; few alternative options for aviation decarbonization

## Slide 8: Potential of H2 in technologically viable sectors requires political support to become economically competitive
Sources: Roland Berger, Green Hydrogen Report (2023); BNEF, Green Hydrogen to undercut grey sibling by end of decade (2023); Cullenward and Wagner, The Washington Post (2023)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Chart: 
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030

 | 5 | 4.9 | 4.9 | 4.8 | 4.6 | 4.5 | 4.4 | 4.3 | 4.2
 | 4.5 | 4.25 | 4.1 | 3.9 | 3.65 | 3.5 | 3.4 | 3.25 | 3.1
 | 2.5 | 2.25 | 2.15 | 2 | 1.75 | 1.5 | 1.25 | 1.1 | 0.85
 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
0,0
0,5
1,0
1,5
2,0
2,5
3,0
3,5
4,0
4,5
5,0
LCOH (unsubsidized, status quo renewables price)
LCOH (unsubsidized, post-IRA renewables price, blue hydrogen pathway)
Subsidized H2 cost (green hydrogen pathway)
Average US grey hydrogen production cost in 2023
Green hydrogen benefits from cheaper renewable electricity under the US Inflation Reduction Act (IRA)
Impact from 45V clean hydrogen production credit
Three requirements for H2 to be green
Additionality
Localized
Time matching
Renewable electricity must be specifically built for H2 production.
Diverting power from existing clean plants increases dependence on conventional power sources and carbon emissions.
Dedicated local clean energy sources are linked to electrolyzers.
The mere buying of ”green” certificates is insufficient.
H2 production is synchronized with clean electricity procurement.
Some electrolyzer technologies (e.g., PEM) work with intermittent input.
Observations
Integrating these production requirements with public support (tax credits, subsidies) enables the scale-up of green hydrogen in technologically viable sectors.
Although potentially delaying ramp-up, this ensures effective allocation of public funds and avoids stranded assets or lock-in of less ideal solutions.
Expected levelized cost of green hydrogen (USD/kg)

## Slide 9: Green H2 Technology and Financials

## Slide 10
Green H2 production costs remain substantially higher than those of grey and blue H2, presenting a major barrier to widespread adoption. The H2 sector faces infrastructure and investment limitations. However, progress is underway through increased subsidy incentives, technological advancement, and expansion of renewable energy production.
  Grey H2 costs an average of $1-3/kg, driven by the low cost of fossil fuels and natural gas.
  Blue H2, while similarly benefiting from lower fossil fuel prices, incurs additional expenses due to carbon capture, utilization, and storage, raising its cost to $2-5/kg.
  Green H2, in contrast, averages between $4-12/kg, with the higher costs attributed to the development of electrolyzer technology and reliance on renewable energy sources.
Green H2 remains significantly more expensive than H2 from less sustainable sources, with a cost premium of approximately $2-10/kg as of 2023. These price variations are influenced by regional factors, levels of private investment, and the extent of government support.
Today, alkaline water electrolysis (AWE) is the most widely used method for green H2 production, primarily due to its low cost. Proton exchange membrane (PEM) electrolysis, however, is also expected to play a significant role in the future, as it is better suited to manage the variability of renewable energy inputs.
Research and development in electrolyzer technology could lead to significant cost reductions and enable specialized applications. For instance, solid oxide electrolyzers can leverage excess industrial heat for enhanced efficiency, while anion exchange membranes offer a compact solution for space-constrained environments.
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Key messages Green H2 Technology and Financials

## Slide 11: Primary challenge for green H2 is balancing its high production cost with its significant emissions abatement potential
Green hydrogen on a carbon abatement cost curve ($/t CO2e)
Source: Goldman Sachs, Carbonomics: The clean hydrogen revolution (2022)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
The diverse applications for green H2 provide decarbonization solutions with varying cost implications.
  The use of H2 for chemical production, energy storage, and power generation is currently cost efficient, with an abatement cost of 100 USD/t CO2e equivalent.
  The use of H2 for producing synthetic aviation fuels represents the highest price point of ~900 USD/t CO2e.
Carbon abatement costs are expected to decrease in the future, driven by reductions in the costs of electrolyzers and renewable energy.
The adoption of H2 applications will be determined not only by the cost per ton of carbon abatement but also by the competitiveness of alternative decarbonization technologies.
Chart: 
 | 50 | 100 | 100 | 120 | 150 | 180 | 250 | 300 | 320 | 350 | 500 | 600 | 900
200
300
400
500
600
700
800
1,000
900
100
Chemicals CCS
H2 energy storage
H2 power turbines
H2
DRI-EAF steel
Electrol. ammonia
Electrol. methanol
FC trucks
Ammonia ships
FC buses
FC trains
H2 heat pumps
H2 boilers
Synthetic fuel aviation
~180
Significant increase in carbon abatement per dollar invested in green hydrogen

## Slide 12: Current production costs of green H2 carry a substantial price premium over fossil-based alternatives
Average green hydrogen premium more than double that of grey hydrogen in 2023 ($/kg)
Sources: BNEF, Green Hydrogen to Undercut Gray Sibling by End of Decade (2023); Center on Global Energy Policy, Columbia University, Demystifying Electrolyzer Production Costs (2023)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
In 2023, green H2 production costs ranged from $4.50 to $12.00/kg, averaging $6.40/kg.
  Blue hydrogen costs are lower, ranging from $1.80 to $4.70/kg.
  Grey hydrogen is the least expensive, varying between $0.98 to $2.93/kg.
The largest cost drivers for green H2 are electrolyzers and the price of renewable electricity.
Despite its current premium, green H2 could achieve cost parity with blue and grey H2 through economies of scale and advancements in technology.
To enable hydrogen offtake, infrastructure, transport, and storage costs must be added to production costs.
Chart: 
 | 0.98 | 1.8 | 4.5
 | 1.95 | 2.9 | 7.5
 | 2.13 | 3.1 | 6.4
0
2
4
6
8
10
12
2.13
Grey H2
3.10
Blue H2
6.40
Green H2
Weighted average

## Slide 13: Relatively small green H2 premium in US compared to EU and Japan
Green hydrogen premiums vary regionally, ranging from $2-5/kg
Source: S&P, Global Commodity Insights Report (restricted)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
Green H2 premiums refer to the additional cost of green H2 compared to more carbon-intensive alternatives, such as grey and blue H2.
The Gulf Coast reported the lowest average price for green hydrogen among three major regions, reflecting the impact of significant US government investments aimed at reducing costs.
  The US Department of Energy’s Hydrogen Shot initiative targets a reduction in clean hydrogen production costs to $1/kg by 2031.
Key efforts to lower green H2 hydrogen costs include substantial investments in infrastructure and tax incentives, such as the 45V tax credit.
Chart: 
 | 0.91 | 2.05 | 3.01
 | 3.04 | 6.74 | 5.66
1
2
3
4
5
6
7
0
US Gulf Coast
Netherlands
Japan
0.91
3.04
2.05
6.74
3.01
5.66
+2.13
+4.69
+2.65
Grey hydrogen
Green hydrogen

## Slide 14: Alkaline water electrolysis now dominant; proton exchange membrane costlier yet suitable for intermittent electricity
Scalability, cost, temperature, and use cases to shape future technology adoption
Sources: Center on Global Energy Policy, Demystifying Electrolyzer Production Costs (2023); US Department of Energy, Hydrogen Production: Electrolysis (2022); IEA, Electrolyzers (2023); IRENA, Green Hydrogen Cost Reduction (2020); Hydrogen Council, Hydrogen Insights May 2023 (2023); graphics by ID Tech Ex from Alex Holland at EE times; various industry sources
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
 | Alkaline water electrolysis (AWE) |  | Proton exchange membrane (PEM) |  | Anion/ hydroxyl exchange membrane (AEM/HEM) |  | Solid oxide electrolyzer (SOEC) | 
Description and schematic overview | Electrolysis of alkaline water using nickel electrodes |  | Water electrolysis with solid polymer membrane and precious metal electrodes |  | Like PEM design; replaces precious metals and titanium with nickel and steel |  | Water steam electrolysis at high temperature (700-1000°C) via solid oxide or ceramic membrane | 
Market share | 60% market share, leading technology |  | 30% market share (higher in Europe and North America) |  | Small market share, future growth potential |  | Small market share, ideal for high waste-heat use cases | 
Advantages | Scalability of manufacturing, cost |  | Compact size, controllability of production allows management of intermittent renewable energy input |  | Compact size, potential cost reduction because made with more easily obtained materials than PEM |  | More efficient than AWE and PEM due to lower voltage levels | 
Limitations | Continuous electricity supply needed for optimal operation |  | Higher cost, potential shortage of rare metals such as iridium |  | Reduced durability |  | High capital investment, high temperatures required | 
Investment cost | ~$600/kW |  | ~$800-1,250/kW |  | >$930/kW |  | >$1,850/kW | 
Big players |  |  |  |  |  |  |  | 
Chart: 
 | 60 | 30 | 1 | 1 | 8
Chart: 
 | 60 | 30 | 1 | 1 | 8
Chart: 
 | 60 | 30 | 1 | 1 | 8
Chart: 
 | 60 | 30 | 1 | 1 | 8

## Slide 15: Both AWE and PEM expected to follow renewables cost reductions and efficiency improvements
Clean tech CapEx for green hydrogen indexed to 2020 levels ($/kW or GW)
Sources: Goldman Sachs, Investment Research Carbonomics (2022); McKinsey, Global Energy Perspective 2023: Hydrogen outlook (2023)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Chart: 
| 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
 | 100 | 80 | 70 | 60 | 50 | 40 | 35 | 30 | 28 | 24 | 20
 | 100 | 95 | 90 | 80 | 75 | 70 | 63 | 60 | 58 | 52 | 48
 | 100 | 98 | 96 | 94 | 90 | 90 | 88 | 80 | 78 | 75 | 68
 | 100 | 90 | 80 | 70 | 65 | 60 | 50 | 45 | 40 | 38 | 35
 | 100 | 95 | 85 | 80 | 75 | 70 | 65 | 60 | 58 | 55 | 50
 | 100 | 90 | 80 | 70 | 60 | 53 | 48 | 45 | 40 | 38 | 35
PEM (kW)
AWE (kW)
Batteries (kW)
Offshore wind (GW)
Onshore wind (GW)
Solar PV (GW)
Observations
The cost of acquiring and operating green hydrogen electrolyzers is expected to decline significantly over the next decade compared to 2020 levels.
  Among the various renewable energy sources, solar PV is projected to experience the fastest cost reductions, while offshore wind is expected to take longer, to lower its capital expenditures.
  Clean H2 electrolyzers are anticipated to follow a similar trend, with a projected CAGR of -60% for both PEM and alkaline technologies.
Green H2's cost reductions will primarily be driven by technology advancements, increased productivity in PEM and alkaline electrolyzers, and greater capital investments in the sector.

## Slide 16: Green H2 Industry Trends

## Slide 17: Hydrogen sector industry trends: Key points
Global demand for green and blue H2 is expected to grow substantially, with estimates indicating an increase from 125 million tonnes per annum in 2030 to 460 Mtpa by 2050. This growth will be driven by both traditional industrial uses and emerging applications, particularly in commercial transport, which is projected to become the largest new demand driver by 2040.
By 2050, green H2 is forecasted to dominate global hydrogen production, accounting for 50 to 65% of the total supply.
  Regional demand growth will initially be led by China and North America, while at the sector level, industry will dominate with offtake agreements, followed by transport, especially in long-haul shipping.
  Green and blue H2 trade is projected to expand fivefold between 2030 and 2050, with North America emerging as the largest net exporter.
  The US and Canada are expected to lead green and blue H2 exports, supported by robust policy frameworks. Long-distance transportation of H2 will be driven by its use in end products like ammonia and synthetic kerosene.
Key players in the fossil fuel, energy, and utility sectors are recognizing H2’s potential as a critical energy carrier. They are incorporating H2 into their strategies, acquiring large-scale hydrogen assets, and increasing investments in green and blue hydrogen projects.
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Key messages Green H2
Industry Trends

## Slide 18: H2 currently used primarily in industrial processes and petroleum refining, with limited application in heat and power sectors
 | Industry | Refining | Heat and power
Role of H2 | H2 is used as feedstock for synthetic fuels (e.g., methanol) or fertilizers (e.g., ammonia). Other industries such as steel and cement aim to adopt H2 to decarbonize their production processes. | The oil refining process uses H2 for hydrotreating and hydrocracking, reducing sulfur content of oil to produce cleaner fuels like diesel and jet fuel. | H2 can generate electricity through fuel cells or be blended into gas turbines for power generation in internal combustion engines and heating applications.
Current market dynamics | The industry sector consumed 53 Mt of H2 in 2022, with 60% used for ammonia production, 30% for methanol production, and 10% for iron and steel production. | H2 use in refining reached 41 Mt in 2022, driven to record levels by strong demand in North America and the Middle East. | As of 2023, H2 accounted for only 0.2% of the global electricity mix.
Green H2 adoption challenges | Cost reductions are crucial in the green H2 sector to compete with low natural gas and grey H2 prices. | Most H2 used in refining is produced on-site as a byproduct of catalytic reformers or ethylene crackers, rather than sourced externally. | H2 use in electricity generation faces compatibility challenges with existing infrastructure and combustion systems.
Large-scale use of grey H2 in industry and refining, with some early green H2 in heat and power
Sources: EIA, Hydrogen Explained (2023); IEA, Global Hydrogen Review 2023 (2023); Methanol Institute, Renewable Methanol; Wood Mackenzie, Low-carbon hydrogen demand in refining could reach 50 Mtpa by 2050 (2022); Yara, Green fertilizers: everything you need to know
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu

## Slide 19: While commercial transport applications remain limited today, they are expected to play a bigger role in the future
Green H2 is expected to play a key role in decarbonizing the commercial transport sector
Sources: Airbus, ZEROe; CSIS, Hydrogen: The Key to Decarbonizing the Global Shipping Industry? (2021); DNV, Maritime decarbonization efforts propelled as orders for alternative-fueled vessels grow (2024); European Maritime Safety Agency, Potential of hydrogen as a fuel for shipping (2023); Global Maritime Forum, Ammonia as a shipping fuel (2023); IEA, Global Hydrogen Review 2023 (2023); International Air Transport Association, Liquid hydrogen as a potential low-carbon fuel for aviation; Rolls Royce, Rolls Royce and easyJet set new world first (2022)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
 | Road transport | Shipping | Aviation
Role of hydrogen | H2 fuel cell electric vehicles (FCEVs) provide faster refueling, longer ranges, and lighter fuel weight compared to electric vehicles. | H2 can power vessels either directly as liquid hydrogen or through synthetic fuels like ammonia and methanol. | H2 fuel cells could power planes for short-haul flights. H2-based sustainable aviation fuel (H2-SAF) has the potential to replace traditional jet fuel.
Current market dynamics | In 2023, China represented 95% of FCEV trucks globally, while South Korea accounted for 50% of private FCEV cars. | In 2023, the global shipping industry ordered 298 vessels designed to operate on alternative fuels, including 138 on methanol, 11 on ammonia, and five on H2. | In 2022, Rolls Royce and easyJet successfully ran an aircraft engine on H2.. Airbus plans to introduce a H2-powered aircraft to market by 2035.
Green hydrogen adoption challenge | FCEVs face limitations due to insufficient fueling infrastructure and competition with battery electric vehicles for market share. | H2’s lower energy density compared to alternative marine fuels makes transport on ships more challenging, necessitating carriers like ammonia or liquid hydrogen. | The main challenge for H2-SAF is its high cost. Sustainable aviation fuel is an existing drop-in fuel for aircrafts, requiring no retrofitting of aircrafts or infrastructure.

## Slide 20: Under IEA’s full decarbonization scenario, demand for green and blue H2 is expected to increase to ~400 Mt by 2050
Projected demand for green and blue hydrogen by sector (Mtpa)
Note: Demand scenarios differ a lot; demand numbers derived from IEA’s net-zero scenario
Sources: IEA, Net-zero scenario hydrogen outlook (2023); McKinsey, Global Energy Perspective 2023: Hydrogen outlook (2024)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
Green and blue H2 adoption across existing and emerging applications could drive H2 demand to ~240 Mt by 2030 and ~390 Mt by 2050, compared to less than 1 Mt in 2023.
The transport sector will be the main driver of demand, accounting for ~34% in 2040 (across aviation, marine, and road transport) and ~46% of total demand in 2050.
Industry (including chemicals and iron and steel) and power generation will also be significant contributors to demand.
  Industry demand will be driven by both conventional uses (replacing grey H2 with green and blue H2) and new applications.
Oil refining will continue to have relatively low demand for green and blue H2, as grey H2 is a byproduct of refining and unlikely to be replaced by green or blue H2 in the near term.
Chart: 
 | 4 | 13 | 21
 | 6 | 7 | 6
 | 9 | 35 | 61
 | 7 | 32 | 48
 | 22 | 68 | 75
 | 4 | 22 | 61
 | 11 | 60 | 116
50
100
150
200
250
300
350
400
0
2030
25%
29%
14%
15%
3%
5%
2040
30%
16%
19%
12%
16%
2%
5%
2050
~60
~240
~390
9%
Aviation and marine fuel
Road transport
Power generation
Iron and steel
Chemicals
Oil refining
Other industry

## Slide 21: Green and blue H2 industry demand projections vary widely around IEA’s ~400 Mt per year by 2050
Projected demand for green and hydrogen, 2030-2050 (Mtpa)
Note: Demand and abatement differ due to varying carbon intensities and emission proportions across sector. Clean H2 includes both blue and green H2.
Sources: IEA, Net-zero scenario hydrogen outlook (2023), BP, Hydrogen (2023); Deloitte, Green hydrogen: Energizing the path to net zero (2023); McKinsey, Global Energy Perspective 2023: Hydrogen outlook (2023), IEA, Hydrogen (2023), IRENA, World Energy Transition Outlook (2023), Wood Mackenzie, 2050: The Hydrogen Possibility (2024)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
In nearly all scenarios, a substantial increase in demand for green and blue H2 is expected.
  Projections suggest total annual volumes could approach 400 Mt by 2050.
  With 50 kWh/kg of green H2, this would require ~20,000 TWh of green electricity by 2050 (today: ~25,000 TWh).
Meeting future demand will require a significant scale-up in production; in 2022, demand for green and blue H2 was ~1 Mt.
At the same time, the IEA estimates the demand for a 1.5°C pathway will be around ~390 Mt in 2050, even under its ambitious net-zero scenario. This is much lower than several industry projections, such as Deloitte’s estimate of ~600 Mt.
Chart: 
| 2030 | 2035 | 2040 | 2050
 | 172 | 289.5 | 407 | 598
 | 17.9 | 40.0667 | 84.4
 | 86.2 | 186.4667 | 387
 | 37.5 | 122.7 | 207.9 | 436.17
 | 63 | 150 | 237 | 388
 | 125 | 224.5 | 324 | 523
 | 25 | 32 | 85 | 210
~20
~ 125
~90
~ 32
~ 63
~ 208
~170
~ 85
~600
~80
~390
~ 38
~520
~ 210
~ 436
~ 237
BP Upper Bound
IEA net-zero scenario
Wood Mackenzie
McKinsey Further Acceleration scenario
BP Lower Bound
IRENA 1.5°C scenario
Deloitte
Following research based on IEA’s net-zero scenario with average demand

## Slide 22: Chemicals industry dominates H2 offtake agreements
Chart: 
 | 1.17 | 0.19 | 0.78
 | 0.19 | 0.08 | 0.13
1.00
0.50
1.25
0.75
1.50
0.25
0.00
Transport
Other
1.36
0.27
0.91
Industry
Industrial sector expected to dominate hydrogen offtake agreements by 2030 (Mt)
Source: IEA, Global Hydrogen Review 2023 (2023)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
The industrial sector is leading in securing offtake agreements, with ~1.3 Mt of demand, half of which has already been firmly implemented.
  Within the industrial sector, the chemicals subsector accounts for 85% of the agreed volumes, largely driven by ammonia production.
While progress in the transport sector has been slower, significant agreements have been made, particularly in shipping.
  Major logistics companies have signed agreements for synthetic methanol and synthetic marine diesel.
Chemicals
Refining
Shipping
Not specified
Other industry
Other transport

## Slide 23: North America expected to become the largest green H2 net exporter, while China and Europe lead as net importers
Source: Hydrogen Council, Global Hydrogen Flows - 2023 Update (2023)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
North America is anticipated to lead in blue and green H2 production, driven by supportive policies in the US and Canada.
By 2050, North America and China are projected to contribute 58% of global blue and green hydrogen supply and 53% of demand.
North America is expected to become a net exporter, with ~30% of its blue and green H2 supply transported over long distance.
Europe and China are projected to be net importers, relying on importing for ~59% and ~25% of their hydrogen demand, respectively.
In addition to long-distance trade, robust inner-continental hydrogen transport is anticipated, such as from Iberia and the Nordic countries to Central Europe.
Long-distance green and blue H2 supply projections, share by region (Mt, 2050)
Long-distance green and blue H2 demand projections, share by region (Mt, 2050)
Chart: 
 | 82 | 29 | 20 | 17 | 16 | 29
40
60
30
70
50
80
20
90
10
0
China
Middle East
Europe
Australia
Rest of world
17
16
North America
Chart: 
 | 58 | 41 | 40 | 26 | 17 | 17
0
10
20
30
40
50
60
70
80
90
North America
Europe
China
Japan, Korea
Asia
Rest of world
58
26
17
17
43% 15% 10% 9% 8% 15%
29% 24% 24% 15% 10% 10%

## Slide 24: Green hydrogen value chain is global, with production and end-use applications often separated by significant distances
Green hydrogen value chain spans three main fields
Observations
The H2 value chain from production to distribution and application operates globally, as supply and demand are often geographically distant.
Inner-continental H2 transport is primarily conducted via pipelines, with three options:
  Blending into existing gas pipelines (up to ~5% of the mix can be H2)
  Retrofitting old gas pipelines
  Building new hydrogen-only pipelines
Long-distance H2 transport relies on marine shipping technologies such as:
  Liquified hydrogen
  Ammonia
  Liquid organic hydrogen carriers
H2 storage is essential at various points along the value chain, including pre- and post-shipping as well as pre-industry use.
Production | Distribution | Application
Production will be concentrated in regions with abundant and low-cost renewable energy. | Depending on the distance, transport occurs via pipelines or is shipped long distance, with storage hubs along the transport route. | Location of end-use applications is mainly determined by regional demand; some use cases might move to places with low-cost renewables.
Source: IRENA, Geopolitics of the Energy Transformation (2022)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Grid power
Electrolyzer
Hydrogen storage unit
Hydrogen transportation
Hydrogen fuel cells
Hydrogen
fuels
Industrial plants
Power market
Transportation
Solar Power
Wind Power
Other

## Slide 25: Three potential H2 carriers are suitable for marine transport
 | Liquified hydrogen (LH2) | Ammonia (NH3) | Liquid organic hydrogen carriers (LOHC)
Description | Produced via extreme cooling, it can be used directly as fuel or converted back into gas at the destination. | Synthesized into ammonia for transport, enabling either direct use as green ammonia or conversion back into H2 through racking. | Transported through hydrogenation and post-transport dehydrogenation by covalently bonding with liquid organic molecules, such as dibenzyl toluene.
Energy density1 | 0.071 kg/L (at -253°C) | 0.12 kg/L (at -33°C) | ~0.05 kg/L (at 25°C)
Process steps |  |  | 
Adoption challenges | Energy intensive; liquefaction is expensive | Energy intensive and expensive cracking; health risks | Expensive hydrogenation; lack of technology readiness for scale-up
Share of volume of announced projects2 | ~5% | ~35% | ~10%
Market readiness | Pilot stage, infrastructure not yet widely available | Established shipping, cracking at pilot stage | Pilot projects, infrastructure for some molecules available
Shipping technologies face significant adoption challenges at various stages
1Energy density of gaseous H2 at 1 atm. Temperature and pressure is 8.9E-10 kg/l; 2 only 50% of announced projects have already decided on technology.
Sources: Spotalisano et al., Liquefied hydrogen, ammonia and liquid organic hydrogen carriers for harbour-to-harbour hydrogen transport (2024); Hydrogen Council, Global Hydrogen Flows-2023 Update (2023), Hydrogen Council, Hydrogen Insights (2022)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
Marine H2 transport requires cooling or carriers due to H2’s low energy density.
Different H2 carriers face bottlenecks related to infrastructure and costs, with technology choices influenced by specific use cases:
  Ammonia synthesis is relatively cost efficient but expensive to crack, making it ideal for direct use as green ammonia (e.g., fertilizers).
  Liquid H2 liquefaction is expensive but suitable where liquefaction is necessary for end use as fuel.
The market’s dominant shipping technology is still undecided:
  Half of announced shipping projects have yet to decide on a specific technology.
  Among projects specifying a carrier, ammonia accounts for 35% of volume, followed by LOHC at 10% and liquid hydrogen at 5%.
Marine transport, storage
Regasification
Liquefaction
Green H2
Distribution and end use
Marine transport, storage
NH3-cracking to H2
NH3 synthesis
Green H2
Distribution and end use
Marine transport, storage
Dehydrogenation
Hydrogenation
Green H2
Distribution and end use
Chart: 
 | 50 | 35 | 10 | 5
Chart: 
 | 50 | 35 | 10 | 5
Chart: 
 | 50 | 35 | 10 | 5

## Slide 26: As forecasts for clean H2 demand increase, major oil companies and utilities are positioning themselves to capture market share
Multibillion-dollar investments and equity stakes are becoming increasingly popular
Sources: Air Products, Air Products, Aramco, ACWA Power, and Air Products Qudra Reach Financial Close (2023); Aramco, Aramco to acquire 50% stake in Air Products Qudra’s Blue Hydrogen Industrial Gases Company (2024); BP, BP to lead and operate one of the world’s largest renewables and green hydrogen energy hubs based in Western Australia; NextEra Energy, Climate Change 2023 (2023); NextEra Energy, Florida Power & Light company announces completion of clean hydrogen hub (2023); NextEra Energy, NextEra Energy sets industry-leading Real Zero goal (2022)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Large-scale investment in M&A for blue H2
$36B investment in green and blue H2 production and export hub
Allocating significant funds to transition from gas to H2 in power generation
In 2024, Aramco acquired a 50% equity stake in Blue H2 Industrial Gases Company.
Blue H2 will be transported by pipeline through Saudi Arabia's Eastern Province, with potential for regional exports.
The investment aligns with Saudi Arabia’s National Green Hydrogen Strategy, which aims to invest $36 billion in green and blue hydrogen by 2030.
In 2022, BP acquired a 40.5% equity stake worth $36 billion in the Australia Renewable Energy Hub (AREH).
Upon completion, AREH will produce 1.6 Mt of green H2 or 9 Mt of green ammonia annually, supported by 26 GW of clean power.
The H2 and ammonia produced by AREH will supply both Australia and regional markets, including Japan and South Korea.
In 2023, the utility announced a commitment of $20 billion to decarbonize its operations in the US.
A key part of its decarbonization strategy is converting 16,000 MW of natural gas power plants to operate on green hydrogen
Florida Power & Light, the largest utility in the US, established the Cavendish NextGen Hydrogen Hub to test hydrogen blends for turbines.

## Slide 27: Green steel production possible key driver for green H2 demand, with each tonne of Green H2 DRI-EAF steel requiring ~50-60kg H2
Sources: Center on Global Energy Policy at Columbia University, Low-Carbon Production of Iron & Steel (2021); IEA, Iron and Steel Technology Roadmap (2020); IEA, Net-zero scenario hydrogen outlook (2023); McKinsey, Decarbonization challenge for steel (2020); BNEF, Scaling Up Hydrogen (2024)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Green H2 Direct Reduced Iron-Electric Arc Furnace (DRI-EAF) uses green hydrogen to replace natural gas as an iron ore reductant; byproduct is water instead of CO2
Case study: Green H2 in Steel
H2 demand for steel (Mt)
Chart: 
 | 0 | 6 | 17 | 41
0
5
10
15
20
25
30
35
40
45
2022
2030
2035
2050
0
100% H2 plants in early stages of development, with first industrial-scale plants planned to operate in 2026
Green H2 direct reduced iron with decarbonization potential of ~90% compared to now dominant Blast Furnace-Basic Oxygen Furnace (BF-BOF)
Iron ore
Iron
Steel

## Slide 28: ~40 Mt of green steel project announced in Europe by 2023, implying 2-2.4 Mt green H2 demand
2025 | 2026 | 2027 | 2028 | 2029 | 2030
As of 2023, ~40 Mt of green steel projects announced in Europe alone
Source: Columbia Business School, H2 Green Steel (2024)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
1-2 Mt
2-3 Mt
>3 Mt
Case study: Green H2 in Steel
Four green steel plants announced as of 2021
As of 2023, ~40 Mt green steel announced in Europe by 2030

## Slide 29: Green H2 Policy

## Slide 30
Over 30 governments, representing ~80% of energy-related CO2 emissions, have adopted national green H2 strategies. The EU and US are at the forefront, supporting research, development, and demonstration projects, while deploying grants and tax incentives to mitigate investment risks and establish standards for large-scale hydrogen initiatives.
Financial incentives have significantly reduced electrolyzer costs and accelerated green hydrogen adoption. However, challenges such as high initial investments, uncertainty in long-term returns, and the need for infrastructure and storage remain significant.
Additional policy frameworks and collaborations are required to scale production and build efficient supply chains despite legal and financial barriers.
  The EU, US, Australia, Japan, and other countries have set ambitious electrolyzer capacity and hydrogen production goals. The EU aims for 40 GW of electrolyzers by 2030, while the US aims to achieve a green H2 price of $1/kg within the next decade.
  Research initiatives, such as the US Department of Energy’s $64 million H2@Scale program, are focused on reducing costs and advancing hydrogen technologies. Infrastructure projects in the US include retrofitting natural gas pipelines and developing new hydrogen storage facilities.
  The US Bipartisan Infrastructure Law dedicates $8 billion to establish seven Regional Clean Hydrogen Hubs, targeting emissions reductions of 1 to 9 Mt/year. In addition, the Inflation Reduction Act introduces the Clean Hydrogen Production Tax Credit (45V), offering incentives up to $3/kg for low-carbon-intensity projects.
Government subsidies, tax credits, and financial initiatives are essential for making green H2 cost competitive with fossil-based grey H2, driving its adoption in the industrial sector and improving its scalability and economic viability.
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Key messages Green H2 Policy

## Slide 31: Over 30 governments, representing ~80% of energy-related CO2 emissions, have implemented green H2 strategies
Global adoption of hydrogen strategies
Source: IRENA, Green Hydrogen Supply (2023)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
Around 30 countries have established national H2 strategies, with an additional 23 countries in the process of developing their own proposals.
The EU and US are leading efforts to support the research, development, and demonstration of H2 projects and technologies.
Governments are introducing mechanisms such as grants, loans, and tax incentives to mitigate investment risks, alongside growing efforts to implement standards and certification schemes for green H2.
Despite growing governmental involvement, large-scale green H2 projects remain underdeveloped in many emerging markets.
In policy discussions or pilot projects
Preparing a national strategy
Published national strategy

## Slide 32: Methane and H2 leakage a concern for the production of grey and blue H2, not for green H2
Sources: Ocko and Hamburg, Climate Consequences of Hydrogen Emissions (2022), Duan and Caldeira, Comment on “Climate Consequences of Hydrogen Emissions” by Ocko and Hamburg (2022) (2023)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
While H2 production and transport play a crucial role in reducing carbon emissions, they can also contribute to the greenhouse gas effect if not managed properly.
  Methane, a greenhouse gas 28x more potent than CO2, can leak into the atmosphere during blue and grey H2 production.
  H2 itself is an indirect greenhouse gas and can contribute to global warming if significant leakages occur.
Other potential environmental effects of H2 production include water and land use, though these effects appear small compared to the overall benefits in most regions.
Despite these challenges, H2's potential to significantly reduce carbon emissions far outweighs the global warming impact of its potential leakage.
Green hydrogen with less warming even with large H2 leakage
Methane (CH4) leakage is a potential concern with grey or blue H2 production, not with green H2
Green H2 is better than fossil alternative, even with 10% H2 leakage

## Slide 33: Government incentives play a critical role in accelerating green H2 adoption, with the EU, US, and other regions leading the charge
Countries are actively exploring various incentives to accelerate the adoption of green and blue H2
Sources: IRENA, Green Hydrogen Supply (2023); EU Clean Hydrogen Partnership (2024); CGEP, Energy Institute, Statistical Review of World Energy (2024); various government sources
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
 | Description | EU | Australia | Japan | United States
Financial incentives | Temporary subsidies can boost green H2 production by reducing investment risks and lowering costs. Public investment in infrastructure, such as pipelines and storage, is essential for the rapid scaling of a H2 economy. | Infrastructure grants through the Important Projects of Common European Interest support investments in pipelines and storage. | Hydrogen Headstart supports large-scale green and blue H2 production with $4 billion in grants. The country provides a $2 tax incentive for each kg of clean H2. | Contracts for Difference program aims to bridge the price gap between clean H2 (domestic and imported) and fossil fuels. | The Inflation Reduction Act and 45V tax incentives promote the adoption of green and blue H2 production.
Policy and regulatory frameworks | Government targets, strategies, and standards such as criteria defining green H2 can build market trust and accelerate scaling efforts. | The EU aims to roll out 40 GW of electrolyzer capacity by 2030. EU-wide CertifHy certification program is being implemented to standardize green and blue H2. | Australian Renewable Hydrogen Hub supports development of export routes. | Country has a target of 3 Mt green and blue H2 production by 2030, increasing to 20 Mt by 2050. | Hydrogen Energy Earthshot initiative aims to reduce the cost of green and blue H2 to $1/kg within a decade.
Education, research, and partnerships | Investments in research and pilot projects can drive technological advancement and facilitate scaling. Educational initiatives and international partnerships can foster public support and global collaboration. | EU is forming partnerships with North African countries to import their green H2 production. | H2 Industry Workforce Development Roadmap focuses on upskilling workers for H2 production and related industries. | Significant investments in H2 technology research have enabled Japan to account for 24% of global H2-related patent applications between 2011 and 2020. | The Department of Energy’s Hydrogen and Fuel Cell Technologies office focuses on advancing research, education, and project implementation.

## Slide 34: Regulatory and economic factors are driving the transition from grey to green H2
Three scenarios outline potential shift from grey to green and blue H2 through 2030
1Renewable Energy Directive
Source: McKinsey, Global Energy Perspective 2023: Hydrogen outlook (2023)
Credit: Friedrich Sayn-Wittgenstein, Nadine Palmowski, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim & Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
The phase-out of grey H2 will depend on carbon pricing and supportive policies such as blending mandates for clean fuels or ammonia.
These measures are expected to drive industry commitments and amplify consumer demand for a green H2 transition.
  Current scenario: By 2030, around 10% of grey H2 could shift to renewable or low-carbon alternatives, primarily driven by industry pressure.
  Accelerated trajectory: Carbon costs of $50 to $100 per ton could result in around 30% of grey H2 transitioning, particularly in regions with lower green and blue H2 costs and facilities that can be readily upgraded.
  Ambitious trajectory: High carbon pricing and additional incentives could enable a 50% conversion rate. Examples include EU’s RED II/III and California’s Low Carbon Fuel Standard.
 | Current scenario | Accelerated trajectory | Ambitious trajectory
Share of grey H2 converted (% by 2030) |  |  | 
Required CO2 price and policy (USD/ton CO2) | Low or zero CO2 cost | ~50-100 USD/ton CO2 | 100+ USD/ton CO2
 | Industry commitments and consumer demand are key drivers of decarbonization efforts. | Most cost-optimal use cases convert grey H2 (e.g., close to carbon storage). | Policy incentives (e.g., RED1 and the phase-out of free allowances) further accelerate the transition.
Progress across focused regions |  |  | 
Chart: 
 | 20 | 30 | 50
0-20%
30%
50%
Level of ambition
Case study: H2 Transition Scenarios Across Regions

## Slide 35: While the EU has established ambitious green H2 targets, implementation efforts have fallen behind schedule
Companies like Air Liquide and Siemens have made significant progress in advancing green hydrogen projects
*Final Investment Decision
Sources: CGEP, Low-Carbon Production of Iron & Steel (2021); Energy Institute, Statistical Review of World Energy (2024); IEA, Iron and Steel Technology Roadmap (2020); Journal of Cleaner Production, Towards fossil-free steel (2023); The Oxford Institute of Energy Studies, 2024 State of the European Hydrogen Market Report (2024); Air Liquide, Air Liquide Hydrogen (2024); Siemens Energy, Siemens Hydrogen (2024) Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim & Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
EU regional overview | By setting clear objectives, providing financial incentives, and fostering collaboration, the EU has accelerated the green H2 transition. However, progress on deployment of green and blue H2 projects has not kept pace with these goals. Achieving a sustainable hydrogen economy will require continued policy support, effective implementation, and stronger alignment between targets and execution.
 | Pre-policy adoption (pre-2020) | Policy adoption phase (2020-2024) | Post-policy impact (as of mid-2024)
EU policy landscape | H2 production has mainly relied on fossil fuels, with fragmented national and regional policies, limited infrastructure, and low adoption of hydrogen technologies. | EU launches EU Hydrogen Strategy, aiming for 6 GW of electrolyzer capacity by 2024 and 40 GW by 2030. | Electrolyzer supply has surpassed the targets outlined in the Net Zero Industry Act. However, progress toward 2030 production goals remains slow, with only 3.6% of 2030 projects having reached the FID* stage.
 | Operated hydrogen production facilities but invested minimally in H2 R&D due to regulatory uncertainty and high production costs. | Increased renewable H2 production, expanded H2 refueling stations, and developed optimization tools within its infrastructure across the EU. | Became leader in green H2 production with established initial refueling network. Committed to investing €8 billion in low- emission H2 by 2035 and targeting 3 GW of electrolysis capacity by 2030.
 | Focused on PEM electrolyzers with a few pilot projects, like Hyflexpower, integrating H2 into natural gas infrastructure. | Expanded its H2 activities with investment in large-scale projects, including an 8.75 MW electrolyzer plant in east Germany and a 20 MW electrolyzer in partnership with Air Liquide. | Increased production with large-scale projects, such as Voestalpine in Austria, producing 1,200 cubic meters of green H2/hour to decarbonize steel production.
Case study: EU Green Hydrogen Regulations

## Slide 36: In the US, the Inflation Reduction Act provides further support for green and blue H2 with a production tax credit
Clean Hydrogen Production Tax Credit (45V) provides incentives up to $3/kg
*Scope 1-3 carbon intensity
Sources: PV Magazine, The Hydrogen Stream (2023); US Department of Energy, Financial Incentives for Hydrogen and Fuel Cell Projects; US Department of the Treasury, U.S. Department of the Treasury, IRS Release Guidance on Hydrogen Production Tax Credit to Drive American Innovation and Strengthen Energy Security (2023)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
The Inflation Reduction Act 's Clean Hydrogen Production Tax Credit (Section 45V) is the largest tax credit for green H2 to date.
  Producers can collect a tax credit of up to $3/kg for projects constructed by 2033.
  Both green and blue H2 are eligible, with subsidy values determined by greenhouse gas emissions as measured, as defined under the US Clean Air Act.
Section 45V credit will be key in making the levelized cost of blue and green H2 competitive with grey H2 .
Additional support includes the Advanced Energy Project Credit, offering a 30% tax credit for investments in fuel cells, electrolyzers, or hydrogen infrastructure.
Eligibility for 45V tax credit |  |  |  | 
Carbon intensity* (kg CO2/kg H2) | Hydrogen color | Percentage of full 45V tax credit (%) | Applicable credit value ($/kg H2) | Additional requirements
< 4.0 |  | 20 | 0.60 | Must start construction before 2034 Cannot be combined with the Carbon Capture and Sequestration Tax Credit (45Q) Can be combined with the renewable energy production tax credit and the zero-emission nuclear credit Must promote well-paying jobs
< 2.5 |  | 25 | 0.75 | 
< 1.5 |  | 33 | 1.00 | 
< 0.45 |  | 100 | 3.00 | 
Case study: US Infrastructure Subsidies for Green Hydrogen

## Slide 37: Policy a key driver for the shift away from grey H2, while gas prices determine the balance between blue and green H2
Projected H2 demand (in Mt)
Note: Natural gas price in base case is 31.3EUR/MWh in 2025-2030 and 39.0 EUR/MWh in 2050-2055 (Durakovic et al., 2023)
Sources: IEA, Net-zero scenario hydrogen outlook (2023); Durakovic et al., Are blue and green hydrogen competitive or complementary? (2023)
Credit: Friedrich Sayn-Wittgenstein, Ellie Valencia, Nadine Palmowski, Hyae Ryung Kim, and Gernot Wagner (12 December 2024); share/adapt with attribution. Contact: gwagner@columbia.edu
Observations
Green and blue H2 are expected to complement grey H2 initially but will almost completely replace it by 2050.
  Government policies and incentives are crucial for rapidly scaling H2 production to meet demand.
  Economies of scale and declining CapEx will accelerate the transition to green and blue H2.
The future split between green and blue H2 is difficult to estimate.
  Green H2 is expected to become competitive as renewables and electrolyzer costs decline.
  The share of blue H2 is highly sensitive to natural gas prices due to its reliance on carbon capture, utilization, and storage.
Chart: 
 | 80 | 45 | 14
 | 63 | 237 | 388
0
50
100
150
200
250
300
350
400
450
2030
2040
2050
143
282
402
Green and blue H2
Grey H2
Green H2 share depends on cost factors such as gas prices

## Slide 38: CKI Green H2 Team
Grace Frascati
Bachelor of Science
CKI Fellow
Hoshi Ogawa
Master of Business Administration
CKI Fellow
Friedrich Sayn-Wittgenstein
Master of Public Administration in Environmental Science and Policy
Team Lead
Ellie Valencia
Master of Business Administration
CKI Fellow
Linfei Zhang
Master of Public Administration in Climate, Energy, and Environment
CKI Fellow
Hyae Ryung (Helen) Kim
PhD in Sustainable Development
Senior Research Fellow
hk2901@columbia.edu
Gernot Wagner
Senior Lecturer, Columbia Business School
Faculty Director, Climate Knowledge Initiative
gwagner@columbia.edu
Nadine Palmowski
Master of Public Administration in Environmental Science and Policy
CKI Fellow
Attribution: Sayn-Wittgenstein et al., "Greening Hydrogen,“ Columbia Business School Climate Knowledge Initiative (2024).

## Slide 39: Appendix

## Slide 40: Glossary
AWE | Alkaline water electrolysis
BOS | Balance of system
CAPEX | Capital expenditure(s)
CAGR | Compound annual growth rate
CCUS | Carbon capture, utilization, and storage
CH4 | Natural gas
CO | Carbon monoxide
CO2 | Carbon dioxide
CO2e | CO2 equivalent, using global warming potential as conversion factor
DOE | Department of Energy
DRI-EAF | Direct Reduced Iron-Electric Arc Furnace production process
ETS | Emissions Trading System
Fe | Iron
FeO2 | Iron oxide
FCEV | Fuel cell electric vehicle
FID | Final Investment Decision
GHG | Greenhouse gas
Gt | Gigatonne, equal to 1 billion metric tonnes
H2 | Hydrogen
IRA | Inflation Reduction Act
kWh | Kilowatt-hour
LCOH | Levelized cost of hydrogen
LH2 | Liquid hydrogen
LOHC | Liquid organic hydrogen carrier
Mt | Million metric tonnes
Mtpa | Million metric tonnes per annum
MWh | Megawatt-hour
NH3 | Ammonia
PEM | Proton exchange membrane
PGM | Platinum group metals
PPM | Parts per million
R&D | Research and development
ROI | Return on Investment
SAF | Sustainable aviation fuel
SOEC | Solid oxide electrolyzer cell
Tonne | Metric ton
TWh | Terawatt-hour