## Slide 1: Reenergizing Nuclear
Quint Houwink, Adele Teh, Hinako Arai, Vedant Bhansali, Khande-Jaé Fisher, Brenda Rain, Christian Sandjaja, Clara Zibell, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner
23 September 2025

## Slide 2: Table of contents
The Nuclear Opportunity
Technological Developments
Deployment and Public Perception
Supply Chain
Global Policy
Fusion Technology
Appendix

## Slide 3: The Nuclear Opportunity

## Slide 4
Key messages The Nuclear Opportunity
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
The average age of nuclear power plants has doubled to 31 years since 2000, indicating the potential of extending their lifetime beyond 40 years.
  Extending the lifetime of all nuclear plants by 10 years generates an additional ~30,000 TWh
Nuclear is expected to generate 7% to 11% of global electricity by 2050, growing capacity 1.5 to 3x.
  Nuclear has the lowest carbon intensity of all energy sources at 5 grams CO2e/kWh, even lower than solar photovoltaic (PV) and wind.
There are four pathways for the future of nuclear power:
  Extending the lifetime of nuclear plants, which has the lowest LCOE and can be safe.
  Building new large reactors, which would significantly reduce emissions but is costly and time intensive.
  Building small modular reactors (SMRs), which provide more flexible nuclear power, but LCOE is still highly uncertain.
  Nuclear fusion, which addresses many of nuclear’s problems, if the technology can be commercialized.
Global nuclear capacity is set to double if all announced and initiated plants materialize; China is responsible for ~30% of all new plants.
Nuclear energy use has decreased from its peak of 17% to 9% today, and deployments have moved from Europe and the United States to India and China.
Properly managed nuclear is safe, land efficient, and low waste compared with other energy sources.
  Highly radioactive waste represents less than 0.25% of total nuclear waste.

## Slide 5: Properly managed, nuclear energy is as safe and low waste as renewables and more land efficient
1 Refers to physical material waste, not GHG pollution. 2 See Appendix for further details on waste, land use, and safety comparison. 3 Decommissioning costs as a share of total costs varies by country.
Sources: IAEA, Radioactive Waste Summary (2023); Our World in Data, Death rates per electricity production (2016); Our World in Data, How does the land use of different energy sources compare? (2022); World Nuclear Association, Radioactive Waste Management (2022); World Nuclear Association, Radioactive Waste: Myths and Realities (2025); Sustainability by Numbers, How much waste do solar panels and wind turbines produce? (2023). Credit: Clara Zibell, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).​
Radioactivity of nuclear waste, 2023
Waste1, land use, and death rates by energy source2, 2023
Chart: 
| 0.03 | 1.67 | 0.16 | 89
 | 0.3 | 19 | 99 | 21
0
100
0
50
100
Waste (kg/MWh)
Land use (m3/MWh)
Nuclear
Solar PV
Wind
Coal
Observations
Very low and low radioactive-level waste types are 78% of total nuclear waste by volume and have a radioactivity of <1%.
Nuclear is the only energy source that fully accounts for all its waste throughout its entire lifecycle, with producers paying for nuclear waste disposal, which is about 10% of total costs.3
Fossil fuel operators typically do not internalize the full environmental costs of CO2 emissions, pollution, and methane leaks, making the energy source appear artificially cheaper.
Solar panels and wind blades are often landfilled at end of life.
Nuclear energy uses the least land (0.3 m3/MWh) and produces the least waste (0.03 kg/MWh) out of the sources evaluated; it has a comparable death rate to wind and solar.
Chart: 
 | 0.23 | 22 | 51 | 27
0.23%
High
Intermediate
Low
Very Low
0,03
0,02
0,04
24,62
Deaths/TWh
Waste category by
radioactivity level
High radioactive-level nuclear waste includes used fuel and has 95% of radioactivity but makes up only ~0.2% of total nuclear waste.

## Slide 6: Disproportionate media coverage of nuclear accidents influences public opinion and policy at the expense of nuclear deployment
Direct deaths vs. newspaper coverage 30 days post deadliest power plant accidents,1 1980-2018
1 Includes only direct deaths. 2 >2,300 disaster-related deaths from post-evacuation stress, in addition to ~19,500 who died in earthquake and tsunami. 3 Controversy exists regarding total deaths from Chernobyl; an additional 19 non-direct radiation exposure deaths occurred between 1984 and 2004.
Sources: WNA, World Nuclear Performance Report (2024); WNA, Chernobyl Accident 1986 (2025); WNA, Fukushima Daiichi Accident (2024); IEA, Evolution of nuclear power generation by region, 1972-2026 (2024); IAEA, A Pioneer in Nuclear Power (1984); Wang et al., Analysis on accident types of coal mine in global major coal producing countries (2023); Bisconti Research National Nuclear Energy Public Opinion Survey (2023); WNA, Safety of Nuclear Power Reactors (2025); Kharecha et al., Implications of energy and CO2 emission changes in Japan and Germany after the Fukushima accident (2019); NRC, Defense-in-Depth (2020); U.S. Bureau of Labor Stats, Mining fatalities rose 21.8% from 2020 to 2021 (2023).
Credit: Clara Zibell, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Houwink et al., “Nuclear Transition” (23 September 2025).
Observations
Gas and coal replaced lost nuclear following Japan’s 2011 Fukushima accident, adding 480 MtCO2 cumulative emissions and an estimated 2,300 air pollution-induced deaths in the country (through 2017).
A 20-point perception gap leads people to believe general support for nuclear is lower than it really is: 56% perceived vs. 78% actual support.
Safety is at the forefront of new reactors; a defense-in-depth approach layers backup systems to prevent or contain accidents at every stage.
Lack of a containment structure at Chernobyl resulted in 30 immediate deaths and thousands more long term.
Nuclear plants
Coal mines
Chart: 
 | 10075
 | 7775
2,300
Deaths
(count)
17,850
Chart: 
 | 1114
 | 634
480
Emissions (MtCO2)
1,748
Total emissions and pollution-induced deaths following Japan’s nuclear phaseout, 2011-2017
Chart: 
 | 0 | 0 | -30 | -29 | -165 | -301 | -24 | -550 | -575
 | 11987 | 1134 | 3333 | 2919 | 108 | 961 | 30 | 37 | 90
165
Upper Big Branch
Heilongjiang
301
29
0
24
Chernobyl3
Ghislenghien
30
550
Three Mile Island
CDMX Pemex
0
575
Fukushima2
Ufa train
11,987
1,134
3,303
2,890
660
6
Soma
Deaths
Newspaper count
Pre-Fukushima existing coal and gas plants
Coal and gas that replaced nuclear plants
Avoidable emissions and deaths caused by coal and gas additions following nuclear phase out
Additional emissions and deaths due to coal and gas use following nuclear phaseout
Chernobyl is the only nuclear accident to have caused direct loss of life.
In the U.S., there were 22.6 deaths on average each year between 2017-2021 in coal mines and oil and gas plants.
Gas plants

## Slide 7: Nuclear is a proven source of stable baseload power, offering a more cost-competitive and reliable solution than renewables
Observations
Nuclear power’s high-capacity factor ensures a stable and continuous electricity supply and accommodates fluctuations from renewable sources.
Standalone solar and wind are cheaper, but the need for large-scale storage and grid upgrades raises their true cost significantly, setting premium for solar at $162/MWh and wind at $177/MWh, compared with SMR projections of $69-$120/MWh.
The energy storage requirement to decarbonize with renewables alone is vastly more expensive and unattainable with today's technology.
Upfront nuclear costs are offset by high-capacity factors, grid stability, and long asset life. This generates a viable alternative to renewables with storage.
To replace nuclear as a baseload source, the United States would need 313 GW of new solar and wind and 992 GWh per day of storage (~10x increase of current storage capacity).
Sources: Lazard, LCOE+ (2025); EIA, Hourly Electric Grid Monitor (2025); WNA, Nuclear Power in the USA (2025). Credit: Christian Sandjaja, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Chart: 
 | 525063 | 524972 | 524484 | 524603 | 524958 | 525220 | 525745 | 526084 | 526145 | 522737 | 525717 | 522217 | 522027 | 525077 | 524936 | 524810 | 521511 | 521526 | 521613 | 524764 | 524619 | 524401 | 523924 | 522695
 | 938307 | 903807 | 879967 | 866676 | 852232 | 866134 | 901452 | 966292 | 1001969 | 935522 | 848372 | 783563 | 736676 | 726100 | 726952 | 732898 | 749609 | 796704 | 893410 | 1009231 | 1072999 | 1070528 | 1042817 | 997218
 | 450321 | 435142 | 419645 | 409517 | 407063 | 406871 | 416927 | 429853 | 450666 | 451590 | 431968 | 417954 | 402031 | 387820 | 380017 | 373717 | 369705 | 373375 | 392548 | 426067 | 459128 | 474071 | 471827 | 461255
 | 188793 | 177202 | 168321 | 161565 | 159274 | 158931 | 170907 | 196109 | 213345 | 210466 | 198502 | 179730 | 160540 | 150337 | 141907 | 137540 | 135148 | 140247 | 156131 | 186663 | 212172 | 225241 | 216163 | 201856
 | 396117 | 393540 | 396656 | 396697 | 394867 | 393140 | 389693 | 392920 | 398385 | 398993 | 378610 | 345345 | 343617 | 349002 | 346697 | 344554 | 345393 | 346579 | 346144 | 345649 | 346982 | 360808 | 380967 | 394813
 | 2632 | 1665 | 1592 | 903 | 940 | 832 | 861 | 1094 | 20749 | 110741 | 240787 | 340203 | 410800 | 451777 | 456887 | 454124 | 437950 | 395973 | 305576 | 186026 | 97036 | 47478 | 10462 | 3638
 | 64713 | 51530 | 41506 | 30010 | 25743 | 26351 | 31311 | 42042 | 50582 | 50205 | 43758 | 40804 | 17984 | -11 | -4366 | -5604 | -9202 | -4725 | 4883 | 26956 | 49357 | 73064 | 84861 | 78060
0
200
400
600
800
1.000
1.200
1.400
1.600
1.800
2.000
2.200
2.400
2.600
2.800
12am
6am
12pm
6pm
12am
Nuclear
Natural gas
Coal
Hydro
Wind
Solar
Other sources
U.S. hourly electricity generation by source, GWh; Feb. 27–March 4, 2025; ISO NE
Nuclear provides a 24-hour stable baseload
Peak period covered by solar
Wind generation is higher at night and in early morning.
Natural gas, coal, and hydro allow dispatchable electricity generation, providing space for cheaper solar and wind.

## Slide 8: Nuclear comparable to batteries and geothermal in baseload and grid-stability properties; outperforms in capacity and discharge duration
Nuclear vs. lithium-ion batteries for grid stability
Nuclear vs. geothermal for baseload energy
Chart: 
| Capacity Factor | Siting Flexibility | Cost | Lifespan | Ramp Rate | Land Use
Nuclear | 5 | 3 | 3 | 5 | 3 | 4
SMR | 5 | 5 | 4 | 5 | 2 | 5
Geothermal | 4 | 2 | 4 | 4 | 4 | 2
EGS | 3 | 4 | 3 | 0 | 0 | 2
1 Points at the extremities of the radar chart show the most desirable features (5=most desirable). See Appendix for reasoning behind scale.
Sources: Lazard, LCOE+ (2025); NREL, Annual Technology Baseline: Batteries (2024); DOE, Grid Energy Storage Technology Cost and Performance Assessment (2022); IAEA, Non-Baseload Operation in Nuclear Power Plants (2023); IAEA, What are SMRs (2023); DOE, Benefits of SMRs (2025); EIA Nuclear FAQ (2025); Feutry et al. Nuclear Power Plant Flexibility at EDF (2019); NREL, Annual Technology Baseline: Nuclear (2024); Detering, Nuclear is a Dispatchable Energy Source (2023); Lovering et al., Land Use Intensity of Electricity Production (2022); IEA, The Future of Geothermal Energy (2024); DOE, What is generation capacity (2025); SLB, Beyond Levelized cost: What’s the true value of geothermal energy? (2024). Credit: Clara Zibell, Khande-Jaé Fisher, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).​
24/7 | 24/7 | 2-10 hours
1,000 MWe+ (CF: 90%) | Up to 300 MWe (CF: 70-90%) | 100+ MW (utility scale) (CF: up to 20%)
Up to 12%/min | Up to 10%/min | Instantaneous
40+ years | 40-80 years (estimated) | 10-15 years
High uncertainty (Pilot/demo stage) | $50-$120/MWh (uncertain) | $44-$131/MWh (Wind/solar plus storage)
Medium | Medium-High | High
Large-scale nuclear plus storage
SMRs
Li-ion battery
Discharge duration
Capacity
Lifespan
Ramp rate
Coupling nuclear with thermal storage enhances maneuverability and allows for quicker response to fluctuating demand; standalone nuclear load following is not economically efficient though currently employed in France.
Low
Moderate
High
Performance
LCOE/LCOS
Load following
Observations
SMRs with superior ramping capabilities can provide longer duration energy support for intermittency than batteries.
Staggering SMRs could surpass the capacity factor of large-scale nuclear (>90%), although this has not yet been proved.
Large-scale nuclear and SMRs stand out against geothermal for their higher capacity, longer lifespan, and lower land-use intensity.
In the United States, large-scale nuclear plants typically provide baseload power, but France’s nuclear fleet is designed to meet grid demand (load following). New reactor designs improve ramp rates:
  EPR: +/- 5% of total power per minute between 60% and 100% of total reactor power.
  AP1000: +/- 10% step load changes between 25% and 100% of full power.
Large-scale nuclear
EGS
Conventional geothermal
SMR
Not yet commercialized:

## Slide 9: Nuclear energy has decreased from its peak of 17% of global power to 9% today as supply moves from the West to APAC
Chart: 
 | 22 | 34 | 40 | 47 | 79 | 92 | 113 | 136 | 152 | 185 | 266 | 291 | 346 | 452 | 545 | 601 | 627 | 671 | 705 | 729 | 749 | 751 | 773 | 770 | 792 | 831 | 839 | 833 | 848 | 860 | 889 | 902 | 907 | 928 | 916 | 914 | 872 | 885 | 825 | 854 | 838 | 812 | 806 | 813 | 787 | 768 | 759 | 762 | 765 | 684 | 732 | 609 | 618 | 626 | 645
 | 41 | 58 | 89 | 121 | 184 | 203 | 266 | 293 | 270 | 266 | 289 | 300 | 311 | 347 | 407 | 439 | 483 | 559 | 561 | 612 | 649 | 656 | 647 | 679 | 714 | 715 | 666 | 714 | 772 | 798 | 793 | 805 | 788 | 813 | 811 | 816 | 837 | 838 | 830 | 839 | 821 | 801 | 822 | 831 | 830 | 840 | 839 | 841 | 843 | 823 | 812 | 804 | 808 | 825 | 830
 | 39 | 50 | 62 | 82 | 93 | 108 | 123 | 130 | 143 | 165 | 182 | 195 | 228 | 277 | 326 | 329 | 358 | 402 | 405 | 378 | 396 | 396 | 421 | 409 | 411 | 433 | 430 | 413 | 424 | 428 | 449 | 454 | 469 | 473 | 477 | 493 | 481 | 476 | 480 | 481 | 501 | 506 | 510 | 519 | 530 | 531 | 538 | 538 | 534 | 521 | 538 | 508 | 523 | 550 | 567
 | 1 | 1 | 2 | 2 | 3 | 3 | 2 | 3 | 3 | 3 | 3 | 2 | 4 | 4 | 5 | 5 | 5 | 6 | 5 | 6 | 6 | 7 | 5 | 6 | 8 | 9 | 10 | 12 | 13 | 17 | 19 | 19 | 18 | 17 | 17 | 19 | 17 | 15 | 19 | 26 | 32 | 33 | 34 | 36 | 37 | 38 | 38 | 38 | 45 | 45 | 44 | 46 | 48 | 62 | 76
 | 8 | 10 | 10 | 20 | 26 | 35 | 32 | 65 | 80 | 94 | 102 | 119 | 142 | 171 | 205 | 224 | 261 | 250 | 259 | 288 | 305 | 314 | 342 | 363 | 394 | 414 | 433 | 459 | 458 | 472 | 470 | 455 | 410 | 455 | 494 | 494 | 450 | 452 | 472 | 482 | 304 | 211 | 195 | 205 | 215 | 219 | 214 | 236 | 253 | 240 | 276 | 282 | 311 | 322 | 330
 | 2 | 15 | 13 | 14 | 14 | 14 | 15 | 17 | 17 | 25 | 43 | 50 | 53 | 55 | 62 | 68 | 70 | 74 | 86 | 97 | 112 | 133 | 171 | 213 | 248 | 294 | 348 | 366 | 408 | 418 | 433 | 435 | 467
Year
TWh
71
73
75
77
79
81
83
85
87
89
91
93
95
97
99
01
03
05
07
09
11
13
15
17
19
21
23
25F
Sources: WNA, World Nuclear Performance Report (2024); IEA, Evolution of nuclear power generation by region, 1972-2026 (2024); IAEA, A Pioneer in Nuclear Power (1984).
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
3%
17%
16%
11%
9%
Observations
Very early after the first power plant was connected to the grid in 1954, nuclear power became a significant fraction of global power generation, producing 10% to 20% of the total.
Where growth was driven by Europe and the United States during the first 30 years, China and India have been responsible for the most growth in nuclear over the past 20 years.
Despite having historic nuclear power production in 2025 at 2,915 TWh, the share of nuclear is decreasing due to the exponential growth in global power demand.
Nuclear power generation, 1971-2025, TWh
European Union
U.S.
Other (incl. Russia)
India
Other Asia
China
12%
17%
17%
14%
10%
8%
Fraction of global power demand, %
x%

## Slide 10: Nuclear projected to generate 6-11% of global electricity by 2050 and prevent 1 to 3 GT CO2 annually until 2050
(*) Assumes average grid carbon intensity per region in 2024. As the average includes nuclear, the actual emissions prevented will be slightly higher until 2030 and lower after 2030 as renewables grow.
Sources: IAEA, Climate Change and Nuclear Power (2022); Enerdata, Total electricity generation (2024); IAEA, Energy, Electricity and Nuclear Power Estimates for the Period up to 2050 (2024); Eneroutlook, CO2 intensity of electricity generation (2022).
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Chart: 
 | 645 | 663 | 738.75 | 665.75 | 687 | 992 | 1267.75
 | 830 | 767.7 | 754.2 | 658.8 | 779.4 | 1088.1 | 1690.2
 | 567 | 460.3 | 536.05 | 614.45 | 500.6 | 853.9 | 1222.05
 | 76 | 83.3333 | 176 | 238 | 105.3333 | 286.6667 | 465.3333
 | 330 | 443.6667 | 675 | 843.3333 | 546 | 942.6667 | 1390
 | 467 | 666 | 932 | 1136.6667 | 824.6667 | 1226.6667 | 1630.6667
460
663
238
614
659
666
546
567
501
287
465
2,915
3,084
3,812
4,157
3,443
5,390
7,666
739
687
645
666
444
105
European Union
U.S.
Other (incl. Russia)
India
Other Asia
China
Nuclear power generation outlook, TWh
Nuclear power generation and emissions prevented, 2025-2050
Annual emissions prevented*, MTCO2
10%
7%
8%
11%
8%
6%
9%
Chart: 
 | 92.106 | 94.6764 | 105.4935 | 95.0691 | 98.1036 | 141.6576 | 181.0347
 | 225.594 | 208.6609 | 204.9916 | 179.0618 | 211.8409 | 295.7456 | 459.3964
 | 188.9811 | 153.418 | 178.6655 | 204.7962 | 166.85 | 284.6049 | 407.3093
 | 41.1388 | 45.1083 | 95.2688 | 128.8294 | 57.0169 | 155.1727 | 251.8849
 | 153.549 | 206.4381 | 314.0775 | 392.403 | 254.0538 | 438.6228 | 646.767
 | 230.3711 | 328.5378 | 459.7556 | 560.7177 | 406.8081 | 605.1147 | 804.4079
154
189
226
92
2025
206
45
153
209
95
2030
95
179
205
105
2040
205
179
2050
230
167
212
98
2030
155
142
2040
181
2050
932
1,037
1,358
1,561
1,195
1,921
2,751
254
252
57
Nuclear fraction of global electricity, %
Actual
Low outlook
High outlook
Observations
Current nuclear power production is expected to grow 1.5x to 3x until 2050 depending on the scenario.
Growth will be driven by the United States and emerging economies, which will be responsible for over half of nuclear power by 2050.
Emissions prevented increase with nuclear power. The true impact decreases as grids decarbonize in other ways.
x%

## Slide 11: Life extension is most economically favorable option; new smaller reactors are costlier yet safer and less wasteful
Policies and regulation
Economicviability
Technology
More favorable
Less favorable
(*) Based on a 20-year extension and 7% real discount rate. (**) Extending life and build of large reactors for 2020, smaller reactors from 2019, fusion from 2023.
Sources: IEA, Nuclear Power and Secure Energy Transitions (2022); IAEA, Climate Change and Nuclear Power (2020, 2024); Fusion Industry Association, The global fusion industry (2024); Lazard, LCOE (2025); NUCNET, Nuclear Fusion (2021); IES, Literature Review of Advanced Reactor Cost Estimates (2020); IEA, Projected costs of generating electricity (2020); IEA, The path to a new era for nuclear energy (2025); Smoliski et al., From conception to technological implementation – SMR’s technology readiness levels (2025).
Credit: Brenda Rain, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Pathway | Life extension | New large reactors | New smaller reactors |  | Fusion
Type | Water reactors | Mostly water reactors | Water reactors | Gas, liquid metal, molten salt reactors | MCF or ICF
TRL | 9 | Varies | 3-8 | Most 2-3 | 3-4
Size | > 1,000 MW | > 1,000 MW | XMR (<50 MW) ¦ Small (< ~400 MW) | XMR (<50 MW) ¦ Small (< ~400 MW) | < 500 MW
Construction or deployment time | Immediate | 10-12 years | 3-5 years | 3-5 years | Earliest by mid-2030s
Potential application | Grid services | Grid services | Grid services, district heating, mining, desalination, data centers | Grid services, hydrogen, hard-to-abate industries, data centers | Grid services
Financing | Mostly public funding, some commercial debt | Mostly public funding | Mostly public-private partnership, but MAG-7 and private offtakers increasing | Mostly public-private partnership, but MAG-7 and private offtakers increasing | Public funding and VC, MAG-7 and private offtakers
Waste management | Conventional | Varies | Less waste | Less waste, reprocessing, extended use | Minimal waste
Safety | Active | Active or passive | Mainly passive | Mainly passive | Naturally the safest
Proliferation | LEU < ~5% | Mainly LEU | LEU < ~5% | 20% > HALEU > 5% | Almost free
Supply chain | Mature for fuel but challenging to replace outdated hardware | Mature for water reactors | Mature for fuel but less for hardware of novelty of designs | Immature for fuel and hardware | Highly immature
Initial cost** | 450-950 USD/kWe for 10-20 years of extension | 1,800-4,300 USD/kWe, but 1-5x cost overruns | ~ 4,000 USD/kWe, highly uncertain (HU) | 6,000-7,000 USD/kWe, HU | 4,000-8,000 USD/kWe, HU
LCOE | $30-$40/MWh* | $138-$222/MWh | $50-$120/MWh, HU | $50-$120/MWh, HU | $20-$100/MWh, HU

## Slide 12: The average age of nuclear power plants doubled since 2000 to 31 years, indicating the need to extend their lifetime beyond 40 years
Sources: WNA, World Nuclear Performance Report (2024); Global Energy Monitor, Global Nuclear Power Tracker (2024).
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Chart: 
 | 3220 | 6168 | 8907 | 15877 | 25200 | 35341 | 38183 | 44741 | 46554 | 50182 | 57711 | 68907 | 62559 | 66945 | 85219 | 112302 | 132997 | 144180 | 154629 | 150385 | 155280 | 144878 | 127660 | 99555 | 80580 | 66135 | 49375 | 37232 | 31537 | 29053 | 29980 | 25813 | 28758 | 28244 | 25986 | 27796 | 27161 | 28565 | 23740 | 21349 | 15859 | 16423 | 17819 | 17448 | 22380 | 27505 | 39386 | 44081 | 51953 | 55347 | 53440 | 58508 | 59997 | 60900 | 52316
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1022 | 3220 | 6168 | 8907 | 15877 | 25200 | 35341 | 38183 | 44741 | 46554 | 50182 | 57711 | 68907 | 62559 | 66945 | 85219 | 112302 | 132997 | 144180 | 154629 | 150385 | 155280 | 144878 | 127660 | 99555 | 80580 | 66135 | 49375 | 37232 | 31537 | 29053 | 29980 | 25813 | 28758 | 28244 | 25986 | 27796 | 27161 | 28565 | 23740 | 21349 | 15859 | 16423 | 17819 | 17448 | 22380 | 27505 | 39386
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1022 | 3220 | 6168 | 8907 | 15877 | 25200 | 35341 | 38183 | 44741 | 46554 | 50182 | 57711 | 68907 | 62559 | 66945 | 85219 | 112302 | 132997 | 144180 | 154629 | 150385 | 155280 | 144878 | 127660 | 99555 | 80580 | 66135 | 49375 | 37232 | 31537 | 29053 | 29980 | 25813 | 28758 | 28244 | 25986 | 27796 | 27161 | 28565 | 23740
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1022 | 3220 | 6168 | 8907 | 15877 | 25200 | 35341 | 38183 | 44741 | 46554 | 50182 | 57711 | 68907 | 62559 | 66945 | 85219 | 112302 | 132997 | 144180 | 154629 | 150385 | 155280 | 144878 | 127660 | 99555 | 80580 | 66135 | 49375 | 37232 | 31537 | 29053 | 29980
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1022 | 3220 | 6168 | 8907 | 15877 | 25200 | 35341 | 38183 | 44741 | 46554 | 50182 | 57711 | 68907 | 62559 | 66945 | 85219 | 112302 | 132997 | 144180 | 154629 | 150385 | 155280 | 144878 | 127660
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1022 | 3220 | 6168 | 8907 | 15877 | 25200 | 35341 | 38183 | 44741 | 46554 | 50182 | 57711 | 68907 | 62559 | 66945 | 85219
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1022 | 3220 | 6168 | 8907 | 15877 | 25200 | 35341 | 38183
1970
1980
1990
2000
2010
2020
3
35
67
158
243
267
281
300
308
332
368
396
48+
40-47
32-39
24-31
16-23
8-15
<8
Nuclear plant capacity by age of reactor, GW, 1970-2024
<5
Average age of nuclear plant, years in operation
xx
<5
5
6
8
12
16
20
25
27
30
31
Observations
Global capacity of operational nuclear plants grew rapidly to 243 MW in 1990, which then gradually grew to 396 MW today.
Between 2000 and 2010, few new plants were constructed, leading to a rapid increase in average age that corresponded to the number of years passed (+9 years in 10 years’ time).
Since 2010, new plants have become operational, stabilizing the increase in average plant age.
With >250 MW capacity at >24 years of age, extending plants’ lifetime is extremely promising.
The U.S. didn’t build any nuclear reactors between 1996 and 2016 and has built only ~3 MW since, compared with 100 MW before 1996.
Between 1982 and 1992, France alone built ~70 GW of nuclear power, which will reach its design lifetime in the next decade.
Deep dive: Extending lifetime

## Slide 13: Extending the lifetime of all nuclear plants by 10 years adds ~30,000 TWh and saves ~950 MtCO2e but comes with uncertainty
Chart: 
0
50
100
150
200
250
300
350
400
2025
2030
2040
2050
2060
2070
2080
2090
2100
GW
(*) Assumes 2025 carbon intensity of grids respective to global distribution of nuclear power today. (**) Assumes Canada’s carbon grid intensity in 2022 (100 g CO2e/kWh).
Sources: IAEA, Climate Change and Nuclear Power (2020); Global Energy Monitor, Global Nuclear Power Tracker (2024); WNA, Global Nuclear Industry Performance (2024); Bruce Power, Life-Extension Program & MCR Project (2023); CEC, Provincial and Territorial Energy Profiles – Canada (2022).
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
40 years
50 years
60 years
70 years
80 years
Lifespan
31 PWh
24 PWh
28 PWh
28 PWh
30% of nuclear capacity today comes from nuclear reactors at ages 40 to 60 years. Most of these are scheduled to retire in the 2030s.
Observations
The 130 GW nuclear capacity coming from nuclear plants at ages over 40 years prove the feasibility of extending lifetimes, although this is uncharted terrain.
Extending plants’ lifetime is cheap and believed to be safe.
An extension of just 10 years of all existing nuclear power generates ~31,000 TWh, which saves 950 MTCO2e*.
This is equivalent to ~2% of annual emissions today. Extending nuclear reactors can thus abate 0.2% of global emissions.
Case study: Bruce Power
In 2015, Bruce Power agreed to invest in refurbishing and extending the lifetime of its nuclear fleet until 2066.
This meant increasing the lifespan for 2 GW power from 40 years to 80 years.
Bruce Power thereby reduces a total of 73 MTCO2e.
Deep dive: Extending lifetime

## Slide 14: Palisades restart driven by state-level support for nuclear and workforce advances, but technical and regulatory barriers remain
Operating plant
Sources: Holtec, Holtec and Wolverine ink historic PPA (2023); Holtec, Palisades restart program – now in the inspections and maintenance phase (2024); Holtec, Palisades cooling system upgraded (2024); Holtec, Historic repowering of Michigan’s Palisades, Holtec obtains up to 1.52B in conditional loan commitment from the DOE (2024); Holtec, Holtec closes $1.52B DOE loan to restart Palisades (2024); DSIRE, NC Clean Energy technology center, Renewable Energy standard (2024).
Credit: Brenda Rain, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Case study: Palisades, Michigan (U.S.)
Filed submission to NRC to reauthorize plant operation
Submitted application to DOE’s LPO for federal funding
Received approval of federal loan to be delivered in 2024 ($150M)
Received accreditation for its Maintenance and Technical Training Program
Upgraded heat exchanger (cooling system)
26 former Palisades operators completed their requalification, ensuring human capital is available by 2026
Started initial training accreditation
Completed startup readiness assessment to ensure highest safety and operation procedures are implemented
Successfully completed emergency preparedness exercises
Received conditional commitment of $1.52B loan guarantee of LPO to support the plant’s resumption
Waiting for response about regulatory submittals
September; expected operation by last quarter of 2025
NRC draft Environmental Assessment completed; didn’t find significant impact from resumed power operations
Received full accreditation for its Operation Training Program from NNAB
Signed multi-decade PPA with nonprofit rural cooperative (Wolverine)
Aug.
March
June
Sept.
Oct.
Feb.
April
May
June
Aug.
Consumers Energy
2024
2025
Chart: 

Silent period
Entergy
Holtec
2023
Holtec closed $1.52B DOE loan to restart Palisades; in March 2025, it is reconfirmed
Received $1.3B of support from USDA to help regional cooperatives with the PPA
Sept.
Early closure resulted in the loss of 739 jobs and an annual loss of $259 million across Berrien, Cass, and Van Buren counties.
Palisades project’s milestones (2023-2025)
May 2022
Dec. 1971
Aging infrastructure and repairs raise safety concerns: Adequate performance of steam generation tubes and control-road seal issues requires a more thorough analysis to ensure the required performance.
Regulatory hurdles: NRC moved the estimated completion from July 31 to September 30, increasing completion risk.
State’s climate commitment in Public Act 235: 80% of energy must come from carbon-free sources by 2035.
Market and political momentum: Two executive orders approved in January 2025 (14154, 14156) favor nuclear financial outlook.
Regulatory support structures: NRC has established a dedicated panel to guide the restarting.
Project details
Capacity: 805 MW
Location: Michigan
Technology: PWR
Extension period: ~26 years (2051)
Owner: Holtec, previously Entergy
Other considerations: Plans to include two additional SMRs; 300MW to benefit from site permits and skilled workforce
Tailwinds
Headwinds

## Slide 15: Global nuclear capacity set to double if all announced and initiated plants materialize; China responsible for ~30% of new plants
Sources: Global Energy Monitor, Global Nuclear Power Tracker (2024); IEA, The Path to a New Era for Nuclear Energy (2025); IEA, Nuclear Power and Secure Energy Transitions (2022).
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
USA
Chart: 
 | 102475
 | 0
 | 30000
30
102
Observations
Global nuclear capacity today is 396 GW, with an additional 75 GW under construction and 270 GW in pre-construction or announced.
Today, most of the capacity is in the United States and Europe, representing ~50% of all reactors.
However, China is leading by far in the number of nuclear plants being built, representing nearly half of all plants under construction.
Europe has announced 71 new plants, nearly equaling China’s 74 planned plants.
Typical development time for a plant in China is five to eight years vs. eight to 12 years in Europe, India, and the U.S.
50
1
5
CAN
Chart: 
 | 14629
 | 0
 | 8000
8
15
UK
Chart: 
 | 6534
 | 3440
 | 8000
8
3
7
3
0
3
4
0
4
India
Chart: 
 | 7540
 | 5900
 | 24000
24
6
8
4
1
5
China
Chart: 
 | 58134
 | 33904
 | 74000
74
34
58
17
9
7
RUS
Chart: 
 | 28576
 | 4212
 | 21000
21
4
29
6
2
4
UKR
Chart: 
 | 13835
 | 0
 | 4000
4
0
14
4
0
0
EU
Chart: 
 | 100745
 | 2121
 | 71000
71
2
101
30
0
11
ROK
Chart: 
 | 27071
 | 2800
 | 2000
2
3
27
6
0
0
JAP
Chart: 
 | 11608
 | 2756
 | 0
0
3
12
2
1
0
World
Chart: 
 | 396484
 | 74925
 | 270000
270
75
396
741
140
18
47
Operating, MW
Construction, MW
Announced/Pre-construction, MW
Number of plant locations within category
Global distribution of nuclear capacity, GW and plant count, 2024
Chart: 
 | 1940
 | 4800
 | 2000
2
5
2
1
1
Chart: 
 | 1763
 | 0
 | 1000
1
2
2
0
ARG
0
1
Africa
Japan has ~21 GW in suspended operation.
Deep dive: New build – large reactors

## Slide 16: Off-grid SMRs are a mid- to long-term solution for increased energy demand from hyperscale and colocation data centers
Observations
Long timelines for transmission connection, gas turbines (more than seven years), and power supply stress the need for off-grid solutions.
Off-grid solar is a strong option for training-only data centers, when uptime requirements are slightly relaxed.
The small size and modularity of SMRs allow these to be sited closer to data centers. This is ideal for inference AI workloads, which have low-latency and high-redundancy requirements.
The data center construction timeline is up to seven years in the United States. SMR technology is expected to be deployed after 2030.
Chart: 
| 50 | 30 | 10 | 5
 | 2.5 | 2 | 0.8 | 0.5
 | 0.5 | 0.9 | 0.2
0.0
3.0
Distance from urban areas (km)
Spatial concentration2
Hyperscale
Colocation
Edge
Distributed
SMRs
Large nuclear plants
Off-grid solar
 | Training AI | Inference AI
Hyperscale | Primary | Common
Colocation | Limited | Common
Edge | Not suitable | Primary
Distributed | Not suitable | Primary
High uncertainty
Chart: 
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
 | 415 | 500 | 590 | 770 | 940 | 1100 | 1250 | 1391.4286 | 1520 | 1600 | 1650 | 1700
 | 415 | 482 | 560 | 680 | 780 | 870 | 945 | 1020 | 1080 | 1130 | 1176.6364 | 1220
 | 415 | 450 | 500 | 550 | 620 | 660 | 680 | 686 | 692 | 698 | 704 | 690
 | 415 | 448 | 485 | 515 | 550 | 575 | 595 | 620 | 645 | 665 | 685 | 702.5
Projected global data center energy demand1 (TWh)
Urban proximity and spatial concentration2
SMRs can power spatially concentrated data center clusters.
Deep dive: New build – SMRs
1 IEA Scenarios are based on projected AI uptake, energy sector bottlenecks, and efficiency improvements. 2 Spatial concentration = electrical output/land area used.
Sources: IEA, Energy and AI (2025); IEA, Electricity (2025); Baranko et al., Fast, scalable, clean, and cheap enough (2024); Ember, Global Electricity Review (2025); BNEF, How AI Influences US Data Center Power Demand (2025); Gartner, Power Shortages Will Restrict 40% of AI Data Centers by 2027 (2024); Last Energy, On-Site Nuclear Power (2023).
Credit: Clara Zibell, Khande-Jaé Fisher, Isabel Hoyos, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
IEA liftoff
IEA base
IEA headwinds
Bloomberg ETS – U.S. demand
Data center type
Energy source
Data center types

## Slide 17: Technological Developments

## Slide 18
Key messages Technological Developments
Credit: Vedant Bhansali, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
There are four main types of coolant: water, gas, metal, and molten salt.
  Pressurized water reactors (PWR) are most common, but they are complex due to the high pressure needed to keep the water liquid.
  Boiling water reactors (BWR) are simpler than PWR, and therefore modern reactors are typically BWR; however, they do have to deal with radioactive steam.
  Gas-cooled reactors have higher thermal efficiency but need specialized materials.
  Liquid metal reactors have high thermal efficiency but also have chemically reactive materials that could cause explosions when leaks occur.
  Molten salt reactors (MSR) have higher thermal efficiency and fuel cycle flexibility but need special tubing to deal with corrosion.
Reactors are similar in their mechanics, although they use different coolants; small modular reactors (SMRs) simplify the existing design.
Nuclear-produced “pink” hydrogen offers an emission-free, cost-competitive, and subsidized option, but scaling remains a challenge.
Water-cooled reactors have evolved significantly over four generations to become safer, standardized, more efficient, and more modular.

## Slide 19: Emerging SMR technology is small and flexible, providing an off-grid and off-site solution for nuclear power
Sources: European Commission, Small Modular Reactors Explained (2025); NEI, Nuclear Plant’s Footprint (2025); IAEA, What are SMRs? (2023); Statista, Construction Time for Nuclear Reactors Worldwide (2024)​; Holtec, SMR FAQs (2025); CNBC, GE Vernova Deploying SMRs (2024). Credit: Adele Teh, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Description | Large-size nuclear power plants | Small modular reactors
Electrical capacity (MWe/unit) | >1,000 | Up to 300
Fuel | Typically light water reactors | May use various coolants and fuel types
Refueling frequency | Every 1-2 years | Every 3-7 years, even up to 30 years
Safety features | Active systems (operator or power dependent) | Passive systems (self-shutdown)
Land area requirement (square miles) | 1.3 | 0.01
Construction approach | Custom built on-site | Factory fabricated and shipped to sites for modular assembly
Siting flexibility | Low; large dedicated sites required | High; suitable for remote, urban, and industrial areas
Construction time | 10 years, often with overruns | 3-5 years
Cost to build ($) | 10B-15B | 2B-4B
Cost structure | Economies of scale; high upfront investment with high financial risk | Economies of series; lower initial capital, but costs per MW may initially be high
LCOE ($/MWh) | 140-220 | 50-120 (uncertain)
Use case | Baseload power for national grids | Flexible: remote/off-grid
Waste management | Established waste management protocols in place, but long-term disposal continues to face public and political resistance | Some studies suggest higher radioactive waste per MWh, though advanced modular reactors may improve waste handling
Deployment status | Mature, globally deployed | First-of-a-kind stage, few operational units; commercial viability yet to be proved
Supply chain readiness | Mature, although often highly specialized and slow moving | Emerging; key components still under development and supplier confidence is needed to scale up
Standards and regulations | Established framework | Adapting existing frameworks and emerging regulatory approaches
High
Medium
Low
Technical specifications
Economics
Operations
Desirability

## Slide 20: All reactor types use similar mechanics and different coolants; small modular reactors simplify the existing design
Sources: U.S. DOE, NUCLEAR 101: How Does a Nuclear Reactor Work?, 2023; NEA, The NEA Small Modular Reactor (SMR) Strategy (2025); IN, Advanced Small Modular Reactors (2025).
Credit: Vedant Bhansali, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
How a typical reactor works
Fuel rods contain fissile material (e.g., U-235) where fission reactions occur, generating heat.
Moderator rods slow down fast neutrons from fission events to increase the probability of further fission.
Control rods control the speed of the reaction by absorbing excess neutrons.
Pressurizer maintains coolant pressure to prevent boiling (for PWR).
Heat transfers to secondary water loop, producing steam.
High-pressure steam flows to spin turbine blades.
The generator converts mechanical energy into electricity.
How SMRs are different
Compact, integrated containment structure
Simplified, passive cooling systems without external pumps
Factory-fabricated modules that allow for faster construction and deployment
Modular and built from components to be factory manufactured and then transported and assembled at the final site
1
2
4
5
7
6
1
2
3
4
4
Coolant systems are the main mechanical difference between reactor types:
Pressurized water reactors (PWR) need high pressure to prevent water from boiling and a second loop for steam generation.
Gas-cooled reactors require specialized pressure vessels to contain the gasses.
Liquid metal and molten salt need specialized equipment to prevent solidification.
3
1
2
3
4
5
6
7
1
2
3
4

## Slide 21: Water-cooled reactors dominate today’s nuclear landscape; advanced coolant types offer efficiency and safety gains
(*) LCOE values are highly uncertain. They depend on assumptions about learning rates, deployment scale, financing costs, and regulatory environment.
Sources: IET, Nuclear Reactor Types (2024); WNA, Nuclear Power Reactors (2025); IAEA, Comparative Evaluation of Nuclear Energy System Options (2023). Credit: Vedant Bhansali, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Water as coolant and moderator; water boils inside the reactor core
Gas (CO₂ or helium) as coolant
Liquid metals (e.g., sodium, lead) as coolant
Molten fluoride or chloride salts used as coolant and sometimes fuel; includes both liquid-fueled and solid-fueled designs (e.g., Kairos FHR); high thermal efficiency and strong passive safety
Description
200
~30
<1
<1
Global capacity, GW, 2024
Boiling water
Gas cooled
Liquid metal
Molten salt
Simpler system than PWRs; direct steam cycle (no steam generator needed); good operational flexibility
High thermal efficiency (~41%); uses diverse fuels; passive safety features (low pressure, high heat tolerance)
Very high thermal efficiency (~40–45%); can “breed” more fuel than consumed; operates at low pressure
Pros
Highest thermal efficiency (~45–50%); strong passive safety (negative temp coefficient); fuel cycle flexibility (e.g., thorium)
Steam is radioactive (direct contact with core); more turbine contamination risk
Needs specialized materials for high temp; higher capital and maintenance costs
Coolants are chemically reactive; material corrosion risks
Cons
Corrosion and material compatibility challenges; no standard regulatory path yet
Scalability
H
M
M
H
$50–$100 per MWh
$70–$120
$80–$140
$90–$150
LCOE*, 2024
Maturity
H
M
L
Water as coolant and moderator; water stays liquid under pressure
950
Pressurized water
Most common reactor type globally; proven safety systems; high capacity for grid-scale power
High-pressure operation increases system complexity; large infrastructure footprint
H
$50–$100 per MWh
H
M

## Slide 22: HTGRs, LMRs, and MSRs have higher efficiency, produce less nuclear waste, and have versatile industrial applications
Sources: Quadrennial Technology Review, Advancing Clean Electric Power Technologies (2015); IAEA, High Temperature Gas Cooled Reactor Fuels and Materials (2010); Idaho National Laboratory, Baseline Concept Description of a Small Modular High Temperature Reactor (2014); Terrestrial Energy, Molten salt reactor technology (2024); IAEA, Molten salt reactors (2024); WNA, Molten salt reactors (2024); Generation IV International Forum, Molten salt reactors (MSR) – Criteria and technologies (2024); Pacific Northwest National Laboratory, Technical report on molten salt reactors (2020); Moltex Energy, Moltex demonstrates reactor’s unique capability to consume nuclear waste and close the fuel cycle (2024); WNA, Nuclear Power Reactor Characteristics (2016). Credit: Hinako Arai, Vedant Bhansali, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Key metrics comparing different types of nuclear reactors
Pressurized water reactor (PWR)
Pressurized light water | Light water | Helium or CO₂ (remains gas) | Liquid sodium or lead, no moderator | Molten salt with dissolved fissile material
33-37% | 33% | ~50% | 33-43% | 45-50%
Active safety | Active safety | Passive safety | Passive safety | Passive safety, lower risk of explosion
High | Higher than PWR | Low | Low | Low
About 315°C, high pressure | 285°C, medium pressure | 750-950°C, low pressure | 480-550°C, low pressure | ~700°C, low pressure
High-temperature gas-cooled reactor (HTGR)
Molten salt reactor (MSR)
Thermal efficiency
Operating temperature
Safety
Low
Moderate
High
Performance
Waste volume
Liquid metal reactor (LMR)
Coolant
Boiled water reactor (BWR)
Water-cooled reactor
Deep dive: MSRs and HTGRs

## Slide 23: Water-cooled reactors have evolved significantly over time to become safer, standardized, more efficient, and more modular
Description | Early reactor protype | Commercial power reactors, usually LWR | Advanced light water reactors | Advanced reactors
Efficiency | 30% | 33% | 39% | 45%
Fuel | Low-enriched uranium (LEU) (2-3%) | LEU (3-5%) | LEU (4-5%) and mixed oxide (MOX) fuel | HALEU (>5%), thorium, MOX, recycled fuels, and refueling cycles between 30 months and 30 years.
Status of commercial reactors |  |  |  | 
Global installed capacity | 0 GW | 271-348 GW | 48 – 125 GW | ~0.2 GW
Ratio in US | 0% | 97.8% | 2.2% | 0%
Pros | Demonstrated the civil use of nuclear fission | Used for large, commercial-scale power generation; relies on active safety systems; based on a set of design principles; has prolonged lifetime | Improved design and economic; streamlined licensing from standardized designs and mass-produced parts; enhanced safety | Improved safety; reduced waste and OpEx
Cons | Short lifespan (20 to 30 years); no standardized designs; small capacity | Expensive and time consuming to build | Construction delays and cost overruns | High R&D costs; regulatory hurdles; requires new fuel cycle infrastructure
Sources: Global Energy Monitor, Global Nuclear Power Tracker (2024); WNA, Economics of nuclear power (2023); WNA, Advanced Nuclear Power Reactors (2021); Columbia University Center on Global Energy Policy, The Uncertain Costs of New Nuclear Reactors (2023); U.S. DOE, Pathways to Commercial Liftoff: Advanced Nuclear (2023); Cleantech Group, Advanced Nuclear Fission’s Role in the Energy Transition (2020); Reuters, China starts up world's first fourth-generation nuclear reactor (2023); Center for Advanced Nuclear Energy Systems, 2024 Total Cost Projection of Next AP1000 (2024); Reinberger et al., The Technological Development of Different Generations and Reactor Concepts (2019).
Credit: Hinako Arai, Vedant Bhansali, Brenda Rain, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Key differences in reactors by generation
  Advanced reactors
Deep dive: Traditional reactors
Pre- construction
In construction
Operational
Retired
  1950
  1960
  1970
  1980
  1990
  2000
  2010
  2020
  2030
  2035
Period of reactor development
Gen I
Gen II
Gen III
Chart: 
 | 0
 | 0
 | 0
 | 30
Gen IV
The last Gen I shutdown in 2015 in the U.K.
Chart: 
 | 7
 | 5
 | 342
 | 193
Chart: 
 | 27
 | 23
 | 50
 | 0
Chart: 
 | 56
 | 35
 | 23
 | 0
Chart: 
 | 2
 | 5
 | 3
 | 0
The first Gen IV reactors started commercial operation in 2023 in China, highlighting the economic uncertainty about these models.​
Gen III+

## Slide 24: Nuclear-produced ‘pink’ hydrogen offers an emission-free, cost-competitive, and subsidized option; scaling remains a challenge
(*) LCOH of pink hydrogen is from Lazard; other LCOH is from IEA.
Sources: National Grid, Hydrogen colour spectrum explained (2023); Hydrogen Insight, Nuclear hydrogen makes a lot of intellectual sense: U.S. energy loans head (2023); Harvard Kennedy School, Belfer Center for Science and International Affairs, The colors of hydrogen (2024); WNA, Hydrogen production and uses (2024); U.S. DOE, Production cost of high-temperature electrolysis (2020); IEA, Global Hydrogen Review 2024 (2024); CTVC, Final Hydrogen Tax Credits Get Greenlight #228 (2025); Lazard, LCOE+ (2024). Credit: Vedant Bhansali, Quint Houwink, Brenda Rain and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Comparison by types of hydrogen production
Levelized cost of hydrogen (2023)
Subsidy under IRA (Section 45V)
Chart: 
 | 1.7 | 0.8 | 1.5 | 2.7 | 3.07
 | 3.4 | 4.9 | 5.2 | 9.3 | 0.79
USD/kg H2
Brown (Coal)
Gray (Natural Gas)
Blue (Natural Gas with CCUS)
Green (Wind or Solar PV)
Pink*
Chart: 
 | 18 | 10 | 1 | 0 | 0
 | 1 | 9 | 3
Tons of CO2/kg H2
Brown (Coal)
Gray (Natural Gas)
Blue (Natural Gas with CCUS)
Green (Wind or Solar PV)
Pink
0
0
Chart: 
 | 0 | 0 | 20 | 33.4 | 100
 | 13.4 | 66.6 | 0
0
40
60
80
100
Range of carbon-credit eligibility (%)
Brown (Coal)
Gray (Natural Gas)
Blue (Natural Gas with CCUS)
Green (Wind or Solar PV)
Pink
0
0
~$3/kg H2
20%
33.4%
Hydrogen tax credits are tied to lifecycle GHG emissions.
With pink hydrogen’s high capital costs (~$5B+ per reactor) and limited infrastructure, tax incentives can support scaling adoption.
Carbon intensity (2024)
99% of the current global hydrogen supply still comes from gray or brown hydrogen.
Issues associated with nuclear plants – including nuclear waste, a long construction period, and high construction cost – as well as difficulties in retrofitting existing plants to produce hydrogen are hindering deployment.
Pink hydrogen uses nuclear-powered electrolysis, offering 24/7 reliability, lower cost, and emission-free production.
Pink hydrogen
Other hydrogen
~$1/kg H2
~$0.6/kg H2
Extra credit by low carbon intensity
Deep dive: Pink hydrogen

## Slide 25: TerraPower leads in advanced reactors, breaking ground in 2024 for its 345 MW natrium reactor planned for 2030
(*) Numbers represent rough estimate from CEO interviews. Sources: TerraPower, About TerraPower (2025); Businesswire, TerraPower Isotopes Brings Actinium-225 to Market (2024); Reuters, Bill Gates' $4 bln high-tech nuclear reactor set for Wyoming coal site (2021); WNN, TerraPower, CNNC team up on travelling wave reactor (2015); Neutron Bytes, TerraPower to Leave China, but Bill Gates Is Still in the Game (2019). Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).​
TerraPower’s unique design
For its design, TerraPower uses the metal sodium (Latin name: natrium) as its coolant.
Where water requires high pressure to prevent boiling above 100°C, sodium doesn’t boil until 883°C, ideal for a reactor operating at ~500°C.
Sodium is highly reactive with water and oxygen; a leak can cause explosions. Historically, liquid metal reactors have been more expensive.
TerraPower believes sodium will allow modular fabrication and have non-nuclear systems, bringing down construction and regulatory costs.
Beyond its unique cooling system, TerraPower includes salt heat storage, which should help the plant react to power demand peaks.
TerraPower’s approach to funding*
2006
2010
2015
2020
2018-19
2021
2024
2030
TerraPower founded by Bill Gates to develop advanced nuclear power
For its first years, TerraPower focused on a traveling wave reactor (TWR), which has much higher fuel efficiency, theoretically requiring no fuel replacements for its lifetime
Starts a JV with Chinese CNNC to build a 600 MW TWR prototype in China
The U.S. stops all partnerships with China on nuclear, killing the JV
Pivots to developing a a natrium reactor together with GE Hitachi
Selects Kemmerer, Wyoming, as its first reactor site
Breaks ground in Wyoming for the 345MW, $4 billion FOAK reactor
TerraPower Isotopes starts commercial-scale production of actinium, which is used in clinical trials for cancer research
The Wyoming plant to deliver its first power to the market
Energy island
Nuclear island
The $4 billion Wyoming plant is a first of a kind (FOAK), meaning its costs are higher than for subsequent reactors.
Rather than assigning all those costs to ratepayers, TerraPower charges regular electricity prices and covers the difference with a $2 billion federal grant and $1 billion equity investment.
It believes that investors and the government will benefit from the IP gained in the FOAK.
Chart: 
 | 1
 | 1
 | 2
Breakdown of Wyoming plant funding
Govt. grant
Equity investors
Ratepayers
$4B
Case study: TerraPower

## Slide 26: Deployment and Public Perception

## Slide 27
Key messages Deployment and Public Perception
Nuclear energy becomes cost competitive when full system costs are counted; matching renewable reliability can increase costs to $162-$177/MWh due to the necessity for storage.
  Nuclear complements intermittent renewable sources by providing low-carbon and reliable baseload power.
Many nuclear power plants store their waste using interim dedicated on-site disposal.
  Deep geological disposal will be needed to dispose of high-level nuclear waste.
At an LCOE of $182/MWh, nuclear is far above gas or renewables with storage solutions; reactor life extension is the cheapest option at $30-$40/MWh.
  Nuclear LCOE has increased 49% since 2009, making it the least affordable energy source option.
  Addressing the capital cost of nuclear will be key in achieving a commercially viable energy transition.
SMR projects are facing severe cost overruns and delays, highlighting scale and execution challenges for first-of-a-kind (FOAK) reactors.
  SMR projects so far have adjusted cost projections upward by up to 400% and increased timelines from four to 12 years.
  This is typical in FOAK projects and doesn’t indicate SMRs are less feasible than other reactor types.
The majority of the public supports nuclear energy deployment, driven by a strong preference for energy reliability.
  There is a strong correlation between the number of reactors operational in a country and public support.
  46% of survey respondents support the use of nuclear energy, while 28% oppose it.
Credit: Christian Sandjaja, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).

## Slide 28: At an LCOE of ~$182/MWh, nuclear is far above gas or renewables with storage solutions; reactor life extension is cheapest option
Chart: 
 | 123 | 96 | 95 | 96 | 104 | 112 | 117 | 117 | 148 | 151 | 155 | 163 | 167 | 173.5 | 180 | 182 | 180
 | 111 | 111 | 111 | 102 | 105 | 109 | 108 | 102 | 102 | 102 | 109 | 112 | 108 | 112.5 | 117 | 118 | 122
 | 89 | 89 | 89 | 89
 | 83 | 96 | 95 | 75 | 74 | 74 | 64 | 63 | 60 | 58 | 56 | 59 | 60 | 65 | 70 | 76 | 78
 | 203.922 | 197.266 | 206.095 | 174.729 | 148.688 | 181.632 | 148.289 | 122.831 | 112.199 | 105.692 | 91.183 | 88.097 | 78.844 | 80.651 | 74.5056 | 74.5056 | 70
 | 75 | 71.25 | 67.5 | 60
 | 251.46 | 243 | 157 | 125 | 98 | 79 | 65 | 55 | 50 | 43 | 41 | 37 | 36 | 48 | 60 | 61 | 58
 | 135 | 124 | 71 | 72 | 70 | 59 | 55 | 47 | 45 | 42 | 40 | 40 | 38 | 44 | 50 | 50 | 61
 | 35 | 35 | 35 | 35
180
200
0
20
220
40
60
240
80
160
360
100
120
140
2010
95
96
112
2015
117
96
155
2020
2025
151
LCOE by technology, $/MWh
Sources: Lazard, LCOE+ (2025); Statista, Construction Time for Nuclear Reactors Worldwide (2024)​. Credit: Christian Sandjaja, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).​
$141-$220
$20-$57
$37-$86
$33-$131
$67-$179
$47-$170
LCOE range (U.S.), $/MWh, 2025
$45-$133
Nuclear
Coal
Onshore wind w/ storage
Gas combined cycle
Offshore wind
Solar PV w/storage
Solar PV
Onshore wind
Nuclear extension
$30-$40
Nuclear
Coal
Onshore w/storage
Gas
Solar w/storage
Solar
Onshore wind
Nuclear life extension
$70-$157
Offshore
Observations
Factors that influence nuclear LCOE increases:
Capital cost – Nuclear power plants have high upfront capital costs, which significantly impacts their LCOE.
Construction delays – Median construction time is 11 years, with most countries experiencing at least one year of delay compared with scheduled startup dates.
Financing cost – High interest rates have particularly affected capital-intensive projects like nuclear power plants.
Renewables with four-hour storage aids grid flexibility but can't ensure 24/7 reliability, underscoring the need for firm sources like nuclear as renewables grow.
Nuclear LCOE should be assessed against solar and wind with storage, as it provides continuous power.
60
35

## Slide 29: Lowering capital cost, which account for ~80% of LCOE component costs, is key to scaling nuclear technologies
LCOE cost components*, $/MWh
Sources: Lazard, LCOE+ (2025); World Nuclear Association, Economics of Nuclear Power (2024); OECD Nuclear Energy Agency, Unlocking Reductions in the Construction Costs of Nuclear (2020); Statista, PPI of concrete products in U.S. 1926-2023 (2024); Institute for Progress, Why Does Nuclear Power Plant Construction Cost So Much? (2023); U.S. Bureau of Labor Statistics, Producer Price Index by Industry (2024); U.S. Bureau of Labor Statistics, Producer Price Index by Commodity: Metals and Metal Products: Iron and Steel (2024). Credit: Christian Sandjaja, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Chart: 
 | 46.5 | 145 | 92 | 150.5
 | 5.5 | 13.5 | 11 | 16
 | 4 | 4.5 | 4.5 | 4.5
 | 22.5 | 37 | 15.5 | 9
4
Gas Combined Cycle
5
Gas Peaking
5
6
5
79
200
123
180
Coal
Chart: 
 | 0.58324
 | 0.083292
 | 0.083292
 | 0.24998
8%
8%
25%
Investment Cost Breakdown
58%
Owner’s
Contingencies
Interest during construction
100%
EPC
*Self-analysis based on Lazard LCOE+
Chart: 
 | 16
 | 38
 | 27
 | 8
 | 7
 | 4
38%
27%
8%
7%
4%
Materials & Components Cost Breakdown
16%
Reactor plant
Turbine plant
Electric plant
Main heat rejection system
Miscellaneous equipment
100%
Civil structure
Materials account for approximately 12% of direct EPC costs, with piping comprising 30-38% of that total.
Nuclear-grade requirements can make concrete 23% and structural steel 41% more expensive compared with standard projects.
A drop in the interest rate from 7% to 4% reduces nuclear LCOE by ~17%, underscoring the critical role of interest rates.
Increasing commodity prices have driven up nuclear construction costs, with steel up 47% and concrete up 65% in the past decade.
Capital cost for nuclear is 84% of total cost. The economics hinge on favorable financing conditions and policy support to mitigate capital risks.
CapEx
Fixed O&M ($/MWh)
Fuel cost ($/MWh)
Variable O&M ($/MWh)
Nuclear

## Slide 30: Poor project management among key drivers of time and cost overruns in new European and North American large reactor builds
1 Indirect services cost includes onsite and offsite project and construction management and design services.
Sources: Energy Technologies Institute, The ETI Nuclear Cost Drivers Project: Full Technical Report (2020); Nuclear Energy Agency, Unlocking Reductions in the Construction Costs of Nuclear: A Practical Guide for Stakeholders (2020); Georgia Power, Nuclear Plant Voglte (2024).
Credit: Clara Zibell, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Cost comparison of conventional nuclear plants in Europe and North America vs. rest of world (ROW)
Chart: 
 | 2776 | 512
 | 956 | 279
 | 105 | 31
 | 3357 | 980
 | 1279 | 373
 | 391 | 114
 | 1345 | 784
 | 178 | 52
$/kW
32%
Europe/North America
31%
ROW
10,387
3,125
Pre-construction costs
Equipment
Materials
Labor
Indirect services costs1
Supplementary costs
Owner’s cost
Financing during construction
Immature supply chain and untrained workforce
Unclear governance structure: Westinghouse acted as the 1) nuclear system supplier, 2) plant design engineer, and 3) consortium leader.
Westinghouse declared bankruptcy in 2017.
Cost drivers Vogtle 3 and 4
Key challenges
Design approval from NRC
July 2008
Schedule approval from GPSC
Construction start with incomplete design
Dec. 2011
Install fuel handling and storage
Begin commercial operation
April 2016
March 2012
Case study: Voglte Unit 3
July 2023
+ 7 years 3 months delay (cumulative)
Feb. 2011
June 2011
Unclear project governance and project development
FOAK AP1000 is first project in 30 years.
Supply of knowledgeable engineers, superintendents, crafts, and other key personnel was limited.
Submodule and rebar installation for the nuclear island did not fit design specifications.
NRC updated safety requirements to protect plants against aircraft impacts.
Sixty license amendment requests were made to NRC since construction start.
Construction and operation license from NRC
Install containment modules
x
Expected timeline
Delayed timeline (non-cumulative)
Time from expected milestone completion date
+10 months
+ 8 months
+ 27 months
+ 41 months
Milestones
Construction delays
Highly focused and intentional national programs drive down costs over time.

## Slide 31: Employing digital tools, streamlined program design, and regulatory collaboration, effective project management cuts complexity, cost overruns
Horizon (U.K.)
Horizon and U.K. regulators codeveloped “papers of principle” to align on safety case revisions; there was a >20% overnight cost reduction for twin-unit ABWR.
Enablers and strategies for reducing project complexity
Case studies
Definitions: ABWR: advanced boiling water reactor; MBSE: model-based systems engineering; NPP: nuclear power plant; PLM: product lifecycle management. Sources: OECD, NEA, Unlocking Reductions in the Construction Costs of Nuclear (2020); Galois, Demonstrating Rigorous Digital Engineering for Nuclear Power Plant Systems (2024); Galois, How Do You Modernize Safety Critical Designs in Nuclear (2024); The Nuclear Institute, Why Nuclear Projects Suffer from Poor Predictability (2019); Locatelli, Why Are Megaprojects Delivered Over Budget and Late? (2018); ETI, Nuclear Cost Drivers Report (2018); Lyons, Production Learning in an SMR Supply Chain (2019); ENEC, Unit 4 start-up at Barakah Plant accelerates UAE towards net zero (2024). Credit: Khande-Jae Fisher, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Galois (U.S.)
Leveraged MBSE to develop a digital instrumentation and control system with enhanced traceability and optimized timelines in under nine months; developed at a fraction of the cost of traditional control systems.
KEPCO APR1400 (Korea)
Streamlined delivery time and efficiency through an integrated delivery chain; received standard design approval from U.S. NRC in 2019.
Barakah plant completed construction for the first unit in five years; Unit 3 was delivered four and five months faster than Unit 2 and 1, respectively.
Early and robust engagement with regulators
Preapproval of standardized designs
Workforce development
Public funding for NPPs
Regulatory collaboration
90%+ completed designs
Design standardization
Clear, incentive-based governance and contracting structures
Repeatable and experienced delivery chain
Streamlined project design & delivery
Digitally enhanced execution and oversight tools, including MBSE, digital twins, advanced modeling, PLM systems, machine learning
Front-end engineering and systems-based modeling
Digital & systems engineering
Technical
Organizational
Reinforces
Supports
Gen III+ construction learning curves are transferrable to SMRs; modularization, simplified design, and standardization can offset diseconomies of scale, particularly with multiunit and serial builds.

## Slide 32: Improvements in design and delivery of NPPs lower the risk profile and significantly reduce costs across the nuclear project lifecycle
Observations
Countries that report lower project costs, such as Korea and Japan, typically begin construction with designs 90%+ completed and plan for standardized, repeatable designs through multiunit and/or serial builds.
Multiunit sites reduce complexity and unit costs by sharing resources and site-specific regulatory, planning, and infrastructure expenses.
Systems engineering enables effective coordination between teams, saving up to 19% in overall time and costs.
Notable companies that have used a 90%+ design completion approach include GE Hitachi, which reduced rework for projects by up to 20x.
Chart: 
 | 5500 | 4600 | 4250 | 3950 | 3800
 | 5500 | 4350 | 3800 | 3600 | 3450
 | 5500 | 4300 | 3550 | 3400 | 3250
 | 5500 | 4300 | 2100
1.000
1.500
2.000
2.500
3.000
3.500
4.000
4.500
5.000
5.500
1st unit
2nd unit
4th unit
6th unit
8th unit
1 unit/site
2 units/site
4 units/site
Barakah
OCC ($/kWe)
The Barakah four-unit project was successful due to a partnership with an experienced consortium, offering a proven supply chain, strong governance, and positive learning effects from a multiunit build.
Chart: 
| 30 | 50 | 50 | 80 | 80 | 80 | 80 | 90 | 90 | 90 | 90 | 90 | 90 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 95 | 100 | 100 | 100 | 100 | 100 | 100
 | 11929.5775 | 10302.8169 | 9711.2676 | 8281.6901 | 3697.1831 | 3007.0423 | 2415.493 | 4929.5775 | 3894.3662 | 3154.9296 | 2661.9718 | 2366.1972 | 1725.3521 | 5422.5352 | 4239.4366 | 4042.2535 | 3697.1831 | 2760.5634 | 2612.6761 | 2415.493 | 2415.493 | 2218.3099 | 3894.3662 | 3549.2958 | 3056.338 | 2859.1549 | 2563.3803 | 2267.6056
0
5.000
10.000
15.000
%
Design completion of 90%+ at construction reduces total capital costs by up to 70%
TCC ($/kW)
70%+ reduction
Chart: 
 | 8 | 17
 | 24 | 20
 | 48 | 31
 | 20 | 13
Traditional
Systems engineering
Verification & validation
Integration & implementation
Detailed design
System design
-20%
Systems engineering reduces time and budget costs by up to ~20%
Standardization decreases unit costs in multiunit builds like the ENEC Barakah nuclear plant

## Slide 33: SMRs have the potential to close the cost gap with large reactors but only if shorter construction times are achieved
Sources: GAIN, Meta-Analysis of Advanced Nuclear Reactor Cost Estimations (2024); Institute for Energy Economics, Small Modular Reactors: Still Too Expensive, Too Slow and Too Risky (2024). Credit: Christian Sandjaja, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).​
Overnight capital cost evolution, 2022 $/kWe
No SMRs have been commercially deployed in the United States as of May 2025; all cost and learning estimates are based on literature, not real-world data.
SMRs are expected to enable faster learning rate and cost reductions through modularity, factory fabrication, and the production of many standardized units.
Faster learning rates (9.5% vs. 8%) and shorter construction times (55 vs. 82 months) are projected to reduce both OCC per kWe and LCOE over time.
Despite these advantages, SMRs are currently projected to have higher initial OCC ($8,000/kWe) than large reactors ($5,750/kWe) by 2030.
However, SMRs' shorter construction reduces financing costs, which narrows the LCOE gap. SMRs can be potentially more competitive under higher financing rates.
Chart: 
| 2030 | 2035 | 2040 | 2045 | 2050
 | 7750 | 7750 | 7500 | 6750 | 6000
 | 10000 | 9500 | 8000 | 7000 | 6250
 | 5750 | 5500 | 4750 | 4250 | 3750
 | 8000 | 6500 | 5250 | 4500 | 4000
 | 5250 | 4000 | 3000 | 2500 | 2250
 | 5500 | 3250 | 2500 | 2250 | 2000
Conservative - Large Reactor OCC
Moderate - Large Reactor OCC
Advanced - Large Reactor OCC
Conservative - SMR OCC
Advanced - SMR OCC
Moderate - SMR OCC
Current status: Early-stage deployment, no commercial ops
Chart: 
 | 54
 | 54
 | 0
 | 66
 | 75
 | 0
 | 93
 | 100
Est. 2030 LCOE; $/MWh, 7.5% WACC
Est. 2030 LCOE; $/MWh, 7.5% WACC + 40% ITC
Chart: 
 | 85
 | 85
 | 0
 | 104
 | 118
 | 0
 | 147
 | 157
Large-Advanced
Large-Moderate
Large-Conservative
SMR-Advanced
SMR-Conservative
SMR-Moderate

## Slide 34: Deep geological disposal remains the preferred option for high-level (radioactive) nuclear waste management
Intermediate-level waste
Spent fuel
High-level waste
New fuel element
Power Plant Operation
Shielded Interim Storage
Reprocessing Fuel Element Fabrication
Pool Interim Storage
Compacted Interim Storage
Near-Surface Disposal
Deep Geological Disposal
High- and intermediate-level (radioactive) waste is stored in deep isolation for non-human intervention.​ Deep geological disposal (DGD) involves storing hazardous materials deep underground in stable geological formations, typically 200 to 1,000 meters below the surface.​
Sources: DoE, Pathways to Commercial Liftoff: Advanced Nuclear (2023); World Nuclear Association, Radioactive Waste: Myths and Realities (2022); World Nuclear Association, Storage and Disposal of Radioactive Waste (2022).
Credit: Christian Sandjaja, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
~40-50 years
~30-50 years
<10 years
671,000 m3
Low-level waste
2,585,000 m3
202,000 m3
519,000 m3
4,000 m3
5,000 m3
Legend:
Cumulative nuclear waste volume
Cumulative nuclear waste supply (2019-2023)

## Slide 35: While Onkalo operates only for Finland’s waste, it created a blueprint for global precedent
Project Overview
Onkala, the world's first permanent deep geological disposal repository for spent nuclear fuel, represents a significant improvement over the temporary storage methods that have dominated global nuclear waste management.
It addresses the mismatch between the extremely long hazardous lifetime of the waste and the temporary nature of existing storage solutions.
Olkiluoto and Loviisa account for 39% of Finland’s domestic electricity consumption, raising the demand for a long-term disposal solution.
Timeline
Challenges and considerations
Long-term safety: Designed to isolate waste for >100,000 years
Public support: Benefited from existing nuclear facilities in the area
Strategic location: Close proximity to Olkiluoto and Loviisa power plants
Funding of nuclear waste management
Ministry of Employment and the Economy; Finnish State Nuclear Waste Management Fund
Licenses
Ministry of Employment and the Economy
Regulatory control
Radiation and Nuclear Safety Authority
Teollisuuden Voima Oyj
Fortum Power and Heat
Posiva Oy
Olkiluoto Power Plant
Sources: Science, Finland built a tomb to store nuclear waste. Can it survive 100,000 years? (2024); Posiva, Introducing ONKALO and its principle of operation (2024); American Nuclear Society, Finland begins trial run of Onkalo repository (2024); World Nuclear Association, WNA Nuclear Fuel Cycle Royal Commission Issues Paper 4 Submission (2015); Pacific Northwest National Laboratory, Nuclear Waste: Challenges for the Next Generation (2007); Posiva, Olkiluoto: A Safe Home for Spent Nuclear Fuel (2011); IAEA/Posiva, Characterization of Spent Fuel for the Management of Final Disposal (2011).
Credit: Christian Sandjaja, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Onkalo licensing, oversight, and funding structure
Final disposal of spent fuel
Loviisa Power Plant
2004
2024
2025-26
2120
Construction begins
Trial run starts
Expected operation
Repository closing
Case study: Onkalo

## Slide 36: A majority of the public supports nuclear energy deployment, driven by a strong preference for energy reliability
Observations
46% of survey respondents support the use of nuclear energy, while 23% oppose it.
22 out of 31 countries surveyed have net support for nuclear energy.
Notable country highlights:
  China – Majority support Nuclear is central to China's strategy to reduce dependence on coal and meet its carbon neutrality target by 2060. It is reflected in government incentives that have resulted in competitive cost ($70/MWh).
  Russia – Majority support Russia leverages nuclear exports for peaceful geopolitical influence, with state-owned Rosatom building around 20 reactors abroad. Nuclear energy, linked to Soviet-era prestige, enjoys strong public support as a symbol of technological strength.
  Thailand – Majority oppose Skeptical due to safety concerns; favors renewables. This is seen in its unsuccessful attempt to reintroduce nuclear power in its Power Development Plan in 2007 and 2010.
% of people who oppose or support nuclear energy's use in their country
Strongly support
Strongly oppose
Tend to support
Tend to oppose
Sources: Radiant Energy Group, Public Attitudes Toward Clean Energy 2024 – Nuclear (2025); World Nuclear News, American Nuclear Society, Surveys reveal public support for, but some concerns on, nuclear energy (2024); Nuclear Business Platform, China’s Nuclear Power Program: A Blueprint for Global Competitiveness (2023); ECNS, China to build 10 new nuclear power units in 2024 (2025); Nuclear energy and international relations: the external strategy of Russia’s Rosatom (2024); Political Science and Security Studies Journal, Nuclear technologies as an instrument of geopolitical confrontation on the borderlands of the Heartland/Rimland (2022); IEEE Xplore, The evaluation of economic and social effect from the revised nuclear power plant planning in Thailand (2011); Hunton, Navigating the Nuclear Landscape: Understanding Thailand’s Laws and Approach (2025). Credit: Christian Sandjaja, Quint Houwink, Brenda Rain, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Chart: 
 | -9 | -15 | -11 | -12 | -13 | -17 | -15 | -13 | -14 | -17 | -16 | -15 | -16 | -20 | -12 | -16 | -18 | -16 | -16 | -18 | -16 | -16 | -18 | -20 | -20 | -20 | -20 | -22 | -22 | -21 | -27 | -16.2105 | -17.75 | -17.4286 | -14.8 | -14.8108
 | -3 | -7 | -5 | -4 | -7 | -6 | -7 | -8 | -13 | -4 | -11 | -6 | -12 | -7 | -10 | -12 | -11 | -9 | -7 | -9 | -11 | -22 | -15 | -19 | -22 | -21 | -16 | -15 | -19 | -15 | -26 | -9.4211 | -15 | -11.5714 | -8.8 | -8.3847
 | 33 | 33 | 21 | 26 | 25 | 24 | 26 | 25 | 15 | 22 | 19 | 25 | 20 | 25 | 16 | 19 | 22 | 20 | 18 | 18 | 18 | 16 | 21 | 18 | 16 | 19 | 19 | 17 | 16 | 16 | 14 | 21.8421 | 18.9167 | 19.1429 | 24 | 25.0345
 | 24 | 24 | 34 | 25 | 26 | 26 | 23 | 23 | 33 | 25 | 27 | 20 | 25 | 17 | 24 | 21 | 18 | 17 | 18 | 18 | 17 | 19 | 12 | 15 | 15 | 11 | 9 | 9 | 10 | 9 | 7 | 21 | 16.8333 | 16.7143 | 21.8 | 20.3089
Taiwan
Poland
Russia
UAE
Finland
India
Egypt
Sweden
Ukraine
South Africa
France
Netherlands
South Korea
Norway
Germany
Philippines
U.K.
Belgium
U.S.
China
Australia
Vietnam
Italy
Spain
Turkey
Singapore
Indonesia
Brazil
Japan
Thailand
-
Nuclear
Non-nuclear
-
G7
Brics 5
=
Global (31)
Canada
57%
57%
55%
51%
50%
49%
46%
40%
45%
45%
37%
42%
36%
33%
26%
28%
33%
31%
30%
26%
25%
21%
43%
36%
51%
48%
48%
47%
40%
40%
36%
35%
35%
36%
46%
46%
26%
33%
29%
24%
23%
12%
22%
16%
16%
20%
23%
22%
21%
27%
21%
27%
21%
28%
27%
22%
28%
29%
25%
23%
27%
27%
38%
33%
39%
42%
41%
36%
37%
36%
41%
53%

## Slide 37: Supply Chain

## Slide 38
Credit: Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Key messages Supply Chain
Despite 60% of nuclear power plants being in the West, more than 50% of OEM and critical component capacity is in China today.
Historically, countries that are actively building new nuclear reactors have also had the largest reactor OEMs.
  During the 1970’s nuclear reactor boom in the West, Westinghouse, GE, and Framatome accounted for 90% of new-build reactors.
  Today, most new reactors are built by CNNC, Rosatom, and Atomenergomash.
Uranium producing and consuming countries have almost no overlap, as most uranium resources are situated in Kazakhstan, Canada, and Australia.
  The world requirement for uranium ore was 68 kilotonnes in 2023. This is significantly more than the 55 kt produced. The difference is made up using stockpiles and recycled uranium.
  The West is highly dependent on Canada and Kazakhstan for its uranium ore.
Mining and enrichment are dominated by a few businesses mostly in Kazakhstan and Russia, while fuel is produced typically in the country where the reactor is located.
  Europe and the United States must invest in uranium enrichment facilities if they want to reduce their dependency on Russia and China.
  Only a few commercial businesses reprocess nuclear fuel. The United States closed its reprocessing plants in the 1970s.

## Slide 39: The traditionally Western nuclear supply chain is increasingly dominated by Chinese players
Supply chain tiers nuclear power plants
Operators
Observations
China hosts 15% of existing nuclear plants but accounts for 30% of new global constructions. It also leads in manufacturing.
Building a nuclear power plant requires highly specialized knowledge. It is for this reason that the nuclear supply chain is highly concentrated.
This concentration allows a few players to benefit from the learning curve. Framatome benefitted from this learning curve when France was building its nuclear fleet in the 1970s and 1980s. Today, CNNC and other Chinese OEMs benefit from the nuclear boom in China.
OEMs have provided fuel, parts, and support for 80+ years, creating lasting technical and geopolitical dependence.
Sources: Global Energy Monitor, Global Nuclear Power Tracker (2024); NIA, The Essential Guide to Nuclear Supply Chain (2010); EOG, Top 9 Nuclear Power Companies Leading the Global Energy Future (2024).
Credit: Quint Houwink, Clara Zibell, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Description
Regional market share, 2024
OEMs
Major components
Specialized components
Subcomponents
Tier
Mostly electrical utility companies operating nuclear power plants
Design, engineer, and construct the reactors
Produce the large parts of the power plant such as pressure vessels, generators, and reactor vessels
Produce niche components that aren’t specific to nuclear but require high standards, such as electronics, valves, and piping
Supply the low-tech components required for a nuclear power plant such as the steel frame, fasteners, and concrete foundation
Local suppliers
Number of players
~200
10-15
20-30
500-1,000
1,000+
Example players
Many
Chart: 
 | 14.6465 | 25.2525 | 27.2727 | 32.8283
15%
25%
33%
China
U.S.
EU
Other
Chart: 
 | 50 | 30 | 20
20%
Chart: 
 | 50 | 25 | 15 | 10
25%
15%
10%
Chart: 
 | 50 | 10 | 30 | 10
10%
10%
Nuclear fuel
Mostly uranium to keep the nuclear plants running
1,000+
0
1
2
3
4
Depends on fuel production stage — see deep dive
Deep dive next

## Slide 40: Reactor manufacturing has shifted from the U.S. and Europe to Russian and Chinese OEMs
Source: IAEA, Nuclear Power Reactors in the World (2024).
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
DUMMY
Observations
During the nuclear boom of the 1970s and 1980s, ~80% of all new nuclear reactors were built by American (Westinghouse, GE) and European (Framatome, Siemens) OEMs.
Since the reemergence of reactors in the past two decades, ~80% of reactors are built by Russian and Chinese manufacturers.
As Western OEMs haven’t built a significant number of new reactors recently, a lot of the know-how has been lost, growing the barriers for new reactors.
Chart: 
0
50
100
150
200
1955
1960
1965
1970
1975
1980
1985
1990
1995
2000
2005
2010
2015
2020
2025
Westinghouse
General Electric
Combustion Engineering
AECL
Framatome
Siemens
Rosatom
Atomenergomash
CNNC
KEPKO
Hitachi
Others
Nuclear reactors under construction by OEM, GW, 1955-2025
Deep-dive: Reactor OEMs

## Slide 41: Uranium producing and consuming countries have little overlap, as most uranium resources are in Kazakhstan, Canada, and Australia
Observations
The world requirement for uranium ore was 68 kilotonnes in 2022. This is significantly more than the 55 kilotonnes produced.
The gap is covered by stockpiles and re-enrichment.
Countries with the highest uranium consumption (United States, Europe, and China) have hardly any uranium production or resources.
This makes the West and China dependent on uranium ore imports. As this is considered a national security risk, countries keep large stockpiles of uranium (the United States keeps ~480 tonnes of unirradiated highly enriched non-military uranium).
(*) Interpolated due to lack of data.
Sources: DoE, Nuclear Energy Supply Chain Deep Dive Assess (2022); WNA, Uranium Enrichment (2024); Storm van Leeuwen, Materials for nuclear power (2019); BGR, Energy Study (2014-2024); International Panel on Fissile Materials (2025).
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Chart: 
 | 22451 | 23127 | 23607 | 24689 | 23321 | 21705 | 22808 | 19477 | 21819 | 21227 | 21100
 | 9331 | 9124 | 13325 | 14039 | 13116 | 7001 | 6938 | 3885 | 4693 | 7351 | 11700
 | 4323 | 3255 | 2993 | 3654 | 4224 | 5525 | 5476 | 5413 | 5753 | 5613 | 7000
 | 6350 | 5001 | 5654 | 6315 | 5882 | 6517 | 6613 | 6203 | 4192 | 4553 | 5500
 | 3135 | 2990 | 3055 | 3004 | 2917 | 2904 | 2911 | 2846 | 2635 | 2508 | 3700
 | 13741 | 12544 | 11670 | 11506 | 11054 | 10502 | 9996 | 9907 | 8716 | 8103 | 6400
2013
2014
2015
2016
2017
2018
2019
2020*
2021
2022
2023
59
56
60
63
61
54
55
48
48
49
55
Other
Russia (8%)
Australia (28%)
Namibia (7%)
Canada (9%)
Kazakhstan (15%)
Chart: 
 | 19.62 | 18.82 | 18.69 | 18.16 | 19 | 19.16 | 18.3 | 17.945 | 17.59 | 18.05 | 18.14
 | 23.25 | 22.77 | 22.44 | 22.87 | 21.52 | 21.1 | 19.51 | 18.625 | 17.74 | 17.67 | 15.9
 | 6.71 | 6.3 | 8.16 | 5.34 | 8.29 | 8.71 | 10.81 | 10.185 | 9.56 | 11.3 | 13.13
 | 5.09 | 5.46 | 4.21 | 6.26 | 5.38 | 5.62 | 6.23 | 6.08 | 5.93 | 6.28 | 5.44
 | 4.22 | 5.02 | 5.02 | 5.01 | 4.73 | 4.59 | 5.12 | 4.695 | 4.27 | 4.11 | 4.31
 | 0.37 | 2.12 | 2.55 | 0.68 | 0.66 | 1.34 | 2.34 | 1.87 | 1.4 | 1.79 | 2.18
 | 5.81 | 5.42 | 5.81 | 5.08 | 5.43 | 6.72 | 5.96 | 5.985 | 6.01 | 6.45 | 8.42
65
66
67
63
65
67
68
65
63
66
68
USA (1%)
Europe (<1%)
China (4%)
Russia (8%)
Korea, Rep.
Japan
Other
Global uranium production and consumption, kt, 2013-2023
Production
Consumption
Countries (% of global natural resources)
Europe has decreased its consumption by ~30% over the past decade.
Uranium suppliers are stable, although Canadian supply decreased between 2020 and 2022 when McArthur River Mine was closed due to low uranium prices.
China increased consumption by 2x since 2013.
Deep dive: Uranium

## Slide 42: Mining and enrichment are dominated by few businesses in non-Western countries; fuel fabrication is more decentralized
(*) Refers to rod/assembly part of fuel production. Percentages differ slightly for pelletizing.
Sources: DoE, Nuclear Energy Supply Chain Deep Dive Assess (2022); WNA, World Uranium Mining Production (2024); Storm van Leeuwen, Materials for nuclear power (2019); The World Nuclear Industry, Status Report (2023); WNA, Nuclear Fuel and its Fabrication (2021); WNA Uranium Enrichment (2025); WNA, Nuclear Fuel and its Fabrication (2021); WNA Processing of Used Nuclear Fuel (2024); WNA, Nuclear Power Economics and Structuring (2024).
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Overview of the nuclear fuel cycle
Material flows
Market share, 2024
Chart: 
 | 23 | 12 | 11 | 9 | 10 | 7 | 28
Cameco
Orano
Uranium One
Kazatomprom
CNNC
Others
CGN
Chart: 
 | 15.8983 | 11.9237 | 43.0843 | 28.4579 | 0.63593
CNNC
12%
Orano
16%
Urenco
Others
1%
Rosatom
Chart: 
 | 9.0463 | 21.0003 | 17.8341 | 23.3523 | 6.4616 | 4.5231 | 17.7824
CNNC
21%
Framatome
18%
9%
Westinghouse
GE
KNFC
Others
TVEL
Observations
Getting from mined uranium to nuclear fuel is an extensive process involving specialized facilities.
Enrichment is concentrated 4 businesses around the world, with Russian Rosatom enriching 43% of global uranium.
Fuel production is more decentralized, with most countries with reactors having their own facilities.
Only a few commercial businesses reprocess nuclear fuel. The U.S. closed it reprocessing plants in the 1970’s.
41% of fuel costs come from mining the uranium, 45% enrichment and only 14% fuel production.
Reactor
Disposal
Enrichment
Fuel production
Mine
Reprocessing
Uranium
Enriched uranium
Depleted uranium
Fresh UO2
Fresh MOX
MOX
Depleted fuel
Spent UO2
Spent MOX
Mining
Enrichment
Fuel production*
Chart: 
 | 53.7975 | 12.6582 | 25.3165 | 8.2278
13%
Mayak
Orano
8%
BARC
Japan Nuclear Fuel
Fuel recycling
MOX is a combination of plutonium dioxide and UO2 and can be used in a few reactors.
Total: 55 kt uranium
Total: 62,900 SWU/year
Total: 15 t LWR fuel
Total: 3,860 t
Deep-dive: Uranium

## Slide 43: Global Policy

## Slide 44
Key messages
Global Policy
Governments have regained interest in nuclear power as a crucial emission-free, reliable energy source to achieve their net-zero targets and a key factor in energy security.
  At COP29 in 2024, 26 countries agreed to triple their nuclear energy capacity by 2050.
  Countries have varying policy stances on nuclear energy.
  U.S.: The Inflation Reduction Act extends tax credits, making existing reactors economical and incentivizing construction. Government also actively supports development of advanced nuclear reactors.
  EU: Countries are divided on nuclear energy policy. France plans to increase nuclear power and boost the development of advanced reactors. Germany has shut down all its reactors, though there is now discussion about potentially reversing that policy.
  APAC: China is leading the global increase in nuclear capacity and development in new nuclear technologies. Japan, Korea, and India aim to increase nuclear capacity to enhance energy security and reduce reliance on fossil fuel.
  Emerging nuclear energy countries: Many African countries are considering including nuclear power in their future energy mix; eight plants are planned or under construction.
Source: IEA, The Path to a New Era for Nuclear Energy (2025).
Credit: Hinako Arai, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Policies for countries pursuing nuclear power include increasing investment in new reactors, extending the operating lifetime of existing ones, and restarting retired plants.
  63 reactors were under construction at the end of 2024, which is expected to generate more than 70 GW.
  In the past five years, the lifetimes of 66 reactors in 13 countries were extended.
  While there are limited cases of the reopening of nuclear plants, Japan has the most experience.
  Overall investment in nuclear was $60 billion in 2023, which is a nearly 50% increase from 2020.
Advanced economies that have not been building new reactors for the past two decades, including rebuilding the skills and industrial base for construction, face deployment challenges.

## Slide 45: Governments have regained interest in nuclear power as a crucial emission-free energy source and a key factor in energy security
Sources: WNA, Country Profiles (2025); IEA, The Path to a New Era for Nuclear Energy (2025); Japan Atomic Energy Commission, White Paper on Nuclear Energy 2020 (2021, only in Japanese); World Nuclear News, Belgium Retires Oldest Nuclear Plant Reactor (2025), World Nuclear News, Feasibility Study for Belarus New Nuclear (2024).; Clean Energy Wire, Economy Minister Confirms end of Germany’s resistance to nuclear power at EU level (2025).
Credit: Hinako Arai, Khande-Jae Fisher, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Changes in nuclear power policy by country during 2014-2024
Currently not supporting but increasing support
Chart: 
| 0.5
 | 1.2
 | 2.9 | 2.6 | 2.7 | 3.2 | 3 | 2.7 | 3.1 | 3.8 | 2.6 | 2.6 | 2.7 | 2.7 | 2.6 | 3.2 | 3.2 | 2.4 | 2.2 | 2.1 | 2.3 | 3.4 | 3.5 | 2.5 | 2.5 | 3.3 | 4 | 0.7
 | 3.2 | 3.7 | 3.4 | 3.5 | 3.6
Iran
Japan
India
Mexico
Hungary
Netherlands
France
Pakistan
Finland
Argentina
Czechia
Russia
China
Slovakia
Slovenia
Canada
Spain
Bulgaria
South Africa
Brazil
South Korea
Belgium
Sweden
Belarus
Ukraine
UAE
U.K.
U.S.
DUMMY
Taiwan
Switzerland
Romania
Currently supporting and increasing support
Currently not supporting and will not support in future
Currently supporting but will decrease support or phase out
Australia
Denmark
New Zealand
Bangladesh
Egypt
Estonia
Ghana
Indonesia
Jamaica
Jordan
Morocco Kazakhstan
Lithuania
Singapore
Turkey
Vietnam
Uganda
Uzbekistan
: The Democratic Progressive Party, elected in 2016, has a nuclear phaseout policy to shut down all nuclear plants by 2025.
: In May, the Swiss Parliament and government decided on a phaseout policy but also the possible removal of a ban on new construction of nuclear power plants.
Other
Europe
Asia
North America
Arrows indicate changes in policy stance between quadrants
Shift to increasing
Shift to phase out or decrease
Change in the use/unuse of nuclear
Future policy
Current policy
Expand
Phase out or decrease
Without nuclear
With nuclear
Number of operating reactors in 2024
Bubble size
: In February 2025, the Spanish Congress approved reversing the nuclear policy it introduced in 2019, which had planned to close all plants by 2035.
Germany: All nuclear plants were shut down in 2023, but the country has reversed its policy and no longer opposes EU initiatives in support of nuclear energy.
: Its first nuclear plant started operation in 2021.
: All nuclear plants shut down after the Fukushima accident in March 2011, but the government aims to increase nuclear reliance.
Italy: The phaseout stance decided following a referendum in 1987 was reversed in March 2025.
Nigeria
Philippines
Poland
Rwanda
Saudi Arabia
Possible increase
Multiple changes in stance in past 10 years
The World Bank lifted its ban on financing nuclear in June and has entered an MOU with the IAEA to expand nuclear capacity, particularly in developing countries.

## Slide 46: Ongoing policy support continues to propel China’s rapid capacity expansion; renewed political backing expected to spur U.S. growth
China
EU
U.S.
Nuclear capacity (GW) | 97 | 98 | 56
LCOE ($/MWh) | 180 | 160 | 70
Main policies | Federal: Inflation Reduction Act; Advanced Reactor Demonstration Program; May 25 Nuclear EO Package | Net-Zero Industry Act | 14th Five-Year Plan (2021-2025)
Policy focus | Lifetime extension, building new reactors, developing advanced reactors | Decision on whether to use nuclear energy left to member countries, nuclear safety | Rapidly construct large-scale plants and advanced reactors
2050 target capacity (GW) | 400 | 150 | 554
Incentives | - Federal: Tax credits on production and investment DOE loans now nuclear focused - State: Zero emissions credits, state-backed loans and funds - Total public commitment to date is >$40B | - Eurotom Research and Training Programme funds nuclear research and innovation, provides financial support for decommissioning - An estimated ~€241B in investments needed to reach target capacity | - Feed-in tariff to decrease the price of nuclear power; VAT refunds to nuclear operators - Latest government study* revealed ~CNY 8.7T (~US$1.3T) needed to lift nuclear capacity to 554 GW by 2050
Lifetime extension | Initial 40-year operating license extended by 20 years, with possible extension of another 20 years | No overarching rule; European Commission investigates and approves extension plans of member countries | Not a priority for China due to relatively new fleet; first lifetime extension in 2021 extended 30-year-old plants by 20 years
Development of advanced reactors | $3.2B in SMRs and other advanced reactor designs; $3.4B in federal funding for the HALEU availability program | Advanced nuclear reactors included in scope of net-zero technologies eligible for financial support | Start operation of ACP100 SMR by 2026, develop floating offshore nuclear power plants
Key policy drivers across main nuclear players
China’s LCOE is less than half that of U.S. and EU.
H
Level of policy support: = High = Medium = Low
M
*The latest Chinese government study mentioned by World Nuclear Association was released in October 2018.
Sources: World Nuclear Association, Nuclear Power in the USA (2025); Lazard, LCOE (2025); Nuclear Europe, Pathways to 2050 (2025); World Nuclear Association, Nuclear Power in China (2025); ForoNuclear, EU recognizes value of nuclear (2025); IEA, The Path to a New Era for Nuclear Energy (2025); ITIF, How Innovative Is China in Nuclear Power? (2024); World Nuclear Association, Economics of Nuclear Power (2023); NEA, Projected Costs of Generating Electricity 2020 Edition (2020); Nuclear Business Platform, China’s Nuclear Power Program (2024).
Credit: Hinako Arai, Adele Teh, Quint Houwink, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Houwink et al., “Nuclear Transition” (23 September 2025).
M
M
M
L
M
H
H
M
H
H
H
H
H
H
H
L
U.S. and China have ambitious targets of 4x and 10x current capacity, respectively; EU 1.5x.
Significant additional capital commitments required to reach capacity goals.
China has fastest growing fleet.

## Slide 47
Measures to be implemented June 2025-2050
Preserved
OBBBA preserves IRA 45U incentives until 2033; foreign entity of concern (FEOC) fuel sourcing rules apply after 2028
Inflation Reduction Act (IRA)
One Big Beautiful Bill Act (OBBBA)
Chart: 

Early expiration
All projects onward will be affected by stricter FEOC restrictions.
United States
45V: Credit available through 2032 for facilities that start construction. Producer can claim up to $3.0/kg until 10 years after the facility is placed into service. Under OBBBA, the credit is available only if construction starts by December 31, 2027.
Wind and solar: 48E ITC of 6%, incrementable up to 30% and 45Y PTC of ¢0.3/kWh incremental up to ¢1.5/kWh. Facilities must be constructed by July 2026 or placed in service by December 31, 2027.
May 23
Executive Order 14299, Deploying Advanced Nuclear Reactor Technologies for National Security: Applies specifically to Gen III+ reactors, SMRs, microreactors, and mobile reactors. Some provisions include deploying techs at military stations, defining critical sites for data centers and providing them with nuclear energy, building up a fuel bank, easing environmental review processes, and promoting nuclear exports.
EO 14300, Ordering the Reform of the Nuclear Regulatory Commission: Includes structure, personnel, regulations, and basic operations.
EO 14301, Reforming Nuclear Reactor Testing at the Department of Energy: Includes updating NEPA rules and establishing a DOE pilot program to allow companies to build test reactors outside of partnerships with national laboratories.
EO 14302, Reinvigorating the Nuclear Industrial Base: Outlines how to strengthen the recycling of nuclear waste and prioritize new nuclear projects.
Sources: IEA, The Path to a New Era for Nuclear Energy (2025); Cres Forum, The Issue Brief: Key Federal Policies Fueling Nuclear Innovation and Reinvestment (2025); IRS, Zero-Emission Nuclear Power Production Credit (2025); DOE, The Hydrogen Production Tax Credit Explained for Nuclear Power Plants (2025); Farr & Gallagher, Tax Credit Opportunities for Nuclear Energy (2024); Congress, One Big Beautiful Bill Act (2025); CGEP Assessing the Energy Impacts of the One Big Beautiful Bill Act (2025); American Action Forum, Trump’s nuclear executive orders: Overview and analysis (2025); Hunton, Recent nuclear executive orders to accelerate US nuclear renaissance (2025).
Credit: Hinako Arai, Brenda Rain, Clara Zibell, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
45U: Tax credit of ¢0.3/kWh incremental up to ¢1.5/kWh if prevailing wages requirements are satisfied. Only facilities placed in service before August 16, 2022, qualify. The benefit starts on December 31, 2023, and fuel sourcing rules apply after 2028.
48E/45Y ‒ nuclear: Preserved in full; fuel sourcing rules apply after 2028.
The U.S. government plans to deploy 400 GW of U.S. nuclear energy capacity by 2050.

## Slide 48: EU countries are divided on nuclear energy policy, with some having phased out or planning to phase out nuclear power
Sources: IEA, The Path to a New Era for Nuclear Energy (2025); WNA, Nuclear Power in the European Union (2025); European Commission, In focus: EU nuclear energy policy – why it matters to us all (2024); European Commission, Nuclear Safety (2025); European Commission, Euratom Safeguards (2025); European Commission, Small Modular Reactors (2024).
Credit: Hinako Arai, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Observations
Nuclear energy accounted for about one-fifth of the EU’s electricity in 2024, with 12 EU countries including nuclear in their energy mix.
The decision to incorporate nuclear power into a country’s energy mix is made by each government.
The European Commission supports countries that use nuclear energy by providing guidance on nuclear safety and advancing the development of next-generation nuclear reactors.
  Euratom Safeguards: Under the Euratom Treaty, the EC established a nuclear material supervision system.
  Euratom Research and Training Programme (2021-2025): €1.38 billion allocated to nuclear research and innovation, including fusion research and development.
  European Industrial Alliance on SMRs (February 2024): Aims to accelerate the deployment of SMRs and strengthen the EU supply chain, including a skilled workforce.
  Net-Zero Industry Act: Seeks to boost European manufacturing of net-zero technologies, including nuclear fission, by addressing production barriers and enhancing competitiveness.
EU member states with operating and/or under-construction nuclear power plant (as of July 2022)
EU member states without nuclear power plants
Non-EU countries with operating and/or under-construction nuclear power plants
Non-EU countries without nuclear power plants
EU governments’ policy stance on nuclear energy
Europe

## Slide 49: France is expanding nuclear power and developing advanced reactors; Germany is considering reversing its phaseout
Sources: IEA, The Path to a New Era for Nuclear Energy (2025); WNA, Nuclear Power in the European Union (2025); WNA, Nuclear Power in Germany (2024); WNA, Nuclear Power in France (2025); EIA, Germany extends the life of its last three operating nuclear power plants until April (2023); Bundestag, The Nuclear Phase-out in Germany (2024).
Credit: Hinako Arai, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Chart: 
 | 1685 | 2215 | 2690 | 2460 | 2122 | 1802 | 1727 | 1227 | 3067 | 5344 | 10455 | 18029 | 17887 | 22652 | 26472 | 33050 | 37979 | 40251 | 39627 | 34779 | 36161 | 34121 | 33045 | 26467 | 21061 | 15982 | 10940 | 8214 | 6832 | 4107 | 4483 | 4483 | 6242 | 6242 | 6242 | 6242 | 6242 | 6242 | 3122 | 3122 | 6242 | 6242 | 6242 | 6242 | 6242 | 6242 | 3122 | 3122 | 6242 | 6242 | 6242 | 6242 | 6242 | 6242 | 3122
 | 86 | 86 | 166 | 316 | 796 | 1073 | 1105 | 1605 | 1605 | 2135 | 2690 | 2460 | 2122 | 1802 | 1727 | 1227 | 3067 | 5344 | 10455 | 18029 | 17887 | 22652 | 26472 | 33050 | 37979 | 40251 | 39627 | 34779 | 34919 | 32879 | 31803 | 25225 | 21061 | 15982 | 10940 | 8214 | 6832 | 4107 | 4483 | 4483 | 21061 | 15982 | 10940 | 8214 | 6832 | 4107 | 4483 | 4483 | 21061 | 15982 | 10940 | 8214 | 6832 | 4107 | 4483
 | 43 | 86 | 86 | 86 | 86 | 43 | 273 | 753 | 1073 | 1105 | 1300 | 1300 | 1830 | 2385 | 2385 | 1547 | 1227 | 697 | 697 | 1982 | 4789 | 10455 | 18029 | 17887 | 22652 | 26472 | 33050 | 36737 | 39009 | 38385 | 33537 | 34919 | 32879 | 31803 | 25225 | 36737 | 39009 | 38385 | 33537 | 34919 | 32879 | 31803 | 25225 | 36737 | 39009 | 38385 | 33537 | 34919 | 32879 | 31803
 | 142 | 142 | 142 | 142 | 1982 | 4789 | 10455 | 18029 | 17887 | 22652 | 26472 | 33050 | 1840 | 4647 | 10313 | 17887 | 17887 | 22652 | 26472 | 33050 | 1840 | 4647 | 8473 | 16047 | 16047 | 20812 | 24632
 | 142 | 142 | 142 | 142
20
40
60
80
0
1970
1990
2000
2010
2020
1980
24-31
16-23
32-39
8-15
40-47
<8
48+
Chart: 
 | 1044 | 1017 | 1689 | 1795 | 2002 | 4087 | 4659 | 6393 | 6833 | 9616 | 9870 | 9870 | 10775 | 8440 | 10346 | 12482 | 13522 | 12349 | 12704 | 14104 | 12759 | 12759 | 10013 | 5771 | 4291 | 4291 | 1400 | 14104 | 12759 | 12759 | 10013 | 5771 | 4291 | 4291 | 1400 | 14104 | 12759 | 12759 | 10013 | 5771 | 4291 | 4291 | 1400 | 12702 | 11357 | 11357 | 10013 | 5771 | 4291 | 4291 | 1400 | 4291 | 4291 | 0 | 0
 | 16 | 16 | 16 | 16 | 143 | 393 | 661 | 499 | 499 | 499 | 1171 | 1171 | 1484 | 3819 | 4659 | 6393 | 6833 | 9616 | 9870 | 9870 | 9455 | 7539 | 9445 | 11581 | 13061 | 10739 | 12704 | 7419 | 8764 | 7539 | 9445 | 11581 | 13061 | 10739 | 12704 | 7419 | 8764 | 7539 | 9445 | 11581 | 13061 | 8411 | 11302 | 0 | 1345 | 0 | 1344 | 4242 | 5722 | 4254 | 7145 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 16 | 16 | 16 | 16 | 16 | 143 | 143 | 86 | 442 | 442 | 442 | 1099 | 1099 | 1029 | 2924 | 3764 | 5513 | 4843 | 7165 | 7419 | 1029 | 1029 | 2254 | 3094 | 4843 | 4843 | 6493 | 7419 | 0 | 0 | 1225 | 2065 | 4171 | 4171 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 357 | 357 | 357 | 1029 | 0 | 0 | 0 | 0 | 357 | 357 | 357 | 357 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
5
10
15
20
25
30
0
1980
1990
2000
2010
2020
1970
France
Policy stance
Germany
Specific policies
Nuclear capacity (MW)
  70% of its electricity from nuclear power
  Actively developing new-generation nuclear reactors
  No nuclear power; phaseout concluded in 2023
  Chancellor Friedrich Merz is in favor of restarting nuclear power plants, sparking a possible reversal of the phaseout policy.
  Grande Carenage program: Extend the lifetime of all nuclear reactors beyond 40 years, totaling 1.3 GW
  France 2030 investment plan: 1 billion euros has been allocated to support the development of innovative reactors, including SMRs, with the goal of commissioning the first SMR by 2035
  Plans to construct six EPR2 reactors and assess the potential need for an additional eight
  Decision to phase out: In 2002, the Atomic Energy Act was amended to phase our nuclear plants. This phaseout was reversed by a new government in 2009 but reinstated in 2011, leading to the immediate shutdown of eight reactors and a plan to close all remaining reactors by the end of 2022.
  Completion of phaseout: The last three nuclear power plants were shut down April 15, 2023. Originally scheduled to close December 31, 2022, their operation was extended due to the energy crisis, but no new fuel elements were allowed. They ceased operation by mid-April 2023.
Lifespan
Europe

## Slide 50: More than half of the nuclear power plants in France went off the grid in the summer of 2022 due to maintenance nuclear shutdowns
Sources: RTE, Generation – Nuclear (2025); WNA, Nuclear Power in France (2025); Clean Air Task Force, The 2022 French nuclear outages: Lessons for nuclear energy in Europe (2023); Bundestag, The Nuclear Phase-out in Germany (2024).
Credit: Hinako Arai, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Observations
Reasons for shutdown:
Corrosion: In December 2021, inspections at Civaux 1 revealed pipe corrosion; similar defects at other units required part replacements and plant shutdowns.
Maintenance delays: COVID‑19 and a shortage of nuclear workers — linked to weak policy support — postponed scheduled outages and extended downtime.
    Cooling restrictions: Regulated use of river water and unusually high water temperatures forced output cuts at operating reactors.
    Policy implications:
Revealed risk of high nuclear reliance.
In the long term, standardizing and modularizing nuclear plant components — rather than undertaking bespoke, labor‑intensive fixes — can improve reliability and streamline future maintenance.
Chart: 
 | 358.779 | 378.225 | 375.935 | 368.5 | 374.914 | 395.2 | 399.585 | 415.515 | 419.814 | 426.883 | 429.978 | 427.855 | 418.609 | 417.468 | 389.188 | 407.875 | 421.118 | 404.792 | 403.757 | 414.3731 | 416.7718 | 383.5407 | 469.0895 | 457.9452 | 426.6802 | 393.1396 | 395.0861 | 331.0075 | 387.04 | 431.1848 | 69.0777
2000
2005
2010
TWh
2020
2025
1995
2015
  1995-2024 average: 404.6 TWh
Electricity generation from nuclear power plants in France
  April 9,
  2025
The lowest nuclear power production in 30 years
26 out of 56 reactors went offline for maintenance
Case Study: France

## Slide 51: China is leading the global increase in nuclear capacity and development in new nuclear technologies
Sources: WNA, World Nuclear Performance Report (2024); IEA, The Path to a New Era for Nuclear Energy (2025); WNA, Nuclear Power in China (2025); WNN, Nuclear Growth Revealed in China’s New Five-Year Plan (2016); Oxford Institute of Energy Studies, Guide to Chinese Climate Policy (2022); NucNet, China/First Hualong One Reactor Begins Commercial Operation at Fuqing (2021).
Credit: Hinako Arai, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Chart: 
 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
 | 2298 | 2298 | 2298 | 2298 | 2298 | 2298 | 2298 | 2298 | 2368 | 4086 | 4736 | 4736 | 4736 | 6856 | 6856 | 6856 | 6234 | 6287 | 5637 | 7855 | 13327 | 17329 | 24534 | 26709 | 33803 | 36118 | 37236 | 38405 | 35202 | 30471 | 24446
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2298 | 2298 | 2298 | 2298 | 2298 | 2298 | 2298 | 2298 | 2368 | 4086 | 4736 | 4736 | 4736 | 6856 | 6856 | 6856 | 6234 | 6287 | 5637 | 7855 | 13327 | 17329 | 24534
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2298 | 2298 | 2298 | 2298 | 2298 | 2298 | 2298 | 2298 | 2368 | 4086 | 4736 | 4736 | 4736 | 6856 | 6856
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2298 | 2298 | 2298 | 2298 | 2298 | 2298 | 2298
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
10
20
70
60
50
40
0
30
2010
2000
1994
GW
2020
24-31
16-23
32-39
8-15
40-47
<8
48+
Lifespan
2011-2015
(12th Five-Year Plan)
2016-2020 (13th Five-Year Plan)
2021-2025 (14th Five-Year Plan)
Plan
Progress
Begin construction at coastal and inland sites to add 25 GW of nuclear capacity by 2015, bringing total capacity to 40 GW
Develop multipurpose water-pressurized SMR, ACP100, with a capacity of 125 MW
Increase nuclear capacity from 27 GW to 58 GW by the end of 2020
Complete four Gen III reactors (U.S.-developed AP1000) and build demonstration units using Chinese-developed technology (Hualong One, CAP1400, etc.)
Targets capacity of 70 GW by 2025
Mandates and increases the use of Gen III or more advanced technologies
Develop ACP100 SMR by 2026 and floating offshore nuclear power plants
Following the March 2011 Fukushima accident, approvals for new nuclear plants suspended, delaying the projects but order revoked in 2012
Preliminary design of ACP100 completed in 2014
Four AP1000 reactors completed in 2018 at Sanmen and Haiyang
ACP100 SMR passed the IAEA safety review in 2016, making it the world’s first SMR to achieve this milestone
Nuclear capacity in China
First Hualong One reactor put into commercial operation in 2021, and two in Pakistan
First ACP100 construction began in 2021 in Hainan
Policy tools used by the Chinese government:
Nuclear plants typically benefit from guaranteed price premiums and priority dispatch.
Major state‑owned nuclear operators (e.g., China National Nuclear Corporation, China General Nuclear Power Group) gain access to low‑cost loans through state-owned banks.
Central and provincial governments facilitate site development by securing land and organizing grid interconnections for new nuclear projects.
China

## Slide 52: Japan, Korea, and India all aim to increase nuclear capacity to enhance energy security and reduce reliance on fossil fuel
 | Japan restarting plants that shut down after March 2011 accident | Korea’s nuclear power phaseout plan reversed by former president | India rapidly expanding nuclear capacity, developing Indian SMRs
Legislative policy | The 7th Strategic Energy Plan Electricity Business Act | 11th (2024-2038) Basic Plan for Long-Term Electricity Supply and Demand | National Electricity Plan of 2023 Nuclear Energy Mission for Viksit Bharat
Trend observed | Of the 54 nuclear reactors that operated before the Fukushima Daiichi accident, 14 have resumed operation, and 12 are scheduled to begin operation. Restarting these nuclear plants is key to increasing energy self-sufficiency and reducing GHG emissions to achieve net zero. | The nuclear phaseout policy, introduced by former President Moon Jae-in in 2017, was reversed in March 2022 by then-President Yoon Suk Yeol. The country formed a public-private partnership comprising 42 entities to advance SMR development. The target is to build two large nuclear reactors and 700 MW of SMRs by 2038. | India will provide funds to construct at least five Indian-designed SMRs, to be operational by 2033. It aims to reach 100 GW of nuclear capacity by 2047. A new program focused on development of SMRs, called the Nuclear Energy Mission, was introduced in the 2025-2026 Union Budget.
Energy mix |  |  | 
Sources: WNA, World Nuclear Performance Report (2024); IEA, The Path to a New Era for Nuclear Energy (2025); METI, Agency for Natural Resources and Energy, Energy in Japan (2025) (available only in Japanese); WNA, South Korea Confirms Need for New Reactors (2025); IEEFA, South Korea’s 11th Power Plan Makes Partial Progress Towards Decarbonization (2025); BloombergNEF, India’s Clean Power Revolution (2020); WNA, Indian Budget Launches Nuclear Energy Mission (2025); Impact and Policy Research Institute, Nuclear Energy Mission for Vikasit Bharat 2025 (2025); Ember, Electricity Data Explorer (2024).
Credit: Hinako Arai, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Chart: 
 | 928.82 | 700.27 | 360
 | 0 | 84.91 | 240
 | 133.9 | 237.12 | 600
2024
50%
20%
30%
13%
68%
8%
23%
2014
87%
0%
1,063
1,022
1,200
2040 (Target)
Renewable
Nuclear
Fossil fuel
TWh
Chart: 
 | 372.8622 | 373.218 | 145.1975
 | 156.7102 | 186.609 | 248.2658
 | 10.8076 | 62.203 | 311.0367
2024
44%
35%
21%
2%
60%
30%
10%
2014
69%
29%
540
622
705
2038 (Target)
Chart: 
 | 1025.49 | 1595.42 | 1565.79
 | 34.69 | 54.7 | 1181.21
 | 202.04 | 407.42
43%
57%
16%
2024
78%
3%
20%
2014
81%
3%
1,262
2,058
2,747
2030 (Forecast)
TWh
TWh
Zero carbon, incl. nuclear
APAC (excluding China)

## Slide 53: Since 2013, Japan has restarted 14 nuclear reactors (~13 GW) under new, stricter safety standards
Case Study: Japan
Political, financial, and energy conditions | Following the 2011 Fukushima accident, Japan’s abrupt suspension of its nuclear fleet led to increased dependence on imported fossil fuels and higher electricity prices. 90% of energy demand was met by imported fossil fuels. Shares of Tokyo Electric Power Co. (Tepco) fell ~70% and it reported $27B+ in losses in 2011. In 2013, Japan began prioritizing energy independence, setting the conditions for a nuclear renaissance.
Key policy and finance levers | Japan created the Nuclear Regulation Authority, establishing new safety and regulatory requirements for nuclear plants in 2013, with revisions in 2019. Tsunami protection, seismic approval, and local government consent were included. The country’s 2014 Strategic Energy Plan reintroduced nuclear as a baseload power source, reinstating it as critical for domestic energy self-sufficiency. By contrast, the previous administration had declared a zero-nuclear future in 2012. Implementation was financed by a combination of private funding and government incentives. Total costs were estimated at $700M-$1B per plant.
Impact | Nuclear now supplies ~8.5% of Japan’s energy demand (compared with ~29% in 2010), with a target of 20% by 2040. A 2023 survey showed that 50%+ of the population supports restarting plants. Tepco’s shares have seen a 200%+ share increase since their lowest point ($1.50 in November 2012).
Sources: EIA, Since Fukushima, Japan has restarted 14 nuclear reactors (2025); WNA, Nuclear Power in Japan (2025); Reuters, Tokyo Electric set to receive $5.9B financing (2013); Google Finance, TKECY (2025); IAEA, Japan (2025); Journal of Energy, Japan’s 2014 Strategic Energy Plan (2017).
Credit: Ariela Farchi, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Sendai 1 2015, 0.89 GW
Sendai 2 2015, 0.89 GW
Ikata 3 2018, 0.89 GW
Ohi 3 2018. 1.18 GW
Ohi 4 2018, 1.18 GW
Mihama 3 2021, 0.83 GW
Onagawa 2 2024, 0.83 GW
Takahama 1 2023, 0.83 GW
Takahama 2 2023, 0.83 GW
Shimane 2 2024, 0.82 GW
Genkai 3 2018, 1.18 GW
Genkai 4 2018, 1.18 GW
Takahama 3 2016, 0.87 GW
Takahama 4 2017, 0.87 GW
Japan’s restarted nuclear reactors

## Slide 54: Many African countries are considering including nuclear power in their future energy mix; 8 plants are planned or under construction
Sources: IEA, The Path to a New Era for Nuclear Energy (2025); IAEA, Argentina Country Highlight (2024); African Energy Newsletter, More African governments consider nuclear power, but costs could scupper plans (2024); Energy for Growth Hub, 2023 Update: Who in Africa Is Ready for Nuclear Power? (2023); World Nuclear News, Permit Granted at El Dabaa (2025); Reuters, Ghana signs agreement to build small NuScale nuclear reactor (2024); Nuclear Business Platform, Nigeria’s Path to Nuclear Energy (2024).
Credit: Hinako Arai, Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
South Africa
Egypt
Ghana
Nigeria
Uganda
Rwanda
  Under the Ghana Nuclear Power Program, the country is in a preparatory work for the construction of its first nuclear power plant.
  It signed an agreement with a U.S. SMR developer, Regnum Technology Group, in 2024, to deploy 12 SMRs.
  The country aims to have 29.7 GW of energy capacity by 2030, of which it plans to power 8% from nuclear power.
  It is constructing its first nuclear power plant, partnering with key nuclear leading countries such as Russia and China.
Two reactors are in operation, with a nuclear capacity of 1.8 GW.
The operational lifetime of the Koeberg Unit 1 nuclear plant was extended for 20 years, until 2044.
Plan to develop two SMR designs.
  Aims to have 9% of electricity generated by nuclear by 2030.
  4.8 GW power plant began construction in November 2022 and is expected to be complete in 2028. The plant uses four large Russian reactors.
Uganda Vision 2040, created in April 2013, lays out the development of significant nuclear capacity for the country’s future energy mix.
Uganda has signed agreements with both Russia (Rosatom) and China (China National Nuclear Corporation).
In 2019, Rwanda decided to collaborate with Russia to build its first nuclear power plant.
In September 2023, Rwanda’s atomic energy board signed a deal with a Canadian-German startup, Dual Fluid Energy, to build a demonstration nuclear reactor.
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
  Operating nuclear plant
  Plant under construction
  Plant planned
  Research reactor operating
N
Emerging Nuclear Energy Countries

## Slide 55: Fusion Technology

## Slide 56
Key messages
Fusion Technology
  Fusion provides energy by fusing two nuclei instead of splitting an atom as in fission.
  Fusion can generate 8x as much energy as fission from 1 kilogram of fuel and without carbon emissions.
  It could theoretically be deployed anywhere in the world, as fuel (deuterium-tritium) is found in seawater and could be produced as a byproduct of fusion.
  There are two main approaches to fusion energy: magnetic confinement fusion (MCF) and inertial confinement fusion (ICF).
  MCF uses magnets to confine and control the plasma as it heats up to the point of fusion.
  ICF uses lasers to heat up a fuel pellet and create enough density to create a plasma and initiate fusion.
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
There are six stages to get to commercial fusion; the world is currently in phase four:
  Fusion starts by forming a plasma, the fourth form of matter besides gas, liquid, and solid.
  The plasma needs to reach 100 million °C to ensure sufficient energy to enable fusion.
  The plasma needs to become sufficiently dense and be sustained.
  The reaction should get to a net energy gain; the energy output exceeds the energy input needed to start and sustain the plasma.
  The reactor then has to generate exportable electricity.
  Finally, fusion energy needs to be commercially competitive.
  Recent years have seen an enormous increase in commercial fusion businesses, from 23 startups in 2021 to 43 in 2024, with a total of $7.1 billion in funding.
  Commonwealth Fusion Systems has received ~$2 billion in funding and is leading in MCF technology.
  Marvel Fusion has received ~$350 million in funding and is leading in ICF technology.
  Most companies hope to have commercial fusion technology by 2035, although experts are skeptical.

## Slide 57: In fusion, two light nuclei fuse release energy without highly radioactive byproducts or emissions
Chart: 
 | 8 | 12 | 29.4924 | 52.7375
Coal
Mineral oil
Fission (U-235)
Fusion (D-T fuel)
24.000.000
96.000.000
~4 x
12M x
Energy density for different energy sources, kWh
Sources: European Nuclear Society, Fuel comparison (2025); University of Leipzig, Energy fundamentals (2025); Greenly, Will nuclear fusion help solve our future energy needs? (2024); Baojie Nie, Nuclear fusion energy research (2024); ITER, Advantages of fusion energy (2025); ITER Tritium Breeding; DOE, DOE Explains...Deuterium-Tritium Fusion Fuel. Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Observations
The two nuclear energy types, fission and fusion, split and fuse nuclei, respectively, to release energy.
Out of all energy sources, nuclear fusion produces the most energy per kilogram of fuel, even more than uranium-235.
Unlike fossil fuels but like fission, fusion generates zero CO₂ emissions during operation.
Fusion reactors cannot melt down or explode and produce no long-lived radioactive waste, making them safer than fission and fossil fuel plants.
In theory, fusion fuel could be generated anywhere in the world from seawater.
Deuterium isotopes are naturally present in seawater.
Tritium (hydrogen isotopes) is a byproduct of some fission reactors and could be a byproduct of fusion, although experiments are still underway for this.
In fission, one heavy atom is split…
…while in fusion, two light nuclei are fused
n
n
n
n
Ba
Kr
U-235
200 MeV
17.6 MeV
Deuterium
Tritium
Helium
n
plasma

## Slide 58: Fusion energy has achieved four of the six milestones to get to commercial viability
Sources: Fusion Industry Association, The Global Fusion Industry in 2024 (2024); ITER, Fusion Energy (2025); DoE, National Laboratory Makes History by Achieving Fusion Ignition (2022);
McCabe, A timeline for fusion energy (2023); EU-Startups, Marvel Fusion bags additional €50 million for nuclear fusion and prototype facility (2025). Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Create plasma
Heat plasma to 100 million °C
Reach sufficient density, be sustained
Achieve net energy gain
Generate exportable electricity
Achieve commercial viability
Plasma needs to reach 100 million °C to ensure sufficient ions collide.
Plasma is typically heated using lasers or radio waves, or by running a current through the plasma.
Plasma must reach sufficient density and be sustained in a fixed space.
This is where advanced devices are required to contain and control the plasma.
A net gain means the fusion energy output exceeds the energy input.
At this point, called ignition, the fusion can sustain itself (in theory, but in practice, obstacles remain).
After achieving net gain, the machine as a whole needs to reach a net gain.
Typically, efficiency losses in the powerplant radically reduce the total gain.
LCOE estimates for fusion range between $25 and $100 per MWh, but this range is extremely uncertain.
Like fission, costs are mostly driven by the high capital costs of the reactor.
Plasma, the fourth form of matter besides gas, liquid, and solid, is needed for nuclei (the positive ions) to fuse.
Plasma is an extremely hot mix of negative electrons and positive ions.
Stage
Description
Progress
Plasma has been was identified in the 19th century.
Plasma was first sufficiently heated in the 1960s, at Los Alamos National Laboratory.
The Joint European Torus (JET) was the first to take this step in 1991.
In 2022, the National Ignition Facility in California was able to get 3.15 MJ output using 2.05 MJ input.
Most continuous operating prototype power plants are scheduled for the early 2030s.
Most commercial companies hope to sell fusion energy by the mid-2030s.
1
2
3
4
5
6
Today

## Slide 59: Magnetic and laser-based confinement are in competition as companies take the fusion baton from flagship research projects
Magnetic confinement fusion (MCF)
Inertial confinement fusion (ICF)
Sources: IAEA, Magnetic Fusion Confinement with Tokamaks and Stellarators (2021); NHSJS, Nuclear Fusion: Overview of Challenges and Recent Progress (2024); U.S. Fusion Energy, Approaches to Fusion (2025); Fusion Industry Association, The Global Fusion Industry in 2024 (2024); Kramer, National Ignition Facility surpasses long-awaited fusion milestone (2022). Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
ITER is the leading MCF research project in the world. This tokamak in France has received ~$18 billion in funding and is expecting to commence operations in the mid-2030s.
There are two leading magnet configurations: donut (tokamak) and a twisted donut (stellarator).
Electromagnets confine and control the plasma.
The plasma is heated using EM waves or a current.
Can theoretically sustain the fusion reaction indefinitely, using the heat from the reaction to continue the plasma
Has seen the most research over the past decades; ~65% of startups use MCF
Instability issues plague MCF, as it can cool down the plasma and damage the vessel wall
A substantial amount of energy (~20%) is lost in cooling the vessel and powering the electromagnets
Powerful lasers send high-frequency pulses toward the target.
Either a fuel pellet is hit directly or ICF uses a cavity that heats up and emits X-rays hitting the fuel pellet indirectly.
As the outside of the pellet heats up, it compresses the inside to become plasma, starting the fusion reaction.
Can theoretically reach higher densities and temperatures, leading to better gains from the reaction itself
Is easier to manufacture in components and operate for short periods of time, improving the operational flexibility
Requires extreme precision from the lasers to fire on the tip of a pencil within a billionth of a second
Low efficiencies in the laser (<1% today) and the cavity X-ray conversion (<50%) need to be overcome to get an overall net gain
The Nation Ignition Facility in California was able to achieve a net gain (3.2 MJ from 2.1 MJ laser energy) for the first time in 2022 using ICF.

## Slide 60: Over half of fusion startups based in U.S., ~one-third in California
10 out 50 U.S. states house fusion startups; ~30% of them are in California (e.g., EMC2, Fuse, Helicity Space, and TAE).
Sources: PitchBook, Company profiles (2025); MIT, MIT spinout Commonwealth Fusion Systems unveils plans for the world’s first fusion power plant (2024); WNN, Germany's Marvel Fusion raises further EUR113 million (2025); Fusion Industry Association, The global fusion industry in 2025 (2025); Nuclear Engineering International, California recognises fusion energy as distinct from nuclear fission (2023).
Credit: Brenda Rain, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Private global fusion ecosystem landscape in 2025
U.S.
Canada
Australia
New Zealand
China
India
Japan
Israel
Germany
France
U.K.
Sweden
Switzerland
29
1
4
1
3
3
1
1
2
3
3
1
1
Observations
Fusion has received a total of $9.7B funding to date; 27% in 2025 and 92% from private sources. Commonwealth Fusion Systems, TAE Technologies, and Helion Energy have all received over $1B.
Most companies (47%) are MCF and use deuterium-tritium as fuel (68%).
Most fusion startups are backed by public-private partnerships, with the United States being the country that provides the most support through the Department of Energy, including:
Milestone-based fusion development program: Supports the development of a fusion pilot plant and fusion power commercialization.
Innovation network for fusion energy (INFUSE): Provides access to national laboratories.
INCITE: Provides access to the DOE’s supercomputing facilities.
Chadwick: Contributes to the development of advanced materials for the first wall of fusion materials.
Concentration of fusion startups
More
Zero
#
Number of fusion startups
Companies are attracted by California’s momentum on fusion, led by universities and their scientific breakthroughs, the state’s venture capital presence, and state government support (California was the first state to recognize fusion as distinct from nuclear fission).

## Slide 61: The two leading startups in MCF and ICF are Commonwealth Fusion Systems and Marvel Fusion, respectively
Sources: PitchBook, Company profiles (2025); MIT, MIT spinout Commonwealth Fusion Systems unveils plans for the world’s first fusion power plant (2024); WNN, Germany's Marvel Fusion raises further EUR113 million (2025).
Credit: Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Chart: 
 | 0 | 0 | 0 | 39.6 | 150 | 121.4
 | 2.7
 | 5 | 10 | 30 | 60 | 70 | 67 | 75
2019
2020
2021
2022
3
2023
2024
2025
40
150
Employees
Funding, $M
Grants, $M
Public-private partnership, $M
Chart: 
 | 5.1 | 1800
 | 84
 | 25 | 115 | 150 | 275 | 500 | 1000 | 1000
2019
84
5
2020
2021
2022
2023
2024
2025
Employees
Funding, $M
Grants, $M
Founded in 2018 as a spin-off from MIT, CFS is by far the best funded fusion company in the world with ~$2 billion in total funding.
CFS believes it can revolutionize fusion engineering employing its research into high-temperature superconducting magnets.
The company aims to build a more compact tokamak, named ARC, in the early 2030s with ~400 MW clean power.
Before that, CFS is developing SPARC to pave the way for ARC. SPARC is expected to produce plasma in 2026 and have a net gain shortly after.
Marvel was founded in 2019 following the Nobel Prize in physics in 2018 for breakthrough laser technologies.
Using this novel laser technology and new fuel pellets, Marvel believes it can improve the efficiency of NIF to reach commercially viable fusion energy by the mid-2030s.
The company is building a $150 million proof of technology with Colorado State University to test the new laser technology by 2027.
Marvel aims to build its first power plant prototype with Siemens Energy by 2032 and have commercial power by 2035.
Case study: Commonwealth and Marvel Fusion

## Slide 62: Despite a long timeline to commercialization, fusion is collecting significantly more funding than fission, driven by ambitious policy
Chart: 
 | 763 | 763 | 1300 | 1300
 | 871.4286 | 871.4286 | 0 | 225
 | 0 | 0 | 1143 | 1480
 | 0 | 0 | 945.4286 | 945.4286
2021
2022
2023
225
2024
1,634
1,634
3,388
3,950
Europe
U.S.
U.K.
China
Chart: 
 | 2700 | 300 | 900 | 1200
 | 50 | 200 | 1300
 | 400 | 50
 | 100
2021
100
400
50
300
2022
200
2023
50
2024
850
1,100
2,550
Chart: 
 | 1500 | 154 | 154 | 154
 | 303.6 | 1500 | 1500 | 1680
 | 0 | 303.6 | 303.6 | 303.6
2021
154
2022
154
2023
154
2024
1,804
1,958
1,958
2,138
Chart: 
 | 200 | 257 | 53.4 | 139
 | 280 | 0 | 2 | 106
 | 63 | 14 | 22 | 15.35
63
280
200
2021
14
257
2022
22
53
2023
106
139
2024
543
271
77
260
Fusion
Fission
Public research funding
Private investments*
(*) Does not include PE investments or state enterprises.
Sources: PitchBook, Nuclear power deal flow (2025); Fusion Industry Association, The Global Fusion Industry in 2024 (2024); Gov.uk, Government announces up to £650 million for UK alternatives to Euratom R&T (2023); Neutron Bytes, Mixed Messages from Congress on Funding Nuclear Energy (2021); EC, Euratom (2025); CFS, The race to lead the world in fusion has begun (2025); Gov.uk, Plan for Change to deliver jobs and growth in UK leading fusion industry (2025); Utility Dive, The answer is a fusion moonshot (2024); AIP, FY23 Budget Outcomes: National Nuclear Security Administration (2023); FIA, FIA Urges Prioritization of Commercializing Fusion Energy (2024); WNN, Germany stepping up investment in fusion (2023). Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Public research funding into nuclear power is unknown for China but likely significant.
Nuclear fusion policy around the world
Governments worldwide have designed policies on how to regulate fusion and how to incentivize it.
United States
Fusion regulated as particle accelerators, making it easier to develop than fission power plants
Approved $790M annual research funding, including $40M for private firms under milestone-based program
European Union
Fusion regulations the same as that for fission reactors
Funds fusion under the Euratom Treaty at $871M annually; Germany has had additional funding since 2023
United Kingdom
Fusion regulated by the Environmental Agency, not the nuclear regulator
Subsidizes £410M for STEP tokamak project until 2027
China
Aims to lead fusion tech through its ~$1.5B annual fusion spend, but regulations similar to that for fission
Has deployed the only new tokamak since 2019
CFS received a $1.8B investment in 2021.
Pacific Fusion raised $900M in 2024.

## Slide 63: CKI Nuclear Team
Quint Houwink
Master of Business Administration
CKI Fellow
Attribution: Houwink et al., "Reenergizing Nuclear" Columbia Business School Climate Knowledge Initiative (2025).
Hinako Arai
Master of International Affairs
CKI Fellow
Vedant Bhansali
BA Financial Economics
CKI Fellow
Christian Sandjaja
Master of Sustainability Management
CKI Fellow
Clara Zibell
BA Sustainable Development
CKI Fellow
Gernot Wagner
Senior Lecturer, Columbia Business School
Faculty Director, Climate Knowledge Initiative
gwagner@columbia.edu
Isabel Hoyos
Master of Sustainability Management
Staff Associate, Climate Knowledge Initiative
Hyae Ryung (Helen) Kim
PhD in Sustainable Development
Senior Research Fellow
hk2901@columbia.edu
Adele Teh
Master of Business Administration
CKI Fellow
Khande-Jaé Fisher
Masters of Science in Sustainability Science
CKI Fellow
Brenda Rain
Master of Sustainability Management
CKI Fellow

## Slide 64: Appendix

## Slide 65: Comparison of current and upcoming nuclear and geothermal technologies for clean baseload electricity supply
 | Nuclear |  | Geothermal | 
 | Large-scale nuclear | SMRs | Conventional geothermal | Enhanced geothermal systems (EGS)
Capacity factor (CF) | 92.3% | Potential to stagger SMRs for greater CF but not yet proven | 70-90% | Geothermal energy potential increases with depth (higher temps)
Siting flexibility | Specific siting requirements according to safety, environment, seismicity, etc. | Possible to site in remote areas or smaller grids | Limited to naturally occurring reservoirs | More flexible than conventional geothermal
Cost (LCOE)1 | $141-$228/MWh, high CapEx | $50-120/MWh (lower though uncertain) | $66-$109/MWh | $200/MWh; costs based on initial demonstration
Lifespan | 32 years on average, possible to extend up to 80 years | 6 to 80 years expected (yet unproven) | 25 years, extendable | Uncertain
Ramp rate | 5-10% per minute depending on reactor design | 5% per minute (expected) | 15% per minute, full range 0-100% | Uncertain
Land use1 | 2.4km2/TWh per year, 500 acres | Modular, 35 acres per site | 7.5km2/TWh per year, larger surface infrastructure | Like conventional but more complex engineering
1 Note that axes are inverted so that lowest values reflect desirability (i.e., lower price = more desirable  score = 5)
Sources: IAEA, Non-Baseload Operation in Nuclear Power Plants (2023); IAEA, What are SMRs (2023); DOE, Benefits of SMRs (2025); EIA, Nuclear FAQ (2025); Feutry et al., Nuclear Power Plant Flexibility at EDF (2019); NREL, Annual Technology Baseline: Nuclear (2024); Detering, Nuclear Is a Dispatchable Energy Source (2023); Lovering et al., Land Use Intensity of Electricity Production (2022); IEA, The Future of Geothermal Energy (2024); , What is generation capacity (2025). Credit: Clara Zibell, Isabel Hoyos, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).​
Scale of 1-5 (least to most desirable)
Appendix: Nuclear opportunity

## Slide 66: Traditional reactors have a proven safety track record, while SMRs take it further with built-in passive protections​
Sources: Nuclear Innovation Alliance, Safety (2021); European Commission, Small Modular Reactors Explained (2024); Union of Concerned Scientists, Small Modular Reactors (2013); NuScale Power, Nuclear Power and Safety (2025); Our World in Data, Death rates per unit of electricity production (2016).
Credit: Christian Sandjaja, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Feature | Small modular reactor | Traditional plant
Safety systems | Passive cooling systems, simpler design | Active cooling systems, complex design
Radioactive inventory | Smaller inventory | Larger inventory
Containment structures | Less robust | More robust
Emergency planning zones | Reduced (e.g., site boundary) | Larger zones (10+ miles)
Risk from natural hazards | Underground siting reduces some risks | Above-ground siting increases exposure
Cumulative risk (multiple units) | Higher if many modules are used | Centralized risk in single reactor
SMR vs. traditional plant safety difference
Death rates per TWh electricity produced
Observations
Nuclear energy stands out as one of the safest energy sources, significantly lower than fossil fuels like coal and oil.
This stark contrast underscores nuclear’s potential to deliver clean and safe energy at scale.
SMRs build on this safety advantage with passive systems, smaller radioactive inventories, and underground siting.
However, less robust containment and scalability risks mean that safety gains depend on strong regulatory oversight.
SMRs are particularly suited for remote or rural regions with limited grid infrastructure, industrial sectors requiring heat or electricity, and nuclear first-timer countries that try to adopt nuclear energy.
Chart: 
 | 32.72 | 24.62 | 18.43 | 6.15 | 4.63 | 2.82 | 1.3 | 0.58 | 0.04 | 0.03 | 0.02
Brown coal
Coal
Oil
Chernobyl*
Biomass
Natural gas
Hydro
Fukushima*
Wind
Nuclear
Solar
Appendix: Deployment

## Slide 67: Various U.S. demographic groups support including nuclear in the energy mix and favor expanding nuclear capacity
U.S sentiment toward building more nuclear power plants
Chart: 
| 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
 | 47 | 41 | 47 | 59 | 52 | 51 | 56 | 57 | 61 | 59 | 63 | 60 | 69 | 63 | 59 | 59 | 57 | 58 | 56 | 54 | 53 | 54 | 53 | 69 | 72 | 71 | 71
 | 30 | 27 | 47 | 34 | 41 | 43 | 37 | 35 | 33 | 35 | 34 | 36 | 28 | 34 | 37 | 40 | 37 | 36 | 36 | 28 | 31 | 30 | 28 | 31 | 28 | 29 | 29
% Agree
% Disagree
Sources: DOE, Pathways to Commercial Liftoff: Carbon Management (2023); Energy Research & Social Science, Establishing Leadership in Bringing CCUS to Scale (2025); Our World in Data, Death rates from energy production per TWh (2021); Bisconti, Record High Support for Nuclear Energy (2024); Nuclear Innovation Alliance, Safety (2025).
Credit: Christian Sandjaja, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Observations
Nuclear's mortality rate is significantly lower than other energy sources, making it one of the safest energy source options.
A few notable nuclear accidents:
  Chernobyl – A critical design flaw, compounded by operator errors and a poor safety culture, resulted in an uncontrollable fission reaction and subsequent steam explosions.
  Fukushima – Loss of both off-site power and backup generators due to flooding eliminated the ability to pump coolant to the reactor, making it impossible to cool the fuel even after shutdown.
Modern nuclear reactors incorporate major advancements in safety principles, which supports positive sentiment.
Due to increased safety, more U.S. power plants renewed their licenses, backed by local community support.
Chart: 
 | 32 | 46 | 20 | 26 | 35 | 24 | 36 | 35 | 35 | 29 | 36 | 25 | 33 | 32
 | 45 | 40 | 50 | 53 | 40 | 51 | 43 | 50 | 43 | 42 | 43 | 49 | 45 | 43
 | 17 | 11 | 22 | 15 | 20 | 18 | 14 | 12 | 17 | 20 | 17 | 20 | 15 | 18
 | 6 | 4 | 8 | 6 | 5 | 7 | 7 | 4 | 5 | 9 | 5 | 6 | 7 | 7
17
45
32
Total
4
11
40
46
Men
8
22
50
20
Women
6
15
53
26
Gen Z
5
20
40
35
Millennial
7
18
51
24
Gen X
7
14
43
36
Boomers
6
12
50
35
Republican
5
17
43
35
Democrat
9
20
42
29
Independent
5
17
43
36
Northeast
6
20
49
25
Midwest
7
15
45
33
South
7
18
43
32
West
4
U.S. sentiment toward using nuclear in energy mix by demographic
Strongly oppose
Somewhat oppose
Strongly favor
Somewhat favor
Appendix: Deployment

## Slide 68: Nuclear waste is much smaller in volume and has significantly fewer negative externalities than any other energy source
Waste management by energy source
Nuclear
Observations
Waste from nuclear energy is strictly regulated and contained while waste from other sources is disposed into the environment.
While coal releases greenhouse gases directly into the atmosphere, nuclear, solar PV, and wind also generate some emissions throughout their lifecycle (manufacturing, mining, installation).
Coal and nuclear generate operational waste, while waste for solar and wind is end of life.
(*) Radiotoxicity is harmful only in the event of improper waste management. (**) Varies by region.
Sources: Sustainability by numbers, How much waste do solar panels and wind turbines produce? (2023); MDPI, The End of Life of Solar PV Systems (2023); Science Direct, End-of-life solar voltaic waste management (2024); MDPI, Waste Management of Wind Turbine Blades (2024); EPA, Coal Ash Basics (2025).
Credit: Clara Zibell and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Operational waste products
Waste risks and challenges
Solar PV
Wind
Energy source
Volume (kg/MWh)
Toxicity
Coal
M
Recyclability
Waste management
Near-surface disposal for LLW and deep geological disposal for ILW and HLW
Coal ash (contains arsenic, lead, mercury) and greenhouse gases
Contaminates soil, water, and air sources, posing threats to human health
Long-term disposal of HLW remains a challenge
Spent fuel rod and unprocessed uranium (radiotoxic)
Trace amounts of lead in solar PV solders
Turbine blades
89
1.67
0.16
0.03
L
H
End-of-life solar panels
Microplastics pollution from blade degradation
H
*
Landfills or recycling (14% global recycling rate**)
Landfills and incineration most common
Landfills and reuse in other materials (concrete or wallboard)
H
L
L
M
**
M
**
Appendix: Deployment

## Slide 69: Nuclear power operations are highly dependent on strategic elements such as lithium-7, uranium, zirconium, and indium
Plant construction (special)
Plant operations
Observations
Concrete
Safety considerations are the main factor determining the amount of concrete needed in a nuclear plant.
After safety incidents and the 9/11 attacks, the regulations for nuclear plants were tightened and concrete requirements nearly doubled since the 1960s.
In Gen IV reactors, the concrete requirement has decreased fivefold due to smarter design.
Zirconium
Zirconium is used in fuel cladding to encase uranium fuel pellets in reactors.
Low neutron absorption allows efficient reactions; it is highly corrosion-resistant.
Zirconium must be purified to remove hafnium, which absorbs neutrons.
Uranium (recoverable)
It is a primary fuel source in nuclear reactors, with uranium-235 undergoing fission to generate energy.
Uranium is typically processed into uranium dioxide (UO₂) pellets and encased in zirconium fuel rods.
It has a heavily fluctuating price.
Sources: DoE, Nuclear Energy Supply Chain Deep Dive Assess (2022); Ashby, Materials and the Environment Ch. 12 (2013); WNA, Advanced Nuclear Power Reactors (2021); Peterson et al., Metal And Concrete Inputs For Several Nuclear Power Plants (2005).
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Chart: 
 | 4.4333
 | 5.2267
 | 5.1
 | 1.8
 | 1.35
 | 1.26
 | 1.03
 | 0.8
370.0
0.8
411.3
Concrete
Carbon steel
Wood
Stainless steel
Copper
Galvanized iron
PVC
Insulation
30.0
1.0
Material intensity (kg/kW)
Chart: 
 | 0.51
 | 0.35
 | 0.3
 | 0.11
 | 0.1
 | 0.04
Manganese
Nickel
Inconel
1,410
510
300
110
Aluminum
100
Lead
40
Chromium
350
Material intensity (g/kW)
Material intensity (g/kW)
Chart: 
 | 0.07506
 | 0.044699
 | 0.03
 | 0.01
 | 0.01
 | 0.01
 | 0.01
500
300
10
Uranium
Zirconium
Lithium-7
Boron
870
Cadmium
Indium
Silver
10
10
10
30
Overview of material intensity by type
Plant construction (local)
Appendix: Supply chain

## Slide 70: Post-Fukushima, Germany quickly decided to shut down reactors; France maintained policy stance given its high reliance on nuclear
Sources: Ember, Electricity Data Explorer (2024); Columbia K=1 Project Center for Nuclear Studies, France: A Study of French Nuclear Policy After Fukushima (2012); Asahi Shimbun, Opposition to Nuclear Growing (2011); Bundestag, The Nuclear Phase-out in Germany (2024); Willsher, Nicolas Sarkozy makes €1bn Commitment to Nuclear Power (2011).
Credit: Hinako Arai, Quint Houwink, and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
Observations
In response to the Fukushima Daiichi disaster in March 2011, France and Germany followed a diverging policy path.
France: Then-President Nicolas Sarkozy stood steadfast on using nuclear power plants given that 74% of the country’s electricity supply came from nuclear at that time. Despite large anti-nuclear protests, the government focused on securing jobs by keeping the plants open.
Germany: Germany had its nuclear phaseout policy from 2002 but decided in 2010 to extend the operating life to continue using nuclear energy while shifting to renewable energy. However, three days after the Fukushima accident in 2011, Germany declared a three-month nuclear moratorium. All plants constructed pre-1980 were shut down immediately and all other operating plants underwent stress testing.
Chart: 
 | 56 | 32
 | 51 | 19
France
Germany
Electricity generation from nuclear power and number of operating reactors
Chart: 
 | 40 | 56
 | 44 | 81
Public perception on the use of nuclear energy (%)
Before Fukushima disaster
After Fukushima disaster
In favor
Against
Chart: 
 | 57 | 57 | 59 | 59 | 59 | 59 | 59 | 59 | 59 | 59 | 59 | 58 | 58 | 58 | 58 | 58 | 58 | 58 | 58 | 58 | 58 | 56 | 56 | 56 | 56
 | 19 | 19 | 19 | 19 | 18 | 18 | 17 | 17 | 17 | 17 | 17 | 17 | 9 | 9 | 9 | 9 | 8 | 8 | 7 | 7 | 6 | 6 | 3 | 3 | 0
 | 169.61 | 171.3 | 164.84 | 165.06 | 167.07 | 163.05 | 167.27 | 140.53 | 148.49 | 134.93 | 140.56 | 107.97 | 99.46 | 97.29 | 97.13 | 91.79 | 84.63 | 76.32 | 76 | 75.07 | 64.38 | 69.13 | 34.71 | 7.22 | 0
 | 415.16 | 421.08 | 436.76 | 441.07 | 448.24 | 451.53 | 450.19 | 439.73 | 439.45 | 409.74 | 428.52 | 442.39 | 425.41 | 423.68 | 436.48 | 437.43 | 403.2 | 398.36 | 412.94 | 399.01 | 353.83 | 379.36 | 294.73 | 338.2 | 379.27
Number of operating reactors
TWh
2000
2005
2010
2015
2020
2024
Germany
France
March 2011
Fukushima Daiichi accident
Appendix: Global policy

## Slide 71: Glossary
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
ADR APAC AI ARG BWR CAN CapEx CCUS CFS COP CO2 D-T fuel DGD DOE EM | Advanced modular reactor Asia Pacific Artificial intelligence Argentina Boiling water reactor Canada Capital expenditures Carbon capture, utilization, and storage Commonwealth Fusion Systems Conference of the Parties Carbon dioxide Deuterium-tritium fusion fuel Deep geological disposal Department of Energy Electromagnetic
EPC EPR EU ETS FOAK GHG GT HALEU HTGR HLW IAEA ICF IDC IEA ILW | Engineering, procurement, and construction European pressurized reactor European Union Emissions Trading System First of a kind Greenhouse gas Gigatonnes High-assay low-enriched uranium High-temperature gas-cooled reactor High-level waste International Atomic Energy Agency Inertial confinement fusions Interest during construction International Energy Agency Intermediate-level waste
IRA ITC JAP JET kWh LCOE LCOH LEU LMR LLW LULCF LWR MCF | Inflation Reduction Act Investment Tax Credit Japan Joint European Torus Kilowatt-hour Levelized cost of energy Levelized cost of hydrogen Low-enriched uranium Liquid metal reactor Low-level waste Land use, land-use change, and forestry Light water reactors Magnetic confinement fusion

## Slide 72: Glossary (cont.)
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).
MeV MJ MSR MOX MWe NIF NRC O&M OCC OEM PDP PTC PV PWR R&D ROK | Megaelectron volts Megajoules Molten salt reactor Mixed oxide fuel Megawatt electrical National Ignition Facility National Regulatory Commission Operations & maintenance Overnight capital costs Original equipment manufacturer Power Development Plan Production Tax Credit Photovoltaic Pressurized water reactor Research & development Republic of Korea
RUS SMRs STEPS U-235 UKR UO2 VAT VLLW | Russia Small modular reactors Stated Policies Scenario (IEA) Uranium-235 Ukraine Greenhouse gas Value-added tax Very low-level waste
AD/CVD APAC ASEAN BIPV BoS BSF c-Si C&I CAGR CAPEX CCS CO2 CPV CSP EMEA | Antidumping and countervailing duties Asia Pacifi Association of Southeast Asian Nations Building Integrated PV Balance of System Back Surface Field Crystal silicone Commercial & Industrial Compound annual growth rate Capital expenditures Carbon capture and storage Carbon dioxide Concentrator PV Concentrated solar power Europe, Middle East, and Africa

## Slide 73: Units, Calculations, and References
Kilowatt (kW) | 1,000 (1 thousand) watts
Megawatt (MW) | 1,000,000 (1 million) watts
Gigawatt (GW) | 1,000,000,000 (1 billion) watts
Terawatt (TW) | 1,000,000,000,000 (1 trillion) watts
One watt equates to one joule of energy per second.
In electrical systems, power (watts) is calculated by multiplying voltage (volts) by current (amps).
Credit: Quint Houwink and Gernot Wagner. Share with attribution: Houwink et al., "Reenergizing Nuclear" (23 September 2025).