## Slide 1: Decarbonizing Cement
Gernot Wagner, Isabel Hoyos, Camilo Avilés, Jessica Cong, Ariela Farchi, Nicolas Herrera Isaza, Hyae Ryung Kim, Shailesh Mishra, Hoshi Ogawa, Hassan Riaz, Sho Tatsuno, Adele Teh, and Soraya van Beek
16 July 2026
First published: 17 October 2024
Cite as: Wagner et al. “Decarbonizing Cement,” Columbia Business School Climate Knowledge Initiative (16 July 2026).

## Slide 2: Cement and concrete production account for ~5% to 8% of global CO2 emissions, mostly scope 1
CO2e emissions in 2025: ~55 billion tons
Cement 20%
Chemicals 16%
Non-ferrous Metals 0.2%
Other Industry 37%
Industry
Iron & Steel 27%
Waste 22%
Agriculture, land use, and waste
Livestock 23%
Aviation 10%
Land Use & Forestry 12%
Marine 5%
Crops 38%
Rail 1%
Agriculture fuel 4%
Road 84%
Transport
Power and heat
Commercial Combustion 18%
Oil 2%
F-Gases 36%
Natural Gas 31%
Residential Combustion 46%
Buildings
Coal 67%
Residual 100%
Residuals
22%
23%
18%
15%
8%
13%

## Slide 3: China has dominated cement production for the past decade, but share expected to decline while emerging markets’ demand grows
China’s production share peaked in 2013, then dipped below 50% of global in 2023 for the first time in 15 years
Demand from emerging markets, led by Sub-Saharan Africa and India, is expected to increase sharply
Chart: 
 | 32.0206 | 29.5664 | 30.4259 | 29.3993 | 28.5115 | 32.6945 | 34.4305
 | 58.3128 | 59.2951 | 57.5412 | 57.5516 | 57.178 | 54.0282 | 49.2537
 | 6 | 6.0841 | 6.5854 | 6.9136 | 8.2195 | 6.8182 | 9.5366
 | 1.9056 | 1.4098 | 1.65 | 2.0121 | 2.5739 | 2.5273 | 2.6085
 | 1.7611 | 1.8971 | 2.0561 | 2.1333 | 2.1268 | 2.0682 | 2.1951
 | 1.7475 | 1.7415 | 1.9901 | 1.3902 | 1.8636 | 1.9756
2%
2011
2013
2015
2017
2019
2021
49%
2023
3.60
4.08
4.10
4.05
4.10
4.40
4.10
2%
-5.2%
Turkey
U.S.
Vietnam
India
China
RoW
Global cement production by country, billion tons
2030 cement demand growth outlook, %
Chart: 
 | 77 | 42 | 39 | 21 | 20 | 15 | 10 | 9 | 1 | 0 | -2 | -28
Sub-Saharan Africa
India
Southwest Asia
LATAM
North America
Southeast Asia
MENA
CIS
Oceania
CEE
Western Europe
East Asia
77%
42%
39%
21%
20%
15%
10%
9%
1%
0%
-2%
-28%
Sources: USGS, Mineral Commodity Summaries (2025); World Cement Association, Industry Outlook (2024).
Credit: Nicolas Herrera Isaza, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).

## Slide 4: Clinker production is ~85% of cement emissions; dry-kiln adoption has led to significant efficiency gains
Dry kilns have replaced wet kilns for clinker production
1 The production process shown assumes dry-kiln processing, which has widely replaced wet-kiln processing globally.
Sources: Environmental Development, Energy conservation and emission reduction for cement (2022); Portland Cement Association (2024); CEMBUREAU, Cement manufacture fact sheet (2021); Mission Possible, Making net-zero concrete and cement possible (2023).
Credit: Nicolas Herrera Isaza, Jessica Cong, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).
Raw meal
Clinker
Concrete
Cement
CaCO3 + heat = CaO + CO2
  Melting clinker
  Precalcining
  Preheat
Vertical cyclones with exhaust gases from the kiln are heated at ~900°C.
Raw meal of crushed limestone and other minerals go in.
Limestone is partially decomposed into lime in a combustion chamber before entering the kiln.
1
2
3
Precalcined meal enters the rotary kiln heated to 1,450°C with fossil fuels combustion.
Clinker is produced.
Chart: 
 | 5.29 | 3.4 | 2.9
Wet kiln
Avg. dry kiln
Optimized dry kiln
-45.2%
-14.7%
Kilns energy efficiency, GJ/t clinker
Observations
Calcination of limestone and combustion of fuels used to bring limestone to the required temperature account for ~90% of clinked production emissions.
The industry is rapidly shifting to adopt dry kilns, with over 80% of global and 90% of European clinker production now using dry kilns. This shift reflects a clear willingness and capacity to change best practices to favor efficiency.
  In dry kilns, raw materials are ground into a fine powder to form a raw meal; in wet kilns, raw materials are mixed with water to form a slurry.
  The wet process is relatively less energy efficient and more resource intensive, with more energy required to evaporate the water in the slurry.
Clinker production is the first step in concrete production1

## Slide 5: Clinker production ~85% of cement emissions; lower clinker-to-cement ratio can drive marginal emissions reductions
Clinker-to-cement production process1
Clinker-to-cement ratios vary considerably by region
Observations
Energy emissions from cement grinding account for ~5% of the sector’s emissions.
The higher clinker-to-cement ratio in the U.S. (0.88 versus 0.76 world average) is due to the U.S.’s use of a lower proportion of SCMs than other countries.
Ordinary Portland cement (OPC) can contain up to 95% clinker.
Blended cements, which partially replace clinker with SCMs, are a deployable and cost-effective technology, though they have struggled to gain market share.
Chart: 
 | 0.89 | 0.86 | 0.77 | 0.65
U.S.
Canada
Europe
China
1 The production process shown assumes dry-kiln processing, which has widely replaced wet-kiln processing globally.
Sources: CEMBUREAU, Net-zero roadmap (2024); Portland Cement Association (2024); CEMBUREAU, Cement manufacture fact sheet (2021); Mission Possible, Making net-zero concrete and cement possible (2023).
Credit: Nicolas Herrera Isaza, Jessica Cong, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).
Raw meal
Clinker
Concrete
Cement
  Grinding and blending
  Cooling
Hot clinker is rapidly cooled to 100°C with air blowers powered by electricity.
1
2
Clinker is mixed with 4% to 5% gypsum.
In some cases, it is mixed with other supplementary cementitious materials (SCMs) (e.g., slag, CCR, clay).
The mixture is ground and blended into cement.

## Slide 6: Concrete demand is expected to rise at a ~1.4% CAGR by 2050, driving an increase in absolute cement emissions
Clinker-to-concrete production process1
Concrete demand, billion m3
Observations
Cement is the binding component in concrete and can be used in less or more quantities depending on the strength needed for the end use.
  Cement comprises 10 to 15% of concrete by weight.
Energy emissions from concrete mixing and transportation account for ~5% of the sector’s emissions.
Concrete is usually made at or near a construction site (an average of 50 kilometers away).
Raw meal
Clinker
Concrete
Cement
  Extra additives
  Add aggregates
  Cement + water
Hydration is a chemical process triggered when these are mixed.
It creates heat and a paste-like substance.
Sand and gravel are the ingredients that provide volume in the concrete mix.
The sand fills in tiny spaces, while bigger pieces like gravel or crushed stone fill in larger gaps.
1
2
3
Substances that act as accelerators, retarders, and air-entraining agents alter how the concrete works and improve its performance.
Chart: 
 | 14 | 20
2024
2050
1.4%
1 The production process shown assumes dry-kiln processing, which has widely replaced wet-kiln processing globally.
Sources: GCCA, Societal demand for cement and concrete (2024); Portland Cement Association, Roadmap to Carbon Neutrality (2021); CEMBUREAU, Cement manufacture fact sheet (2021); Mission Possible, Making net-zero cement possible (2023).
Credit: Nicolas Herrera Isaza, Jessica Cong, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).

## Slide 7: Cost-effective, deployable solutions can partially abate cement emissions; full decarbonization requires emerging technologies
 | Energy efficiency |  | Clinker substitution |  | Alternative production technologies |  |  | Carbon capture
 | Heat optimization | Alternative fuels: Biomass/waste | Blended cement: Traditional SCMs | Blended cement: LC3 | Thermal batteries6 | Alternative feedstock | Electrochemical production | CCUS/CCS
Description | Levers include: Vertical mills or high-pressure grinding rolls Kiln preheaters and improved insulation Waste heat use Digital process control | Using biomass and waste as heat sources can lower thermal emissions: Current kiln heat supply is fossil-fuel dominated (70% coal, 25% oil and gas) | Supplementary cementitious materials (SCMs) Can partially replace clinker in blended cements Include CCR, steel furnace slag, and natural pozzolans | Limestone calcined clay cement (LC3) Blended cement that uses limestone and calcined clay Can replace more clinker than traditional SCMs | High-temperature thermal batteries, powered by cheap electricity, can replace fossil-fueled rotary kilns Can be connected to the grid or powered by off-grid renewables | Non-carbonate rocks can replace limestone as feedstock Can avoid the chemical emissions of limestone calcination | Electrochemistry can break down limestone instead of high-heat kilns Combined with non-carbonate feedstock, it can fully decarbonize cement production | Retrofitting plants with carbon capture can remove CO₂ released during clinker production Captured CO₂ can serve as feedstock, fuels, or building materials
Addressed emissions | Thermal | Thermal | Thermal and chemical | Thermal and chemical | Thermal | Chemical | Thermal | Thermal and chemical
Limiting factor | CapEx | Feedstock availability and cost | Material availability and depletion | Retrofit and CapEx | New tech, CapEx, energy cost | New tech, CapEx | New tech, CapEx, energy cost | High CapEx & OpEx, infrastructure
TRL |  |  |  |  |  |  |  | 
Abatement potential1 | ~9% (2030) ~19% (2050) | ~4% (2030) ~27% (2050) | ~12% (2030) ~39% (2050) | ~8% (2030) ~32% (2050) | ~4% (2030)2 ~12% (2050) | ~4% (2030) ~11% (2050) | ~15-20% (2030)2 ~70-80% (2050) | ~19% (2030) ~69% (2050)4
Abatement cost, $/tCO2e | -46.3/39 (2030) -26.9/14 (2050) | -80/-40 (2030) -25.4/-8 (2050) | -97.7/- 35 (2030) -48.2/- 19 (2030) | -82.7/- 32.2 (2030) -33.2/-11.5 (2050) | 159/414 (2030)3 37/132 (2050) | -44.2/9 (2030)3 -15.4/2 (2050) | 287/593.4 (2030)3 74/152 (2050) | 167/364 (2030)3 46.3/101 (2050)
1Unconstrained theoretical abatement potential for a given ton of cement produced for each approach in isolation. 2Assumes clean energy source. 3Abatement cost of emerging technologies is based on estimates and has high uncertainty. 4Reflects the approximate emissions gap after other measures, not a fixed technical limit. 5Despite TRL9, market penetration remains minimal due to slow standards adoption, limited supply chain coordination, and conservative procurement practices. 6Thermal batteries’ abatement potential and cost are based on off-grid renewables.
Sources: DOE, Pathways to Commercial Liftoff Report (2023); Mission Possible, Net-zero concrete and cement (2023); CATF, Recasting the Future (2025); ACA, Roadmap to Carbon Neutrality (2021); GCCA, Concrete Future (2022); ClimateWorks Foundation, Low-carbon cement (2023); Energies, Alternative Fuels and Energy Efficiency in Cement (2023); International Journal of Greenhouse Gas Control, BioCCS in cement (2023); IEA, Bioenergy Annual Report (2022); RMI, The Business Case for LC3 (2024); Energy Innovation, Industrial Thermal Batteries (2023).
Credit: Camilo Avilés, Nicolas Herrera Isaza, Soraya Van Beek, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).
Mature and commercialized
Pilot plant stage
R&D/Lab stage
Ready for commercialization
5

## Slide 8: Emerging technologies like thermal batteries, alternative feedstock, and electrochemistry are key to achieving full decarbonization
Observations
Currently deployable measures can deliver up to 30% emission reductions through energy efficiency, alternative fuels, and blended cement (conventional SCMs and LC3).
Alternative feedstock and electrochemical production can virtually eliminate cement production emissions but require significant technological advancements and transformational changes to production process.
Thermal batteries' successful deployment depends heavily on low-cost and low-carbon electricity.
Electrochemistry faces challenges including high energy demand and competition for feedstock.
CCS costs vary widely depending on carbon transportation and storage infrastructure.
Abatement cost1 vs. potential2 for key decarbonization pathways by 2030 vs. 2050
500
400
300
200
100
0
600
-100
-200
30%
40%
30%
20%
10%
40%
70%
Abatement potential (%)
70%
Energy efficiency
SCMs
Alt. feedstock
CCUS/CCS5
Alt. fuels
Electrochemical production
LC33
1Abatement cost of emerging technologies is based on estimates and has high uncertainty. 2Abatement potential is calculated as unconstrained and theoretical for each approach in isolation. 3Despite TRL 9, market penetration of LC3 remains low due to slow standards adoption, limited supply chain coordination, and conservative procurement practices. 4Thermal batteries' abatement potential and cost are based on off-grid renewables; see slide 25 for grid power. 5CCUS/CCS calculations reflect the approximate emissions gap after other measures, not a fixed technical limit.
Sources: DOE, Liftoff Report (2023); Mission Possible, Net-zero concrete and cement (2023); CATF, Recasting the Future (2025); ACA, Roadmap to Carbon Neutrality (2021); GCCA, Concrete Future
(2022); ClimateWorks Foundation, Low-carbon cement (2023); Energies, Alternative Fuels and Energy Efficiency in Cement (2023); International Journal of Greenhouse Gas Control, BioCCS in cement (2023); IEA, Bioenergy Annual Report (2022); RMI, The Business Case for LC3 (2024); Energy Innovation, Industrial Thermal Batteries (2023).
Credit: Camilo Avilés, Nicolas Herrera Isaza, Soraya Van Beek, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).
Thermal batteries4
500
400
300
200
100
0
600
-100
-200
Abatement cost ($/tCO2e)
10%
10%
10%
5%
10%
20%
Abatement potential (%)
20%
5%
Electrochemical production
CCUS/CCS5
Thermal batteries4
Alt. fuels
SCMs
LC33
Energy efficiency
Alt. feedstock
2030
2050

## Slide 9: Blended cements partially replace clinker, reducing emissions with minor changes to production process or added costs
Observations
Global clinker production is ~3.8 Gt/year. Replacing 50% of global clinker would require SCM supply far above today’s ~500 to 600 Mt/year of usable materials; only LC3 offers long-term, scalable supply.
At the product level, furnace slag has the potential to replace up to 50% of clinker, but global availability limits slag-based substitution.
Coal combustion residuals (CCR) cements can substitute 30% to 35% at the plant level but globally only ~10% to 20% due to limited supplies of high-quality CCR as coal plants retire.
LC3 can deliver 30% to 40% clinker reduction, but current industrial capacity is small (~1% to 2% of global cement) and significant new calcination and production infrastructure is required.
 | Clinker | Furnace slag (GGBFS) | Coal combustion residuals (CCR) | Calcined clay (LC3)
Replacement potential | N/A | 30-50%1 | 30-35% | 30-40%
Availability | 3.8 billion Mtpa | 520-680 Mtpa | 500-800 Mtpa | 3.5-5 Mtpa
Availability-adjusted replacement potential | N/A | ~10-18% | ~10-20% | 1-2%
Emissions reduction potential2 | N/A | ~15-30% | ~15-30% | ~30-40%
Price $/ton | ~65-75 | ~51 | ~45 | ~20-35
Blended cements
-20
-15
-10
-5
0
-25
30%
30%
-14
-20
-22
31.6%
Abatement cost3 ($/tCO2e) vs. emission abatement potential (% tCO2e)
1 30% to 50% replacement in CEM II/B-S or CEM III/A; up to 60% to 70% in CEM III/B. 2 The % CO2 reduction achieved if the full technical replacement potential is used. 3 Cost relative to clinker.
Sources: CKI analysis; DOE, Liftoff Report (2023); RMI, The business case for LC3 (2024); IEA, Net Zero by 2050 (2023); GCCA, Concrete Future Roadmap (2021).
Credit: Nicolas Herrera Isaza, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).

## Slide 10: Financing, operating, and stakeholder barriers are preventing the adoption of low-carbon cement and concrete
Financing
Stakeholder
Operating
High CapEx and limited financing options
Complex intermediaries
- Greenfield plants will be capital intensive. A new U.S. cement plant at 1+ MTPA commercial scale can require ~$0.5 billion to $1 billion in CapEx per deployment.
- Major investments are typically financed on the balance sheet with limited use of project finance.
Lack of long-term offtake agreements
Technological uncertainty
- Approximately 96% of all cement shipped goes through intermediaries.
- The value chain is highly fragmented at intermediary tiers between cement manufacturers and large buyers such as government procurement.
- Measures such as CCUS or alternative production methods for low-carbon cement have not been tested at commercial project scale in the U.S.
- Cement companies and investors will need to see technologies and business models de-risked before they pursue the substantial capital investments required for deployment at scale.
- Ready-mix companies and contractors purchase on an as-needed basis and are reluctant to commit to longer term offtake due to uncertainty about long-term demand amidst boom-and-bust construction market cycles.
- This makes it challenging to create a credible long-term demand signal for the scale-up of new technologies for low-carbon cement.
Lack of standard process and limited data
Risk aversion and long adoption cycles
- There is no single standard methodology to assess the embodied carbon of products, making it challenging to compare cements and concretes during a competitive procurement process.
- Lack of robust emissions data for specific inputs and production makes it challenging to conduct standardized environmental product declarations.
- The cement sector has a ~10- to 20-year adoption cycle for new blends and materials ― both from the long lead time to update standards and a long customer adoption cycle.
- Contractors, engineers, and ready-mix companies are risk-averse to adopting new technologies that may lead to budget and schedule overruns or safety risks.
Source: DOE Liftoff Report, Low carbon cement (2023).
Credit: Hoshi Ogawa, Sho Tatsuno, Jessica Cong, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).

## Slide 11: High CapEx and long horizons mean climate hard-tech startups must overcome technological and commercial ‘Valleys of Death’
Technological
Valley of Death
Commercial
Valley of Death
Observations
The two valleys are qualitatively different: the technological valley is a capital availability problem (negative IRR, no debt possible); the commercial valley is a risk-return mismatch (VC-level risk, infra-level returns).
Have elaborate development and testing process with high capital costs due to the hard-tech character of climate start-ups.
Capital scales ~5x to 10x at each stage; the largest absolute jump is to FOAK ($80M-$900M in a single step), when project finance is often not available yet.
The FOAK range ($100M-$1B) is the widest of any stage, reflecting sector variation.
Stages 1 and 3 show no IRR because they are funded from the corporate balance sheet: no standalone investment case yet.
"High teens to 25%" at FOAK reflects investor required rates, not realized returns — often a hurdle to obtaining investments.
Overcoming the first valley involves technological de-risking; the second requires proof of commercial viability and bankability of hard-tech solutions
Lab development
Pilot factory
Commercial-scale testing
FOAK1 plant
1
2
3
4
SOAK* plant
5
Product stage
Size of tech
1 small reactor
Multiple small reactors (e.g., 5x)
1 big reactor
Multiple big reactors (e.g., 20x)
Multiple big reactors
(e.g., 100x)
Proof of concept
Technology
Technical scalability
Commercial size technology
Commercial scalability and profitability
Commercial returns
Similar to FOAK but lower unit costs
Capital costs2
$1M-$20M
$5-$40M
$20-$100M
$100M-$1B
Expected
IRR
n/a
Negative IRR
n/a
High teens to 25%
n/a
System layout
Small system, testing technology
Integrated system with real process conditions
Larger engineering validation
Full integrated commercial plant
Replicated commercial plant
Deep Dive: FOAK Valleys of Death
1FOAK = first of a kind; SOAK = second of a kind. 2Capital costs refer to construction CapEx only; excludes OpEx, financing costs, and pre-FID development expenditure.
Sources: DOE, Learning from Case Studies: Financing and Development Approaches from Recent First-of-a-Kind Projects (2024); Sightline Climate, Meet the FOAK folks (2025); Extantia Capital, The FOAK Question: Essential Insights for Financing and Planning First-Of-A-Kind plants (2023).
Credit: Soraya van Beek, Isabel Hoyos, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).

## Slide 12: Capital efficiency key to overcoming technological Valley of Death; risk transfer across value chain key for commercial valley
Technological
Valley of Death
Commercial
Valley of Death
Reduction of capital needs by keeping team light and using existing equipment and materials (not reinventing every step in process).
Partnerships without equity, to develop pilot scale and establish first relationships for offtake agreements (hyperscalers often have the capital and risk appetite).
Government grants/loans, which should be politically agnostic (e.g., independence rather than climate).
Offtake agreements, to prove demand to secure potential project finance.
Tailored niche product instead of diversification (e.g., high-quality iron instead of high-volume steel)
Integration in established value chain with experienced partners for supply and construction.
Government grants and loans.
Observations
The technological valley solutions are primarily about capital efficiency: reducing what you need to spend; the commercial valley solutions are about risk transfer: shifting risk onto counterparties (offtakers, value chain).
Government grants are equally critical at the commercial valley: DOE/EU funding has been an enabler of FOAK project debt in recent cases (e.g. Stegra, LanzaJet).
"Tailored niche product" is a highest risk commercial strategy: It narrows the customer base, but protects margin if it works.
High-risk construction often leads to companies turning to in-house development.
The two solution sets are sequentially dependent.
Climate-tech startups must de-risk demand and often leverage public, concessional, or philanthropic capital to finance FOAK* commercial plants
Bench-scale testing
Pilot factory
Commercial-scale testing
FOAK* plant
SOAK* plant
1
2
3
4
5
Climate-tech start-ups are forced to self-develop and build their own plants because unproven technology and high construction risk make it impossible to find a licensing partner; only once commercial viability is demonstrated can they transition to the higher margin role of equipment provider or licensor.
Deep Dive: FOAK Valleys of Death
1FOAK = first of a kind; SOAK = second of a kind. 2Capital costs refer to construction CapEx only; excludes OpEx, financing costs, and pre-FID development expenditure.
Sources: DOE, Learning from Case Studies: Financing and Development Approaches from Recent First-of-a-Kind Projects (2024); Sightline Climate, Meet the FOAK folks (2025); Extantia Capital, The FOAK Question: Essential Insights for Financing and Planning First-Of-A-Kind Plants (2023).
Credit: Soraya van Beek, Isabel Hoyos, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).

## Slide 13: Investment capacity and infrastructure drive CCUS in Global North; clay reserves and capital constraints drive LC3 in South
North America and the EU account for 92% of stated capacity from announced cement CCUS projects.
High capital needs and strong policy support (e.g., U.S. 45Q tax credit) drive CCUS deployment in high-income countries.
Existing oil and gas infrastructure in developed markets (e.g., pipelines, storage facilities, geological data) enable faster rollout. For example, Norway’s Northern Lights project uses existing North Sea oil infrastructure to store CO2..
Cement CCUS capacity1, global distribution, Dec. 2024
Clay calciner capacity1, global distribution, Dec. 2024
<1%
1-3%
3-5%
5-10%
10-15%
15-20%
<1%
1-3%
3-5%
5-10%
10-15%
15-20%
1 Expected at full operation based on stated disclosed carbon capture capacity for CCUS and stated disclosed installed capacity for clay calciner.
Source: GCCA and LeadIT, Green Cement Technology Tracker (2024).
Credit: Adele Teh, Isabel Hoyos, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).
Africa accounts for 44% of stated capacity from announced clay calciner projects.
Clay calcination kilns are less capital intensive and easily integrated into existing cement plants than CCUS installations, making them a more attractive option for countries with limited industrial investment capacity.
Many developing countries have abundant clay reserves but rely on imported clinker due to the scarcity of high-grade limestone. Clay-based alternatives offer a cost-effective solution to meet rising cement demand amid rapid urbanization in developing countries.

## Slide 14: U.S., China, and EU + UK have deployed policies across the full carrots-sticks spectrum to incentivize cement decarbonization
2023: 71 MtCO2 World Rank: 3rd
Push
Improve project economics of cement decarb tech (credits, grants, concessional finance).
Pull
System
enablers
Penalize
Prohibit
Incentivize demand via procurement, disclosure, or embodied carbon rules.
Remove barriers via standards, codes, or infrastructure, to allow for new materials and supply chains.
Internalize externalities by raising costs or removing negative existing incentives.
Legal bans or caps on fuels, clinker, or emissions.
IRA 45Q tax credit for CCS since 2023, preserved under OBBBA.
Innovation Fund: 16 cement projects have been funded.
Carbon CfD pilot.
Green Credit Guidelines (updated 2021). Banks prioritize lending to green investments including green cement.
Buy Clean (federal/state) in 2021.
Public procurement guarantees demand. Federal canceled in 2025.
National Embodied Carbon Disclosures (e.g., France RE2020) binding since 2021. Creates demand for verified low-carb cement.
GB/T Green Building Code (MOHURD ’17+, revised ’20). Green materials in public projects. Pulls low-carb cement.
States’ DOT adoption of ASTM C1157 (Performance Cement Spec). Removes prescriptive clinker limits.
EN 197-5 Standard – CEN 2021. Active. Approves calcined clay (LC3) blends, enables clinker substitution.
GB 175-2023 and related SCM specs (GB/T 1596; GB/T 18046) legally define types and allow lower-clinker compositions.
California Cap-and-Trade Program (CARB, since 2013). Impact: Adds ~$2 to $35/tCO₂ to clinker cost.
RGGI C&T: $1.5B revenues in ’24.
EU ETS Phase IV and CBAM phase-in 2023-26. Tightens free allocation; border tariff raises cost of carbon-intensive imports.
National ETS expansion to cement; first compliance end of 2025. Absolute caps signaled for 2027.
Colorado DOT GWP caps for cement and concrete, Jan. 1, 2025; applies to projects with construction on or after July 1, 2025.
UK coal phase-out (BEIS, binding 2025). Cement kilns must shift away from coal fuels.
No new clinker capacity and strict capacity replacement (2024). Tougher replacement ratios (e.g., ~2:1 in air-polluted regions).
2023: 40 MtCO2 World Rank: 5th
2023: 718 MtCO2 World Rank: 1st
United States
EU and UK
China
Sources WEF, Industry NZ tracker (2023); EU, Innovation Fund (2024); EU, Net-Zero Industry Act (2024); EU, ETS (2024); ICAP, California ETS (2024); EU, CBAM (2024); GPP Pledge (2023); Office of Sustainability, Federal Buy Clean Initiative (2024); S&P, IRA 45Q (2023); EU; CCfDs (2024); DOE, Industrial Demonstrations Program (2023); Chinese Standards, Common Portland cement (2023); Global Carbon Atlas, Carbon Emissions (2023); ICAP, China ETS (2024); Reuters, China’s bank to extend carbon lending tool (2024); Colorado DOT, Buy Clean Colorado Act (2025); ICAP, USA - (RGGI) (2025). Credit: Nicolas Herrera Isaza, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).
Policy type
Carrots
Sticks
Neutral

## Slide 15: EU + UK and China are tightening restrictive policies; U.S. is pulling back on incentive-based support
Chart: 
| 4 | 2 | 2.97 | 2.1 | 2 | 2.1
 | 4.6 | 4 | 3.1 | 2 | 1.2 | 1.2
 | 4.6 | 4 | 3 | 2 | 2
 | 4.6 | 4 | 2.9 | 2 | 1.2
45Q+IDP (F)
ASTM C1157 (S)
ETS (S)
GWP limits (S)
SB 596 (S)
Inn. Fund (R)
RE2020 (C)
EN197-5
ETS (R)
CBAM
Retrofit Fund
Green materials
SCM specs
ETS
Rest. clinker cap
Buy Clean (S)
Unbalanced and mixed landing zone
Mid-balanced and
mixed landing zone
Effective balance &
stronger landing zone
China’s mix features strict capacity caps (1.8B ton) but low carbon prices and diffuse financing.
Low direct funding, but new construction standards permit SCMs.
Strong national plans target 30% of cement capacity to reach benchmark energy efficiency1 by 2025.
ETS now covers cement. Price ~$13 per ton.
New ambitious NDC → outlook is positive.
Lean heavily on sticks; low balance score but high strength.
Carbon prices around €79/t.
CBAM (’26) closes carbon leaks.
Innovation Fund just covered 16 cement projects for ~€2.4B vs. ~€180B in revenue for ETS.
Uneven lower clinker content standards adoption (EN197-5).
Strengthening at a slower pace.
1 States include California, Oregon, Washington, Connecticut, Delaware, Maine, Maryland, Massachusetts, New Hampshire, New Jersey, New York, Pennsylvania, Rhode Island, and Vermont.
Sources: WEF, Industry NZ tracker (2023); Climate Bond Initiative (2023); EU, Innovation Fund (2024); EU, Net-Zero Industry Act (2024); EU, ETS (2024); ICAP, California ETS (2024); EU, CBAM (2024); GPP Pledge (2023); Office of Sustainability, Federal Buy Clean Initiative (2024); S&P, IRA 45Q (2023); EU; CCfDs (2024); DOE, Industrial Demonstrations Program (2023); Chinese Standards, Common Portland cement (2023); Global Carbon Atlas, Carbon Emissions (2023); ICAP, China ETS (2024); Reuters, China to extend carbon lending (2024); Colorado DOT, Buy Clean Colorado Act (2025); C2ES, US state carbon pricing (2025); Global Cement, EU funds 14 projects (2025); EU, ETS (2025); China Briefing, China’s CO2 reduction plan (2024); Climate Bonds, China’s green finance catalogue (2025). Credit: Nicolas Herrera Isaza, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).
U.S.: Carrots being removed, few and weak sticks
EU + UK: Strong sticks, need stronger incentives
China: Refreshed ambitious NDC
U.S.
EU + UK
China
Relative strength
Moderate mix of carrots and sticks. Relative to the EU and China, the U.S. offers more carrots and puts less pressure on companies.
Large push incentives (e.g., 45Q $85) tCO2e + IDP) support limited number of projects.
Carbon pricing is limited to a few states (i.e., 13 states1) ~$30/tCO₂.
Outlook relaxes policies’ strength.
Medium
High
Low
S: State; F: Federal; R: Region; C:Country
Carrots
Sticks
Neutral
Outlook

## Slide 16: As EU ETS free allowances phase out, carbon is projected to represent ~30% to 50% of cement costs by 2034
Even in a conservative scenario, total allowance costs to the cement industry will see a sharp increase by 2034
Total cement costs could increase by ~50% to 100% by 2034 due to carbon pricing alone
Deep dive: EU policy
Assumptions: Emissions intensity 0.57 tCO2e/t cement as benchmark; stable cement consumption (production-exports+imports) at 160 Mt/year
Sources: CKI analysis; BCG, Decoding ETS and CBAM (2025); European Environment Agency, Use of EU ETS revenue (2024).
Credit: Nicolas Herrera Isaza, Isabel Hoyos, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).
Chart: 
 | 0 | 53.34 | 216.79 | 543.69 | 1360.94 | 3060.82 | 3878.07 | 4695.32 | 5512.57 | 6427.89
 | 0 | 15.24 | 61.94 | 155.34 | 388.84 | 874.52 | 1108.02 | 1341.52 | 1575.02 | 1836.54
 | 0 | 15.24 | 61.94 | 155.34 | 388.84 | 874.52 | 1108.02 | 1341.52 | 1575.02 | 1836.54
 | 0 | 15.24 | 61.94 | 155.34 | 388.84 | 874.52 | 1108.02 | 1341.52 | 1575.02 | 1836.54
0
2025
2026
2027
2028
2029
2030
2031
2032
2033
6,428
2034
99
5,684
11,938
70-90 €/EUA
90-110 €/EUA
110-130 €/EUA
ETS total allowance costs scenarios for cement industry, € million
Incremental carbon pricing impact over cement costs, €/t of cement
Chart: 
 | 37.1721 | 37.1721 | 37.1721 | 37.1721 | 37.1721
 | 0.3311 | 3.3749 | 18.9995 | 29.1454 | 39.9
 | 0.0946 | 0.96425 | 5.4284 | 8.3273 | 11.4
 | 0.0946 | 0.96425 | 5.4284 | 8.3273 | 11.4
 | 0.0946 | 0.96425 | 5.4284 | 8.3273 | 11.4
80
2026
80
2028
80
80
2032
80
2034
.
81
86
115
134
154
2030
+40
+74
Base Cost
70 €/EUA
90 €/EUA
110 €/EUA
130 €/EUA
0.4-1%
4-7%
20-30%
27-40%
33-50%
%
Carbon cost share in total cement cost

## Slide 17: Different roadmaps consider efficiency, material substitution, and CCUS as key decarbonization levers, with CCUS abating ~36%-50%
Comparison of global cement and concrete decarbonization levers by 2050
Chart: 
 | 47 | 44 | 42.5 | 24 | 20.39
 | 37 | 36 | 38 | 7 | 56.93
 | 16 | 9 | 12.5 | 45 | 23.44
 | 11 | 7 | 7 | 19.18
 | 17
IEA
GCCA
MPP
45%*
24%
McKinsey
CEMBUREAU
120%
Europe
Energy efficency & alternative fuels
Material substitution
CCUS
Material efficiency
Unabated emissions
Global
Total abatement exceeds 100% because the roadmap includes carbon removal strategies (e.g., CCUS, carbonation) that go beyond reducing emissions, enabling net-negative emissions (-131 kg CO₂/t) by 2050.
Percentage share of CO2 emissions abated by key levers
Sources: DOE, Pathways to Commercial Liftoff (2023); GCCA, Concrete future: Roadmap to net zero (2021); McKinsey, Zero-carbon cement (2020); ClimateWorks Foundation (2021); CEMBUREAU, From Ambition to Deployment (2024).
Credit: Beatrice Klein, Isabel Hoyos, Shailesh Mishra, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Decarbonizing Cement” (16 July 2026).

## Slide 18
CKI Cement Team – Fellows and Alumni
Alumni
Current Fellows
Jessica Cong
Master of Business Administration
CKI Fellow
Hyae Ryung (Helen) Kim
PhD in Sustainable Development
Sho Tatsuno
Master of Business Administration
CKI Fellow
Shailesh Mishra
MPA in Development Practice
CKI Fellow
Adele Teh
Master of Business Administration
CKI Fellow
Nicolás Herrera Isaza
MS in Sustainability Management
CKI Fellow
Hoshi Ogawa
Master of Business Administration
CKI Fellow
Hassan Riaz
Master of Business Administration
CKI Fellow
Soraya van Beek
Master of Business Administration
CKI Fellow
Camilo Avilés
MS in Sustainability Management
CKI Fellow

## Slide 19
Shiho Kawashima
Associate Professor of Civil Engineering and Engineering Mechanics, Columbia University
Kimberly E. Kurtis
Associate Dean of Faculty Development & Scholarship, Engineering, Georgia Institute of Technology
CKI Cement Staff, Faculty, and Advisors
Pia Doris Morrow
M.S. in Sustainability Management
Staff Associate
pm3346@columbia.edu
Selen Bilgin Olmez
M.S. in Sustainability Management
Staff Associate sb5151@columbia.edu