## Slide 1: Storing Energy
Birru Lucha, Petr Jenicek, David Foye, Ashley Kim, Devashri Mehrotra, Shailesh Mishra, Hassan Riaz, Xiaodan Zhu, Hyae Ryung Kim, and Gernot Wagner
4 March 2025

## Slide 2
The energy storage opportunity
Mobility energy storage
Utility energy storage

## Slide 3: Executive Summary: The energy storage opportunity

## Slide 4
Utility: Renewables like solar and wind must grow twelvefold, with expected combined capacity of ~15 TW to achieve net zero by 2050.
  Energy storage is essential for supporting the growth of renewables, with global capacity projected to reach 1.5 TW by 2030, mainly for front-of-the-meter applications.
  However, capacity growth so far is failing to keep pace with rapid solar and wind growth.
Energy storage has the potential to abate up to 17 Gt of CO2 emissions across sectors by 2050, primarily by supporting renewable power and the electrification of transport.
Credit: Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Mobility: EVs are expected to reach 95% share in vehicle sales by 2035 under the Net Zero Emissions (NZE) Scenario.
The shift is expected to drive rapid growth in global EV battery demand, with capacity needs projected to exceed 20 TWh by 2050.
Demand will grow by ~23% annually until 2035, driven by EV adoption and government policies before stabilizing as EV market penetration reaches saturation.
Key messages The energy storage opportunity
Energy storage plays a critical role in the transition to a clean and sustainable energy future, tackling the challenges of using intermittent renewable energy sources, improving grid stability and dispatchability, and powering electric vehicles (EVs).
Innovations in battery storage have reduced costs and curtailment issues, enhancing economic competitiveness. However, timely grid infrastructure updates and storage deployment are critical to fully integrate renewables.

## Slide 5: The energy storage system (ESS) plays three key roles: Providing stability, dispatchability, and portability
Improves reliability by reducing transmission constraints and providing grid stability services.
For instance, an ESS can provide frequency regulation to maintain a system's frequency at 60 Hz, which helps balance the network's load and the power generated.
Sources: C3controls, Understanding Energy Storage Systems (2023); EVESCO, Battery Energy Storage; Renault Group, Rallying Heritage (2022); Drive Clean, Battery-Electric Cars.
Credit: Devashri Mehrotra, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Stability
Enables electricity generated at one time to be used at a later time.
Demand for energy storage plays an increasingly important role in maintaining the balance between supply and demand as renewable energy sources (wind, hydroelectric, solar) expand and electricity becomes more decentralized.
Dispatchability
Allows EVs to be charged and used anywhere and at any time.
It controls the frequency of the AC power being sent to the motor, which directly influences an EV’s speed.
Portability

## Slide 6: Energy storage can help abate up to 17 Gt of CO2e emissions by 2050 in select subsectors depending on the transition scenario
Waste 21%
Oil 3%
Agricultural fuel 4%
Natural 3%
LULUCF 17%
Agriculture, land use, and waste
Coal 14%
Road 22%
Industry
Non-ferrous 2%
Refining 4%
Aviation 10%
Non-metallic minerals 2%
Coal mining 7%
Marine 10%
Chemical 13%
Crops 27%
Oil and gas 21%
3%
Transport
Iron and steel 9%
Remaining industry 17%
Buildings
31%
28%
18%
15%
8%
Residential 53%
HFCs 27%
Commercial 20%
Power and heat
Livestock 31 %
Cement 16%
Abatement in Economic Transition Scenario
Additional abatement in NZE Scenario
48% to 80%
in all power and heat
36% to 54% in road
5% to 8%
in iron and steel
~1% in cement
~1% in marine, rail, and aviation combined
CO2e emissions in 2024*: ~50 billion tonnes
*2024 emissions based on projections.
Sources: Scope 1 emissions from Rhodium Group Climate Deck (September 2024); abatement estimates from BloombergNEF (2024), IRENA, and IEA (2023). Credit: Devashri Mehrotra, Birru Lucha, Theo Moers, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Other
3%

## Slide 7: Focus on energy storage technologies in mobility and utility sectors to identify future opportunities
Areas to explore
Utility
Pumped-storage hydropower (PSH)
Compressed-air energy storage (CAES)
Battery
Thermal energy storage (TES)
Hydrogen
Flywheel
Credit: Ashley Kim, Xiaodan Zhu, Devashri Mehrotra, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Mobility
Lithium iron phosphate (LFP)
Nickel cobalt manganese (NCM)
Nickel cobalt aluminum (NCA)
Solid state
Sodium ion
Nickel-metal hydride
Lead-acid
Ultracapacitors
Demand projections
Characteristic by technology, including:
  Maturity
  Pros and cons
  Market share
  Cost projections
  Growth opportunities
Technologies with the greatest potential are highlighted in forthcoming slides, based on:
Current market share
Growth potential
Cost projections
Uses in mobility and utility

## Slide 8: CO2 emissions from passenger vehicles could be largely eliminated by 2050
Sources: IEA, Net Zero by 2050 (2021); IEA, Batteries and Secure Energy Transitions (2024).
Credit: Devashri Mehrotra, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Global CO2 transport emissions by mode, Gt
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Light-duty Vehicles | 3.1 | 3.3 | 2 | 0.6 | 0.2
Heavy Trucks | 1.5 | 1.8 | 1.7 | 1 | 0.3
Other Road | 0.6 | 0.5 | 0.45 | 0.25 | 0.1
Shipping | 0.8 | 0.85 | 0.65 | 0.3 | 0.2
Aviation | 0.77 | 0.5 | 0.7 | 0.4 | 0.3
Rail | 0.2 | 0.2 | 0.15 | 0.1 | 0.05
Observations
CO2 emissions from transport are projected to drop to ~0.7 Gt by 2050 based on the Next Zero Emissions Scenario.
Despite this decline, passenger travel is expected to almost double by 2050, and freight activity will more than double from 2020 levels.
Electric vehicle adoption will be an important part of that shift, with the quantity of battery-electric, plug-in hybrid, and fuel-cell-powered electric cars and vans rising from just 11 million in 2020 to 350 million by 2030 and approaching 2 billion by 2050.
Mobility

## Slide 9: EVs to play an important role, with sales projected to increase to as much as 95% of vehicle purchases by 2035
Chart: 
| 2023 | 2030 | 2035
 | 15 | 65 | 95
 | 15 | 45 | 66
 | 15 | 40 | 50
 | 17.8 | 45 | 59
0
10
20
30
40
50
60
70
80
90
100
EV sales share by IEA and BNEF scenarios1 (%)
65
50
592
Electric vehicle adoption rate by scenario
Observations
In the NZE Scenario, EV sales as a share of new vehicles grow over the next few years, reaching about 65% in 2030 and 95% in 2035.
Two-/three-wheeler and light-duty vehicles are expected to lead adoption by 2035 with 60% to 100% adoption across scenarios, while trucks lag at 20% to 55% adoption.
However, the discrepancy between policy implementation and announced ambitions continues to widen over time, as many initiatives, including the U.S. IRA, the EU Green Deal Industrial Plan, and China’s 14th Five-Year Plan, tend to prioritize short- to medium-term incentives.
[IEA] Net Zero Emission by 2050 Scenario
[IEA] Announced Pledges Scenario
[IEA] Stated Policies Scenario
[BNEF] Economic Transition Scenario
1) IEA scenario: All EVs except two- and three-wheelers; BNEF scenario: Passenger EVs. 2) Assumed linear growth from 2030 to 2040.
Sources: IEA, Global EV Outlook 2024 (2024); BloombergNEF, Electric Vehicle Outlook (2024).
Credit: Ashley Kim, Devashri Mehrotra, Birru Pagi Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
| 0.25 | 0.75 | 1.25 | 1.75
 | 100 | 98 | 86 | 57
 | 74 | 67 | 39 | 29
 | 61 | 54 | 29 | 22
 | 12 | 16 | 2 | 1
Two-/three-
wheeler
Light-duty
vehicle
Bus
Truck
0
10
20
30
40
50
60
70
80
90
100
EV sales share by mode and IEA scenario (%), 2035
Net Zero Scenario
Announced Pledge Scenario
Stated Policies Scenario
2023
Mobility

## Slide 10: Global battery demand for EVs expected to reach >5 TWh in 2030
Observations
Annual global demand for batteries will grow at a rate of ~23% p.a. until 2035.
The steep increase until 2035 will be driven by advancements in EV adoption, in places like:
  Norway, which continues to lead in EV deployment, with electric cars accounting for ~93% of total sales in 2023.
  China, representing ~60% of all new electric car registrations worldwide in 2023.
  Canada, targeting at least 60% of zero-emission vehicles by 2030.
  The United States and European Union, which recently implemented emissions standards for heavy-duty vehicles, paving the way for increased adoption of electric trucks and buses in the years ahead.
Demand growth will subsequently slow to 5%-10% p.a. between 2040 and 2050, as the global EV sales share is expected to reach 98% by 2035.
Sources: IEA, Global EV Outlook (2024); IEA, Net Zero Roadmap (2023).
Credit: Birru Pagi Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 770 | 5400 | 9000 | 22800
2023
2030
2035
2050
0.8
5.4
9.0
19-28
+23%
5%-8%
Global EV battery demand, TWh/year
Note: Projection until 2035 is based on the IEA Global EV Outlook for EV battery only. Projection for 2040 to 2050 is based on extrapolation from road transport electricity demand from IEA.
IEA projection
Extrapolated from IEA electricity demand growth projection for road transport
CAGR, % p.a.
Mobility

## Slide 11: To achieve net zero, intermittent sources such as solar and wind must grow; energy storage is critical to enable integration
Source: BloombergNEF, New Energy Outlook (2024).
Credit: David Foye, Birru Lucha, Hyae Ryung Kim , and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
However, energy storage is failing to keep pace with rapid renewable capacity growth
Chart: 
 | 2831.4551 | 2863.4515 | 2913.3434 | 2974.5232 | 3056.3512 | 3156.9667 | 3294.1152 | 3417.6176 | 3514.6185 | 3625.361 | 3774.494 | 3880.5267 | 3940.5785 | 4049.9072 | 4163.3784 | 4277.5867 | 4390.7109 | 4461.8881 | 4565.0721 | 4620.1518 | 4702.3094 | 4756.1744 | 4854.8123 | 4938.4987 | 5064.5537 | 5134.6468 | 5230.0246 | 5339.7351 | 5421.2486 | 5493.774 | 5608.5212 | 5755.449 | 5922.8714 | 6080.3315 | 6252.1254 | 6434.908 | 6641.6022 | 6827.8905 | 7021.7776 | 7198.8352 | 7346.1279 | 7471.6637 | 7605.8875 | 7743.0101 | 7885.098 | 8040.9407 | 8181.2146 | 8311.4852 | 8447.5877 | 8590.3151 | 8737.8387
 | 18.1338 | 22.9996 | 29.4457 | 36.2966 | 44.3511 | 54.9752 | 69.7158 | 89.4108 | 120.488 | 165.226 | 216.0806 | 280.001 | 375.3073 | 450.6495 | 544.0339 | 662.2944 | 792.0876 | 945.9815 | 1099.2737 | 1279.871 | 1528.9764 | 1811.4802 | 2144.6705 | 2654.1873 | 3211.487 | 3824.8625 | 4458.2262 | 5158.9553 | 5901.3447 | 6694.7669 | 7392.3364 | 8129.6171 | 8812.8661 | 9437.8749 | 10017.2056 | 10554.6804 | 10953.3858 | 11334.1514 | 11647.3829 | 12040.2892 | 12366.5617 | 12703.6219 | 13056.5948 | 13387.2128 | 13716.3701 | 13996.3359 | 14344.1439 | 14705.2023 | 15022.192 | 15314.2204 | 15639.4622
0
5
10
15
20
25
2000
2010
2020
2030
2040
2050
Intermittent (solar and wind generation)
Dispatchable (coal, gas, hydrogen, nuclear, and oil)
Energy storage will play a significant role, as solar and wind capacity is projected to reach ~15 TW by 2035
Chart: 
 | 119.9927 | 126.0386 | 133.6471 | 137.0321 | 140.3479 | 146.32 | 160.1662 | 191.4011
 | 1738.1643 | 1903.3414 | 2074.4148 | 2245.9264 | 2436.9043 | 2708.8119 | 3017.1911 | 3383.8373
0.0
0.5
1.0
1.5
2.0
2.5
3.0
3.5
2015
2016
2017
2018
2019
2020
2021
2022
Storage capacity
Renewable energy capacity
Global intermittent generation vs. dispatchable generation from 2000 to 2050, TW
Installed capacity of storage compared to renewable energy, TW
Utility

## Slide 12: Integrating storage expected to gradually boost renewable energy economics relative to fossil fuels
1) Solar PV installation paired with four-hour duration battery storage; 2) VALCOE is value-adjusted LCOE. That includes both the cost of the electricity and the value to the electricity system.
Source: IEA, Batteries and Secure Energy Transitions (2024).
Credit: David Foye, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Observations
Further innovations in battery chemistry and manufacturing are expected to lower the global average cost of lithium-ion batteries by 40% between 2023 and 2030.
The competitiveness of solar PV combined with batteries compared to new coal- and natural gas-fired plants varies:
  In India, the current cost is already competitive.
  In China and the US, the cost will be competitive before 2030.
Chart: 
| 2022 | 2030
 | 80 | 55
 | 65 | 70
 | 75 | 45
 | 65 | 90
Chart: 
| 2022 | 2030
 | 70 | 50
 | 65 | 65
 | 70 | 45
 | 65 | 70
LCOE and value-adjusted LCOE (VALCOE)1 for solar PV plus battery storage,2 coal, and natural gas for China and the United States, USD/MWh
China
U.S.
Solar PV with storage (VALCOE)
Coal (VALCOE)
Solar PV with storage (LCOE)
Coal (LCOE)
Gas (VALCOE)
Solar PV with storage (LCOE)
Gas (LCOE)
Utility
Solar PV with storage (VALCOE)

## Slide 13: Delays in grid upgrades and energy storage deployment to slow transition from fossil-based sources to renewables
1) EJ = exajoules, a unit of measurement for energy; 1 exajoule is 277.7 TWh
Sources: IEA, Electricity Grids and Secure Energy Transitions (2023); McKinsey, How grid operators can integrate the coming wave of renewable energy (2024).
Credit: David Foye, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Grid delay inhibits transition from coal and gas by ~37 and ~31 EJs, respectively, while reducing renewable energy power generation by ~15% in 2050 vs. pledges
Observations
Energy storage is essential to achieving significant reductions in fossil fuel use by enabling greater integration of renewable energy sources.
Energy storage can help balance the variability of renewable energy by storing excess energy and releasing it when needed.
Grid operators must invest in modernizing grid infrastructure to handle the intermittent nature of renewable energy, reduce congestion, and improve grid flexibility.
Timely updates to grid infrastructure and energy storage deployment are essential for reducing dependency on coal and natural gas.
Chart: 
| 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
 | 98.88 | 98.45 | 83.13 | 70.06 | 50.07 | 37.42 | 27.55
 | 98.88 | 98.45 | 83.48 | 78.8 | 71.21 | 68.29 | 64.27
 | 54.92 | 55.97 | 49.75 | 42.1 | 37.94 | 34.37 | 30.97
 | 54.92 | 55.97 | 49.95 | 50.26 | 54.47 | 58.34 | 60.68
Coal (announced pledge)
Coal (in case of grid delay)
Gas (announced pledge)
Gas (grid delay)
Chart: 
| 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
 | 9 | 17 | 30 | 41 | 49 | 55 | 59
 | 9 | 17 | 29 | 35 | 39 | 42 | 44
Solar and wind (announced pledge)
Solar and wind (in case of grid delay)
Coal and gas transition, EJ1
Share of solar and wind in total generation capacity, %
Utility

## Slide 14: Growth in battery storage capacity has reduced curtailment and stabilized electricity pricing in California
1) The day-ahead market is made up of three market processes that run sequentially (market power mitigation test, integrated forward market, and residual unit commitment process. 2) The real time is a spot market in which utilities can buy power to meet the last few increments of demand not covered in the day-ahead market.
Sources: California Energy Commission, Electric Generation Capacity and Energy; CAISO, Special Report on Battery Storage (2023), CAISO LMP (2024); ISO New England.
Credit: David Foye, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 503.3 | 2506 | 4217.4 | 5018
 | 20960 | 22299 | 23754 | 27155
 | 32.4956 | 52.3618 | 89.0927 | 61.509
 | 25.5698 | 43.1859 | 79.7575 | 51.5178
0
4,000
2,000
6,000
8,000
10,000
12,000
14,000
16,000
18,000
20,000
22,000
24,000
26,000
28,000
LMP, USD/MW
2020
2021
2022
2023
23,754
20,960
Capacity, MW
22,299
4,217
5,018
27,155
2,506
+6%
+7%
+14%
LMP_DAM
LMP_RT
Battery capacity
Solar and wind capacity
Observations
California’s Independent System Operator (CAISO) experienced a notable increase in renewable energy capacity, challenging the grid's ability to integrate this supply.
The surge in renewable energy led to higher levels of curtailment, wasting excess energy and driving up locational marginal pricing (LMP) in both the day-ahead market1 and real-time market.2
LMP provides a method for wholesale electricity prices to represent the value of electric energy at various locations, considering load patterns, generation, and the physical constraints of the transmission system.
Utility
Cumulative CAISO intermittent capacity plus battery storage capacity vs. LMP, MW, USD/MW

## Slide 15: Global installed energy storage capacity projected to grow 5x by 2030, and >80% at front-of-the-meter
Source: IEA, Batteries and Secure Energy Transitions (2023).
Credit: David Foye, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Observations
Front-of-meter storage will continue to grow, driven by the need for large-scale grid support and renewable energy integration.
These operations are largely managed by utility companies and aim to address the energy needs of diverse consumers.
Behind-the-meter storage will grow as well, due to the adoption of renewable energy in residential and commercial settings.
BTM, combined with distributed generation and other grid assets implemented at the distribution level, is broadly known as distributed energy resources (DERS).
BTM storage differs from FTM, depending on the ownership of the systems, their installation locations, as well as the size and number of systems deployed.
Front-of-the-meter (FTM) vs. behind-the-meter (BTM) energy storage
Chart: 
 | 33 | 203
 | 213 | 1294
2023
2030
246
1,497
~500%
FTM
BTM
FTM
Meter
BTM
Global installed energy storage capacity, GW
FTM storage refers to energy-related activities that occur on the utility side of the grid, typically involving large-scale energy generation, transmission, and distribution. infrastructure.
BTM storage refers to customer-sited stationary storage systems that are connected to the distribution system on the customer’s side of the utility’s service. meter
Utility

## Slide 16
The energy storage opportunity
Mobility energy storage
  Technology landscape
  Opportunities and unlocks
  Case study
Utility energy storage

## Slide 17: Mobility energy storage

## Slide 18
The energy storage opportunity
Mobility energy storage
  Technology landscape
  Opportunities and unlocks
  Case study
Utility energy storage

## Slide 19
Market trends: NCM led the EV battery market with a 60% share in 2023, due to its superior energy density. However, LFP has been gaining momentum of late, driven by Chinese OEMs and concerns about cobalt and nickel availability.
1) LFP = lithium iron phosphate; NCM = nickel cobalt manganese; NCA = nickel cobalt aluminum; NCX = NCM and NCA variants
Credit: Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Future scenarios: We expect LFP to surpass NCM in market share over the next five to 10 years, driven by advancements in energy storage, with other chemistries also entering the mix. For these technologies to gain market share:
LFP should improve energy density (e.g., through lithium manganese iron phosphate or LMFP, a promising new cathode material) while decentralizing capacity across regions.
NCX will need to resolve issues with thermal runaway while ensuring critical mineral supply availability.
Li-S/Air will require sufficient investment in R&D to realize the theoretical level of energy density and efficiency.
Key messages Mobility energy storage: Technology landscape
Various storage technologies are available for electric vehicles, with lithium-ion batteries being the most prevalent due to their high energy density and reliable performance. LiBs consist of diverse chemistries, including LFP, NCM, NCA, and solid-state batteries.
Sodium-ion batteries, an emerging battery chemistry, are a lower-cost alternative to LiBs due to the abundance of sodium resources. They are also safer and made with similar manufacturing processes. However, challenges remain to achieve an energy density comparable to that of LiB.

## Slide 20: LiBs dominate the market due to high energy density and strong track record; SiBs ramping up as an alternative
*Adjusted based on 2020 CPI; cell cost of NCM 811 is used for NCM.
Sources: IEA, Global EV Outlook (2024); Drive Electric Tennessee (2023); Wood Mackenzie, LFP cathode supply (2023); Journal of Energy Storage (2024); BloombergNEF, Top 10 Energy Storage Trends (2023). Credit: Ashley Kim, Devashri Mehrotra, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Non-exhaustive | Lithium-ion battery (LiB) |  |  |  | Sodium-ion battery (SiB)
 | LFP | NCM | NCA | Solid-state battery | 
Description | Uses lithium iron phosphate as cathode | Uses nickel cobalt manganese as cathode | Uses nickel cobalt aluminum oxide as cathode | Li-ion battery with solid electrolyte | Transfers energy through the movement of charged sodium ions between the cathode and the anode during charge and discharge cycles
Pros and cons | Low cost due to relatively inexpensive critical raw materials Safer with thermal stability Lower energy density (175-425 Wh/kg) shortens driving range Reduced capacity and power output in low temperatures | Higher energy density (340-420 Wh/kg), increasing driving range Uses nickel and cobalt, two relatively expensive raw materials | Aluminum oxide allows for faster charging capabilities Costly due to limited supply of cobalt and nickel | Enables packing more energy into less space Pushes cell-level energy density up to 500 Wh/kg Safer due to non-flammable electrolytes Sensitive to contaminants and therefore requires large volumes of high-quality materials | Saves manufacturing time by ~50% and reduces plant CapEx by ~30% compared to LiBs, as it doesn't require formation Inherently safer with no risk of thermal runaway Significantly more cost effective, with sodium hydroxide as a key raw material Suitable for a broader range of applications given its adaptability to varying temperatures Lower energy density (130-160 Wh/kg) suitable for only two-/three-wheelers or stationary batteries
Global average cell cost*, USD/KWh |  |  |  | Not yet commercialized | Data not available
Chart: 
 | 101 | 35
 | 200
-10% p.a.
Chart: 
 | 105 | 52
-7% p.a.
Chart: 
 | 112 | 58
-6% p.a.
2020
2030F

## Slide 21: Other batteries used for more limited or complementary applications
Sources: Encyclopedia of Electrochemical Power Sources (2009); Solar Energy Materials and Solar Cells (2014); Green Cars (2024); Mobility Engineering Tech (2023).
Credit: Ashley Kim, Devashri Mehrotra, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Non-exhaustive | Nickel-metal hydride (NiMH) | Lead-acid | Ultracapacitor
Description | Uses nickel hydroxyl oxide as cathode material and a hydrogen-absorbing alloy as anode | Consists of an anode made of spongy or porous lead, a cathode made of lead dioxide, and an electrolyte composed of sulfuric acid | Double-layer capacitors that store polarized liquid between an electrode and an electrolyte
Pros and cons | Lasts longer than a Li-B and is safe to use Can be operated across a broad temperature range (below -30°C and above 100°C) Expensive to produce Generates a lot of heat at high temperatures Has a high discharge rate | Inexpensive and safe to use Relatively short life Worse performance in cold weather Heavy and less durable than nickel and lithium-based systems when deep-cycled | Can be charged multiple times with almost no battery degradation Higher power density than batteries makes it more suitable for high-drain applications Lower energy density than batteries, so it is less suitable for long-range EVs
Applications | Typically used in hybrid vehicles, where a gasoline engine operates alongside electric motors and recharges the onboard battery While mostly altered by Li-B, a few Indian motor companies and Toyota still favor NiMH for some applications (e.g., hybrid-electric vehicles) | In EVs, it cannot independently power the electric motor but is primarily used to assist auxiliary features, such as providing backup power for power steering, brake boosting, and safety features | Serves as secondary storage devices, aiding in load balancing for lithium-ion battery packs Provides EVs an extra boost of power for acceleration

## Slide 22: LFP chemistries increasing in market share compared to NCX chemistries, with 2030 forecasts indicating majority share
Battery market share (based on capacity) by cathode type, %
1) NCM refers to Li-based batteries with nickel-cobalt-manganese based cathode; NCA refers to Li-based batteries with nickel-cobalt-aluminum based cathode.
Sources: IEA, Global EV Outlook (2024); Argus, NMC to LFP transition (2023); Nature, Future material demand for automotive Li-based batteries (2020); Focus Distribution, Forecasting demand for batteries (2022).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 72 | 63 | 60 | 20 | 15 | 10
 | 28 | 37 | 40 | 20 | 25 | 30
 | 0 | 0 | 0 | 60 | 60 | 60
0
2021
0
2022
0
2023
2030
2040
2050
Actual market shares
Projected market shares
Observations
NCM has been dominating the market for EV batteries due to the high energy density.
The recent shift to LFP is driven by fierce cost competition, with Chinese OEMs spearheading this expansion.
Future market share among battery chemistries is still uncertain given the continuously evolving technology. However, recent capacity expansions in LFP suggest a large share in LFP.
  Once cost reductions saturate across chemistries, achieving further performance improvements may be necessary to achieve dominance in the field.
These scenarios will affect raw material demand and necessitate a further review of reserve availability.
LFP
NCM
NCA

## Slide 23: NCM and LFP currently the leading technologies in battery systems; room for further technological development exists
Thermal runaway at > 210°C | 250°C | 270°C | 190°C (All solid-state Li-S)
2,400 Wh/kg | 2,400 Wh/kg | 1,100 Wh/kg | 2,600-11,140 Wh/kg
$95-$100/kWh | $95-$100/kWh | $70-$75/kWh | N/A (not commercialized yet; expected to be cheaper given that sulfur is $0.10-$0.15/kg vs. cobalt at $33-$35/kg)
500-1,500 cycles | 500-1,500 cycles | >2,000 cycles | <1,000 cycles
0.7-1C | 0.7C | Charging c-rate of 1C | 3C
How the different Li-ion battery technologies rate on key features
NCM
NCA
LFP
Safety
Service time per charge
Price2
Lifespan
(Endurance)
Energy
density1
Observations
As of 2022, ~50% of EV makers relied on NCM batteries because their high energy density is crucial for maximizing driving range.
NCM battery and EV makers have adjusted cathode active material components to improve energy density and manage raw material risks, increasing nickel content.
  LG supplied NCM 811 batteries (80% nickel, 10% cobalt, and 10% manganese) for Tesla’s Model 3S in China.
  Tesla, VW, and others are developing high-nickel batteries for larger vehicles.
Starting in 2023, price and safety are increasingly critical factors, as driving range requirements are largely being met.
  LFP is becoming more popular because of qualities like its competitive cost and relative safety. LFP technology has also advanced to overcome its inferior driving range.
  NCX is being modified to cut costs by lowering cobalt content and enhance safety by decreasing nickel content and increasing manganese content.
NCA, deployed by Tesla, Samsung SDI, and Panasonic, has innate limitations because it doesn’t use manganese, a crucial safety element. Reducing cobalt content for cost saving in NCA has been difficult, since it plays a key balancing role.
Despite offering energy density that is potential higher than conventional Li-ion batteries like NCM/NCA/LFP, Li-S batteries must overcome multiple technical challenges before they are ready for commercialization.
1) Compared to theoretically achievable cell-level energy density, Li-S has achieved 450 Wh/kg and Li-air has achieved 610 Wh/kg for practical applications. 2) Cell costs as of 2023, adjusted to 2020 CPI. For NCM, the cell cost is weighted by the 2023 market share distribution across NCM 111, 532, 622, 811, and 955.
Sources: IEA, Net Zero by 2050 (2021); IEA, Batteries and Secure Energy Transitions (2024); One Charge (2023); Flash Battery (2022); Energies (2019); Volts (2021); S&P Global, Gas and Power; Journal of Energy Storage (2023); Materials for Renewable and Sustainable Energy (2022); SmartMat (2023); ArenaEV (2022); Joule (2022); Lyten (2022); Chemistry Europe (2018).
Credit: Devashri Mehrotra, Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Low
Moderate
High
Performance
Li-S/air

## Slide 24: Technological advancements, raw material supply chains, and market adoption to determine which chemistries lead in the future
Sources: Nature, Material demand for lithium-based batteries (2020); S&P Global, Lithium-ion battery capacity (2023); S&P Global, Lower lithium prices (2024); Argus, NMC to LFP transition (2023); Forbes, Lithium Iron Phosphate (2023); Journal of Energy Storage, Deploying lithium sulfur batteries (2023).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Key conditions to be satisfied for individual chemistries to achieve dominance
Level of difficulty
Li-S/air
LFP
Market adoption
Investments needed in R&D to overcome technical challenges
H
Increasingly being adopted in light-duty vehicle market
L
NCX
Supply chain, including raw material supply
More investment needed in LFP supply outside of China (both upstream and downstream)
Need for a stable, cost-effective, and circular supply of nickel and a shift away from cobalt
Technological advancement
Overcome technical challenges to achieve theoretical energy density and efficiency levels that provide an advantage over conventional LiBs
H
Improve energy density at cell level (e.g., LMFP) and pack level (e.g., advanced cell-to-pack technology)
Resolve technical shortcomings, including safety issues like greater risk of thermal runaway and shorter battery lifespan
M
M
H
M
L
Low
M
Moderate
H
High
N/A
N/A

## Slide 25: While dominant today, NCX must resolve safety issues and improve battery lifespan to stay on top
Technological advancements required
Supply chain, including raw material
Bottlenecks
Potential solutions and level of difficulty
Lifespan: NCM batteries degrade fast, lasting just 800 to 2,000 cycles, or three to four years. LFP batteries are more durable, lasting ~3,000 cycles, or seven to eight years.
A battery thermal management system, along with CAM improvements such as the introduction of a single crystalline structure, efficient current distribution, and optimal electrode configurations can extend the battery’s lifecycle. However, NCX's battery chemistry means its upper cycle threshold will typically be lower than for LFP.
Safety: Physically damaged batteries or those with manufacturing defects are more prone to thermal runaway, with six recalls in the past three years (e.g., Chevrolet Bolt).
The release of oxygen from the nickel-cobalt mixture during an internal short circuit can increase heat and raise safety issues.
Battery enhancement options include additives to active materials, improvements in separators, and external measures such as battery management systems, cooling, and cell balancing. However, they tend to come at the expense of energy density, power, and charging time.
Solid-state batteries could provide better stability without losing the advantages of NCM.
Reducing nickel content and increasing manganese could also help prevent NCM thermal runaway.
M
Nickel (Ni) and cobalt (Co) are relatively scarce and production is geographically concentrated, leading to high prices and high price volatility.
Ni and Co prices doubled from 2021 to mid-2023 in the wake of the Russia-Ukraine War and due to increased demand for EVs.
Battery chemistry advancements like cobalt-free batteries (in which cobalt is replaced with nickel for higher performance and manganese for lower cost) and recycling will significantly mitigate long-term supply risk, but it could be hard to avoid a shortage in cobalt supply through at least 2028 or potentially through 2033
Supply chain diversification will also be important. Australia, which has all four key elements for NCX battery production, could be an alternative source of raw materials.
More sustainable practices include:
Efforts led by international organizations (e.g., IMF) and industry leaders (e.g., BASF) to formalize the cobalt supply chain, including introducing common standards and metrics, implementing a monitoring or assessment process, and promoting knowledge sharing.
High-pressure acid leaching can offer a less energy-intensive extraction technique for nickel. Bioleaching employs microorganisms to extract metals from ore or e-waste, offering an easier method to process ore, without relying on high temperatures.
Sourcing of Ni and Co can be controversial:
The Democratic Republic of Congo produces >70% of the world's cobalt and possesses ~50% of the world’s reserve, but mining utilizes child labor and Congo faces political instability.
Nickel mining involves significant environmental damage, including water pollution and energy-intensive smelting processes with high GHG emissions.
M
Sources: Nature, Material demand for lithium-based batteries (2020); S&P Global, Lithium-ion battery capacity (2023); S&P Global, Lower lithium prices (2024); Argus, NMC to LFP transition (2023); Forbes, Lithium Iron Phosphate (2023); Journal of Energy Storage, Deploying lithium sulfur batteries (2023); IEF, Nickel (2024); Nature, Battery technology and recycling (2022); Journal of Energy Chemistry, Lithium-ion battery safety concerns (2021); WEF, Making Mining Safe and Fair (2020); Frontiers in Batteries and Electrochemistry (2024).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).

## Slide 26: LFP already popular in China, but wider adoption required to keep growing market share
Bottlenecks
Potential solutions and level of difficulty
Technological advancements required
Energy density: As of 2023, LFP battery cells deliver an energy density of about 160 Wh/kg, allowing a range of around 200 miles (320 km). This is inferior to NCM battery cells, which offer a higher energy density of about 250 Wh/kg, enabling a range of roughly 300 miles (480 km).
M
Blend with other materials to achieve higher energy density at the cell level.
Chinese battery manufacturers as well as European, American, and Korean players are developing LMFP or other variations of LFP (e.g., CATL’s M3P), which are expected to achieve 15% to 20% higher energy density in comparison to conventional LFP.
Realize higher energy density at the pack level:
At the battery-pack level, LFP energy density can effectively match that of NCM, thanks to its lower thermal runaway risk, which allows for tighter cell packing.
Cell-to-pack technology builds a pack from battery cells without modules, reducing the need for inert materials and helping to increase energy density.
Sources: Argus, NMC to LFP transition (2023); Forbes, Lithium Iron Phosphate (2023); Journal of Energy Storage, Deploying lithium sulfur batteries (2023); Nature, EV battery chemistry (2024); S&P Global, Lithium-ion battery capacity (2023); Stellantis (2023); Ford, BlueOval Battery Park Michigan (2024); IEA, Global EV Outlook (2024); Nature, EV battery chemistry (2024), S&P Global, China, South Korea battery-makers (2024).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Market adoption
The first-mover advantage of LFP in China has led to limited LFP uptake outside of China.
LFP's market share in Europe is a mere 5.2% and less than 10% in the U.S. as of 2023.
Non-Chinese OEMs targeting the low/entry car segment are increasingly announcing plans to adopt LFP because of its low cost (e.g., the Stellantis-CATL partnership, Ford’s BlueOval Battery Park).
L
Supply chain, including raw material
The LFP supply chain is extremely concentrated in China, making it vulnerable to disruption.
In the upstream, a significant share of CAM materials, including cobalt and nickel, currently comes from operations with substantial ownership by China-headquartered companies, making diversification extremely difficult.
Mid- to downstream, China produced 95% of LFP batteries in 2022, while the U.S. produced just 3% of light-duty vehicles with LFP batteries.
Increase investment in battery metals extraction, refining, and battery production capabilities outside China.
One option is to build refining capacities in North America and FTA partners, especially for minerals with limited local reserve availability, such as cobalt and nickel.
LFP production in South Korea-headquartered battery producers could open up the commercialization of LFP batteries in North America.
Global flows of lithium
H
See appendix for full-size diagram.

## Slide 27: Li-S/air batteries must overcome technical challenges before mass production and widespread market adoption
Technological advancements required
Bottlenecks
Potential solutions and level of difficulty
Li-sulfur battery (LiSB): Needs to overcome multiple technical challenges to achieve theoretical energy density levels, including self-discharging and high internal resistance due to the shuttle effect (Fig. 1), rapid capacity failing, and above all, reaction stability.
LiSB: Active research is underway, including:
Securing a level of reaction stability comparable to LiB without adding guardrails that may compensate for energy density, which will be key.
Constructing novel nanostructured sulfur electrodes and developing appropriate electrolytes/separators to overcome the disadvantages.
LAB: Multiple areas still require further study to achieve the theoretical level of performance, including:
Discharge-recharge mechanisms and kinetics
Improvement in ionic conductivity and stability of electrolytes
Trade-off strategies for balancing interfacial compactness and catalysts to enable high energy density
While LiSB is closer to commercialization, LAB is increasingly seen as a less viable option, mainly due to the openness of the thermodynamic system, which may lead to extremely high entropy.
Market adoption
LiSB/LAB: Commercialization remains in early stages for both, mainly due to their significantly shorter lifecycle.
For example, to be marketable, LiSB cells must demonstrate trustworthy performance for at least 200 cycles without a capacity drop of more than 60%. If they maintain performance for 500 cycles, meanwhile, they can be adopted in a wider range of applications.
LiSB: OEMs (e.g., Stellantis) are investing in LiSB startups (e.g., Lyten) to accelerate commercialization.
LAB: A LAB design developed in 2023 operated in a stable manner over 1,000 cycles of test charging/discharging.
Sources: Journal of Energy Storage, Deploying lithium sulfur batteries (2023); Stellantis, Invests in Lyten (2023); Science, Room temperature rechargeable Li2O-based lithium-air battery (2023); BatteryBits, Introduction to Solid-State Batteries (2022); SmartMat, Solid-state Li–air batteries (2023).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Li-air battery (LAB): Faces challenges in interfacial continuity/compatibility, air stability, significant overpotential during discharge/charge, and the working mechanism of solid-state electrolytes.
Polysulfide shuttle effect
The shuttle effect refers to the phenomenon where soluble polysulfide intermediates that formed during the battery’s charge and discharge cycles dissolve into the electrolyte and travel between the anode and cathode.
This results in loss of active material, self-discharging, poor energy efficiency, and degradation of electrodes.
H
H
See appendix for full-size diagram

## Slide 28: SiBs offer cost, temperature range, and safety advantages compared to LiBs; energy density still a challenge
Observations
SiB technology is rising as an alternative to LiB, as it is less susceptible to resource availability issues, has a low material cost, and is less dependent on the Chinese supply chain than LiB.
Sharing the same cell structures and electro-chemical reaction processes as LiB but utilizing Na+ as the charge carrier instead of Li+, SiB has some advantages in terms of cost and safety. However, achieving an energy density comparable to that of LiB remains a challenge.
Sources: MIT Technology Review, How sodium could change the game (2023); ING, Can sodium-ion batteries replace lithium-ion ones? (2023); Engineering, Sodium-Ion Batteries (2023); Shanghai Metals Market, Spot Metal Prices (2025).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
| Cost-saving | Energy density | Safety | Cycling stability | Temperature range
SIBs | 4.5 | 3.8 | 4.9 | 4.7 | 4.9
LIBs | 2 | 5 | 2.6 | 5 | 3
LABs | 4.4 | 2.3 | 3.2 | 2.7 | 4
How established rechargeable battery technologies stack up
Cost:
Sodium is abundant and therefore inexpensive, especially relative to lithium (pure sodium cost USD $290/MT in 2023 vs. a lithium compound cost of USD $35,000/MT)
SiBs are made using technology similar to that in LiBs, requiring minimal additional capital investments.
Energy density:
SiBs could reach pack densities of nearly 150 Wh/kg by 2025, approaching the energy density of LiBs typically used in EVs (250-300 Wh/kg)
New electrode materials could enable SiBs to improve their energy density even further, achieving a level close to that of LiBs.
Safety:
SiBs could possibly avoid thermal runaway:
By avoiding highly flammable diethyl carbonate (DEC) and dimethyl carbonate (DMC) used in LIBs, SIBs can utilize electrolytes with higher propylene carbonate content, significantly enhancing safety.
Unlike LIBs, which require transport at a specific state of charge to prevent copper foil dissolution, SIBs can be stored and transported in a fully discharged state (0V), providing an ultimate safety condition.
Chart: 
| 2010 | 2015 | 2016 | 2017 | 2018 | 2019 | 2021 | 2022
 | 87 | 117 | 111 | 126 | 140 | 143 | 159 | 160
 | 141 | 80 | 149 | 123 | 108 | 139 | 173 | 126 | 145 | 149 | 173 | 162 | 169 | 170 | 171 | 181 | 161 | 169 | 177 | 188 | 190 | 200 | 206
 | 112 | 140
Battery pack energy density (Wh/kg)
LFP
NCX
SiB

## Slide 29
The energy storage opportunity
Mobility energy storage
  Technology landscape
  Opportunities and unlocks
  Case study
Utility energy storage

## Slide 30
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Key messages Mobility energy storage: Opportunities and unlocks (1/2)
Batteries are critical components of the EV ecosystem. The full value chain includes battery production (from raw material extraction to battery recycling), charging systems and infrastructure, and related services such as vehicle-to-grid (V2G) systems.
Battery:
The battery (Li-ion) value chain could become a >$400 billion market by 2030, with cell manufacturing and active materials being the largest segments. China dominates with around a 70% share of global production capacity, followed by Korea, which has an approximate 20% share.
The battery market will likely be oversupplied through 2030. Government incentives are playing an essential role:
    In the United States, the IRA has boosted investments, with over $140 billion in incentives. In the first year after the IRA was signed into law, planned gigafactory capacity increased by 67%.
    China’s battery industry has benefited from approximately $29 billion in government incentives since 2009 and strategic international raw material acquisitions. China now controls more than 80% of global refining capacity.
  Technological advancement will continue to drive cost declines:
    EV battery cost has dropped by 40%-50% since 2010 and is expected to drop by as much as 90% by 2030.
    The cost of materials will continue to drive overall battery costs. As such, LFP is anticipated to remain the cheapest chemistry in 2030 (<$50/kWh) because of its low material cost.

## Slide 31
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Key messages Mobility energy storage:
Opportunities and unlocks (2/2)
Battery (continued):
Critical minerals used in battery production may be in short supply in the next five to 10 years without additional development. Recycling of these minerals could help fill the gap, but profitability remains a challenge:
  Challenges in scaling up the recycling business include limited supply and competition with mining/refining players.
  The market today is highly fragmented, and the players that can build a closed-loop ecosystem from supplier to customer are the ones that will survive.
  Policies around mandating OEM end-of-life collection and recycling are critical to boosting the recycling business and ensuring long-term availability of raw materials.
EV charging:
Extensive investments are required. LDV chargers will need to grow by 5x and HDV chargers will need to grow by 6x through 2030.
Incorporating smart energy services will likely help distinguish business models in the charging ecosystem, followed by the hardware and charging services.
Norway and China are instructive as examples of how to boost charging infrastructure through incentive programs:
  Norway: Public funding of charging infrastructure in rural and remote areas where independent business cases do not provide required returns, with grants to residential owners and developers covering up to 75% of charging port costs.
  China: Large-scale public funding of charging infrastructure together with strict mandates for developers and building owners to provide EV charging infrastructure.

## Slide 32: Batteries form an important part of the overall EV ecosystem
Battery
Raw material mining
Raw material processing and refining
EV
EV production
Charging
  Power generation
  Charging equipment manufacturing
Related services
Cathode and anode material manufacturing
Cell fabrication
Battery packing
EV sales
  Charging operations
  Vehicle-to-grid (V2G)
Battery recycling
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
EV value chain (non-exhaustive)
Focus of this section
V2G is discussed in the utility section

## Slide 33: Li-ion battery value chain expected to >$400 billion market by 2030, mostly due to growth in cell manufacturing and active materials
Observations
As demand for Li-ion batteries surges across industries, revenues for components across the value chain are projected to increase fivefold, from ~$85 billion in 2022 to >$400 billion in 2030.
Cell manufacturing and active materials will likely be two of the largest markets.
  When it comes to sourcing battery materials, mining is one option while recycling is another.
  Battery recycling is expected to be relatively limited in 2030, but it is projected to grow more than threefold in the following decade, as more batteries reach end of life.
While China is the biggest player today, the EU and U.S. are expected to increase their share over time given plans for new mining, refining, and cell production projects in those regions.
Revenues in 2030, USD$B
Chart: 
 | 13 | 39
 | 13 | 61
 | 13 | 118
 | 46 | 185
2022
2030
~85
>400
China
Total
Europe
U.S.
Mining
Extraction of raw ore/ material required for battery
15
34 (9%)
10
6
3
Refining
Processing and refining of raw material into precursors for battery
22
52 (13%)
15
9
5
Active materials
Manufacture of cathode and anode materials, electrolytes, separators, and casings
54
110 (27%)
31
14
11
Battery
cells
Fabrication of battery cells
53
121 (30%)
37
20
11
Battery
pack
Integrate cells into pack, including electronics, sensors, and battery management system
34
74 (18%)
22
11
7
Reuse and recycle
Recovery of critical materials, cathodes, and anodes and/or reuse of used batteries in storage applications
6
13 (3%)
3
2
2
Rest of world
Source: McKinsey Battery Insights (2022).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Battery

## Slide 34: Many stages of EV battery supply chain dominated by a limited number of countries and companies
Chart: 
 | 35 | 28
Li
Ni
Share of total production of top three companies across supply chain,* 2021
Chart: 
 | 27 | 42
Cathode
Anode
Chart: 
 | 65
Cells
Geographical distribution of the global EV battery supply chain,** 2022
Chart: 
 | 13 | 5 | 2 | 80
 | 2 | 5 | 70 | 2.5
 | 55 | 35 | 3 | 2.5
 | 30 | 15 | 5 | 15
 | 40 | 20
Li
Ni
Co
Gr
Other
Russia
Indonesia
Australia
DRC
Korea
Japan
United States
Europe
China
Chart: 
 | 60 | 32 | 65 | 70
 | 2 | 10 | 15 | 5
 | 3 | 15 | 20 | 25
 | 35 | 13
 | 30
Li
Ni
Co
Gr
Chart: 
 | 70 | 80
 | 14 | 14
 | 14 | 5
 | 2 | 1
Cathode
Anode
Chart: 
 | 78
 | 7
 | 6
 | 3
 | 5
 | 1
Cells
Mining
Refining
Active materials
Cell production
Sources: IEA, Global Supply Chains of EV Batteries (2022); U.S. Geological Survey (2022); Benchmark Mineral Intelligence; BloombergNEF; S&P Global.
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
**Geographical breakdown refers to the location of the production. Mining is based on production data. Material processing is based on refining production capacity data. Active material production is based on cathode and anode material production capacity data. Battery cell production is based on battery cell production capacity data.
* Mining by production capacity; cathode and anode by production capacity; cell production by MWh produced
Mining
Cell production
Active materials
Observations
Across all stages of the EV battery supply chain, production is concentrated among only a few companies due to their economies of scale.
The same is true for countries, with China in particular dominating production at every stage of the EV battery supply chain downstream of mining.
Battery

## Slide 35: Battery production located close to demand centers, with 81% in China
Source: IEA, Global EV Outlook (2024).
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Global trade flows for lithium-ion batteries and EVs in 2023
Installed regional Li-ion battery cell manufacturing capacity by location in 2023, GWh
Chart: 
 | 8 | 23 | 66 | 53 | 32 | 3
 | 9 | 123 | 39 | 10 | 4
 | 14 | 20 | 42 | 11
 | 182
 | 85.306
1570
14
China
Europe
United States
Korea
Japan
3
Others
1783
166
147
42
18
Chinese headquarters
Korean headquarters
Japanese headquarters
U.S. headquarters
European headquarters
Other headquarters
80%
8%
7%
2%
2%
1%
72%
19%
4%
3%
1%
1%
Location, share by country
Capacity ownership, share by country
China
China
China
Europe
Europe
Europe
North America
North America
North America
Japan
Japan
Japan
Rest of world
Rest of world
Rest of world
South Korea
Battery
Production
Registration
Battery

## Slide 36: With significant recent investments in batteries, top 10 companies currently dominate 94% of the market
Sources: IEA, Global EV Outlook (2023); IEA, Electric Vehicles; LG Energy Solution, Beyond Carbon Neutrality; Battery Inside, Battery-Powered Future (2022); SNE research, SNE Research, January Global Monthly EV and Battery Monthly Tracker (2024); Energy Post, China's CATL.
Credit: Devashri Mehrotra, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Split of major battery makers globally in 2023, %
Recent news from the major players:
CATL vs. BYD
China’s Contemporary Amperex Technology Co., Limited (CATL), the world’s leading EV battery manufacturer, has announced plans to reduce battery costs by up to 50% this year, engaging in a price war with FinDreams, a subsidiary of Build Your Dreams (BYD), China’s second-largest EV battery producer.
LG EnSol
LG Energy Solution (LG EnSol) is expected to expand its market share in the United States through its collaboration on Ultium Cells, a joint venture with General Motors, alongside other CapEx investments in the United States.
LG Chem will invest KRW 6 trillion in expanding battery material production capacity by 2025 to meet the rising demand for batteries. Additionally, it aims to establish anode material factories in Gumi, Korea, by 2026, with a target production capacity of 260,000 tons.
Chart: 
 | 37 | 37 | 53 | 67 | 73 | 78 | 83 | 88 | 100
 | 16 | 14 | 6 | 5 | 5 | 5 | 12
CATL
BYD
LG EnSol
Panasonic
SK On
CALB
Samsung SDI
Others
Total
Battery

## Slide 37: Battery oversupply challenge through 2030; additional investments needed to reach NZE by 2050
Source: IEA, Global EV Outlook (2024).
Credit: Devashri Mehrotra, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Energy storage demand vs. planned capacity, TWh
Observations
In China, the total planned battery manufacturing capacity by 2030 is more than double the domestic demand under the Announced Pledges Scenario (APS), allowing the export of both batteries and battery-equipped EVs manufactured in the country.
In the U.S. and EU, current and committed battery manufacturing capacity is nearly enough to meet the projected demand under the APS by 2030.
Companies operating in the U.S. and EU will need to rapidly scale up production and prove cost competitiveness to fully or largely satisfy their domestic demand.
Over 40% of China’s planned manufacturing capacity is based on the expansion of existing facilities.
In the U.S. and EU, meanwhile, 80% of planned manufacturing capacity will come from new plants, with new companies expected to enter these markets in the coming years.
~14 TWh gap to 2050 NZE target
Chart: 
 | 770 | 5400 | 22800
 | 2500 | 9000
2.5
2023
9.0
2030
2050
0.8
5.4
22.8
IEA projection
Manufacturing capacity
Extrapolated from IEA electricity demand growth projection for road transport
70% committed capacity (~6 GW), including plants that are already in operation with 85% plant utilization
Battery

## Slide 38: Inflation Reduction Act boosts U.S. gigafactory investments, with a nearly 70% increase in the first year alone
Focus areas | Policy details
Battery and EV manufacturing | Qualifying Advanced Energy Project Credit of up to 30% on battery projects’ capital costs, capped at $10 billion Advanced Manufacturing Production Credit (45X credit): 10% of production costs for battery mineral manufacturing $35/kWh for domestically produced battery cells, $10/kWh for domestically produced battery modules
EV sales | New Clean Vehicle Credit (30D credit): $7,500 for EVs that meet certain requirements with regards to the share of critical minerals that are mined, processed, or recycled within the U.S. or by a country with a free-trade agreement and share of components that are manufactured or assembled in the U.S.
Charging infrastructure | Alternative Fuel Infrastructure Tax Credit (30C credit): Residential charging: Credit for up to 30% of the item's cost, capped at $1,000 Fleet charging: Credit for 6% to 30% of the property cost, capped at $100,000
Battery recycling | No specific incentives for battery recycling; however, recycled battery materials are eligible for the Clean Vehicle Credit
Observations
The CapEx cost of building gigafactories in the U.S. is about 30% higher than in China, a gap the IRA has strategically addressed.
Automakers and battery producers could get more than $140 billion in benefits from battery production tax credits over the next decade, with Tesla and Panasonic likely to be the main beneficiaries.
However, the U.S. still lacks battery recycling mandates, which are critical to ensure that raw material supply is sufficient long term.
The U.S. also has various grants under the Department of Energy to support R&D in battery technology and EV infrastructure.
IRA provides subsidies on both the supply and demand side to support a supply chain expansion…
…resulting in a 67% increase in gigafactory investment since 2022
Sources: IEA, Global EV Outlook – Policy Development (2023); IEA, Global EV Policy Explorer (2024); CGEP, The IRA and the US Battery Supply Chain (2023); DOE, Tax credits; Grist, The US doesn’t have a law mandating EV battery recycling. Should it? (2023)
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
| 18993 | 19024 | 19052 | 19083 | 19113 | 19144 | 19174 | 19205 | 19236 | 19266 | 19297 | 19327 | 19358 | 19389 | 19417 | 19448 | 19478 | 19509 | 19539
 | 19.5031 | 19.5031 | 19.5031 | 19.5031 | 19.5031 | 19.5031 | 19.5031 | 63.5031 | 213.5031 | 213.5031 | 243.5031 | 293.5031 | 293.5031 | 333.5031 | 413.5031 | 433.831 | 453.5031 | 473.831 | 493.5031
Jul-22
Jan-23
Jul-23
0
1000
950
1050
900
1100
850
1150
800
1200
750
Jan-22
+67%
U.S. gigafactory investment pipeline, GWh
U.S. passed the IRA in August 2022
Battery

## Slide 39: Battery subsidies in the U.S. exceed EU’s, but EU gigafactory capacity expected to grow due to market regionalization
Sources: Menon Economics, Battery subsidies in EU, Norway, and U.S. (2023); IEA, Global EV Outlook (2024).
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Actual and estimated state aid for battery production facilities, % of total investment in production facilities
Chart: 
 | 26 | 30 | 210
IPCEI
TCTF
IRA
26%
30%-35%
210%
EU
U.S.
Important Project of Common European Interest: Investment subsidy for mass production involving significant innovation; run and funded by participating countries in the EU
Temporary Crisis and Transition Framework: Aid for green tech production facilities capped at a certain percentage of investment costs
Observations
U.S. producers have access to considerably larger subsidies than European manufacturers, leading to an estimated 1,000 GWh capacity expected by 2030 (from 70 GWh in 2023). Partners that committed to investments include:
  Tesla, Our Next Energy, Ultium Cells (General Motors and LG Energy Solutions JV), SK On, and StarPlus Energy (Stellantis and Samsung JV)
Although more public support is available in the U.S., battery production in the EU will continue to grow, with 1,375 GWh capacity expected by 2030 (from 110 GWh in 2023), driven by:
  Regionalization of battery and car markets, to avoid supply chain disruption.
  The EU’s plan to phase out new ICE sales by 2035, which will boost battery demand.
  Potential for significant bottlenecks in U.S. production, including labor shortages, limited access to materials, and lengthy permitting processes.
Battery

## Slide 40: China has spent the past 15 years focusing on EVs, enabling rapid growth and allowing EVs to capture ~40% of the car market
EV sales as a percent of all automobile sales in China, %
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
 | 0.0001 | 0.00034 | 0.00073 | 0.00095 | 0.004 | 0.01 | 0.015 | 0.024 | 0.047 | 0.05 | 0.057 | 0.16 | 0.29 | 0.38
0
5
10
15
20
25
30
35
40
38%
2009-2010:
EV financial subsidies are piloted in cities
2016:
Major expansion of fast chargers for EVs begins
2018:
Price equivalency with ICE reached and zero emission vehicle credit policy launched, which replaced subsidies
2020:
National EV subsidy phaseout postponed due to COVID-19
2021:
EV sales surge, reflecting the culmination of over a decade of supportive EV policies
2022:
China’s BYD Co., the world’s second-largest EV manufacturer, sells 1.85 million EVs
Sources: IEA, Global EV Outlook - Policy Explorer (2024); WRI, Countries Adopting EVs (2023); MIT Technology Review, How did China come to dominate the world of electric cars? (2023); Berkeley Law, China Dual Credit Policy Brief (2022); IFC, Assessment of PLI scheme on EV manufacturing in India (2024).
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
2023:
After slow EV sales growth, a tax break package set to be in place from 2024 to 2027 aims to boost EV purchases
Observations
Through a 15-year concerted policy effort, China has been able to rapidly dominate the EV market.
China's supply-side policies include:
  $29 billion in subsidies for EV and battery manufacturing
China's demand-side policies include:
  Financial and tax breaks for EV consumers since 2009
  The zero-emission vehicle credit system, which has provided credits for manufacturers since 2018
Other factors:
  760,000+ fast public chargers and 1 million slow public chargers installed
  2,000+ battery-swapping stations installed
  Control of over 80% of global raw material refining capacity
Battery

## Slide 41: Technology advancements continue to drive cost declines, with material costs remaining the most important factor
77%
47%
77%
Chart: 
 | 37.7772 | 33.9937 | 29.2926 | 28.0569 | 26.8939 | 25.1308 | 12.3349 | 8.9034 | 7.3977 | 5.8144 | 5.572 | 4.4176 | 3.8838 | 3.5349 | 3.0959 | 2.8434 | 2.5875 | 2.4245 | 2.2307 | 2.0473 | 2.044
 | 9.1985 | 8.2773 | 7.1326 | 6.8317 | 6.5485 | 6.1762 | 3.1095 | 2.271 | 1.8863 | 1.48 | 1.4183 | 1.1259 | 0.98751 | 0.90251 | 0.78857 | 0.72445 | 0.65862 | 0.61665 | 0.5666 | 0.51949 | 0.5191
 | 91.9853 | 82.7727 | 71.3257 | 68.3168 | 65.4851 | 61.7621 | 31.095 | 22.7102 | 18.863 | 14.7997 | 14.1826 | 11.2588 | 9.8751 | 9.0251 | 7.8857 | 7.2445 | 6.5862 | 6.1665 | 5.666 | 5.1949 | 5.191
 | 6.751 | 6.075 | 5.235 | 5.014 | 4.806 | 3.864 | 1.038 | 0.457 | 0.387 | 0.333 | 0.319 | 0.237 | 0.234 | 0.172 | 0.171 | 0.155 | 0.148 | 0.144 | 0.141 | 0.135 | 0.13
 | 17.535 | 15.757 | 13.546 | 12.969 | 12.43 | 11.213 | 5.341 | 3.702 | 3.021 | 2.275 | 2.18 | 1.625 | 1.363 | 1.201 | 1.028 | 0.923 | 0.831 | 0.802 | 0.732 | 0.679 | 0.702
 | 56.268 | 50.59 | 43.529 | 41.683 | 39.953 | 32.047 | 11.445 | 6.695 | 5.493 | 4.271 | 4.093 | 2.935 | 2.711 | 2.264 | 2.014 | 1.792 | 1.666 | 1.499 | 1.451 | 1.268 | 1.266
 | 45.872 | 32.939 | 28.819 | 25.606 | 23.175 | 19.886 | 17.093 | 14.958 | 13.311 | 10.643 | 8.814 | 8.831 | 9.378 | 7.674 | 6.158 | 5.017 | 3.675 | 2.803 | 1.986 | 1.182 | 0.454
 | 152.908 | 115.576 | 106.735 | 100.417 | 96.562 | 88.38 | 81.397 | 76.708 | 73.948 | 64.504 | 58.758 | 64.934 | 76.87 | 71.051 | 65.507 | 62.708 | 55.678 | 53.908 | 52.262 | 49.24 | 45.356
418
346
306
289
276
248
163
136
124
104
95
95
105
96
87
81
72
68
65
60
56
-87%
Chart: 
 | 52.7381 | 47.4877 | 41.0689 | 32.818 | 31.5178 | 25.3201 | 16.7907 | 12.3389 | 10.5817 | 8.9941 | 8.0997 | 6.823 | 5.7061 | 5.1921 | 4.4564 | 4.1717 | 3.7325 | 3.4569 | 3.2272 | 3.1186 | 2.9746
 | 13.0795 | 11.7798 | 10.1871 | 8.0653 | 7.7457 | 6.2221 | 4.2643 | 3.161 | 2.7109 | 2.3036 | 2.0726 | 1.7485 | 1.4587 | 1.3308 | 1.1399 | 1.0674 | 0.95392 | 0.88281 | 0.82341 | 0.79575 | 0.7588
 | 130.7948 | 117.7984 | 101.8708 | 80.6533 | 77.4571 | 62.2211 | 42.643 | 31.6101 | 27.1095 | 23.0359 | 20.7264 | 17.4847 | 14.5866 | 13.3079 | 11.3986 | 10.6739 | 9.5392 | 8.8281 | 8.2341 | 7.9575 | 7.588
 | 6.806 | 6.101 | 5.282 | 5.047 | 4.848 | 3.9 | 1.066 | 0.483 | 0.413 | 0.358 | 0.343 | 0.261 | 0.258 | 0.196 | 0.194 | 0.178 | 0.171 | 0.166 | 0.163 | 0.157 | 0.152
 | 25.774 | 23.062 | 19.907 | 14.625 | 14.044 | 11.238 | 7.035 | 5.256 | 4.354 | 3.68 | 3.236 | 2.596 | 2.099 | 1.881 | 1.559 | 1.459 | 1.264 | 1.182 | 1.098 | 1.089 | 1.036
 | 63.943 | 57.26 | 49.467 | 41.82 | 40.16 | 32.181 | 13.758 | 8.487 | 7.348 | 6.108 | 5.574 | 4.328 | 3.7 | 3.138 | 2.757 | 2.529 | 2.26 | 2.067 | 2.001 | 1.864 | 1.754
 | 52.502 | 33.716 | 30.467 | 27.553 | 24.501 | 21.676 | 18.15 | 14.921 | 12.77 | 10.538 | 8.763 | 7.84 | 7.668 | 6.026 | 4.736 | 3.707 | 2.66 | 1.972 | 1.357 | 0.775 | 0.283
 | 173.507 | 116.803 | 111.341 | 106.55 | 100.589 | 94.838 | 84.928 | 75.018 | 69.444 | 62.368 | 56.922 | 56.143 | 61.356 | 54.295 | 48.886 | 44.836 | 38.797 | 36.415 | 34.203 | 30.803 | 26.795
519
414
370
317
301
258
189
151
135
117
106
97
97
85
75
69
59
55
51
47
41
-92%
Material
Scrap
Energy
Labor
Building and land
Machinery
Maintenance
Overhead
Annual cost breakdowns for Li-ion battery cell chemistries, $/kWh
NMC811
LFP
Observations
By 2030, cell costs are anticipated to drop by more than 85% compared with 2010, not including material costs.
  This shift will likely be driven by technological advancements in manufacturing, increased production volume, and improvements in cell performance.
As a result of this shift, material costs will become a growing portion of overall cell costs (both due to a decrease in total costs and an increase in material costs).
  LFP is expected to continue to be the cheapest battery chemistry (~$41/KWh) through 2030. While the technology has relatively high machinery costs, it has the lowest material costs (~$27/KWh).
1) CPI assumes index 1982-1984 to be 100; Note: NMC811 and NCA-GR are two.
Sources: Journal of Energy Storage, Lithium-ion battery cost (2024); Federal Reserve Bank of St. Louis, Consumer Price Index.
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
XX%
Average material cost contribution
Chart: 
 | 38.0447 | 34.1005 | 29.4536 | 28.1179 | 26.9709 | 25.2371 | 12.4184 | 8.9958 | 7.8346 | 6.5419 | 5.6297 | 4.8848 | 4.1446 | 3.783 | 3.2598 | 3.0551 | 2.711 | 2.5811 | 2.4418 | 2.2293 | 2.1649
 | 9.2637 | 8.3033 | 7.1717 | 6.8465 | 6.5672 | 6.2021 | 3.1302 | 2.2941 | 1.9988 | 1.668 | 1.4325 | 1.2463 | 1.0543 | 0.96605 | 0.83033 | 0.77863 | 0.68989 | 0.6565 | 0.62061 | 0.56595 | 0.54966
 | 92.6366 | 83.0328 | 71.7173 | 68.4654 | 65.6724 | 62.021 | 31.3018 | 22.9411 | 19.9878 | 16.68 | 14.3245 | 12.4634 | 10.5433 | 9.6605 | 8.3033 | 7.7863 | 6.8989 | 6.565 | 6.2061 | 5.6595 | 5.4966
 | 6.799 | 6.094 | 5.264 | 5.025 | 4.82 | 3.883 | 1.049 | 0.467 | 0.398 | 0.343 | 0.328 | 0.247 | 0.244 | 0.182 | 0.18 | 0.164 | 0.157 | 0.153 | 0.15 | 0.144 | 0.139
 | 17.627 | 15.774 | 13.591 | 12.969 | 12.439 | 11.236 | 5.343 | 3.704 | 3.088 | 2.551 | 2.181 | 1.798 | 1.397 | 1.253 | 1.048 | 0.966 | 0.855 | 0.817 | 0.767 | 0.712 | 0.714
 | 56.604 | 50.685 | 43.709 | 41.715 | 40.011 | 32.141 | 11.463 | 6.716 | 5.886 | 4.888 | 4.108 | 3.334 | 2.918 | 2.396 | 2.144 | 1.902 | 1.769 | 1.598 | 1.547 | 1.357 | 1.351
 | 49.571 | 35.945 | 31.345 | 27.781 | 25.086 | 21.462 | 18.375 | 16.265 | 14.537 | 11.405 | 9.392 | 9.489 | 10.058 | 8.278 | 6.693 | 5.496 | 4.04 | 3.091 | 2.196 | 1.313 | 0.508
 | 165.237 | 126.122 | 116.092 | 108.947 | 104.525 | 95.387 | 87.499 | 83.409 | 80.763 | 69.12 | 62.616 | 69.769 | 82.443 | 76.651 | 71.204 | 68.706 | 61.217 | 59.435 | 57.786 | 54.717 | 50.763
2015
2020
21F
2025F
2030F
258
436
360
318
300
286
2010
171
145
134
113
100
103
113
103
94
89
78
75
72
67
62
-86%
NCA-GR
  Adjusted based on 2020 CPI (258.84)1
41%
64%
45%
Battery

## Slide 42: Material costs projected to grow; savings in other areas expected to contribute to an overall decline in battery costs
Source: Journal of Energy Storage, Lithium-ion battery cost (2024).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Factors influencing cost declines of Li-ion batteries and their contributions, %
Observations
From 2010 to 2020, efforts to thin separator, anode, and cathode foils led to cathode active material (CAM) savings, becoming the largest source of cost declines (16.4%), followed by specific energy enhancement (15.3%).
But in the future, scrap rate improvement is expected to lead the downward cost trajectory from 2021 to 2030 (~14% cost reductions in both scenarios).
  Technological enhancement will outweigh the anticipated cost increase from price increase in some of the critical materials, such as graphite, nickel, and cobalt, resulting in a continued decline in cell cost.
Historical (2010-2020)
Chart: 
 | 16.4378 | 15.3589 | 11.4098 | 10.708 | 8.37 | 6.0051 | 5.9893 | 5.7049 | 5.0686 | 3.4517 | 2.7584 | 2.5897 | 2.291 | 1.293 | 0.90112 | 0.76689 | 0.59893 | 0.43774 | 0.26394 | 0.031148 | -0.035485
Cathode active material cost saving
Specific energy enhancement
Electrode manufacturing developments
Energy utilization rate
Scrap rate enhancements
Cell finishing developments
Machinery utilization rate
Cell assembly developments
Separator material saving
Labour utilization rate
Overhead utilization rate
Graphite price
Anode foil material saving
Building and land utilization rate
Electrolyte price
Nickel price
Maintenance utilization rate
Cathode foil material saving
Cobalt price
Maganese price
Lithium price
Chart: 
 | 12.5242 | 8.0411 | 11.4669 | 5.1836 | 13.5978 | 5.9162 | 5.7733 | 5.9024 | 4.9573 | 2.8499 | 2.3275 | -4.7569 | 6.5352 | 0.29938 | 0 | -4.0766 | 0.57733 | 0.62459 | -4.0358 | -0.053041 | -0.61018
Chart: 
 | 11.6221 | 8.9883 | 9.9678 | 4.7324 | 13.8883 | 5.5569 | 5.3455 | 5.1357 | 4.3246 | 2.5048 | 2.1637 | -4.8508 | 5.7013 | 0.30201 | 0 | -6.6375 | 0.53455 | 0.54477 | -6.49 | -0.085858 | -0.67765
Leading sources of cost reductions in each period
Projected (2020-2030)
LFP scenario
Projected (2020-2030)
NCX scenario
Battery

## Slide 43: Battery lifetime can be extended by limiting full charging and deep discharging, unlocking second-life repurposing of EV batteries
Source: Jeff Dahn, Dalhousie University
Credit: Xiaodan Zhu, Jeff Dahn, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Observations
Battery life can be extended by:
  Charging to 80% or less. Limiting charge voltage to 4.06V (a charge of around 80%) allows batteries to retain 90% or more of their original capacity, even after 10 years of use or around 3,000 cycles (the equivalent of 500,000 km of typical EV use), as shown in the NMC811/graphite cell data (left).
  Taking EVs out for short but frequent drives. Smaller depth of discharge cycles (e.g., 25% or 50% DOD) significantly extend battery lifespan. Testing shows that at 50% DOD, batteries can last up to 7,430 cycles, and at 25% DOD, they can last even longer, up to 16,680 cycles. This suggests that frequent short drives followed by charging are better for battery longevity compared to infrequent, deep discharges.
  Careful usage practices may allow battery lives to be extended by as long as 80 or 100 years past the life of the EV, significantly reducing recycling need, as second-life repurposing in areas like grid integration would be unlocked.
100% Depth of discharge
75% Depth of discharge
50% Depth of discharge
25% Depth of discharge
500,000 km
Charge level impact on capacity
Depth of discharge impact on capacity
100% Charge level
80% Charge level
Battery

## Slide 44: Longer battery lifetime outlives EVs, creates opportunity for second use, driving down battery lifetime costs
Chevrolet Bolt
Hyundai Genesis GV60
Tesla Model 3 LFP (CATL)
Tesla Model 3 NCA 21-70 (Panasonic)
Observations
Results from Renewable Energy Storage Lab at Dalhousie University (Lukas Swan)
Four different used EV battery packs, each at varying states of health, have been successfully connected to the grid.
It is feasible to connect and use "random" used EV batteries in grid storage applications.
Practical considerations include testing battery capacity to ensure reliability:
  Aim for batteries with at least 70% remaining capacity.
  Group batteries with similar health states for optimal performance and management.
Additional considerations before wide-scale implementation include development of a purpose-built BMS and reliably addressing fire hazard concerns stemming from repurposing and merging various EV cells into one system.
Source: Jeff Dahn, Dalhousie University
Credit: Xiaodan Zhu, Jeff Dahn, Petr Jenicek, Birru Lucha, Hyae Ryung Kim & Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Proof of concept: BESS created from second-life EV batteries
Four different used EV battery cell packs linked with a custom battery management system (BMS) connected to the grid as a BESS:
Conceptual proof that used cell packs from different EVs and manufacturers can be linked to create an energy storage system that can be connected to a building/the grid.
Battery

## Slide 45: Although EV battery supply currently sufficient, critical mineral shortages expected to develop in the coming years
Lithium
Nickel sulphate
Cobalt
Chart: 
 | 10 | 330 | 450 | 420 | 410
 | 200 | 20 | 50 | 40 | 30
 | 200 | 330 | 750 | 1100 | 1350
 | 200 | 280 | 550 | 905 | 1300
 | 200 | 280 | 475 | 750 | 1000
Kt Li
2023
2025
2030
2035
2040
Short-term supply is expected to fulfill the demand, but more projects are needed to meet the rapid growth driven by EV expansion.
In the NZE Scenario, demand is expected to reach 1,700 kt by 2050, a tenfold increase from today’s levels.
Lithium is prone to significant supply risks due to price volatility and low deployment of secondary supply and reuse.
Only 3% of lithium is sourced from secondary supply today.
Chart: 
 | 0.6 | 0.7 | 0.9 | 0.9 | 0.9
 | 0.05 | 0.1 | 0.1 | 0.1
 | 0.1 | 0.2 | 0.4
 | 0.5 | 1.2 | 2.9 | 3.5 | 3.6
 | 0.5 | 0.9 | 2 | 2.9 | 3.3
 | 0
0.0
0.5
1.0
1.5
2.0
2.5
3.0
3.5
4.0
Mt Ni
2023
2025
2030
2035
2040
Base case
High production case
Secondary
Supply and demand balances for critical minerals based on existing and announced projects
Battery-grade nickel, or nickel sulphate, may face supply gaps to meet NZE targets, even help from secondary supply.
New EV designs will likely lead to additional development. The timeline from EV design to production spans around four years, on average, and nickel sulphate capacity scaling takes 18 to 24 months.
One emerging risk worth monitoring is recent low nickel prices, which could lead to further mine closures or the suspension of ongoing projects.
Chart: 
 | 240 | 270 | 320 | 270 | 220
 | 40 | 35 | 40
 | 200 | 250 | 350 | 340 | 310
 | 200 | 210 | 300 | 310 | 320
 | 200 | 210 | 290 | 290 | 280
Kt Co
2023
2025
2030
2035
2040
Even with demand growth slowing due to a preference for low-cobalt batteries, in the longer term, cobalt supply may fall short of meeting primary supply needs.
Global mined supply may begin to decline starting in 2030 as reserves in the DRC deplete, which strong growth in Indonesia may partly offset.
Future cobalt supply could be threatened as mining projects are delayed with weak cobalt prices persisting.
Expected supply*
Primary supply requirements
*Base case includes production from existing assets and those under construction, along with projects that have a high chance of moving ahead, having secured all necessary permits and financing and/or established offtake contracts; high production case additionally considers projects at a reasonably advanced stage of development, seeking financing and/or permits.
Sources: IEA, Global Critical Minerals Outlook (2024); Nikkei Asia, Nickel shortage (2024).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
NZE
APS
STEPS
Beginning of shortage under NZE Scenario
Non-exhaustive
Battery (recycling)

## Slide 46: Critical mineral for batteries widely distributed across continents, with China and Australia having a competitive advantage
Observations
Major reserves of lithium, cobalt, nickel, and manganese, which are crucial for the global supply, are found in the U.S., China, Australia, Congo (Kinshasa), and Chile..
Vital for energy storage and EV markets, these reserves position the above countries as key players in the renewable energy transition.
China leads in LFP battery production with all three essential elements — lithium, phosphate, and iron — available in large quantities. This integration significantly enhances its production capabilities and dominance in the market.
For NCM, Indonesia, South Africa, and Congo significantly influence the NCX battery market due to their substantial shares in nickel, cobalt, and manganese production. Their resource availability is crucial and may impact global market prices.
Additional sources of critical minerals are being investigated (e.g. lithium extraction from oil and gas brine, offshore cobalt, and nickel and manganese mining in the U.S., Australia, and Canada), as expected price increases enable higher cost extraction business cases.
Nevertheless, battery recycling is likely to play a major role in procurement of critical minerals.
Global reserves distribution of battery’s critical minerals
Sources: USGS, Mineral commodity summaries (2024); Statista, Reserves of lithium (2023).
Credit: Xiaodan Zhu, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Note: The length of the bar in each chart indicates the relative fraction of the total reserve of the respective minerals.
Battery (recycling)

## Slide 47: Achieving profitability in battery recycling challenging due to feedstock shortage and cost advantage of mining
Collection, logistics, and sorting
Discharge and dismantle
Pretreatment
Battery materials recovery
Sources: BCG, Striking Gold with EV Battery Recycling (2023); McKinsey, Battery recycling (2023); Catalyst podcast, World of battery recycling (2024).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Observations
The key EV battery recycling challenge is feedstock shortages:
  Due to extended battery life, recyclers supplement their supply with waste material from battery cell manufacturing. However, scrap rates are expected to fall as battery manufacturers improve production efficiency.
  Having battery manufacturers as both key suppliers and primary customers, recycling companies are facing massive margin pressure from both sides of the market.
Lack of scale makes it difficult for recyclers to compete with incumbent raw material producers, given that the core recycling technologies are not fundamentally different from primary material processing.
While battery recycling is essential for creating a circular supply chain, making a profitable business case is challenging.
Traditional recycling players are advised to compete for the overall materials recovery profit pool, not just the front-end
  Building a cross-value-chain ecosystem through partnerships can be an option
  Investing in technologies that bring better material recovery rates, product quality, and process efficiency is essential to be chosen by OEMs
Potential value pool across the value chain
Collection point
Transport and charging
Sorting and warehousing
Discharging and dismantling
Material sorting
Pack disassembly
Shredding and sorting
Pyro and hydrometallurgy
Hydrometallurgy
Refining
Chart: 
 | 60 | 30 | 10
60
30
10
Collection point
Transport & discharging
Others
Chart: 
 | 50 | 50
30
30
Discharging &
dismantling
Material sorting
Chart: 
 | 5.5556 | 94.4444
10
170
Pack disassembly
Shredding & sorting
Chart: 
 | 8 | 92
40
460
Pyro & hydrometallurgy
Hydrometallurgy
100
60
180
500
Activities with low entry barriers, such as shredding, already face overcapacity in part due to a lack of scrap for recycling, resulting in lower margin.
Highest upside potential if given large enough scale and additional value such as new CAM technologies.
Steepest entry barriers are due to CapEx and the expert knowledge required.
Business models
EBITDA estimate by 2030 in Europe ($M)
Profit potential
Smaller margin potential but has lower commodity price risk and requires fewer skills.
Battery (recycling)

## Slide 48: Players with a closed-loop ecosystem from supplier to customer will survive among currently fragmented business archetypes
Business models across EV battery value chain
Collection, logistics, and sorting
Discharge and dismantle
Pretreatment
Battery materials recovery
Value chain coverage
Description
Success factors
Sources: BCG, Striking Gold with EV Battery Recycling (2023); McKinsey, Battery recycling (2023).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Collection only (independent or OEM-related)
High-coverage infrastructure network
Market/factory proximity
Favorable regulations
Decentralized network
Collection and discharging
Warehouse storage provider
Same as pure logistics provider and HV certification to discharge
Add-on services beyond logistics, e.g., dismantling/sorting
Same as pure shredder and sufficient feedstock (>20k Mt)
Black mass production from delivered battery packs
Cheap energy supply
Reliable supply with black mass
Black mass production from disassembly to shredding
Decentralized network
Shredding feedstock (>10K Mt)
Collection of EoL batteries and processing to black mass
Technological know-how
Established customer network
Full battery recycling from discharging to metal recovery
Sufficient feedstock for scale economies
Metals/salts recovery done by (P)CAM/battery manufacturers
Recovery of metals/salts through hydro and pyro metallurgical process
Sufficient feedstock for scale economies and process know-how
Full recycling from collection, discharging to metal recovery
Technological know-how
Specialized logistics network
Observations
Companies are trying to establish a foothold in niches of the market based on existing capabilities.
Success will be determined by the ability to forge closed-loop ecosystems.
  Companies can’t create competitive advantage with technology alone; supplier and customer relationships are key.
  It is critical for smaller players to integrate capabilities into functioning ecosystems often formed around large OEMs and battery cell manufacturers.
Pure collector
Pure logistics provider
Forward-integrated logistics provider
Black mass (BM) recycler
Pure shredder
Collection-integrated BM recycler
E2E recycler
Recovery-integrated upstream player
Pure metallurgists/ direct recyclers
Collection-integrated E2E recycler
Players
  Some OEMs own battery recycling players to ensure a closed loop while maintaining material ownership and supply chain visibility.
Battery (recycling)

## Slide 49: Policies that enshrine recycling responsibilities to OEMs critical for creating robust supply
Chart: 
 | 917 | 1103 | 1454 | 3400 | 24503
0
5,000
10,000
15,000
20,000
25,000
2017
2018
2019
2020
2021
1,103
1,454
3,400
24,503
Yearly registrations of regulated and unregulated EV recyclers in China
Observations
Under the 2018 policy framework “Provisional Measures on the Recycling and Repurposing of EV Power Storage Batteries,” China has enshrined end-of-life recycling responsibilities to OEM manufacturers.
This has led to a list of 88 white-listed recyclers that meet recycling standards proposed by the policy framework. However, these regulated recyclers have been dwarfed by a rise in noncompliant recyclers.
Policy actions to address this concern include:
  Subsidies for compliant recyclers to increase recycled volumes, combined with cracking down on unregulated recyclers
  A battery leasing model (e.g., NIO) where batteries are leased from OEMs by consumers, incentivizing OEMs to increase the recycling network
  Battery traceability standards to serialize all produced batteries for government third-party agencies to track (e.g.: EU Battery Passport policy announced by the EU in 2023)
Chart: 
 | 20 | 80
% Regulated channels
% Unregulated channels
Sources: Dialogue Earth, China EV battery-recycling (2023); S&P Global, China new used EV power batteries rules (2024).
Credit: Hassan Riaz, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Battery (recycling)

## Slide 50: Extensive charging station investments, including dedicated HDV charging, required to meet growing needs of the ecosystem
Public charging for LDV could increase sixfold by 2035, accelerating EV adoption
Overnight depots will drive HDV charging, supplemented by opportunity charging
1) L1 = slowest option, adding about 3 to 5 miles of range per hour; L2 = faster, adding 20 to 30 miles of range per hour; L3 = fastest option, adding 100+ miles of range in 20 to 30 minutes.
Source: IEA, Global EV Outlook (2024).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Observations
Private home charging (mostly L11) is currently the most common method of charging.
  Early EV adopters have typically resided in homes with easy and cost-effective access to home charging. Meanwhile, public chargers have predominantly been installed in urban locations.
Public charging infrastructure, particularly fast charging (L2/L3), must expand significantly to support broader EV adoption and ensure equitable access.
  To serve EVs required to achieve zero emissions by 2030, 1.2 million public chargers need to be constructed and operated by the same year in the United States.
  By 2035, the share of electricity coming from chargers outside homes is expected to reach almost 45%, compared to less than 35% in 2023.
Dedicated HDV charging facilities are still in the early development and deployment stage.
  Mitigation plans for possible challenges imposed on the electricity grid should be implemented at the same time (e.g., stationary storage batteries colocated with high-powered chargers).
Chart: 
 | 26 | 137 | 142 | 273 | 304
 | 10 | 58 | 59 | 124 | 135
 | 3 | 9 | 10 | 14 | 15
 | 1 | 6 | 6 | 9 | 9
Light-duty vehicle charger stock,
Mn chargers
2023
STEPS
APS
STEPS
APS
40
210
220
420
460
Public (fast)
Public (slow)
Private (other)
Private (home)
2030
2035
Chart: 
 | 0.7 | 2.2 | 2.6 | 4.1 | 5.4
 | 0 | 0 | 0 | 0 | 0
 | 0.3 | 3.3 | 4 | 9.6 | 12.4
 | 0 | 0 | 0 | 0.1 | 0.1
Heavy-duty vehicle charger stock,
Mn chargers
2023
STEPS
APS
STEPS
APS
1
6
7
14
18
2030
2035
Truck (opportunity)
Truck (depot)
Bus (opportunity)
Bus (depot)
Private (other) refers to charging points that are neither publicly accessible nor charging points at private residences.
Opportunity charging is the practice of charging a battery in short intervals throughout the day instead of charging it in full all at once.
Charging

## Slide 51: Business models that encompass smart energy services most likely to enjoy the largest profits
Business models and prospective profit pools in the EV charging value chain
Site provision
Hardware
Planning and
installation
Charging
back end
Operations
Electricity sales
Smart energy
services
Aggregators &
roaming
Mobility service
provider
Charge point operator
(open/closed)
Charging solution provider
End-to-end network operator (open/closed)
Cloud energy provider (downstream focus)
Software (SW)
Hardware (HW)
SES provider
Aggregator
Mobility service
provider
1
2
3
4
5
6
7
Business models
Estimated profit pools
Sources: Bain & Company, EV Charging in High Gear (2022); EV Charging Summit, Top 20 EV Charging Solutions (2023).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Pure models
Hardware and software provider
Observations
The current capital market prefers integrated models:
  Tesla’s primary focus is on L3 and seamlessly integrating with the supercharger network (50,000 superchargers globally) and its apps.
  Other players still mix between L2 and L3, with the main advantage being compatibility for all EVs.
The smart energy services profit pool will grow faster due to a shift from HW to SW.
Extensive operating areas for some companies
Chart: 
| 0.18 | 0.18 | 0.18 | 0.43 | 0.43 | 0.43 | 0.76 | 0.76 | 0.76
 | 0.2 | 0.4 | 0.6 | 0.2 | 0.4 | 0.6 | 0.2 | 0.4 | 0.6
Smart energy services
Charging services
Hardware and services
  Including vehicle-to-grid and vehicle-to-home EV charging
Total profit, €B
(EU market)
2020
0.5-0.7
2030
3.0-5.0
2040
7.5-11.0
Major players
  Multinational oil & gas company bp entering EV charging business as part of its transition to an integrated energy company
Charging

## Slide 52: Effective tax policies and incentives to fuel robust infrastructure development critical for ensuring sustainable EV market growth
Observations
EV-to-charger ratio reflects market maturity:
  A declining ratio in the United States and Norway indicates mature markets where policies and infrastructure align to support widespread EV adoption.
  India and China show higher ratios, with EV sales outpacing infrastructure, reflecting markets in the promotion phase.
Impact of tax and policies:
  Norway leads with effective incentives like VAT exemptions, toll discounts, and free parking, which is driving infrastructure optimization and high EV adoption.
  U.S. policies under the Inflation Reduction Act focus on incentivizing domestic manufacturing and private charging infrastructure, resulting in significant progress by 2030.
  India and China focus on subsidies and production-linked incentives (PLI) to accelerate EV sales but need to prioritize infrastructure growth.
India’s infrastructure challenges:
  India’s high EV-to-charger ratio reflects the need for aggressive investment in charging infrastructure to match its growing EV market.
Policy drivers | 
 | Focuses on domestic EV manufacturing with tax credits (IRA). Incentives for charging infrastructure include bidirectional charging tax credits.
 | Provides tax incentives (e.g., VAT exemptions) and extensive EV charging infrastructure (34,000 by 2023).
 | Aggressively expands EV and battery production with tax breaks and subsidies. Aims for a 40% NEV sales share by 2030.
 | PLI scheme promotes domestic manufacturing. Goals include 15% passenger EVs by 2030 and significant investment in battery capacity.
 | Prioritizes sustainable mobility, battery recycling, and raw material supply. Targets 30 million passenger ZEV stock by 2030.
Sources: Statista, EV chargers (2023); Statista, EVs per charger (2023); Statista, EV charging infrastructure U.S. (2024); Statista, Norway EVs (2024); NREL, National Charging Network (2023); IEA, Global EV Outlook (2023).
Credit: Xiaodan Zhu, Petr Jenicek, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 168000 | 4980887.0116 | 27000 | 500000 | 2700000 | 3894614.5723 | 10900 | 1320000
 | 26 | 1.1786 | 34 | 3.8857 | 8 | 17.1429 | 1.0917 | 37.8788
1M
2M
3M
0M
14M
33M
0
5
10
15
20
25
30
35
40
Total EV chargers
EVs per charger
2022
2030
2022
170K
33M
27K
0.5M
2.7M
14M
10K
1.3M
2030
2022
2030
2022
2030
Total number of chargers
Number of EVs per charger
Chargers and EV-charger ratio across geographies
Charging

## Slide 53
The energy storage opportunity
Mobility energy storage
  Technology landscape
  Opportunities and unlocks
  Case study
Utility energy storage

## Slide 54: Contemporary Amperex Technology Co. Ltd. (CATL) is a global leader in battery production based in China
Technology and market
Financials
Operations
Specialization in lithium iron phosphate (LFP) batteries, which are safer and cost effective, and have longer life cycles
Case study: CATL
165 GWh
Has been global leader for seven straight years, capturing 37% of 2023 market share (total 165 GWh)
30% CAGR
Capitalized on 30% CAGR in global battery EV market since 2013
$2.8B raised
In 2020, nine investors, including UBS AG and JPMorgan, invested $2.8 billion USD in equity financing (private share placement)
6x revenue in 2 years
Large increase in reported revenues from $7 billion to $46 billion from 2020 to 2022
22.6% gross margin reported in FY2023 (compared to industry average of 15.76% in the same period)
22.6% gross margin
13 plants
11 domestic and two European (German and Hungarian) production plants, including active material production, cell manufacturing, and assembly
$1.5B expansion fund
New fund managed by Lochpine Capital dedicated to capacity expansion in Europe
$950 million acquisition of Yajiang Mining Development in 2021 to own 100% exploration rights at Dechenonba Mine
Overview
CATL is the world’s largest EV battery producer, holding around 37% of the global market in 2023. With 2023 production capacity exceeding 165 GWh, future goals are to quadruple production to 600 GWh by 2025.
Sources: CATL; Financial Times, China’s battery giant taps Europe’s elite to expand supply chain (2024); S&P Global, CATL buys Chinese lithium mine (2023).
Credit: Hassan Riaz, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).

## Slide 55: CATL’s trajectory to success began 25 years ago…
 | First foray into batteries for early gen smartphones | Early R&D in e-mobility accelerated with generous policy support | Massive volume expansion as leading battery supplier for NEVs
Timeline |  |  | 
Highlights | 1999 – Amperex Technology Ltd. (ATL) acquires technology licenses from American and Japanese companies to produce batteries 2001 – Sales grow to 1 million+ devices 2005 – Acquired by Japanese firm TDK with specialties in cassette and CDs 2007 – Early research into batteries for e-mobility explored by ATL | 2008 – Beijing begins concerted policy effort to grow and nurture nascent EV industry, evident through the first demonstration of a demo electric bus fleet supplied by ATL batteries 2009 – State issues “Ten Cities, Thousand Vehicles” policy plan to introduce 1,000 EVs each in 10 cities with CATL’s first foray into batteries for consumer EVs 2011 – Chinese investors, including Huang Shiling and Robin Zeng, spin off CATL from TDK, to acquire 85% ownership stake 2013 – Through partnership with BMW, all-electric Zinoro is launched, building additional German engineering expertise 2014 – CATL eyes international expansion, launches first international subsidiary, in Germany | 2018 – In addition to official IPO on the Shenzhen Stock Exchange, the first overseas production facility in Erfurt, Germany, is launched 2019 – Sales of Chinese EVs reach 1 million units per year, 10x from 2013, with CATL being a large beneficiary 2021 – Milestone in energy storage project with construction of a 220 MWh facility in Texas 2023 – With launch of new product platforms (e.g., Qilin) and accelerating year-over-year growth in NEVs, CATL is well positioned to lead in the future
1999
Formation of ATL
Case study: CATL
Acquisition by TDK
2005
2011
CATL founded through spin-off of ATL
2014
First international subsidiary in Germany with CATG
CATL goes public on Shenzhen Stock Exchange
2018
220 MWh energy storage project in Texas, largest in the world
2021
JV established with Geely Auto Group
2019
Public demonstration of electric bus fleet at 2008 Beijing Olympics
2008
2013
Partnership with BMW to develop all-electric Zinoro
Sources: CATL; Quartz, How CATL became the world's biggest electric car battery company (2019); TNI, The new Darwinian world of the energy transition (2024).
Credit: Hassan Riaz, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).

## Slide 56: Through a combination of key differentiating factors, CATL has captured 37% of the market
CATL’s keys to success helped it capture 37% of the total global battery market in 2023
Capitalizing on rapid domestic EV growth
From market growth of 18,000 EVs to over 9 million over the past 10 years, CATL capitalized on exponential market growth.
Product innovation
With 20,000 R&D engineers and scientists, CATL filed 1,061 patents in 2022 vs. BYD’s 662.
Early-mover advantage
CATL’s early research, bolstered by technology licenses and state support, was key to developing initial EV batteries.
Strong vertical integration
Mining subsidiaries, exploration partnerships, and large purchasing power drives down battery cost structure.
Case study: CATL
Chart: 
 | 36.8
 | 15.8
 | 13.6
 | 6.4
 | 4.9
 | 4.7
 | 4.6
 | 13.2
Others
Samsung SDI
CALB
SK On
Panasonic
LG Energy Solution
BYD
CATL
706.5 kWh
Observations
In the early 2010s, CATL was a small player (<5%) of the global battery market.
Specific factors that led to its current widespread success include:
  Drove down cost of Li-ion batteries by 90% from 2010 to 2023, leading to market expansion
  Effective long-term agreements with both domestic and international EV manufacturers
  Focus on core strengths in producing batteries (BYD, in comparison, also focused on manufacturing NEVs)
Sources: CATL; Insights by GreyB, CATL Patents (2024); SNE Research, Global electric vehicle battery usage (2024); Bloomberg, Dawning Age of the Battery (2020).
Credit: Hassan Riaz, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).

## Slide 57
The energy storage opportunity
Mobility energy storage
Utility energy storage
  Technology
  Opportunities and unlocks
  Case study

## Slide 58: Utility energy storage

## Slide 59
The energy storage opportunity
Mobility energy storage
Utility energy storage
  Technology
  Opportunities and unlocks
  Case study

## Slide 60
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Key messages Utility energy storage: Technology landscape
Several energy storage technologies are currently available for utility-scale deployment of long-duration energy storage (LDES), each with its own set of advantages: mechanical (e.g., pumped hydro (PSH), compressed air (CAES), gravitational storage), electrochemical (various battery technologies), chemical (hydrogen fuel cell) and thermal.
Pumped storage hydropower is currently the most prevalent, commercialized and widely deployed utility-scale storage technology, largely due to its high efficiency, wide range of discharge capabilities and its low green house gas emissions.
The main downsides of PSH are its requirements for favorable geographical and geological conditions as well as its limited modularity. Other novel storage technologies are primarily attempting to solve these downsides, with various degrees of success.
Discharge duration time: Discharge duration range varies significantly across different energy storage technologies. However, only hydrogen and CAES reach a discharge duration range comparable to that of PSH (up to 24 hours).
Lifecycle environmental impact: Thermal storage is the only technology that beats PSH in total lifecycle GHG emissions. Other technologies fall short of PSH mostly due to a significantly lower total lifetime.
Cost: CAES leads in lowest installed cost ($100-$130 USD/MW) due to the use of preexisting geological formations, with PSH second ($250-$300 USD/MW) for the same reason and Li-ion battery ($310-$430 USD/MW) third. Further development is needed in the technology space to achieve an LCOS goal of $0.05 USD/kWh to facilitate commercial viability of large-scale LDES deployment.
Applicability and modularity: The applicability of various technologies for LDES at the utility level varies significantly on the scale required and the deployment location. Several battery technology systems as well as other novel storage technologies offer high modularity and versatility for a wide range of applications. At the current stage, these benefits are not seen as valuable enough to balance out the drawbacks in performance metrics when comparing novel technologies to PSH.

## Slide 61: Wide range of storage technologies available in the market, each with advantages and limitations
Various energy storage technologies
Observations
Mechanical: Storing energy in physical forms, such as potential or kinetic energy, providing durability and scalability
Electrochemical: Storing energy through chemical reactions, typically offering high energy density and efficiency
Electrical: Storing energy in electric fields or magnetic fields, providing quick response times and high-power output:
  Current electrical technologies such as capacitors are good for complementary purposes due to their lower energy storage capability (as a result, they will not be highlighted in the Deep Dive).
Chemical: Storing energy in chemical bonds, offering high energy density and flexibility
Thermal: Storing energy in the form of heat, which can be used for various applications including power generation and industrial processes
Sources: Renewable and Sustainable Energy Reviews, Stationary energy storage (2022); MDPI, Supercapacitors: An Efficient Way for Energy Storage Application (1998).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Energy storage technologies
Chemical
Thermal
Hydrogen
Latent phase change material
Thermochemical
Thermal
Electrochemical
Electrical
Liquid batteries
Capacitor
Supercapacitor
Superconducting magnetic energy storage (SMES)
Mechanical
Pumped hydro
(PSH)
Compressed air (CAES)
Gravitational storage
Explained in deep dive
Solid-state batteries

## Slide 62: PSH currently the cornerstone of LDES due to several advantages
 | Pumped storage hydro and novel (PSH) | Compressed air energy Storage (CAES) | Gravitational storage
Description | Uses two water reservoirs at different elevations. Energy is stored by pumping water from the lower reservoir to the upper one, typically during off-peak hours, when demand for electricity is low. | Uses electricity to compress air; the compressed air is then stored and later re-expanded to generate electricity. | Excess electrical energy is used to lift heavy blocks onto a large tower. When electricity is required, the blocks are lowered, spinning a motor to generate electricity.
Advantages | Long lifetime, low-cost solution for bulk storage | Does not face fundamental technical challenges | Versatile technology that can be readily deployed at a variety of scales
Barriers | Difficult to finance (long duration times, large size, high and uncertain capital costs); geographical constraint | Availability of suitable, large-scale underground air storage | Supply chain, maintenance, efficiency, and lower lifetime.
Lifetime | 50-100 years | 30 years | 20-35 years
Round-trip efficiency | 70%-85% | 40%-70%* | 70%-90%
Discharge duration at max power | Several hours to days | Several hours to days | Several hours
Cost (LCOS) | Low | Low | Medium
Development stage for utility-scale grid applications | Widely commercialized | Initial commercialization | Initial commercialization
*As CAES can rely on both electricity to compress air and a fuel to expand the air (depending on technology used), its efficiency cannot be directly compared to other storage technologies.
Sources: Greening the Grid, Storage Technologies; MIT, The Future of Energy Storage (2022); ENTEC, Energy Storage Database and Use Case Matrix (2022).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Mechanical
1
2
3

## Slide 63: Battery systems the most advanced out of non-mechanical tech
 | Battery technologies | Hydrogen | Thermal
Description | Interconverted chemical and electrical energy through reduction and oxidation (redox) reactions. These reactions occur on both the positive and negative electrodes connected by an external circuit and frequently separated by electrolyte. | Produced with electricity and stored until there is demand for the stored energy, at which point, the hydrogen is converted to generate electric power. | Systems use electricity to heat up a material, which is then insulated until the energy is needed. The heat is converted back to electricity through a power conversion device.
Advantages | Versatile technology that can be readily deployed at a variety of scales | Ability to scale power and storage capacities independently; use beyond energy storage | Heat can be stored in cheap materials
Barriers | Supply chain, thermal runaway, lower lifetime, support and safety technologies required (e.g. climate control, fireproofing) | High production costs, safety concerns, difficulty storing | Difficulty converting heat back into electricity efficiently and cost effectively
Lifetime | 10-20 years | 5-30 years | 10-50 years
Round-trip efficiency | 40%-90%* | 20%-40% | 55%-99%
Discharge duration at max power | Minutes to days (technology dependent) | Several hours to months | Several hours to months
Cost (LCOS) | Medium to high (technology dependent) | High | High
Development stage for utility-scale grid applications | Commercialized/prototyped (technology dependent) | Pilot stage | Initial commercialization
*Efficiency highly dependent on the battery technology selected.
Sources: Greening the Grid, Storage Technologies; MIT, The Future of Energy Storage (2022); ENTEC, Energy Storage Database and Use Case Matrix (2022).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Electrochemical
Chemical
Thermal
1
5
6
4

## Slide 64: CAES (compressed air) is a proven technology with significant geological requirements, similar to novel PSH
Source: Quidnet Energy
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Sample projects
Technical specifications
Maturity | Initial commercialization
Modularity | Dependent on project (container systems are modular, while systems using salt caverns are not)
Deployment size (MW) | 200-500
Nominal duration (hours) | 5-48+
Round-trip efficiency (%) | 40-70
Use cases
Intraday
Multiday
Seasonal
Remote or off-grid
Intermittent daily RE generation
Grid stability services
Weather-driven outages
Grid congestion
Seasonal imbalances
Long-term outages
Grid stabilization
Backup power
Company | Project | Location | Rated power (MW) | Duration (hrs.) | Status
 | McIntosh CAES Plant | Alabama, U.S. | 110 | 26 | Operational
 | Goderich Energy Storage Facility | Ontario, Canada | 2 | 5 | Operational
Definition
Excess electricity is used to compress and cool air, which is then stored under pressure either in specialized containers (CapEx intensive) or underground (e.g., In salt caverns). Air can be stored as pressurized gas (CAES) or liquified (LAES). Heat from the compression process can be stored in a separate thermal store for later use. To discharge, heat (from the thermal store or combustion of natural gas) is introduced back into the compressed/liquid air, which is released to spin a turbine and generate electricity.
Hot thermal store
Storage (cavern or container)
Air in
Air out
Expansion
Compression
Power out
Power in
Waste heat
Mechanical - CAES

## Slide 65: Gravitational storage stores energy by way of a heavy mass kept at an elevated height, so space is a serious limitation
Gravitational storage utilizes excess electricity to raise heavy weights, creating gravitational potential energy. When masses are lowered during discharge, potential energy is converted to kinetic energy, turning a turbine and generating electricity. However, only so much energy can be stored per block, making extensive amounts of space a prerequisite for use of gravitational storage technologies.
Sample projects
Technical specifications
Maturity | Pilot
Modularity | Modularity limited by space requirements
Deployment size (MW) | 20-1,000
Nominal duration (hours) | 0-20
Round-trip efficiency (%) | 70-90
Use cases
Intraday
Multiday
Seasonal
Remote or off-grid
Intermittent daily RE generation
Grid stability services
Weather-driven outages
Grid congestion
Seasonal imbalances
Long-term outages
Grid stabilization
Backup power
Company | Project | Location | Rated power (MW) | Duration (hrs.) | Status
 | EV 1 Tower | Castione, Switzerland | 4-8 | 8-16 | Demonstration prototype
 | EVx GEE | Rudong, China | 25 | 4-16 | In construction
Fully discharged
Charging/discharging state
Fully charged
Charging
Excess electricity produced by renewables is used to pull weights to the top of the shaft.
Discharging
When electricity is required, the weights are lowered, turning motors and generating electricity.
Sources: Energy Vault; Graviticity
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Mechanical - GS
Definition

## Slide 66: Lithium-ion batteries offer efficiency and energy density, at the cost of short duration and lifespan and high maintenance requirements
Sample projects
Technical specifications
Maturity | Commercialized
Modularity | Highly modular, limited only by safety requirements
Deployment size (MW) | 10-100+
Nominal duration (hours) | 0-8
Round trip efficiency (%) | 75-90
Use cases
Company | Project | Location | Rated Power (MW) | Duration (hrs.) | Status
 | Moss Landing | California, U.S. | 750 MW | 4 | Operational
 | Victorian Big Battery | Victoria, Australia | 450 MW | 1.5 | Operational
Lithium-ion batteries store electrical energy by moving lithium ions between two electrodes — typically a graphite anode and a lithium metal oxide cathode — through an electrolyte, a process that unfolds during both charging and discharging cycles. Lithium-ion batteries are currently the most widely used energy storage technology, largely due to their modularity, fast response times, and relatively high energy density. But major drawbacks, such as low duration, fast degradation, fire risks, and extensive O&M needs, may offer an opening for other technologies to dominate in LDES.
Intraday
Multiday
Seasonal
Remote or off-grid
Intermittent daily RE generation
Grid stability services
Weather-driven outages
Grid congestion
Seasonal imbalances
Long-term outages
Grid stabilization
Backup power
Sources: EIA, Battery Storage in the United States (2023); Enel X, Energy Storage; American Jobs Project.
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Electrochemical
Definition

## Slide 67: Flow batteries have a longer lifespan than Li-ion and are safer but have a much lower energy density and carry higher CapEx costs
Sources: DOE, Energy Storage Reports and Data; Invinity; Lockheed Martin.
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Dis-charging
Sample projects
Technical specifications
Maturity | Wide range (R&D through commercial stages)
Modularity | Highly modular without safety concerns
Deployment size (MW) | 10-100
Nominal duration (hours) | 5-48+
Round trip efficiency (%) | 50-80
Use cases
Company | Project | Location | Rated Power (MW) | Duration (hrs.) | Status
 | Energy Superhub Oxford | Oxford, UK | 5 MWh | 2-10 | Active
 | GridStar Flow battery | Alberta, Canada | 6.5 MW | 8 | Announced
Aqueous electrolyte flow batteries, also referred to as simply flow batteries, store energy as a potential difference across two liquid electrolytes stored in separate tanks. During discharge, pumps bring the electrolytes together into a single container separated by a selective membrane. Half reactions at the two electrodes then generate an electric current. To recharge the battery, a current is run in the opposite direction through the battery, replenishing the electrolytes in the tanks. However, scaling energy capacity requires progressively larger tanks, and CapEx costs are high.
Intraday
Multiday
Seasonal
Remote or off-grid
Intermittent daily RE generation
Grid stability services
Weather-driven outages
Grid congestion
Seasonal imbalances
Long-term
outages
Grid stabilization
Backup power
e-
e-
v+4
v+5
v+2
v+3
Positive electrolyte (e.g., V+5/V+4)
Negative electrolyte (e.g., V+2/V+3)
Pump
Pump
Electrochemical
Electrochemical
Definition

## Slide 68: Metal air batteries offer safety, energy density, and lower costs, at the expense of a significantly shorter lifespan
Sources: DOE, Energy Storage Reports and Data; Form Energy.
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Sample projects
Technical specifications
Maturity | R&D/pilot
Modularity | Highly modular without safety concerns
Deployment size (MW) | 10-100
Nominal duration (hours) | 20-200
Round-trip efficiency (%) | 40-70
Use cases
Company | Project | Location | Rated Power (MW) | Duration (hrs.) | Status
 | Great River Energy | Minnesota, U.S. | 1 | 150 | Announced
Metal-air batteries are composed of a metal negative electrode and an air positive electrode. Oxygen from the air serves as the positive electrode and reacts with the metal electrode to drive a current. During discharge, the process is reversed and oxygen is released back into the atmosphere.
Intraday
Multiday
Seasonal
Remote or off-grid
Intermittent daily RE generation
Grid stability services
Weather-driven outages
Grid congestion
Seasonal imbalances
Long-term outages
Grid stabilization
Backup power
Discharging
Negative electrode (meta)
Positive electrode (carbon-based and air permeable)
External circuit
Fe
OH-
OH-
Fe (OH)2
O2
e-
e-
Electrochemical
Definition

## Slide 69: Solid-state and other new batteries are safer than Li-ion technologies, with significantly lower energy density
Sources: DOE, Energy Storage Reports and Data; Microsoft.
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Sample projects
Technical specifications
Maturity | Multiple projects in pilot phases, with technology set to be tested in utility-scale usage
Modularity | Highly modular without safety concerns
Deployment size (MW) | 10-1,000
Nominal duration (hours) | 4-24
Round trip efficiency (%) | 80-90
Use cases
Solid-state batteries and other novel chemistry batteries use elements like metal alloys, solid metals, and salt electrolytes to hold a charge. These technologies are usually safer and easier to maintain than Li-ion batteries because they're more stable in extreme temperatures and don't pose a fire risk. They don't utilize lithium, which is in high demand — a factor that serves as a competitive advantage and allows solid-state batteries to avoid competing with mobility-designated battery technologies. However, these technologies have much lower energy densities and durations and are being used at a very limited scale.
Intraday
Multiday
Seasonal
Remote or off-grid
Intermittent daily RE generation
Grid stability services
Weather-driven outages
Grid congestion
Seasonal imbalances
Long-term outages
Grid stabilization
Backup power
Negative electrode
(metal alloy)
Project | Location | Storage capacity | Status
Microsoft | Massachusetts, U.S. | 40 kWh | Implemented
6.6”
~7”
Positive electrode (solid metal particles)
Electrolyte (molten salt)
Example of cell configuration
Schematic cross-section
Electrochemical
Definition

## Slide 70: Hydrogen storage technologies are well suited for long-term storage, but high CapEx costs inflate their LCOS
Sources: DOE, Energy Storage Reports and Data; Siemen; Engie
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Sample projects
Technical specifications
Maturity | Pilot (with commercial project announced)
Modularity | Project dependent (container systems are modular, while systems using salt caverns are not)
Deployment size (MW) | 10-100
Nominal duration (hours) | 500-1,000
Round-trip efficiency (%) | 40-55
Use cases
Intraday
Multiday
Seasonal
Remote or off-grid
Intermittent daily RE generation
Grid stability services
Weather-driven outages
Grid congestion
Seasonal imbalances
Long-term outages
Grid stabilization
Backup power
Hydrogen storage involves energy stored in the form of chemical bonds (generally H2 or synthesis gas). During charging, renewable electricity is used to power an electrolyzer that splits water into hydrogen and oxygen. The hydrogen is then compressed and stored in tanks or underground caverns, where it can then be used to produce electricity, either through combustion in a turbine or by running it through a fuel cell. Hydrogen storage provides very long duration, making it suitable for long-term storage. However, CapEx costs remain high, driving a high LCOS.
Company | Project | Location | Rated Power (MW) | Duration (hrs.) | Status
 | Mohammed bin Rashid Al Maktoum Solar Park | Dubai, UAE | Size not announced (projected to generate 20.5 kg H2/hour) |  | Operational
 | Ingrid Hydrogen Demonstration Project | Troia, Italy | 12 | 30+ | Operational
 | Hyflexpower | Saillat-sur-Vienne, France | 12 | N/A | Announced
O2
Hydrogen storage
Electricity
H2O
Electrolyzer
H2
Compression
Solar energy
Electricity
H2
H2
Chemical
Definition

## Slide 71: Thermal energy storage typically utilizes heat to store energy, though efficiency ranges widely with these technologies
Sources: DOE, Energy Storage Reports and Data; Malta.
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Sample projects
Technical specifications
Maturity | Wide range (R&D through commercial phase)
Modularity | Modular but limited by infrastructure requirements
Deployment Size (MW) | 10-500
Nominal Duration (hours) | 25-200
Round trip efficiency (%) | 20-90
Use cases
Intraday
Multiday
Seasonal
Remote or off-grid
Intermittent daily RE generation
Grid stability services
Weather-driven outages
Grid congestion
Seasonal imbalances
Long-term outages
Grid stabilization
Backup power
Company | Project | Location | Rated Power (MW) | Duration (hrs.) | Status
 | NB Power Thermal Storage | New Brunswick, Canada | 100 MWh | 26 | Canceled
 | TES, POD | Egypt | 0.25 MW | 13 | Bankrupt
A heat pump or electric resistance heater converts electrical energy into thermal energy by heating up a material (e.g., molten salt, volcanic rock) and/or chilling a liquid. Or, in an alternative approach, the heat needed for thermal energy storage can be provided by concentrated solar power. Then, when energy is needed, the heated or cooled substance can be converted back into electrical energy using a heat engine. For heated materials, for instance, the heat is used to power a steam turbine and thus generate electricity.
Energy gathered from wind, solar
Electricity drives a heat pump, heating/cooling liquid
Temperature difference turned back into electricity
Heat pump method shown here
Thermal
Thermal
Definition

## Slide 72: PSH best positioned to support renewable energy grid integration, while batteries have wider application for short duration
Comparison of key characteristics for energy storage technologies (2022-2023 basis)
Parameter | Pumped storage hydro (PSH) | Compressed air (CAES) | Gravitational | Battery | Green hydrogen (Fuel cell) | Thermal energy storage (TES)
Discharge duration at max power (hours) | 5-21 | 2-25 | N/A | 1-8 | 3-26 | Several hours
Lifecycle GHG emission (gCO2/kWh) | 145-179 | 161-272 | N/A | 259-335 | 386-700 | ~26
Costs: |  |  |  |  |  | 
Installed cost (USD/kWh) | 250-300 | 100-130 | 455 | 310-430 | 260-340 | ~700
LCOS (USD/kWh) | ~0.1 | ~0.1 | ~.0.2 | 0.1-0.3 | 0.3-0.4 | ~0.5
Applications: |  |  |  |  |  | 
Renewable energy integration | Yes | Yes | Yes | Yes (Li-Ion) | Yes | Yes
Bulk energy storage | Yes | Possible | Yes | Possible (Li-Ion) | Yes | Yes
Ancillary services | Partial | Partial | Partial | Yes | Yes | Partial
Energy management | No | Partial | No | Yes | Yes | No
Sources: Applied Energy, Energy storage technologies (2016); Joule, Projecting LCOE Storage Technologies (2019); Oxford University Press, Monetizing Energy Storage (2023); PNNL, Energy Storage Cost and Performance; PNNL, LCOS Estimates; Applied Energy, Comparison of electricity storage options using LCOS (2016).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Most favorable for renewable energy integration
Least favorable for renewable energy integration
Observations
PSH dominates due to its wide discharge duration range, making it suitable for a wide range of applications. PSH also emits relatively low levels of GHGs.
CAES, meanwhile, has limited applications and is difficult to scale up due to geographic constraints.
And while hydrogen's long duration is promising, the technology has significant GHG emissions due to poor round-trip efficiency.
Batteries can be used widely for short-duration applications.

## Slide 73: Hydrogen, PSH, and CAES deliver the longest discharge duration of current technologies, offering grid reliability
Discharge durations for stationary energy storage technologies operational in 2022
(hours)
Sources: Oxford University Press, Monetizing Energy Storage (2023); DOE, Long-Duration Energy Storage; Alsym Energy, Understanding Short-, Medium- and Long-Duration Energy Storage (2024).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Observations
Long-duration energy storage (LDES) technologies like hydrogen, PSH, and CAES deliver discharge durations of over 10 hours, offering significant value for grid reliability and renewable energy integration. They do this by:
  Providing a consistent and reliable energy supply. This positions LDES as a replacement to traditional baseload power sources.
  Storing excess renewable energy during periods of low demand and discharging during periods of high demand.
Short-duration energy storage (SDES) is intended for short and high-power discharges, with key applications like:
  Stabilizing the frequency of power grids, which is essential for maintaining the reliability and efficiency of electrical distribution systems.
  Reducing strain on the grid during peak periods.
Chart: 
 | 3 | 5 | 2 | 1 | 1
 | 26 | 21 | 25 | 4 | 4
Hydrogen (Chemical)
PSH
CAES
Lithium-ion
Lead (Pb-Acid)
LDES > 10 hrs..
SDES < 4 hrs.
Lasts days or even months, depending on storage capacity
Long-duration energy storage
Short-duration energy storage
Primary use case:
Discharge duration at max power

## Slide 74: Most battery technologies are significantly more versatile in minimum size and maximum duration vs. competition
 | 1 MW |  |  |  |  |  |  | 10 MW |  |  |  |  |  |  | 100 MW |  |  |  |  |  |  | 1,000 MW |  |  |  |  |  | 
Duration (hours) | 2 | 4 | 6 | 8 | 10 | 24 | 100 | 2 | 4 | 6 | 8 | 10 | 24 | 100 | 2 | 4 | 6 | 8 | 10 | 24 | 100 | 2 | 4 | 6 | 8 | 10 | 24 | 100
Lithium-ion LFP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Lithium-ion NCM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Lead acid |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PSH1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CAES1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Hydrogen |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Thermal |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Gravitational |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1) Four hours for PSH and CAES represents a sweet point. Inefficiencies are seen at very short durations like two hours. PSH and CAES can match the continuous discharge capability that batteries and other technologies are at six and eight hours.
Source: DOE, Grid Energy Storage Technology Cost and Performance Assessment (2022).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Capacity (MW)
Feasible size and duration of the technology
Discharge duration at max power

## Slide 75: Of the technologies commercialized today, thermal and PSH offer the lowest total GHG emissions
Observations
Hydrogen appears to be the largest producer of GHG emissions, due to production methods and low system efficiency.
Pumped storage hydropower, meanwhile, produces limited GHG emissions because renewable energy is incorporated into the grid mix used for the pump’s electricity. PSH facilities also have long lifetimes, and economies of scale could reduce GHG emissions even further.
  PSH has lower impacts in all categories except land-use requirements.
Hydrogen's GHG emissions could be greatly reduced and the technology could compete with PSH and CAES if electricity with a low GHG-intensity is used in H2 production.
Thermal produces the lowest GHG emissions because abundant, low-impact materials are used in its storage, it seamlessly integrates with renewable energy sources, and it is highly efficient, with minimal losses.
Results reflect a cradle-to-grave analysis. Lifecycle stages considered were production, use, and end-of-life.
1) All emissions totals calculated in cradle-to-grave framework for ~100 MW system. Sources: Energy Conversion and Management, Assessment of energy storage technologies (2020); Environmental Science & Technology, Life Cycle Assessment of PSH (2023); Energy, Assessment of stationary electricity storage (2017); International Journal of Energy and Environmental Engineering, Life-cycle of PHS (2017).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
GHG emissions across lifecycle,1 gCO2/kWh
Chart: 
 | 26 | 145 | 161 | 259 | 386
 | 26 | 179 | 272 | 335 | 700
0
Thermal
PSH
CAES
Lithium-ion
Hydrogen
Lifecycle GHG emissions

## Slide 76: CAES the most cost-effective technology when it comes to both the initial CapEx requirement and LCOS
LCOS vs. installed cost across storage technologies in 2023 for 100 MW/10 hours
Observations
Compressed air (CAES) boasts some of the lowest installed costs and LCOS due to its use of preexisting geological formations such as caverns, aquifers, and other rock formations.
  Not having to construct new storage facilities provides significant cost savings.
Of the different battery chemistries, lithium (LFP) stands out because of its moderate costs and LCOS. While not the cheapest, lithium compares favorably to lead, which has higher costs and a higher LCOS, reflecting lead's lower efficiency, shorter life, and maintenance needs.
Hydrogen has competitive installed costs, but its LCOS is high due to poor system round-trip efficiency, attributable to inefficiencies in the conversion process involved in storing and retrieving energy.
*Hydrogen system capital costs reflect 2021 estimates, since hydrogen was not part of the 2024 research effort.
Sources: PNNL, Cost; PNNL (LCOS).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 0.1 | 0.12 | 0.17 | 0.17 | 0.18 | 0.23 | 0.28 | 0.35
 | 112.5 | 278.7 | 349.1 | 454.9 | 302.5 | 388.8 | 430.9 | 295.4
0.00
0.05
0.10
0.15
0.20
0.25
0.30
0.35
113
CAES
PSH
349
Lithium (LFP)
Gravitational
303
Thermal
Lithium (NMC)
Lead
295
Hydrogen
0.28
0.10
0.12
0.17
0.17
0.18
0.23
0.35
Installed cost (USD/kwh)
LCOS (USD/kWh)
Cost

## Slide 77: Further development needed for all technologies if they are to achieve a LCOS goal of $0.05/kWh
Sources: PNNL, LCOS; DOE, Energy Storage Grand Challenge Roadmap (2020); DOE, Achieving the Promise of Low-Cost Long Duration Energy Storage (2024).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Observations
Hydrogen is the only technology expected to see significant reductions in its LCOS by 2030, thanks to advancements in electrolysis, storage methods, and system integrations.
That said, all technologies, including hydrogen, are projected to fall short of the U.S. Department of Energy’s 2030 Energy Storage Grand Challenge Roadmap target of a LCOS of $0.05/kWh for long-duration stationary applications.
Achieving the $0.05/kWh LCOS target is essential for energy storage to be commercially viable across a broad range of stationary tasks.
Continued innovation in preexisting storage technologies such as batteries, hydrogen, and thermal storage will be critical to bridge the cost gap.
With an estimated $750 million investment over eight years, CAES could reach a LCOS as low as $0.03/kWh.
PSH, meanwhile, could reach an even lower LCOS, $0.02/kWh, with a $560 million investment over the same period.
LCOS expectations for 100 MW/10 hours systems, $/kWh
Chart: 
 | 0.35 | 0.19
 | 0.28 | 0.27
 | 0.23 | 0.18
 | 0.18 | 0.17
 | 0.17 | 0.14
 | 0.17 | 0.16
 | 0.12 | 0.12
 | 0.1 | 0.1
 | 0.19 | 0.16
 | 0.27 | 0.086
 | 0.17 | 0.112
 | 0.14 | 0.07
0.00
0.05
0.10
0.15
0.20
0.25
0.30
0.35
0.40
2022
2030
2030 with investment
Lithium NMC
Gravitational
Hydrogen
Lead acid
Thermal
Lithium LFP
PSH
CAES
Target LCOS
by DOE
= $0.05/kWh
(by 2030)
DOE target date for $0.05/kWh LCOS
Cost

## Slide 78: PSH and CAES offer cost advantages, but batteries provide super-scalability for the future
Source: Oxford University Press, Monetizing Energy Storage (2023).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Observations
Power-specific cost reflects the cost related to power delivery and is most important when very high power must be delivered for very short periods.
The energy-specific cost denotes the cost of storing energy and, therefore, is the most critical factor for applications that require a high amount of energy to be stored for a long period of time.
Both PSH and CAES can boast of low costs for both power at $/kW and energy at $/kWh. This dual power-energy advantage makes it suitable for balancing grid demand over a longer duration.
Lithium-ion batteries are positioned in the high-cost but high-performance option. In power delivery, in respect to short-duration storage, it is the best. This includes solutions that require quick energy discharge.
Hydrogen is extremely effective in terms of capacity, but the high costs per kW prohibit the use of hydrogen when power output is important. It is still an option for long-term, large-scale energy storage.
While PSH and CAES are cost effective for both, scalability is bound by geography and infrastructure.
Chart: 
| 1100 | 1300 | 250 | 300 | 5000
 | 50 | 40 | 300 | 320 | 30
PSH
CAES
Lithium ion
Lead acid
Hydrogen
Investment cost per power capacity and per energy capacity for stationary energy storage technologies, $/kW by $/kWh
Increasing power (kW) is…
…high cost
Low cost
Increasing energy (kWh) is…
…high cost
Low cost
Cost

## Slide 79: Energy storage technologies are used across various applications in the utility system
Source: ADB, Handbook on Battery Energy Storage Systems (2018).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Application areas | 
Renewable energy integrations | Time shifting: Storing the excess generation of renewable energy and releasing it when demand is higher or intermittent generation is lower.
 | Firming capacity: Keeping the grid stable in the face of potential wind and solar intermittency.
Bulk energy | Peak shaving: Reducing the energy consumed during peak demand on the electric grid by introducing energy stored to shave off the top of the power demand curve.
 | Arbitrage of energy: Purchasing power at low price and selling it in high-price periods on wholesale or retail markets.
Ancillary services | Voltage support: Normally, designated power plants are used to generate reactive power (expressed in VAr) to offset reactance in the grid. These power plants could be displaced by strategically placed energy storage within the grid at central locations or by multiple VAr-support storage systems placed near large loads, following the distributed approach.
 | Load balancing: Evenly distributing the amount of energy used across different applications to avoid power outages.
 | Spinning reserve: The operation of an electric grid requires reserve capacity that can be called on when some portion of the normal electric supply resources unexpectedly becomes unavailable.
 | Black start: Providing an active reserve of power and energy within the grid that can be used to energize transmission and distribution lines and provide station power to bring power plants online after a catastrophic failure of the grid.
 | Frequency balancing: Balancing short-term mismatches in supply and demand, to maintain smooth and reliable power flow from the grid.
Energy management | Enhancing power quality: Protecting on-site load against short-duration power loss or variations in voltage or frequency.
 | Power reliability: Covering temporal lack of variable supply and providing power during blackouts.
Definitions
Application

## Slide 80: A technology’s application suitability varies depending on its power and duration properties
Sources: Applied Energy, Energy storage technologies (2016); HuntKey, Gravity Energy Storage; Journal of Energy Storage, Capability study of dry gravity energy storage (2019); Renewable and Sustainable Energy Reviews, review of stationary energy storage (2022).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Application areas |  | Mechanical |  |  | Batteries |  | Thermal
 |  | PSH | CAES | Gravitational | Li-ion | Pb-Acid | 
Renewable energy integrations | Time shifting |  |  |  |  |  | 
 | Firming capacity |  |  |  |  |  | 
Bulk energy | Peak shaving |  |  |  |  |  | 
 | Arbitrage of energy |  |  |  |  |  | 
Ancillary services | Voltage support |  |  |  |  |  | 
 | Load balancing |  |  |  |  |  | 
 | Spinning reserve |  |  |  |  |  | 
 | Black start |  |  |  |  |  | 
 | Frequency balancing |  |  |  |  |  | 
Energy management | Enhancing power quality |  |  |  |  |  | 
 | Power reliability |  |  |  |  |  | 
PSH, CAES, thermal, Li-ion, and VRFB are the most suitable energy storage technologies for renewable energy integrations
Suitable application
Possible application
Unsuitable application
Application

## Slide 81
The energy storage opportunity
Mobility energy storage
Utility energy storage
  Technology
  Opportunities and unlocks
  Case study

## Slide 82
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Key messages Utility energy storage: Opportunities and unlocks
Pumped storage hydropower remains the dominant technology (74% share of global capacity) for long-duration energy storage due to its maturity and capacity edge.
Traditional PSH struggles with deployment given geographical constraints, high upfront capital costs, and long construction timelines. As a result, novel developments in PSH are emerging as the future, offering more flexibility and cost efficiency.
Novel PSH offers ~33% cost savings resulting from efficiency in underground work and optimized civil works. India expects an internal rate of return of 10% to 12% for this technology.
Quidnet Energy's innovative geomechanical PSH approach reached a key milestone with its NYSERDA partnership and recently announced 300 MW commercial facility.
Battery will surpass PSH in utility energy storage due to faster response, significant cost reductions in battery technology, and flexibility in location.
BESS cost declines are driven by advancements in cell and pack technology; further improvements are needed to reduce system costs.
In the United States, California and Texas lead in battery energy storage, though other regions could see significant growth.
In the United States, interconnection queues present a bottleneck, with a 3.5x discrepancy between projected builds and active projects. This challenge is delaying capacity deployment across the country.
Grid integration, smart grid, and vehicle-to-grid (V2G) could be a potential solutions:
Grid integration: Interconnecting the grids would create a more expansive network, which would enable power flows among regions and reduce congestion.
Smart grid: Data-based decision-making would enable better allocation of the location of new generation, and continuous monitoring of the grid would allow for more efficient interconnection requests.
V2G: The addition of vehicles to the grid would increase the capacity of storage needed to reach decarbonization targets.

## Slide 83: Amongst mechanical technologies, pumped storage hydro leads due to lifetime proposition; batteries stand to advance
Fast power delivery, small market
 | Batteries | PSH
Description | Batteries convert chemical energy to electrical energy via reduction and oxidation (redox) reactions. These reactions occur along both the positive and negative electrodes, which are connected by an external circuit and frequently separated by electrolyte. | With PSH, two water reservoirs are built at different elevations. Energy is stored by pumping water from the lower reservoir to the upper one, typically during off-peak hours, when demand for electricity is low.
Rationales for future technology domination | Scalability and flexibility: Batteries can be scaled in various sizes in a way other technologies can not. | Legacy storage: PSH is a mature technology that offers large-scale energy storage and grid balancing.
 | Quick response time: Batteries can provide immediate power at the peak of demand or during periods of instability, thus fitting as a combination for intermittent sources like solar and wind. | High efficiency: PSH is capable of storing and releasing energy at very high efficiencies (over 80%) for a long period.
 | Technological advancements: Continuous cost reductions and technology improvements are lengthening batteries' duration and making them better equipped for bulk energy storage uses in larger electricity markets. | Environmental considerations: PSH requires large reservoirs, which often have significant environmental impact. Expansion could be possible via dam retrofit.
1
2
Sources: IEA, Global installed energy storage capacity (2024); DOE, Pumped Storage Hydropower; EIA, Pumped storage electricity generators in the U.S. (2019).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Bulk energy, large market

## Slide 84: PSH’s dominance faces competition with batteries expected to grow
Sources: IEA, Global installed energy storage capacity (2024); DOE, Pumped Storage Hydropower; EIA, Pumped storage electricity generators in the U.S. (2019).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Global installed energy storage capacity, GW
Chart: 
 | 181 | 293
 | 33 | 203
 | 32 | 1001
13%
13%
74%
2023
67%
14%
20%
2030
250
1500
Utility-scale batteries
Behind-the-meter batteries
Pumped hydro
Capacity of pumped storage hydropower in 2023 by leading countries, GW
Chart: 
 | 50940
 | 21814
 | 19288
 | 5354
 | 4786
 | 4700
 | 4039
51
22
19
5
5
5
4
China
Japan
United States
Germany
India
South Korea
Italy
PSH
Observations
There are two types of pumped storage plants: open-loop plants, which have an associated natural water source, like a river, for one or both of the reservoirs, and closed-loop (or off-river) plants, which do not have a connected natural-water source. Instead, the same water is cycled between the two reservoirs for pumping and generation.
The PSH market should continue to grow as countries look to this tried-and-true energy storage mechanism for renewable energy integration with a relatively limited environmental impact.
The Chinese government has placed importance on PSH, as seen in its 14th Five-Year Plan for Scientific and Technological Innovation in the Energy Sector.
In Japan, where the geography is characterized by mountainous terrain and abundant water resources, emphasis has been placed on PSH technologies in places like the Kyushu region.
Pumped storage capacity in the U.S., meanwhile, is largely dated, having been built mostly between 1960 and 1990. Upgrading or building new PSH will require significant capital investments and the ability to navigate geographic constraints as well as lengthy permitting processes.
Unlike PSH, battery storage systems can be deployed virtually anywhere. Their scalability, combined with short installation times, sets them up to be commercially favored.

## Slide 85: Global PSH remains a critical driver for storage through 2030
Chart: 
 | 163 | 173 | 185 | 197 | 215 | 243 | 299 | 358
2023
2024
2025
2026
2027
2028
2029
2030
+12%
Sources: Statista, Pumped hydro storage market; TERI, Pumped Storage Plants (2023); GEM, Global Hydropower Data
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
NZE global installed electric capacity of pumped hydro, GW
Chart: 
 | 535.31 | 592.22 | 655.18 | 724.83 | 801.89 | 887.14 | 981 | 1086
0
500
1,000
1,500
2023
2024
2025
2026
2027
2028
2029
2030
+11%
PSH market size projections (USD$M)
Chart: 
 | 1443 | 1036 | 1032 | 824 | 697 | 552 | 493 | 312 | 244 | 200.6
0
500
1,000
1,500
UK
Phillipines
Canada
China
India
Australia
Serbia
U.S.
Slovenia
Morocco
Top countries by prospective PSH capacity growth, prospective/operating (MW/MW)
Observations
The global pumped storage hydropower market is expected to grow steadily through 2030. Over this period, the PSH market is projected to expand by 11%, reflecting increased investments and demand for energy storage solutions.
The United Kingdom is expected to grow its pumped storage capacity the most over the next decade, with a staggering 1,443% in projected growth, signaling a major strategic shift in energy storage.
While China is expected to have a relatively smaller growth rate of 824%, because it already has a vast operating capacity, China should see the largest absolute increase in megawatts worldwide.
India’s and Canada’s prospective growth reflects their commitment to bolstering energy storage as part of their renewable energy push.
Australia’s 552% growth highlights its efforts to stabilize its renewable-heavy grid. The planned expansion will be essential for the country’s energy transition and decarbonization targets.
Philippines, Morocco, and Slovenia are rapidly positioning themselves as key players in the global pumped storage market. These countries are demonstrating significant commitment to integrating renewable energy and enhancing grid stability.
PSH

## Slide 86: The bulk of conventional PSH costs come from indirect, contingency, and power station equipment costs
Source: NREL, A Component-Level Bottom-Up Cost Model for Pumped Storage Hydropower (2024).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 99.93 | 90.93 | 80.01 | 73.37 | 50.41 | 48.7 | 46.64 | 44.83 | 44.14 | 25.7 | 25.7
 | 9 | 10.92 | 6.64 | 22.96 | 1.71 | 2.06 | 1.81 | 0.69 | 18.44
PSH system
Resevoir, dams, and waterways
Water conductor
Power plant structure
Power station equipment
2
Switchyard
2
Trans-mission lines
2
Roads, railroads, and bridges
1
Land, and land rights
Contingency costs
Other indirect costs
Component-specific cost breakdown for large pumped storage hydro system, %
Observations
More than a quarter of total PSH project costs are tied to other indirect costs, a category that includes engineering, permitting, taxes, and interest during construction. The size of these expenses underscores the importance of rigorous project management and early-stage financial planning to manage cash flows and optimize cost structures.
Another 18% of costs come from contingency provisions, which account for unforeseen variables such as construction delays, technical challenges, or regulatory changes. This cost driver shows the high levels of uncertainty inherent in PSH projects and speaks to the need for risk mitigation strategies in these kinds of projects.
At 23% of total costs, power station equipment (including turbines, generators, and other essential machinery) constitutes the largest share of direct expenditures, indicating the critical role of advanced technology procurement and supply chain management in maintaining operational efficiency and reducing long-term costs.
Categories such as reservoirs, dams, and waterways (9%) and powerplant structures (7%) also represent key infrastructure investments. Although not the largest cost drivers, these components require careful planning and robust contractor management to avoid budget overruns.
PSH

## Slide 87: Novel PSH provides an alternative: Relying on suitable geological conditions instead of two vertically separated lakes
Excess electricity is used to pump water from a reservoir down a well and into a body of rock where it is stored under pressure between rock layers. When electricity is needed, the well is opened, allowing pressurized water to flow through a turbine, generating electricity for the grid.
Example projects
Technical specifications
Maturity | Commercial
Modularity | More modular than large-scale hydro but geographically constrained by need for underground rock bodies for storing water under pressure
Suitable deployment size (MW) | 10-100
Suitable nominal duration (hours) | 5-48+
Round-trip Efficiency (%) | 70-85
Use cases
Intraday
Multiday
Seasonal
Remote or off-Grid
Intermittent daily RE generation
Grid stability services
Weather-Driven Outages
Grid congestion
Seasonal Imbalances
Long Term Outages
Grid Stabilization
Backup Power
Company | Project | Location | Rated power (MW) | Duration (hrs.) | Status
 | NYSERDA geomechanical pumped storage | New York, U.S. | 2 | 10 | Announced
Charging
Water pumped underground and pressurized
Discharging
Water released and runs through turbine, generating electricity
Pond
Facility
Well
Reservoir
Source: Quidnet Energy.
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Definition
PSH

## Slide 88: Novel PSH could drive down cost by ~30% by requiring less underground work and savings on indirect and contingency costs
Sources: DOE, Cost Effective Small Scale Pumped Storage Configuration (2019); DOE, Review of Technology Innovations for Pumped Storage Hydropower (2022).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Cost saving for conventional PSH vs. sample novel PSH, 2019 USD/KW
Conventional PSH - $2,517/KW
Novel PSH - $1,677/KW
Chart: 
 | 2517 | 2475 | 2042 | 2042 | 2038 | 1840 | 1677 | 1677
 | 42 | 433 | 0 | 4 | 198 | 163
Conventional
42
Civil work savings
Underground work savings
0
Electro-mechanical savings
4
Transmission
Indirect savings
Contingency savings
Total novel PSH
2,517
1,677
-33%
Observations
Novel PSH technologies represent a transformative evolution in the field of energy storage. Unlike conventional PSH systems, which often require extensive aboveground infrastructure and are limited by geographical constraints, novel PSH designs utilize innovative underground and resource-efficient methods.
Novel PSH designs offer significant cost savings, reducing costs from $2,517/KW to $1,677/KW, due to more efficient underground work and optimized civil works.
Novel PSH technologies are expected to outcompete conventional, large-scale aboveground PSH, leveraging innovative designs to minimize resource-intensive construction and thus accelerate project timelines.
The anticipated outperformance of novel PSH technologies over conventional large-scale projects could lead to broader adoption and integration by encouraging private investment in projects with more clear timelines and shorter payback periods.
PSH

## Slide 89: Novel PSH projects in India with the potential to achieve 10%-12% IRR
Source: McKinsey, Net-zero power (2021).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Observations
A renewable developer in India is combining renewable energy with novel pumped storage hydro to achieve attractive internal rates of return.
India’s electricity demand is projected to rise sharply due to increased electrification of sectors like heating and transportation. Decarbonizing India’s power supply will require the adoption of flexible solutions like PSH to manage demand and grid stability.
The novel PSH system could experience a faster cost reduction trajectory, leading to higher returns.
The case modeled was a six-hour PSH 300 MW/ 1800 MWh system in combination with 600 MW of contracted hybrid renewable energy (solar and/or wind).
Assumptions: 2021 investment decision date
Commercial operation date: 2023
WACC: 10%
RE cost outlook: Midpoint scenario
PPA contract duration: 20 years
Net Present Value for a renewable developer, USD$M
Chart: 
 | 700 | 700 | 1350 | 1370
 | 650 | 20
Peak power supply
Off-peak power supply
Stability services provision
Total Value Creation
Chart: 
 | 450 | 200 | 200
 | 1000 | 250
Capital invested
Fixed O&M
NPV
1,000
IRR ~10%-12%
~700-800
~650-750
~20-40
~1,300-1,500
~100-300
PSH

## Slide 90: BESS set to dominate the energy storage market as capital costs continue to decrease
Chart: 
 | 71 | 115 | 224 | 398 | 616 | 861 | 1091 | 1330
0
500
1,000
1,500
2023
2024
2025
2026
2027
2028
2029
2030
Sources: BloombergNEF, New Energy Outlook (2024); McKinsey, Battery energy storage systems (2023); IEA, Battery storage capability (2021); NREL, Cost Projections Utility-Scale Battery Storage (2023)
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Projected trend of BESS
Chart: 
 | 39.6 | 48.1 | 57 | 66.3 | 81 | 95.45 | 114.75 | 129
2023
2024
2025
2026
2027
2028
2029
2030
+29%
Observations
Battery energy storage systems are set to dominate the global energy storage market with installed capacity expected to grow significantly through 2030.
Europe leads the prospective BESS capacity for 2026, followed closely by China, India, and the United States.
The BESS market size is projected to expand by 29% by 2030, which reflects heightened demand for energy storage solutions to accommodate flexible grid management.
Growth in the BESS market is expected to expand partly due to the forecasted drop in capital costs, potentially dropping below $200/kWh by 2050.
China is expected to experience one of the largest increases in BESS capacity given its access to necessary resources.
India and the United States are positioned to ramp up their BESS efforts.
BESS market size projections, USD billions
Chart: 
 | 38.6 | 34.1 | 31 | 23 | 21.3 | 9.4
Europe
China
India
USA
Rest of Asia
Rest of World
4-Hr BESS capital cost, 2022 $/kwh
Chart: 
| 2022 | 2023 | 2024 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
 | 482 | 500 | 503 | 496 | 403 | 390 | 380 | 370 | 350
 | 482 | 463 | 443 | 388 | 326 | 300 | 270 | 250 | 220
 | 482 | 347 | 327 | 310 | 245 | 210 | 200 | 190 | 175
High
Medium
Low
NZE global installed electric capacity of BESS, GW
Prospective BESS capacity by country in 2026, GWh
Battery

## Slide 91: BESS cost declines driven by advancements in cell and pack technology; further improvements needed to reduce system costs
Sources: CEA, BESS Price Forecasting (2023); Fastmarkets, Copper outlook (2024); Fitch Ratings, Steel outlook (2024); DOE, Battery Energy Storage Systems (2024).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 53.2 | 12.7 | 14.5 | 11.4 | 8.2
Category | Component | Key commodity | Price outlook
Cell | LIB cell COGS | Lithium carbonate | 
Cell | LIB cell COGS | Synthetic graphite | 
Cell | Profit margins | N/A | 
Rack | DC racking, container and enclosure | Steel | 
Rack | Switchgear and power conditioners | Power electronics | 
Module | Busbars and cabling | Copper | 
Module | Assembly/labor | Electronic manufacture | 
BMS/EMS | Rack/container | Software | 
↑
Price direction
↔
↓
↓
↑
↔
↓
↓
Observations
BESS container prices are primarily driven by cell COGS and vendor margins.
Declining lithium carbonate prices due to greater supply and investment and weaker than expected near-term EV demand should improve Li-ion pricing.
Synthetic graphite, another key part of Li-ion costs, could see rising prices as trends like price weakness due to Chinese overcapacity and diminished graphite electrode demand for electric arc furnaces reverse.
For steel, prices have continued to drop due to weak global demand, high export levels from China, and supply-side issues. Future U.S. tariffs on Chinese steel could lead to price increases.
Competition in the software space looks to place upward pressures on personnel costs for industrial controls development.
Construction cost is the area of most variability and holds the greatest potential for cost reduction potential, e.g., through standardized modular designs.
Cell
Module
Rack
Container
Integrator margin
↑
↑
U.S. manufactured DC container
price breakdown, unsubsidized
↓
↑
Battery

## Slide 92: In the U.S., California and Texas lead in battery energy storage; other regions have potential for significant growth
Chart: 
 | 84 | 15 | 1
Chart: 
 | 19 | 27 | 54
Cumulative grid-scale energy storage volume by state through 2033, MW
Top 31
Top 102
Other
U.S. energy storage market share in 2023 vs. 2033, MW
Observations
The U.S. energy storage market is undergoing a shift: Three states held 84% of the market share in 2023, but that is projected to drop to 54% by 2033.
This shows diversification and the entries by other states. States like Nevada, Arizona, and New York are looking to significantly increase their capacity.
Federal incentives and state-level clean energy mandates have played a pivotal role in this growth. States that have battery energy storage system mandates or targets, including California, Texas, and Arizona, are expected to remain key players.
States in the Midwest and Southeast that have historically had lower storage capacity are expected to see rapid expansions by 2033.
1) Top three states include California, Texas, and Arizona. 2) Top 10 include previous states plus Florida, Massachusetts, Nevada, Colorado, New Mexico, and New York.
Sources: Wood MacKenzie, US storage sector outlook (2024); EIA, U.S. battery storage capacity (2024).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Battery

## Slide 93: Interconnection queues hindering U.S. energy storage growth; streamlining critical
Regional projected storage build through 2032 vs. active-queue projects, GW
U.S. projected build through 2032 vs. active-queue capacity, GW
Observations
The U.S. energy storage sector faces a 3.5x discrepancy between 134 GW of projected builds and the 476 GW of projects sitting in interconnection queues. This indicates a major bottleneck that could delay or prevent necessary capacity from being deployed.
CAISO (California), PJM (Mid-Atlantic), and NYISO (New York) are significantly overloaded with five to 10 more projects in queues than their projected builds through 2032.
As a result, many projects in line may never be fully deployed due to capacity limitations and process hurdles. This poses a risk of underdelivery on the critical capacity needed for renewable integration and grid stability.
Streamlining the interconnection process represents a major opportunity to unlock tens of GWs of storage capacity, ensuring the U.S. stays on track for its goals.
Source: Wood MacKenzie, US storage sector outlook (2024).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 134 | 476
Projected built through 2032
Active projects in queues
3.5x
Chart: 
 | 21 | 26 | 5 | 17 | 5 | 10 | 5
 | 108 | 108 | 30 | 79 | 34 | 105 | 12
ERCOT
ISO-NE
MISO
NYISO
PJM
SPP
CAISO
5.1x
4.2x
6x
4.6x
6.8x
10.5x
2.4x

## Slide 94: Three potential technological solutions to debottleneck grid interconnections currently being explored and developed
1
3
2
Grid integration
Smart grids
Vehicle-to-grid (V2G)
Horizontally integrating the grid would require development of interconnections between individual ISOs and uniting grid control under a single operator.
This would unlock the potential to balance load across time zones and climates, significantly smoothing out the load curve.
Smart grids utilize an array of sensors, smart meters, and control devices to maximize optimization potential and prevent grid instabilities.
A fully developed smart grid enables full demand response and ensures maximum flexibility on both supply and load sides.
V2G technology allows EVs to act as a modular battery energy storage system, significantly expanding the total storage capacity of the grid.
Significant development is required in both the hardware and software infrastructure as well as in market design and compensation.
Sources: GridX; Prysmian.
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).

## Slide 95: Horizontal grid integration a potential option for optimizing cost and improving grid stability
Observations
The U.S. operates three primary power grids: the Eastern Interconnection, Western Interconnection, and ERCOT. These grids function independently, with little interconnection.
A horizontally integrated national grid would better handle extreme weather events by allowing power to flow to areas in crisis, such as Texas during its 2021 storm.
Studies have found that an integrated nationalized grid could provide consumer savings of up to $47.2 billion by optimizing grid efficiency and reducing congestion.
Creating a national grid would involve many challenges, including resistance at the state level, pushback from the fossil fuel industry, and the technological complexity of grid integration.
Engaging in such a project could cost as much as $4 billion to $5 billion and would be paid for by taxpayer dollars.
Sources: American Security Project, Why the US Needs a National Power Grid (2021); Texas Scorecard, Is Nationalizing the Power Grid the Answer? (2024); NREL, Interconnections Seam Study; ACORE, Energy Assurance Depends on a Resilient Transmission Grid (2022).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Integration challenges and opportunities for a national power grid
Grid integration

## Slide 96: Smart grids address grid instability with real-time monitoring and automation
Smart meters
Smart meters measure consumers' real-time energy consumption, providing detailed information on consumption patterns to both the consumer and the energy provider.
Sensors and automation devices
These are installed throughout the grid to monitor voltage, current, and load capacity. They can automatically adjust parameters to prevent overloads and prolonged, large-scale blackouts.
Communication networks
Software and analytics
The backbone of any smart grid, communication networks facilitate the transmission of data between various components, including sensors, automated devices, and control centers.
Smart grids generate massive amounts of data. To manage, analyze, and interpret this data, utilities rely on advanced software and analytics tools.
Sources: IBM, Optimizing energy production (2023); Heliyon, Recent developments in smart grid (2024).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Components of a smart grid
Differences between a conventional grid and a smart grid
Category | Conventional grid | Smart grid
Consumer desire | Does not allow customers to choose how they acquire electricity. | Provides customers with access to a range of power sources.
Distribution system | Requires unidirectional power transmission. Power from primary plants is distributed using traditional infrastructure. | Enables electricity supply in both directions. A supplementary power source provides electricity to customers.
Power plant monitoring | Utilizes manual monitoring for energy distribution. | Employs cutting-edge technology and can self-monitor to reduce power outages.
Method of energy control | Energy suppliers have limited control over the energy they supply. | Offers better control over electricity distribution through smart grid technologies and sensors.
Power restoration and maintenance | Personnel travel to the physical location of a distribution system breakdown for maintenance and repair. | Uses sensors to detect and repair anomalies without requiring a physical presence.
Technological aspects | Uses electromechanical power, resulting in limited internal regulation and communication. | Employs digital technologies to give devices autonomy and enable communication.
Addition of sensors | Limited control over infrastructure restricts the use of sensors, making flaw detection harder. | Enables the installation of multiple sensors along the line, aiding in fault detection.
Smart grids

## Slide 97: Investments in smart grids are underway across the world, aiming to bolster resilience and enable renewables implementation
Legislative and regulatory actions on grid modernization in Q1 2024
International plans to invest in smart grids
Observations
Several major countries have invested in smart grids as part of broader grid modernization efforts to enhance grid resilience, efficiency, and digitization.
Forty-nine U.S. states and Puerto Rico engaged in actions related to grid modernization during the first quarter of 2024.
  A total of 567 grid modernization actions were taken, with New York, Massachusetts, Michigan, California, Connecticut, and New Jersey taking the greatest number of actions during the quarter.
Several states, including Maryland and Colorado, also passed legislation on virtual power plants, which utilize the capabilities of smart grids as a backbone.
Sources: NC Clean Energy, 50 States of Grid Modernization (2024); IEA, Smart Grids.
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Countries | Highlight
EU | Presented an EU action plan, “Digitalisation of the energy system,” at the end of 2022. Plans to spend about $184 billion on grid digitization by 2030.
China | Plans to spend an equivalent of $442 billion on modernizing and expanding power grids between 2021 and 2025.
Japan | Announced plan in 2022 to invest an equivalent of $155 billion to promote smart power grid investments.
India | Launched a $38 billion program in 2022 mandating installation of smart meters across the country.
U.S. | Announced the Grid Resilience and Innovation Partnerships (GRIP) program in 2022, with up to $10.5 billion available to support the upgrade and expansion of U.S. electric grids.
Canada | Is investing $100 million through its Green Infrastructure Smart Grid Program to support the development of smart grid technologies and smart integrated systems.
Smart grids

## Slide 98: Renewable energy and EV growth cause volatility in the electricity system; batteries have significantly improved grid stability
Source: NYT, Giant Batteries Are Transforming the Way the U.S. Uses Electricity (2024).
Credit: Xiaodan Zhu, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Observations
  The growth of solar power and electric vehicles has caused instability in the grid:
    During midday, the abundance of solar energy significantly reduces the grid's net load, while peak demand at night requires conventional energy sources to ramp up quickly to meet the demand.
    The increasing adoption of electric vehicles also results in a substantial rise in electricity demand in the evening.
  Integrating batteries into the grid has reduced the frequency and severity of grid instability events, such as blackouts and brownouts:
    Economic benefits include reduced costs associated with grid instability and less frequent need for expensive emergency interventions.
    Public safety improves, as critical services are less likely to be disrupted.
California grid net load in April 2021 vs. 2024 impacted by battery installation, MW
Midday solar abundance
With significant battery integration, the midday solar power excess is absorbed and stored, smoothing out the excess energy spike that used to create the “duck's belly.” This results in a more stable and flattened curve.
Evening peak
Batteries discharge stored energy during the evening peak, reducing the steep rise in demand for conventional power sources. This leads to a less abrupt increase in grid load, stabilizing the grid and minimizing the 'neck' effect seen in the traditional 'duck curve.'
V2G

## Slide 99: EVs could serve as an additional measure against grid instability, providing energy storage capacity through V2G technology
Solutions to reduce grid instability | Description | Effectiveness
Energy storage incentives | Battery storage: Deploy batteries to store excess energy during low demand and supply it during peak demand. Pumped hydro storage: Develop large-scale hydro storage systems to balance supply and demand. | Battery storage: 1,000 MW in California, reducing ramp by 20%. Pumped hydro storage: Large-scale solutions.
Demand response programs | Time-of-use pricing: Encourage consumers to shift usage to off-peak times with variable pricing. Incentives for load shifting: Offer incentives for industrial and commercial users to reduce or shift energy use during peak periods. | Time-of-use pricing: Shifts 15% residential use. Demand response: Reduces peak by 30%.
Grid modernization | Smart grid technologies: Invest in smart meters, grid automation, and real-time monitoring to enhance grid management. Infrastructure upgrades: Strengthen transmission and distribution networks to handle variable energy sources efficiently. | Smart grid tech: Reduces peak by 30%. Flexible infrastructure: Enhances balancing.
Vehicle-to-grid (V2G) | Bidirectional charging: Enable EVs to discharge electricity back into the grid during peak demand times, acting as distributed energy storage. Incentives for V2G: Provide financial incentives for EV owners to participate in V2G programs. | Nuvve Corporation Pilot Programs: In several pilot programs, Nuvve has demonstrated that V2G can reduce peak demand by up to 15% to 20% in participating regions. For instance, a pilot in Denmark showed significant peak shaving during high demand periods. UK Power Networks: A study by UK Power Networks found that V2G could help reduce peak load by 10%, thus delaying the need for grid infrastructure upgrades.
Sources: Nuvve Corporation, Pilot programs; UK Power Networks, TransPower Vehicle to Grid; Governor of California, 10,000 Megawatts of Battery Storage (2024); Brattle Group, Time-of-use rate (2019); DOE, Smart Grid; PNUCC, Northwest Regional Forecast.
Credit: Xiaodan Zhu, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Deep dive next
V2G

## Slide 100
Simple charging | Time-of-use and self consumption |  |  | Demand response participation |  | Backup power, discharge, and self-sufficiency | Full-level grid services Feed energy back into the grid for: Power quality and voltage control Congestion management and curtailment Reserve and frequency services, etc.
 | Load shifting | Peak shaving | Priority charging | Implicit demand response (price signals) | Explicit demand response (control signals) |  | 
Level 0
Level 1 and Level 2
Level 3
Level 4
Grid Compliance | G2V/H1 | V2B/H2 | V2G
Use Cases
1) Grid-to-vehicle/house smart demand response; 2) Vehicle to battery/house.
Source: CRA, Introduction to V2G (2022).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Vehicle-to-grid (V2G) could act as a mobile BESS and play a key role in stabilizing the grid without the need for a grid upgrade
V2G

## Slide 101: V2G could single-handedly satisfy grid storage demand; up to 62 TWh to be unlocked in combination with second-use
 | 6 TWh |  |  |  |  |  |  |  |  | 62 TWh
100% |  |  |  |  |  |  |  |  |  | 
90% |  |  |  |  |  |  |  |  |  | 
80% |  |  |  |  |  |  |  |  |  | 
70% |  |  |  |  |  |  |  |  |  | 
60% |  |  |  |  |  |  |  |  |  | 
50% |  |  |  |  |  |  |  |  |  | 
40% |  |  |  |  |  |  |  |  |  | 
30% |  |  |  |  |  |  |  |  |  | 
20% |  |  |  |  |  |  |  |  |  | 
10% |  |  |  |  |  |  |  |  |  | 
 | 10% | 20% | 30% | 40% | 50% | 60% | 70% | 80% | 90% | 100%
Vehicle-to-grid participation
Second-use utilization rate
Source: Nature, Electric vehicle batteries alone could satisfy short-term grid storage demand by as early as 2030 (2023).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Total actual available capacity under various conditions in STEP-NCX scenario in 2050
Observations
  V2G participations plays a role in determining the real-world capacity for short-term grid storage using EV batteries together with second-use utilization rates.
  When both V2G participation rates and second-use rates are at 50%, the projected real-world capacity reaches between 25 and 48 TWh by 2050 (STEP-NCX scenario).
  For participation rates between 23% and 96%, the impact on capacity ranges from -24% to +21%, respectively. This indicates the impact V2G adoption could have.
  Meeting grid storage demands by 2050 (3.4 to 19.2 TWh) can be done with different combinations of V2G and second-use. Without any second-use batteries in stationary storage, grids would require V2G participation rates of an achievable 12% to 43%.
  Assuming half of second-use batteries are used for grid storage, the required participation rate of V2G drops to below 10%.
2050 grid storage demand
V2G

## Slide 102: Large barriers to widespread adoption and scaling of V2G exist at different stages in the value chain
Source: CRA, Introduction to V2G (2022).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Electric vehicles
Only a few EV models on the market fully V2G-compatible
Messaging from OEM dealerships often unclear.
Power grids
While larger hubs can adopt procedures similar to those for BESS, fewer established processes exist for on-street chargers
Little low-voltage grid visibility and smart meter adoption
EV chargers
V2G chargers have 5x to 10x price premium
Limited compatibility with latest ISO standards
Little availability of V2G-ready AC chargers
Consumers' home
Lack of consumer awareness about V2G
Strict requirements for consumers to participate in V2G, such as the EV needing to remain plugged in at specific times of day
Regulators
Underdeveloped regulations for flexible procurement limit revenue streams available to V2G systems
Regulatory enforcement of V2G standards and protocols is early stage and remains rare
V2G

## Slide 103: The most promising V2G applications are frequency control and load leveling; charging power and efficiency can enhance benefits
Factors influencing the net revenue of V2G business
Player
Application
Technical conditions
Other factors
Chart: 
 | 0 | 580 | 1400 | 940 | 750 | 1400 | 550
0
Energy arbitrage
Charging cost reduction
Load leveling
Peak shaving
Primary response
Secondary response
Tertiary response
1,400
1,400
Relative effects of key factors on net revenue, €
Numbers on the right are regression coefficients from a multivariate model with:
Dependent variable: net revenue (revenue - battery degradation cost)
Independent variables: applications, players, technical conditions, market conditions, control variables
The larger the positive coefficient the independent variable has, the higher the net revenue observed
Chart: 
 | 0 | -30 | 550
0
Grid operator
(30)
Fleet aggregator
Vehicle owner
Chart: 
 | 0 | 1160
0
BEV
PHEV
1,160
Chart: 
 | 0 | 360
0
G2V
V2G
Chart: 
 | 30 | 40 | 840 | -370
30
Charging power
40
Battery capacity
Efficiency round trip
(370)
Depth of discharge
Vehicle tech.
Charging tech.
Others
Key profitability factors
Base case (intercept)
Energy trading
Load control
Frequency control
Source: Renewable and Sustainable Energy Reviews, Factors influencing the economic success of grid-to-vehicle and vehicle-to-grid applications (2021).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Observations
Secondary frequency response and load leveling are expected to be V2G's most beneficial use cases.
Individual vehicle owners seem to generate higher revenues than aggregated fleet operators or grid operators.
  However, grid operators may enjoy additional advantages by counteracting negative impacts from RES generation.
Technical variables will play a crucial role in shaping the vehicle and charging technology:
  A higher charging power enhances the flexibility.
  A higher round-trip efficiency significantly boosts benefits by minimizing the system losses.
  A greater battery capacity has a notable positive effect, as it increases revenue potential and reduces battery degradation by lowering the number of charge cycles required.
The effect of the following variables needs to be further investigated as more data accumulates:
  The number of PEVs in relation to the balancing market size could be a critical factor, as the revenue from both frequency and load control markets decrease with an increasing number of participants in the market.
  Charging locations (e.g., home, work, public charging stations) influence charging timing and thus the suitability for time-sensitive applications.
  More data points are needed for meaningful analysis on the impact of market conditions such as RES share, electricity price, energy archetype, and countries.
  Biased because 85% of PHEV cases are from the U.S., where the average net revenue is the highest.
V2G

## Slide 104: Key regions implementing policies to advance V2G adoption
 | V2G pilot project with EV batteries in North Carolina | Electric school bus effort in Beverly, Massachusetts | Electric school bus powers V2G in Durango, Colorado | New York City government moves to all-electric fleet
Vehicle | Passenger light-duty EVs | Electric school buses (MHD EVs) | Electric school buses (MHD EVs) | Passenger light-duty EVs
Description | Roanoke Cooperative partnered with Fermata Energy to carry out a V2G pilot project in North Carolina. The project looked at the financial value provided by V2G using the batteries in an EV when the vehicle was parked at home and assessed how the EV could contribute power to the grid during periods of high demand and grid strain. | In a V2G pilot carried out by New England utility National Grid during the summer of 2021, an electric school bus was used to provide power to the grid to reduce grid strain during peak demand. The project was an early instance of an electric school bus being used for V2G. | Colorado got its first V2G-compatible electric school bus in 2021 as part of a collaboration between the V2G tech company Nuvve, bus manufacturer Blue Bird, and electricity distribution co-op La Plata Energy Association (LPEA). Durango School District 9-R was also provided with infrastructure to support the bus's use in V2G, like a bidirectional charging station. The district can use the electric bus to pick up students — incurring cheaper fuel costs in the process — as well as to supply energy to the grid. | In 2023, it was announced that all city government vehicles will have to be fully electric by 2038 and its ridesharing vehicles to be zero emission or wheelchair accessible to 2030. To accompany this, NineDot partnered with Revel and Fermata Energy to launch New York City’s first V2G pilot at Revel’s Red Hook warehouse in Brooklyn to assist peak demand for Con Edison.
Key Takeaways | Using V2G in this way allowed Roanoke Cooperative to cut down its electricity consumption during peak usage by an average of around 14 kW. It also produced more than $2,600 a year in savings for the utility. V2G capabilities became a source of back-up power for Roanoke's microgrid, improving resilience during periods when it was operating independently. | The electric school bus was utilized 30 different times that summer, working for more than 50 hours and delivering nearly 3 MWh of electricity to the grid — roughly the amount of electricity used by 100 homes in a day. School buses are an especially good fit for efforts like these because they are often underutilized, especially in the summer, when electricity demand is high. | The Colorado effort was largely funded by a state alternative fuels grant, with additional funding provided by LPEA. In a given afternoon, the bus might charge for a period — powered by extra solar energy — then transport students home from school, before an evening of supplying the grid with energy, helping balance out high electricity demand. | TBD
Sources: Electrification Coalition, Advancing V2G Technology Adoption (2022), Nine Energy, NYC EV charging solutions, NYC Government Vehicles, NYC Ride Share
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Policies in select regions
V2G

## Slide 105
The energy storage opportunity
Mobility energy storage
Utility energy storage
  Technology
  Opportunities and unlocks
  Case study

## Slide 106: Quidnet Energy’s journey from innovation to commercial
 | First foray into novel pumped storage | Department of Energy support of supercharged scaling
Timeline |  | 
Highlights | 2013 – Quidnet is founded with the goal of exploring energy storage using subsurface rock formations. In its initial years, the company refines the concept of geomechanical pumped storage. This novel pumped storage hydropower technique looks to leverage subsurface reservoirs to store energy by pressurizing water underground. 2016 – Quidnet gains momentum after securing seed funding, allowing the company to initiate pilot projects in Texas. 2017 – Breakthrough Energy Ventures leads Quidnet’s Series A funding. 2018 – ARPA-E awards Quidnet $3.3 million grant to continue expanding research and development of geomechanical pumped storage. | 2020 – Quidnet closes a Series B round of $10 million backed by Breakthrough Energy Ventures and Evok Innovations. The funding helps scale operations and secure a contract with the New York State Energy Research and Development Authority (NYSERDA) for a 2MW/2MWh project. 2021– Quidnet receives ARPA-E SCALEUP funding to retire technical risks associated with the deployment of geomechanical pumped storage. 2022 – Quidnet enters into a 15-year commercial agreement with CPS Energy in San Antonio, Texas. The partnership involves deploying a 10Mh system, which becomes its first commercial-scale implementation of geomechanical pumped storage. 2024: Quidnet announces a 300MW partnership with a $10 million investment from Hunt Energy Network.
2013
Formation of Quidnet
Case study: Quidnet
Initial pilot project in Texas
2016
2018
2022
Series A funding
2017
2020
ARPA-E award
SCALEUP
2021
2022
New York State contract
Commercial agreement with CPS Energy
300 MW partnership with Hunt Energy Network
Sources: Quidnet, ARPA-E, Quidnet Energy.
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).

## Slide 107: Natron Energy pioneers the commercialization of SIBs
 | Early battery innovation and market entry | Accelerated research and strategic partnerships | Commercial-scale expansion and industry leadership
Timeline |  |  | 
Highlights | 2012 – Colin Wessells and other researchers from Stanford University found Alveo Energy with the goal of developing sodium-ion battery (SIB) technology using Prussian blue analogs. 2012 – ARPA-E grants Alveo Energy funding through its Grid-Scale Rampable Intermittent Dispatchable Storage (GRIDS) program. | 2017 – The company rebrands from Alveo Energy to Natron Energy to reflect its focus on commercialization of its sodium-ion technology. 2019 – Natron closes strategic investment from Chevron Technology ventures to support the development of stationary energy storage systems for demand-charge management at EV charging stations. 2020 – Colocation provider H5 adds Natron Energy technology for test installation of cooling at its data center campus in Phoenix, Arizona. 2020 – Natron raises $35 million in Series D financing to expand sodium-Ion battery commercialization led by ABB Technology Ventures, NanoDimension Capital, and Volta Energy Technologies. | 2020 – Natron achieves an industry first Underwriters Laboratories (UL) listing of sodium-ion for data center usage. 2022 – Natron and Arxada announce world’s first large-scale production of battery-grade Prussian blue materials. This enables 600 MW of annual production of Natron’s sodium-ion battery products for data center, uninterruptible power supply, and energy storage. 2023 – Natron Energy achieves first-ever commercial-scale production of sodium-ion batteries in the U.S., in Holland, Michigan.
2012
Formation of Alveo Energy
Case study: Natron
ARPA-E GRIDS
2012
2019
Strategic investment from Chevron Technology Ventures
2020
Natron raises Series D to expand
Natron announces first-ever UL-listed sodium-ion battery
2020
First-ever commercial-scale production
2023
World’s first production of battery-grade Prussian blue
2022
Rebrands to Natron Energy
2017
2020
H5 adds Natron Energy technology to campus
Sources: Natron Energy, ARPA-E, Natron Energy.
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).

## Slide 108: World’s largest battery located at Tesla’s Hornsdale Power Reserve
 | The problem and initial engagement | Government response and project planning | Construction, deployment, and impact
Timeline |  |  | 
Highlights | September 2016 – Storms cause significant and sustained statewide blackouts in South Australia. March 2017 – Tesla CEO Elon Musk and Atlassian entrepreneur Mike Cannon-Brookes begin discussing interest in a battery solution to the problem. Musk makes a promise of completion: “100 days from contract signature or its free.” | March 2017 – The South Australian government announces an AUD$550 million energy plan to increase grid reliability that, among other objectives, includes building a 100 MW battery before the 2017/2018 Australian summer. March 2017 – The South Australian government opens a two-stage competitive procurement process for national and international companies interested in constructing the 100 MW battery. July 2017 – The Hornsdale Power Reserve consortium, led by Neoen and using Tesla’s battery equipment, is awarded the contract to build the battery and the project agreement is signed. | September 2017 – The grid connection agreement is signed with ElectraNet, the electricity transmission network operator, and approved by the Australian Energy Market Operator. Musk’s 100-day deadline begins. December 2017 – The battery is constructed and connected to the NEM, ahead of the 100-day promise. December 2017 – The first opportunity for the battery to respond to a grid stabilization issue arises when a coal generator in New South Wales shuts down. The battery responds to the sudden loss of 689 MW of generation within a fraction of a second, faster than any other existing generation technology.
Sept. 2016
Storms start conversation
Case study: Tesla
Musk and Cannon-Brooks discuss plan
March
2017
March
2017
SA government opens procurement
ElectraNet connection signed; timeline starts
Sept.
2017
Battery responds to downed coal generator
Dec.
2017
Battery constructed in under 100 days
Dec.
2017
SA government announces plan
March
2017
July
2017
Hornsdale Power Reserve forms
Sources: Global Infrastructure Hub, Hornsdale Power Reserve Project, Australia (2019).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).

## Slide 109: CKI Energy Storage Team
Birru Pagi Lucha
Master of Science in Sustainability Management
Team Lead
Devashri Mehrotra
Master of Business Administration
CKI Fellow
Xiaodan Zhu
Master of Science in Financial Economics; PhD in Chemical Engineering
CKI Fellow
Hyae Ryung (Helen) Kim
PhD in Sustainable Development
Senior Research Fellow
hk2901@columbia.edu
Gernot Wagner
Senior Lecturer, Columbia Business
School; Faculty Director, Climate Knowledge Initiative
gwagner@columbia.edu
Hassan Riaz
Master of Business Administration
CKI Fellow
Shailesh Mishra
Master of Public Administration in Development Practice
CKI Fellow
Petr Jenicek
Master of Business Administration
CKI Fellow
Attribution: Lucha et al., "Storing Energy," Columbia Business School Climate Knowledge Initiative (4 March 2025).
David Foye
Master of Business Administration
CKI Fellow
Ashley Kim
Master of Business Administration
CKI Fellow
Notes: baps

## Slide 110: Appendix

## Slide 111
  Mobility energy storage – policy scan
  Utility energy storage – policy scan
  Other supporting pages
  Glossary

## Slide 112: EV sales are accelerating with uptake rates ranging across countries; Norway leads with 93% share of EV sales in 2023…
Sources: IES, Global EV Outlook - Policy Explorer (2024); ERI, Countries Adopting EVs (2023); IEA, Global EV Data Explorer (2024).
Credit: Devashri Mehrotra, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Share of EV sales across countries, %
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
 | 0.0065 | 0.03 | 0.034 | 0.16 | 0.2 | 0.15 | 0.26 | 0.42 | 1.2 | 1.1 | 2.8 | 5.1 | 12
 | 0.01 | 0.034 | 0.073 | 0.095 | 0.4 | 1 | 1.5 | 2.4 | 4.7 | 5 | 5.7 | 16 | 29 | 38
 | 0.0049 | 0.052 | 0.11 | 0.23 | 0.45 | 0.73 | 0.74 | 1.6 | 2 | 3 | 14 | 26 | 31 | 24
 | 0.021 | 0.056 | 0.0072 | 0.016 | 0.038 | 0.017 | 0.026 | 0.031 | 0.03 | 0.024 | 0.12 | 0.35 | 1.2 | 2
 | 0.005 | 0.023 | 0.041 | 0.049 | 0.093 | 0.22 | 0.33 | 0.95 | 3.8 | 2.3 | 2.4 | 5.8 | 8.5 | 7.9
 | 0.28 | 1.4 | 3.1 | 5.8 | 15 | 22 | 29 | 39 | 49 | 56 | 75 | 86 | 89 | 93
 | 0.012 | 0.15 | 0.42 | 0.71 | 0.77 | 0.7 | 0.99 | 1.3 | 2.3 | 2.1 | 2.3 | 4.7 | 7.4 | 9.5
 | 0.011 | 0.068 | 0.16 | 0.27 | 0.41 | 0.68 | 0.9 | 1.4 | 2.4 | 2.6 | 4.2 | 8.9 | 14 | 18
12
24
2
93
Australia
China
Germany
India
Korea
Norway
U.S.
World
Observations
EV sales are accelerating at different years for different countries; following a similar S-curve, exponential growth was observed when EV share reached 1%.
Most EV leaders are from high-income countries, where EV growth is supported by government policy and financial incentives, enabling the cost of EV to fall.
Norway is currently leading with >90% share of EV sales, while China is the biggest EV player.
Norway’s key success factors are:
EV incentives: Tax breaks for EV users include purchase tax and VAT exemption as well as local incentives (e.g., tolls and parking discount)
EV charging incentives results in a total of 34,000 charging points as of 2023

## Slide 113: …supported by government incentives across the EV ecosystem
 | U.S. | EU | China | India
Main policy focus | Incentivize industry to boost domestic growth in EV ecosystem | Enable faster permitting, financial support, enhanced skills, and open trade for net zero projects | A plan to reach carbon peaking before 2030 sets a target for the sales share of NEVs to reach around 40% by 2030 | Incentivize industry to boost local manufacturing of EVs and related infrastructure
Main policies | Inflation Reduction Act (IRA) | Green Deal Industrial Plan Fit for 55 package | 2030 Carbon Peak Action Plan | Production-linked incentive (PLI)
Raw material extraction | No specific policies | Critical Raw Material Act (proposal) to ensure security of supply, extraction, and environmental standards | No specific policies | No specific policies
Battery and EV manufacturing | Tax credits on capital and production cost | Net Zero Industry Act (proposal) to scale up manufacturing of clean technologies, including batteries | Subsidies and tax break | Advanced chemistry cell PLIs to reach a cumulative 50 GWh in domestic manufacturing capacity by 2030
EV sales | Clean vehicle tax credit for EV purchases that meet certain requirements (e.g., % of locally processed material) | Sustainable and Smart Mobility Strategy to achieve 30 million passenger ZEV stock by 2030 and nearly all passenger LDV and HDV stock by 2050 | Subsidies and tax break for EV producers and consumers; market-based zero-emission vehicle credit system to replace direct subsidies | Automobile and auto component PLIs to incentivize sales of BEV and FCEV and respective components
Charging infrastructure | Alternative fuel infrastructure tax credit for EV charging, including bidirection charging | Alternative Fuels Infrastructure Regulation to ensure minimum coverage of publicly accessible recharging points for LDVs and HDVs | 14th Five-Year Plan targets to achieve high-quality charging infrastructure system by 2030 | FAME Scheme Phase II targets an additional 7,432 public fast-charging stations by 2024
Battery recycle | No specific policies | EU Batteries Regulation mandates that new batteries meet minimum recycled content requirement | Circular Economy Promotion Law mandates extended producer responsibility (EPR), including battery manufacturers to recycle the products | Battery Waste Management Rules (2022) based on EPR concept
1
2
3
4
Observations
Despite shared goals, each country has distinct approaches; the U.S., China, and India are heavy on incentivizing EV growth and battery manufacturing.
The U.S. IRA is a strategic catalyst to boost giga factory developments, due to its significant gap vs. the EU’s incentive program.
The EU is the only region with explicit policies addressing the security of the raw material supply for EV batteries. This reflects Europe's desire to reduce dependence on foreign sources and ensure sustainable procurement.
China and India have an ambitious target for developing charging infrastructures, a key to increased EV adoption rates.
Sources: IEA, Global EV Outlook – Policy Developments (2023); IEA, Global EV Outlook - Policy Explorer (2024); EU Commission, Compass to boost EU competitiveness; CGEP, IRA and the US Battery Supply Chain (2023); DOE, Tax Credits.
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Policy overview across select countries/region

## Slide 114: EU policies have addressed entire EV ecosystem, but incentives vary across member states
European Union
Focus areas | Policy details | Examples by countries
Raw material extraction | Critical Raw Materials Act (2023 proposal) focuses on: Strategic critical raw mineral application A network of European agencies to anticipate supply risks A resilient supply chain, e.g., 30% of the EU's demand for refined lithium should originate from the EU by 2030, or to recover at least 20% of the rare earth elements by 2030 | Spain: Government awards €18.8 million for the construction of Extremadura New Energies’ lithium hydroxide plant, located next to the mining site. It reinforced the country’s ambition to maintain a leading position in the EU for the development of EV supply chain from locally available critical raw materials.
Battery and EV manufacturing | Net Zero Industry Act (2023 proposal): EU battery manufacturers to meet 90% of EU demand, with a combined capacity of at least 550 GWh by 2030, in line with European Battery Alliance objectives | Germany and France: Subsidies from Important Projects of Common European Interest (IPCEI) for select projects, such as Automotive Cells Company (ACC), Verkor, and Northvolt factories
EV sales | Sustainable and Smart Mobility Strategy to achieve 30 million passenger ZEV stock by 2030 and nearly all passenger LDV and HDV stock by 2050 | Netherlands: Tax exemption for zero-emission cars Sweden: Low annual road tax for zero-emission vehicles Belgium: €5,000 premium for a new zero-emission car purchased by retail customers
Charging infrastructure | Alternative Fuels Infrastructure Regulation, under which member states must ensure: Publicly accessible recharging stations are set up in proportion to the number of registered vehicles Adequate deployment of recharging stations along the trans-European transport network road network Sufficient coverage of recharging points for HDVs | Norway: Grant up to 20% of charging point purchases and installation cost Sweden: Grant up to 50% cost of residential charging points installation Belgium: 100% deductible for charging installation accessible to public 15% tax reduction for private owners for mono- and bidirectional charging installation
Battery recycling | EU Batteries Regulation mandates that new batteries meet the minimum recycled content requirement by 2030: Recycling target of 80% for lead-acid and 70% for Li-ion Material recovery target of 95% for cobalt, copper, lead, and nickel and 70% for lithium | Germany: Waste Management Act, which turns a waste management culture into a resource management culture, minimizing waste generation and maximizing reuse and recycling
Detailed EU policies across EV ecosystem
Sources: IEA, Global EV Outlook – Policy Developments (2023); IEA, Global EV Outlook - Policy Explorer (2024); EU Commission, Compass to boost EU competitiveness; CGEP, IRA and the US Battery Supply Chain (2023); DOE, Tax Credits.
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).

## Slide 115: Norway, an early EV adopter, has prioritized EV and charging incentives, though its battery value chain is still emerging
European Union
Norway EV sales share, %
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
 | 0.28 | 1.4 | 3.1 | 5.8 | 15 | 22 | 29 | 39 | 49 | 56 | 75 | 86 | 89 | 93
56%
1990-2010: Government gradually rolls out tax breaks and other benefits for EV buyers
2012: EVs become cheaper to own over lifetime than ICE vehicles when including tax breaks
2013: Country has more public EV chargers per capita than any other country
2017: New target for all new car sales to be zero-emissions by 2025
2021: EVs become cheaper to buy vs. ICE, including tax breaks; some incentives begin to phase out
2022: Norway has 2.5x more public fast chargers per capita than any other country
Launched its Roadmap for a Green Industrial Initiative, highlighting the battery value chain as a priority area
Sources: IEA, Global EV Outlook - Policy Explorer (2024); WRI, Countries Adopting EVs (2023); IEA, Global EV Data Explorer (2024); Wallbox, Norway’s Unique EV And EV Chargers Perks; Norwegian Ministry of Trade, Industry and Fisheries, Norway’s battery strategy (2022).
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Observations
Norway has shown that replacing ICE vehicles with EVs is achievable, with the total cost of ownership for EVs now lower, supported by tax breaks and high taxes on ICE vehicles to internalize carbon costs.
Key success factors for Norway to lead global EV adoption rates:
  EV incentives offer considerable tax breaks for EV users:
      National tax benefits include exemption from purchase tax and VAT, no road traffic insurance tax, and company car tax discount.
      Local incentives include half-price tolls, half-price parking, and the flexibility to use bus and taxi lanes.
  EV charging incentives have resulted in a total of 34,000 charging points as of 2023.
Norwegian industry has recently begun consolidating its battery value chain initiatives through various joint projects, including the construction of a giga factory.

## Slide 116: China’s EV growth mainly supported by direct subsidies and massive expansion of fast-charging networks
China EV sales share, %
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
 | 0.01 | 0.034 | 0.073 | 0.095 | 0.4 | 1 | 1.5 | 2.4 | 4.7 | 5 | 5.7 | 16 | 29 | 38
China’s key success factors:
EV and battery manufacturing: Financial and tax breaks with a total of $29 billion in subsidies from the government
EV sales:
  Financial and tax breaks for both EV producers and consumers since 2009
  Since 2018, direct subsidies have been gradually replaced with market-based zero-emission vehicle credit system for Corporate Average Fuel Consumption (CAFC) and new energy vehicle (NEV) in light-duty vehicles
Charging infrastructure:
  Massive expansion on fast charging drives EV growth; China has installed 760,000 public fast-charging points and 1 million public slow-charging points, more than ROW combined
  Promote 10,000 battery swapping-enabled EVs with 1,000 swapping stations before 2025
In addition, China has been proactively acquiring raw material extraction from local and international resources, controlling more than 80% of global raw material refining capacity for battery production and 75% of the battery cell market.
In battery recycling, China has established a closed-loop system in which battery manufacturers bear the primary responsibility for recycling old batteries, and established a network of recycling service centers, supported by a government platform for battery tracing.
2009-2010:
EV financial subsidies begin piloting in cities
2016:
Major expansion of EV fast chargers begins
2018:
EVs start to become cheaper than gas vehicles when including financial incentives
Zero-emission vehicle credit policy launches to replace direct subsidies
2020:
National EV subsidy phaseout postponed due to COVID-19
2021:
EV sales surge as more than a decade of pro-EV policies culminate
2022:
China’s BYD Co. sells 1.85 million EVs, has become the world’s second-largest EV manufacturer
Sources: IEA, Global EV Outlook - Policy Explorer (2024); WRI, Countries Adopting EVs (2023); IEA, Global EV Data Explorer (2024); MIT Technology Review, How did China come to dominate the world of electric cars? (2023); Berkeley Law, China dual credit policy brief (2022); IFC, PLI Scheme on EV Manufacturing in India (2024).
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
2023:
Tax break package rolls out over four years for EVs purchased from 2024 to 2027 to boost slower EV growth
China’s EV ecosystem has grown rapidly as the country aims to reach NEV sales share of around 40% by 2030…
…supported by incentives, tax breaks, and a strategic push to dominate EV, battery production
China

## Slide 117: India heavily incentivizing EV ecosystem to boost growth in EV supply chain through Production Linked Incentive scheme
India
Sources: IEA, Global EV Outlook - Policy Explorer (2024); IFC, PLI Scheme on EV Manufacturing in India (2024).
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
India has an aggressive target to grow its EV ecosystem…
…with a total of ~$ 7 billion in incentives allocated to support the industry
EV market growth target
Battery industry growth target
Composition of the EV market, % share
Battery industry capacity, GWh
Chart: 
 | 85 | 100
 | 5 | 100
 | 7 | 65
 | 1 | 15
2023
2030
85%-90%
5-7%
7-9%
1%
100%
100%
65%
15%
2W
3W
Buses
Passenger vehicles
Chart: 
 | 20 | 220
2023
2030
India still in early stage in battery value chain, mainly involved in battery packing and still reliant on imports from China, Taiwan, and EU
India’s previous policy and incentives (a total of ~$ 1.7 billion) have played a crucial role in fostering the EV industry in India. They include:
FAME (Faster Adoption and Manufacturing of Hybrid and Electric Vehicles), which focuses on lowering car costs, promoting R&D, and constructing charging infrastructure
GUTS (Green Urban Transport Scheme), which aims to reduce air pollution by switching to eco-friendly public transport
However, those policies emphasize primarily consumer incentives and market growth, with inadequate focus on addressing supply chain challenges. Hence, the country launched its Production Linked Incentive (PLI) in 2022 to bridge the supply chain gaps:
First scheme (auto initiative) to promote advanced automotive technology products:
  Allocated a ~$ 3 billion budget spanning five fiscal years (since 2022)
  Successfully raised a total investment of ~$ 9 billion in 2022
Second scheme to set up manufacturing facilities for advanced chemistry cells:
  Allocated ~$ 2 billion budget over a two-year span (since 2023) before introducing the next scheme, which will span a five-year period (until 2029)
In addition, India has the disadvantage of mineral import dependence for battery production, due to a lack of national reserves. As such, the country is turning inward to capitalize on the untapped potential of battery recycling and mineral conservation to achieve self-sufficiency.

## Slide 118
  Mobility energy storage – policy scan
  Utility energy storage – policy scan
  Other supporting pages
  Glossary

## Slide 119: EU, U.S., and China at the forefront of solar and wind, but gaps remain in stationary energy storage capacity…
Share of solar and wind in total electricity mix for select countries, %
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
 | 0.15691 | 0.19639 | 0.27866 | 0.29762 | 0.36543 | 0.44246 | 0.65018 | 0.83398 | 1.3229 | 1.8323 | 2.2631 | 2.9215 | 3.5441 | 4.3095 | 4.8304 | 5.2958 | 6.4739 | 7.6574 | 8.1029 | 9.0095 | 10.8249 | 12.2097 | 13.933
 | 0.60887 | 0.72043 | 0.9701 | 1.1688 | 1.5245 | 1.8122 | 2.1072 | 2.6609 | 3.113 | 3.7967 | 4.2714 | 5.7209 | 6.9354 | 8.161 | 9.0879 | 10.5469 | 10.6476 | 12.2691 | 12.9916 | 14.9916 | 17.4044 | 16.9451 | 20.194
 | 0.046985 | 0.052669 | 0.055678 | 0.057726 | 0.063898 | 0.084464 | 0.13828 | 0.17746 | 0.43124 | 0.73159 | 1.0771 | 1.5467 | 2.0492 | 2.8762 | 3.1546 | 3.8484 | 4.8971 | 6.1818 | 7.6062 | 8.4148 | 9.3841 | 11.456 | 13.3176
 | 0.30033 | 0.38681 | 0.44627 | 0.56095 | 0.66497 | 0.87719 | 1.2727 | 1.4436 | 1.6446 | 2.0676 | 2.0274 | 2.4492 | 2.907 | 3.1517 | 3.2763 | 3.3494 | 4.6862 | 5.3854 | 6.5929 | 7.4297 | 8.417 | 9.2292 | 10.2231
 | 0.043454 | 0.07608 | 0.098965 | 0.15951 | 0.22298 | 0.28598 | 0.34943 | 0.40163 | 0.46443 | 0.57489 | 0.64559 | 0.85666 | 1.042 | 1.6361 | 2.6181 | 3.8146 | 4.8501 | 5.6967 | 6.5753 | 7.4142 | 8.6592 | 9.0974 | 10.0049
 | 0.21045 | 0.25669 | 0.33744 | 0.3978 | 0.49873 | 0.5912 | 0.73 | 0.90122 | 1.1565 | 1.4789 | 1.7399 | 2.2588 | 2.7558 | 3.3739 | 3.7991 | 4.4614 | 5.153 | 6.1009 | 6.8806 | 7.8433 | 9.056 | 10.1345 | 11.7114
14%
20%
13%
10%
10%
12%
Sources: IEA electricy mix China; IEA electricity mix EU; IEA electricity mix U.S.; IEA electricity mix India; IEA electricity mix Japan; Ember Climate (2021); Wind Exchange (2024); EIA (2024); Energy EC EU; S&P Global (2024); GlobalData (2023); Renewables Now (2024); PV Magazine (2023); China Daily (2024); IEEFA (2023); TERI (2023); Wikipedia; Mercom India (2024).
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
U.S.
EU
China
India
Japan
World
EU, U.S., and China are leading in growing solar and wind power generation
Observations
Growth projection:
The EU, U.S., and China have a 60% share of global solar and wind capacity.
China has been scaling up rapidly, with 37% p.a. capacity growth for solar and wind, the fastest rate among the other leading countries.
Current gaps:
The EU, U.S., and China have significant capacity gaps between solar and wind vs. energy storage, highlighting the need for more storage solutions.
China leads in solar and wind with 1,050 GW, but its energy storage capacity remains at only 85 GW.
The U.S. and EU show a more balanced growth in solar, wind, and storage capacity, yet gaps persist.
India and Japan trail with smaller storage capacities, underscoring a need for further development.
Energy storage is growing, but significant capacity gaps remain
12%
x
% annual capacity growth from 2017-2022 (average)
18%
37%
23%
28%
13%
Chart: 
 | 250 | 553 | 1049.5 | 111.48 | 95.2
 | 38 | 40 | 85.44 | 4.76 | 30
U.S.
EU
China
India
Japan
1,050
Solar + wind
Stationary energy storage
Installed capacity of solar and wind vs. stationary energy storage in 2023, GW

## Slide 120: …requiring strong government supports through policy and incentives to drive investments
Sources: IEA (2024); U.S. RPS (2021); FERC Order (2018); Net-Zero Industry Act (2023); RE Directive (2023); EU Green Deal (2019); MoP (2023); MoP (2024); MoP (2022); Apko Worldwide (2024); IHA (2024); BNEF (2024).
Credit: Shailesh Mishra, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Observation:
Add the significance of energy storage
Add the key highlight from each country
 | U.S. | EU | China | India | Japan
Main policy focus | Renewable energy expansion Grid reliability and innovation in energy storage | Renewable energy expansion Circular energy system | Renewable energy expansion Large-scale deployment and technological advancement | Renewable energy expansion Grid stability and renewable integration | Renewable energy expansion Grid stability
Key policies (related to energy storage) | Renewables Portfolio Standards (RPS, 2021) FERC Order 841 (2018): Integrates storage into wholesale markets American Energy Innovation Act (2020): Framework for energy innovation, including storage Investment Tax Credit | Net-Zero Industry Act (2023): Simplifies the regulatory framework for net-zero technologies Renewable Energy Directive (2021, 2023): Sets binding targets for renewable energy and storage integration EU Green Deal (2019): Comprehensive plan for decarbonization | 14th Five-Year Plan (2021-2025): Targets 30 GW of non-hydro energy storage by 2025 New Energy Storage Implementation Plan: Aims for 100 GW by 2030 National Development and Reform Commission (NDRC) Energy Regulation (2021) | National Framework for Promoting Energy Storage Systems (2023) Viability Gap Funding (VGF) scheme for BESS (2024) Energy Storage Obligation (ESO) and Renewable Purchase Obligation (RPO) framework (2022) | Renewable Energy Act Act on Special Measures Concerning Procurement of Electricity from Renewable Energy Sources by Electricity Utilities (2022), for standalone BESS business
Key incentive programs (non-exhaustive) | ITC: 30% credit for standalone ES projects Federal loan guarantees: Up to 80% of project costs for ES projects Self-Generation Incentive Program (SGIP) in California for residential DOE Energy Storage Grand Challenge for energy storage R&D | Horizon Europe funding for R&D ($105 billion) European Regional Development Fund (ERDF) ($220 billion) Feed-in tariffs (FiTs) capacity market payments EU Innovation Fund: $11 billion | Cost reduction target: 30% cost reduction in storage by 2025 Additional provincial subsidies and incentives for storage projects $93.9 billion investment in new-type energy storage by 2032 | Production Link Incentive (PLI) scheme: ~$2.18 billion over five years, by FY28-29 VGF: Up to 40% of capital cost for BESS projects Transmission charge waivers: 25 years for hydro PSP or 12 years for BESS | Green Innovation Fund: ~$14 billion Tax incentive of ~$12 billion in 10 years Transition finance: $1.05 trillion in public-private investments by 2030, supporting battery production and storage technologies
Observations
U.S.: Leading in market integration (FERC Order 841), with significant federal incentives for storage (ITC, SGIP)
EU: Strong regulatory framework for net-zero technologies
China: Focused on large-scale deployment and cost reduction strategies
India: Leading in financing mechanisms for storage through its PLI scheme and VGF for BESS
Japan: Strong incentives for innovation through the Green Innovation Fund and support for large-scale energy storage transition projects
Policy overview across select countries/regions

## Slide 121: California, New York, and Massachusetts are leading states in advancing storage and reintegration
United States
States have put in place significant policies and incentives to boost renewables and achieve their renewables mandates
U.S. is projected to increase energy storage capacity by 7x (2027 vs. 2023)
State | Renewables mandate | Storage target | Financial incentives
California | 60% by 2030, 100% clean energy by 2045 | 1,325 MW by 2020 | ~$450 million consumer rebate in 2019 $830 million rebate for behind-the-meter technologies by 2026
New York | 50% by 2030 | 1.5 GW by 2025 6 GW by 2030 (3 GW bulk storage) | $35 million in incentive and $200 million fund to provide loans $15.5 million funding from NYSERDA
Massachusetts | 35% by 2030 | 1 GWh by 2025 | ~ $20 million in grants for 26 energy storage projects
Maryland | 50% by 2030 | 5 MW by 2022 | Tax credits for energy storage systems: $5,000 for residential and up to $75,000 for commercial applicants
Nevada | 50% by 2030 | 590 MW by 2023 | Low-Income Solar Program: $1 million per year until 2023 EV and other ESS: $15 million in total
Oregon | 25% by 2025 | Established storage mandates | $2 million earmarked for rebates Capped at $2,500 for residential ESS and $15,000 for low-income service providers
Hawaii | 100% by 2045 | Included in RE goals ~2.3 GWh by 2045 | Through state and federal programs, exact numbers not specified
Sources: NYSERDA; NY policy; State policies; IEA (2024); BNEF (2024); IEA (2024a); IEA Mid-Year (2024); Rhodium Group (2024); IEA U.S. (2024); EIA (2024; World hydropower outlook (2024).
Credit: Shailesh Mishra, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 38 | 75
2023 (actual)
2027 (projected)
U.S. energy storage capacity (battery and PSH), GW
Even share between PSH and battery; ~40% of total battery capacity in California

## Slide 122: EU aims to increase utility-scale energy storage by 5x from 2023 to 2030; UK and Italy lead investments
European Union
Chart: 
 | 38 | 187
2023 (actual)
2030 (projection)
~40
190-200
EU targets significant growth by 2030
Sources: REN (2024); EASE (2022); Eco Affect (2024); ITA (2024); EnergyTrend (2024); EY Renewable Energy Country Attractiveness Index (2024); Energy Storage news (2024).
Credit: Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
UK and Italy lead the investment pipeline, backed by strong government support
Chart: 
 | 3.5 | 30
Chart: 
 | 3 | 15
2023 (actual)
2030 (projection)
15-20
The UK has launched multipronged policy support to boost investment for LDES:
As of 2023, the UK has 80 GW planned capacity in project pipelines; it is the largest deployer in the EU.
Sophisticated energy market design includes a well-established and diverse revenue stack for BESS. Upgrades to the National Grid ESO’s Open Balancing Platform supports the bulk dispatch of battery storage in real time.
A new energy bill classes BESS as a generation asset, easing rules around construction and offering specific tariff structures.
The government is committing £20 billion to establishing a world-leading battery industry by 2030.
A new Cap & Floor scheme is being introduced to attract private investment, ensuring achievable minimum returns for various types of technology (PSH, batteries, CAES, etc).
Residential installations face slower growth, while utility-scale projects show promise:
Residential:
  In 2023, residential energy storage dominates the country’s energy storage landscape.
  Italy introduced Superbonus in 2020, a tax credit program for residential PV and battery storage system installation, along with net metering policy.
  However, a recent reduction in the tax credit has impacted the growth in this space.
Utility scale:
  The utility-scale sector is still in its infancy and suffers from regulatory uncertainties, supply difficulties, and increasing costs.
  To boost the scale, Italy will aid the investment in the BESS facility for over £17 billion in the next 10 years.
  The new storage capacity will be acquired through tenders published by Terna, with a target of a 12 to 15 GW capacity addition by 2030. The aim is to create a centralized electricity storage system to support the integration of renewable energy into the Italian power grid.
EU utility-scale energy storage capacity, GW
Italy
United Kingdom

## Slide 123: China’s 14th Five-Year Plan for stationary energy storage targets broad development in a variety of technologies
China
 | Strategy | Overview | Targets | Examples
Hydro energy storage | Accelerate capacity growth | With a large existing base of over 480 GW, hydro energy storage synergizes well with existing hydro capacity. | 120 GW by 2030 (current capacity: 32 GW) | World’s largest pumped storage system at 3.6 GW, Fengning Pumped Storage system commences operations in 2024.
Battery energy storage | Accelerate capacity growth | China has long dominated the lithium battery supply chain and is setting its sights on applications in utility energy storage. | 100 GW by 2030 (current capacity: 10 GW) | “World’s first” large-scale semi-solid BESS connects to grid in China with 100 MW in capacity in 2024.
Compressed air storage | Promote innovation | As this is a more nascent technology, China has supported partnerships with Tsinghua University to promote R&D in the field. | No specific targets found at this time | China's first salt cavern compressed air energy storage starts operation in 2022.
Thermal energy storage | Promote further development with solar/wind projects | With existing solar utility projects developing, there is policy incentive to combine utility-scale solar projects with thermal energy storage. | No specific targets found at this time | 30+ CSP, with thermal energy projects under construction in Qinghai and Gansu provinces, totaling over 2.5 GW.
$13.9 billion
Investment recorded from 2021-2023
$93.9 billion
Current market size in 2023
Chart: 
 | 3.1 | 9
 | 52 | 120
 | 34.5 | 100
3
2022
9
2030
90
229
Sources: ChinaDaily (2024); PAMIR (2024); Apco Worldwide (2023); CarbonBrief (2024).
Credit: Hassan Riaz, Shailesh Mishra, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
…with a massive investment to achieve its target of ~230 MW capacity by 2030
Battery
PSH
Other
China’s policy focuses on the transition to clean energy sources, emphasizing new-type energy storage systems…
Forecasted growth of utility-scale energy storage in China to 2030, GW
18.9% CAGR
Forecasted growth from 2023 to 2030

## Slide 124: India poised to achieve its 2030 renewable energy targets, with energy storage playing a critical role
India
 | Policy name | Target | Policy details | Financial incentives
Overall energy storage | National Framework for Promoting Energy Storage Systems, MoP (2023) Waiver of Inter-State Transmission Charges, MoP (2021) | 50 GW by 2030 Supports transmission of RE paired with storage systems | Integration of energy storage across the energy value chain, including both grid-scale and distributed energy storage systems Waiver of interstate transmission charges for solar, wind, hydro PSP, and BESS projects commissioned by June 2025 | Fiscal incentives, subsidies, and support for R&D ~40% VGF to initial BESS projects; must be completed within 18 to 24 months Waiver applicable for 25 years for hydro PSP or 12 years from commissioning for BESS
Battery development | Production Linked Incentive (PLI) scheme on battery storage, MoHI (2021) VGF for BESS, MoP (2024) | Not specified 4,000 MWh of BESS by 2025-26 | Focus on scaling up local production capacities for various battery technologies to reduce dependency on imports VGF up to 40% of the capital cost for BESS projects, targeting grid stability and renewable energy integration | ~$2.18 billion in five years, by FY 2028-29 Firms setting up >5 GWh of advanced chemistry cell manufacturing Total outlay of $1.13 billion, including $451.51 million in budgetary support, with disbursements in five tranches
PSH development | Guidelines to Promote Development of Pumped Storage Projects (PSP), MoP (2023a) | Not specified, PSH to support 500 GW RE by 2030 | Encourages the development of pumped storage projects as critical for grid balancing and RE integration | Subsidies, low-interest loans, and waivers to reduce development costs
Others | RPO and ESO, MoP (2022) | RPO ~43.33% and ESO ~4% by FY 2029-30 | Obligates DISCOMs to procure power from renewable sources, including energy storage | Trading in RECs to meet RPO/ESO obligations
India has established various incentives to promote BESS and PSH development to support the transmission of renewable energy in the country
Sources: MoP (2023); MoHI (2021); MoP (2023a); MoEFCC (2022); MoP (2024); MoP (2022); MoP (2021); Rose et al. (2020); PIB.gov (2022).
Credit: Shailesh Mishra, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Note: VGF = viability gap funding, RPO = renewable purchase obligation, ESO = energy storage obligation, DISCOM = distribution companies
Targeting over 70 GW utility energy storage capacity by 2030
Chart: 
 | 4.7 | 27
 | 0.1 | 47
0.1
2023 (actual)
2030 (projected)
4.8
74.0
4.7
47.0
27.0
Battery
PSH

## Slide 125: Japan energy storage development is lagging; recent government incentives aim to achieve 60 GW capacity by 2030
Japan
 | Policy name | Target | Policy details | Financial incentives
Overall energy storage | Green Growth Strategy (2021) | Achieve carbon neutrality by 2050 Integrate 100 GW of renewable energy by 2030 | Promotes RE integration and battery storage, supports smart grids and emphasizes hydrogen, ammonia, and next-gen nuclear | Green Innovation Fund: $13.66 billion over 10 years to leverage $102 billion of private R&D and investment. Tax incentive of $11.64 billion over 10 years
Energy storage development | Battery Industry Strategy (2022) | 750 GWh battery manufacturing capacity by 2030, 100% domestic battery recycling by 2030 | Focus on domestic manufacturing and recycling: EV and stationary batteries Advance all-solid-state battery technologies | Government funding for large-scale manufacturing infrastructure, tax incentives for R&D, and capital investments; numerical value not specified
 | 6th Strategic Energy Plan (METI, 2021a) | 36%-38% renewable energy share by 2030 10 GW of BESS and 50 GW of PSH capacity by 2030 | Supports the integration of energy storage for grid stability Enables advanced battery technologies for distributed systems | FIT and FIP incentives for renewable energy and storage projects Significant investments in grid reinforcement
Others | Japan’s Green Transformation (GX) Plan (2023) | 10 GW of offshore wind 104-118 GW solar capacity by 2030 | Promotes decarbonization strategies with energy storage for renewable energy and industrial applications | Transition finance: $1.05 trillion in public-private investments by 2030, including support for battery production and storage technologies
Most recent incentive schemes are set to boost renewables and battery storage growth
Aims to grow its storage capacity to 60 GW by 2030; ~$50 billion in investments are underway
Sources: METI (2022); MoFA (2021); METI (2021a); Green Transformation (2023); EIA (2024); IEA (2021); BNEF (2024); IEA Mid-Year (2024); Rhodium Group (2024); Power Technology (2023); World Hydropower Outlook (2024); BNEF (2024).
Credit: Shailesh Mishra, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 27.5 | 50
 | 2 | 10
2
2023 (actual)
2027 (projected)
30
60
Japan’s energy storage capacity (battery and PSH), GW
Battery
PSH

## Slide 126
  Mobility energy storage – policy scan
  Utility energy storage – policy scan
  Other supporting pages
  Glossary

## Slide 127: Material content in different anodes and cathodes
Source: IEA, Global EV Outlook (2023).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).

## Slide 128: Costs of cathode active materials by technology, 2022-2023 ($/kWh)
Source: S&P Global, Lower lithium prices support adoption of lithium-rich EV batteries (2024).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
BACK

## Slide 129: Sankey diagram for global flows of lithium
Source: Nature, Electric vehicle battery chemistry affects supply chain disruption vulnerabilities (2024).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
BACK

## Slide 130: LiSB polysulfide shuffle effect
Source: Nature, Recent advancements and challenges in deploying lithium sulfur batteries as economical energy storage devices (2023).
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
BACK

## Slide 131: In China, state support is driving force behind completion of Fengning pumped storage power station
Observations
China has set a new global benchmark with the completion of its Fengning Pumped Storage Power Station, the largest of its kind in the world.
Located in Hebei province, this facility has a total installed capacity of 3.6 GW and is operated by the State Grid Corporation of China.
State support enables China to overcome infrastructural, financial, regulatory, and environmental barriers, driving projects like the Fengning station to successful completion
The project reached completion on August 11, 2024, with the operation of the 12th and final reversible turbine unit.
Construction on the station began in June 2013, with Gezhouba Group securing the main construction contract in April 2014.
The project was built in two phases, each involving six 300 MW reversible pump turbine units.
The Fengning plant now surpasses the Bath County project in the U.S. as the largest pumped hydro station worldwide in terms of capacity.
With the Fenining station now online, China is on track to expand its pumped storage capacity to 80 GW by 2027.
Source: IHA, China's Fengning Station (2024); GEM, Led by China, Eastern Asia can meet key target for pumped storage (2023).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 51 | 51 | 55 | 65 | 74 | 80 | 90 | 101 | 114
 | 4 | 10 | 9 | 6 | 10 | 11 | 13 | 5
Operating
4
2023
10
2024
9
2025
6
2026
10
2027
2028
2029
5
2030
Chart: 
 | 4.125 | 95.875
Fengning PSPS
China’s 2027 PSH goal
China’s PSH capacity increases by year, GW
PSH

## Slide 132: Wider deployment of pumped storage hydropower (PSH) faces technical and socioeconomic barriers
Technical and environmental barriers to deployment |  | Socioeconomic barriers to deployment | 
Lacking infrastructure | The foremost barrier in reviewed studies. Absence of roads and transmission lines prevents access to cheap surplus power, creating a technical barrier that delays development. | Project investment | The foremost socioeconomic barrier. Complex financial hurdles include capital costs, operation and maintenance costs, payback period, and other economic parameters. Additionally, the payback period is considered another hurdle, as it requires at least 2.5 to 5.5 years to repay loans.
Landscape topology | Decides the type, height (head or elevation), slope, and shape of a dam, the head-to-length ratios, and the amount of earthwork required to built it. | Public opposition | Public acceptance, lack of awareness, “not in my backyard” syndrome, business impact, forced displacement, construction time complaints, and scattered settlement issues, among other issues.
Land acquisition challenges | Land use, vegetation clearing, and land ownership among environmental complications that affect pumped hydro development. | Institutional challenges | Absence of legal frameworks, lack of decision-making, and lack of coordination among participating institutions.
Water Issues | Water availability, water quality, water loss, conflict of interest with the local water supply (for open loop), loss of oxygen, and other hydrological effects. | Political government interference | Government lobbying, bureaucratic drag, and corruption.
Biodiversity loss | Environmental impacts on birds and fisheries as well as temperature changes and soil erosion. | Market failures | State-controlled energy sector, market rule uncertainties, and a lack of skilled labor.
Geological faults | Geological constraints such as active faults, large-scale faults and fracture zones and the presence of permeable bedrock should be considered as they may increase overall construction time | Sponsorship | Very rarely do organizations or private investors agree to finance such long-term projects due to licensing timeframe uncertainties or long backpack periods. A study found most PSH systems in operation are financed under public sector ownership
Source: Cleaner Engineering and Technology, Drivers and barriers to the deployment of pumped hydro energy storage applications (2021).
Credit: Shailesh Mishra, Petr Jenicek, Birru Lucha, Hyae Ryung Kim & Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
PSH

## Slide 133: Strategic financial structuring and operational insights: Kurukutti PSH Project
Sources: TATA, Techno-Commercial Feasibility Report (2020); TERI.
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Parameter | Planned value
Basic project cost (including FC) | 4377.00 Rs. in crores
Indirect cost (IDC) | 531.00 Rs. in crores
Power component (total cost including IDC and FC) | 4908.00 Rs. in crores
Debt | 3435.60 Rs. in crores
Equity | 1472.40 Rs. in crores
Debt: Equity ratio | 30%
Rate of O&M charges | 3.50%
Annual increment in O&M charges | 4.77%
Spares (15% of O&M charges) | 15.00%
Interest on working capital | 10.00%
Rate return on equity | 21.71%
Rate of depreciation | 5.28%
Discounting rate | 10.00%
Input energy | 3338 Mu
Annual energy generation | 2527 Mu
Aux. consumption | 1.20%
Weighted average rate of interest | 10%
Plant useful life | 40 years
Observations
Kurukutti PSH is a project developed by Adani Green Energy for the Andhra Pradesh region.
Per the feasibility report, the proposed Kurukutti PSH plant envisions recycling stored water between upper and lower reservoirs and having to fill the reservoirs only once in their lifetime.
Kurukutti PSH envisions a scheme to generate 1200 MW of peak power on weekdays.
Project is expected to be completed by 2028.
PSH

## Slide 134: Novel PSH technologies currently in development (1/4)
 | Small PSH with reservoirs of corrugated steel and floating membranes | PSH using submersible pump turbines and motor generators | Geomechanical PSH
Description | Creation of a closed-loop system using corrugated steel for the upper reservoir and a floating membrane reservoir in a larger body of water | Use of submersible pump turbines and motor generators, both in a vertical shaft, to eliminate the need to construct a powerhouse | Water pumped down into the ground between rock layers, where water is kept under pressure
Advantages | Modularity: Lower cost and higher accessibility due to use of off-the-shelf equipment and materials Scalability: More potential locations due to relatively small plant size. Quick installation: Use of prefabricated materials such as corrugated steel and floating membranes, allowing for quicker setup | Cost effective: With no need to construct an underground powerhouse, lower cost and less construction time Scalable: Highly adaptable, which supports a wide range of project sizes Versatility: Applicable for development of pumped storage capabilities at existing hydropower plants and for applications at non-power dams | Fast construction: Underground deployment leads to an accelerated timeline Scalable: Flexible for various project sizes; modular design allows phased growth Low project cost: Reduced capital expenditures compared with CapEx for PSH or battery storage
Estimated unit plant size (MW) | 1-10 | 10-200 | 16-320
Plant lifetime (years) | 30 | 60 | 30
LCOS range ($/MWh) |  |  | 
Source: DOE, Technology Innovations for Pumped Storage Hydropower (2022).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 246 | 338
Chart: 
 | 156 | 174
Chart: 
 | 127 | 158
PSH

## Slide 135: Novel PSH technologies currently in development (2/4)
 | Hybrid PSH and wind plant | Integrated PSH and desalination plant | Underground PSH using TBM for storage excavation
Description | A small concrete reservoir is constructed around the foundations of wind turbines located on a hill. | Combines a seawater PSH plant with a reverse-osmosis desalination plant to provide an integrated energy storage and fresh-water supply system. | Uses tunnel boring machines (TBM) to excavate a lower reservoir in solid rock. Excavated rock is used to construct an upper reservoir on the surface for a closed-loop system.
Advantages | Cost reduction: Lower expenses through standardized construction and prefabricated components. Dual functionality: Possibility of hybrid operations with other renewable resources in addition to wind. Environmental impact: By utilizing the space directly around the wind turbine base, the design minimizes land usage and reduces footprint. | Synergies: Future demand for both energy storage and freshwater production is expected. Additional revenue: Addition of freshwater production adds another revenue stream for project developers. Location: Addresses energy storage and freshwater needs, making it an efficient, dual-purpose infrastructure solution for coastal communities facing water scarcity and energy demand. | Flat geography solution: Enables large amounts of energy storage in areas that do not have the topography to support conventional PSH plants. Large capacity and duration: Supports large plant sizes at around 500 MW, which makes it economically viable. Community benefits: Underground development limits disruptions to daily life.
Estimated unit plant size (MW) | 8-32 | 100-500 | 500-1000
Plant lifetime (years) | 50 | 60 | 60
LCOS range ($/MWh) |  |  | 
Chart: 
 | 151 | 208
Chart: 
 | 174 | 230
Chart: 
 | 210 | 230
PSH
Source: DOE, Technology Innovations for Pumped Storage Hydropower (2022).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).

## Slide 136: Novel PSH technologies currently in development (3/4)
 | Underground mine PSH | Open-pit mine PSH | Hybrid modular closed-loop scalable PSH
Description | Uses the tunnels and galleries of an existing abandoned mine as a lower reservoir and constructs an existing surface reservoir to serve as an upper reservoir for the PSH plant. | Uses the infrastructure of decommissioned open-pit mines for the development of PSH projects. | Converts electrical energy into chemical energy for storage and reverses the process to release it, stabilizing the grid during demand shifts.
Advantages | Reduced project costs: Using mine structures can lower overall project costs in comparison to building new reservoirs. Economic and environmental benefits: Repurposing mines reduces the need for extensive civil works. Market potential: Many abandoned mines in the U.S. could be converted into PSH plants. | Improved water conveyance: Provides better water conveyance hydraulics compared to underground alternative. Scalability: Supports a range of plant sizes, from 100 to over 2,000 MW. Market potential: Many open-pit mines in the U.S. could be converted into PSH plants. | Geographic flexibility: Batteries can be installed almost everywhere, meaning they can be located closer to demand centers, reducing transmission losses and infrastructure costs. Scalability: Allows utilities to add capacity incrementally as demand grows. Faster response time: Response to changes in load and generation needs happens within milliseconds.
Estimated unit plant size (MW) | 20-100 | 100-2000 | 1-10
Plant lifetime (years) | 60 | 60 | 20
LCOS range ($/MWh) |  |  | 
Sources: Department of Energy; Engie.
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 162 | 201
Chart: 
 | 193 | 193
Chart: 
 | 221 | 369
PSH

## Slide 137: Novel PSH technologies currently in development (4/4)
 | Pressurized vessel PSH | Thermal underground PSH | High-density fluid PSH
Description | Uses water to pressurize air in a high-pressure vessel. Water is used as a liquid piston to compress air. Storage occurs when water is pumped into the vessel, increasing air pressure. | Both the upper and lower reservoirs of the PSH plant are built underground, allowing geothermal energy to heat water. | Uses a high-density fluid instead of water to reduce the size of reservoirs and infrastructure.
Advantages | Modularity: Can be implemented in both small systems and large-scale installations. No geographic restrictions: Suitable for regions without elevation differences. Cost effective: Use of high-pressure pipe segments and underground reservoirs can reduce cost. | Multipurpose: Can provide electricity, heating, and cooling to enhance efficiency and flexibility. Urban use: Suitable for urban and industrial areas with significant heat demand. Minimal environmental impact: System prevents any impact on natural water sources. | Reduced plant size: Small reservoirs and infrastructure due to high-density fluid. Cost savings: Significant decrease in project costs when compared to traditional PSH plants. Geographically diverse: Can be implemented in geographically diverse locations with lower elevation differentials due to lower hydraulic head requirement.
Estimated unit plant size (MW) | 1-300 | 300-1,000 | 5-50
Plant lifetime (years) | 30-60 | 60 | 60
LCOS range ($/MWh) |  |  | 
Sources: Department of Energy; Rhe Energise
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 143 | 827
Chart: 
 | 213 | 258
Chart: 
 | 127 | 173
PSH

## Slide 138: India's first utility-scale battery energy storage system completed in record time with tariff boost
Observations
India achieved a significant milestone with the regulatory approval of its first commercial utility-scale battery energy system project, paving the way for further BESS integration throughout the country.
The initiative is supported by the Global Energy Alliance for People and Planet’s (GEAPP) concessional loan, which amounts to 70% of the total project cost.
The project is a 20 MW/40 MWh BESS, strategically installed at BSES Rajdhani Power’s 33/11 kV Kilokari substation.
India set the BESS tariff 55% lower than the previous benchmark, which sets a new standard for BESS affordability in India and makes this the fastest BESS to be commissioned, with a record time of 18 to 20 months.
The project boasts a comprehensive Monitoring, Evaluation, and Learning plan aimed at sharing key insights and learnings with other Indian distribution companies and other GEAPP BESS Consortium members in Asia, Africa, Latin America, and the Caribbean.
India’s urgent need for BESS integration in distribution is underscored by the country’s substantial variable renewable energy penetration, which exceeds 12% in certain regions.
Source: GEAPP, India’s First Commercial Utility-Scale Battery Energy Storage System (2024).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Chart: 
 | 1 | 47
2026
2032
+90%
Chart: 
 | 130 | 57.6
Previous benchmark
Project tariff
-55%
India’s projected growth in utility-scale battery energy storage by 2030, GW
Tariffs for India’s first utility-scale battery energy storage project, INR/kWh
Battery

## Slide 139: Italy's energy policies facilitate rapid growth in battery storage market
Observations
Italy aims to integrate 40% renewables into its energy mix by 2030.
The country’s BESS market currently stands at around 2.3 GW, mainly in small-scale residential systems integrated with solar.
Utility-scale BESS is still in early stages but set for rapid growth with an ambitious Integrated National Energy and Climate Plan targeting 11 GW of new capacity by 2030.
Italy has introduced the Electricity Storage Capacity Procurement Mechanism as a long-term contract system to encourage battery energy storage investments.
Government-backed tenders worth €17 billion will push this expansion with a focus on lithium-ion batteries.
The areas showing the most promise for stand-alone BESS look to be in south Italy, in regions like Sicily and Calabria.
Sources: EY, Renewable Energy Country Attractiveness Index (2024); ITA, Italy Energy Storage; Timera, Italy rolls out new model for BESS investment (2024).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).
Italy’s regional congestion levels for stand-alone BESS deployment
High congestion
Low congestion
Battery

## Slide 140: Modeling V2G, Australian Renewable Energy Agency (2022)
Objective
Input data
Scenarios
Optimize the energy supply cost for a customer while ensuring that EVs are adequately charged to meet upcoming trip demands, all within the given constraints
An example optimization formulation for a customer with a single EV and solar considering import and export tariffs that vary as a function of the day |  | 
Target function |  | t: a time period 𝐼𝑡: the costs of importing energy from the grid, 𝐸𝑡: the payment for exporting energy to the grid 𝑃𝑖𝑚𝑝,𝑡: the amount of power imported, 𝑃𝑒𝑥𝑝,𝑡: the amount of power exported to the grid The costs and amount paid will vary depending on the specific tariffs used
Constraint 1 | 𝑃𝑖𝑚𝑝,𝑡 +𝑃𝑒𝑥𝑝,𝑡+𝑃𝑠𝑜𝑙,𝑡+𝑃𝑐ℎ,𝑡+𝑃𝑑𝑖𝑠,𝑡=0 | 𝑃𝑠𝑜𝑙,𝑡: the solar generation, 𝑃𝑐ℎ,𝑡: the EV charging energy, 𝑃𝑑𝑖𝑠,𝑡: energy discharged from the EV
Constraint 2 | −𝑀𝑎𝑡𝑏1,𝑡≤𝑃𝑑𝑖𝑠,𝑡≤0, 0≥𝑃𝑐ℎ,𝑡≥(1−𝑏1,𝑡)𝑀𝑎𝑡 −𝑀𝑏2,𝑡≤𝑃𝑒𝑥𝑝,𝑡≤0, 0≥𝑃𝑖𝑚𝑝,𝑡≥(1−𝑏2,𝑡)𝑀 | The constraints on the left are applied to reflect that the EV cannot be charged and discharged at the same time, as well as to ensure that power cannot be imported from and exported to the grid at the same time: 𝑏1,𝑡 and 𝑏2,𝑡: binary decision variables, 𝑀: a large value, 𝑎𝑡: a binary value representing whether the EV is plugged in and available to charge
An example optimization formulation for a customer with a single EV and solar considering import and export tariffs that vary as a function of the day |  | 
Target function |  | t: a time period 𝐼𝑡: the costs of importing energy from the grid, 𝐸𝑡: the payment for exporting energy to the grid 𝑃𝑖𝑚𝑝,𝑡: the amount of power imported, 𝑃𝑒𝑥𝑝,𝑡: the amount of power exported to the grid The costs and amount paid will vary depending on the specific tariffs used
Constraint 1 | 𝑃𝑖𝑚𝑝,𝑡 +𝑃𝑒𝑥𝑝,𝑡+𝑃𝑠𝑜𝑙,𝑡+𝑃𝑐ℎ,𝑡+𝑃𝑑𝑖𝑠,𝑡=0 | 𝑃𝑠𝑜𝑙,𝑡: the solar generation, 𝑃𝑐ℎ,𝑡: the EV charging energy, 𝑃𝑑𝑖𝑠,𝑡: energy discharged from the EV
Constraint 2 | −𝑀𝑎𝑡𝑏1,𝑡≤𝑃𝑑𝑖𝑠,𝑡≤0, 0≥𝑃𝑐ℎ,𝑡≥(1−𝑏1,𝑡)𝑀𝑎𝑡 −𝑀𝑏2,𝑡≤𝑃𝑒𝑥𝑝,𝑡≤0, 0≥𝑃𝑖𝑚𝑝,𝑡≥(1−𝑏2,𝑡)𝑀 | The constraints on the left are applied to reflect that the EV cannot be charged and discharged at the same time, as well as to ensure that power cannot be imported from and exported to the grid at the same time: 𝑏1,𝑡 and 𝑏2,𝑡: binary decision variables, 𝑀: a large value, 𝑎𝑡: a binary value representing whether the EV is plugged in and available to charge
Vehicle data | ACT government fleet data | Assumes the vehicle is plugged in and could be used for V2G when it is at its home location
 | Electric nation charge data | The charger energy data assumes that vehicles participating in the Electric Nation trial could engage in V2G functionality only when plugged in, which typically occurs only every few days
Energy and generation data | ACT government consumption data | The dataset includes metering data from ACT government sites involved in the REVS program. It contains 30-minute time-series energy transfer data at connection points but does not include solar PV data
 | NetGen energy data | The data set consists of de-identified behind-the-meter consumption data for homes involved in the NextGen trial, including information on consumption, generation, and battery power
Pricing | Current pricing | Customers are optimized against an existing retail price, assigned based on the customer class: Houses are assigned the “ActewAGL Home Time of Use” tariff Offices are assigned the “ActewAGL LV TOU demand” tariff
 | Dynamic pricing | Dynamic pricing builds a price signal that reveals the underlying nature of price drivers. It is split into two components: A network price, based on the EVO energy “smart battery” tariff A market price which is directly passed through for consumption, scaled to 90% for feed-in
Conservatism | None | The optimizer charges vehicles for planned trips or when necessary to achieve the optimization target. Unless otherwise specified with a conservation level, all results assume free battery use.
 | 50% | 50% of the battery’s capacity reserved for driving, which is equivalent to approximately 135 km range in a 40 kWh Nissan Leaf
 | 90% | 90% of the battery’s capacity reserved for driving, which is equivalent to approximately 243 km range in a 40 kWh Nissan Leaf
Source: Australian Renewable Energy Agency (2022)
Credit: Ashley Kim, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Lucha et al., “Storing Energy” (4 March 2025).

## Slide 141
  Mobility energy storage – policy scan
  Utility energy storage – policy scan
  Other supporting pages
  Glossary

## Slide 142: Glossary
ACC | Advanced chemistry cell | DER | Distributed energy resources
AEI | American Energy Innovations | DISCOM | Distribution companies
APS | Announced Pledges Scenario | DOE | Department of Energy
BASF | Badische Anilin- und Sodafabrik | DRC | Democratic Republic of the Congo
BESS | Battery energy storage system | E2E | End to end
BEV | Battery electric vehicles | EPR | Extended producer responsibility
BM | Black mass | ESO | Energy storage obligation
BNEF | Bloomberg New Energy Finance | ESS | Energy storage system
BoS | Balance of system | ETS | Economic Transition Scenario
BTM | Behind the meter | EU | European Union
CAES | Compressed air energy storage | EV | Electric vehicles
CAFC | Corporate average fuel consumption | FAME | Faster Adoption and Manufacturing of (Hybrid &) Electric Vehicles
CAGR | Compound annual growth rate | FCEV | Fuel cell electric vehicles
CAISO | California's Independent System Operator | FCH | Fuel cell hydrogen
CAM | Cathode active material | FERC | Federal Energy Regulation Commission
CapEx | Capital expenditure | FIT | Feed-in tariff
CATL | Contemporary Amperex Technology Co. Ltd. | FTM | In front of the meter
CCS | Carbon capture and storage | G2V | Grid-to-vehicle
CPI | Consumer price index | GEAPP | Global Energy Alliance for People and Planet
DAM | Day-ahead market | GHG | Greenhouse gas emissions

## Slide 143: Glossary
NZE | Net Zero Emissions | SW | Software
O&M | Operations and maintenance | T&D | Transmission and distribution
OEM | Original equipment manufacturer | TCO | Total cost of ownership
p.a. | Per annum | TCTF | Temporary Crisis and Transition Framework
PEV | Plug-in electric vehicles | TEN-T | Trans-European Transport Network
PHEV | Plug-In hybrid electric vehicles | TES | Thermal energy storage
PLI | Production Linked Incentive | TL fee | Transmission loss/levy fee
PNIEC | Integrated National Energy and Climate Plan | TOU pricing | Time-of-use pricing
PSH | Pumped storage hydropower | TWh | Terawatt hour
PSP | Pumped storage projects | V2G | Vehicle-to-grid
R&D | Research and development | VALCOE | Value-adjusted levelized cost of energy
REC | Renewable energy certificate. | VAr | Volt-ampere reactive
RPO | Renewable purchase obligation | VAT | Value-added tax
RT | Real time | VGF | Viability gap funding
SDES | Short duration energy storage | VRFB | Vanadium redox flow battery
SGCC | State Grid Corporation of China |  | 
SGIP | Self-Generation Incentive Program |  | 
SiB | Sodium-ion battery |  | 
SOH | State of health |  | 
STEPS | Stated Policies Scenario |  |