## Slide 1: Rethinking Plastics
Anika Behrndt, Smarth Galhotra, Una Oljaca, Mariana Castano, Yosafat Partogi, Paula Sanchez, Khande-Jaé Fisher, Ariela Farchi Behar, Hyae Ryung Kim, Gernot Wagner
December 2025

## Slide 2: Current system generates ~450 Mt of plastics and ~2 Gt CO₂e; projected to grow significantly if current trends continue
Plastics demand expected to grow ~2 to 3x by 2060 under “business as usual” projections
Plastics emissions increased ~28% in the past five years; projected to grow 150% by 2050
Key Assumptions
Plastic demand projections assume no changes in production technologies or regional demand structure. They reflect three forward-looking scenarios:
  OECD (2022): ~2.5% to 4% annual growth driven by income and population growth in non-OECD economies
  Dokl et al. (2024): CAGR of ~2.2%; regression-based optimization on historical trends (extrapolated to 2060)
  Pottinger et al. (2024): CAGR of ~1.1%; machine learning + Monte Carlo; explicitly more conservative than OECD
All three exclude microplastics (tires, textiles), PFAS, behavior/system change, and informal-sector waste flows
Emissions based on OECD projection, which assumes 2.5% annual demand growth and current recycling trends
Plastics production1 (million metric tons/year)
Total annual emissions and future projections from plastics5 (Gt CO₂e/year)
GHG emissions
Uncertainty range6
High-ambition scenario5
Chart: 
| 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050 | 2051 | 2052 | 2053 | 2054 | 2055 | 2056 | 2057 | 2058 | 2059 | 2060
 | 449.53 | 460.993 | 472.7483 | 484.8034 | 497.1659 | 509.8436 | 522.8447 | 536.1772 | 549.8497 | 563.8709 | 578.2496 | 592.9949 | 608.1163 | 623.6233 | 639.5257 | 655.8336 | 672.5573 | 689.7076 | 707.2951 | 725.3311 | 743.8271 | 762.7947 | 782.2459 | 802.1932 | 822.6491 | 843.6267 | 865.1391 | 887.2002 | 909.8238 | 933.0243 | 956.8164 | 981.2152 | 1006.2362 | 1031.8953 | 1058.2086 | 1085.1929 | 1112.8653 | 1141.2434 | 1170.3451 | 1200.1889 | 1230.7937
 | 464 | 474.0688 | 484.3561 | 494.8666 | 505.6052 | 516.5769 | 527.7866 | 539.2395 | 550.941 | 562.8965 | 575.1113 | 587.5912 | 600.342 | 613.3694 | 626.6795 | 640.2784 | 654.1725 | 668.368 | 682.8716 | 697.6899 | 712.8298 | 728.2982 | 744.1023 | 760.2493 | 776.7467 | 793.6021 | 810.8233 | 828.4181 | 846.3948 | 864.7616 | 883.5269 | 902.6994 | 922.288 | 942.3017 | 962.7496 | 983.6413 | 1004.9863 | 1026.7945 | 1049.0759 | 1071.8409 | 1095.0998
 | 547 | 552.7435 | 558.5473 | 564.4121 | 570.3384 | 576.3269 | 582.3784 | 588.4933 | 594.6725 | 600.9166 | 607.2262 | 613.6021 | 620.0449 | 626.5554 | 633.1342 | 639.7821 | 646.4998 | 653.2881 | 660.1476 | 667.0791 | 674.0835 | 681.1614 | 688.3135 | 695.5408 | 702.844 | 710.2239 | 717.6812 | 725.2169 | 732.8317 | 740.5264 | 748.3019 | 756.1591 | 764.0988 | 772.1218 | 780.2291 | 788.4215 | 796.6999 | 805.0653 | 813.5184 | 822.0604 | 830.692
OECD
Dokl et al.
Pottinger et al.
Chart: 
 | 1.55 | 1.612 | 1.6765 | 1.7435 | 1.8 | 1.845 | 1.8911 | 1.9384 | 1.9869 | 2.0365 | 2.0874 | 2.1396 | 2.1931 | 2.248 | 2.3042 | 2.3618 | 2.4208 | 2.4813 | 2.5434 | 2.6069 | 2.6721 | 2.7389 | 2.8074 | 2.8776 | 2.9495 | 3.0232 | 3.0988 | 3.1763 | 3.2557 | 3.3371 | 3.4205 | 3.506 | 3.5937 | 3.6835 | 3.7756 | 3.87
 | 2.0503 | 2.1042 | 2.1608 | 2.2203 | 2.2827 | 2.3481 | 2.4167 | 2.4885 | 2.5636 | 2.6422 | 2.7243 | 2.81 | 2.8994 | 2.9926 | 3.0898 | 3.1909 | 3.2961 | 3.4056 | 3.5195 | 3.6379 | 3.7609 | 3.8888 | 4.0217 | 4.1597 | 4.303 | 4.4518 | 4.6063 | 4.7668 | 4.9333 | 5.1062 | 5.2857 | 5.472
 | 1.5497 | 1.5858 | 1.6214 | 1.6565 | 1.6911 | 1.725 | 1.7582 | 1.7908 | 1.8226 | 1.8537 | 1.884 | 1.9135 | 1.9422 | 1.97 | 1.997 | 2.023 | 2.0481 | 2.0722 | 2.0953 | 2.1172 | 2.1381 | 2.1577 | 2.176 | 2.1929 | 2.2084 | 2.2224 | 2.2347 | 2.2453 | 2.254 | 2.2608 | 2.2655 | 2.268
0
1
2
3
4
5
6
2015
2020
2025
2030
2035
2040
2045
+150%
+28%
2050

## Slide 3: ~70% of plastic lifecycle emissions come from the production process, ~20% from fossil feedstocks, ~10% from end of life
Key Decarbonization Challenges
Stage 1 (upstream): Around 18% of emissions come from the extraction of fossil fuels, used as feedstock and fuel energy sources of plastic production. Extraction of fossil fuels causes direct emissions, like CH4 leakage and flaring, along with emissions from fuel combustion
Stage 2 (production): Around 71% of CO2 emissions are generated in the production phase, where fossil fuels are burnt to achieve the high temperatures needed for the production of monomers and subsequent final plastics materials
Stage 3 (downstream): The remaining emissions come from end-of-life management, primarily from incinerating plastic waste using fossil fuels, the most common disposal method
Breakdown of emissions by lifecycle stage in traditional fossil fuel-based plastics
Chart: 
 | 18.018 | 18.018 | 32.4324 | 44.1441 | 67.5676 | 74.7748 | 90.0901 | 100
 | 14.4144 | 11.7117 | 23.4234 | 7.2072 | 15.3153 | 11
2.3 Gt
End-of-life management
Upstream
Downstream
0.4 GtC02
1.6 GtC02
0.3 GtC02
Production
71%
Product shaping
Polymerization
Monomer production
Other chemical production
Hydrocarbon refining and processing
Extracting
Source: Strategies to reduce the global carbon footprint of plastics (Zheng and Suh, 2019).
Credit: Anika Behrndt, Isabel Hoyos, Hyae Ryung Kim, Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).

## Slide 4: Plastics remain difficult to replace because of significant material and cost advantages compared with alternative materials
Plastics have a higher insulating capacity and are significantly more resistant and lighter than alternative materials
Plastics are 2 to 3x cheaper than other materials with similar use cases
Relative behavior of selected chemical capabilities of other materials compared with plastics
Weight3
Corrosion Resistance
Insulating Capacity
Poor conductivity of plastics make it a good thermal and electrical insulator, increasing design flexibility
Metals, paper, and glass do not have the same insulating capabilities as plastics
Impact Resistance²
Durable properties of plastics help them absorb and distribute energy from sudden impacts or shocks
Metals and glass, which can crack or fail over time, are less resistant to fatigue compared with plastics
Plastics resist damage when exposed to acids, lubricants, paint strippers, and other substances
Plastics’ flexible qualities allow for the production of ultra-lightweight materials
Chemical substances may cause rust or corrosion in other materials, such as metals and paper
Material density of metals and glass result in heavier materials
Average cost of materials in the U.S. ($/Kg)
Chart: 
 | 2.78 | 1.595 | 1.27 | 1.065
 | 0.5 | 1.5 | 2.5 | 3.5
 | 0.5 | 1.5 | 2.5 | 3.5
Glass & Fiberglass
Aluminium & Steel
Paper
Plastic¹
~2.80
~1.60
~1.30
~1.10
¹Using PE as a proxy for overall plastics prices, representative given high market share. ²Impact resistance (robustness): The ability to withstand sudden force or shock without breaking, cracking, or deforming. ³Comparing the weight of a 0.5L container using different materials.
Sources: Climate impact of plastics (McKinsey, 2022); The Advantages of Plastics Compared to Other Materials (Atlas Fibre, 2023); Aluminum (Trading Economics, 2025); Steel (Trading Economics, 2025); Spot Offers (The Plastics Exchange, 2025).
Credit: Anika Behrndt, Una Oljaca, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).

## Slide 5: Plastics decarbonization will need five levers to decouple from fossil fuels and reduce production emissions
Multi-tiered breakdown of solutions for plastics decarbonization
Solutions
Goal |  |  |  |  | 
Intervention | Reduce | Substitute | Recycle | Electrify | Carbon capture
Description | Eliminate redundant plastics and switch to reuse models where possible | Replace virgin fossil-based plastics with bio-plastics and other lower carbon alternatives | Scale mechanical and chemical recycling to extend material lifetime and reduce emissions-heavy incineration | Switch energy inputs for industrial processes from fossil fuels to renewable energy | Capture process emissions and repurpose CO₂ to offset hard-to-abate residual emissions in production
Impact (Mt of CO2)1 | 6,000-9,000 | 900-3,800 | 2,800-4,100 | 250-3,300 | 210-380
Cost (US$B)2 | ~150 | Medium | ~160 | ~700 | Medium
Implementation complexity | Medium | Medium to high | Medium to low | Medium | High
Challenges | Strong policy alignment required | Technology readiness level still low; more R&D required | Requires high up-front investment | High up-front investment for infrastructure investment | Technology highly ambiguous, expected to be ready in next 10 years
Reduce reliance on virgin fossil fuel feedstock
Decarbonize production processes
1All values are indicative, rounded, non-exhaustive, and based on current trajectory. See Appendix 1 for detailed notes of sources and assumptions. 2 Low: $0 to US$50 billion; Medium: US$51billion to US$300 billion; High: US$301 billion+. Refer to section “Key requirements to unlock change” for more cost details and assumptions.
Sources: Plastic Waste by region and end of life fate (OECD, 2023); Plastic Recycling: Techno Economic Analysis (Salahuddin et al., 2023);
Credit: Anika Behrndt, Isabel Hoyos, Hyae Ryung Kim, Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).

## Slide 6: Packaging and consumer products with the highest potential for plastic reduction
Elimination and reuse measures can reduce plastic waste by ~30%, with the highest reduction in packaging2
Plastic elimination is most relevant for packaging and household products, while reuse applies across industries
Reduce
Solutions
Packaging
Household
Construction
Automotive
Responsible stakeholder






Retailers, consumer goods brands
Consumer goods brands, OEMS, construction companies
Elimination
Reuse
 Applicable1
1 Can be more easily implemented/adapted and lead to a higher impact. 2 Absolute values for global plastic waste reductions are approximated by applying EU sectoral reduction rates from Systemiq’s Circularity Scenario to global plastic-use baselines. 3 Based on the four largest contributing sectors, which together account for ~80% of total plastic waste generated.
Sources: Reshaping Plastics (Systemiq, 2022); Pathways to reduce global plastic waste mismanagement and greenhouse gas emissions by 2050 (Pottinger et al., 2024).
Credit: Khande-Jae Fisher, Ariela Farchi, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).
Chart: 
 | 96.18
 | 130.53
 | 75.57
 | 219.84
Baseline waste
~500
Chart: 
 | 77.6
 | 18
 | 127.194
 | 4
 | 65.568
 | 10
 | 136.289
 | 84
84
10
4
18
Reduction impact on waste
Mt plastic waste in 20503
Packaging
Household
Construction
Automotive
Short lifecycles and high turnover of packaging and consumer products results in plastic elimination having the highest impact in these categories
Eliminated plastics

## Slide 7: ‘Bioplastics’ refers to a wide range of materials that emerge as a lower emission substitute for traditional plastics​
Polymer material matrix, categorized by source and biodegradability
Abatement potential
Substitute
Solutions
Bio-based
Fossil-based
Non- biodegradable
Biodegradable
Material substitution (e.g., PLA, PHA, PBS, starch blends)
e.g., PBAT, PCL, PBS
Drop-in (e.g., bio-based PE, bio-based PET, bio-PE or -PS) or non- drop-in
e.g., PE, PP, PET
Traditional plastics
Bioplastics
Bioplastics is an umbrella term; “drop-in” bio-based materials are chemically identical to petrochemicals, while new polymers have different structures
Commonly referred to as bioplastics
Sources: The New Plastics Economy (Ellen MacArthur Foundation, 2015); The role of bioplastics in the Circular Economy (McKinsey & Company, 2019); European Bioplastics website; Biobased plastic (European Union, 2022); Bioplastics for a circular economy (Nature Reviews Material, 2022).
Credit: Paula Sánchez, Ariela Farchi, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).
4
4
0.5
Kg of CO2e saved per kg of polymer produced, against traditional plastic
Traditional plastics
Bio-based & biodegradable
Bio-based & non -biodegradable
Fossil-based &
biodegradable
Illustrative, directional metrics
Baseline
No CO2 savings
Chart: 
| Fossil & Non-biodegradable | Fossil & Biodegradable | Biobased & Non-biodegradable | Biobased & Biodegradable
Serie 1 | 0 | 0.25 | -0.25 | 1
Serie 2 | 0 | 0.25 | 4 | 3

## Slide 8: Narrowing performance and cost gaps is key for scaling bioplastics adoption; polylactic acid is closest to reaching parity
Observations
20+ FDA-approved products show polylactic acid’s (PLA) highest technology readiness is in medical applications
Bio-resins still carry a clear premium vs. commodity petro-plastics
PLA is often quoted at $3 per kg, PBS at $3.20, PHA at $4 to $6, and PBAT (lower cost biodegradable) at about $1.85 to $1.90; in contrast, PP generally trades close to $1 to $1.30 per kg
Bioplastics face two key parallel challenges: reducing costs and improving performance1
Performance and cost of bioplastics compared with traditional plastics
1Performance is measured considering tensile strength, elongation at break, heat deflection, and water vapor permeability.
Sources: CKI analysis; BusinessanalytiQ; Physical and thermal properties (Nazrin et al., 2020); Tensile Behavior of High-Density Polyethylene (Amjadi and Fatemi, 2020); Poly(Butylene Adipate/Terephthalate-Co-Glycolate) (Wang et al., 2020); A review on bio-based polymer (Rajendran et al., 2024); Poly(Lactic Acid)-Based Microparticles (Vlachopoulos et al., 2022).
Credit: Smarth Galhotra, Paula Sánchez, Ariela Farchi, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).
Chart: 
| 0.4 | 1.8 | 3.5 | 2.1 | 6
 | 0.6 | 0.8 | 0.8 | 0.5 | 0.9
0.2x
0.6x
1.0x
1.4x
1.8x
Cost
Performance*
TPS
PLA
PHA
PBAT
PBS
The cost gap is driven by expensive bio-feedstocks and monomers, extra unit operations, and lower utilization plants
Attractive Cost Better Performance
High Cost Better Performance
High Cost Suboptimal Performance
Attractive Cost Suboptimal Performance
The functional performance gap is closing faster than the cost premium
Substitute
Solutions

## Slide 9: Only ~10% of plastic waste is recycled; design and sorting issues render over 60% of collected plastics unrecyclable
Global plastics recycling stages (material flow and losses)
Recycle
Solutions
Total waste
Collected waste
Recyclables
Uncontaminated
recyclables
Recycled
waste
High value
15-20% loss
60-65% loss
5-10% loss
~5% loss
Incurred losses
Plastic waste across recycling stages
Low-value recyclate
High-value recyclate
Amount (in Mt) | % of total waste | Description
350 | 100% | Total annual post-consumer plastics waste
280-300 | 80-85% | All plastic waste formally collected; the remaining share is mismanaged
55-65 | 20-25% | Plastics sorted as recyclables
40-55 | 10-15% | Yield after removing contamination from food and beverages
30-40 | 5-10% | Washed, shredded, and pelletized for resale
~30 | ~5% | Cascaded recycling: Recycling into other, lower value recycling applications
>10 | <2% | Closed-loop recycling: Recycling into same or similar value material
Sources: Policy Scenarios for Eliminating Plastic Pollution by 2040 (OECD, 2024); Plastics and the circular economy – deep dive (Ellen MacArthur Foundation, 2019).
Credit: Anika Behrndt, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).

## Slide 10: Recycling can abate 20% to 35% of total plastics emissions
Scaling mechanical and chemical recycling methods has the potential to abate up to 35% of total lifecycle emissions…
…but requires redesign, collection, infrastructure, and stimulating demand
Recycle
Solutions
Mechanical
Recycling
Chemical
Recycling
Reuse
Monomer Fabrication
Polymerization
Compounding & Processing
Sale and Consumer Use
EOL Disposal
Waste/Incineration
1
2
4
3b
~15-25% of CO2e reduction1
~5-10% of CO2e reduction1
3a
Design for recyclability
>70% of plastics remain non-recyclable due to complex design and mixed materials
1
Develop collection systems
Around 2 billion people lack access to regular waste collection, leading to widespread mismanagement
2
Scale recycling infrastructure
Scale chemical recycling: New facilities in regions with limited processing infrastructure
Advance mechanical recycling: Improve efficiency and operations
3
Stimulate market for recycled materials
4
Policies are needed to enforce both recycling as an end-of-life methodology, as well as mandatory use of recycled materials
1 Mechanical recycling can reduce the lifecycle emissions of plastics by ~40% compared to incineration and chemical recycling by around 20% compared to incineration.
Source: Breaking the Plastic Wave (Pew, 2020).
Credit: Anika Behrndt, Ariela Farchi, and Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).

## Slide 11: Electrifying plastics production could tackle >50% of emissions; monomer fabrication is the largest lever but has lowest TRL
Value chain stage | Feedstock processing (extraction of non-renewables and refining to produce naphtha, ethane, etc.) | Monomer fabrication (cracking hydrocarbons to produce monomers such as ethylene) | Polymerization (converting monomers to polymers such as polyethylene) | Product manufacturing (fabrication of finished plastic products) | End-of-life disposal (incineration, landfill, leakage of plastics waste)
Key electrifica-tion levers & implications | Petrochemical feedstock production using carbon-free generated electricity Electrification tech is commercially available but in pilot phase for large-scale furnaces | Significant emissions abated by avoiding burning fossil fuels in steam cracking FOAK crackers in pilot, to be powered with renewables | Electric heating available Mature technology, given lower temperatures, but not industry-standard | Stage already largely electrified All-electric machines are mature and should use low-carbon electricity | Limited impact from electrification Embedded carbon released in incineration
Limiting factor | Retrofitting cost | High temperatures required | Retrofitting cost | Retrofitting cost | Emissions inherent to combustion
TRL |  |  |  |  | 
Retroffiting cost range | $$$ | $$$ | $$ | $$ | $
Abatement potential | ~15% | >20% | ~10% | ~15% | 0-5%
Electrify
Solutions
Sources: Tackling heat electrification (McKinsey, 2024); Can carbon help decarbonize chemicals (BCG, 2023); Seadrift (X-Energy); Electrification (ETA, 2022); Levelised cost of petrochemicals for selected feedstocks and region (IEA, 2018); Carbon capture, utilization & storage in the energy transition (Energy Transitions Commission, 2022).
Credit: Paula Sánchez, Ariela Farchi, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).

## Slide 12: Electrified steam cracking (E-SC) could decarbonize monomer fabrication but is limited by renewable energy availability
Fossil hydrocarbons
After extraction, separation, and purification…
~25% of emissions from plastic production come from steam cracking at >850ºC
CO2 emissions of steam cracking and E-SC by electricity generation method (KgCO₂ kgC₂H₄¹)
Observations
E-SC powered by renewables could decrease CO₂ emissions from ethylene production by 18%*
The share of renewables in net U.S. electricity generation is set to grow from 24% in 2024 to ~70% in 2050. As E-SC remains energy intensive, renewable generation will be key for at-scale production
Production facilities can implement on-site renewable power generation to ensure source of energy for on-site E-SC
Steam cracking*
…hydrocarbons are then broken down into monomers
Polymerization
Monomers are then chemically bonded into long-chain polymers, the base material for plastics
Conventional steam cracking
Electrified steam cracking1
Chart: 
 | 3.44 | 3.73 | 3.45 | 3.26 | 3.21 | 3.21 | 3.21
 | 4.35 | 6.28 | 4.39 | 3.17 | 2.84 | 2.84 | 2.84
U.S. mix
Coal
Natural gas
Geothermal
Hydropower
Solar
Wind
Conventional steam cracking
Electrified steam cracking
Preferred
energy sources
Illustrative (directional metrics for ethylene)
Monomer Fabrication
Electrify
Solutions
1 Still in the pilot and demonstration phase.
Sources: Electrified steam cracking for a carbon neutral ethylene production process (Gu et al., 2022); Annual Energy Outlook 2025 (U.S. Energy Information Administration, 2025); Aligning the value chain to decarbonize plastics (McKinsey, 2025); Electric Cracking (Coolbrook); Piloting RotoDynamic Technology (Coolbrook).
Credit: Una Oljaca, Paula Sánchez, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).

## Slide 13: Carbon capture can be applied to feedstock production, monomer fabrication, and end-of-life treatment with utilization
 | Carbon Capture and Utilization (CCU) | Carbon Capture (CC) | 
Value chain stage | Feedstock production | Monomer fabrication | EOL disposal
Application and reduction potential | Conversion of CO2 to precursors and/or monomers through chemical and biological pathways Reduction varies with pathway, energy inputs, product grade, and regional economics | Retrofit steam crackers with carbon capture systems | Retrofit WtE incinerators with carbon capture systems
Cost – $/ton CO₂ avoided | CO2-methanol: ~$120 to $300 CO2-ethylene: ~$300 to $1,880 CO2-to-formic acid: Highly variable, lab-scale only | ~$56 to $108 per ton CO2 saved | Up to $288 per ton CO2 saved, but economics can be improved through power and heat integration1
TRL | TRL varies with some pathways already reaching commercialization while other pathways being developed | Most plants in feasibility study phase | Most plants in development/ pilot phase
Key challenges | Stoichiometric limits for polymer (up to ~50% CO2 by weight) High energy requirements; abundant, low carbon electricity necessary to significantly reduce footprint (ideally <6 g of CO2e per kWh ) Most pathways not yet at parity | Energy penalty of retrofitting CC lowers economic feasibility of capture Small waste-to-energy (WtE) plant sizes limit economics when compared with alternative power generation | Energy penalty of retrofitting CC lowers economic feasibility of capture
1Based on MEA capture and 60 MWe plant; LCA reduction for CCU based on GWP-100.
Sources: How the plastics industry can go green and at what cost (ING, 2023); Putting CO2 to use (IEA, 2019); Integration of CCUS in WtE plants (Acampora et al., 2025); Can the Plastics Industry become a carbon capture leader (IDTechEx, 2022); Life cycle assessment of polyols from polyurethane production using CO2 as feedstock (von der Assen et al., 2014); Achieving net-zero greenhouse gas emissions plastics by a circular carbon economy (Meys et al., 2021); Designing the Ethylene Factory for Products of CO2 Reduction (Pinto et al., 2025); Economic Feasibility tool for CO2 Utilization (NREL); Challenges and Opportunities of CO2 utilization (Pappjin et. al, 2020); Co2-based polyurethane foam (Karulf et al., CO2 Utilization, 2025); Current challenges and perspectives in Co2-based polymers (Liu et al, 2023). Credit: Khande-Jae Fisher, Ariela Farchi, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).
CCUS
Solutions

## Slide 14: Investment in plastics is projected to grow, led by petrochemical companies with strategic interests to prolong demand
Company | Project Name | Location | Cost | Polypropylene | Ethylene | Polyethylene
ExxonMobil | Corpus Christi | U.S. | $10B |  | x | x
ExxonMobil | Baton Rouge | U.S. | $0.5B | x |  | 
ExxonMobil | China Petroleum Complex | China | $10B | x |  | 
Total Energies | Port Arthur | U.S. | ~$2B |  | x | x
Chevron Phillips Chemical | Ras Laffan Petroleum Complex | Saudi Arabia | $6B |  | x | x
Chevron Phillips Chemical | Golden Triangle Petrochemical Company | U.S. | $8.5B |  | x | x
Shell | Pennsylvania Petrochemical Hub | U.S. | $6B |  | x | x
LyondellBasell | Thailand Parnets HMC Polymers | Thailand | N/A | x |  | 
LyondellBasell | Ulsan PP/ Poly Mirae | South Korea | $0.42M | x |  | 
Seven firms account for ~30% of global plastic production
Oil and gas companies continue to invest in new single-use plastics assets (2023)
Chart: 
 | 5.4 | 5 | 4.5 | 4.3 | 4.2 | 4 | 2.8 | 2.3 | 2.3 | 2.3 | 2 | 1.8 | 1.7 | 1.6 | 1.5 | 1.4 | 1.4
Sinopec
ExxonMobil
LyondellBasell
Saudi Aramco
PetroChina
Dow
INEOS
Reliance Industries
Indorama Ventures
Borealis
TotalEnergies
Formosa Plastics
Lotte Chemical
SIBUR
China Energy Investment Group
Alpek SAB de CV
PTT
~50% of production from top 17 plastic producers globally, 2023
5%
5%
4%
4%
4%
3%
2%
2%
2%
2%
2%
2%
2%
2%
1%
1%
5%
Top 7 producers
Sources: Plastic Waste Makers Index (Minderoo Foundation, 2023); Majority of the world’s plastics (Zero Carbon Analytics, 2025); Once Seen as Industry Savior, Petrochemicals Losing Financial Appeal (IEEFA, 2024).
Credit: Yosafat Partogi, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).
  Major petrochemical players are also oil and gas companies.
  Single-use applications

## Slide 15: Current capital deployment is skewed toward recycling; greater upstream investment is needed to reach decarbonization potential
Investors favor more tangible, infrastructure-heavy and commercially familiar levers, while lower-demand and material-substitution pathways offer better abatement efficiency but get less capital
Estimated plastic decarbonization investments by activity1 (US$B, 2018-2023, 2024-2050e)
Chart: 
 | 17 | 8 | 52.3 | 4 | 4
 | 150 | 80 | 160 | 367.7476 | 90
0
50
650
200
700
150
750
100
250
Substitute
17
~90
~150
Electrify
4
CCUS
~167
~88
~212
~704
~94
4
Reduce
~80
Recycle
8
~160
~700
2018-2023
2024-2050e
Investment
Policy & Finance
1All values indicative, rounded, non-exhaustive and based on current trajectory. See Appendix 1 for detailed notes of sources and assumptions.
Source: Plastic demand could reduce by up to 30% in an accelerated energy transition scenario (Wood Mackenzie, 2024).
Credit: Mariana Castaño, Anika Behrndt, Paula Sánchez, Khande-Jae Fisher, Ariela Farchi, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).
Abatement potential, 2050 (~Mt of CO₂)
900–3,800
2,800–4,100
250–3,300
210–380
6,000–9,000

## Slide 16: Decarbonization levers must overcome key financial barriers for investment, especially high CapEx and unclear business models
Comparison of decarbonization levers across TLR, business model, finance, and policy
1 Current reduction strategies face challenges including limited profitability, complex reverse logistics, behavioral inertia from consumers, and insufficiently robust policy frameworks to create demand or enforce adoption. 2 Recycling requires high capital due to asset-heavy infrastructure, the need for decentralized deployment, and parallel investment across mechanical and chemical technologies. 3 Abatement potential assessment for CCUS reflects only plastics’ share of global CCUS deployment (~4%); global potential is substantially higher.
Credit: Mariana Castaño, Ariela Farchi, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).
Reduce
Substitute
Recycle
Electrify
CCUS
High
Medium
High
Medium
Low3
Medium
Medium
Medium
High
Medium
Low
Low
Medium
Medium
Low
Medium
Low
Medium
Low
Low
High
Medium
High
Medium
Low
Favorable factor
Lack of scalable business models and limited policy1
Scale-up limited by feedstock supply, downstream infrastructure, and weak policy
High infrastructure costs from decentralized setup and dual system scaling2
High CapEx for low-carbon infrastructure and limited policy robustness
Limited economies of scale and unclear monetization pathways
Major constraint
!
!
Abatement potential
Required investment
Business model maturity
Policy & regulation readiness
Technology maturity
Solution
Key financial barrier
!
!
!
!
!
!
!
Investment
Policy & Finance

## Slide 17: Policy alignment, risk-sharing tools, and robust data are essential to mobilize capital toward plastics solutions
Comparison of current barriers and potential actions across critical enablers of plastics investment
Policy & Finance
1 Digital profiles capturing content, emissions, and recyclability per product. 2 Government or multilateral guarantees that backstop investment risk, reducing downside exposure. 3 Public or catalytic actors that absorb early losses, improving the risk-return profile for commercial investors in the future. 4Joint instruments like guarantees, subordinated debt, or insurance mechanisms. Credit: Mariana Castaño, Ariela Farchi, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al., “Rethinking Plastics” (1 July 2026).
Policy & Regulation
Investment Risk Mitigation
Why it matters
Policies remain fragmented across geographies and solutions, with limited long-term clarity, weak enforcement, and scarce demand-pull mechanisms
Data is inconsistent, siloed, and lacks standard formats for emissions, material flows, and solution performance, limiting investor confidence
Financial instruments like concessional loans, guarantees, and insurance remain underused, especially for technologies with uncertain revenue streams or infrastructure lock-in
Clear mandates, stable incentives, and long-term targets provide visibility, demand certainty, and market signals that reduce investor risk
Robust, standardized, and transparent data systems enable investors to assess risks, track impact, and evaluate returns across the plastics value chain
Targeted financial tools reduce exposure to early-stage risks, enabling private capital to enter and scale innovative or unproven solutions
Align national policies across all levers
Commit to targets that reduce virgin plastic use and increase recycled material uptake
Enforce emission limits for plastics production
Develop interoperable traceability platforms.
Standardize digital product passports1
Mandate emissions disclosure standards across the value chain
Ensure third-party impact verification
Expand blended finance models
Deploy public guarantees2
Offer first-loss capital3
Co-design risk-sharing tools4 with public-private investment vehicles
Current gap
Enabling moves
Data & Tracking Systems

## Slide 18: CKI Plastics Team
Hyae Ryung (Helen) Kim
PhD in Sustainable Development
Senior Research Fellow
hk2901@columbia.edu
Gernot Wagner
Senior Lecturer, Columbia Business School
Faculty Director, Climate Knowledge Initiative
gwagner@columbia.edu
Yosafat Partogi Simbolon
Master of Business Administration
CKI Fellow
Paula Sanchez Encinar
M.S. in Sustainability Management
CKI Fellow
Smarth Galhotra
Master of Business Administration
Ariela Farchi
Staff Associate III, CKI
Mariana Castaño
Master of Business Administration
CKI Fellow
Isabel Hoyos
Senior Staff Associate, CKI
Una Oljaca
BA in Sustainable Development
CKI Fellow
Khande Jae Fisher
M.S. in Sustainability Science
CKI Fellow
Anika Behrndt
M.S. in Sustainability Management
CKI Fellow

## Slide 19: Glossary
ACR
Acrylic
APC
Aliphatic polycarbonates
BAU
Business as usual
CCUS
Carbon capture, utilization, and storage
CP
Casein polymers
CR
Cellulose regenerates
CX
Customer experience
EOL
End of life
EPR
Extended producer responsibility
EPS
Expanded polystyrene
E-SC
Electrical steam cracking
LDPE
Low-density polyethylene
MENA
Middle East and North Africa
NYL
Nylon
PA
Polyamides
PBAT
Poly(butylene adipate-co-terephthalate)
PBS
Polybutylene succinate and copolymers
PE
Polyethylene
PEF
Polyethylene furanoate
PET
Polyethylene terephthalate
PHA
Polyhydroxyalkanoates
PLA
Polylactic acid
PP
Polypropylene
PTT
Polytrimethylene terephthalate
PUR
Polyurethane
PVC
Polyvinyl chloride
SCPC
Starch containing polymer compounds
SUP
Single-use plastic