## Slide 1: Powering Grids Executive Summary
Gernot Wagner, Hasan Alawadhi, Sevgi Helin Tilkicioglu, Dominica Wambold, Ilayda Tezcan, Gunay Kiran, Stephanie Chen, Christy Wong, Ryon Roque, Vincent Sandow-Straesser, Isabel Hoyos, Ariela Farchi, and Pia Doris Morrow
Cite as: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative
(28 September 2026).

## Slide 2: Modern energy grids are meant to provide power in a way that maximizes security while minimizing emissions and costs
Maximizing grid security
Minimizing carbon emissions
  Intermittent and inverter-based technologies are being prioritized; they are the readiest source available and fastest to connect
  These present unique challenges to the grid and its operations
Minimizing cost of power
  Affordable electricity is a human right, while achieving it and connecting any form of new generation requires expensive change that needs to be paid for somehow
  Grids must seek creative ways to achieve returns while ensuring that costs are fairly allocated and without raising backlash from customer costs
  Supply of energy must meet demand wherever required on the grid and maintain reliability
  Energy powers the economy; lost hours are directly related to lower productivity and standard of life, while constrained grids prevent industrial expansion
  Grids must be secure and sovereign, with cybersecurity and supply chain challenges posing an increasing threat to connected assets
1
2
3
Sources: CKI Analysis (2026).
Credit: Hasan Alawadhi, Stephanie Chen, Sevgi Helin Tilkicioglu, Isabel Hoyos, Dominica Wambold, Ariela Farchi, Pia Doris Morrow, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment

## Slide 3: Global grids face the critical need to adapt due to demand growth, a changing energy landscape, aging assets and extreme weather
Increasing Demand
Energy Transition
Aging Infrastructure
Extreme weather
Rapid growth in electricity demand
Critical aging infrastructure
Structural shift in the electricity system
Escalating climate & weather events
Driven by intensive load growth from AI/Data centers and the rapid electrification of transport and heating
Over 40% of global grid assets (up to 70% in the U.S.) are reaching the end of their 50-year design life, necessitating urgent replacement
Transitioning from centralized fossil-fuel generation to a decentralized, multi-directional energy network with more distributed abundant energy resources
Increased frequency and severity of extreme weather events require immediate and large-scale grid hardening
Drivers of
Grid Modernization
and Expansion
Sources: World Energy Investment (IEA, 2026); Global Landscape of Energy Transition Finance (IRENA, 2025).
Credit: Christy Wong, Ariela Farchi, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment

## Slide 4: Global electricity demand growth has been led by China, but is projected to accelerate across nearly all major regions
Chart: 
| 2010 | 2015 | 2020 | 2025 | 2035 | 2050
 | 0 | 12.587 | 25.244 | 49.0387 | 74.7904 | 129.8241
 | 0 | 14.1966 | 28.8801 | 52.1189 | 96.1582 | 188.534
 | 0 | 38.2066 | 84.9005 | 151.3632 | 215.5525 | 283.4178
 | 0 | -1.0101 | -2.4267 | 8.601 | 11.2203 | 28.5159
 | 0 | -3.3844 | -7.2067 | -6.9448 | 19.2266 | 53.2566
 | 0 | 13.9599 | 21.5094 | 39.3324 | 38.4632 | 101.6414
Observations
China has been the clear demand-growth outlier since 2010, with electricity demand up ~150% by 2025 versus ~50% globally
Sharp trajectory shift happens in mature markets: U.S. and European demand was broadly stagnant through 2025 but is projected to return to sustained growth
Recent growth from electrification, renewables, and data centers is a major challenge for decades-old grid systems, requiring massive investment
Other estimates forecast electricity growth to exceed that of the IEA’s Stated Policies Scenario, more than doubling by 2050
Electrification, data centers, and other new loads are driving the “age of electricity,” reversing decades of stagnant demand in mature markets
% Change in electricity final demand vs. 2010 baseline, 2010-2025 actuals, 2026-2050 forecasted1
World
Asia excl. China
China
United States
Europe
Rest of World
12010-2025 data from Energy Institute 2026 Statistical Review of World Energy; 2026-2050 modeled based on IEA Stated Policies scenario, from IEA World Energy Outlook 2025
Sources: Statistical Review of World Energy (Energy Institute, 2026); World Energy Outlook 2025 (IEA, 2025); Electricity 2026 (IEA, 2026); New Energy Outlook (BNEF, 2026); Power generation from renewables set to jump 84% in next five years (BNEF, 2026).
Credit: Pia Doris Morrow, Ariela Farchi, Dominica Wambold, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
“Age of electricity”
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment

## Slide 5: Electrification and data centers are among primary drivers accelerating electricity demand across the US, EU, and China
Observations
Building and transportation electrification, industry, and data centers are leading to compounding electricity demand growth in the 2020s
While data center electricity demand represents a small portion of all growth, its average annual growth rate is expected to double again in the years ahead under base scenarios and is the leading electricity demand growth driver in the U.S.
Electricity demand characteristics from each of these drivers pose distinct challenges to grids; each can drive significant increases in peak as well as average demand, with different levels of predictability and control
By 2030, data centers projected to account for ~50% of U.S. demand growth, building and transport electrification lead in the EU, and industrial electrification in China
Chart: 
 | 29.1829 | 190.6615 | 64.2023
 | 5.8366 | 9.7276 | 27.2374
 | 36.965 | 19.4553 | 36.965
 | 31.1284 | 110.8949 | 204.2802
 | -17.5097 | 27.2374 | 23.3463
 | -75.8755 | 5.8366 | 56.4202
 | -38.9105 | 13.6187
2015-2020
2020-2025
2025-2030
Industry
Cooling
Heat pumps
Data centers
Rest of building
Transport
Other
Chart: 
 | 9.743 | 8.2441 | 50.2141
 | 11.9914 | 14.9893 | 17.9872
 | 2.2484 | 11.9914 | 23.2334
 | -3.7473 | 28.4797 | 35.2248
 | -41.97 | -4.4968 | 50.9636
 | -17.2377 | -5.2463 | 113.1692
 | -31.4775 | -42.7195 | 5.2463
2015-2020
2020-2025
2025-2030
Electricity demand total growth by sector and end-use in the US, EU, and China, 2015-2030, TWh
United States
European Union
Chart: 
 | 1005 | 1084 | 1090
 | 140 | 176 | 165
 | 0 | 16 | 65
 | 30 | 51 | 160
 | 825 | 813 | 710
 | 75 | 133 | 325
 | 55 | 66 | 75
2015-2020
2020-2025
2025-2030
China
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment

## Slide 6: Global grid investment is expected to rise to +$500B in 2026 and increase through 2030, driven by infrastructure, materials, and labor
Chart: 
 | 670 | 800
2030
Chart: 
 | 85 | 80 | 75 | 75 | 70 | 65 | 65 | 70 | 80 | 90 | 140
 | 65 | 70 | 70 | 75 | 75 | 85 | 95 | 105 | 110 | 125 | 140
 | 50 | 55 | 55 | 60 | 65 | 70 | 65 | 75 | 95 | 115 | 145
 | 65 | 60 | 60 | 50 | 45 | 50 | 50 | 55 | 60 | 65 | 70
 | 10 | 10 | 10 | 10 | 20 | 20 | 20 | 20 | 20 | 25 | 25
 | 10 | 10 | 10 | 5 | 5 | 5 | 10 | 10 | 10 | 10 | 10
 | 25 | 25 | 20 | 20 | 15 | 15 | 15 | 20 | 20 | 20 | 20
2016
2018
2020
2022
2024
2026e
310
310
300
295
295
310
320
355
395
450
550
+11% p.a.
Investment grew ~85% over 5 years, targeted to reach $600B by 2030 in NZE1
2040-2050, 80% of investment needs to be used to modernize and 20% to expand
Observations
Grid investment needs to be spread across physical grid infrastructure, and grid enhancing technologies
Investing in robust supply chains and a prepared work force, alongside infrastructure and technology, will be critical to achieving global targets
  Increasing costs of equipment divest grid investments away from potential new infrastructure
Venture capital investments into grids has increased significantly in 10 years
  Investment in grid hardware rose 4x from ~$200M in 2015 to ~$800M in 2025
  Investment into optimisation (reinforcements) rose from ~$50M to ~$400M
  Largest rise was in VPPS and Derms, from ~$50M to ~$650M
ROW
Africa
Central and South America
APAC ex. China
Europe
North America
China
Investment in power grid infrastructure, 2016-2026e USD Billions
Chart: 
 | 19 | 19 | 54 | 100
 | 35 | 46
19%
New connections
35%
Asset replacement
45%
Grid Reinforcement
$800-900B
2040-2050
Breakdown of global annual investment required, 2040-2050
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment

## Slide 7: Optimizing, modernizing, and expanding will upgrade insufficient and aging infrastructure into a resilient, intelligent grid ecosystem
 | Optimize grid assets​ | Modernize and harden the core | Expand grid networks
Definition | Maximize the value of the grid through digital intelligence and demand management | Upgrade and modernize the core with capital efficient physical and technical augmentation | Structurally extend the grid's network to integrate available and emerging generation
Physical and Capital Profile1 | Digital intelligence & demand-side solutions Asset-light | Hardware solutions at existing grid nodes Capital efficient | Net new and upgraded grid transmission Capital intensive
Highlighted Solutions | Load Shifting Technologies Distributed Energy Resource Management Systems (DERMS) Virtual Power Plants (VPPs) Bi-directional charging | Grid-Forming Inverters (GFM) Grid-Scale Battery Storage Flexible AC Transmission Systems (FACTS) Advanced Metering Infrastructure (AMI) Digital Twins | New transmission and distribution HVDC
Time to Deploy | 1-2+ years | 1-4+ years | 5-15+ years
Investment Opportunity2 | Estimated $50-$150B+/yr from 2030-20351 Systems savings potential of $150B+ by 2035 | Estimated $200B-$400B+/yr from 2030-2035 | Estimated $200B+/yr from 2030-2035
Key Policy Levers | Performance based regulation reform DER aggregation reform, NWA incentives | Smart grid grants and incentive programs Cap and floor and depreciation schemes | Regional/interregional transmission planning Permitting, siting, and queue reform
1The capital profile indicated is relative (e.g., battery system capital efficiency vs. new transmission) and intended to reflect the grid capital investment (e.g., excludes consumer EV batteries).
2Investment opportunity is global and based on projected investments for highlighted solutions as defined in each solution area, supplemented by World Energy Investment 2025-2026 reports aligned to STEPS 2030 and BNEF NZE and ETS scenarios. Grid expansion is driven significantly by net-new wires (transmission & distribution); modernize & harden the core includes IEA’s Power segment of battery storage; the optimize range includes grid orchestration software and a subset of end-use related charging infrastructure, with savings potential reflecting estimated grid value from demand flexibility.
Sources: Building the future transmission grid (IEA, 2025); World Energy Investment (IEA, 2026); World Energy Investment (IEA, 2025); Electricity 2026 (IEA, 2026); Energy storage enters the 100 gigawatt era (BNEF, 2026); Electric Vehicle Outlook (BNEF, 2026); The Value of Demand Flexibility (IEA, 2025); Building grids faster (Energy Transitions Commission, 2024); Electricity Grids and Secure Electricity Transitions (IEA, 2023).
Credit: Dominica Wambold, Ariela Farchi, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment

## Slide 8: Optimizing existing assets unlocks the lowest-cost grid capacity, while expansion offers unlimited investment opportunity
Observations
AI could turn turn large loads into flexible grid assets, unlocking existing capacity while catalyzing investment in grid optimization and modernization
  ~100 GW of latent capacity: Flexible data center demand could unlock substantial capacity from infrastructure that already exists
  Faster interconnection: By reducing or shifting demand during constrained hours, large loads could connect without waiting for equivalent amounts of new grid build-out
  Investment catalyst: Data center investment flows can help deploy grid optimization and modernization technologies, including for storage, DERMS, and grid-forming inverters
  Untapped capacity: AI-enabled demand flexibility is estimated to be able to raise system efficiency up to 30% more broadly
Globally, storage and flexibility offer a major potential source of bridge power to meet growing demand while deferring as much as $1.8T in global grid investment through 2050
Illustrative
Capacity (GW, illustrative)
Price per unit capacity ($/MW, illustrative)
Ceiling
Floor
Optimize
1-2+ yrs, load shifting,
DERMS, VPPs, V2G
Modernize
1-4+ yrs, capital efficient
GFM, storage, FACTS, AMI, digital twins
Expand
5-15+ yrs, capital intensive
HVDC, new transmission
Uncapped upside
AI is both driving grid demand and mitigating grid constraints
AI-enabled data center flexibility could unlock ~100 GW of dormant capacity while accelerating grid optimization and modernization
20% of capacity
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment

## Slide 9: Scaling grid solutions requires overcoming distinct stakeholder bottlenecks across optimization, modernization, and expansion
Observations
Grid constraints are increasingly institutional, not technological:
  Optimizing requires access to existing flexibility,
  Modernizing requires mechanisms to monetize grid value,
  Expanding requires agreement on approvals, cost allocation, and project delivery
Barriers become more complex as solutions scale: Distributed-energy scaling is being held back by fragmented regulation and utility incentives, while transmission policy is explicitly focused on planning and cost allocation
Key bottlenecks range from market access in Optimize to utility incentives in Modernize and permitting and cost allocation in Expand
 | Optimize grid assets | Modernize and harden the core | Expand grid networks
 | Load shifting, DERMs, VPPs, V2G | GFM, storage, FACTS, AMI, digital twins | HVDC, new transmission
Regulators & policymakers1 | Enable DER aggregation and compensation; load flexibility could deliver >$15B annual system savings | Set standards and create markets for reliability services; Ireland increased allowable non-synchronous penetration from ~50% to 75%, targeting 95% | Resolve permitting and co-allocation to unlock >100 GW HVDC project pipeline
Utilities, planners & operators | Procure and orchestrate flexibility; ~200 GW of cost-effective US load flexibility could reduce peak constraints | Deploy upgrades where they defer new build; FACTS can increase transmission capacity by ~30-50% | Plan and operate new corridors capable of adding multi-GW capacity per project
Technology providers & developers | Scale orchestration platforms; coordinated DERs could form an ~80-160 GW VPP fleet | Supply grid hard- and software; >80% of US storage capacity is front-of-meter | Develop HVDC systems offering ~30-50% lower losses over long distances vs. comparable AC
Customers & beneficiaries | Monetize existing flexible assets; North America already has between 30-60 GW of VPP capacity on the grid | Participate through batteries, smart meters and flexible assets; AMI enables demand response and operational savings | Benefit from greater transfer capacity while ultimately funding regulated investment through tariffs
Investors & financiers | Fund asset-light platforms; coordinated DER/VPP deployment could generate ~$10B/year in grid savings | Finance storage and regulated/ contracted grid assets across a rapidly scaling market | Provide long-duration infrastructure capital once permitting and cost allocation are resolved
Critical stakeholder | Utilities and market operators | Utilities and regulators | Regulators and planners
Key bottleneck | Market access & orchestration | Utility incentives & standards | Permitting, cost allocation & delivery capacity
Make flexibility accessible, dispatchable & monetizable
Reward capacity unlocked, reliability delivered and costs avoided
Accelerate approvals and align who benefits with who pays
Keys to unlock capacity
1Including permitting authorities.
Sources: Virtual Power Plants Projects (U.S. Department of Energy, 2026); Pathways to Commercial Liftoff: Virtual Power Plants (U.S. Department of Energy, 2025); Operating Procedure for Calculation of NWA Financial Incentives (NY Dept of Public, 2020-2022); Electricity Grids and Secure Energy Transitions (IEA, 2023).
Credit: Pia Doris Morrow, Ariela Farchi, Dominica Wambold, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment

## Slide 10: Load Shifting Technologies move non-essential electricity use from high-demand periods to times when the grid is less stressed
1
Smart devices (data centers, thermostats, EV chargers, industrial controls) receive signals from the utility about when electricity is cheap, expensive, or scarce
2
When it is expensive, algorithms or customer-set preferences determine which load can be delayed without affecting comfort or operations
3
During high-demand periods, the device reduces consumption and during low-demand hours, it increases consumption.
4
Smart meters or built-in sensors track the load shifts so the system can fine-tune behavior, and the customer can benefit from lower bills, incentives, or grid-support payments
Reduces peak load and grid stress: Demand smoothing
Enhances renewable energy utilization: Better alignment
Customer behavior and participation: Engagement needed
Communication reliability: Stable signals
Limited visibility: Data gaps without AMI or sensors
How does load shifting work?
Advantages
Disadvantages
Why is it critical for the energy transition?
Moves consumption away from peak hours, reducing stress on lines, transformers, and generators
It helps match demand to renewable production times, rather than forcing renewables to follow a fixed demand profile
By shaving peaks and filling valleys, load shifting reduces the need for carbon-intensive peaker plants
Wider use of smart thermostats, heat pumps, water heaters, industrial load control, and EV smart charging linked to time-varying prices and automation
Source: Order No. 2222 Explainer: DERs in Electricity Markets (FERC, 2020); California's Biggest Battery Test Ever (PG&E, 2025); How Many Smart Meters Are Installed in the US? (EIA, 2023)
Credit: Sevgi Helin Tilkicioglu, Hasan Alawadhi, Pia Doris Morrow, Vincent Sandow-Straesser, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Device signaling
1
Flexible loads
2
Load shift
3
Compensation
4
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
Load Shifting

## Slide 11: Load flexibility is a deployable solution that allows data centers to operate as grid-responsive assets
Flexible load capacity (load shedding potential) by grid service duration and response speed1, % power drop
Demonstration of Peak Load relief (TV pickup effect example2)
Emerald AI demonstrated data centers can shift up to 40% of non-critical load in <40 seconds
AI-automated demand response lowers data center consumption in response to peak demand
Observations
Converting data centers from static to flexible consumers improves speed-to-power and affordability by making best use of existing infrastructure
Expedited access to constrained grids in exchange for flexibility guarantees can effectively incentivize load-shifting adoption
EPRI’s DCFlex initiative and Mosaic framework provide resources for utilities seeking to integrate data centers as flexible loads
Emerald AI’s workload orchestration solution has enabled operational-scale grid flexibility in the U.K. and in several U.S. states
  In a collaboration between Santa Clara, Emerald AI, and Silicon Valley Power, SVP is pioneering a program where data centers that are willing to be flexible are more likely to be granted additional capacity
1Emerald AI, EPRI, National Grid, and Nebius ‘AI Factory’ modeling with automated clustered response to grid disturbances across multiple use cases and scenarios; 2 UK phenomenon – during football matches, use of domestic appliances, such as tea kettles, picks up significantly during half-time and at the end of the match, causing demand peaks.
Sources: Power-Flexible AI Factories (Emerald AI, 2026); Flex Mosaic (EPRI, 2026); Global Effort to Prepare Future-Ready Grids (EPRI, 2025); AI data centers as grid-interactive assets (Nature Energy, 2025); Fast, Flexible Solutions for Data Centers (Rocky Mountain Institute, 2025); Blowing Off Steam (NVIDIA, 2026); AI drives demand, and will soon manage it (Silicon Valley Voice, 2026).
Credit: Dominica Wambold, Ariela Farchi, Gunay Kiran, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Chart: 
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 42 | 44 | 46 | 48 | 50 | 52 | 54 | 56 | 58 | 60
 | 120 | 120 | 120 | 120 | 119.9 | 119.2 | 116.8 | 111.8 | 104.2 | 95.2 | 90 | 95.2 | 104.2 | 111.8 | 116.8 | 119.2 | 119.9 | 119.7 | 118.8 | 116.1 | 111 | 104.2 | 100.2 | 100.2 | 104.2 | 111 | 116.1 | 118.8 | 119.7 | 120 | 120
 | 123.8 | 116.5 | 122.1 | 115.9 | 123.5 | 114.8 | 120.2 | 107.5 | 108.1 | 91 | 94.2 | 91.5 | 107.9 | 108.2 | 120.5 | 115.1 | 123.4 | 116 | 122.3 | 112.5 | 115.2 | 100.1 | 103.8 | 96.5 | 108 | 107.1 | 119.8 | 114.2 | 123.1 | 116.3 | 122.8
 | 30 | 30 | 30.01 | 30.03 | 30.07 | 30.15 | 30.32 | 30.58 | 30.85 | 31.08 | 31.2 | 31.08 | 30.85 | 30.58 | 30.32 | 30.15 | 30.07 | 30.09 | 30.18 | 30.35 | 30.55 | 30.73 | 30.8 | 30.8 | 30.73 | 30.55 | 30.35 | 30.18 | 30.09 | 30 | 30
Data center power targets (kW)
Data center power consumption (kW)
Grid demand (GW)
Time (minutes)
AI cluster power draw (kW, illustrative)
Automated workload orchestration curtailed data center power draw by ~25%, providing an alternative source for peak relief
Chart: 
 | 38 | 33.3 | 40 | 25
Frequency stabilization / rapid dispatch
<40 seconds
Peak relief / shaving
Real-time (inverse-tracking)
Sustained load reduction
2-10 hours (sustained)
Carbon intensity matching
5-minute matching granularity
35-40%
~35%
Grid demand (GW, illustrative)
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
Case Study

## Slide 12: Bidirectional charging enables vehicle-to-building and vehicle-to-grid interactions, turning EVs into flexible energy storage
1
An EV first participates through V1G, where charging is intelligently timed or managed while electricity still flows one way from the grid to the vehicle
2
With a bidirectional charger, the EV can charge and discharge, enabling electricity stored in the car’s battery to be used when needed
3
That stored electricity can be directed to budlings (V2B) or the grid (V2G) to reduce peak demand, support resilience, or optimize site electricity use
4
EVs are connect to the grid through a bi-directional inverter and communication interface, allowing an aggregator or utility to coordinate discharge across multiple vehicles simultaneously
These aggregated EVs export to the grid and respond to real-time utility or market signals, such as frequency regulation or demand responses, to provide system-wide flexibility and grid services
Unlocks additional value from EV batteries while vehicles are parked
Can support resilience, peak management, and renewable integration
Creates value for EV owners through lower bills/increased home resilience (V2B), or by generating revenue streams (V2G)
Requires bidirectional-capable hardware, controls, and coordination
Depends on standards, interconnection, and compensation mechanisms
Participation and value vary by site readiness, driver behavior, and market design
How does Bidirectional Charging for grid systems work?
Advantages
Disadvantages
Why is it critical for the energy transition?
EV batteries represent a rapidly growing flexible storage resource
Bidirectional charging can help balance peaks, improve resilience, and support renewable integration
It allows parked vehicles to provide value beyond transportation
It can defer grid and building infrastructure upgrades by using existing battery capacity
Source: Vehicle-to-Grid Integration Assessment Report, (US DOE, 2025); Global EV Outlook 2026, (IEA, 2026); EV Batteries Could Satisfy Short-Term Grid Storage Demand, (Nature, 2023)
Credit: Sevgi Helin Tilkicioglu, Hasan Alawadhi, Isabel Hoyos, Vincent Sandow-Straesser, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
Bidirectional charging
Vehicle
1
Bidirectional charger
2
Buildings and energy grids
3

## Slide 13: V2G could play a significant role in fulfilling grid storage demand, unlocking up to ~60 TWh in combination with second-use
 | 6 TWh |  |  |  |  |  |  |  |  | 62 TWh
100% |  |  |  |  |  |  |  |  |  | 
90% |  |  |  |  |  |  |  |  |  | 
80% |  |  |  |  |  |  |  |  |  | 
70% |  |  |  |  |  |  |  |  |  | 
60% |  |  |  |  |  |  |  |  |  | 
50% |  |  |  |  |  |  |  |  |  | 
40% |  |  |  |  |  |  |  |  |  | 
30% |  |  |  |  |  |  |  |  |  | 
20% |  |  |  |  |  |  |  |  |  | 
10% |  |  |  |  |  |  |  |  |  | 
 | 10% | 20% | 30% | 40% | 50% | 60% | 70% | 80% | 90% | 100%
Vehicle-to-grid participation
Second-use utilization rate
Source: Electric vehicle batteries alone could satisfy short-term grid storage demand by as early as 2030 (Nature, 2023).
Credit: David Foye, Petr Jenicek, Birru Lucha, Hyae Ryung Kim, Dominica Wambold, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Total actual available capacity under various conditions in STEP-NCX scenario in 2050
2050 grid storage demand
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
Bidirectional charging
Observations
Leveraging V2G and re-use are two domestic sources for battery storage deployment
V2G participation in grids could play a role in providing the real-world capacity for short-term grid storage, with EV batteries together with second-use utilization rates reducing other battery and generation needs
When both V2G participation rates and second-use rates are at 50%, the projected real-world capacity reaches between 25 and 48 TWh by 2050 (STEP-NCX scenario)
Meeting grid storage demands by 2050 (3.4 to 19.2 TWh) can be done with different combinations of V2G and second-use. Without any second-use batteries in stationary storage, grids would require V2G participation rates of an achievable 12% to 43%
Assuming half of second-use batteries (retired EV batteries repurposed for stationary grid storage after falling below automotive performance thresholds) are used for grid storage, the required participation rate of V2G drops to below 10%

## Slide 14: Distributed Energy Resource Management Systems orchestrate millions of small assets into a single, dispatchable grid resource
1
Distributed energy resources (DERs), e.g., rooftop solar, batteries, EVs and thermostats, are connected and registered to the platform
2
Each asset continuously reports its output, state of charge and availability
3
The platform forecasts load, solar and wind output, prices and grid constraints
4
It optimizes a dispatch that respects grid limits and market signals
Defers grid capex: Avoids new wires
Fast to deploy: Software-led
Unlocks DER value: Idle assets earn
Improves reliability: Local flexibility
Integrates renewables: Absorbs solar/wind swings
Integration complexity: Many vendors & systems
Needs enrollment & rules: Opt-in, standards, FERC 2222
Cybersecurity: Millions of endpoints to secure
How does DERMS for grid systems work?
Advantages
Disadvantages
Why is it critical for the energy transition?
Unlocks flexibility hidden in millions of behind-the-meter assets, turning passive load into a controllable, grid-supporting resource
Lets the distribution grid absorb far more rooftop solar and EVs without costly wire upgrades, by actively managing local flows
By aggregating DERs into virtual power plants, it provides capacity and ancillary services otherwise met by fossil peakers
Shifts the grid from centralized, supply-following dispatch to a distributed, demand-flexible system
Source: Pathways to Commercial Liftoff: Virtual Power Plants (US DOE, 2025); Order No. 2222 Explainer: DERs in Electricity Markets (FERC, 2020); GridOS DERMS: Distributed Energy Resource Management System (GE Vernova, 2025).
Credit: Sevgi Helin Tilkicioglu, Hasan Alawadhi, Pia Doris Morrow, Vincent Sandow-Straesser, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
5
Setpoints go back to the assets: charge, discharge, curtail or shift load
Delivered response is verified and participants are paid, then the loop repeats
6
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
DERMS
Distributed energy resources
1
Metering & telemetry
2
Forecasting
3
Optimization
4
Dispatch & control
5
Verify & settle
6

## Slide 15: DERMS provide an increasingly distributed grid with improved visibility, dispatch efficiency, interoperability and market integration
Observations
Without centralized coordination, 81% of US distribution transformers could be overloaded by 2050, dropping to just 28% with DERMS-based coordination and reducing peak load by 17%
DERMS unlocks DERs as dispatchable non-wires alternatives, deferring costly infrastructure upgrades, tripling US VPP capacity to 80–160 GW by 2030 could save $10B annually in grid costs
Enables TSO-DSO coordination, bridging two operators who historically lack real-time data exchange across the T/D interface
1DERMS are used to size metered loads of Commercial and Industrial (C&I) customers to figure out how much a C&I customer needs to be paid when their process load is curtailed and use the information credit the customer.
Sources: Renewable electricity capacity growth by technology segment (IEA, 2025); Coordinating distributed energy resources for reliability can significantly reduce future distribution grid upgrades and peak load (Navidi et al., Joule, 2023); US DOE VPP Liftoff (U.S. DOE, 2025); Use Cases and Digital Twins Solutions (ENTSO-E & DSO Entity, 2026); Batteries and Secure Energy Transitions (IEA, 2024).
Credit: Hasan Alawadhi, Isabel Hoyos, Dominica Wambold, Ariela Farchi, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Renewable power capacity growth by technology1 TW, 2013-2030
Chart: 
 | 47 | 46 | 26
 | 205 | 138 | 154
 | 297 | 565 | 872
 | 155 | 704 | 1499
 | 283 | 917 | 2046
0.0
0.5
1.0
1.5
2.0
2.5
3.0
3.5
4.0
4.5
5.0
16%
2013-2018
30%
2019-2024
33%
2025-2030
PV-utility
PV-distributed
Wind
Hydropower
Other
  Does not include Behind the Meter batteries which are expected to be ~2 TW total by 2030
Visibility
Grid operators can see availability and charge level of resources behind the meter, enabling forecasts on generation
Dispatch and constraint management
Aggregates and dispatches DERs, optimizing peak shaving and economics while adhering to security constraints. Plus, settle C&I flexibility payments1
Interoperability and market integration
DERMS bridge the system gap integrating different DERs to the tech stack with dispatch optimization and wholesale / flexibility markets
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
DERMS

## Slide 16: Virtual power plants aggregate thousands of distributed assets into a single, dispatchable, market-facing power plant
1
Aggregate thousands of distributed energy resources (DERs), e.g., rooftop solar, home and commercial batteries, EVs and smart thermostats, into one cloud-managed portfolio
2
Monitor every asset in real time and forecast generation, load and market prices
3
Optimize and dispatch the resources. Software decides when each asset charges, discharges or curtails to meet grid and market needs
4
Bid the combined capacity into wholesale energy, capacity and ancillary markets, or into utility programs
Fast & low-cost: Deploys in months
Cheaper than peakers: ~Half the cost
Pays participants: Owners earn for it
Scales with DERs: Solar, batteries, EVs
Boosts resilience: Peaks & emergencies
Market access: Patchy rules, FERC 2222 to 2028
Interoperability: Opt-in & multi-vendor control
Undervalued: Operators cap & under-credit VPPs
How do VPPs work?
Advantages
Disadvantages
Why are they critical for the energy transition?
Turn millions of DERs into firm, dispatchable capacity, with no new power plant built
Deliver peak capacity at roughly half the cost of a new gas peaker or grid-scale battery, easing affordability
Distributed batteries charging on midday solar and discharging at peak absorb renewable variability and displace fossil peakers
Among the fastest, cheapest ways to meet near-term load growth (e.g., data centers and electrification) while transmission lags
Source: Pathways to Commercial Liftoff: Virtual Power Plants (US DOE, 2025); 2025 North America VPP Market (Wood Mackenzie, 2025)
Credit: Vincent Sandow-Straesser, Ariela Farchi, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
5
Deliver the committed service and share the revenue back with participating owners
Distributed energy resources
Grid & wholesale markets
Aggregate
1
Monitor & forecast
2
Optimize & dispatch
3
Bid into markets
4
Deliver & settle
5
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
VPP

## Slide 17: Google and Voltus collaborate on building a virtual power plant to unlock flexible capacity for datacenters
Demand flexibility agreements are in place for data centers across the U.S.
The Voltus-Google BYOC deal unlocks 100MW of accredited capacity in PJM
Observations
A Virtual Power Plant (VPP) eases the need for asset-heavy solutions to meet increasing demand
Engaging distributed resources through demand flexibility can deliver significant energy benefits to households, commercial, and industrial consumers
  Estimates in the U.S. project up to $110- $170 B in savings over the next decade
  This presents a capital-efficient solution to improve grid utilization
BYOC is an example of how big tech can participate in grid investments; hyperscalers like Google bring in critical financing
  Data center investments can expedite the flexibility technology learning curve
0% 10% 20% 30% 40% 50%
Average electricity bill change
Supply mix cleared in PJM ‘28-’29 auction, MW
Chart: 
 | 46 | 20 | 18 | 5 | 4 | 2 | 2 | 1
4%
5%
Natural gas
Nuclear
Coal
Demand response
Hydro
Wind
Oil
Solar
Deal Dynamics
Google compensates Voltus to aggregate 100MW annually of customer flexibility over 3 years in a PPA-like structure
Voltus centralizes and compensates customers who participate in the VPP to respond to demand signals via an automated system
The agreement contributes to aggregating capacity to meet increased demand from data centers and bridge PJM’s shortfall, increasing grid resilience
Flexibility arrangement
Potential flexibility arrangement
Google locations with flexible data center agreements
Voltus will aggregate up to 100 MW of DERs each year (batteries, smart thermostats, and other flexible assets) from local businesses and homes into a Google-funded VPP
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
Case Study

## Slide 18: Advanced Metering enables two-way digital communication between utilities and customers, enabling smarter grid operations
1
Each meter communicates usage data between utilities and customers, creating a two-way digital link – instead of a one-way, reading-only method
2
The utility’s software receives the measurements, checks for errors, and organizes the data to ensure accurate billing and reliable operational information
3
The Meter Data Management System (MDMS) stores detailed consumption and generation data, applies validation rules, and prepares the data for billing, forecasting, outage detection, load analysis, and customer dashboards
4
The AMI data feeds many utility functions: outage detection, demand response, dynamic pricing programs, remote connect/disconnect, and dashboards that show customers their real-time electricity use
Better visibility: Real-time data
Foundation for a smart grid: Digital layer
Supports flexible demand: Dynamic control
Faster outage detection: Instant alerts
Multi-purpose: Smart meters at customer premises, networks & MDM with utilities
Upfront cost: Major investment, utility-paid
Integration complexity: System alignment
Customer acceptance: Trust and adoption
Data utilization: Despite high AMI adoption, deriving DER value of the analytics layer lags
Smart meter
1
Communication tower
2
Meter Data Management System (MDMS)
4
Utility software
3
Utility
5
How does Advanced Metering Infrastructure (AMI) 2.0 work?
Advantages
Disadvantages
Why is it critical for the energy transition?
Provides near- real-time visibility of electricity use
Enables dynamic tariffs, demand response, smart EV charging, and integration of rooftop solar and batteries at scale
Better data and price signals help shift and reduce consumption, lowering peak demand and allowing more renewables to operate without curtailment
Smarter AMI 2.0 platforms combine metering, grid monitoring, and customer apps into one digital layer for the grid
1-15 mins
Sources: Demand Response and Advanced Metering (FERC, 2025); Electricity Grids and Secruity Energy Transitions (IEA, 2024); What is advanced metering infrastructure (AMI) (IBM, 2026).
Credit: Sevgi Helin Tilkicioglu, Hasan Alawadhi, Isabel Hoyos, Dominica Wambold, Ariela Farchi, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
AMI

## Slide 19: Closing the AMI implementation gap requires interoperability mandates, targeted grants, and demand response market pricing
Chart: 
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
 | 7.4896 | 11.2957 | 16.3588 | 20.9115 | 25.1286 | 29.4375 | 33.3026 | 36.9682 | 41.5439 | 48.1249
 | 4.6047 | 8.9811 | 14.1407 | 18.1385 | 22.0655 | 25.7714 | 29.797 | 33.5621 | 37.5379 | 45.3658
 | 2.1815 | 4.1815 | 8.1815 | 15.1815 | 18.1815 | 22.1815 | 27.1815 | 32.1815 | 39.1815 | 44.1815
0
40
70
60
75
55
80
50
85
45
65
47
54
62
54
58
38
69
66
58
63
61
73
69
51
68
57
77
73
44
75
50
84
81
52
80
40
45
40
43
65
AMI adoption is largely achieved via the rate base and grant funding
Effective policy drives value capture, assisted by performance incentives and interoperability
Observations
The US pathway illustrates the ‘slow and steady’ route to AMI deployment in mature markets
  Funded through the utility rate-base PUC process, with costs and system savings passed through via OpEx reductions
  Evolution from AMI 1.0 to AMI 2.0 is in progress as meters age
Concessional capital delivered via grants, development finance, and incentives can accelerate utility and customer adoption especially in undercapitalized areas
Mandates may help drive high value data utilization and complete adoption throughout grid systems, maximizing the value of demand management programs
AMI is a foundational technology for many demand response capabilities
US AMI deployment percentage by application, 2015-2024
Residential
Commercial
Industrial
US federal grant programs offer concessional capital primarily for underserved utility areas, a model for EMDEs
The US AMI deployment ramp to ~80% across residential, commercial, and industrial reflects the efficacy but slow pace of financing via rate base
Enabling Policies | 
System Design | Set and govern time-of-use (TOU) rates, critical peak pricing, and real-time dynamic pricing to incentivize customer behavior Optimize pricing and measure impacts to ensure data translates into system savings
Regulation | Establish a national framework for AMI data sharing, interoperability, and cybersecurity Mandate functional interoperability, secure and non-discriminatory data governance, pay-for-performance, dynamic rating, and adoption
Public Finance | Authorize concessional capital (incentives, grants, DFIs) to drive adoption, focusing on under-capitalized utility systems or regions Require default time-varying rates to access grants and other public revenue sources
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
AMI

## Slide 20: Grid-forming inverters paired with intermittent energy sources and battery enable the stability support critical for grid reliability
1
GFMs connect to inverter-based resources (IBRs) like solar panels, wind systems, or batteries to transform electricity from DC to AC for grid integration in non-synchronous systems
2
GFMs adopted in place of Grid Following Inverters (GFLs) improve grid operations. While GFLs only match grid voltage and frequency, GFMs enable active control of the AC output through advanced power electronics
3
GFMs enable grid stability in by offsetting the loss of inertia from synchronous, turbine-based sources
Advantages over GFLs:
A voltage source independent of the grid
Frequency support during a disturbance
Monetizable synthetic inertia
Bi-directional control
Black start capabilities
How do Grid-Forming Inverters (GFM) work?
2
Grid forming inverter (GFM)
3
Utility scale grid
1
Power generation
& battery storage
Sources: Getting the Grid to Net-Zero (IEEE Spectrum, 2024); Introduction to Grid Forming Inverters (NREL, 2024); Optimization of power management in PV-based smart grids using grid-support and grid-forming inverters (PLoS, 2026).
Credit: Dominica Wambold, Sevgi Helin Cikicioglu, Stephanie Chen, Pia Doris Morrow, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Why is it critical for the energy transition?
To integrate non-firm, synchronous power sources, the grid needs an alternative source of stability
Allow high penetration of renewable, non-synchronous energy sources in a grid
Installing GFMs in place of GFLs as the default selection can strengthen the overall grid
Required for renewable resources and batteries to be compensated for inertia services
Incremental cost (firmware, PCB, sensors, testing)
Integration resistance, considered “emerging tech”
Without policy, OEMs lack demand signal to ramp at scale and reduce premiums
Increased lead times as supply chain is developed
Advantages
Disadvantages
Enables renewables and battery grid integration >60%
Provides the hardware basis for inertia services
Are cost-competitive and mature enough to deploy
Procurable via existing OEM supply chain
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
GFM

## Slide 21: Mass adoption of grid-forming inverters is required to connect the pipeline of available energy resources to the grid
Requiring GFMs for energy storage in the active queue is critical to safely deploy this capacity into the grid
Organic GFM deployment pathways do not meet NREL’s safe minimum share of 25% for systems with 60%+ IBRs
The historic trajectory reflects true organic growth, with no regional or national mandates or enforced standards in place prior to 2026, while the projected trajectory anticipates an uplift from the 2026 ERCOT and 2027 Southwest Power Pool mandates for new inverter-based resources as well as the initiation of enforcement under FERC directives and NERC requirements for PRC-029-1 compliance. Projections proceeded 2026 U.S. supply chain restrictions on Chinese-made grid-firming inverters.
Sources: US storage sector outlook (Wood MacKenzie, 2024); Queued Up (Lawrence Berkeley National Laboratory, 2026); Examining Supply-Side Options to Achieve 100% Clean Electricity by 2035 (NREL, 2022); Electric Power Monthly Tables (U.S. EIA, 2026); FERC Order 901 Directives Mapping (NERC, 2026).
Credit: Dominica Wambold, David Foye, Petr Jenicek, Birru Lucha, Hasan Alawadhi, Ariela Farchi, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
  Annual IBR capacity additions to the grid exceed 90% of all net-new grid energy resources
  Even anticipating NERC enforcement of reliability standards, current GFM adoption is not sufficient to ensure stability
  Nationwide, GFMs would remain well below the 25% threshold through 2033
U.S. IBR Capacity (GW) vs. GFM Inverter Share (%) Projections, 2015-2035
U.S. projected build through 2032 vs. active queue capacity, GW
Chart: 
 | 21 | 26 | 5 | 17 | 5 | 10 | 5
 | 108 | 108 | 30 | 79 | 34 | 105 | 12
CAISO
ERCOT
ISO-NE
MISO
NYISO
PJM
SPP
5.1x
4.2x
6x
4.6x
6.8x
10.5x
2.4x
Projected Storage Build
Active queue capacity
Chart: 
 | 0 | 0 | 0.02 | 0.15 | 0.95 | 6.1 | 23.4 | 49.8
 | 114.2 | 170.8 | 247.9 | 342.1 | 463.5 | 724.5 | 1218 | 2010
0%
20%
40%
60%
80%
100%
2015
2026
2035
Cumulative IBR Fleet (GW)
GFM Fleet Share of Inverters (% of total)
  25% is NREL’s estimated minimum GFM inverter share to support high IBR systems. Localized concentration can drive risk even at higher levels
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
GFM

## Slide 22: Flexible AC transmission systems are critical, stabilizing power flow and voltage in real time for safe and reliable grid operations
1
When demand changes, renewable output fluctuates, or a line approaches its limit, causing voltage drops, overload risk, or unstable power flow
2
FACTS control systems measure voltage, current, and phase angle, and detect deviations from normal operating limits
This helps controllers determine whether power must be injected or absorbed, or redirected
3
High-speed electronic valves switch on or off, changing electrical conditions on the line by adjusting voltage support or line impedance
4
The correction prevents overloads, stabilizes voltage, and allows more power to flow safely through the network
Increases line capacity: Better utilization
Reduces congestion: Optimized flow
Enables to avoid new lines: Faster deployment
High capital cost: Device costs
Complex control systems: Advanced software
Specialized maintenance: Skilled workforce
How do FACTS for grid systems work?
Advantages
Disadvantages
Why is it critical for the energy transition?
Allow operators to actively control power flow and voltage in real time, allowing existing AC transmission lines to operate more effectively
Provide fast, dynamic control that helps integrate renewables without waiting for new transmission lines
Reduce the need for grid expansions by increasing the usable capacity of existing infrastructure
Play a critical role in congested corridors and renewable-heavy regions
Sources: How Advanced Transmission Technologies Can Revamp the US Power Grid (WRI, 2025); Pathways to Commercial Liftoff: Innovative Grid Deployment (US DOE, 2024).
Credit: Sevgi Helin Tilkicioglu, Hasan Alawadhi, Pia Doris Morrow, Vincent Sandow-Straesser, Ariela Farchi, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
1
Transmission Line
2
FACTS systems
3
Controlling
4
Stabilizing Transmission
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
FACTS

## Slide 23: FACTS devices reduce transmission bottlenecks and reliability risk by controlling power flow and voltage
Thyristor-based2
VSC-based1
1Uses voltage-source converters. It is fast and flexible. 2Prove technology, mainly used to control voltage (reactive power), less flexible. 3Selected not exhaustive Source: SVC PLUS (STATCOM) (Siemens Energy, 2025); Static Var Compensator (SVC) (Hitachi, 2025); Thyristor controlled series compensation (Hitachi, 2025); FACTS (ABB, 1999); Fixed series compensation (Hitachi, 2025); Unified power flow controller (Astrophysics Data System, 2001); Phase shifting transformer (PST) (Entsoe, 2025); Flexible AC Transmission System (EEP, 2015).
Credit: Sevgi Helin Tilkicioglu, Stephanie Chen, Hasan Alawadhi, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Flexible AC Transmission Systems (FACTS)3
Category
System
Operational / investment value
Deployment maturity
TCSC – Thyristor-Controlled Series Capacitor
SSSC – Static Synchronous Series Compensator
STATCOM – Static Synchronous Compensator
TSSC – Thyristor-Switched Series Capacitor
TCSR – Thyristor-Controlled Series Reactor
SVC – Static VAR Compensator
UPFC – Unified Power Flow Controller
IPFC – Interline Power Flow Controller
Series
Shunt
Combined series-shunt
Control line impedance or inject series voltage to manage line loading
Inject or absorb reactive power to regulate local voltage
Coordinate series and shunt control to manage power flow and voltage
Combined series-series
Coordinate power flow across multiple transmission lines
Helps operators maintain voltage stability during heavy load, renewable output swings, or grid disturbances. Useful where voltage limits are blocking new load or renewable interconnection
Helps operators balance loading across multiple transmission lines in the same corridor. Useful where one path overloads while nearby lines remain underused
Provides high-control capability on critical corridors by managing both line flow and voltage from one installation. Useful where a single constrained corridor has high reliability or congestion value
Helps operators relieve overloaded lines by shifting power flows across the network. Useful where congestion is recurring and new transmission is slow, expensive, or difficult to permit
Low
High
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
FACTS

## Slide 24: Grid-scale batteries offer storage solutions for intermittency, transmission and distribution nodes, and reserve capacity
1
At Generation - co-located with intermittent generation charge during peak production and discharge during evening ramp, reducing the need for curtailment while producing a more predictable grid energy source
2
Storage as a Transmission Asset (SATA) - using grid-scale storage at weak or congested nodes to reinforce and strengthen the existing transmission network
3
Nodal reinforcement at Distribution - supports localized grid resilience and manages extreme load swings from clustered private assets or industrial manufacturing at the substation level without overloading transformers
How do grid-scale batteries work?
Advantages
Disadvantages
Why is it critical for the energy transition?
Pairing battery with renewable sources increases their ease of integration and value to grids and generators
Solar + storage is the fastest energy technology to deploy, enabling it to capture investment and meet rising electricity demand
Increasingly attractive for capacity and reserve functionality as cost and ease of digital integration improve due to location flexibility and fast-response capabilities
LDES as an alternative to new natural gas peaking capacity can avoid stranded asset buildouts with better scalability and flexibility
1Storage as a transmission asset
Sources: How battery storage could unlock the grid and make power more affordable (World Economic Forum, 2026); Energy Storage Enters the 100 Gigawatt Era (BNEF, 2026), Why batteries are the electric grid’s most powerful asset (SEIA, 2025), Grid Scale Storage (IEA, 2024).
Credit: Dominica Wambold, Ariela Farchi, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
2
Batteries + Transmission (SATA1)
Batteries + Intermittent Generation
1
3
Batteries + Distribution
Battery Energy Storage Systems (BESS) and Long-Duration Energy Storage (LDES) are among the most scalable type of grid-scale storage.
Reduces curtailment: Higher system value
Baseload matching: Combined with VREs
Smoothing the curve: Via energy shifting
Multi-purpose: Offer peak shaving, load smoothing, and grid stability services (with GFMs)
Reduced CapEx: With nodal reinforcement
Revenue uncertainty: Highly dependent on electricity market compensation mechanisms
Duration constraints: For cost competitive technologies (though improving)
LDES cost profile: Dependent on subsidy
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
Battery Storage

## Slide 25: ERCOT and CAISO have driven highest U.S. battery deployment; CAISO’s contracts helped achieve grid stability with renewables
ERCOT Battery Fleet, 2020-20261
CAISO Battery Fleet, 2020-20261
Private investment and arbitrage returns drove high battery deployment in ERCOT
CAISO leads battery deployment, surpassing 15GW of rated power in 2025
Observations
Battery deployment continues to accelerate as battery cell costs reduce and duration is extended
The global battery storage market is expected to exceed $100B in 2026, led by grid-connected batteries (~80%)2
Batteries can help balance the grid, complement renewables, and lower customer electricity costs
Regulatory uncertainty, permitting, interconnection delays, and saturation are investor challenges
Merchant project finance and ancillary markets are key financing mechanisms
Tolling & hybrid agreements are emerging, and some developers are shifting towards behind-the-meter, contract-backed deals
Contracts (capacity, resource adequacy) offer lower risk profiles
Chart: 
 | 0.1 | 0.212 | 0.822 | 2.021 | 3.985 | 7.886
 | 0.112 | 0.61 | 1.199 | 1.964 | 3.901 | 6.002
 | 0.22025 | 1.026 | 2.621 | 6.059 | 11.766 | 22.853
2020
0
2021
1
1
2022
2023
2024
2025
Chart: 
 | 0.355 | 0.456 | 2.175 | 4.578 | 7.282 | 11.302
 | 0.101 | 1.718 | 2.403 | 2.704 | 4.02 | 4.668
 | 1.822 | 8.5698 | 17.7017 | 28.0638 | 44.0488 | 60.5675
2020
0
2021
2022
2023
2024
2025
Energy Capacity (GWh)
New Rated Power (GW)
Existing Rated Power (GW)
ERCOT’s pure merchant risk model with energy arbitrage and ancillary services revenue, paired with permissive permitting, accelerated battery deployment and reduced ratepayer bills. RTC+B should help incentivize longer duration arbitrage, helping increase total energy capacity in the system
Mandates drove utility capacity contracts, unlocking institutional capital to fund a high energy capacity fleet. Though market spreads compressed, CAISO still leads the U.S. in deployment
Energy Capacity (GWh)
New Rated Power (GW)
Existing Rated Power (GW)
1Modo Energy reporting cross-referenced with CAISO and ERCOT data, respectively
Sources: ERCOT Annual Buildout Report (Modo Energy, 2026); CAISO battery fleet crosses 15 GW after record 4.7GW year (Modo Energy, 2026); Batteries have reshaped ERCOT’s Ancillary Services Procurement (Waldoch, 2026); Understanding Battery Energy Storage Systems (Texas Solar + Storage Association, 2026); Battery storage is scaling up and taking on a larger system role (IEA, 2026); World Energy Investment (IEA, 2026); Special report on battery storage (CAISO, 2025), Gridstatus.io (Grid Status, 2026).
Credit: Dominica Wambold, Ariela Farchi, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
Battery Storage

## Slide 26: High Voltage Direct Current enables multi-GW power transfer over thousands of kilometers efficiently
1
2
3
How do HVDC Transmission Lines work?
Advantages
Disadvantages
Why they are critical for the energy transition?
HVDC can move large loads of power over long distances with lower losses and precise control
Makes it practical to connect remote renewables (offshore wind, desert solar, large hydro) to distant demand centers
By reducing losses and unlocking large-scale renewables, HVDC cuts the need for fossil generation and extra backup capacity
Efficient for long distance: Lower losses
Ability to connect asynchronous (different frequencies)1 systems: Grid bridging
Suitability for underwater applications: Subsea capable
Ability to handle longer periods of overload operations: Stable transfer
High upfront cost: Major investment
Greater complexity in components: Advanced equipment
Power generation
AC Transmission Line
AC Transmission Line
Distribution and end use
A converter station transforms AC into direct current (DC), which flows in one steady direction, making long-distance transmission more efficient
In HVDC lines the DC power moves through a line with lower losses, better controllability, and greater efficiency than an equivalent AC line
A second converter station changes the DC back into AC so it can be used by the local grid
1AC grids must stay synchronized with same frequency and timing. When two grids run at different frequencies (e.g., 50 vs 60 Hz) or aren’t in sync, a direct AC connection would be unstable and HVDC interconnection via DC conversion would be needed
Source: Assessing HVDC Transmission for Impacts of Non‐Dispatchable Generation (EIA, 2018).
Credit: Sevgi Helin Tilkicioglu, Hasan Alawadhi, Pia Doris Morrow, Vincent Sandow-Straesser and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
AC to DC converter
1
HVDC Transmission Line
2
DC to AC converter
3
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment
HVDC

## Slide 27: U.S. grid expansion is a coordination challenge across rules, capital, assets and siting which causes significant delays
Primary Decision Gate
Secondary Influence
Who is included | Roles & Responsibilities |  | Planning & Need | Financing & Cost Allocation | Interconnection application | Siting& Permitting | Procurement & Construction
FERC | Federal rule setter: Sets interstate transmission, wholesale market, interconnection, cost-allocation rules |  |  |  |  |  | 
DOE / GDO / national labs | Federal deployment enabler: Identifies national infrastructure needs, funds and de-risks projects, and informs planning |  |  |  |  |  | 
NERC + Regional Entities | Reliability authority: Sets enforceable reliability, planning, operations and cybersecurity standards |  |  |  |  |  | 
RTOs, ISOs, ERCOT | Regional planners / operators: Operate grid and markets, manage congestion & coordinate regional interconnection |  |  |  |  |  | 
State PUCs / PSCs, | State regulatory gatekeepers: Approve utility investment, rates, cost recovery and siting where applicable |  |  |  |  |  | 
State Energy Offices | State policy coordinators: Align with state energy policy, resilience & energy targets and federal funding opportunities |  |  |  |  |  | 
Transmission owners, IOUs, public power, co-ops | Asset owners / builders: Build, own, maintain and modernize transmission and distribution assets |  |  |  |  |  | 
Federal land agencies, state/ local gov., Tribal gov. | Permitting and public acceptance actors: Determine whether projects can be sited, permitted & built on acceptable timelines |  |  |  |  |  | 
Generators, DCs, industrials | Interconnection customers / demand drivers: Create generation and load needs, submit interconnection requests |  |  |  |  |  | 
OEMs / EPCs / workforce / investors | Delivery and capital ecosystem: Provide equipment, EPC services, qualified labor, grid technologies and capital |  |  |  |  |  | 
1Interconnection Request to Commercial Operation Date. 2. Q2 2025 at ~2.5 years (128 weeks) for power transformers and ~2.8 years (144 weeks) for Generator Step-Up (GSUs).
Sources: FERC Orders 1920 and 2023; CITAP (DOE, 2024); Long-Term Reliability Assessment (NERC 2024); 2025 Edition Characteristics of Power Plants Seeking Transmission Interconnection As of the End of 2024 (Berkeley Lab, 2025); Wood Mackenzie Q2 2025 Survey Results.
Credit: Ilayda Tezcan, Ariela Farchi, Pia Doris Morrow, and Gernot Wagner. Share with attribution: Wagner et al. “Powering Grids,” Columbia Business School Climate Knowledge Initiative (28 September 2026).
Delay hotspot stages
Build & Deploy
Finance
Regulate
Demand
>4 yr
median IR-to-COD1
~4 yr
federal permitting
>2.5 yr2
equipment lead times + constrained EPC capacity
Industry Overview
Solutions: Optimize
Solutions: Modernize
Solutions: Expand
Deployment

## Slide 28
Hasan Alawadhi
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Gunay Kiran
MS in Sustainability Management
Climate Knowledge Initiative Fellow
Christy Wong
MPA, Columbia SIPA
Climate Knowledge Initiative Fellow
Vincent Sandow-Straesser
MS in Climate Finance
Climate Knowledge Initiative Fellow
Sevgi Helin Tilkicioglu
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Stephanie Chen
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Ryon Roque
BS in Civil Engineering
Climate Knowledge Initiative Fellow
CKI Grids Team
Fellows
Dominica Wambold
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Ilayda Tezcan
MBA, Columbia Business School
Climate Knowledge Initiative Fellow

## Slide 29
Isabel Hoyos
MS in Sustainability Management
Former Senior Staff Associate
CKI Team Staff, Faculty, and Alumna