## Slide 1: Geothermal Heating and Cooling
Gernot Wagner, Pia Doris Morrow, Zacharia Thurston, Faradisa Anintya, Una Oljaca, Leo Gordon, Hassan Riaz, Hyae Ryung Kim, and Isabel Hoyos
10 March 2026
Cite as: Wagner et al. “Geothermal Heating and Cooling,” Columbia Business School Climate Knowledge Initiative (10 March 2026).

## Slide 2: Geothermal Opportunity

## Slide 3
Nearly 80% of geothermal energy today is used for heating and cooling (42% heat pumps, 26% district heating systems), not electricity generation. Deployment is concentrated in 10 countries accounting for 90% of global use, with China alone representing 50% of all heating and cooling capacity.
Geothermal heating and cooling is a mature, proven technology that is projected to double by 2050 through residential and district heating expansion, with significant untapped potential for decarbonizing building thermal loads.
Geothermal electricity currently supplies less than 1% of global power, with conventional installations limited to ~16 GW in key geographic areas. Yet, geothermal energy reserves are multiples larger than all known oil and gas reserves, with the technical potential to meet global electricity demand 140 times over.
Global energy demand is projected to rise 10 to 20% by 2050, driven by growth in emerging economies, electrification, and AI data center expansion. This demand is creating urgent need for firm, reliable, round-the-clock clean power, a role geothermal is uniquely positioned to fill.
Next-generation technologies including horizontal drilling, enhanced geothermal systems, closed-loop systems, and AI-enabled exploration are expanding geothermal's reach to virtually every region around the globe, overcoming the geographic constraints that limit conventional geothermal today while reducing costs.
Technological, policy, and financial synergies with the oil and gas industry can dramatically reduce costs and accelerate deployment, particularly by applying advanced subsurface modeling to reduce exploratory drilling risk, the highest barrier in project development.
With continued innovation and cost declines, geothermal could become cost competitive with solar and wind plus storage by 2035 and meet up to 15% of global electricity demand growth by 2050, representing 800 GW of capacity and 6,000 TWh annually.
Geothermal electricity will play an outsized role in select markets, supplying 5 to 45% of power generation in countries like the U.S., Kenya, the Philippines, and Indonesia.
Executive Summary
Opportunity

## Slide 4: Geothermal energy technologies span heating & cooling and power generation, with conventional approaches most widely deployed
Geothermal Opportunity
Key pathways for harnessing geothermal energy for heating & cooling and power generation
Conventional/hydrothermal
Underground thermal energy storage
Geothermal heat pumps
Direct-use heat
Borehole thermal energy storage
Aquifer thermal energy storage
Mine thermal energy storage
Advanced geothermal/ closed-loop systems
Enhanced geothermal systems
Next-generation technologies (commercialization <5 years)
Superhot rock
Frontier technologies (commercialization 5+ years)
Geopressured systems
Heating and cooling
Power
Production
Storage
Production
Storage
Cavern thermal energy storage
Pit thermal storage
Reservoir thermal storage
Magma-based geothermal
High-temperature geothermal energy storage
Geomechanical energy storage

## Slide 5: Today, 10 countries consume 90% of global geothermal energy, with almost 80% of end use for heating and cooling
Heating: China is the most significant country, accounts for nearly 50% of global geothermal final energy consumption, dedicated entirely to space heating.
Electricity: The U.S., Indonesia, Türkiye, the Philippines, and New Zealand generate two-thirds of global geothermal electricity, with Iceland, Italy, Kenya, Mexico, and Japan contributing an additional 25%.
Total final geothermal energy consumption
by consuming countries, 2023
Total final geothermal energy consumption
by application, 2023
Opportunity: Heating & cooling
Chart: 
 | 620.8403 | 590 | 220 | 110 | 60 | 50 | 50 | 30 | 30 | 20 | 20
0
400
500
300
1.400
200
100
Global
U.S.
Turkiye
Sweden
Indonesia
Iceland
Japan
New Zealand
Germany
Philippines
Consumption (PJ)
China
0.2%
0.5%
1.0%
3.7%
2.5%
5.2%
30.0%
0.3%
18.8%
0.3%
14.6%
% of geothermal to total energy consumption, 2023
Chart: 
 | 100 | 58.13 | 32.06 | 24.95 | 21.79 | 21 | 21
 | 41.87 | 26.07 | 7.11 | 3.16 | 0.79
Total
42%
Geothermal heat pumps
26%
District heat
7%
Direct residential & comm.
3%
Agriculture & fishing
1%
Industry & other
Power (Electricity)
100%
21%
1,400 PJ
Heating & cooling (79%)

## Slide 6: By 2050, geothermal heating use is projected to almost double, driven largely by China and building and district heating
Geothermal heating use doubles in 2050 under a realistic government Stated Policies Scenario (STEPS), with China as the biggest source of growth. Yet, it remains only 0.5% of total heat consumption globally.
From the use-case perspective, nearly 90% of geothermal heating consumption comes from residential and commercial buildings, mainly through district heating networks, including thermal baths in the tourism and wellness sector.
Geothermal heating consumption (PJ), projection by region 2023-2050
Increase (%) by heating application globally, 2023-2050
Opportunity: Heating & cooling
Chart: 
 | 1106 | 600 | 160 | 135 | 145 | 35 | 31
 | 2000 | 1250 | 240 | 185 | 175 | 55 | 41
0
500
1.000
1.500
2.000
Global
China
U.S.
EU
Other Europe
Japan
RoW
2023
2050
Incl. Sweden, Germany, France
Incl. Türkiye, Iceland, Norway
2.0%
0.5%
0.5%
1.5%
0.2%
<0.1%
0.5%
xx%
% of geothermal to total heat consumption, by 2050
Chart: 
 | 101 | 12 | 6 | 6
 | 89 | 6
Total increase
89%
Res. & comm.
6%
Industry & other
Agriculture & fishing
6%

## Slide 7: Global geothermal heating and cooling capacity is ~173,300 MWth, with over 50% of global installed capacity in China
Observations
China holds over 50% of installed capacity, and the 10 largest consumers account for ~90% of the global total.
Europe is expected to scale as a result of the EU Green Deal.
Geothermal heat pumps account for 72% of installed capacity, while 28% is direct use.
Global geothermal potential up to 3 km and >90ºC is ~320 TW, while the potential for <90ºC increases 10x.
Global geothermal heating & cooling installed capacity, MWth
Opportunity: Heating & cooling
Largest installed capacity per capita (KWth) | 
Iceland | 7.177
Sweden | 0.69
Finland | 0.41
Switzerland | 0.27
Norway | 0.21

## Slide 8: GSHPs could reach millions of U.S. homes by 2050, enabled by tax incentives, business innovation, and workforce development
Total U.S. residential potential
(million homes equivalent)
Total U.S. commercial potential
(million homes equivalent)
Observations: Key drivers to successful liftoff
Policy and financial support: Tax incentives are often the single most impactful factor making commercial geothermal projects viable. The OBBA spared ground sourced heat pumps (GSHPs).
Workforce readiness: Availability of trained drillers and installers is a major bottleneck; national and regional training pipelines and certification programs are needed to expand this workforce.
Tech and deployment: Demonstration projects across diverse geographies and use cases (urban, rural, cold and hot climates) help de-risk investment and validate business models. Standardized designs, permitting, and interconnection protocols are needed to streamline and reduce soft costs.
Business model innovations: Utility-driven thermal energy networks (TENs utility-ownership) could provide a scalable and replicable model, especially as an alternative to gas infrastructure.
Opportunity: Heating & cooling
Chart: 
| 2020 | 2023 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
 | 25 | 25 | 28 | 32 | 36 | 41 | 46
 | 11 | 11 | 12 | 14 | 16 | 18 | 20
 | 1 | 1 | 2 | 3 | 4.5 | 6 | 8
 | 1 | 1 | 2.5 | 4.5 | 8 | 13 | 20
Chart: 
| 2020 | 2023 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
 | 18 | 18 | 20 | 23 | 26 | 29 | 32
 | 8 | 8 | 9 | 10 | 12 | 14 | 16
 | 0.5 | 0.5 | 1 | 1.5 | 2 | 3 | 4
 | 0.5 | 0.5 | 0.8 | 2 | 4 | 8 | 16
Liftoff
Liftoff
Economic potential
Market potential
Expected installation (baseline)
Liftoff trajectory

## Slide 9: Global energy demand expected to grow ~10-20% by 2050, largely driven by emerging economies, electrification, and data centers
India, ASEAN*, Africa, and the Middle East will be responsible for ~65-95% demand growth
New data centers and electrification of industry and buildings will drive ~5-10% demand growth
Observations
By 2050, global energy demand is expected to grow 11 to 8%, with 66 to 95% of that growth concentrated in emerging economies such as ASEAN, India, and the Middle East — regions that currently rely heavily on fossil fuels for baseload power.
New demand will likely stem from the electrification of industry and buildings, accounting for over half of demand. Data centers (2,500 to 4,500 TWh, or 5 to 9% of demand), green hydrogen (179 Mtpa, driving ~20% annual power demand growth), and EVs (~10% annual growth, with BEVs dominating car sales) will add to this surge.
To meet such demand, economies will need reliable, non-intermittent baseload solutions for their energy grids.
Opportunity: Power
Chart: 
1990
2000
2010
2020
2030
2040
2050
Chart: 
 | 11.5 | 13 | 20
 | 11.5 | 13 | 20
 | 0.75 | 1 | 10
 | 0.75 | 2 | 6
 | 0.75 | 2 | 8
1
1
2023
1
2
2
2030
2050
27
31
64
+3.5%/ year
Industry
Buildings
H2 and Synfuels
Data Centers
Transport
Global power consumption by sector (thousands of TWh)
Global primary energy demand (million TJ)
India
ASEAN
Africa
Middle East
Rest of World
Latin America
China
North America
OCED Europe
OECD Asia Pacific
~10-20%
Growth

## Slide 10: With vast untapped thermal resources and emerging technological advancements, geothermal power is primed for a breakout decade
Potential of proven oil & gas reserves vs. 1% geothermal resources*, trillion MWh
Projected global geothermal under different scenarios, GW
Historical installed geothermal capacity by country, GW
Opportunity: Power
Chart: 
 | 2793 | 2216 | 2252 | 2133 | 2152 | 2285 | 2274 | 2214 | 2229 | 2382 | 2405 | 2409 | 2592 | 2607 | 2514 | 2542 | 2517 | 2483.3 | 2444.3 | 2555.4 | 2571.9 | 2596.7 | 2648.6 | 2695.8 | 2725
 | 525 | 785 | 785 | 805 | 820 | 850 | 850 | 980 | 1052 | 1189 | 1189 | 1226 | 1336 | 1343.5 | 1403.5 | 1438.3 | 1533.3 | 1808.3 | 1948.3 | 2130.7 | 2130.7 | 2286.05 | 2360.33 | 2597.51 | 2638.8
 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1916.1 | 1916.1 | 1916.1 | 1916.1 | 1928.1 | 1928.1 | 1928.1 | 1928.1 | 1932 | 1951.8 | 1951.8
 | 18 | 18 | 18 | 15 | 15 | 15 | 23 | 23 | 30 | 77 | 94 | 114 | 162 | 311 | 405 | 624 | 821 | 1063.7 | 1282.518 | 1514.688 | 1613.188 | 1676.17 | 1691.338 | 1691.338 | 1734.338
 | 418 | 417 | 372 | 382 | 382 | 437 | 437 | 456 | 578 | 617 | 742 | 742 | 768 | 840 | 966 | 990 | 985 | 985 | 1009 | 1009 | 1043 | 1043 | 1050 | 1050 | 1275.4
 | 843 | 843 | 853 | 953 | 953 | 953 | 953 | 958 | 958 | 958 | 883 | 808 | 833 | 858 | 868 | 898 | 923.5 | 948.5 | 948.5 | 973.5 | 973.5 | 998.5 | 998.5 | 998.5 | 998.5
 | 58 | 58 | 58 | 58 | 128 | 128 | 128 | 128 | 128 | 163 | 198 | 198 | 205.5 | 205.5 | 366.1 | 618.9 | 652.9 | 672.9 | 683.8 | 683.8 | 863.13 | 863.13 | 949.73 | 984.73 | 939.73
 | 172 | 202 | 202 | 202 | 202 | 232 | 422 | 485 | 575 | 575 | 575 | 665 | 665 | 665 | 665 | 665 | 665 | 709.958 | 755.558 | 755.558 | 756.158 | 756.208 | 757.58 | 787.58 | 787.58
 | 590 | 573 | 666 | 707 | 642 | 671 | 671 | 671 | 671 | 695 | 728 | 728 | 728 | 729 | 768 | 768 | 767 | 767.19 | 767.19 | 767.19 | 771.79 | 771.79 | 771.79 | 771.79 | 771.79
 | 533 | 533 | 533 | 535 | 535 | 535 | 532 | 532 | 532 | 535 | 537 | 537 | 512 | 512 | 508 | 516 | 526 | 471.366 | 473.115 | 480.714 | 487.004 | 486.814 | 436.814 | 456.054 | 489.054
 | 144.71 | 144.71 | 144.71 | 162.71 | 165.71 | 165.711 | 165.711 | 165.711 | 165.711 | 165.711 | 165.711 | 217.461 | 217.461 | 217.461 | 217.461 | 217.361 | 206.86 | 206.86 | 206.86 | 261.86 | 261.86 | 258.84 | 262.66 | 262.66 | 262.66
 | 332 | 377.5417 | 423.0833 | 468.625 | 514.1667 | 559.7083 | 605.25 | 650.7917 | 696.3333 | 741.875 | 787.4167 | 832.9583 | 878.5 | 924.0417 | 969.5833 | 1015.125 | 1060.6667 | 1106.2083 | 1151.75 | 1197.2917 | 1242.8333 | 1288.375 | 1333.9167 | 1379.4583 | 1425
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
16
2
2012
2004
2016
2020
2024
United States
Indonesia
Philippines
Turkey
New Zealand
Mexico
Kenya
Iceland
Italy
Japan
Costa Rica
2000
Rest of World
2008
Chart: 
 | 2.55
 | 0
 | 1257
2.55
Proven fossil reserves
1% geothermal resources
Chart: 
 | 2.55
2.55
500x
potential energy
(all geothermal resources)
Chart: 
| 2010 | 2022 | 2023 | 2030 | 2035 | 2040 | 2050
 | 10000 | 15000 | 14850 | 22000 | 31000 | 40000 | 56000
 | 14850 | 25810 | 39630 | 52860 | 83340
 | 14850 | 29000 | 44250 | 59500 | 90000
 | 14850 | 38660 | 61080 | 79630 | 111120
0
10
20
30
40
50
60
70
80
90
100
110
120
Chart: 
 | 2405 | 2409 | 2592 | 2607 | 2514 | 2542 | 2517 | 2483.3 | 2444.3 | 2555.4 | 2571.9 | 2596.7 | 2648.6 | 2695.8 | 2725
 | 1189 | 1226 | 1336 | 1343.5 | 1403.5 | 1438.3 | 1533.3 | 1808.3 | 1948.3 | 2130.7 | 2130.7 | 2286.05 | 2360.33 | 2597.51 | 2638.8
 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1916.1 | 1916.1 | 1916.1 | 1916.1 | 1928.1 | 1928.1 | 1928.1 | 1928.1 | 1932 | 1951.8 | 1951.8
 | 94 | 114 | 162 | 311 | 405 | 624 | 821 | 1063.7 | 1282.518 | 1514.688 | 1613.188 | 1676.17 | 1691.338 | 1691.338 | 1734.338
 | 742 | 742 | 768 | 840 | 966 | 990 | 985 | 985 | 1009 | 1009 | 1043 | 1043 | 1050 | 1050 | 1275.4
 | 883 | 808 | 833 | 858 | 868 | 898 | 923.5 | 948.5 | 948.5 | 973.5 | 973.5 | 998.5 | 998.5 | 998.5 | 998.5
 | 198 | 198 | 205.5 | 205.5 | 366.1 | 618.9 | 652.9 | 672.9 | 683.8 | 683.8 | 863.13 | 863.13 | 949.73 | 984.73 | 939.73
 | 575 | 665 | 665 | 665 | 665 | 665 | 665 | 709.958 | 755.558 | 755.558 | 756.158 | 756.208 | 757.58 | 787.58 | 787.58
 | 728 | 728 | 728 | 729 | 768 | 768 | 767 | 767.19 | 767.19 | 767.19 | 771.79 | 771.79 | 771.79 | 771.79 | 771.79
 | 537 | 537 | 512 | 512 | 508 | 516 | 526 | 471.366 | 473.115 | 480.714 | 487.004 | 486.814 | 436.814 | 456.054 | 489.054
 | 165.711 | 217.461 | 217.461 | 217.461 | 217.461 | 217.361 | 206.86 | 206.86 | 206.86 | 261.86 | 261.86 | 258.84 | 262.66 | 262.66 | 262.66
3.5x by 2050 (56 GW)
5.2x by 2050 (83 GW)
5.6x by 2050 (90 GW)
Stated Policies
Announced Pledges
DOE Liftoff
Net Zero Emissions
In 2025, 32 countries had geothermal power, for a total of ~16 GW global capacity, from 3,700 production wells with an average 3 MWh capacity per well.
6.9x by 2050 (111 GW)

## Slide 11: Conventional geothermal power installations have reached ~16 GW but remain constrained to key geographic areas
Observations
The U.S., Indonesia, the Philippines, Mexico, Türkiye, New Zealand, Japan, Kenya, Iceland, and Italy lead in installed geothermal capacity.
Conventional geothermal relies on rare hydrothermal reservoirs—where heat, water, and permeable rock naturally align near tectonic boundaries like the Pacific Ring of Fire.
As a result, geothermal generation is concentrated in volcanically active regions. Most other nations face steep costs and technical barriers.
Conventional resources are too limited to assist in meeting global energy demand
Enhanced and closed-loop geothermal systems aim to overcome geographic limits, unlock deeper heat sources, and deliver 24/7 renewable power worldwide.
Geologically active areas show geothermal potential beyond countries with installed capacity
Opportunity: Power

## Slide 12: Next-generation technologies enable deeper drilling to unlock greater power potential
Heat reservoir formation process and access
The ability to drill deeper is key to accessing more power*
Opportunity: Power
1 km
2 km
3 km
4 km
5 km
6 km
7 km
8 km
Rainfall flows from higher elevations into the ground.
Water is heated by surrounding rock.
Water travels through faults and fractures.
Permeable rock traps and stores rising hot water or steam.
Geothermal reservoir is formed.
1
2
3
4
5
1
2
3
4
5
Next-generation
Hydrothermal
Depth (km)
Tech type | Depth & temp. (ranges depending on location) | Power potential
Hydrothermal | ~1-3 km, 90-370℃ (some may exceed) | 
Next-generation | ~5-7.5 km, 120-370℃ | 
Superhot rock | ~7.5+ km, +400℃ | 

## Slide 13: Next-generation drilling unlocks globalized clean energy access, with notable overlap in emerging economies by 2050
Global EGS hotspots concentrated in emerging economies
Potential for next-gen geothermal power capacity by region, GW (IEA projections)
Opportunity: Power
Chart: 
 | 0.05856 | 2.928 | 58.56 | 146.4 | 240 | 300
 | 0.03904 | 1.952 | 39.04 | 97.6 | 160 | 200
 | 0.01952 | 0.976 | 19.52 | 48.8 | 80 | 100
 | 0.015616 | 0.7808 | 15.616 | 39.04 | 64 | 80
 | 0.00976 | 0.488 | 9.76 | 24.4 | 40 | 50
 | 0.01952 | 0.976 | 19.52 | 48.8 | 80 | 100
500
600
400
700
300
800
200
900
100
0
2025
2030
2035
2040
2045
2050
0.1625
8
162
405
664
830
China
United States
India
Southeast Asia
Europe
Rest of the world
5-7.5 km
7.5-10 km
10-12.5 km
12.5+ km
Estimate
United States: 3,400 GW
China: 300 GW
India: 80 GW
Southeast Asia: 64 GW
Europe: 50 GW
Project InnerSpace
IEA
Global next-gen geothermal projections vary. Project InnerSpace’s projections likely reflect greater accuracy of global geothermal potential, driven by superior subsurface data collection. IEA estimates are deliberately conservative, focusing on what is deployable under today’s policy, cost, and financing conditions.
United States: 200 GW

## Slide 14: Geothermal power offers clean baseload capacity to replace retiring coal plants and prevent overreliance on peaker plants
Loss of baseload power leads to overreliance on peaker plants and can drive up costs for consumers
Heavy dependence on intermittent renewables without baseload capacity threatens grid reliability
Opportunity: Power
Fossil energy will plateau despite energy demand increasing.
Grids that are overreliant on wind and solar (intermittent energy) without baseload capacity risk rolling blackouts during periods of low renewable generation.
Cost of generation ($)
Hourly net load (year average) in California
Global final energy consumption for Continued Momentum scenario, by fuel, millions of terajoules
What is baseload?
28,000
26,000
24,000
22,000
20,000
18,000
16,000
14,000
12,000
10,000
0
12am
3am
6am
9am
12am
3pm
6pm
9pm
2020
2018
2019
2017
2016
2015
2014
2013
2012
Increased ramp
Potential overgeneration
Megawatts
Baseload
Mid-load
Peak load
Coal
N. gas
Nuclear
The most common sources of baseload power, chosen for their low LCOE. Gas can be used but has higher OpEx.
Baseload power is the minimum amount of electricity the electrical grid needs at any given time. Runs continuously at a steady output.
Chart: 
 | 24.5 | 25 | 40 | 24.5 | 24.5 | 24.5 | 24.5
 | 100 | 115 | 125 | 120 | 140 | 125 | 105
 | 45 | 77.5 | 110 | 90 | 120 | 110 | 98
 | 35 | 40 | 45 | 37 | 31 | 25 | 21
 | 2 | 8 | 10 | 12 | 16 | 18 | 21
 | 35 | 37.5 | 40 | 50 | 100 | 120 | 150
 | 10 | 11.8333 | 13.6667 | 15.5 | 17.3333 | 19.1667 | 21
1990
2000
2010
2020
2030
2040
2050
Other
Electricty
Hydrogen
Bioenergy
Natural gas
Oil
Coal

## Slide 15: Key barriers limiting geothermal deployment include exploration risks, drilling technology limits, and heat flow variability
Barriers to geothermal achieving global, dispatchable, and cost-competitive clean power
Opportunity: Power
Barrier | Description | Impact on Deployment | Emerging Solutions
Exploration Risk & Cost | High upfront cost for resource identification; drilling success uncertain | Major cost bottleneck; limits financing | AI/geophysical modeling, remote sensing, cheaper slim-hole drilling
Drilling Technology Limits | Conventional rigs struggle with deep/hard rock, high heat, and corrosive fluids | Limits depth/temperature access → limits energy yield | Advanced drilling (plasma, millimeter wave, laser), O&G transfer tech
Reservoir Stimulation & Permeability | Creating or maintaining fluid pathways in hot dry rock is challenging | Determines long-term productivity; EGS sites often fail after testing | Hydraulic shearing, closed-loop systems, supercritical fluid modeling
Materials & Corrosion Resistance | Equipment degradation in harsh conditions (heat, pressure, minerals) | Raises O&M costs and reduces lifetime of wells | High-temp alloys, ceramics, coatings
Power Conversion Efficiency | Efficiency drops at lower temperatures; limited by thermodynamic cycles | Restricts viable sites; reduces energy output | Supercritical CO₂ cycles, binary cycle optimization
Monitoring & Reservoir Management | Hard to track subsurface dynamics and avoid induced seismicity | Safety/regulatory constraints; performance loss over time | Fiber-optic sensing, real-time data analytics, seismic monitoring
Transmission & Integration | Geothermal sites often remote; grid connection costs high | Slows scalability and investment interest | Colocation with industrial heat users, modular systems
Public & Regulatory Challenges | Concerns about seismicity, permitting delays | Adds time and uncertainty to projects | Streamlined EGS permitting frameworks
Major Barriers

## Slide 16: Exploratory drilling carries the highest project development risk, which can be reduced through advanced subsurface modeling
High drilling costs and geological uncertainty make exploration the riskiest phase of geothermal development
Inaccurate subsurface modeling can mischaracterize resources, resulting in failed wells and losses exceeding $10M per site
Geothermal Opportunity
AI-enabled companies are helping de-risk exploration by providing solutions for accurate subsurface reconnaissance and drilling
Cumulative Cost
Years 1-2
Years 2-3
Years 4-6
Years 6-8
Years 8+
Stage
Risk Level
Surface Reconnaissance $1M-2M
Exploratory Drilling
$20M-$30M
Production Drilling
$20M-$120M
SAGS Power Plant
$20M-$200M
Operations and Maintenance
Upstream Resource Development
Downstream Plant Construction and Operations
100%
50%
0%
Time
Subsurface temperature, permeability, and fluids can be confirmed only through drilling; surface surveys and models provide limited accuracy, making exploratory wells costly and high risk.
Inaccurate measurements of reservoir pressure can reduce recoverable power; length of estimated drilling time may ward off willingness for upfront investment in exploratory stages.
Geothermal project finance has initial high risk: Tens of millions of dollars are spent upfront on drilling with no guarantee of a viable resource. This uncertainty makes traditional financing challenging, often requiring government support, insurance, or hybrid financing to secure bankability.
Applied AI geosensing to discover new reservoirs around the underperforming Lightning Dock geothermal facility, which now ranks among the most productive in the U.S.
Focus
Resource Risk
Operational Risk

## Slide 17: Technological, policy, and financial synergies with the oil & gas industry can drive down geothermal costs and scale deployment
Geothermal Opportunity
Technological synergies
Policy priorities
Cost trends for successful synergy
Chart: 
 | 5 | 8 | 5 | 4 | 6 | 8
 | 5 | 8 | 4 | 6 | 8 | 4
5
4
6
3
7
2
8
1
0
Geoscience
Well production
Formation evaluation
Drilling competencies
Surface production
Reservoir engineering
Oil & gas engineer
Geothermal engineer
Geothermal and O&G engineering skillset overlap*
Competency level
Subsurface exploration and drilling
Oil and gas data on hydrocarbon reserves and well logs can cut geothermal exploration costs and improve success rates.
Well completion and management
Simulation and zonal isolation techniques from O&G enhance reservoir longevity and reinjection efficiency.
Data and digital innovation
O&G’s digital twins and real-time monitoring tools improve geothermal reservoir modeling and predictive maintenance.
Countries leading the workforce transition
Chart: 
 | 12 | 37 | 11 | 40
12%
37%
11%
40%
Evaluation, planning, management
Non-transferrable expertise
Surface facilities
Drilling & completion
Chart: 
 | 12 | 24 | 7 | 57
12%
24%
7%
57%
Chart: 
 | 6 | 18 | 11 | 65
6%
18%
11%
65%
Share of geothermal technology investments that overlap with the O&G industry
Conventional
EGS
AGS
~10%
~20-30%
~30%
Cross-sector skill transfer can unlock faster workforce deployment and lower technical risk.
U.S.: DOE GeoVision + GEODE Consortium
Iceland: Integrated geothermal-O&G training pipeline
Türkiye: EGS demonstration from hydrocarbon basins
R&D and learning-by-doing acceleration
Reduction in exploration risk and resources mapping
Drilling and completion efficiency gains via O&G rigs and methods
Enhanced geothermal systems (EGS) exhibit the highest transferable expertise (~70%), while advanced geothermal systems (AGS) retains greater reliance on O&G drilling and surface integration.
3

## Slide 18: Underground thermal energy storage offers greater capacity potential than battery alternatives and natural gas
Geothermal Opportunity
Natural Gas
Solid Batteries
Minutes
Hours
Days
Weeks
Months
Years
Typical Energy Storage Capacity
10 BTU
10^4 BTU
10^7 BTU
10^10 BTU
10^13 BTU
Wh
KWh
MWh
GWh
TWh
Super-Capacitor
Fly Wheel
Gravity
Flow Battery
Hydrogen
Ramped Hydroelectric
Compressed Air
Underground thermal energy storage (UTES)
Geologic storage method
Non-geologic storage method
UTES
Supply Cold
Store Excess Cold
Integrated Cooling Loop
Cold Underground UTES
Electrical Cooling Load
Winter
Winter
Summer
With Cold UTES
Standard
Supply Heat
Store Excess Heat
Integrated Heating Loop
Hot Underground UTES
Produce Power
Electrical Heating Load
Summer
Summer
Winter
With Hot UTES
Standard
Both systems can coexist regardless of season due to the earth’s insulating properties, but storage of excess heat and cold will be more likely during the summer and winter, respectively (i.e., lakes in the summer vs. winter).

## Slide 19: Geothermal Heating and Cooling Technology

## Slide 20
Geothermal heating and cooling involves the harnessing of stable underground temperatures via closed- or open-loop circulation.
  Among conventional geothermal technologies, geothermal heat pumps (GHPs) are the most common, accounting for 72% of global installed H&C capacity. GHPs can harness lower temperatures (4-22ºC) at an average COP of 3-5.
  Advancements in next-generation geothermal technologies have expanded the use cases, temperature range, and production capacity of geothermal heating and cooling compared with conventional geothermal technologies.
Global geothermal heating and cooling capacity is 173,303 MWth. Over 50% of global installed capacity is in China, while Iceland has the largest per-capita installed capacity (7.18 kWth).
Drilling is the largest and most variable cost driver of both conventional and next-generation geothermal heating and cooling, typically contributing over 50% of total project cost and/or LCOE.
  For conventional geothermal technologies, geography and loop design are the primary drivers of drilling costs, due to dependence on hydrothermal reservoirs and the comparative costs of vertical versus horizontal borehole loops.
  For next-generation geothermal technologies, well depth and temperature are the primary drivers of drilling costs.
Synergies with the oil and gas industry can push down geothermal heating and cooling costs and improve efficiency, and growing interest from the O&G industry has led to partnerships and upfront investments, particularly for next-generation geothermal.
  Subsurface data and modeling techniques from the O&G industry can help de-risk geothermal heating projects and lower costs, as demonstrated by the Eavor-LiteTM demonstration project in Alberta, Canada.
  Technical synergies between the geothermal and oil and gas industries highlight strong workforce transferability, which can help streamline geothermal commercialization.
Due to limited deployment of conventional geothermal for industry heating or direct use, next-generation geothermal may bypass resource-related constraints of conventional technologies and open new avenues for scaling the industry.
  Next-generation geothermal heating and cooling is most viable for use in direct industrial (process) or district (space) heating.
  Next-generation geothermal costs fell as much as 50% from 2022 to 2024, and the IEA estimates that costs could fall an additional 80% by 2035 with proper policy and technical support.
Key messages
Technology

## Slide 21: Geothermal heating & cooling technologies are proven, deployable solutions for decarbonizing building thermal loads
Technology
 | Geothermal Heat Pumps (GHPs) | Direct-Use Geothermal | Underground Thermal Energy Storage (UTES)
Description | Constant temperatures are harnessed via open- or closed-loop fluid circulation and transferred through heat pumps. | Hot water from naturally occurring underground reservoirs is used directly for heating applications. | Seasonal energy storage in underground formations such as boreholes (BTES) or aquifers (ATES) accommodates later use.
Depth range | 50-300 meters | 400-2,000 meters | 20-1,000 meters
Temperature | 4.5-21ºC | 20-150ºC | 0-100ºC
Alternative to | Air-source heat pumps Boilers/propane heaters | Coal, oil, gas boilers used for district heating systems | Peaking fossil fuel systems Boilers and furnaces
Advantages | High COP (3-5) Peak load reduction Weather resistance | Suitable for large-scale applications Can target higher temperature | Energy savings and grid energy use optimization Low land use
Barriers | Site specificity Skilled workforce needs | Site specificity Limited use slowing cost reductions | Site specificity Heat loss over time Cost and efficiency uncertainties
Cost | US$66-$109/MWh | US$66-$109/MWh | N/A

## Slide 22: Geothermal heat pumps can be closed loop, open loop, or hybrid, and are most often used in residential or commercial settings
GHP Technology
Closed loop
Vertical
Heat pump
Horizontal
Pond/Lake
Open loop
Hybrid
Heat pump
Well discharge
Surface discharge
Cooling tower
Heat pump
1
2
3
1
2
Low land use; more common in large buildings
Most cost efficient for residential installations; highest land use
Cost effective; less land use and maintenance
Hybrid systems typically combine a geothermal resource with a cooling tower. Hybrid systems are most effective when cooling needs are significantly higher than heating needs (e.g., data centers). Hybrid systems can reduce up to 50% of the cost vs. non-hybrid systems while increasing installation speed.
Compared with closed-loop GHPs, open-loop systems have more efficient heat transfer but require greater pump energy use. Open-loop systems also have a shorter lifespan (10-15 years) and can worsen water quality when discharged.

## Slide 23: Underground thermal energy storage supports renewable energy integration, but adoption is limited by infrastructure needs
UTES Technology
Borehole thermal energy storage (BTES)
Heat pump
Heat exchanger
Aquifer thermal energy storage (ATES)
Heat exchanger
Extraction Well
Injection Well
Charging
Discharging
Extraction Well
Injection Well
Heat exchanger
Heat exchanger
Aquifer
Impermeable layer
Soil & rock
Charging
Discharging
Heat pump
Heat is stored directly in rock.
Heat is stored in groundwater.
BTES and ATES Compared |  | 
 | BTES | ATES
Energy Density | 15-30 kWh/m3 | 30-40 kWh/m3
Temperature | ~80ºC | <25ºC
Storage Efficiency | Low in first years, increases after 3-4 years; 45-60% | 70-100% (cold storage); 50-80% (heat storage)
Storage Volume | 3-5 m3 for 1 m3 water equivalent | 2-3 m3 for 1 m3 water equivalent
Use Cases | Wider range of applications | Large-scale applications
Risks | Thermal contamination; subsurface instability | Groundwater contamination
Investment Costs | 20-60 US$/m3 | 58-70 US$/m3
Lifespan | Can exceed 100 years | 25-50 years

## Slide 24: Drilling currently drives ~54% of next-gen geothermal LCOE; investments to reduce that share target heat resistance, permeability, and drill-bit life
Emerging technologies aimed at lowering next-generation geothermal drilling costs
Breakdown of projected LCOE components of next-generation geothermal in a low-cost case (US$/MWh)
Drilling Technology
High-powered millimeter-wave beams from a gyrotron vaporize rock and drill ultradeep boreholes, bypassing the wear and tear of traditional drilling methods.
Millimeter-Wave Drilling
Directional Steel-Shot Drilling
Repetitive Pulsed Electric Drill (RePED)
High-Pressure Water Jet-Assisted Drilling
A full-scale demonstration drilled 10 feet deep using 100 kW of millimeter-wave power; Quaise also plans to deploy a 1 mW gyrotron within two years to reach commercially viable depths.
Tetra Innovation Institute and NREL partnered to advance the technology, with potential drilling cost reductions of 75% and applications in industries beyond geothermal.
High-voltage electric pulses fracture rock, avoiding mechanical contact. Reduces wear on equipment and is designed to work with existing drilling infrastructure.
Drilling solutions startup Canopus is collaborating with TNO and European partners to test the drill system in the Netherlands, funded by a Dutch subsidy scheme.
Steel-shot particles are released under high pressure to erode rock formations and reduce resistance to further rotary drilling.
ORCHYD combines high-pressure water jets with fluid-driven percussion drilling, aiming to cut drilling costs by 65%. The project received Horizon 2020 funding from the EU in 2021.
High-pressure water jets cut rock into shapes that can be broken apart more easily by fluid-powered percussive hammers.
Chart: 
 | 51 | 25.5 | 22.3
 | 59.9 | 25.5 | 7.5
54%
46%
2025
50%
50%
2035
25%
75%
2050
111
51
30
Drilling costs
Other
Drilling, loop supplies, and installation also comprise 55-65% of conventional geothermal (GHP) costs in the U.S. (2025).

## Slide 25: Eavor-LiteTM demonstrates the potential of leveraging oil & gas sector knowledge for next-generation geothermal heating
Case study: Eavor-LiteTM
~150 people employed during planning and construction
20 GWth produced since 2019
In 2019, Eavor launched Eavor-LiteTM, a full-scale demonstration project in Alberta, Canada, of a closed-loop geothermal system (Eavor-LoopTM). Eavor leveraged advances from the shale drilling revolution and growing interest from the oil & gas industry to drive down costs and improve efficiency.
Drilling Phase
Subsurface Exploration
Alberta Energy Regulator’s Core Research Center has collected:
  > 1.55 million boxes of well core
  Daily drilling reports from over 417,000 oil & gas wells
  > 20 million vials of drill-cutting samples
This data supported Eavor’s subsurface exploration and reduces the need for experimental drilling in future projects.
Precision Drilling deployed two rigs to drill 2,400-meter multilateral wells in low-quality sandstone rock.
Shell International Exploration and Production provided technical expertise on drilling, completion, facility construction, and follow-up on commercial implementation.
Investments
February 2021: BP and Chevron were investors in a $40 million funding round for Eavor.
June 2023: Eavor received a $34 million investment from OMV, an Austrian oil and gas company, in its Series B equity round.
In May 2020, Eavor announced an Eavor-LoopTM heat and power project in Geretsried, Germany. An additional contract was signed in May 2024 for the development of a district heating network.

## Slide 26: Eavor-LiteTM demonstrates the potential of leveraging oil & gas sector knowledge for next-generation geothermal heating
Case study: Eavor-LiteTM
Insulated Drill Pipe
Rock-PipeTM
Thermosiphon Effect
Magnetic Ranging
Magnetic ranging signals are used to drill upper wells directionally toward lower wells.
Signals are interpreted by a specialized receiver in the lower wellbore.
Previously used in the oil & gas industry.
Seals the casing on the Eavor-LoopTM vertical wellbore, improving efficiency.
Decreases well permeability by 10-100x and isolates working fluid within the system.
Is activated using non-hazardous fluids.
Differential density between warm and cold working fluids enables the Eavor-LoopTM to operate without a pump.
A pump was used during only 783 hours of >30,000 hours of total operation during initial startup and testing.
Enables deeper and hotter drilling by regulating bottom-hole temperatures.
Cools standard drilling equipment for operation in extreme conditions.
Previously used in the oil & gas industry.
Eavor-LiteTM System Performance
3-5x reduction in average permeability due to Rock-Pipe
99.9% system seal rate due to Rock-Pipe technology
99.6% system uptime (excluding trials)
50ºC stable outlet temperature after four years
20 m3/hour production rate after four years

## Slide 27: Next-generation geothermal may bypass resource-related limitations of conventional geothermal, opening new avenues for scaling the industry
Technology
Geothermal heating and cooling consumption by application globally
Conventional geothermal is limited by geographical and temperature constraints…
… making next-generation geothermal attractive for reducing emissions in industrial and district heating use
Chart: 
 | 4 | 53 | 9 | 1 | 33
4%
1%
Agriculture & Fishing
GHPs
Direct Use
Industry
District Heat
Industrial Heat | In a low-cost APS scenario, next-generation geothermal could economically displace ~3 EJ of fossil fuel consumption by 2035 for industrial heat globally (10% of industrial heat <200ºC) and almost 10 EJ by 2050 (35% of industrial heat <200ºC). Up to 230 Mt of CO2 emissions could be avoided.
District Heat | In a low-cost scenario, next-generation geothermal could capture 20% of district heating growth between 2035 and 2050. Investment costs below US$4,000/kW would make next-generation geothermal district heating cost competitive. Co-generation (CHP) plants are an economically attractive application due to revenue generation from electricity shares
Share of total supply for next-generation geothermal heating, 2030-2050 (%)
Chart: 
 | 0.3 | 8 | 9.2
 | 0.1 | 1.3 | 3.6
2030
2040
2050
Industrial Heat
District Heat
Conventional geothermal heat use in industry remains limited due to geographical dependence on hydrothermal reservoirs and lower relative temperatures.
Direct use can require greater temperatures than those accessed via conventional geothermal.
GHPs remain the most cost-effective application of conventional geothermal resources.

## Slide 28: For industrial applications, geothermal energy is viable for temperature applications <200ºC; New Zealand has harnessed this potential since 1957
Temperature requirements and potential geothermal applications for key industrial processes
Kawerau Geothermal Field in New Zealand highlights existing direct-use geothermal industrial heating
Technology
Temperature (ºC) | Industrial applications | Geothermal application
<100ºC | Food & beverage processing Textile processing Paper processing | GHPs are most competitive for satisfying low-temperature industrial heat demand.
100-200ºC | Paper & chemicals production Auxiliary processes in cement production & food processing | Next-generation geothermal can provide midrange temperatures across a wide geography.
200-400ºC | Petrochemical cracking Cement & steel pre-processing Aluminum smelting | Fuel combustion or direct electricity use will most likely remain necessary.
Geothermal energy suppliers
Geological conditions
250-310ºC downhole temperature range
35 km2 area covered by the geothermal field
350-570 MW estimated available resources
Key industrial processes
Paper & pulp mill
Wood drying
Dairy processing
Supplies various industrial customers in Kawerau
Process steam supplied at pressures of 7-16 bar and process water at 170ºC
~14.8 PJ geothermal energy produced annually
90% less carbon; 0.007 tCO2e/GJ compared with LNG (0.054 tCO2e/GJ)
Ngāti Tūwharetoa Geothermal
Ngāti Tūwharetoa Geothermal (heating)
Eastland Generation, Mercury Energy (power)

## Slide 29: Geothermal Heating and Cooling Supply Chain

## Slide 30
Geothermal heat pumps (GHPs) rely on critical raw materials like copper, aluminum, steel, and refrigerants, making them vulnerable to supply chain disruptions.
Shared supply chain dependencies with other renewable energy sectors create risks for material availability, cost fluctuations, and project feasibility. For instance, copper demand is surging due to its role in solar PV, wind turbines, and EV manufacturing, leading to supply constraints and price volatility.
Lack of access to drilling rigs can be a constraint for deep geothermal projects, especially for heating and cooling applications in areas without nearby oil and gas activity. In the U.S., geothermal rigs make up only 0.5% of active rigs, while 81.6% are used for oil and 17.9% for gas. In regions where oil and gas operations are active, geothermal developers can often access the same rigs, crews, and supply chain.
Air-source heat pumps (ASHPs) dominate the market (93% vs. 1.5% for GHPs) due to lower costs and easier installation. Regulatory, labor, and installation challenges make ASHPs the preferred choice for consumers, shifting industry focus and investment away from GHPs.
The workforce trained in geothermal drilling, installation, and maintenance is limited, which is a significant barrier to industry scaling. Countries and corporations must invest in workforce expansion, licensing reforms, and training programs to scale geothermal adoption.
Key messages Supply Chain

## Slide 31: Geothermal heat pump systems comprise four core components that consist of a significant share of common raw materials
Observations
A geothermal heat pump is generally composed of four elements:
  Air distribution system
  Thermostat and control
  Heat pump unit
  Ground loop system
Raw material inputs drive the entire GHP supply chain. Essential materials like steel, HDPE, PVC, copper, aluminum, refrigerants, and ethanol/glycol/methanol (used for antifreeze solutions) are the foundation of component parts manufacturing.
The common raw materials demonstrate complex interconnections across the value chain. Multiple raw materials feed into multiple components, highlighting the dependence on supply chain stability, especially for metals such as copper, aluminum, and steel.
Simplified materials breakdown of the GHP value chain
Exploration and raw materials
Development
End use
For forced-air systems
For hydronic systems
HDPE: High-density polyethylene PVC: Polyvinyl chloride
Heat exchanger
Ethanol/glycol or methanol
Raw materials
Component parts
Core component
End-product
Geothermal Heat Pump (GHP) System
Ground loop system
Pipes
Heat pump unit
Compressor
Evaporator/ condenser coil
Expansion valve
Air distribution system
Air handler/ fan coil unit
Radiant Heating
Ductwork
HDPE
Copper
PVC
Ethanol/glycol or methanol
Steel
Aluminium
Refrigerants
Thermostat & control
Circuit boards

## Slide 32: Geothermal heating and energy storage face significant challenges across the value chain — specifically for raw materials
Observations
The demand for copper is skyrocketing due to its critical role in renewable energy infrastructure (solar panels, wind turbines) and electric vehicles (EVs).
Since GHPs require copper for their heat exchangers, wiring, and compressors, this puts them in direct competition with solar PV, wind power, and EV manufacturers, leading to supply bottlenecks and price volatility.
Drilling rigs are essential for geothermal systems, but they share similar equipment and expertise with O&G, which drives up costs and limits availability.
The skilled workforce for drilling, maintenance, and system operation is also in high demand for O&G projects, making talent scarce and expensive for the geothermal sector.
Disposal issues stem from hazardous materials used in GHPs, primarily:
  Refrigerants in compressors
  Heat transfer fluids (glycol- or methanol-based solutions)
  Plastics and coatings (HDPE pipes and Teflon seals)
These materials require specialized disposal and recycling infrastructure, adding complexity to the end-of-life phase.
Key challenges along the geothermal value chain
Geothermal supply challenges of
geothermal heat pumps (GHPs) and underground thermal energy storage (UTES)
End of life
Exploration & raw materials
Operations & maintenance
Copper
HDPE
Glycol
Methanol
Steel
Drilling rigs
ASHPs vs. GHPs
Semiconductors
Skilled workforce
Thermal imbalance
Scaling & fouling
Disposal
Site restoration
Deep dive
Deep dive
Deep dive
Deep dive
A
B
C
E
Compressors
Development & drilling
Deep dive
D

## Slide 33: High copper intensity of renewable energies and electric vehicles are propelling copper demand and price surges
Key drivers of copper demand and pricing
A
Exploration & raw materials
Demand driver #1: Renewable energy
Offshore wind
9.6 t/MW
Onshore wind
4.3 t/MW
Solar PV
5 t/MW
Demand driver #2: Electric vehicles
Battery electric bus
0.369 t/vehicle
Battery EV
0.083 t/vehicle
Hybrid EV
0.038 t/vehicle
Copper intensity of EVs
Copper intensity of renewables
Observations
Copper has the highest electrical conductivity of all non-precious metals, making it essential for efficient power transmission in renewable energy systems and electric vehicles.
Solar PV systems use 2,450 to 6,985 kg of copper per MW, while a 660-kW wind turbine contains around 350 kg, primarily for wiring, cabling, and heat exchangers.
EVs use up to four times more copper than internal combustion engine cars, with fully electric models requiring up to a mile of copper wiring in components like motors and inverters.
Copper demand is expected to nearly double by 2035, but the limited economically recoverable portion of global copper resources poses risks to the energy transition.
Citi forecasts copper prices will hit US$10,000 per metric ton by the end of the year, climbing to US$12,000 by 2026, driven by strong demand and tight supply.
Geothermal systems' low copper intensity offers a cost and supply chain advantage as rising copper demand pushes up prices — making it more resilient than wind or solar.
Chart: 
2025
2020
2015
US$ per metric ton

## Slide 34: Clustered along the U.S. Gulf Coast, HDPE resin facilities face natural disaster disruptions, leading to supply shortages
Major HDPE resin facilities in the United States
B
Exploration & raw materials
Monaca, PA
Charleston, SC
Point Comfort, TX
La Porte, TX
Baytown, TX
HDPE scarcity root causes and consequences
High-density polyethylene (HDPE) production relies on petrochemical feedstocks like ethylene monomer and co-monomers, requiring a stable supply chain. However, recent extreme events have disrupted these key chemicals, leading to shortages. The U.S. Gulf Coast, home to major HDPE resin factories, has faced repeated disruptions, including:
Production and demand Imbalances: Coming out of pandemic lockdowns, demand for plastic materials surged. HDPE pipe manufacturers saw resin prices skyrocket 60 cents per pound from January 2020 to mid-2021 (versus the pre-2020 norm of 1- to 2-cent annual increases). This extreme resin demand and shortage left pipe makers with limited inventories and backlogs of six to eight months on orders.
Weather disasters Severe weather events, including Gulf Coast hurricanes and the Texas freeze in February 2021, shut down resin plants unprepared for extreme conditions. These disruptions severely reduced HDPE resin supply nationwide, leading to shortages. | Pandemic shutdowns COVID-19 outbreaks caused temporary plant closures and workforce shortages in chemical and plastics factories. Restarting complex chemical plants took time, delaying production and worsening shortages despite rising demand.

## Slide 35: While shallow geothermal heating rigs are readily available, deep drilling rigs remain largely controlled by the oil & gas industry
Recent joint ventures in the geothermal drilling space
OMV and Wien Energie (“Deeep,” 2024): Deep geothermal energy for up to 20,000 Viennese households from 2028 on; scalable to 200,000 households.
Elemental Energies and Iceland Drilling (2025): Subsurface-to-drilling service integration.
Arverne Group and Herrenknecht (“DrillDeep,” 2024): $4.7M by Herrenknecht backs Arverne's $2.6B geothermal-lithium push.
Quaise Energy and Nevada Gold Mines (2024): Targets 30% GHG cut by 2030; enables 10× more power per well.
Chevron and Baseload Capital (2022): Scaling from ~1 MW San Ardo pilot to Weepah Hills project, accelerating geothermal retrofits in U.S. oilfields.
U.S. land rig market segmentation and key players
C
Development & drilling
 | Oil drilling rig | Gas drilling rig | Geothermal drilling rig1
Description | Extraction of crude oil from underground reservoirs, often using rotary or directional drilling techniques | Extraction of natural gas from underground formations, including conventional and shale gas reservoirs | Access to underground heat by drilling deep wells into hot rock formations
Market share (2024) | 81.6% | 17.9% | 0.5%
Active rig count (2024) | 473 | 104 | 3
Avg. rig count (2013-2024) | 700 | 172 | 2
Key players |  |  | 
Chart: 
 | 81.6 | 17.9 | 0.5
Chart: 
 | 81.6 | 17.9 | 0.5
Chart: 
 | 93 | 3.2 | 2.3 | 1.5 | 0.05

## Slide 36: Drilling for sustainable heat: OMV and Wien Energie join forces to tap deep geothermal for Vienna
Joint venture “Deeep”
C
Case study: OMV and Wien Energie
Project Scope
Up to 200 MW of geothermal capacity planned
Aims to supply 200,000 households with climate-neutral district heating
Supports Vienna’s 2040 climate-neutral heating target
Graph: APA, Source: Wien Energie
In November 2023, Wien Energie and OMV founded the joint venture “Deeep” to develop deep geothermal projects in Greater Vienna.
Initial Project: Aspern, Vienna-Donaustadt
Located above a geologically favorable basin with high water availability and heat flow
Part of Vienna’s urban expansion zone — ideal for integrating infrastructure and clean energy
Drilling depth: Up to 3,000 meters to access deep geothermal heat
Drilling begins: December 2024
Operations start: 2028
Strategic Partnership
Combines OMV's expertise in deep drilling with Wien Energie's district heating network, supporting Vienna’s target of climate-neutral heating by 2040
Thermal water is pumped up.
Heat exchanger
Heat from deep water is transferred and fed into district heating network.
Cooled water is returned to the depths.
Graph: APA, Source: Wien Energie
District heating
Conglomerate
Thermal water in the Aderklaa
VIENNA
Comparison: Subway network up to 35 m deep
Drilling diameter 30 cm

## Slide 37: The increasing adoption of ASHPs is shifting manufacturing and investment priorities away from geothermal heating and cooling
Comparison of ASHPs vs. GHPs
D
Development & drilling
 | Air-source heat pump | Geothermal heat pump
Description | Transfers heat between the air and a refrigerant to provide heating and cooling | Uses underground loops to extract and dissipate heat for more efficient heating and cooling
Market share | 93% share of U.S. heat pump market (2022), 13% of installed residential heating (15.9 million homes) | 1.5% share of U.S. heat pump market (2022), 1% of installed residential heating (1.3 million homes)
Investment costs | $3,000 - $10,000 for residential systems $214 - $714 per kW for 4-ton system (14 kW) | $10,000 - $30,000+ due to ground loop installation $714 - $2,143 per kW for 4-ton system (14 kW)
Installation complexity | Easier installation and less regulatory hurdles; can be retrofitted to most buildings | Requires drilling or trenching for ground loops with respective permits, making it more labor-intensive
Key manufacturers |  | 
Chart: 
 | 93 | 3.2 | 2.3 | 1.5 | 0.05
Chart: 
 | 93 | 3.2 | 2.3 | 1.5 | 0.05

## Slide 38: To stay competitive, geothermal must grow its workforce through investments in education, automation, oil & gas talent migration
Global number of geothermal energy jobs (2018-2023)
E
Operations & maintenance
Investments in education and training
On-the-job training and apprenticeships
Diversity and inclusion of underrepresented groups
Technology and automation for complex operations
Action implications for geothermal workforce expansion
Chart: 
 | 94 | 99 | 96 | 196 | 152 | 50
 | 7
 | 9
 | 94
2018
2019
2020
2021
2022
9
7
2023
160
+104%
Other
The geothermal industry experienced a sharp rise in jobs from 96,000 to 196,000 in 2021, but growth has since stagnated. In contrast, the oil and gas sector employed 12.4 million people in 2023 — a 5% increase from the previous year — with further growth expected in the coming year.
China leads in geothermal employment, while the U.S. and EU must take strategic actions to expand their workforce.
Transition of oil and gas talent and workforce to geothermal energy
Number of jobs in thousands

## Slide 39: Connecticut leads by example, tackling workforce shortages and supply chain bottlenecks with strategic and targeted solutions
E
Case study: Connecticut workforce
Context
The Connecticut Geothermal Workforce Development Plan was created for the District Geothermal Heating + Cooling Deployment project in Wallingford, Connecticut.
Funded by the U.S. Department of Energy, the initiative aims to develop a low-temperature geothermal heating and cooling system for a low-income community.
Led by the Connecticut Department of Energy and Environmental Protection and a coalition of partners, the plan addresses workforce gaps through a needs assessment and workshops, proposing strategies for workforce expansion over 30 months.
Implementation depends on securing additional funding, including support from the New England Heat Pump Accelerator Coalition.
Action steps for identified bottlenecks
Needs assessment
The Connecticut Geothermal Workforce Needs Assessment, conducted by NEEP between October 2023 and April 2024, identified three key barriers to geothermal adoption:
  Lack of awareness and interest in geothermal careers
  Workforce shortages amid rising project demand, particularly in drilling
  High upfront costs, limiting system adoption and workforce growth
Surveys were conducted with industry stakeholders, including utilities, training centers, and drilling companies, with 19 interviews and 11 survey responses collected.
Workshops in May 2024 brought together 45 industry representatives to discuss licensing, training, drilling, and workforce expansion.
Set equity-based recruitment goals.
Invest in targeted outreach.
Provide financial support.
Offer wraparound services like childcare and transportation stipends.
Track demographic data.
Incorporating equity
Launch awareness campaigns.
Expand education in technical high schools and community colleges.
Increase hands-on learning opportunities.
Engage unions and workforce organizations.
Recruiting new entrants
Clarify licensing rules.
Streamline the licensing process for workers.
Develop a heat pump-specific license.
Provide guidance and out-reach to help workers under-stand licensing requirements.
Increasing license accessibility
Retrain existing well water and oil drillers.
Support union apprenticeship programs.
Encourage public ownership of drilling rigs.
Establish a centralized Drilling Center of Excellence.
Fostering rig availability

## Slide 40: Responsible disposal protects full lifecycle sustainability of geothermal heating and cooling systems
Observations
Proper disposal of geothermal systems involves safely removing refrigerants and fluids to prevent emissions and recycling hardware to preserve climate benefits. HVAC contractors, installers, or specialized firms are typically capable of handling this process.
Most hardware components are steel or copper, with insulation removed before recycling. Electrical parts go to mixed recycling where plastics are separated and copper is recovered. Frames and casings, made entirely of steel, are easily recycled through established processes.
Solution: Companies entering disposal stage services
Refrigerant Lifecycle
Paid Wholesale
Usage
Return to Gas
Decant
Reclamation & Separation
Packaging
Bulk
Recovery
Analysis
Refrigerant is extracted into an A-GAS cylinder during removal.
Alto Energy collects and transports the unit to its warehouse.
A certified engineer transfers the refrigerant for A-GAS shipment.
Cleaned refrigerant is stored and resold for reuse.
A-GAS tests the refrigerant.
Hardware Recycling
Frames & Casings
All frame and casing components are made entirely of steel. Steel is the most recycled metal on the planet; as such, processes for recycling are efficient.
Electrical components can be transferred to a mixed recycling facility, where the plastic is removed and the copper components are recycled.
Electrical Components
All mechanical components are steel or copper. Some components have insulation, which needs to be removed and disposed of before the metal can be recycled.
Mechanical Components
Refrigerant Recycling
F
End of life

## Slide 41: Responsible disposal protects full lifecycle sustainability of geothermal heating and cooling systems
Observations
Proper end-of-life management for geothermal systems requires safely removing refrigerants and heat transfer fluids to prevent emissions and contamination, along with responsibly recycling hardware like piping and pumps to preserve climate benefits. Such work can be done by HVAC contractors, installers, or reclamation firms.
Relatherm provides a sustainable, cost-effective solution by reclaiming thermal fluids such as Dowtherm A®, Therminol® VP-1, Therminol® 66, Marlotherm SH, and Therminol® 55. The process restores used fluids to near-virgin quality, achieving 50-95% recovery rates. This reduces waste, cuts disposal costs, and minimizes the need for full fluid replacement.
Solution: Companies entering disposal stage services
F
End of life
Heat Exchange Fluid Reclamation
Highlights
Offers a sustainable alternative to incineration or landfill disposal.
Allows reuse of reclaimed fluids, avoiding full replacement and yielding significant cost savings — especially in large systems.
Reclaimed fluids match the performance of virgin fluids and are suitable for continued use.
Relatherm has successfully recycled various fluids including Dowtherm A®, Therminol® VP-1, Therminol® 66, Marlotherm SH, and Therminol® 55.
Reprocessing yields range from 50 to 95%, depending on degradation severity.
Virgin fluid top-off is provided when needed.
1st Sample Analysis
Outbound Transportation:
2nd Sample Analysis
Reprocessing (Phase I)
Reprocessing (Phase II)
3rd Sample Analysis
Inbound Transportation
Heat Exchange Fluid Reclamation Process

## Slide 42: Emerging supply chain trends emphasize cost reduction through modular design, predictive maintenance, and circularity
Modular geothermal systems are gaining traction due to their scalability, reduced installation time, and cost effectiveness.
The systems allow for phased implementation, making geothermal solutions more accessible for various building types.
First movers:
Modular geothermal systems
Trend #1
Artificial intelligence is impacting HVAC systems by enabling predictive maintenance, which anticipates equipment failures before they occur.
The use of AI enhances system reliability, extends equipment lifespan, and reduces operational costs.
​First movers:
AI for predictive maintenance
Trend #2
The principles of reuse, refurbishment, and recycling of products and materials to minimize waste also apply to geothermal systems.
This includes designing systems for longevity, using recyclable materials, and establishing take-back schemes for end-of-life components.
First movers:
Circular economy for GHPs
Trend #3

## Slide 43: Geothermal Heating and Cooling Global Policy

## Slide 44
Four key policy priorities can help scale geothermal heating and cooling (H&C) deployment and lower costs.
  Global collaboration on geothermal energy largely favors power generation over H&C.
  As a human capital-intensive industry, transitioning the oil and gas workforce, which has extensive overlapping competencies with the geothermal sector, is a high policy priority.
  Strong funding for R&D is key in scaling geothermal H&C across diverse geographies and in driving down next-generation geothermal costs.
  Geothermal projects carry high early-stage risks, necessitating strong risk mitigation policies to incentivize adoption.
Current policy on geothermal H&C remains an afterthought in the global policy landscape.
  Only ~30 countries have active geothermal H&C policies compared with >100 for solar PV and wind.
  Strong H&C policy is concentrated in Europe, while China leads in deployment on the domestic level.
  While the U.S. has the second-highest installed H&C capacity, fragmented federal policy has prevented economies of scale in the industry.
  Geothermal H&C leads in deployment, yet there are more active policies in place for power generation.
Country-level geothermal H&C policy, primarily in Europe and China, has enabled conventional geothermal to scale and next-generation technologies to take root.
  China’s robust R&D policy support enabled Sinopec to double its installed H&C capacity in four years.
  While Iceland punches above its weight in the sector through workforce development, France’s risk mitigation schemes have supported 81% of conventional geothermal adoption since 1970.
  Through streamlined permitting policy, the number of exploration permits for deep geothermal plants in Germany doubled from 82 in 2023 to 155 in 2025; these permitting improvements may serve as a model for the Netherlands, which aims to similarly scale geothermal H&C adoption.
Key messages Global Policy

## Slide 45: Four key policy priorities can help scale geothermal heating & cooling deployment and drive down costs
Observations
Stronger implementation of policy goals could boost new geothermal heat developments 50% by 2030 in the APS compared with the Stated Policies scenario.
Strong policy can also help drive next-generation geothermal cost reductions of up to 80% by 2035.
In the APS, expanding policy support and cost reductions would scale GHP consumption to almost 3,000 PJ — 50% higher than in the Stated Policy scenario (China, U.S., and Europe together account for 80% of this growth).
Almost two-thirds of geothermal power capacity additions between 2024 and 2030 are expected to be policy-driven – primarily tax credits, fixed tariffs, and premiums.
Policy
Global Collaboration
Global collaboration on geothermal energy – particularly heating and cooling – lags behind other renewables, slowing innovation and increasing risk. Stronger, more large-scale collaboration is a priority.
Workforce Development
Geothermal expansion will require a skilled workforce in engineering, geology, and drilling sectors. Transitioning the oil and gas workforce will streamline geothermal workforce development.
Research & Development
Poor funding infrastructure for geothermal exploration and drilling drives up investment costs and slows technological progress. Strong funding mechanisms will be necessary to speed geothermal deployment.
Risk Mitigation
Geothermal projects have higher predevelopment risks compared with other renewable energy technologies due to complex geological and subsurface conditions. Mitigating risk is critical in lowering project costs.

## Slide 46: Global collaboration favors geothermal power production, leaving room for growth in heating and cooling expansion
Drivers of variable global collaboration on geothermal power versus heat
Heating projects tend to be more localized, limiting returns compared to large-scale power projects.
There is a differential global emphasis on electricity access compared to heating access.
The development of EGS has spurred greater collaboration on geothermal power generation.
Scalability of power projects attracts greater private investment.
Opportunities for collaboration on H&C
Integrate geothermal heating into decarbonization strategies.
Develop standardized financing mechanisms.
Invest in combined heat and power projects to maximize returns.
Policy
Scale | Heating & Cooling |  | Power Generation | 
Global |  | Although World Bank does not have a dedicated global program for geothermal heating, it has provided one-off investments in district heating in countries including Türkiye and El Salvador. |  | The Global Geothermal Development Plan (GGDP), launched by ESMAP in 2013 to scale geothermal power, has supported 13 countries and brought three projects online.
Regional |  | Geothermica’s €32.5 million Joint Call 2021 aims to accelerate geothermal heating and cooling projects by 2030 through large-scale, commercially viable projects. |  | The GRMF finances geothermal power projects in East Africa, expanding to include heating in 2022; 26 power and 5 direct-use projects have received funding.
Bilateral |  | The German Agency for International Cooperation and the Central American Integration System have cooperated on geothermal heating and cooling in El Salvador, including a pilot geothermal-powered coffee dryer. |  | Japan’s International Cooperation Agency invests in building geothermal power capacity in Latin America and Africa, including over 400 MW of geothermal power plants in Kenya.

## Slide 47: Leveraging oil & gas capabilities can lower geothermal power costs and accelerate deployment
Policy: Workforce development
Problem | Current Challenge | Oil & Gas Synergy | Limitations | Case Example
Resource Identification | Accurate geothermal resource identification and modeling require multi-parameter surface data (seismic, geology, heat flow, permeability). | Oil and gas surface imaging and drilling data reduce exploration risk and improve reservoir targeting. | Legacy oil and gas datasets often lack thermal gradient resolution or long-term heat recharge data. | Hungary and the Netherlands: Open oil and gas subsurface databases reduce geothermal exploration costs and uncertainty.
Skilled Workforce Needs | Skilled workforce shortages in reservoir engineering and well completion delay project scaling. | Oil and gas professionals have skills that can apply to geothermal exploration, development, and operation. | Current policy frameworks provide limited financial incentives for geothermal workforce transfer. | DOE Geothermal from O&G Initiative: Demonstrates feasibility of cross-sector workforce and skill transfer.
Drilling Costs | Subsurface drilling represents 60 to 80% of total next-generation geothermal CapEx. | Hydrocarbon well technology (e.g., horizontal drilling, multistage stimulation) can be directly transferred to EGS. | Geothermal wells require sustained reinjection and higher temperatures tolerance than O&G operations. | Fervo Energy’s Project Red: Achieved record flow rates by adapting shale fracking and fiber-optic monitoring.
Co-production and Well Repurposing | High initial exploration, drilling, and completion costs can be a limiting factor in geothermal projects. | Co-production or heat extraction from abandoned wells can de-risk geothermal projects. | Wells require a large heat gradient and flow rate, flexible permitting, and proximity to demand. | Zanskar Project (U.S.): AI-driven reservoir modeling revitalized legacy wells, cutting exploration risk by >50%.
Level of shared competencies

## Slide 48: High workforce needs in the geothermal industry create room for skill development and workforce transition from fossil fuel sectors
Drivers of job creation in the geothermal industry
Extensive site exploration, drilling, and subsurface analysis requires skilled labor in the development phase.
Continuous plant operation, subsurface resource management, and system upkeep contribute to long-term O&M needs.
Job creation per MW installed* By project phase
Geothermal and oil & gas engineering skillset overlap*
Policy: Workforce development
Chart: 
 | 12 | 19 | 34
Solar PV
Geothermal
*Both power and H&C
Chart: 
 | 20 | 55 | 25
Other
Construction
O&M
Chart: 
 | 5 | 8 | 5 | 4 | 6 | 8
 | 5 | 8 | 4 | 6 | 8 | 4
5
4
6
3
7
2
8
1
0
Geoscience
Well Production
Formation Evaluation
Drilling Competencies
Surface Production
Reservoir Engineering
Oil & Gas Engineer
Geothermal Engineer
Competency Level
Transitioning oil and gas workers presents a strong opportunity to meet the skilled workforce needs of the geothermal industry.

## Slide 49: Field testing, cross-sector collaboration, and specialized research facilities are key to strengthening R&D
Policy: R&D
R&D priorities for scaling geothermal H&C
Pilot Projects
Public-Private Partnerships
Case Study: Heerlen Minewater Project | Heerlen, Netherlands
Only three of 326 projects funded by the EU Innovation Fund were for geothermal R&D.
Scaling pilot projects is key in field testing and improving new technologies.
PPPs enhance data sharing, de-risk innovation, and optimize policy frameworks.
High upfront costs deter private investment without strong risk-sharing mechanisms.
Kirchweidach Deep Geothermal Heating Project: Received funding support from KfW to construct a district heating network in Bavaria.
The DOE’s Community Geothermal H&C Initiative funded a district-scale geothermal project in Framingham, Massachusetts, in partnership with Eversource.
 | Timeline | Highlights
Phase 1: Pilot | 2003: Pilot project launched for heat extraction from abandoned coal mines | Funded by the European Interreg IIIB NWE Program Provided H&C to 2 buildings, (>40,000m2)
Phase 2: System Upgrades | 2013: System upgraded to a demand-driven, automated thermal smart grid to increase efficiency | Supplied heat for 200,000m2 of building equivalents 4 MW installed capacity Excess heat provided further input to the grid
Phase 3: Optimization | 2020-present: Optimization via a self-learning and adaptive intelligent control framework | Funded by the EU’s Horizon 2020 65% reduction in regional H&C CO2 emissions
> €25 million in EU funding advanced the project in its exploration stage.
Restructuring the initiative into a district-owned enterprise helped secure private investment and strengthen technical knowledge and capacity.
Current Limitation
Highlight

## Slide 50: Successful geothermal risk mitigation policies target early-stage resource and exploration risks; grant schemes lead in nascent geothermal markets
Early-stage geothermal risks and relevant risk mitigation schemes
Conventional geothermal capacity additions by risk mitigation scheme
2024-2030
Chart: 
 | 8 | 6 | 34 | 31 | 21
Resource Assessment
Subsidized Loans
Grants
Public Insurance
State-Led Development
Limited geological data increases uncertainty.
Lengthy permitting processes can slow project timelines.
High upfront drilling costs can stunt private investment.
Wells may have low temperature or flowrates.
Observations Grants are useful and most common in nascent geothermal markets. Some schemes target exploration only, while others also support drilling and operations; strong policy supports both.
Policy Priorities
Relevant Risk Mitigation Scheme(s)
Increase data quality and accuracy
Create open-source data repositories
Resource assessment
State-led development
Simplify and consolidate permitting processes
Expand geothermal-specific permitting regimes
Public insurance
State-led development
Invest in drill efficiency technologies
Expand financial incentives for private-sector investment
Grants
Subsidized loans
Strengthen R&D on subsurface modeling
Account for well failure in subsidies and grants
Grants
Public insurance
Policy: Risk mitigation

## Slide 51: Europe leads in geothermal heating & cooling regional policy adoption and collaboration; rest of the world lags behind
Observations
Over half of all countries with geothermal policies in place (16 of 31) focus exclusively on power generation.
Regional policy schemes in Latin America and East Africa are not included in this map.
Only eight countries (all in Europe) have adopted geothermal roadmaps for their heating & cooling sectors.
>100 countries have policies in place for solar PV and onshore wind — over 3x as many as for geothermal energy.
Europe is a regional hub for geothermal heating & cooling policies, while China leads on the country level.
Geothermal energy is a priority mitigation option in only 9% of NDCs’ submitted data.
While the risk mitigation-to-remuneration policy ratio is ~1:2 for solar and wind energy, the ratio for geothermal energy is ~1:1 due to high early-stage risk.
Countries with geothermal policies in place, 2024 (risk mitigation and/or remuneration)
Global policy

## Slide 52: While strong policy support is concentrated in China and Europe, installed capacity grows even in subpar policy landscapes
Observations
China has one of the strongest policy frameworks, but its geothermal heating policies may not be easily transferrable.
In Europe, both domestic and regional interest in geothermal heating & cooling has grown in the context of energy security concerns.
Untapped potential is concentrated in Africa and Latin America, where geothermal power is prioritized over H&C due to warmer climates and regional needs.
Legacy markets such as the U.S. have high installed capacity, but fragmented policy has inhibited economies of scale.
While global leaders have strong policy on conventional geothermal, emerging players are increasingly investing in next-generation technologies.
Global policy and installed capacity matrix for geothermal heating & cooling
Global policy
Global Leaders
Legacy Markets
Emerging Players
Untapped Potential
Installed Capacity
Policy
Iceland
China
USA
Sweden
Netherlands
Indonesia
Croatia
South Korea
Germany
Mexico
Brazil
India
South Africa
France
Morocco
Türkiye

## Slide 53: China leads in domestic policy and capacity addition; Europe has scaled domestic and regional policy support
Global policy: Leaders
 | China |  | Iceland |  | France |  | Sweden | 
Share of Global Installed Capacity |  | 58% (100,219 MWt) |  | 1.6% (2,823 MWt) |  | 1.7% (2,868 MWt) |  | 4.2% (7,280 MWt)
Global Collaboration |  |  |  |  |  |  |  | 
 | Global involvement primarily in bilateral partnerships |  | Extensive global leadership in workforce development and policy |  | Growing interest in the French geothermal export market |  | Primarily regional collaboration; minimal bilateral activity | 
Workforce Development |  |  |  |  |  |  |  | 
 | Home to ~40% of the global geothermal workforce |  | Global leader in training programs and specialized studies |  | Professionals and associations are united through the AFPG |  | Strong domestic workforce with dedicated training programs | 
Research & Development |  | 70% of all geothermal investments globally |  |  |  |  |  | 
 | Accounted for 70% of all geothermal investments in 2023, with R&D focused on digitalization |  | Renewed interest in geothermal R&D, with over €3 million awarded to 8 exploration projects |  | ADEME financed 71 feasibility studies and 31 investment projects with €7.9 million in aid in 2024 |  | Early adoption of carbon pricing spurred investment in GHP R&D; strong EU research collaboration | 
Risk Mitigation |  |  |  |  |  |  |  | 
 | National and regional subsidies; international grants and loans |  | While abundant geothermal resources reduce risk, Iceland has maintained a strong grant program |  | Four risk mitigation funds currently active, yet risks remain high for next-generation projects |  | Lacks strong subsidies for next-generation technologies, despite being a global leader in GHPs | 
Policy Strength
Deep dive B
Deep dive C
Deep dive A
Chart: 
 | 57.8 | 42.2
Chart: 
 | 1.6 | 98.4
Chart: 
 | 1.7 | 98.3
Chart: 
 | 4.2 | 95.8
Note: See subsequent slides for deep dives on the challenges highlighted above.

## Slide 54: Emerging players across Europe and Asia have scaled geothermal H&C policies to advance energy security and clean energy targets
Global policy: Emerging players
 | Germany |  | Netherlands |  | South Korea |  | Croatia | 
Installed Capacity |  | 3.1% (5,381 MWt) |  | 1.1% (1,830 MWt) |  | 0.93% (1,622 MWt) |  | 0.04% (74 MWt)
National Target | Scale deep geothermal from 1.8 TWh to 10 TWh per year by 2030 |  | 25-30% of heat demand supplied by geothermal energy by 2050 |  | 1 GW geothermal heating & cooling capacity by 2030 in Seoul |  | > 36.6% renewable energy in final energy consumption by 2030 | 
Status and Pipeline of Geothermal Projects | 42 deep geothermal projects in operation >150 projects in planning phase |  | 28 operating projects with >70 projects in the pipeline |  | Five geothermal landmarks in major areas in Seoul are being planned |  | 12 active production areas and 24 active exploration areas | 
Policy Highlights | Current number of exploration permits has almost doubled, from 82 in 2023 to 155 in 2025 |  | NL RNES Geothermal Guarantee Scheme provides grants and insurance up to 85% of testing and drilling costs |  | R&D funding in 2023 supported a hybrid energy supply system including GSHPs |  | €30 million approved for geothermal R&D in 2023, with the first major geothermal conference held in March 2025 | 
Current Limitations | Changes in leadership at the federal level have left investors uncertain of the risk associated with new geothermal projects |  | Permitting delays increase the risk of losing subsidies given a strict realization term of four years |  | A 5.5 magnitude earthquake in 2017 linked to an EGS project led to increased public opposition and a reorientation toward GHPs |  | The government has not yet developed a streamlined permitting process, prolonging project timelines | 
Deep dive E
Deep dive D
Chart: 
 | 3.1 | 96.9
Chart: 
 | 1.1 | 98.9
Chart: 
 | 0.93 | 99.1
Chart: 
 | 0.04 | 99.6
Note: See subsequent slides for deep dives on the challenges highlighted above.

## Slide 55: Through research and development policy integration, Sinopec doubled its geothermal H&C installed capacity in four years
Case study: Sinopec Green Energy’s Arctic Green Center of Innovation
Sinopec Green Energy (SGE) is a joint venture between Sinopec (51%) and Iceland’s Arctic Green (49%)
SGE is the world’s largest and most technically advanced geothermal heating & cooling company
Government policy incentivized investment and scale, including research funding, land access for pilot projects, and grid integration mandate
Global policy: China deep dive
SGE's Timeline
SGE's Operational Coverage
Began construction on Xiong’an, China’s first smog-free city.
Expanded into Hebei, doubling heating capacity.
Established Sino-Icelandic geothermal technology R&D center (Arctic Green Center of Innovation) as a global hub for geothermal expertise, research, and capacity-building, with state support accelerating R&D.
Expanded into Beijing and Tianjin, increasing total heating capacity by 26%.
Announced global expansion, focusing on the high-growth markets of Central Europe, the Middle East, and Indonesia.
2009
2011
2016
2021
2023
SGE has invested over half a billion dollars in geothermal since 2009.
Over 920 wells have been drilled in over 70 cities and municipalities.
SGE doubled its geothermal district heating coverage from approximately 60 million m² in 2020 to 120 million m² by year-end 2024. Total installed geothermal direct utilization capacity is over 4 GW.
Holds over 130 patents related to geothermal resource development.
Xiong’an was recognized by IRENA as a global showcase for city energy transition.
Xiong’an
States SGE has expanded into since 2009
A

## Slide 56: Despite common geothermal barriers, China has scaled low- to medium-temperature resources for clean urban heating
Resource availability
Only viable to specific areas with high geothermal activity and easily accessible underground hydrothermal reservoirs
Regulatory and environmental barriers
Opposition could arise due to potential environmental impacts, including increased seismicity risks, gas leak risks, and high water consumption for cooling.
Technology limitations
Barriers
Solutions
Strong government support and policy initiatives
Geothermal is a significant part of clean-heating policies by local governments, especially in northern China, since the early 2000s, as part of efforts to replace coal-based heating systems. There is also a specific implementation of a regional plan, e.g., Hebei Province Geothermal Resources Exploration and Development Five-Year Plan.
At the country level, the Chinese government has integrated geothermal into its broader energy transition and carbon-neutrality goals since 2017, through policies including its Five-Year Plans for Renewable Energy.
Policies and subsidies for district heating projects have incentivized investment.
Creation of green financing instruments: green loans, green bonds, and green equity funds
Actively investing in geothermal R&D
4- to 8-year permitting timeline
High risk and upfront costs
40-60% LCOE vs. solar & wind
Commercial risk
Exploration
Drilling
Construction
Large and diverse range of geothermal resources
High Temp
Medium, Low Temp
Power
Direct Heating
Tibet, Yunnan
Northern, Eastern China
Financial incentives and instruments creations for Sinopec Chinese oil & gas company
Low scalability
EGS immature, expansion = more drilling, difficult + expensive
Energy system
$ invested by 2020
Expansion
130 geothermal technology patents
Geothermal
+$500M
14 provinces
Global policy: China deep dive
A

## Slide 57: Xiongxian Field shows how geothermal success can drive national momentum through local innovation and private-public partnership
Capacity
  Largest single project of its kind (largest district heating capacity in the world from a single geothermal field)
  Currently supplying heat for 4.5 million sqm of homes; supports the entire city of Xiongxian (390,000 residents), meeting 100% of home heating needs from geothermal energy
Ownership & Operator
  Operated by Sinopec Green Energy Geothermal Development Co. (SGE), a joint venture established in November 2006 between:
    Sinopec Star Co. (a subsidiary of Sinopec Corp., a state-owned oil company)
    Arctic Green Energy Corp. (an Icelandic company)
GovernmentSupport
  Local governments began promoting the large-scale utilization of geothermal resources for heating around 2000.
    In 2009, Xiongxian County reached an agreement with SGE to develop geothermal resources sustainably.
  The establishment of the Xiong'an New Area in 2017, which includes Xiongxian, has put a spotlight on geothermal resources nationally.
    In 2017, the National Development and Reform Commission included guidelines for geothermal energy in the National Five-Year Plan for the first time, potentially leading to state subsidies and tripling the volume of geothermal heating systems.
  While initial development lacked significant government support, the success of the Xiongxian geothermal field has led to increased attention and backing from both local and national authorities, positioning it as a key component in China's clean energy strategy.
Global policy: China deep dive
A

## Slide 58: Europe is the third-largest growth market for geothermal H&C with policy leadership fueled by security concerns and transition goals
European countries with geothermal H&C roadmaps, 2024
Global policy: Europe deep dive
R&D Funding
Data Transparency
Technical Potential
Long-Term Geothermal Target
District Heating Leadership
Regulatory Support
Geothermal energy could provide ~8 TW of heat at 90ºC — 30 times the energy currently supplied by district heating systems — to supply over 70 million people in the region.
The European Geological Data Infrastructure standardizes data for public access; Germany, Italy, the Netherlands, and France have also developed public-access geothermal repositories.
The EU Implementation Plan’s vision for 2050 has geothermal supplying >25% of Europe’s space heating & cooling demand, >25% in the agricultural sector, and 5% in industrial sectors.
The EU’s $80 billion Horizon 2020 Program funded large research projects that deployed EGS, promoted national risk mitigation schemes, and advanced resource mapping and assessment.
>86% of district heating systems are in EU member states, and the European continent hosts 6 GWh of district heating capacity.
Chart: 
 | 86.1272 | 13.8728
14%
EU
Non-EU
The Net-Zero Industry Act supports strategic net-zero technologies to simplify permitting processes and increase access to funding.

## Slide 59: Through its global leadership on workforce development, Iceland punches above its weight in the geothermal H&C sector
Through the GRÓ Geothermal Training Program, Iceland has strengthened workforce development, engaging over 60 countries
Iceland has also contributed to two centers of excellence to advance regional workforce development in resource-rich areas
Global policy: Iceland deep dive
Six-Month Trainee Program
Draws trainees from developing and transitional countries with high geothermal potential.
816 fellows from 67 countries have graduated from the program.
MSc and PhD Scholarships
Trainees can extend their studies to an MSc or PhD.
89 fellows have graduated with an MSc.
6 fellows have graduated with a PhD.
El Salvador Centre of Excellence
Provides coursework for professionals in Latin America and the Caribbean.
Formed via a collaboration with El Salvador’s state geothermal company.
Over 700 professionals have participated.
World Bank announced a $150 million investment over the next six years, in part funding El Salvador’s Centre of Excellence.
Kenya Centre of Excellence
Aims to develop skilled labor in the geothermal industry in Africa.
Formed via a collaboration between UNEP, Iceland’s International Development Agency, and geothermal developers in Kenya.
22 students have been trained.
World Bank awarded the center $10.8 million for upgrades, training, and infrastructure development.
Key Topics
Geophysical exploration and reservoir engineering
Drilling technologies
Project management and financing
Chemistry of thermal fluids
B

## Slide 60: France’s risk mitigation schemes have helped scale conventional geothermal capacity in recent decades
Risk insurance overseen by ADEME fueled 81% of conventional geothermal development in France between 1970 and 2015
Since 2009, the Heat Fund has supported additional district heating and GHP installation
Global policy: France deep dive
 | Short-Term Fund (1981-1999) | Long-Term Fund (1982-2015)
Insurance Structure | 20% of drilling cost in case of failure Additional compensation up to 90% | 20% of the cost of drilling Insurance over 15 years of operations
Investment Amount | €3.4 million in high-priority R&D and repair initiatives €200 million guaranteed for drilling | €260 million guaranteed for drilling works and geothermal loops, insuring long-term operations in addition to early-stage risk
Highlights | 500 MWth installed, saving 3 MTOE of fossil fuels over 35 years 102 wells drilled between 1970 and 2015 benefitted from the funds For every €1 invested by the state, €33 of investments were covered for 25 years | 
Challenges | Operating income, indexed to the cost of fossil fuels, fell with oil prices after 1987, leading to debt renegotiations. Risk mitigation for next-generation technologies has proved more difficult. | 
Eligible technologies: Biomass, solar thermal, geothermal, and heat recovery
Heat Fund grants finance up to:
60% of feasibility studies
45% of investment in renewable energy
30% of investments for waste heat recovery
40% of investment in district H&C networks
Bonus of 10-20% for SMEs
Grant outcomes:
€106 million invested in geothermal projects
678 geothermal installations subsidized
C

## Slide 61: Germany’s investments in deep geothermal align with its heating transition goals; streamlined permitting enables faster growth
Global policy: Germany deep dive
The term Energiewende (energy transition) is introduced, with Wärmewende (heating transition) becoming an increasingly important component of that.
The German Renewable Energy Sources Act (EEG) comes into force, introducing feed-in tariffs for renewables including geothermal.
Germany’s largest deep geothermal initiative, the Schäftlarnstraße project, is drilled, after which Munich’s energy supplier sets a goal of generating 100% of Munich’s district heating from renewable sources by 2040.
The Climate Action Program 2030 introduces carbon pricing for heating, targeting emissions from the heating sector.
The government outlines a target of 100 new geothermal projects and 10 TWh of geothermal output by 2030, which could create ~24,000 new jobs and reduce CO2 emissions by 34 million tons.
The number of exploration permits for deep geothermal plants doubles from 82 in 2023 to 155 in 2025, with the potential to provide 1 to 2 GW of heat.
A legislative package is approved to expedite geothermal project approvals, simplifying bureaucratic processes.
1980
2000
2018
2019
2022
2024
May 2025
Jan. 2025
Germany’s new government plans to abolish and replace the current heating law, increasing uncertainty about federal policy moving forward.
Munich-Schäftlarnstraße Deep Geothermal Project
Policy Strengths of Germany’s Legislative Changes*
6 wells completed at a depth of 3,000-4,000 meters
50 MWt output at a reservoir temperature of ~100ºC
Highest availability of all heating plants in Germany
Bavarian geothermal systems have achieved COPs up to 36
*Policy uncertainty in the early stages of the new government may increase investor uncertainty
Simplified and digitalized approval procedures
Maximum deadlines for approval procedures
Geothermal classified as a paramount public interest
D

## Slide 62: In the Netherlands, streamlining permitting processes is a priority as strong policy frameworks for geothermal energy use emerge
Observations
The TU Delft project advanced despite permitting delays, enabled by public co-investment and subsidies, showing the power of targeted support.
The project demonstrates urban geothermal viability and underscores the urgency of Mining Act reform to unlock future projects at scale.
Policy Asks:
Develop geothermal-specific permitting track and harmonize legal frameworks to reduce intersectoral conflicts.
Accelerate project timeline, with Germany’s success with Mining Act reform acting as a model.
Strengthen public-private partnerships to de-risk and accelerate rollout.
Global policy: Netherlands deep dive
Project overview
Strategic relevance
Delivers ~95% of TU Delft’s heat demand
Case Study: TU Delft Geothermal Doublet
Supplies TU Delft and part of Delft city with 25 MW of geothermal heat
Integrated geothermal, HT-ATES, and heat pump technologies
Managed by TU Delft, Shell, EBN (state owned), Aardyn
Funded by Dutch Research Council and EPOS-NL (EU geoscience data infra.)
Anchors geothermal in NL and EU research agendas; enhances EU-wide data sharing
Showcases smart system integration
Proves viability of geothermal heating in urban settings
Acts as model for scaling urban geothermal
As public-private model, improves scalability and financial viability
Policy and Permitting Bottlenecks
Policy misalignment
Permitting delays
The Mining Act is unclear on heat zones, permits, and sector overlap.
Delays erode investor trust; industry calls process “disastrous."
22 SDE++ projects are at risk of a 3- to 5-year delay.
Follow-up permit criteria remain vague, stalling progress.
National Target
Policy Architecture
23% of national heat from geothermal by 2050
€2B in grants (2023) → 18+ projects funded
Roadmap: 6.8 PJ (2022) → 200+ PJ (2050)
Supports target of 55-60% CO₂ reduction by 2030
Risk coverage: 5% underperformance insured
SDE++: CO₂-reduction subsidy —makes geothermal cost competitive
E

## Slide 63: Geothermal Heating and Cooling Finance

## Slide 64
Residential (small-scale) GHPs systems
By 2050, millions of U.S. homes and businesses could adopt geothermal heat pumps with a positive lifetime payback. To reach this, the industry must grow 10% plus 2% per year and install GHPs in 7 million homes and businesses by 2035.
GHPs cost more than conventional HVAC systems, but tax credits can reduce upfront costs and improve access. Without incentives, ROI is 3 to 4%; with federal credits, ROI rises to 6 to 7% and can reach 13 to 14% in states like Massachusetts. Tax incentives are key to reaching the DOE’s goal of 7 million homes and businesses by 2035.
District GHPs systems
GHP district systems are growing in the U.S., with over 20 installed as of 2023 – first on college campuses and now expanding to communities and mixed-income housing. Campus pilots show 30 to 65% annual energy savings and 19 to 45% lower emissions, proving performance at scale. Federal incentives are helping make GHPs cost competitive, enabling wider deployment through investment, development, and public-private partnerships.
Private sector trends
Geothermal startups attracting the most funding are those with innovations in closed-loop systems, horizontal drilling, and dispatchable clean energy.
Investors are favoring scalable, flexible geothermal tech that serves large, reliable off-takers (like data centers) or enables mass adoption via affordability and ease of deployment.
Rising startups like Dandelion Energy aim to bring geothermal mainstream – like Tesla for EVs and Sunrun for solar – by simplifying adoption, cutting costs, and building trust.
Key messages
Finance

## Slide 65: Not one size fits all: Geothermal projects globally leverage different financing options
Finance
 | Description | Advantages and Challenges | Example
Public-Private Partnerships | Combines government funding with private equity/debt | Leverages both public oversight and private sector efficiency. Involves complex coordination and legal frameworks. | Kenya’s Rift Valley development (World Bank support) Large-scale power generation and infrastructure projects (2019-present)
Green Bonds | Debt instruments for renewable projects | Attracts investors seeking green investments; scalable. Dependent on investor confidence and credit ratings. | Iceland’s geothermal expansion via bonds Utility-scale geothermal expansions (2018-present)
Government Grants | Federal and state funding for R&D and deployment | Non-dilutive funding; promotes innovation and early-stage support. Often limited in size and competitive to obtain. | U.S. DOE $200,000 grants for geothermal heating & cooling tech. Pilot/demo projects, new tech in heating & cooling (grants announced in 2020)
Concessional Loans | Low-interest loans from development banks | Reduces financing cost for developing countries. Can lead to debt accumulation; tied to lender conditions. | Philippines’ geothermal sector (international aid) Exploration, drilling, and plant development in emerging markets (2010-2015)

## Slide 66: GHPs require incentives to overcome high upfront costs — but deliver long-term returns that pay for systems over their lifetime
Est. median CapEx of HVAC
U.S. residential ($K/household)
Est. cost and benefit across
GHP lifetime (20 years) ($K/household)
Observations
All U.S. states:
ROI without tax credit: 3-4%
ROI with tax credit: 6-7%
Massachusetts specific:
ROI with tax credit and state rebates: 13-14%
Tax credits help break the biggest barrier – high upfront costs – making GHPs more accessible and financially viable.
Incentives are key to unlocking mass adoption and reaching DOE’s Liftoff goal of 7 million homes by 2035.
Finance
Chart: 
 | 4.4 | 16 | 20
 | 24.4
 | 15.6
15.6 (35%)
24.4 (55%)
4.4 (10%)
GHP (no incentives)
Gas Furnace + Central AC
Air-Source Heat Pump
Non-loop mechanical HVAC
Loop supplies, drilling, installation
Weatherization/ retrofit
44.4
~4 ton/household capacity assumption
Conventional alternatives
Key forecasts:
NREL projects that costs could decrease ~20-30% with expanded pilots, workforce training, thermal energy networks, and standardization.
GHP costs can decline with scale.
Key assumptions:
GHP installation capacity: 3 to 5 ton/household (urban to suburban).
Estimated annual energy savings with GHP installed: $1.5K-$2.5K/household.
Incentive is 30% federal ITC.
Chart: 
 | 44.4 | 31 | 16 | 16
 | 13.4 | 15
CapEx
Tax Credit Incentives
15.0
State Rebates
Net CapEx with Incentives
Chart: 
 | 35
 | 40
Benefits
Cumulative energy savings
Avoided costs (gas line replacement)
75
Federal
Massachusetts-specific

## Slide 67: Different incentives created to overcome structural barriers of GHP installation at residential scale
United States
Federal: Homeowners can receive a 30% tax credit on GHP installations (2022-2032) via the Residential Clean Energy Credit, with a gradual decrease in 2033-2034.
Massachusetts-specific: Substantial rebates on GHP installations via the Mass Save program.
  Whole-home systems: Up to a $15,000 rebate; partial-home systems: $2,000 per ton, up to $15,000; income-eligible households: enhanced rebates up to $25,000.
  Rebates are complemented by a 30% federal tax credit and 0% interest Mass Save HEAT Loan (up to $50K over seven years) to help cover installation costs.
Canada
Federal: Homeowners can receive $125 to $5,000 grants for eligible retrofits (including GHP and air-source), plus $600 for energy evaluations, as well as interest-free loans up to $40K with a 10-year term to help finance GHP installations via the Canada Greener Homes programs.
Ontario-specific: HRS (Home Renovation Savings) Program offers up to $12,000 for ground source and $7,500 for air-source heat pumps, based on system size and current heating.
Toronto-specific: HELP (Home Energy Loan Program) provides up to $2,500 in rebates for cold-climate systems, stackable with federal incentives.
Germany
Offers subsidies up to €18,000 for ground source (geothermal) heat pumps; scheme is scheduled to run until 2030.
France
Grants up to €15,000 for GHPs, with the amount based on family income under the MaPrimeRénov Scheme.
Barriers of GHP at residential scale
Incentives across different countries for homeowners
Finance: Residential
High upfront cost: Installation often exceeds $30K, deterring homeowners despite long-term savings.
Site and installation challenges: Vertical loops need deep drilling and permits; horizontal loops require large land area, limiting feasibility.
Lack of awareness: Many homeowners don’t know geothermal is an option or don’t understand the benefits.
Expertise gaps: Installer expertise is regionally uneven, leading to inconsistent quality and higher risk; availability of trained drillers and installers is a major bottleneck; and current drilling capacity is dominated by water well and oil and gas industries.

## Slide 68: GHP district heating & cooling is moving from pilot campus use to community-scale clean infrastructure
Observations
As of 2023, there were >20 GHP-based district energy systems in the U.S., with the majority located on college campuses (as pilot projects); there has also been growing deployment in communities (e.g., Whisper Valley, Texas) and mixed-income housing developments.
Technology: A mix of fourth- (centralized) and fifth-generation (decentralized) is ideal for mixed-use or retrofit-heavy districts where flexibility and building-level control are critical.
Cost and performance: The average construction cost is $3,050/ton (equal to ~$870/kWth) with COP of 4.7; there are no performance or cost differences between fourth- and fifth-gen systems.
U.S. government support: DOE is funding pilot systems in Alaska, Colorado, Vermont, and Oklahoma, many in underserved or rural communities; DOE also is supporting feasibility/design for 11 new systems. NREL has built:
dGeo: Modeling tool to assess shallow geothermal market potential
LeGUp: Performance model for fifth-gen systems to support scale-up
The U.S. is moving from campus pilots to mainstream community deployments, opening opportunities for investment, development, and public-private partnerships.
GHP-based district energy systems in the U.S.
Finance: District
Colorado Mesa Univ.
Whisper Valley
Southeastern Louisiana Univ.
Rogers State Univ.
Missouri Univ. of Science & Tech
West Union
Roosevelt School Condos
Carleton College
Notre Dame
Lake Land College
Epic Campus
Monroe County College
Ball St Univ.
Miami Univ.
Antioch College
Westchester Univ.
Skidmore College
Nome
Seward
Carbondale
Hinesburg
Community scale
College campuses
Installed
In progress
Cornell University

## Slide 69: Successful district-scale GHP pilots demonstrate strong performance, resulting in cost savings and emission reductions
Finance: District
Stronger rationale to push GHP district on a commercial scale: (1) Proven impact from campus pilot: 30-65% annual energy savings, 19-45% annual carbon emission reductions. (2) Federal incentives make GHPs more cost competitive: Commercial and utility-scale GHP systems benefit from a 10% federal tax credit and accelerated depreciation – businesses may deduct 40% of system costs upfront – making district-scale deployment significantly more financially attractive and helping construction costs compete with conventional systems like gas furnaces and central AC.
Technology & system | Capacity (tons) | Coverage | Constr. CapEx | Annual O&M | COP
5th generation, decentralized GHPs | Heating: 2,728 tons Cooling: 3,113 tons | 16 buildings (0.5 km2) | 26.6 US$M | 1.6 US$M | 3.1-6.1
Conventional (3rd or 4th gen), centralized energy stations | Heating: 1,833 tons Cooling: 2,300 tons | 10 buildings (0.1 km2) | 32.0 US$M | N/A | 5.2
Conventional (3rd or 4th gen), centralized energy stations | Heating: 678 tons Cooling: 10,000 tons | 47 buildings (3 km2) | 100.2 US$M | 1.8 US$M | 3.7-4.3
5th generation, decentralized GHPs | Heating & cooling: 274 tons total | 11 buildings (7 km2) | 10.2 US$M | 23.0 US$K | 9.7-13.7
Chart: 
 | 4500 | 7700 | 9400 | 10964.4369 | 2400
Colorado Mesa Univ.
Miami Univ.
Ball State Univ.
West Union Community
CapEx US$/ton
37,200
Geothermal heat pumps
Gas furnace + central AC
(conventional alternatives)
1,800-3,000
Higher cost is driven by smaller capacity, installation under urban retrofit and infrastructure constraints, and bundled cost with broader street upgrades.

## Slide 70: Overcoming challenges and barriers to GHP adoption on a district scale requires more than financial incentives
United States
30% federal investment tax credit for commercial, nonprofit, municipal, and multifamily geothermal heat pump systems; includes accelerated depreciation for for-profit businesses.
New York state: Additional 25% state tax credit (up to $5,000) via NYSERDA, plus rebates and financing under NYS Clean Heat.
Innovative financing tools such as C-PACE, long-term, low-interest loans repaid via property tax; large-scale loans/guarantees for geothermal heating & power infrastructure through DOE Loan Programs Office.
Norway
Enova-funded support for district heating & cooling network construction and expansion, and local renewable heat plants (e.g., GSHPs, thermal storage, waste heat recovery).
Retrofit grants: Up to 25% of costs, capped at NOK 100-150K.
Includes free technical advisory (Enova Answers) and low-interest Husbanken loans for large projects.
United Kingdom
Boiler Upgrade Scheme: Successor to the Renewable Heat Incentive, supporting the shift from fossil fuel heating to low-carbon heat pumps or biomass boilers.
Applies to small and medium non-domestic buildings (e.g., offices, schools, community halls). Offers £7,500 grants for ground or air-source heat pumps (≤45 kWth).
China
Low-interest loans for small and medium-size enterprises in geothermal project development. Select city-level subsidies (e.g., Tianjin): Up to $3,700 for heat pumps to support coal-to-electric transitions.
Barriers to GHP at district scale
Incentives across different countries for commercial/district GHPs
Finance: District
High upfront cost: Drilling and piping push GHP install costs to ~$3,050/ton, above central AC and gas furnace ($1,800 to $3,000/ton).
Efficiency risk from oversizing: Conservative sizing can overshoot demand, which wastes energy and raises loop temps, as seen at Ball State. Avoiding this requires accurate load forecasts, soil analysis, and precise system modeling.
Urban retrofit complexity: Retrofitting GHPs in dense areas is challenging due limited space for boreholes, utility conflicts, and disruption to roads or buildings.
Workforce gap: There is a shortage of skilled professionals with expertise in GHP design, installation, and long-term maintenance.

## Slide 71: Rising geothermal startups with innovations and scalable technologies have attracted the most funding
Finance
 | Focus | Product and Target Market | Key Tech/ Differentiator | Recent Transactions
 | Heating & Cooling | Residential geothermal HVAC systems; simplified drilling and installation Targets single-family homes, small buildings | Alphabet X spinoff; 3,000+ installations; streamlined installation process | $134.5M raised
 | Heating & Cooling | Advanced drilling, subsurface modeling for affordable geothermal urban/commercial HVAC Targets residential developers, property owners | Aims to make installations "so affordable" developers can generate strong ROI; active in CO, UT regions | $12M Series A (Jan. 2025)
 | Heating & Cooling, Power Generation | Eavor-Loop closed-loop system, no need for aquifers or volcanic heat | Makes geothermal viable in non-traditional locations; scalable technology | $504M+ raised; plants in Canada, Germany
 | Heating & Cooling, Power Generation | Geopressured geothermal and energy storage to power data centers | Secured a major contract with Meta for a 150 MW facility | Info not available
 | Heating & Cooling | Manufacturing of heating and cooling systems (especially for the concrete industry); advanced heat pumps and chillers designed for commercial, industrial, and other sectors. | Innovative, fully electric HVAC solution (e.g., ChillMaster product line) | Acquired by Swegon (Feb. 2025)
Small scale, residential
Large utility scale
Geothermal startups attracting the most funding focus on innovations like closed-loop systems and dispatchable clean energy. Investors favor scalable, flexible technologies aligned with high-growth sectors and reliable off-takers (e.g., data centers).

## Slide 72: Dandelion Energy aims to make residential GHPs mainstream
Case study: Dandelion
High reliance on fossil fuels: Millions of U.S. homes, especially in the Northeast, still depend on fuel oil or propane for heating, which are both expensive and carbon-intensive.
Barriers to geothermal adoption: Traditional geothermal systems were expensive, required complex custom installations, and had limited consumer awareness.
Vertically integrated solution for residential geothermal heating and cooling, including:
Ground-loop installation using Dandelion’s proprietary drilling technology.
A high-efficiency heat pump replaces both the furnace and AC.
Software and financing: $0-down financing plans to tackle the barrier of $30K+ upfront cost.
Over 2,000+ systems installed, primarily in New York, Connecticut, and Massachusetts. Expansion continues in the Northeast U.S., where homes are older, heating needs are higher due to the colder climate, and fossil fuel use is prevalent.
Impact per home: Homeowners typically save $1,000 to $2,000 per year on energy bills after switching from oil/propane. Each installation reduces ~80% of a home’s carbon emissions from heating and cooling.
Well-positioned to leverage the IRA 30% tax credit and state-level rebates (e.g., Mass Save rebates in Massachusetts, NYSERDA in New York).
Potential for expansion into other states (e.g., Pennsylvania, Illinois).
A workforce trained in geothermal-specific roles, including drill operations and clean HVAC installation, created an asset.
Company Profile
Based in Mount Kisco, New York.
Founded in 2017 as a spinoff from Alphabet’s X lab (formerly Google X).
Raised $100M+ funding from investors including GV, NEA, Breakthrough Energy Ventures.
Has ~150 employees (as of 2023), including in-house drillers and HVAC installers.
Positions geothermal like a scalable tech product, not a one-off construction job.
Aims to bring geothermal mainstream – like Tesla for EVs or Sunrun for solar – by simplifying adoption, cutting costs, and building trust.
Key pain points
Product & solutions
Impact generated
Future opportunities

## Slide 73: Geothermal Heating and Cooling Deployment

## Slide 74
Site suitability and feasibility assessment Successful deployment hinges on six core factors: Available land area for horizontal/vertical loops, soil composition and thermal conductivity, building heating and cooling loads, groundwater availability (for open-loop systems), geological stability (seismic activity, faults), and underground utilities. Underground utility mapping tools like NREL’s dGeo model and Multicriteria Decision Analysis frameworks assess geospatial feasibility and local economic impacts.
Design optimization and system engineering A case study with 90 boreholes at 500 feet served 132 apartments in 28 buildings. Key design inputs include soil thermal data, heating and cooling loads, and code compliance. Maximizing HDPE piping and grout conductivity reduces borehole length and CapEx. Accurate modeling of peak outdoor air loads and heat pump energy use (COP) ensures system efficiency.
Permitting, mobilization, and deployment barriers U.S. projects face 45-month average permitting involving 14+ agencies; globally, timelines range from four to eight years. Geothermal heating and cooling systems rely on smaller drills and shallower boreholes, easing deployment compared to power systems. Equipment mobilization is highly sensitive to permitting delays, affecting logistics and cost.
Community engagement, education, and safety Early outreach (e.g., town halls, school visits, open houses) builds trust and understanding. Shared value strategies include heat networks, job training, and revenue sharing. Cultural sensitivity is essential near Indigenous lands, requiring co-development, not just consultation. Worker protection: OSHA standards (1910.132, 1926.55) govern PPE, silica, and hot pipe hazards. Costliest injuries include amputations ($126,033) and burns ($52,222).
Lifecycle O&M and responsible decommissioning Monitoring includes temperature probes, flow rates (e.g., 180 L/min), and pressure controls. Failure risks include probe malfunction, leaks, and mechanical wear. Annual maintenance ($300 to $500) avoids repair costs >$2,000 and extends system life. Decommissioning safeguards against groundwater contamination, ensures land restoration and meets variable regulatory requirements. Early planning and budgeting is critical for compliant closure.
Key messages
Deployment

## Slide 75: Identifying key stakeholders is crucial to successful deployment of a geothermal heating & cooling project
Key deployment stages and stakeholder engagement map
Deployment
Planning
Design & Engineering
Permitting
Construction & Installation
Operations & Maintenance
Decommission
1
6
5
4
2
3
Stage | Key stakeholders | Key activities
 | Site owners/building operators | Provide site access and building data
 | Geologists and geothermal consultants | Conduct subsurface and thermal analysis, execute feasibility assessment
 | Local utilities | Assess infrastructure for integration
 | Community organizations | Facilitate local engagement and feedback
 | Project developers and investors | Initiate and fund planning
 | Local, state, and environmental regulators | Approve land use and drilling activities, ensure compliance
 | Legal advisors | Prepare and submit legal compliance documents
 | Engineers and HVAC designers | Design system layout and HVAC compatibility
 | Software modelers | Run thermal simulations to optimize performance
 | Building architects | Incorporate system into building design
 | Drilling contractors | Drill boreholes and install piping systems
 | Construction crew | Install mechanical and electrical infrastructure
 | Site safety and quality assurance officer | Ensure field safety and risk compliance
 | Facility managers and maintenance contractors | Oversee operation, handle routing servicing and repairs
 | Local authorities | Authorize decommissioning procedures
 | Restoration contractors | Restore landscaping and ecological balance
1
2
3
4
5
6
1
1
1
1
2
3
3
4
4
6

## Slide 76: Requirements for site suitability and risk avoidance
1
Deployment: Planning
4
5
3
2
6
1
Frameworks for site suitability assessment:
Comprehensive Multicriteria Decision Analysis Framework
dGeo Model
NREL's WIRED Model Suite
Define Decision Context
Establish Criteria Categories & Metrics
Weight Criteria
Score Alternatives
Aggregate Results
Sensitivity & Uncertainty Analysis
Interpret & Recommend
NREL model, uses a high-resolution geospatial database to evaluate the feasibility of geothermal heat pumps in specific regions
Suite of models by NREL, designed to evaluate the local economy-wide impacts of geothermal heat pump installations, district heating and cooling, and power generation plants
dGeo Model
Cornell University Geothermal Plan
Available Land Area: Sufficient space is crucial for ground loops (horizontal and vertical) depending on site needs.
1
Soil Composition and Thermal Conductivity: The type of soil and its heat transfer ability play a significant role in the systems efficiency.
2
Building Heating & Cooling Loads: The buildings’ type and size must match the buildings’ energy requirements.
3
Ground Water Availability: Ground water is necessary for open-loop systems; quality and availability must be assessed.
4
Geological Conditions: Faults and areas with high seismic activity can impact drilling capabilities and system performance.
5
Underground Utilities: The location of existing utilities must be carefully considered to avoid drilling conflicts.
6
*List is relevant for residential, commercial, and public-private use.

## Slide 77: The key to community acceptance lies in educating stakeholders about the benefits of geothermal energy
Mitigation Strategies
Early Engagement: Involve communities in town halls, school visits, and open houses before drilling begins.
Transparent Communication: Clear info on safety, benefits, and impacts to demystify the technology.
Shared Value: Offer community heat networks, job training, or revenue sharing.
Cultural Sensitivity: Especially when operating on or near Indigenous land, it is crucial to co-develop, not just consul.
Robust Compensation Models: This includes compensation for land use, disruption, or visual impact.
Key community challenges during the planning phase of geothermal heating and cooling projects
1
Deployment: Planning
Lack of understanding
Land use conflicts
Access inequity
NIMBY (not in my backyard)
Cultural sensitivities
Drilling concerns
Fear of drilling, induced seismicity, or visual or noise concerns during drilling
Misconceptions about environmental impact and technology
Disputes over subsurface rights, private wells, or land devaluation
Upfront costs as a barrier, lack of financing options for low-income households
Support in principle, but resistance to installations near homes or schools
Projects intersect with culturally significant lands or sacred Indigenous sites

## Slide 78: Several site-specific factors dictate the design and economics of a GHP system
Several design criteria are critical to GHP system designers:
Soil characteristics – Allowable drill depths, soil thermal conductivity, and soil composition influence the heat transfer characteristics of geothermal reservoir.
Piping and grouting – Grouting and HDPE thermal conductivity need to be maximized to minimize total borehole length (to reduce project CapEx).
Outdoor air peak load – Determined by measuring the maximum amount of heat the GHP system would need to transfer during the hottest and coldest periods of the year.
Heat pump energy load – Dictating the system’s overall coefficient of performance (COP), energy load for compression and pumping compared to total heat transfer capabilities determines the energy costs of the system.
Typical geothermal heat pump system
2
Deployment: Design
Vertical
Heat pump
Horizontal
B
D
C
A
A
B
C
D
Highlight: GHPs can cut energy bills by up to 65% compared to traditional HVAC systems and typically recoup their upfront cost within 10 years through energy savings.

## Slide 79: COMSOL Geothermal Heat Transfer Models can predict temperature profiles of geothermal heat sources
Through computational thermodynamics, the temperature profile of a simulated vertical ground source heat pump system can be determined.
Based on peak HVAC load requirements and closed-loop heat transfer properties, the borehole length can be optimized using the simulated temperature profile.
Upstream oil and gas reservoir modeling expertise is transferable to larger commercial and industrial geothermal projects.
Thermal interference effects — such as heat drawdown between closely spaced boreholes — can reduce efficiency and must be accounted for in system design.
Subsurface groundwater flow significantly influences heat recovery rates, underscoring the need for accurate multiphysics simulation in layered geological settings.
Temperature profile of a shallow 130-meter vertical GHP system with a 3-part HDPE piping system
2
Deployment: Design
Chart: 
 | 12.5
 | 12.5
 | 12.5
 | 12.5
 | 12.5
 | 12.5
 | 12.5
 | 12.5
Temperature profile (oC)
14
12
10
8
6
4
2
0
At 60 to 70 meters, the site contains an aquifer that can be modeled.

## Slide 80: Utilizing effective siting and design methodologies to design a CapEx-efficient geothermal system
Observations
The community geothermal design case study used effective siting and design methodologies to design a CapEx-efficient geothermal system.
The total system will supply heating to 132 apartments in 28 buildings. Project specifics include:
  Drill 90 500-foot boreholes
  Construct pump house
  Distribute water/glycol fluid to apartments
  Retrofit apartments with water-source heat pumps
The UConn Institute for Advanced Systems Engineering and LN Consulting led the engineering design work. Design factors included:
  Heating and cooling loads
  Soil thermal data
  Applicable codes
2
Deployment: Design
Site Data
Energy Modeling (EnergyPlus/ OpenStudio)
GHP Modeling (TRNSYS)
Conceptual Design Analysis
Detailed Design
Site Visits
Site Drawings
Integrating Energy and GHP Modeling
Energy Audit
Utility Data
Site Visits
Design Process Overview
Project Financials (units in millions)
Key Project Facts
Chart: 
 | 8.7 | 8.595 | 7.855 | 4.713 | 4.713
 | 0.105 | 0.74 | 3.142
$8.70
Total CapEx
$0.11
WED Incentive
$0.74
State Incentive
$3.14
Federal ITC
New CapEx
$4.71
- 31%
- $12.9 million
Reduction in tenants’ heating bill
Savings in 30-year lifetime costs vs. gas retrofit

## Slide 81: The average permitting process in the U.S. takes 45 months on average and includes 14+ responsible agencies
Permitting process in the U.S.
3
Deployment: Permitting
Multilevel responsible agencies
Federal agencies | 
 | Bureau of Land Management (for federal lands)
 | Environmental Protection Agency
 | Federal Energy Regulatory Commission (for power)
 | Public utility commissions, if it involves district heating sales
State agencies | 
 | Department of Natural Resources
 | State water resource agencies
 | State environmental agencies
 | Department of Water Resources
 | Department of Environmental Conservation
Local agencies | 
 | County zoning offices
 | County drilling permits
 | Municipal water authorities
 | County building departments
 | Local utilities
Land Use
Land lease
Right of way
1-6 months
Exploration
Exploration permit/license
3-12 months
Drilling
Well drilling permit
2-6 months
Environmental
Environmental impact assessment
NEPA Review
6-36 months
Water Use
Water rights
Extraction permit
2-12 months
Construction
Building permit
Mechanical permit
1-3 months
Grid connection
Interconnection agreement
Grid access permit
3-9 months
Operation
Operational license
1-6 months
Decommission
Plan for decommission/ closure
3-12 months
15-75 months until construction completed
4-18 months including end of life
3-9 months
If hybrid power generation
Until end of life
Until construction completion

## Slide 82: Permitting leaders are streamlining processes, while challenges arise for countries with fragmented processes
Best practices and challenges by countries
3
Deployment: Permitting
Iceland
Centralized under the National Energy Authority (Orkustofnun); a national priority
Simple property rights: Landowner owns resources on private land
Long-established legal and technical frameworks
6-12 months
Sweden
Clear distinctions for shallow vs. deep geothermal
Simple notification process for most residential/medium-depth systems
One main ordinance governs process (1998:899)
1-3 months (shallow); up to 6-12 months for deeper systems or protected zones
France
Simplified in 2023 to halve permitting times
Coordinated support from ADEME (environment/energy agency)
Clear licensing system under Mining Code for deep geothermal
1-2 years (previously longer)
USA
Jurisdiction split among federal (BLM, EPA), state (natural resources, water rights), and local (zoning/building)
NEPA reviews add years unless expedited
Each project requires navigating at least 5-7+ agencies
5-10 years (worst case); with expedited reforms (2025), aim for 1-2 years
Best practice: Streamlined
Challenged: Fragmented
Türkiye
Multiple layers including provincial and national agencies
Inconsistent enforcement, political/ bureaucratic delays
Water, drilling, and land permits handled by separate ministries
2-5 years depending on project and province
Netherlands
Dual licensing under the Mining Act and the Environmental Licensing Act
Coordination needed between Ministry of Economic Affairs and State Supervision of Mines
3.5-9.5 years depending on depth, location, and complexity

## Slide 83: Alongside nuclear energy, geothermal power has the longest permitting timelines among all renewable energy sources
Best practices and challenges by renewables
3
Deployment: Permitting
Geothermal
Permitting time: 4-8 years
Phases:
Resource exploration
Leasing (often BLM for federal land)
Drilling and testing
Construction and operation
Wind
Onshore permitting time: 1-3 years
Offshore permitting time: 5-7+ years
Phases:
Site identification + leasing (BOEM for offshore)
Environmental review (NEPA)
Construction and operations plan (COP)
Grid interconnection and local/state approvals
Solar
Permitting time: 1-2 years
Phases:
Site selection and feasibility
Environmental assessments (especially on federal land)
Local/state/federal permitting
Grid interconnection
Nuclear
Permitting time: 5-10+ years
Phases:
Early site permit (ESP)
Combined license (COL)
Design, construction, commissioning
Carbon Capture
Permitting time: 2-5 years
Phases:
Site selection
EPA Class VI well permitting
NEPA review
Construction and monitoring
Short Permit
Long Permit

## Slide 84: Geothermal installation workers face hazards including drilling accidents, heat exposure, and confined space risks
OSHA regulations require employers to protect workers by providing proper PPE, guarding hot pipes, and limiting exposure to hazardous
Injury Data
4
Deployment: Installation
Trenching and excavation dangers: Cave-ins have caused fatal incidents.
Exposure to hot water and steam: Risk of severe burns from sudden heat release.
Toxic gas exposure: Hydrogen sulfide leaks may cause respiratory distress or collapse.
Confined space hazards: Chemical fumes and oxygen depletion may lead to serious illness.
Slips and falls: Workers risk falling into hot water pools or other hazards at remote sites.
Mechanical Injuries: Equipment malfunctions and handling heavy tools can cause fractures and other injuries.
OSHA requires workers to have personal protective equipment: 1910.132(a); keep a distance of 15 inches to 7 feet from hot water pipes: 1910.261(k)(11); limit exposure to an 8-hour working window 29 CFR (1926.55, 1910.1000).
Hazards
Chart: 
 | 126033 | 63044 | 62240 | 52222
Other Trauma
Fracture, Crush, Dislocation
Burns Community
Amputation
$63,044
$62,240
$52,222
$126,033
**EU regulations address similar requirements through OSH, Machinery, and Pressure Equipment Directives but often impose stricter exposure limits than OSHA. Asian jurisdictions also regulate these risks through frameworks such as KOSHA and other country-specific OSHA equivalents, though standards and enforcement can vary by country. This list is not exhaustive.

## Slide 85: Critical parameters like temperatures, system pressure, and flow rates need to be monitored
GHP system monitoring includes:
Temperature set points: Primarily temperature in the internal environment. Based on specified target temperatures, actual temperatures are continuously measured for deviance using probes.
System-level controllers: Primarily pressures and flow rates of the heat pump loop. As seen in the study shown left, the heat pump system is activated to release 180 L/minute once the control room temperature falls below 14.5℃.
Risk factors: Temperature probe failure, mechanical leaks, and more can affect system operation.
Main service providers and players:
Temperature vs. system flow rate during 36 hours of a GHP system operation in Korea
5
Deployment: Operation
Chart: Hours of Operation (36-hour window)

## Slide 86: Consistent maintenance checklists can help minimize lifetime OpEx
A GHP system’s overall maintenance costs and reliability can be optimized through proactive owner engagement:
Integrate GHP maintenance into facility management: For commercial facilities with regular maintenance staff, critical areas such as testing refrigerant and examining leaks should be included in maintenance checklists.
Monitor performance: Observe GHP performance and track utility consumption for efficiencies, engaging with trusted technicians for any adjustments needed.
Budget for routine service: Annual maintenance that requires technicians can cost $300 to $500 per year, but that service extends GHP system life and reduces the need for eventual equipment replacement or repairs that can cost more than $2,000.
Key parameters and checklist
5
Deployment: Operation
Parameter | Overview | Schedule | Conducted by | Importance to System
Check and replace air filters | Inspect filters monthly and replace as needed | Monthly | Owner | 
Monitor system performance | Monitor energy bills for inconsistency | Monthly | Owner | 
Inspect coils | Check air handler and heat pump coils for dirt/debris | Biannual | Owner | 
Clean condensate drains | Inspect condensate drains for any clogs and leaks | Biannual | Owner | 
Inspect ductwork | Look for visible signs of damage or disconnections | Biannual | Owner | 
Test thermostat | Verify thermostat is accurately reading temperature | Biannual | Owner | 
Refrigerant level check | Get technician to verify refrigerant levels | Annual | Technician | 
Electrical component inspection | Conduct comprehensive testing of electrical components | Annual | Technician | 
Ground loop pressure test | Check for proper pressure for efficient heat transfer | Annual | Technician | 
Heat pump performance evaluation | Schedule professional testing of heating & cooling modes | Annual | Technician | 
Ductwork cleaning | Have professional inspect and clean ductwork | Annual | Technician | 
M
M
M
M
M
H
H
H
H
L
L
Level of Importance
L
Low
Moderate
High
M
H

## Slide 87: Adhering to guidelines prevents groundwater contamination and ensures quality of land and reuse
Observations
Decommissioning geothermal systems is critical to prevent or control for:
Groundwater contamination
Restoration of land usability
Adherence to regulatory requirements enforced by various levels of government
While the core objectives of decommissioning are consistent, permitting requirements, timelines, and costs vary significantly by jurisdiction and project scale, making planning and budgeting essential to successful project closure.
Proper decommissioning is essential to protect groundwater, comply with local regulations, and ensure safe removal of equipment and fluids
6
Deployment: Decommission
Evaluate
Disconnect
Remediate
Assess
Identify system (closed loop, open loop, direct exchange) and type (residential vs. commercial).
Determine local and state permitting and environmental regulations.
Turn off equipment, drain heat exchange fluid/ refrigerants, and remove hardware.
Grout boreholes, seal wells, restore landscaping, and document and submit closure reports.
System Type | General Decommissioning Steps
Open Loop | Cut well 4 feet below surface. Fill well with gravel, clean sand, or stone. Fill upper 10 feet with cement/6% bentonite and allow overflow, preventing water contamination. Compact soil above well cutoff.
Closed Loop | Remove and dispose of heat exchange fluid per state and local guidelines. Excavate hole at least 5 feet around well. Fill loop with high-solids bentonite slurry and allow for overflow, preventing water contamination.
Direct Exchange | Follow the first two steps of closed-loop decommissioning. 2. Fill loop with cement grout and allow for overflow, preventing water contamination.

## Slide 88: Team

## Slide 89
Pia Doris Morrow
MS in Sustainability Management
Team Lead | Climate Knowledge Initiative Fellow
Zacharia Thurston
MS in Sustainability Management
Climate Knowledge Initiative Fellow
Faradisa Anintya
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Una Oljaca
BA in Economics, Political Sciences, and Government
Climate Knowledge Initiative Fellow
Leo Gordon
MPA, Columbia SIPA
Climate Knowledge Initiative Fellow
Hassan Riaz
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
CKI Geothermal Team
Fellows

## Slide 90
Hyae Ryung (Helen) Kim
PhD in Sustainable Development
Former Senior Research Fellow
CKI Team Staff, Faculty, and Alumna

## Slide 91: Appendix

## Slide 92: Glossary (1/2)
CKI Guideline for Geothermal Terms
Baseload power | Electricity supplied consistently over time to satisfy the minimum level of demand
Peaker plant | A power-generation facility that is used only during periods of high electricity demand (peak loads) rather than continuously
Hydrothermal: Conventional geothermal | A geothermal system in which naturally occurring heat, fluid, and rock permeability are present, allowing heat extraction without major engineering of the reservoir
Dry steam power plants | A geothermal plant type in which steam (rather than hot water) from the reservoir is piped directly to a turbine to generate electricity
Flash steam power plants | A geothermal plant type in which high-pressure hot water from underground is brought to the surface, the pressure drops, water “flashes” into steam that drives a turbine, and remaining fluid is often reinjected
Binary cycle power plants | A geothermal plant in which geothermal fluid (often lower temperature) transfers heat to a secondary “working fluid” via a heat exchanger; the working fluid vaporizes and drives a turbine, while the geothermal fluid remains in a closed loop and is reinjected
Next-generation geothermal | An umbrella term for geothermal approaches beyond conventional hydrothermal resources; that is, systems using engineered reservoirs, closed loops, or other technologies to expand geothermal potential
Closed-loop geothermal systems (CLGS) | Geothermal systems in which the working fluid is circulated through sealed loops of pipe drilled into hot rock, extracting heat by conduction rather than relying on natural rock permeability or fluid pathways
Enhanced geothermal systems (EGS) | A method to develop geothermal energy in hot but low-permeability rock by artificially creating or improving the permeability (for example via hydraulic stimulation) so that fluid can circulate and extract heat
Advanced geothermal systems (AGS) | Often used interchangeably with closed-loop systems, geothermal systems that are engineered and do not depend on naturally favorable permeability or hydrothermal fluids
Superhot rock geothermal | Geothermal systems operating at very high temperatures (for example >400°C), often in rock that may reach or exceed super-critical conditions, thus offering a high-potential energy yield per well

## Slide 93: Glossary (2/2)
CKI Guideline for Geothermal Terms
Plasma drilling | A drilling method under development in which plasma (ionized gas) is used to erode or vaporize rock ahead of the drill bit, aiming for faster penetration in very hot or hard rock
Thermal spallation | A drilling technique under development in which rapid heating of rock causes spalling, rapid flaking, or fracturing of the rock surface, to assist borehole advancement in high-temperature conditions
Millimeter-wave drilling (Gyrotron) | A drilling technique under research using high-power electromagnetic waves at millimeter wavelengths (often from a gyrotron) to heat or vaporize rock ahead of the drill, to enable drilling in extreme rock/temperature environments
Laser-assisted drilling | A drilling technique under development in which lasers are used to ablate or weaken rock ahead of the drill bit, thereby improving the drilling rate or reducing bit wear in hard/high-temperature formations
Frontier technologies | Emerging and experimental geothermal technologies beyond current commercial practice, including advanced drilling, novel stimulation techniques, and reservoir-creation methods (please refer to technologies below)
Magma-based geothermal | Geothermal systems that aim to extract heat directly from molten or partially molten rock (magma) or adjacent high-temperature zones; a higher-risk/higher-reward approach in the geothermal field
Geopressured geothermal | Geothermal systems in sedimentary basins where hot fluids are under high pressure (geopressure), sometimes containing dissolved gas (e.g., methane), which can provide combined heat and gas resource potential
Directional drilling | A drilling technique in which the wellbore is steered off vertical (horizontal or angled) to reach target zones of heat, fluid, or permeability that are not directly beneath the surface well pad
Hydraulic fracturing | A stimulation technique in which fluid is injected at high pressure into rock to open or expand fractures, thereby creating or enhancing permeability so that fluid can circulate; used in EGS development