## Slide 1: Geothermal Heating and Cooling Executive Summary
Gernot Wagner, Pia Doris Morrow, Zacharia Thurston, Faradisa Anintya, Hassan Riaz, Una Oljaca, Leo Gordon, Isabel Hoyos, and Hyae Ryung Kim
10 March 2026
Cite as: Wagner et al. “Geothermal Heating and Cooling,” Columbia Business School Climate Knowledge Initiative (10 March 2026).

## Slide 2: Geothermal energy technologies span heating & cooling and power generation, with conventional approaches most widely deployed
Geothermal Opportunity
Key pathways for harnessing geothermal energy for heating & cooling and power generation
Conventional/hydrothermal
Underground thermal energy storage
Geothermal heat pumps
Direct-use heat
Borehole thermal energy storage
Aquifer thermal energy storage
Mine thermal energy storage
Advanced geothermal/ closed-loop systems
Enhanced geothermal systems
Next-generation technologies (commercialization <5 years)
Superhot rock
Frontier technologies (commercialization 5+ years)
Geopressured systems
Heating and cooling
Power
Production
Storage
Production
Storage
Cavern thermal energy storage
Pit thermal storage
Reservoir thermal storage
Magma-based geothermal
High-temperature geothermal energy storage
Geomechanical energy storage

## Slide 3: Today, 10 countries consume 90% of global geothermal energy, with almost 80% of end use for heating and cooling
Heating: China is the most significant country, accounts for nearly 50% of global geothermal final energy consumption, dedicated entirely to space heating.
Electricity: The U.S., Indonesia, Türkiye, the Philippines, and New Zealand generate two-thirds of global geothermal electricity, with Iceland, Italy, Kenya, Mexico, and Japan contributing an additional 25%.
Total final geothermal energy consumption
by consuming countries, 2023
Total final geothermal energy consumption
by application, 2023
Opportunity: Heating & cooling
Chart: 
 | 620.8403 | 590 | 220 | 110 | 60 | 50 | 50 | 30 | 30 | 20 | 20
0
400
500
300
1.400
200
100
Global
U.S.
Turkiye
Sweden
Indonesia
Iceland
Japan
New Zealand
Germany
Philippines
Consumption (PJ)
China
0.2%
0.5%
1.0%
3.7%
2.5%
5.2%
30.0%
0.3%
18.8%
0.3%
14.6%
% of geothermal to total energy consumption, 2023
Chart: 
 | 100 | 58.13 | 32.06 | 24.95 | 21.79 | 21 | 21
 | 41.87 | 26.07 | 7.11 | 3.16 | 0.79
Total
42%
Geothermal heat pumps
26%
District heat
7%
Direct residential & comm.
3%
Agriculture & fishing
1%
Industry & other
Power (Electricity)
100%
21%
1,400 PJ
Heating & cooling (79%)

## Slide 4: By 2050, geothermal heating use is projected to almost double, driven largely by China and building and district heating
Geothermal heating use doubles in 2050 under a realistic government Stated Policies Scenario (STEPS), with China as the biggest source of growth. Yet, it remains only 0.5% of total heat consumption globally.
From the use-case perspective, nearly 90% of geothermal heating consumption comes from residential and commercial buildings, mainly through district heating networks, including thermal baths in the tourism and wellness sector.
Geothermal heating consumption (PJ), projection by region 2023-2050
Increase (%) by heating application globally, 2023-2050
Opportunity: Heating & cooling
Chart: 
 | 1106 | 600 | 160 | 135 | 145 | 35 | 31
 | 2000 | 1250 | 240 | 185 | 175 | 55 | 41
0
500
1.000
1.500
2.000
Global
China
U.S.
EU
Other Europe
Japan
RoW
2023
2050
Incl. Sweden, Germany, France
Incl. Türkiye, Iceland, Norway
2.0%
0.5%
0.5%
1.5%
0.2%
<0.1%
0.5%
xx%
% of geothermal to total heat consumption, by 2050
Chart: 
 | 101 | 12 | 6 | 6
 | 89 | 6
Total increase
89%
Res. & comm.
6%
Industry & other
Agriculture & fishing
6%

## Slide 5: Geothermal heating & cooling technologies are proven, deployable solutions for decarbonizing building thermal loads
Technology
 | Geothermal Heat Pumps (GHPs) | Direct-Use Geothermal | Underground Thermal Energy Storage (UTES)
Description | Constant temperatures are harnessed via open- or closed-loop fluid circulation and transferred through heat pumps. | Hot water from naturally occurring underground reservoirs is used directly for heating applications. | Seasonal energy storage in underground formations such as boreholes (BTES) or aquifers (ATES) accommodates later use.
Depth range | 50-300 meters | 400-2,000 meters | 20-1,000 meters
Temperature | 4.5-21ºC | 20-150ºC | 0-100ºC
Alternative to | Air-source heat pumps Boilers/propane heaters | Coal, oil, gas boilers used for district heating systems | Peaking fossil fuel systems Boilers and furnaces
Advantages | High COP (3-5) Peak load reduction Weather resistance | Suitable for large-scale applications Can target higher temperature | Energy savings and grid energy use optimization Low land use
Barriers | Site specificity Skilled workforce needs | Site specificity Limited use slowing cost reductions | Site specificity Heat loss over time Cost and efficiency uncertainties
Cost | US$66-$109/MWh | US$66-$109/MWh | N/A

## Slide 6: Geothermal heat pumps can be closed loop, open loop, or hybrid, and are most often used in residential or commercial settings
GHP Technology
Closed loop
Vertical
Heat pump
Horizontal
Pond/Lake
Open loop
Hybrid
Heat pump
Well discharge
Surface discharge
Cooling tower
Heat pump
1
2
3
1
2
Low land use; more common in large buildings
Most cost efficient for residential installations; highest land use
Cost effective; less land use and maintenance
Hybrid systems typically combine a geothermal resource with a cooling tower. Hybrid systems are most effective when cooling needs are significantly higher than heating needs (e.g., data centers). Hybrid systems can reduce up to 50% of the cost vs. non-hybrid systems while increasing installation speed.
Compared with closed-loop GHPs, open-loop systems have more efficient heat transfer but require greater pump energy use. Open-loop systems also have a shorter lifespan (10-15 years) and can worsen water quality when discharged.

## Slide 7: Underground thermal energy storage supports renewable energy integration, but adoption is limited by infrastructure needs
UTES Technology
Borehole thermal energy storage (BTES)
Heat pump
Heat exchanger
Aquifer thermal energy storage (ATES)
Heat exchanger
Extraction Well
Injection Well
Charging
Discharging
Extraction Well
Injection Well
Heat exchanger
Heat exchanger
Aquifer
Impermeable layer
Soil & rock
Charging
Discharging
Heat pump
Heat is stored directly in rock.
Heat is stored in groundwater.
BTES and ATES Compared |  | 
 | BTES | ATES
Energy Density | 15-30 kWh/m3 | 30-40 kWh/m3
Temperature | ~80ºC | <25ºC
Storage Efficiency | Low in first years, increases after 3-4 years; 45-60% | 70-100% (cold storage); 50-80% (heat storage)
Storage Volume | 3-5 m3 for 1 m3 water equivalent | 2-3 m3 for 1 m3 water equivalent
Use Cases | Wider range of applications | Large-scale applications
Risks | Thermal contamination; subsurface instability | Groundwater contamination
Investment Costs | 20-60 US$/m3 | 58-70 US$/m3
Lifespan | Can exceed 100 years | 25-50 years

## Slide 8: Next-generation geothermal may bypass resource-related limitations of conventional geothermal, opening new avenues for scaling the industry
Technology
Geothermal heating and cooling consumption by application globally
Conventional geothermal is limited by geographical and temperature constraints…
… making next-generation geothermal attractive for reducing emissions in industrial and district heating use
Chart: 
 | 4 | 53 | 9 | 1 | 33
4%
1%
Agriculture & Fishing
GHPs
Direct Use
Industry
District Heat
Industrial Heat | In a low-cost APS scenario, next-generation geothermal could economically displace ~3 EJ of fossil fuel consumption by 2035 for industrial heat globally (10% of industrial heat <200ºC) and almost 10 EJ by 2050 (35% of industrial heat <200ºC). Up to 230 Mt of CO2 emissions could be avoided.
District Heat | In a low-cost scenario, next-generation geothermal could capture 20% of district heating growth between 2035 and 2050. Investment costs below US$4,000/kW would make next-generation geothermal district heating cost competitive. Co-generation (CHP) plants are an economically attractive application due to revenue generation from electricity shares
Share of total supply for next-generation geothermal heating, 2030-2050 (%)
Chart: 
 | 0.3 | 8 | 9.2
 | 0.1 | 1.3 | 3.6
2030
2040
2050
Industrial Heat
District Heat
Conventional geothermal heat use in industry remains limited due to geographical dependence on hydrothermal reservoirs and lower relative temperatures.
Direct use can require greater temperatures than those accessed via conventional geothermal.
GHPs remain the most cost-effective application of conventional geothermal resources.

## Slide 9: Geothermal heating and energy storage face significant challenges across the value chain — specifically for raw materials
Observations
The demand for copper is skyrocketing due to its critical role in renewable energy infrastructure (solar panels, wind turbines) and electric vehicles (EVs).
Since GHPs require copper for their heat exchangers, wiring, and compressors, this puts them in direct competition with solar PV, wind power, and EV manufacturers, leading to supply bottlenecks and price volatility.
Drilling rigs are essential for geothermal systems, but they share similar equipment and expertise with O&G, which drives up costs and limits availability.
The skilled workforce for drilling, maintenance, and system operation is also in high demand for O&G projects, making talent scarce and expensive for the geothermal sector.
Disposal issues stem from hazardous materials used in GHPs, primarily:
  Refrigerants in compressors
  Heat transfer fluids (glycol- or methanol-based solutions)
  Plastics and coatings (HDPE pipes and Teflon seals)
These materials require specialized disposal and recycling infrastructure, adding complexity to the end-of-life phase.
Key challenges along the geothermal value chain
Geothermal supply challenges of
geothermal heat pumps (GHPs) and underground thermal energy storage (UTES)
End of life
Exploration & raw materials
Operations & maintenance
Copper
HDPE
Glycol
Methanol
Steel
Drilling rigs
ASHPs vs. GHPs
Semiconductors
Skilled workforce
Thermal imbalance
Scaling & fouling
Disposal
Site restoration
Deep dive
Deep dive
Deep dive
Deep dive
A
B
C
E
Compressors
Development & drilling
Deep dive
D

## Slide 10: Four key policy priorities can help scale geothermal heating & cooling deployment and drive down costs
Observations
Stronger implementation of policy goals could boost new geothermal heat developments 50% by 2030 in the APS compared with the Stated Policies scenario.
Strong policy can also help drive next-generation geothermal cost reductions of up to 80% by 2035.
In the APS, expanding policy support and cost reductions would scale GHP consumption to almost 3,000 PJ — 50% higher than in the Stated Policy scenario (China, U.S., and Europe together account for 80% of this growth).
Almost two-thirds of geothermal power capacity additions between 2024 and 2030 are expected to be policy-driven – primarily tax credits, fixed tariffs, and premiums.
Policy
Global Collaboration
Global collaboration on geothermal energy – particularly heating and cooling – lags behind other renewables, slowing innovation and increasing risk. Stronger, more large-scale collaboration is a priority.
Workforce Development
Geothermal expansion will require a skilled workforce in engineering, geology, and drilling sectors. Transitioning the oil and gas workforce will streamline geothermal workforce development.
Research & Development
Poor funding infrastructure for geothermal exploration and drilling drives up investment costs and slows technological progress. Strong funding mechanisms will be necessary to speed geothermal deployment.
Risk Mitigation
Geothermal projects have higher predevelopment risks compared with other renewable energy technologies due to complex geological and subsurface conditions. Mitigating risk is critical in lowering project costs.

## Slide 11: Leveraging oil & gas capabilities can lower geothermal power costs and accelerate deployment
Policy: Workforce development
Problem | Current Challenge | Oil & Gas Synergy | Limitations | Case Example
Resource Identification | Accurate geothermal resource identification and modeling require multi-parameter surface data (seismic, geology, heat flow, permeability). | Oil and gas surface imaging and drilling data reduce exploration risk and improve reservoir targeting. | Legacy oil and gas datasets often lack thermal gradient resolution or long-term heat recharge data. | Hungary and the Netherlands: Open oil and gas subsurface databases reduce geothermal exploration costs and uncertainty.
Skilled Workforce Needs | Skilled workforce shortages in reservoir engineering and well completion delay project scaling. | Oil and gas professionals have skills that can apply to geothermal exploration, development, and operation. | Current policy frameworks provide limited financial incentives for geothermal workforce transfer. | DOE Geothermal from O&G Initiative: Demonstrates feasibility of cross-sector workforce and skill transfer.
Drilling Costs | Subsurface drilling represents 60 to 80% of total next-generation geothermal CapEx. | Hydrocarbon well technology (e.g., horizontal drilling, multistage stimulation) can be directly transferred to EGS. | Geothermal wells require sustained reinjection and higher temperatures tolerance than O&G operations. | Fervo Energy’s Project Red: Achieved record flow rates by adapting shale fracking and fiber-optic monitoring.
Co-production and Well Repurposing | High initial exploration, drilling, and completion costs can be a limiting factor in geothermal projects. | Co-production or heat extraction from abandoned wells can de-risk geothermal projects. | Wells require a large heat gradient and flow rate, flexible permitting, and proximity to demand. | Zanskar Project (U.S.): AI-driven reservoir modeling revitalized legacy wells, cutting exploration risk by >50%.
Level of shared competencies

## Slide 12: Europe leads in geothermal heating & cooling regional policy adoption and collaboration; rest of the world lags behind
Observations
Over half of all countries with geothermal policies in place (16 of 31) focus exclusively on power generation.
Regional policy schemes in Latin America and East Africa are not included in this map.
Only eight countries (all in Europe) have adopted geothermal roadmaps for their heating & cooling sectors.
>100 countries have policies in place for solar PV and onshore wind — over 3x as many as for geothermal energy.
Europe is a regional hub for geothermal heating & cooling policies, while China leads on the country level.
Geothermal energy is a priority mitigation option in only 9% of NDCs’ submitted data.
While the risk mitigation-to-remuneration policy ratio is ~1:2 for solar and wind energy, the ratio for geothermal energy is ~1:1 due to high early-stage risk.
Countries with geothermal policies in place, 2024 (risk mitigation and/or remuneration)
Global policy

## Slide 13: While strong policy support is concentrated in China and Europe, installed capacity grows even in subpar policy landscapes
Observations
China has one of the strongest policy frameworks, but its geothermal heating policies may not be easily transferrable.
In Europe, both domestic and regional interest in geothermal heating & cooling has grown in the context of energy security concerns.
Untapped potential is concentrated in Africa and Latin America, where geothermal power is prioritized over H&C due to warmer climates and regional needs.
Legacy markets such as the U.S. have high installed capacity, but fragmented policy has inhibited economies of scale.
While global leaders have strong policy on conventional geothermal, emerging players are increasingly investing in next-generation technologies.
Global policy and installed capacity matrix for geothermal heating & cooling
Global policy
Global Leaders
Legacy Markets
Emerging Players
Untapped Potential
Installed Capacity
Policy
Iceland
China
USA
Sweden
Netherlands
Indonesia
Croatia
South Korea
Germany
Mexico
Brazil
India
South Africa
France
Morocco
Türkiye

## Slide 14: Not one size fits all: Geothermal projects globally leverage different financing options
Finance
 | Description | Advantages and Challenges | Example
Public-Private Partnerships | Combines government funding with private equity/debt | Leverages both public oversight and private sector efficiency. Involves complex coordination and legal frameworks. | Kenya’s Rift Valley development (World Bank support) Large-scale power generation and infrastructure projects (2019-present)
Green Bonds | Debt instruments for renewable projects | Attracts investors seeking green investments; scalable. Dependent on investor confidence and credit ratings. | Iceland’s geothermal expansion via bonds Utility-scale geothermal expansions (2018-present)
Government Grants | Federal and state funding for R&D and deployment | Non-dilutive funding; promotes innovation and early-stage support. Often limited in size and competitive to obtain. | U.S. DOE $200,000 grants for geothermal heating & cooling tech. Pilot/demo projects, new tech in heating & cooling (grants announced in 2020)
Concessional Loans | Low-interest loans from development banks | Reduces financing cost for developing countries. Can lead to debt accumulation; tied to lender conditions. | Philippines’ geothermal sector (international aid) Exploration, drilling, and plant development in emerging markets (2010-2015)

## Slide 15: GHPs require incentives to overcome high upfront costs — but deliver long-term returns that pay for systems over their lifetime
Est. median CapEx of HVAC
U.S. residential ($K/household)
Est. cost and benefit across
GHP lifetime (20 years) ($K/household)
Observations
All U.S. states:
ROI without tax credit: 3-4%
ROI with tax credit: 6-7%
Massachusetts specific:
ROI with tax credit and state rebates: 13-14%
Tax credits help break the biggest barrier – high upfront costs – making GHPs more accessible and financially viable.
Incentives are key to unlocking mass adoption and reaching DOE’s Liftoff goal of 7 million homes by 2035.
Finance
Chart: 
 | 4.4 | 16 | 20
 | 24.4
 | 15.6
15.6 (35%)
24.4 (55%)
4.4 (10%)
GHP (no incentives)
Gas Furnace + Central AC
Air-Source Heat Pump
Non-loop mechanical HVAC
Loop supplies, drilling, installation
Weatherization/ retrofit
44.4
~4 ton/household capacity assumption
Conventional alternatives
Key forecasts:
NREL projects that costs could decrease ~20-30% with expanded pilots, workforce training, thermal energy networks, and standardization.
GHP costs can decline with scale.
Key assumptions:
GHP installation capacity: 3 to 5 ton/household (urban to suburban).
Estimated annual energy savings with GHP installed: $1.5K-$2.5K/household.
Incentive is 30% federal ITC.
Chart: 
 | 44.4 | 31 | 16 | 16
 | 13.4 | 15
CapEx
Tax Credit Incentives
15.0
State Rebates
Net CapEx with Incentives
Chart: 
 | 35
 | 40
Benefits
Cumulative energy savings
Avoided costs (gas line replacement)
75
Federal
Massachusetts-specific

## Slide 16: Identifying key stakeholders is crucial to successful deployment of a geothermal heating & cooling project
Key deployment stages and stakeholder engagement map
Deployment
Planning
Design & Engineering
Permitting
Construction & Installation
Operations & Maintenance
Decommission
1
6
5
4
2
3
Stage | Key stakeholders | Key activities
 | Site owners/building operators | Provide site access and building data
 | Geologists and geothermal consultants | Conduct subsurface and thermal analysis, execute feasibility assessment
 | Local utilities | Assess infrastructure for integration
 | Community organizations | Facilitate local engagement and feedback
 | Project developers and investors | Initiate and fund planning
 | Local, state, and environmental regulators | Approve land use and drilling activities, ensure compliance
 | Legal advisors | Prepare and submit legal compliance documents
 | Engineers and HVAC designers | Design system layout and HVAC compatibility
 | Software modelers | Run thermal simulations to optimize performance
 | Building architects | Incorporate system into building design
 | Drilling contractors | Drill boreholes and install piping systems
 | Construction crew | Install mechanical and electrical infrastructure
 | Site safety and quality assurance officer | Ensure field safety and risk compliance
 | Facility managers and maintenance contractors | Oversee operation, handle routing servicing and repairs
 | Local authorities | Authorize decommissioning procedures
 | Restoration contractors | Restore landscaping and ecological balance
1
2
3
4
5
6
1
1
1
1
2
3
3
4
4
6

## Slide 17: The average permitting process in the U.S. takes 45 months on average and includes 14+ responsible agencies
Permitting process in the U.S.
3
Deployment: Permitting
Multilevel responsible agencies
Federal agencies | 
 | Bureau of Land Management (for federal lands)
 | Environmental Protection Agency
 | Federal Energy Regulatory Commission (for power)
 | Public utility commissions, if it involves district heating sales
State agencies | 
 | Department of Natural Resources
 | State water resource agencies
 | State environmental agencies
 | Department of Water Resources
 | Department of Environmental Conservation
Local agencies | 
 | County zoning offices
 | County drilling permits
 | Municipal water authorities
 | County building departments
 | Local utilities
Land Use
Land lease
Right of way
1-6 months
Exploration
Exploration permit/license
3-12 months
Drilling
Well drilling permit
2-6 months
Environmental
Environmental impact assessment
NEPA Review
6-36 months
Water Use
Water rights
Extraction permit
2-12 months
Construction
Building permit
Mechanical permit
1-3 months
Grid connection
Interconnection agreement
Grid access permit
3-9 months
Operation
Operational license
1-6 months
Decommission
Plan for decommission/ closure
3-12 months
15-75 months until construction completed
4-18 months including end of life
3-9 months
If hybrid power generation
Until end of life
Until construction completion

## Slide 18: Team

## Slide 19
Pia Doris Morrow
MS in Sustainability Management
Team Lead | Climate Knowledge Initiative Fellow
Zacharia Thurston
MS in Sustainability Management
Climate Knowledge Initiative Fellow
Faradisa Anintya
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Una Oljaca
BA in Economics, Political Sciences, and Government
Climate Knowledge Initiative Fellow
Leo Gordon
MPA, Columbia SIPA
Climate Knowledge Initiative Fellow
Hassan Riaz
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
CKI Geothermal Team
Fellows

## Slide 20
Hyae Ryung (Helen) Kim
PhD in Sustainable Development
Former Senior Research Fellow
CKI Team Staff, Faculty, and Alumna