## Slide 1: Geothermal Power
Gernot Wagner, Zacharia Thurston, Pia Doris Morrow, Sevgi Helin Tilkicioglu, Heather Hartel, Stephanie Chen, Shubhangi Prasad, Faradisa Anintya, Una Oljaca, Thomas Smith, Leo Gordon, Ariela Farchi Behar, Hyae Ryung Kim, and Isabel Hoyos
10 March 2026
Cite as: Wagner et al. “Geothermal Power,” Columbia Business School Climate Knowledge Initiative (10 March 2026).

## Slide 2: Geothermal Opportunity

## Slide 3
Nearly 80% of geothermal energy today is used for heating and cooling (42% heat pumps, 26% district heating systems), not electricity generation. Deployment is concentrated in 10 countries accounting for 90% of global use, with China alone representing 50% of all heating and cooling capacity.
Geothermal heating and cooling is a mature, proven technology that is projected to double by 2050 through residential and district heating expansion, with significant untapped potential for decarbonizing building thermal loads.
Geothermal electricity currently supplies less than 1% of global power, with conventional installations limited to ~16 GW in key geographic areas. Yet, geothermal energy reserves are multiples larger than all known oil and gas reserves, with the technical potential to meet global electricity demand 140 times over.
Global energy demand is projected to rise 10 to 20% by 2050, driven by growth in emerging economies, electrification, and AI data center expansion. This demand is creating urgent need for firm, reliable, round-the-clock clean power, a role geothermal is uniquely positioned to fill.
Next-generation technologies including horizontal drilling, enhanced geothermal systems, closed-loop systems, and AI-enabled exploration are expanding geothermal's reach to virtually every region around the globe, overcoming the geographic constraints that limit conventional geothermal today while reducing costs.
Technological, policy, and financial synergies with the oil and gas industry can dramatically reduce costs and accelerate deployment, particularly by applying advanced subsurface modeling to reduce exploratory drilling risk, the highest barrier in project development.
With continued innovation and cost declines, geothermal could become cost competitive with solar and wind plus storage by 2035 and meet up to 15% of global electricity demand growth by 2050, representing 800 GW of capacity and 6,000 TWh annually.
Geothermal electricity will play an outsized role in select markets, supplying 5 to 45% of power generation in countries like the U.S., Kenya, the Philippines, and Indonesia.
Executive Summary Opportunity

## Slide 4: Geothermal energy technologies span heating & cooling and power generation, with conventional approaches most widely deployed
Geothermal Opportunity
Key pathways for harnessing geothermal energy for heating & cooling and power generation
Conventional/hydrothermal
Underground thermal energy storage
Geothermal heat pumps
Direct-use heat
Borehole thermal energy storage
Aquifer thermal energy storage
Mine thermal energy storage
Advanced geothermal/ closed-loop systems
Enhanced geothermal systems
Next-generation technologies (commercialization <5 years)
Superhot rock
Frontier technologies (commercialization 5+ years)
Geopressured systems
Heating and cooling
Power
Production
Storage
Production
Storage
Cavern thermal energy storage
Pit thermal storage
Reservoir thermal storage
Magma-based geothermal
High-temperature geothermal energy storage
Geomechanical energy storage
Sources: Underground Thermal Energy Storage (Nature, 2012); Pathways to Commercial Liftoff: Geothermal Heating and Cooling (DOE, 2024); The Future of Geothermal Energy (IEA, 2024).
Credit: Sevgi Helin Tilkicioglu, Una Oljaca, Pia Doris Morrow, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al. "Geothermal Power," Columbia Business School Climate Knowledge Initiative (10 March 2026).

## Slide 5: Today, 10 countries consume 90% of global geothermal energy, with almost 80% of end use for heating and cooling
Heating: China is the most significant country, accounts for nearly 50% of global geothermal final energy consumption, dedicated entirely to space heating.
Electricity: The U.S., Indonesia, Türkiye, the Philippines, and New Zealand generate two-thirds of global geothermal electricity, with Iceland, Italy, Kenya, Mexico, and Japan contributing an additional 25%.
Total final geothermal energy consumption
by consuming countries, 2023
Total final geothermal energy consumption
by application, 2023
Opportunity: Heating & cooling
Chart: 
 | 620.8403 | 590 | 220 | 110 | 60 | 50 | 50 | 30 | 30 | 20 | 20
0
400
500
300
1.400
200
100
Global
U.S.
Turkiye
Sweden
Indonesia
Iceland
Japan
New Zealand
Germany
Philippines
Consumption (PJ)
China
0.2%
0.5%
1.0%
3.7%
2.5%
5.2%
30.0%
0.3%
18.8%
0.3%
14.6%
% of geothermal to total energy consumption, 2023
Chart: 
 | 100 | 58.13 | 32.06 | 24.95 | 21.79 | 21 | 21
 | 41.87 | 26.07 | 7.11 | 3.16 | 0.79
Total
42%
Geothermal heat pumps
26%
District heat
7%
Direct residential & comm.
3%
Agriculture & fishing
1%
Industry & other
Power (Electricity)
100%
21%
1,400 PJ
Heating & cooling (79%)

## Slide 6: By 2050, geothermal heating use is projected to almost double, driven largely by China and building and district heating
Geothermal heating use doubles in 2050 under a realistic government Stated Policies Scenario (STEPS), with China as the biggest source of growth. Yet, it remains only 0.5% of total heat consumption globally.
From the use-case perspective, nearly 90% of geothermal heating consumption comes from residential and commercial buildings, mainly through district heating networks, including thermal baths in the tourism and wellness sector.
Geothermal heating consumption (PJ), projection by region 2023-2050
Increase (%) by heating application globally, 2023-2050
Opportunity: Heating & cooling
Chart: 
 | 1106 | 600 | 160 | 135 | 145 | 35 | 31
 | 2000 | 1250 | 240 | 185 | 175 | 55 | 41
0
500
1.000
1.500
2.000
Global
China
U.S.
EU
Other Europe
Japan
RoW
2023
2050
Incl. Sweden, Germany, France
Incl. Türkiye, Iceland, Norway
2.0%
0.5%
0.5%
1.5%
0.2%
<0.1%
0.5%
xx%
% of geothermal to total heat consumption, by 2050
Chart: 
 | 101 | 12 | 6 | 6
 | 89 | 6
Total increase
89%
Res. & comm.
6%
Industry & other
Agriculture & fishing
6%

## Slide 7: Global geothermal heating and cooling capacity is ~173,300 MWth, with over 50% of global installed capacity in China
Observations
China holds over 50% of installed capacity, and the 10 largest consumers account for ~90% of the global total.
Europe is expected to scale as a result of the EU Green Deal.
Geothermal heat pumps account for 72% of installed capacity, while 28% is direct use.
Global geothermal potential up to 3 km and >90ºC is ~320 TW, while the potential for <90ºC increases 10x.
Global geothermal heating & cooling installed capacity, MWth
Opportunity: Heating & cooling
Largest installed capacity per capita (KWth) | 
Iceland | 7.177
Sweden | 0.69
Finland | 0.41
Switzerland | 0.27
Norway | 0.21

## Slide 8: GSHPs could reach millions of U.S. homes by 2050, enabled by tax incentives, business innovation, and workforce development
Total U.S. residential potential
(million homes equivalent)
Total U.S. commercial potential
(million homes equivalent)
Observations: Key drivers to successful liftoff
Policy and financial support: Tax incentives are often the single most impactful factor making commercial geothermal projects viable. The OBBA spared ground sourced heat pumps (GSHPs).
Workforce readiness: Availability of trained drillers and installers is a major bottleneck; national and regional training pipelines and certification programs are needed to expand this workforce.
Tech and deployment: Demonstration projects across diverse geographies and use cases (urban, rural, cold and hot climates) help de-risk investment and validate business models. Standardized designs, permitting, and interconnection protocols are needed to streamline and reduce soft costs.
Business model innovations: Utility-driven thermal energy networks (TENs utility-ownership) could provide a scalable and replicable model, especially as an alternative to gas infrastructure.
Opportunity: Heating & cooling
Chart: 
| 2020 | 2023 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
 | 25 | 25 | 28 | 32 | 36 | 41 | 46
 | 11 | 11 | 12 | 14 | 16 | 18 | 20
 | 1 | 1 | 2 | 3 | 4.5 | 6 | 8
 | 1 | 1 | 2.5 | 4.5 | 8 | 13 | 20
Chart: 
| 2020 | 2023 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
 | 18 | 18 | 20 | 23 | 26 | 29 | 32
 | 8 | 8 | 9 | 10 | 12 | 14 | 16
 | 0.5 | 0.5 | 1 | 1.5 | 2 | 3 | 4
 | 0.5 | 0.5 | 0.8 | 2 | 4 | 8 | 16
Liftoff
Liftoff
Economic potential
Market potential
Expected installation (baseline)
Liftoff trajectory

## Slide 9: Global energy demand expected to grow ~10-20% by 2050, largely driven by emerging economies, electrification, and data centers
India, ASEAN*, Africa, and the Middle East will be responsible for ~65-95% demand growth
New data centers and electrification of industry and buildings will drive ~5-10% demand growth
Observations
By 2050, global energy demand is expected to grow ~10 to 20%, with ~65 to 95% of that growth concentrated in emerging economies such as ASEAN, India, and the Middle East — regions that currently rely heavily on fossil fuels for baseload power.
New demand will likely stem from the electrification of industry and buildings, accounting for over half of demand. Data centers (2,500 to 4,500 TWh, or ~5 to 10% of demand), green hydrogen (179 Mtpa, driving ~20% annual power demand growth), and EVs (~10% annual growth, with BEVs dominating car sales) will add to this surge.
To meet such demand, economies will need reliable, non-intermittent baseload solutions for their energy grids.
Opportunity: Power
Chart: 
1990
2000
2010
2020
2030
2040
2050
Chart: 
 | 11.5 | 13 | 20
 | 11.5 | 13 | 20
 | 0.75 | 1 | 10
 | 0.75 | 2 | 6
 | 0.75 | 2 | 8
1
1
2023
1
2
2
2030
2050
27
31
64
+3.5%/ year
Industry
Buildings
H2 and Synfuels
Data Centers
Transport
Global power consumption by sector (thousands of TWh)
Global primary energy demand (million TJ)
India
ASEAN
Africa
Middle East
Rest of World
Latin America
China
North America
OCED Europe
OECD Asia Pacific
~10-20%
Growth

## Slide 10: With vast untapped thermal resources and emerging technological advancements, geothermal power is primed for a breakout decade
Potential of proven oil & gas reserves vs. 1% geothermal resources*, trillion MWh
Projected global geothermal under different scenarios, GW
Historical installed geothermal capacity by country, GW
Opportunity: Power
Chart: 
 | 2793 | 2216 | 2252 | 2133 | 2152 | 2285 | 2274 | 2214 | 2229 | 2382 | 2405 | 2409 | 2592 | 2607 | 2514 | 2542 | 2517 | 2483.3 | 2444.3 | 2555.4 | 2571.9 | 2596.7 | 2648.6 | 2695.8 | 2725
 | 525 | 785 | 785 | 805 | 820 | 850 | 850 | 980 | 1052 | 1189 | 1189 | 1226 | 1336 | 1343.5 | 1403.5 | 1438.3 | 1533.3 | 1808.3 | 1948.3 | 2130.7 | 2130.7 | 2286.05 | 2360.33 | 2597.51 | 2638.8
 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1916.1 | 1916.1 | 1916.1 | 1916.1 | 1928.1 | 1928.1 | 1928.1 | 1928.1 | 1932 | 1951.8 | 1951.8
 | 18 | 18 | 18 | 15 | 15 | 15 | 23 | 23 | 30 | 77 | 94 | 114 | 162 | 311 | 405 | 624 | 821 | 1063.7 | 1282.518 | 1514.688 | 1613.188 | 1676.17 | 1691.338 | 1691.338 | 1734.338
 | 418 | 417 | 372 | 382 | 382 | 437 | 437 | 456 | 578 | 617 | 742 | 742 | 768 | 840 | 966 | 990 | 985 | 985 | 1009 | 1009 | 1043 | 1043 | 1050 | 1050 | 1275.4
 | 843 | 843 | 853 | 953 | 953 | 953 | 953 | 958 | 958 | 958 | 883 | 808 | 833 | 858 | 868 | 898 | 923.5 | 948.5 | 948.5 | 973.5 | 973.5 | 998.5 | 998.5 | 998.5 | 998.5
 | 58 | 58 | 58 | 58 | 128 | 128 | 128 | 128 | 128 | 163 | 198 | 198 | 205.5 | 205.5 | 366.1 | 618.9 | 652.9 | 672.9 | 683.8 | 683.8 | 863.13 | 863.13 | 949.73 | 984.73 | 939.73
 | 172 | 202 | 202 | 202 | 202 | 232 | 422 | 485 | 575 | 575 | 575 | 665 | 665 | 665 | 665 | 665 | 665 | 709.958 | 755.558 | 755.558 | 756.158 | 756.208 | 757.58 | 787.58 | 787.58
 | 590 | 573 | 666 | 707 | 642 | 671 | 671 | 671 | 671 | 695 | 728 | 728 | 728 | 729 | 768 | 768 | 767 | 767.19 | 767.19 | 767.19 | 771.79 | 771.79 | 771.79 | 771.79 | 771.79
 | 533 | 533 | 533 | 535 | 535 | 535 | 532 | 532 | 532 | 535 | 537 | 537 | 512 | 512 | 508 | 516 | 526 | 471.366 | 473.115 | 480.714 | 487.004 | 486.814 | 436.814 | 456.054 | 489.054
 | 144.71 | 144.71 | 144.71 | 162.71 | 165.71 | 165.711 | 165.711 | 165.711 | 165.711 | 165.711 | 165.711 | 217.461 | 217.461 | 217.461 | 217.461 | 217.361 | 206.86 | 206.86 | 206.86 | 261.86 | 261.86 | 258.84 | 262.66 | 262.66 | 262.66
 | 332 | 377.5417 | 423.0833 | 468.625 | 514.1667 | 559.7083 | 605.25 | 650.7917 | 696.3333 | 741.875 | 787.4167 | 832.9583 | 878.5 | 924.0417 | 969.5833 | 1015.125 | 1060.6667 | 1106.2083 | 1151.75 | 1197.2917 | 1242.8333 | 1288.375 | 1333.9167 | 1379.4583 | 1425
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
16
2
2012
2004
2016
2020
2024
United States
Indonesia
Philippines
Turkey
New Zealand
Mexico
Kenya
Iceland
Italy
Japan
Costa Rica
2000
Rest of World
2008
Chart: 
 | 2.55
 | 0
 | 1257
2.55
Proven fossil reserves
1% geothermal resources
Chart: 
 | 2.55
2.55
500x
potential energy
(all geothermal resources)
Chart: 
| 2010 | 2022 | 2023 | 2030 | 2035 | 2040 | 2050
 | 10000 | 15000 | 14850 | 22000 | 31000 | 40000 | 56000
 | 14850 | 25810 | 39630 | 52860 | 83340
 | 14850 | 29000 | 44250 | 59500 | 90000
 | 14850 | 38660 | 61080 | 79630 | 111120
0
10
20
30
40
50
60
70
80
90
100
110
120
Chart: 
 | 2405 | 2409 | 2592 | 2607 | 2514 | 2542 | 2517 | 2483.3 | 2444.3 | 2555.4 | 2571.9 | 2596.7 | 2648.6 | 2695.8 | 2725
 | 1189 | 1226 | 1336 | 1343.5 | 1403.5 | 1438.3 | 1533.3 | 1808.3 | 1948.3 | 2130.7 | 2130.7 | 2286.05 | 2360.33 | 2597.51 | 2638.8
 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1916.1 | 1916.1 | 1916.1 | 1916.1 | 1928.1 | 1928.1 | 1928.1 | 1928.1 | 1932 | 1951.8 | 1951.8
 | 94 | 114 | 162 | 311 | 405 | 624 | 821 | 1063.7 | 1282.518 | 1514.688 | 1613.188 | 1676.17 | 1691.338 | 1691.338 | 1734.338
 | 742 | 742 | 768 | 840 | 966 | 990 | 985 | 985 | 1009 | 1009 | 1043 | 1043 | 1050 | 1050 | 1275.4
 | 883 | 808 | 833 | 858 | 868 | 898 | 923.5 | 948.5 | 948.5 | 973.5 | 973.5 | 998.5 | 998.5 | 998.5 | 998.5
 | 198 | 198 | 205.5 | 205.5 | 366.1 | 618.9 | 652.9 | 672.9 | 683.8 | 683.8 | 863.13 | 863.13 | 949.73 | 984.73 | 939.73
 | 575 | 665 | 665 | 665 | 665 | 665 | 665 | 709.958 | 755.558 | 755.558 | 756.158 | 756.208 | 757.58 | 787.58 | 787.58
 | 728 | 728 | 728 | 729 | 768 | 768 | 767 | 767.19 | 767.19 | 767.19 | 771.79 | 771.79 | 771.79 | 771.79 | 771.79
 | 537 | 537 | 512 | 512 | 508 | 516 | 526 | 471.366 | 473.115 | 480.714 | 487.004 | 486.814 | 436.814 | 456.054 | 489.054
 | 165.711 | 217.461 | 217.461 | 217.461 | 217.461 | 217.361 | 206.86 | 206.86 | 206.86 | 261.86 | 261.86 | 258.84 | 262.66 | 262.66 | 262.66
3.5x by 2050 (56 GW)
5.2x by 2050 (83 GW)
5.6x by 2050 (90 GW)
Stated Policies
Announced Pledges
DOE Liftoff
Net Zero Emissions
In 2025, 32 countries had geothermal power, for a total of ~16 GW global capacity, from 3,700 production wells with an average 3 MWh capacity per well.
6.9x by 2050 (111 GW)

## Slide 11: Conventional geothermal power installations have reached ~16 GW but remain constrained to key geographic areas
Observations
The U.S., Indonesia, the Philippines, Mexico, Türkiye, New Zealand, Japan, Kenya, Iceland, and Italy lead in installed geothermal capacity.
Conventional geothermal relies on rare hydrothermal reservoirs—where heat, water, and permeable rock naturally align near tectonic boundaries like the Pacific Ring of Fire.
As a result, geothermal generation is concentrated in volcanically active regions. Most other nations face steep costs and technical barriers.
Conventional resources are too limited to assist in meeting global energy demand
Enhanced and closed-loop geothermal systems aim to overcome geographic limits, unlock deeper heat sources, and deliver 24/7 renewable power worldwide.
Geologically active areas show geothermal potential beyond countries with installed capacity
Opportunity: Power

## Slide 12: Next-generation technologies enable deeper drilling to unlock greater power potential
Heat reservoir formation process and access
The ability to drill deeper is key to accessing more power*
Opportunity: Power
1 km
2 km
3 km
4 km
5 km
6 km
7 km
8 km
Rainfall flows from higher elevations into the ground.
Water is heated by surrounding rock.
Water travels through faults and fractures.
Permeable rock traps and stores rising hot water or steam.
Geothermal reservoir is formed.
1
2
3
4
5
1
2
3
4
5
Next-generation
Hydrothermal
Depth (km)
Tech type | Depth & temp. (ranges depending on location) | Power potential
Hydrothermal | ~1-3 km, 90-370℃ (some may exceed) | 
Next-generation | ~5-7.5 km, 120-370℃ | 
Superhot rock | ~7.5+ km, +400℃ | 

## Slide 13: Next-generation drilling unlocks globalized clean energy access, with notable overlap in emerging economies by 2050
Global EGS hotspots concentrated in emerging economies
Potential for next-gen geothermal power capacity by region, GW (IEA projections)
Opportunity: Power
Chart: 
 | 0.05856 | 2.928 | 58.56 | 146.4 | 240 | 300
 | 0.03904 | 1.952 | 39.04 | 97.6 | 160 | 200
 | 0.01952 | 0.976 | 19.52 | 48.8 | 80 | 100
 | 0.015616 | 0.7808 | 15.616 | 39.04 | 64 | 80
 | 0.00976 | 0.488 | 9.76 | 24.4 | 40 | 50
 | 0.01952 | 0.976 | 19.52 | 48.8 | 80 | 100
500
600
400
700
300
800
200
900
100
0
2025
2030
2035
2040
2045
2050
0.1625
8
162
405
664
830
China
United States
India
Southeast Asia
Europe
Rest of the world
5-7.5 km
7.5-10 km
10-12.5 km
12.5+ km
Estimate
United States: 3,400 GW
China: 300 GW
India: 80 GW
Southeast Asia: 64 GW
Europe: 50 GW
Project InnerSpace
IEA
Global next-gen geothermal projections vary. Project InnerSpace’s projections likely reflect greater accuracy of global geothermal potential, driven by superior subsurface data collection. IEA estimates are deliberately conservative, focusing on what is deployable under today’s policy, cost, and financing conditions.
United States: 200 GW

## Slide 14: Geothermal power offers clean baseload capacity to replace retiring coal plants and prevent overreliance on peaker plants
Loss of baseload power leads to overreliance on peaker plants and can drive up costs for consumers
Heavy dependence on intermittent renewables without baseload capacity threatens grid reliability
Opportunity: Power
Fossil energy will plateau despite energy demand increasing.
Grids that are overreliant on wind and solar (intermittent energy) without baseload capacity risk rolling blackouts during periods of low renewable generation.
Cost of generation ($)
Hourly net load (year average) in California
Global final energy consumption for Continued Momentum scenario, by fuel, millions of terajoules
What is baseload?
28,000
26,000
24,000
22,000
20,000
18,000
16,000
14,000
12,000
10,000
0
12am
3am
6am
9am
12am
3pm
6pm
9pm
2020
2018
2019
2017
2016
2015
2014
2013
2012
Increased ramp
Potential overgeneration
Megawatts
Baseload
Mid-load
Peak load
Coal
N. gas
Nuclear
The most common sources of baseload power, chosen for their low LCOE. Gas can be used but has higher OpEx.
Baseload power is the minimum amount of electricity the electrical grid needs at any given time. Runs continuously at a steady output.
Chart: 
 | 24.5 | 25 | 40 | 24.5 | 24.5 | 24.5 | 24.5
 | 100 | 115 | 125 | 120 | 140 | 125 | 105
 | 45 | 77.5 | 110 | 90 | 120 | 110 | 98
 | 35 | 40 | 45 | 37 | 31 | 25 | 21
 | 2 | 8 | 10 | 12 | 16 | 18 | 21
 | 35 | 37.5 | 40 | 50 | 100 | 120 | 150
 | 10 | 11.8333 | 13.6667 | 15.5 | 17.3333 | 19.1667 | 21
1990
2000
2010
2020
2030
2040
2050
Other
Electricty
Hydrogen
Bioenergy
Natural gas
Oil
Coal

## Slide 15: Key barriers limiting geothermal deployment include exploration risks, drilling technology limits, and heat flow variability
Barriers to geothermal achieving global, dispatchable, and cost-competitive clean power
Opportunity: Power
Barrier | Description | Impact on Deployment | Emerging Solutions
Exploration Risk & Cost | High upfront cost for resource identification; drilling success uncertain | Major cost bottleneck; limits financing | AI/geophysical modeling, remote sensing, cheaper slim-hole drilling
Drilling Technology Limits | Conventional rigs struggle with deep/hard rock, high heat, and corrosive fluids | Limits depth/temperature access → limits energy yield | Advanced drilling (plasma, millimeter wave, laser), O&G transfer tech
Reservoir Stimulation & Permeability | Creating or maintaining fluid pathways in hot dry rock is challenging | Determines long-term productivity; EGS sites often fail after testing | Hydraulic shearing, closed-loop systems, supercritical fluid modeling
Materials & Corrosion Resistance | Equipment degradation in harsh conditions (heat, pressure, minerals) | Raises O&M costs and reduces lifetime of wells | High-temp alloys, ceramics, coatings
Power Conversion Efficiency | Efficiency drops at lower temperatures; limited by thermodynamic cycles | Restricts viable sites; reduces energy output | Supercritical CO₂ cycles, binary cycle optimization
Monitoring & Reservoir Management | Hard to track subsurface dynamics and avoid induced seismicity | Safety/regulatory constraints; performance loss over time | Fiber-optic sensing, real-time data analytics, seismic monitoring
Transmission & Integration | Geothermal sites often remote; grid connection costs high | Slows scalability and investment interest | Colocation with industrial heat users, modular systems
Public & Regulatory Challenges | Concerns about seismicity, permitting delays | Adds time and uncertainty to projects | Streamlined EGS permitting frameworks
Major Barriers

## Slide 16: Exploratory drilling carries the highest project development risk, which can be reduced through advanced subsurface modeling
High drilling costs and geological uncertainty make exploration the riskiest phase of geothermal development
Inaccurate subsurface modeling can mischaracterize resources, resulting in failed wells and losses exceeding $10M per site
Geothermal Opportunity
AI-enabled companies are helping de-risk exploration by providing solutions for accurate subsurface reconnaissance and drilling
Cumulative Cost
Years 1-2
Years 2-3
Years 4-6
Years 6-8
Years 8+
Stage
Risk Level
Surface Reconnaissance $1M-2M
Exploratory Drilling
$20M-$30M
Production Drilling
$20M-$120M
SAGS Power Plant
$20M-$200M
Operations and Maintenance
Upstream Resource Development
Downstream Plant Construction and Operations
100%
50%
0%
Time
Subsurface temperature, permeability, and fluids can be confirmed only through drilling; surface surveys and models provide limited accuracy, making exploratory wells costly and high risk.
Inaccurate measurements of reservoir pressure can reduce recoverable power; length of estimated drilling time may ward off willingness for upfront investment in exploratory stages.
Geothermal project finance has initial high risk: Tens of millions of dollars are spent upfront on drilling with no guarantee of a viable resource. This uncertainty makes traditional financing challenging, often requiring government support, insurance, or hybrid financing to secure bankability.
Applied AI geosensing to discover new reservoirs around the underperforming Lightning Dock geothermal facility, which now ranks among the most productive in the U.S.
Focus
Resource Risk
Operational Risk

## Slide 17: Technological, policy, and financial synergies with the oil & gas industry can drive down geothermal costs and scale deployment
Geothermal Opportunity
Technological synergies
Policy priorities
Cost trends for successful synergy
Chart: 
 | 5 | 8 | 5 | 4 | 6 | 8
 | 5 | 8 | 4 | 6 | 8 | 4
5
4
6
3
7
2
8
1
0
Geoscience
Well production
Formation evaluation
Drilling competencies
Surface production
Reservoir engineering
Oil & gas engineer
Geothermal engineer
Geothermal and O&G engineering skillset overlap*
Competency level
Subsurface exploration and drilling
Oil and gas data on hydrocarbon reserves and well logs can cut geothermal exploration costs and improve success rates.
Well completion and management
Simulation and zonal isolation techniques from O&G enhance reservoir longevity and reinjection efficiency.
Data and digital innovation
O&G’s digital twins and real-time monitoring tools improve geothermal reservoir modeling and predictive maintenance.
Countries leading the workforce transition
Chart: 
 | 12 | 37 | 11 | 40
12%
37%
11%
40%
Evaluation, planning, management
Non-transferrable expertise
Surface facilities
Drilling & completion
Chart: 
 | 12 | 24 | 7 | 57
12%
24%
7%
57%
Chart: 
 | 6 | 18 | 11 | 65
6%
18%
11%
65%
Share of geothermal technology investments that overlap with the O&G industry
Conventional
EGS
AGS
~10%
~20-30%
~30%
Cross-sector skill transfer can unlock faster workforce deployment and lower technical risk.
U.S.: DOE GeoVision + GEODE Consortium
Iceland: Integrated geothermal-O&G training pipeline
Türkiye: EGS demonstration from hydrocarbon basins
R&D and learning-by-doing acceleration
Reduction in exploration risk and resources mapping
Drilling and completion efficiency gains via O&G rigs and methods
Enhanced geothermal systems (EGS) exhibit the highest transferable expertise (~70%), while advanced geothermal systems (AGS) retains greater reliance on O&G drilling and surface integration.
3

## Slide 18: Underground thermal energy storage offers greater capacity potential than battery alternatives and natural gas
Geothermal Opportunity
Natural Gas
Solid Batteries
Minutes
Hours
Days
Weeks
Months
Years
Typical Energy Storage Capacity
10 BTU
10^4 BTU
10^7 BTU
10^10 BTU
10^13 BTU
Wh
KWh
MWh
GWh
TWh
Super-Capacitor
Fly Wheel
Gravity
Flow Battery
Hydrogen
Ramped Hydroelectric
Compressed Air
Underground thermal energy storage (UTES)
Geologic storage method
Non-geologic storage method
UTES
Supply Cold
Store Excess Cold
Integrated Cooling Loop
Cold Underground UTES
Electrical Cooling Load
Winter
Winter
Summer
With Cold UTES
Standard
Supply Heat
Store Excess Heat
Integrated Heating Loop
Hot Underground UTES
Produce Power
Electrical Heating Load
Summer
Summer
Winter
With Hot UTES
Standard
Both systems can coexist regardless of season due to the earth’s insulating properties, but storage of excess heat and cold will be more likely during the summer and winter, respectively (i.e., lakes in the summer vs. winter).

## Slide 19: Geothermal Power Technology

## Slide 20
Traditional hydrothermal geothermal taps naturally occurring hot water and steam reservoirs near the surface. These mature systems provide reliable, low-cost baseload power but are geographically limited to areas with accessible heat and permeability.
Petrothermal (enhanced or engineered geothermal systems) use advanced drilling and stimulation to access dry, hot rock at greater depths, creating artificial reservoirs where none existed. This breakthrough could unlock geothermal potential worldwide, independent of surface resource availability, making geothermal energy a truly global rather than niche solution.
At extreme depths and temperatures (>400°C), superhot rock systems could generate 5 to 10 times more energy per well than conventional geothermal. These projects promise ultraefficient, zero-emission power, though they remain in early demonstration phases.
Modern drilling techniques — some borrowed from the oil and gas industry — include directional drilling, hydraulic fracturing, and plasma or millimeter-wave drilling. These techniques are driving cost reductions and deeper resource access, expanding geothermal’s viable footprint.
Geothermal brines are rich in critical minerals such as lithium, manganese, and zinc, enabling co-production of clean energy and essential materials for batteries and energy storage. This overlap strengthens geothermal’s strategic value across the energy transition supply chain.
Artificial intelligence and machine learning are transforming exploration by analyzing geophysical data, seismic imaging, and well logs to identify optimal drilling zones, predict subsurface conditions, and reduce exploration risk and cost.
Nuclear and geothermal are the only scalable, zero-carbon baseload technologies capable of providing continuous power independent of weather, season, or geography. Nuclear fusion innovation has found cross-sector use cases in drilling applications aiming to induce capabilities to melt granite and basalt.
Key messages
Technology

## Slide 21: Conventional hydrothermal systems tap natural reservoirs; next-generation technologies reach broader heat resources
Technology
The three most important criteria to generate geothermal power are heat, fluid requirement, and permeability
Heat (varies by depth)
Fluid
Permeability
Conventional/ hydrothermal
Next-generation/ frontier technologies
0.1-4.5 km
2-10 km
Required
Required
>200°C
85-180°C+
Can be injected or circulated in closed loop
Created via stimulation or closed loop
Key pathways for harnessing geothermal for power
Conventional/hydrothermal
Advanced geothermal/ closed-loop systems
Enhanced geothermal systems
Next-generation technologies
Superhot rock
Frontier technologies
Geopressured systems
Generation
Storage
Magma-based geothermal
High-temperature geothermal energy storage
Geomechanical energy storage
Detailed next

## Slide 22: Next-generation geothermal technologies advance scalability, while conventional geothermal remains the most cost effective
Technology
 | Conventional (Hydrothermal) | Next-Generation |  | Frontier
 | Dry Steam, Flash Steam, Binary Cycle | Enhanced Geothermal Systems (EGS) | Closed-Loop Geothermal Systems (CLGS) | Superhot Rock Geothermal
Description | Naturally occurring geothermal reservoirs are accessed, with hot water circulating in permeable rock. Open fluid circulation through the system. | Engineered reservoirs are created via hydraulic, chemical, or thermal stimulation of rock to increase permeability and enable open fluid circulation. | Hot rock is accessed via wellbores in a closed-circuit system. Working fluid is used to extract heat via conductive heat transfer. | Superhot rock resources (>400°C) at great depth are accessed. Water is circulated through natural or engineered fractures to produce supercritical fluid for power generation.
Advantages | Well-developed, niche technology for power generation and heating & cooling. | Synergies with oil & gas technology have improved flow rates and flow consistency; greater geographic reach. | Minimal environmental impact, lowest water use, potential for use in unproductive conventional geothermal wells and abandoned oil & gas wells. | Highest energy density among geothermal technologies; location independent.
Barriers | Geographical constraints, geological uncertainty regarding reservoir productivity. | Concerns over induced seismicity, water use, and water contamination. | Engineering challenges including maintaining heat flow rates and reducing drilling costs. | Requires long development time and high cost; extreme drilling challenges and equipment limitations.
Depth | 50-300 meters | 2,000-4,000 meters | Typically, below 5,000 meters | 5,000-15,000
Location Suitability | Extraction limited by natural reservoir dependence. | Flexible siting | Flexible siting | Flexible siting
Scalability | Limited due to geographic constraints. | Highest commercial readiness among next-generation geothermal technologies. | Dependent on technological advancements and cost reduction. | Lowest technological readiness.
Cost | New plants commissioned in 2021 demonstrated an LCOE of $0.068 per kWh. | Current cost ~$0.225 per kWh; U.S. DOE target for LCOE of $0.045 per MWh by 2035. | Current cost ~$0.293 per kWh, with potential cost reductions to $0.08 to $0.09 per MWh by 2035. | Not commercial yet (not producing power, in research phase).

## Slide 23: Next-generation geothermal technologies are reaching the brink of commercialization, presenting an opportunity for strategic investment
Technology
Opportunity for next-gen strategic investment
Bench scale
Lab work
Pilot scale
Commercially scaled
Deployed
Capital requirement x technology risk
High-Temp Alloys & Nano Drilling
AI-enabled exploration
Critical Mineral Recovery
EGS
Super Critical Conditions
Closed-loop
Technology | Funding | Key Barriers
Super-Critical Conditions | $82M+ – NZ Regional Infrastructure Fund | Extreme T/P drilling; material durability; limited demos; high CapEx.
High-Temp Alloys and Nano Drilling | $4M+ – DOE FOAs, VC pilots (e.g., Hephae $4M) | Costly R&D/testing; limited alloy supply chain; expensive field trials.
Critical Mineral Recovery | $1.63B+ – CA geothermal lithium (e.g., ATLiS) | Scale-up challenges; brine management; permitting; price volatility.
AI-Enabled Exploration | $200M-$1.2B+ – VC, corporate, grants (Zanskar ~$40M; Microsoft & G42 $1B) | Sparse data; limited field validation; physics-ML integration; regulatory trust.
EGS Closed-Loop | $900M+ private (5 years); DOE: $165M (2022), $44M (FORGE 2023); $14.2M (2024), $60M (2024) | EGS: Seismicity; stimulation efficiency; well integrity; financing. Closed-loop: Technology validation; sustained heat output; drilling cost; permitting.
Geothermal Heating/Cooling
Binary, Combined, Flash Steam, Dry Steam
Innovation in geothermal power is scaling quickly, attracting a large volume of diverse investments
*Graph is illustrative, reflecting general trends

## Slide 24: Conventional geothermal capacity has nearly doubled since 2000, reaching ~15 GW; growth has slowed in the past five years
Observations
Nearly all commercial geothermal power plants today are hydrothermal.
Hydrothermal systems are mature and commercially proven, but they are location constrained, typically requiring shallow, naturally occurring reservoirs near tectonic plate boundaries.
Conventional hydrothermal capacity grew rapidly between 2015 and 2020, but expansion has slowed in recent years, potentially due to these geographic limitations.
Countries like Indonesia, Türkiye, and Kenya have recorded the fastest growth because they still possess large untapped resources. However, early leaders such as the United States and the Philippines have seen slower expansion in recent years as their most accessible fields are already developed.
Global geothermal power installed capacity by country, GW
Conventional power generation
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
 | 2793 | 2216 | 2252 | 2133 | 2152 | 2285 | 2274 | 2214 | 2229 | 2382 | 2405 | 2409 | 2592 | 2607 | 2514 | 2542 | 2517 | 2483.3 | 2444.3 | 2555.4 | 2571.9 | 2596.7 | 2648.6 | 2695.8 | 2725
 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1916.1 | 1916.1 | 1916.1 | 1916.1 | 1928.1 | 1928.1 | 1928.1 | 1928.1 | 1932 | 1951.8 | 1951.8
 | 525 | 785 | 785 | 805 | 820 | 850 | 850 | 980 | 1052 | 1189 | 1189 | 1226 | 1336 | 1343.5 | 1403.5 | 1438.3 | 1533.3 | 1808.3 | 1948.3 | 2130.7 | 2130.7 | 2286.05 | 2360.33 | 2597.51 | 2638.8
 | 843 | 843 | 853 | 953 | 953 | 953 | 953 | 958 | 958 | 958 | 883 | 808 | 833 | 858 | 868 | 898 | 923.5 | 948.5 | 948.5 | 973.5 | 973.5 | 998.5 | 998.5 | 998.5 | 998.5
 | 418 | 417 | 372 | 382 | 382 | 437 | 437 | 456 | 578 | 617 | 742 | 742 | 768 | 840 | 966 | 990 | 985 | 985 | 1009 | 1009 | 1043 | 1043 | 1050 | 1050 | 1275.4
 | 590 | 573 | 666 | 707 | 642 | 671 | 671 | 671 | 671 | 695 | 728 | 728 | 728 | 729 | 768 | 768 | 767 | 767.19 | 767.19 | 767.19 | 771.79 | 771.79 | 771.79 | 771.79 | 771.79
 | 18 | 18 | 18 | 15 | 15 | 15 | 23 | 23 | 30 | 77 | 94 | 114 | 162 | 311 | 405 | 624 | 821 | 1063.7 | 1282.518 | 1514.688 | 1613.188 | 1676.17 | 1691.338 | 1691.338 | 1734.338
 | 172 | 202 | 202 | 202 | 202 | 232 | 422 | 485 | 575 | 575 | 575 | 665 | 665 | 665 | 665 | 665 | 665 | 709.958 | 755.558 | 755.558 | 756.158 | 756.208 | 757.58 | 787.58 | 787.58
 | 533 | 533 | 533 | 535 | 535 | 535 | 532 | 532 | 532 | 535 | 537 | 537 | 512 | 512 | 508 | 516 | 526 | 471.366 | 473.115 | 480.714 | 487.004 | 486.814 | 436.814 | 456.054 | 489.054
 | 58 | 58 | 58 | 58 | 128 | 128 | 128 | 128 | 128 | 163 | 198 | 198 | 205.5 | 205.5 | 366.1 | 618.9 | 652.9 | 672.9 | 683.8 | 683.8 | 863.13 | 863.13 | 949.73 | 984.73 | 939.73
 | 476 | 469 | 527.5 | 551.4 | 533.1 | 603.116 | 622.016 | 719.036 | 719.316 | 716.716 | 717.016 | 784.766 | 869.366 | 868.666 | 864.716 | 867.166 | 862.574 | 927.665 | 956.095 | 1025.105 | 1026.305 | 1044.52 | 1098.959 | 1106.419 | 1099.619
0.0
0.6
0.8
1.0
1.2
1.4
1.6
1.8
2.0
2.2
2.4
2.6
2.8
0.2
0.4
Indonesia
Italy
New Zealand
Turkey
Iceland
Japan
Mexico
Kenya
Other
United States
Philippines
-0.2
+2.7
+2.5
+3.1
+1.7
World
xx
5-year % change

## Slide 25: Conventional geothermal energy can utilize all three power plant design methods, each suited to different temperature ranges
Global capacity, %
LCOE, $US/MWh (Conservative estimate, 2030)
TBU
~56
~84
Efficiency, %
20-30
25-35
10-20
30-40
Temperature range, °C
180+
150-200
85-170
180-220
Advantages/ disadvantages
Proven and mature technology
Lower plant complexity
Rare resource availability
Resource depletion risk
Potential emissions
Most common technology
High efficiency
High temperature requirement
Mineral scaling and corrosion
Water management challenges
Lower temperature requirement
Closed secondary loop
Lower efficiency
Higher CapEx and OpEx
Secondary fluid risks
23%
14%
Hydrothermal (conventional)
Dry steam power plants
A
Flash steam power plants
B
Binary cycle power plants
C
19%
Double flash
42%
Single flash
Conventional power generation

## Slide 26: Deep-dive on technology: Direct dry steam (1/3)
Conventional power generation
A
Process
Advantages
Disadvantages
Hot steam is directly drawn from geothermal reservoirs, and unlike flash or binary plants, steam is used as it is, without converting hot water first.
The steam flows into the turbine, and as the turbine spins, it drives the generator to produce electricity.
The condensed water is pumped down through the reinjection well, which returns the water to the underground reservoir to sustain the geothermal cycle.
After passing through the turbine, the lower-energy steam is cooled in a condenser and condenses back into water.
Generator
Turbine
Condenser
Wellhead
Wellhead
Ground surface
Subsurface injection
Proven and mature technology – first geothermal plants (e.g., the Geysers, California) use dry steam
Lower plant complexity – simpler design compared to flash or binary cycle plants
Rare resource availability – requires underground reservoirs of naturally occurring steam
Resource depletion risk – steam fields may decline in pressure and output over time
Potential emissions – some non-condensable gases (CO2, H2S) released with steam
Geothermal steam
Geothermal water

## Slide 27: Deep-dive on technology: Single/double flash cycle (2/3)
Conventional power generation
B
Very hot geothermal fluid is pumped up from deep underground, and unlike dry steam, it is mostly pressurized hot water (>180°C).
The fluid enters a separator and, as the pressure drops, part of the hot water flashes (vaporizes) instantly into steam; the remaining stays as water.
The steam flows into the turbine, and as the turbine spins, it drives the generator to produce electricity.
Generator
Turbine
Condenser
Wellhead
Wellhead
Ground surface
Subsurface injection
Separator
After passing through the turbine, the lower-energy steam is cooled in a condenser and condensed back into water.
The condensed water is pumped down through the reinjection well, which returns the water to the underground reservoir to sustain the geothermal cycle.
Advantages
Disadvantages
Most common geothermal technology – proven at commercial scale worldwide
Higher resource availability – can use hot water reservoirs, which are more common than dry steam
High efficiency – suitable for high-temperature reservoirs (>180°C)
Requires very hot resources – limited to areas with high-temperature reservoirs
Mineral scaling and corrosion – dissolved minerals in hot water can clog or damage equipment
Water management challenges – large volumes of brine need proper reinjection
Process
Geothermal steam
Geothermal water

## Slide 28: Deep-dive on technology: Binary cycle (3/3)
Conventional power generation
C
Moderately hot geothermal fluid (usually 100-180°C) is pumped from the underground reservoir.
The geothermal fluid enters a heat exchanger. It transfers heat to a secondary working fluid with a much lower boiling point (often an organic fluid like isobutane or pentane).
The secondary fluid absorbs the heat and vaporizes. The vapor drives the turbine, which spins the generator to produce electricity.
After passing through the turbine, the secondary vapor is cooled in the condenser and returns to liquid form.
The cooled geothermal fluid is returned to the reservoir through a reinjection well.
Advantages
Disadvantages
Process
Turbine
Generator
Wellhead
Wellhead
Ground surface
Subsurface injection
Heat exchanger
Condenser
Pump
Can use lower-temperature (100-180°C) resources – much more widely available
Closed secondary loop – no gases or steam released to atmosphere (very low emissions)
Lower efficiency – compared to flash and dry steam (extra heat exchange step)
Higher CapEx and OpEx – requires pumps, heat exchangers, and secondary working fluids
Secondary fluid risks – organic fluids can be flammable or toxic if leaked
Geothermal steam
Geothermal water
Working fluid (vapor)
Working fluid (liquid)

## Slide 29: Location dependence is main barrier for conventional geothermal deployment, followed by high upfront costs and low efficiency
Conventional power generation
Barriers to adoption
Chart: 
 | 44.4 | 38.6 | 32.7 | 32.2 | 30.4 | 10
 | 30
Natural gas
.Fossil fuel average
Nuclear
Coal
Oil
Hydrothermal
40
Location dependent
Due to the requirements for heat, fluid, and permeability, hydrothermal resource cluster in specific locations, especially along tectonic and volcanic belts.
For example, in the United States, hydrothermal resources are concentrated in the West, particularly in states such as Alaska, Arizona, California, Colorado, Hawaii, Idaho, Montana, Nevada, New Mexico, Oregon, Utah, Washington, and Wyoming.
Thermal power plant efficiency in the United States, %, 2023
Low efficiency considering heat content
Constraint
Example
High initial investment and cost variance
2.1
High initial investment
2.2
Exploration risks and cost variance
Drilling costs comprise some 35 to 40% of the total capital costs of a geothermal project. Thus, drilling hazards such as loss circulation can cause very high variance. For example, the circulation loss costs in the U.S. in geothermal drilling operations is approximately 10% of overall well costs and 20% for exploration wells.
Conventional geothermal, compared with wind and solar, typically requires high upfront capital, has longer payback periods, and is less modular.
Roughly 80% of its LCOE comes from CapEx and ~20% from fixed O&M.
Variation based on tech type

## Slide 30: Kızıldere is the largest geothermal power plant in Türkiye, accounting for ~15% of the country’s total geothermal power production
Case study: Kızıldere
Kızıldere I, built in 1984, was the first conventional geothermal power plant in Türkiye; Kızıldere III was completed in 2018.
It is located in Denizli, Türkiye, a region known for tectonic activity caused by an active continental rift zone and for the hot springs in Pamukkale.
The reservoir temperature is approximately 246°C, with a depth range of 1.9 to 3.4 km.
Resource characteristics
Technology & output
The plant is known for its high-efficiency triple-flash and binary system, operating at an efficiency rate of about 18%.
The overall Kızıldere complex — with Kızıldere I having 15 MW capacity, Kızıldere II 80 MW, and Kızıldere III, consisting of two units, 100 MW and 65 MW — has a total capacity of 260 MW.
Lessons learned
After privatization in 2008, Zorlu Enerji acquired ownership and used the initial plant (Kızıldere I) as a training ground, building internal expertise over successive phases. Through the expansion to Kızıldere III, the company relied heavily on prior research conducted during stages I and II by both private companies and government institutions.
Zorlu integrated community benefits early by supplying geothermal heat from Kızıldere I to 2,500 homes in Sarayköy and to greenhouses for agriculture, strengthening local support and enabling long-term project sustainability.
The company continuously sought industrial synergies, capturing naturally occurring CO₂ from geothermal fluids and supplying it to a nearby dry ice and CO₂ plant, reducing emissions while creating additional economic value.
Over time, to address a decline in reservoir pressure, Zorlu redesigned reinjection systems and installed ESPs, further developing technical expertise and ensuring long-term operational reliability.

## Slide 31: As a vapor-dominated geothermal system, Darajat faces the risk of reservoir dryout
Case study: Darajat
Located near Mount Kendang in Garut, West Java, about 1,750 to 2,000 meters above sea level, within a volcanic zone of the Malabar-Papandayan-Kendang complex.
The field lies inside a structurally complex area formed by volcanic activity and faulting that enhances permeability and steam migration.
The Darajat reservoir has 1.5 to 3 km depth and temperatures around 240°C.
Resource characteristics
Technology & output
It is a dry-steam power complex consisting of three units constructed between 1994 and 2009, with a total installed capacity of 271 MW (Unit I with 55 MW, Unit II with 95 MW, and Unit III with 121 MW).
Average plant efficiency is 17 to 18% and capacity factor is 70%, depending on steam pressure.
Lessons learned
The project highlighted the importance of continuous reinjection to stabilize the declining reservoir pressure observed after the early 2000s, though concerns remain.
Operational studies found high auxiliary power use reduced efficiency. For example, installing variable frequency drives and Mitsubishi retrofitted turbine upgrades increased net output by about 8 MW.
Ongoing optimization studies propose hybrid operation with binary cycles to recover waste heat and extend resource life.

## Slide 32: Next-generation technologies enable energy extraction from hot dry rock with little to no natural fluid
Next-gen & frontier power generation
Advanced geothermal (AGS)/ closed-loop systems
Enhanced geothermal systems (EGS)
Superhot rock geothermal
Next-gen technologies
EGS creates or improves permeability in hot dry rock to circulate injected fluid between wells.
Closed-loop geothermal circulates a working fluid in sealed pipes to conductively draw heat from hot rock, with no groundwater contact and no reliance on rock permeability.
Superhot rock geothermal taps ultradeep formations where water becomes a supercritical fluid, enabling vastly higher heat and power output than EGS or AGS systems.
A
B
Definition
Advantages/ disadvantages
Higher thermal efficiency compared to AGS
Potentially higher scale
Seismicity risks
Reservoir uncertainty
Water losses
Geographic flexibility
No brine requirement
No seismic risk
Lower thermal efficiency
Higher CapEx requirements compared to EGS
Much higher energy
Long development time and highest cost requirement
Extreme drilling challenges and equipment limitations
Frontier technologies
C

## Slide 33: Enhanced geothermal systems fracture hot rock to unlock geothermal resources beyond natural hydrothermal zones
A
Next-gen & frontier power generation
Disadvantages
Created fracture network
Pre-production steps: - Drill an injection well and a production well into hot, low-permeability rock. - Perform hydraulic stimulation to create/enhance a fracture connecting the wells. - Pump water down the injection well.
Water flows through the engineered fractures, heating up as it contacts the hot rock. The heated water returns up the production well to the surface.
The geothermal fluid enters a heat exchanger. It transfers heat to a secondary working fluid with a lower boiling point.
The secondary fluid absorbs the heat and vaporizes. This vapor drives the turbine, which spins the generator to produce electricity.
After passing through the turbine, the secondary vapor is cooled in the condenser and returns to liquid form.
Process
The cooled geothermal fluid is returned to the reservoir through a reinjection well.
Turbine
Generator
Production well
Injection well
Ground surface
Subsurface injection
Heat exchanger
Condenser
Pump
Seismicity risk – hydraulic stimulation can trigger induced earthquakes, while AGS avoids that
Reservoir uncertainty – fracture networks may close and permeability can decline, which would decrease productivity
Water losses – injected fluid may migrate, unlike with AGS, where working fluid is contained
Advantages
Higher thermal efficiency – direct fluid/rock contact transfers heat more effectively than AGS
Potentially higher scale – compared to AGS, can access vast resources with stimulation
Leverages oil & gas skills – uses drilling, fracturing, and reservoir management expertise of the oil and gas sector
Geothermal steam
Geothermal water
Working fluid (vapor)
Working fluid (liquid)

## Slide 34: Commercial capacity of global EGS could reach 108 TW by 2050, equivalent to 3.5x current global yearly electricity consumption
A
Next-gen & frontier power generation
Commercial potential
Technical potential
Maximum technical potential
The economically and environmentally viable portion of the EGS resource that can be developed under current or projected cost and water availability conditions
The technically recoverable portion of the EGS resources that could be harnessed, ignoring economic limits but still considering water constraints and other physical feasibility factors
The total capacity in theory that could be developed if both economic and water constraints were removed and capacity be limited only by geology, temperature, and drilling depth
Chart: 
 | 201403 | 133145 | 5432.1623
 | 102574.8377
103
5
201
133
108
2030
2050
Estimated global EGS power potential, TW 2030-2050
Observations
Global commercial EGS capacity could reach ~108 TW by 2050, increasing from ~5 TW in 2030.
This is equivalent to 3.5 times current global electricity demand.
The technical potential (~133 TW) and maximum technical potential (~201 TW) show that commercial EGS would utilize about 80% of the technical and approximately 54% of the total theoretical resources by 2050.

## Slide 35: Closed-loop technology circulates fluid through underground pipes, eliminating need for natural reservoirs or fracturing
B
Next-gen & frontier power generation
Pre-production step: A sealed well or multilateral U-tube is drilled into hot rock. Unlike EGS, no fractures are stimulated and no reservoir water is used.
A working fluid circulates inside the closed loop, heating as it flows through the hot rock. The heated loop fluid reaches the surface and enters a heat exchanger. Heat is transferred to a secondary working fluid with a low boiling point. The secondary fluid vaporizes.
The steam flows into the turbine, and as the turbine spins, it drives the generator to produce electricity.
After passing through the turbine, the lower-energy steam is cooled in a condenser, and it condenses back into water.
The condensed fluid is pumped back underground to repeat the cycle.
Process
Turbine
Generator
Production well
Injection well
Ground surface
Subsurface injection
Heat exchanger
Condenser
Pump
Advantages
No seismicity risk – avoids because no stimulation or fracture creation is needed
No produced brine – avoids scaling, corrosion, and handling of H₂S or dissolved minerals
Geographic flexibility – can work in low-permeability formations where EGS/hydrothermal are not viable
Disadvantages
Lower thermal efficiency – conductive heat transfer through rock to wellbore is less efficient than fracture-based fluid flow in EGS
High CapEx – requires advanced well design, materials, and long laterals/coaxial wells
Geothermal steam
Geothermal water
Working fluid (vapor)
Working fluid (liquid)

## Slide 36: Next-generation pilots to increase avg. capacity over time; cost, geologic variability, and seismicity risks uphold commercialization
Next-gen & frontier power generation
Observations
Since the 1980s, numerous pilot demonstrations of petro-thermal systems have been conducted. In addition to the projects shown left, other early pilots, such as Ormat in the U.S. and Eavor-Lite in Canada, were completed.
However, the transition from pilot/feasibility studies to commercial-scale deployment is still challenging due to difficulties in standardization and replication across different geological sites.
Also, induced seismicity is posing a significant risk and can decrease public acceptance. For example, “felt earthquakes” led to the shutdown of EGS projects in Basel, Switzerland (2006), and Pohang, South Korea (2017).
Currently, the U.S. dominates EGS pilot projects, with commercial deployment anticipated in the mid- to late 2030s. DOE took action in 2024 by deciding to support three feasibility projects, with the goal being to cut the cost of EGS by 90% by 2035.
Location
Capacity, MW
Status
Projects
Deployment date
Chevron New Energies
California, U.S.
Planned
2029-2033
20
Mazama Energy
Oregon, U.S.
Planned
2025-26
200
XGS Energy (Meta collaboration)
New Mexico, U.S.
Planned
2027-30
150
Eavor Loop – Geretsried
Bavaria, Germany
Ongoing construction
2025
8.2
GEL – United Downs
Cornwall, UK
Operational
2025
3-5
Soultz-sous-Forets
Alsace, France
Operational
2010-present
1.7
EGS
Superhot rock
AGS/closed-loop
DOE funded
Fervo – Cape Station I
Utah, U.S.
Ongoing construction
2026
100
Fervo – Cape Station II
Utah, U.S.
Planned
2028
400

## Slide 37: Superhot rock is the least mature geothermal technology, with capacity to surpass the limitations of hydrothermal and EGS/AGS
C
Next-gen & frontier power generation
How does it work?
Works by drilling very deep underground and reaching highly heated rocks. When water is injected into these rocks, it changes into a supercritical fluid, a condition that is neither liquid nor steam. Then, the fluid rises to the surface, where electricity is generated using its energy.
How does it differ?
Compared to hydrothermal, uses supercritical reservoir for power generation instead of naturally occurring water.
Compared to EGS, it reaches to extreme depths to access naturally supercritical, ultra-high-temperature conditions.
What is the potential?
Nearly unlimited — there are different models but potentially 63 TW
Depth and temperature
5-15 km depth
<400°C
Examples
IDDP 1 & 2 (Iceland)
IDDP-J Project (Japan)
DOE Superhot Rock Initiative (U.S.)
Subsurface injection
Geothermal steam
Supercritical water
Ground surface
Generator
Turbine
Condenser
Wellhead
Separator
Supercritical reservoir
Superhot rock potential, TW by depth
Chart: 
 | 3349.5769 | 3349.5769 | 19441.8012 | 36660.9524
 | 16092.2243 | 17219.1512
5-7.5 km
16,09
7.5-10 km
44,25
10-12.5 km
3,35
63,69

## Slide 38: IDDP-1 and IDDP-2 projects in Iceland are pioneering initiatives advancing the global understanding of superhot rock geothermal
Case study: Iceland Deep Drilling Project
Active volcanic rift systems (Krafla for IDDP-1 and Reykjanes for IDDP-2).
IDDP-1 was drilled in 2008 to approximately 2.1 km, producing steam at 452°C (targeted depth was 4.5 km, but drilling terminated upon encountering a rhyolitic magma body at temperatures of >900°C).
IDDP-2 was drilled in 2016 to 4.7 km with temperature measured at 426°C and pressure at 340 bars, achieving supercritical conditions (formation temperature is estimated to be 500 to 600°C).
Resource characteristics
Technology & output
Both IDDP wells were designed for scientific research rather than electricity generation. They were not connected to power plants but demonstrated that supercritical geothermal fluids exist and can be accessed.
Injection/tracer tests at IDDP-2 revealed deep fracture connectivity to nearby shallower wells, supporting the potential for a deep superhot EGS.
Lessons learned
IDDP-1 was the world’s hottest production well, but due to the failure of several surface valves in 2012, the well had to be cooled down, cemented up, and permanently abandoned with a sunk cost of €15M. However, the project proved magma-enhanced geothermal systems are possible.
IDDP-2, the deepest well drilled in Iceland, demonstrated that ultradeep, superhot drilling is feasible but also revealed significant challenges, including a casing damage encountered during operations.
High-temperature, oxygen-rich injection water and corrosive supercritical reservoir fluids caused rapid casing and valve degradation, highlighting the need for corrosion-resistant alloys, improved well design, and strict injection-fluid control in future deep geothermal projects.
The IDDP’s commitment to open publication and data sharing established a new international standard, directly influencing Japan’s IDDP-J and the U.S. DOE Superhot Rock initiatives.
IDDP-3 is expected to be drilled in Nesjavellir in 2026, targeting a previously drilled superhot zone, and aims to test improved designs using lessons learned from IDDP-1 and IDDP-2.
IDDP-2
IDDP-3 (planned)
IDDP-1

## Slide 39: Geothermal storage for electricity has relatively lower technological readiness compared with heating and cooling applications
Storage technology
 | High-temperature geological thermal energy storage | Geomechanical energy storage
 | Geological thermal energy storage | Geopressure storage
Description | Deep geologic reservoirs engineered to store high-temperature heat (often charged by solar or intermittent resources) and discharge as firm power and/or industrial heat | Subsurface reservoirs that store energy as pressurized water in rock and release it through turbines
Usage area | Multi-hour to seasonal storage of electricity and heat | Multi-hour to seasonal storage of electricity and heat
Grid-scale long-duration storage | Yes | Yes
Depth | Deep ~500-3,000 meters | Shallow to deep: ~500-2,500 meters (formation dependent)
Temperature | < 80-250°C | Not temperature-driven; energy stored as pressure, not heat
Example projects | EarthBridge Energy (Texas) GeoBattery (West Texas) | Quidnet Energy (Texas) Sage Geosystems (Texas)

## Slide 40: Sage Geosystems is advancing long-duration geothermal storage that can deliver firm, flexible clean power
Case study: Sage Geosystems
Sage is developing projects in Texas, including its full-scale commercial demonstration near Brooks County.
The company uses subsurface formations to create pressure-based energy storage, not dependent on high geothermal heat.
Sage’s system is designed to work in sedimentary formations with suitable mechanical properties, but the company does not publicly disclose specific reservoir depths or geology.
Resource characteristics
Technology & output
Sage’s system, Sage Geomechanical Energy Storage, stores energy by injecting fluid into a sealed subsurface reservoir and releases it to generate power through controlled depressurization.
The company achieved 16-hour-long discharge in its early Texas pilot.
In 2023, Sage completed a 200-hour-long storage demonstration, validating multiday storage.
Sage plans to deploy a 3 MW commercial project integrated with ERCOT.
Lessons learned
Pilot results showed repeatable charge-discharge cycles with controlled pressure management.
The 200-hour test confirmed potential for multiday and resilience-focused applications.
Findings supported Sage’s progression toward commercial-scale deployment.

## Slide 41: Innovations in drilling technologies are key to accessing higher thermal potential
Comparison of drilling technologies (non-exhaustive)
Drilling technology
10-500 m
Groundwater
5 km
3 mi
10 km
6 mi
15 km
9 mi
20 km
12 mi
Conventional
Oil & Gas Drilling
(Reference)
Conventional Geothermal
Recent EGS
Description | Baseline method for moderate depths, well-known in oil & gas, adapted to geothermal | Enhanced drilling with high-temp tools, directional drilling for reservoir targeting, or EGS creation | Millimeter-wave drilling, plasma/ hybrid thermal drilling
Drilling bits | Tricone roller-cone 0-3 km Polycrystalline diamond compact (PDC) 3-5 km | Thermally stable PDC (TSP) 5-8 km Diamond-impregnated bits 6-10 km | Millimeter-wave (gyrotron) 10-15 km Plasma or thermal spallation 15-20 km Laser-assisted drilling 20+ km
Opportunities | Mature and reliable | Reaches harder rock (basalt, granite, etc.) | Potential to unlock superhot rock
Challenges | Slow, wear issues | Higher cost, stress on materials and wellbore stability | Cost and uncertainty risk
Drilling Bits/
Technology
Superhot Rock
(Developing)
Laser-
assisted
drilling
Conventional
Next Generation
Next Generation
Conventional
Frontier
Frontier

## Slide 42: Drilling currently drives ~54% of next-gen geothermal LCOE; investments to reduce that share target heat resistance, permeability, and drill-bit life
Emerging technologies aimed at lowering next-generation geothermal drilling costs
Breakdown of projected LCOE components of next-generation geothermal in a low-cost case (US$/MWh)
Drilling technology
High-powered millimeter-wave beams from a gyrotron vaporize rock and drill ultradeep boreholes, bypassing the wear and tear of traditional drilling methods.
Millimeter-Wave Drilling
Directional Steel-Shot Drilling
Repetitive Pulsed Electric Drill (RePED)
High-Pressure Water Jet-Assisted Drilling
A full-scale demonstration drilled 10 feet deep using 100 kW of millimeter-wave power; Quaise also plans to deploy a 1 mW gyrotron within two years to reach commercially viable depths.
Tetra Innovation Institute and NREL partnered to advance the technology, with potential drilling cost reductions of 75% and applications in industries beyond geothermal.
High-voltage electric pulses fracture rock, avoiding mechanical contact. Reduces wear on equipment and is designed to work with existing drilling infrastructure.
Drilling solutions startup Canopus is collaborating with TNO and European partners to test the drill system in the Netherlands, funded by a Dutch subsidy scheme.
Steel-shot particles are released under high pressure to erode rock formations and reduce resistance to further rotary drilling.
ORCHYD combines high-pressure water jets with fluid-driven percussion drilling, aiming to cut drilling costs by 65%. The project received Horizon 2020 funding from the EU in 2021.
High-pressure water jets cut rock into shapes that can be broken apart more easily by fluid-powered percussive hammers.
Chart: 
 | 51 | 25.5 | 22.3
 | 59.9 | 25.5 | 7.5
54%
46%
2025
50%
50%
2035
25%
75%
2050
111
51
30
Drilling costs
Other
Drilling, loop supplies, and installation also comprise 55-65% of conventional geothermal (GHP) costs in the U.S. (2025).

## Slide 43: Companies at the frontier of drilling technology innovation show successes in pilots and field testing
Drilling technology
Key Highlights
Tech Approach | EGS/horizontal drilling | Geopressured | Laser-assisted drilling | Conductive heat transfer | Plasma drilling | Millimeter-wave (gyrotron)
Technology Readiness Level | Commercial pilot | Commercial pilot | Pilot/demo | Early pilot/demo | Pilot/field test | Pilot/field test
Target depth/ temperature | 2-4 km 175-250° C | 3-5 km 150-200°C | 3-6 km High-temp rock | 3-6 km >200° C (superhot) | 5-10 km High-temp, hard rock | 10-20 km >374°C (superhot)
Valuation | $1.4B | ∼$150M | $3.8M-$4M | ∼$50M | ∼$140M | $95M-$105M
Geographic focus | U.S. (Nevada, Utah) | U.S. (Texas, Gulf Coast) | U.S. (California, Oregon) | U.S. (Texas) | Slovakia, U.S. | U.S./global through MIT link
Major projects | Project Red (Nevada EGS) | Pilot plant in Christine, Texas | Early EGS tests, laser enhanced drilling R&D | Pilot with DOE support | Field trials with oilfield partners | MIT test rigs, demo planned approx. 2028
Key advantage | Proven horizontal EGS, scalable beyond volcanic zones | Hybrid approach allows energy storage and power generation | Novel stimulation and rock weakening with lasers | Closed-loop avoid fluid- loss and is scalable in many regions | Works in ultrahard formations, extended tool life | Ultra-deep, contactless drilling enables access to superhot rock
Overview of first-mover companies (non-exhaustive)

## Slide 44: High-efficiency CO₂ turbines can accelerate geothermal commercialization
CO₂/sCO₂ turbines in superhot geothermal systems
Drilling technology
Why CO2?
CO₂ as a working fluid: Provides non-explosive, non-flammable, non-toxic, and low-cost alternative to water.
Thermosiphon effect: Large density change with temperature creates strong buoyancy forces, reducing or eliminating pumping power in geothermal wells.
High thermal efficiency: Achieved through low compression work and extensive heat recovery from turbine exhaust.
Compact, efficient design: In its supercritical state, CO₂ is nearly twice as dense as steam, allowing for smaller turbines and pumps, a reduced plant footprint, and lower capital costs.
Advantages
Higher efficiency (especially at high temperatures) vs. steam cycles
More compact turbine/less bulky equipment (higher power density)
Lower parasitic losses (reduced compression work) and strong heat recovery potential
Key Challenges
Materials and durability under high temperature, performance, corrosion
Heat exchanger design and integration
Turbomachinery sealing, leakage, and fluid purity
Control complexity (nonideal gas behavior)
Matching geothermal temperature and heat delivery to turbine design

## Slide 45: Millimeter-wave drilling, pioneered for nuclear fusion, is being adapted to unlock terawatt-scale geothermal potential
MMW from nuclear innovation to geothermal application
Superhot rock could unlock TW of firm power
Observations
Technology: MMW drilling originated from nuclear fusion research in the mid 20th century and has recently been leveraged for geothermal applications.
Power potential: Accessing superhot rock at greater depths (10-20km) by using MMW drilling technology could unlock terawatts of power in the U.S.
Cost trajectory: As MMW drilling matures and learning curves accelerate, LCOE is projected to fall from early pilot levels (~$150/MWh) to ~$20-$35/MWh, reaching parity with solar and wind.
Challenge: Conventional drilling struggles with extreme temperature and pressure at superhot depths, which MMW aims to overcome by minimizing mechanical contact and material wear.
Drilling technology: Superhot
1950-1960
Gyrotron technology is developed to create high-power millimeter waves for plasma heating in nuclear fusion.
1970-1990
Fusion research accelerates, with gyrotrons refined for use in magnetic confinement systems.
2000-2010
Advances in materials and controls (vacuum tubes, superconducting magnets, beam focusing) make gyrotrons more efficient.
2010-2020
MIT spinoff Quaise Energy begins adapting gyrotron-based MMW drilling to vaporize rock.
2020+
National labs (DOE and ORNL) identify superhot rock as a terawatt-scale resource, begin development of pilot projects.
Chart: 
 | 0.9 | 3
 | 0.9
 | 0.4
Conventional Geothermal
.4 TW
.9 TW
3 TW
Superhot Rock (MMW)
.9 TW
4.3 TW
Estimated U.S. energy potential from conventional vs. SHR geothermal
12.5 km
10 km
7.5 km
Chart: 
 | 66 | 45 | 150 | 20
 | 43 | 30 | 150 | 15
Traditional Geothermal
Enhanced Geothermal (EGS)
SHR Geothermal (FOAK)
Mature SHR Geothermal (NOAK)
$66-$109
$45-$75
$150-$300
$20-$35
LCOE for traditional, EGS, and SHR geothermal power

## Slide 46: AI can improve accuracy in geothermal exploration and reduce the costs and timelines of project development
Drilling technology: AI
Remote sensors collect geological data.
AI/ML models process geological data.
Data is translated into real-time and predictive models.
Geosensing is the use of remote sensing such as drones, satellites, or sensors to detect geological characteristics.
With the use of AI, geothermal reservoirs will be more easily and accurately identified. AI-enabled geosensing will address the uncertainties and challenges of geothermal exploration including identifying sites, subsurface characteristics, and geological risks.
3
1
4
Data Collection
Data collected through remote sensing (satellite thermal imaging, LiDAR), seismic surveys, magnetic/gravity data, or well logs.
Data Processing
Utilize AI models (e.g., convolutional neural networks, random forests) to detect correlations and hidden patterns.
Prediction & Mapping
AI generates heat flow maps, reservoir probability zones, and drilling targets.
Feedback Loop
AI refines predictions as new drilling/seismic data is collected.
AI Process Map
Application
2
Satellite collects thermal imaging of geological area.
AI models detect promising geological resources.
Models are generated with reservoirs with a high probability of success.
Models are consistently improved based on new and existing data

## Slide 47: AI is transforming geothermal deployment by enabling faster, more accurate subsurface characterization
Key characteristics across exploration and project development
AI will transform deployment across the geothermal value chain
Temperature
Temperature range of 210-300℉/99-149℃
Minerals
Low mineral content
Seismic Activity
Limiting seismic activity
Permeability
Assess fluidity for traditional geothermal or EGS
Gaseous Emissions
Low gas content
Geochemistry
Assess composition for siting and drilling
Transmission
Availability of transmission lines
Permitting & Regulatory
Timelines and regulatory standards
Finance
Assess project risk, returns, and financing
Siting & Design
Siting and design plant and wellbores
Drilling
Improved drilling performance
Operations
Continuous assessment of performance
Project Development
Exploration
 | Traditional | AI-Enabled
Time | Up to 10 years to commission a geothermal project | Decrease exploration and project development timeline
Costs | Exploration, preparation, and drilling accounts for more than 50% of LCOE | Reduce costs across geothermal development, especially drilling, the most expensive cost.
Drilling Rate | Exploratory drilling has a success rate of only 25% | Achieve higher success rate with increased accuracy and improved drilling performance
New Regions | Challenges to resource mapping due to complexities of geographical regions | Enables resource mapping in unexplored regions (Africa, SE Asia, Latin America) and improves accuracy
Sustainability | Exploratory drilling required for feasibility studies, with a success rate of 25% | Minimizes environmental footprint by reducing exploratory drilling.
Drilling technology: AI

## Slide 48: Geothermal Power Global Policy

## Slide 49
Four key policy priorities can help scale geothermal heating and cooling (H&C) deployment and lower costs.
  Global collaboration on geothermal energy largely favors power generation over H&C.
  As a human capital-intensive industry, transitioning the oil and gas workforce, which has extensive overlapping competencies with the geothermal sector, is a high policy priority.
  Strong funding for R&D is key in scaling geothermal H&C across diverse geographies and in driving down next-generation geothermal costs.
  Geothermal projects carry high early-stage risks, necessitating strong risk mitigation policies to incentivize adoption.
Drilling is the largest and most variable cost driver of both conventional and next-generation geothermal heating & cooling, typically contributing over 50% of total project cost and/or LCOE.
  For conventional geothermal technologies, geography and loop design are the primary drivers of drilling costs, due to dependence on hydrothermal reservoirs and comparative costs of vertical versus horizontal borehole loops.
Synergies with the oil & gas industry can drive down geothermal power costs and improve efficiency, and growing interest from the O&G industry has led to partnerships and upfront investments, particularly for next-generation geothermal.
  Subsurface data and modeling techniques from the oil & gas industry can help de-risk geothermal heating projects and drive down costs, as demonstrated by the Eavor-LiteTM demonstration project in Alberta, Canada.
  Improved oil & gas drilling techniques (e.g., fracking) can drive down drill time and risk and improve drilling efficiency.
  Technical synergies between the geothermal and the oil & gas industries highlight strong workforce transferability, which can help streamline geothermal commercialization.
Key messages
Global Policy

## Slide 50: Four key policy priorities can help scale geothermal power deployment and drive down costs
Observations
Stronger implementation of policy goals could boost new geothermal heat developments 50% by 2030 in the APS compared with the Stated Policies scenario.
Strong policy can also help drive next-generation geothermal cost reductions of up to 80% by 2035.
In the APS, expanding policy support and cost reductions would scale GHP consumption to almost 3,000 PJ — 50% higher than in the Stated Policy scenario (China, U.S., and Europe together account for 80% of this growth).
Almost two-thirds of geothermal power capacity additions between 2024 and 2030 are expected to be policy-driven – primarily tax credits, fixed tariffs, and premiums.
Global policy
Global Collaboration
Global collaboration on geothermal energy – particularly heating and cooling – lags behind other renewables, slowing innovation and increasing risk. Stronger, more large-scale collaboration is a priority.
Workforce Development
Geothermal expansion will require a skilled workforce in engineering, geology, and drilling sectors. Transitioning the oil and gas workforce will streamline geothermal workforce development.
Research & Development
Poor funding infrastructure for geothermal exploration and drilling drives up investment costs and slows technological progress. Strong funding mechanisms will be necessary to speed geothermal deployment.
Risk Mitigation
Geothermal projects have higher predevelopment risks compared with other renewable energy technologies due to complex geological and subsurface conditions. Mitigating risk is critical in lowering project costs.

## Slide 51: Global leaders in deployment are developing policies not only for geothermal power but heating and cooling as well
Observations
Over half of all countries with geothermal policies in place (16 of 31) focus exclusively on power generation.
Regional policy schemes in Latin America and East Africa are not included in this map.
Only eight countries (all in Europe) have adopted geothermal roadmaps for their heating & cooling sectors.
>100 countries have policies in place for solar PV and onshore wind — over 3x as many as for geothermal energy.
Europe is a regional hub for geothermal heating & cooling policies, while China leads on the country level.
Geothermal energy is a priority mitigation option in only 9% of NDCs’ submitted data.
While the risk mitigation-to-remuneration policy ratio is ~1:2 for solar and wind energy, the ratio for geothermal energy is ~1:1 due to high early-stage risk.
Countries with geothermal policies in place, 2024 (risk mitigation and/or remuneration)
Global policy

## Slide 52: Global collaboration favors geothermal power production, leaving room for growth in heating and cooling expansion
Drivers of variable global collaboration on geothermal power versus heat
Power projects tend to be larger and have bigger returns compared to more localized heating projects.
There is a differential global emphasis on electricity access compared to heating access.
The development of EGS has spurred greater collaboration on geothermal power generation.
Scalability of power projects attracts greater private investment.
Global policy
Scale | Power Generation |  | Heating & Cooling | 
Global |  | The Global Geothermal Development Plan (GGDP), launched by ESMAP in 2013 to scale geothermal power, has supported 13 countries and brought three projects online. |  | Although World Bank does not have a dedicated global program for geothermal heating, it has provided one-off investments in district heating in countries including Türkiye and El Salvador.
Regional |  | The GRMF finances geothermal power projects in East Africa, expanding to include heating in 2022; 26 power and 5 direct-use projects have received funding. |  | Geothermica’s €32.5 million Joint Call 2021 aims to accelerate geothermal heating and cooling projects by 2030 through large-scale, commercially viable projects.
Bilateral |  | Japan’s International Cooperation Agency invests in building geothermal power capacity in Latin America and Africa, including over 400 MW of geothermal power plants in Kenya. |  | The German Agency for International Cooperation and the Central American Integration System have cooperated on geothermal heating and cooling in El Salvador, including a pilot geothermal-powered coffee dryer.

## Slide 53: Successful geothermal risk mitigation policies target early-stage resource and exploration risks; grant schemes lead in nascent geothermal markets
Early-stage geothermal risks and relevant risk mitigation schemes
2024-2030
Chart: 
 | 8 | 6 | 34 | 31 | 21
Resource Assessment
Subsidized Loans
Grants
Public Insurance
State-Led Development
Limited geological data increases uncertainty.
Lengthy permitting processes can slow project timelines.
High upfront drilling costs can stunt private investment.
Wells may have low temperature or flowrates.
Observations Grants are useful and most common in nascent geothermal markets. Some schemes target exploration only, while others also support drilling and operations; strong policy supports both.
Policy Priorities
Relevant Risk Mitigation Scheme(s)
Increase data quality and accuracy
Create open-source data repositories
Resource assessment
State-led development
Simplify and consolidate permitting processes
Expand geothermal-specific permitting regimes
Public insurance
State-led development
Invest in drill efficiency technologies
Expand financial incentives for private-sector investment
Grants
Subsidized loans
Strengthen R&D on subsurface modeling
Account for well failure in subsidies and grants
Grants
Public insurance
Case study: France
Sources: The Future of Geothermal Energy (IEA, 2024); The successful geothermal risk mitigation system in France from 1980 to 2015 (European Federation of Geologists, 2016); France launches $54m geothermal risk mitigation fund (ThinkGeoEnergy, 2015); EUR 195M guarantee fund approved for deep geothermal projects in France (ThinkGeoEnergy, 2023).
Credit: Una Oljaca, Pia Doris Morrow, and Gernot Wagner. Share with attribution: Wagner et al. “Geothermal Power,” Columbia Business School Climate Knowledge Initiative (10 March 2026).
Conventional geothermal capacity additions by risk mitigation scheme

## Slide 54: U.S. ranks No. 3 in superhot rock potential, has 12% of total global geothermal potential, and is set to scale with policy support
U.S. geothermal power policy timeline
U.S. 2021 energy demand vs. 1% geothermal power potential, GWh
Case study: United States
1970
Landmark law grants federal authority over geothermal leasing on public lands (via BLM and U.S. Forest Service), enabling competitive leasing with royalties and rentals as part of a broader energy policy to address rising demand and foreign oil dependence.
2009-16
2024-25
IRA incentives repealed but geothermal spared — tax credits phase down after 2033. Global tariffs and U.S. support for tech reshoring boost emerging EGS startups (Fervo, Sage) supplying data centers with baseload power.
2005
Energy Policy Act: Is overhauled, streamlining leasing and permitting and adjusting royalty structures.
2017-21
Trump 2.0: OBBA, Global Tariffs, Domestic Tech Giant Incentives
Biden: Bipartisan Infrastructure Law (2021) + IRA (2022)
Trump 1.0:
Obama Era
Energy Policy Act
Geothermal Steam Act
Chart: 
 | 4374671 | 4374671
 | 31336521
5-7.5 km
7.5-10 km
10-12.5 km
12.5+ km
2021-24
Excess of 31,336,521 GWh
Ability to power NYC
660x over
Majority of U.S. population
High-density population pocket
Provides broad support of renewable energy development, support for DOE funding for EGS; geothermal included in net-zero planning.
Rollbacks in environmental policies broadly ease permitting; renewable incentives are de-emphasized.
DOE’s Geothermal Tech program advances EGS demonstrations.
Modern EGS technology could access ~3,400 GWs of non-superhot rock power in Q4 2025.
35,711,192
Equivalent to
21B
barrels of oil
2021 energy demand (CATF)
1% of superhot rock potential

## Slide 55: OBBBA keeps IRA 45Y and 48E incentives for geothermal power until 2035; foreign entity of concern (FEOC) rules apply after 2026
Case study: United States
Preserved
Inflation Reduction Act (IRA)
One Big Beautiful Bill Act (OBBBA)
Chart: 

Early expiration
All projects onward will be affected by stricter FEOC restrictions.
45V – clean hydrogen: Credit available through 2032 for facilities that start construction. Producer can claim up to $3.0/kg until 10 years after the facility is placed into service. Under OBBBA, the credit is available only if construction starts by December 31, 2027.
Wind and solar: 48E ITC of 6%, incrementable up to 30% and 45Y PTC of ¢0.3/kWh incremental up to ¢1.5/kWh. Facilities must be constructed by July 2026 or placed in service by December 31, 2027.
48E/45Y ‒ geothermal: Preserved in full; sourcing rules apply after 2028. Phaseout set to begin in 2033, through 2035.
Executive Order: Declaring a National Energy Emergency
Cites geothermal heat under the definitions for the terms energy or energy resource, 30 U.S.C. 1606 (a)(3).
Executive Order: Protecting American Energy from State Overreach
States intention to remove illegitimate impediments for the discovery and production of geothermal power.
Secretarial Order: Unleash Golden Era of American Energy Dominance
States intention to focus time, resources, and technologies of the DOE’s R&D toward the development of geothermal.
DOE Office of Hydrocarbons and Geothermal
Supports the development of EGS and superhot technologies through financing and R&D efforts.
Geothermal Power Under Trump Administration
The GTO’s programs are building toward their strategic goal of supplying 60 GW of EGS and hydrothermal resources deployment by 2050.

## Slide 56: U.S. policy support for geothermal emphasizes national energy security and global leadership
Case study: United States
Rationale and significance for geothermal
Example actions
Resilience
National security
Energy dominance
Domestic, fuel-independent power generation reduces geopolitical and import risks.
Geothermal requires no imported fuel, no complex supply chains, no mineral inputs, and no fuel transport, making it one of the most secure firm resources.
Extreme weather and volatile loads require power that is always available and not weather dependent, making firm power that is resilient and stable important.
Geothermal operates through storms and grid stress, with underground infrastructure that is inherently physically resilient.
Access to firm clean energy technology enables countries to gain manufacturing advantage, export capability, and stable industrial power.
Next-gen geothermal (e.g., EGS, closed-loop) utilizes U.S. drilling prominence, offering a domain where the U.S. can become the global leader and have energy dominance in clean firm baseload technology.
Executive Order 14008, “Tackling the Climate Crisis at Home and Abroad” (2021), recognized climate change as a national security threat and directed the United States toward a carbon, pollution-free electricity sector by 2035.2
The U.S. Air Force, U.S. Army, and the Defense Innovation Unit launched geothermal pilot projects with the main goal of improving energy resilience at military bases. They tested the systems at Mountain Home Air Force Base in Idaho and Joint Base San Antonio in Texas to help ensure bases could keep reliable power even when the main electric grid went down.1
The Department of Energy’s Utah FORGE site served as a dedicated EGS field laboratory in Milford, Utah, with R&D funding and project investment opportunities.3
Geothermal electricity plants qualified for the federal Investment Tax Credit, and the Inflation Reduction Act extended these clean energy credits, allowing eligible geothermal projects to claim a 30% credit.4

## Slide 57: With 8% of the world’s geothermal resources, China’s potential for geothermal power could fast-track its 2060 net-zero targets
Geothermal power lacks representation in Chinese energy policy
China’s 2050 energy demand projections and 1% geothermal power potential in GWh
Case study: China
Chart: 
 | 11515878 | 11515878
 | 75969417
2050 energy demand
1% of superhot rock potential
87,485,295
Excess of 75,969,417 GWh
2005
Provides broad support for renewable energy outbuild, with geothermal explicitly mentioned
2016-20
Reach +1.1B meters of geothermal heating & cooling and increase power to 500-530 MW by 2020
2021
Promote deep geothermal heating & cooling and boost geothermal power generation
2023
Renewable Energy Law
13th Five Year Plan
14th Five Year Plan
Geothermal Industry Standard and Beijing Declaration
Industry Standard focuses on heating & cooling; Beijing Declaration prioritizes geothermal development as one of the most popular energy sources of the future
2020
Achieve carbon peak by 2030, reduce emissions rapidly by 2045, and reach deep decarbonization and neutrality by 2050
Net-Zero 2060 Plan
5-7.5 km
7.5-10 km
10-12.5 km
12.5+ km
94% of population lives in East China
Equivalent to
51B
barrels of oil
Ability to power Beijing
683x over

## Slide 58: 20% of global EGS potential is in Africa, providing opportunity for economic development and surpassing projected 2050 demand
Kenya holds the majority of the continent’s installed conventional capacity
Next-generation geothermal development presents a significant opportunity to reliably meet Africa’s growing energy needs and foster sustainable development
Case study: Africa
5-7.5 km
7.5-10 km
10-12.5 km
12.5+ km
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
 | 65.3 | 65.3 | 65.3 | 65.3 | 135.3 | 135.3 | 135.3 | 135.3 | 135.3 | 170.3 | 205.3 | 205.3 | 212.8 | 212.8 | 373.4 | 626.2 | 660.2 | 680.2 | 691.1 | 691.1 | 870.43 | 870.43 | 957.03 | 992.03 | 947.03
Africa
Cumulative installed capacity of geothermal power (MW)
Chart: 
 | 99.2 | 0.8
Kenya
1%
Ethiopia
Chart: 
 | 8.5 | 12.4
2021 Global Electric Capacity
1% of African Superhot Rock Potential
1.5x
global electric capacity in 2021
Electric Capacity TW
Spotlight Countries for Superhot Rock (estimated GW)
Sudan
Chad
Niger
Ethiopia
Nigeria
Cameroon
Somalia
S. Sudan
Angola
Kenya
Chart: 
 | 2000 | 800
Chart: 
 | 1800 | 1200
Chart: 
 | 1200 | 350
Chart: 
 | 1100 | 550
Chart: 
 | 1000 | 800
Chart: 
 | 1000 | 800
Chart: 
 | 300 | 200
Chart: 
 | 300 | 200
Chart: 
 | 280 | 200
Chart: 
 | 270
1
2
3
4
5
6
7
8
9
10
Africa approaches 1 GW of conventional geothermal power, with Kenya leading 99% of installed capacity. Ethiopia holds the remaining 1%.
Africa’s population is expected to rise from
1.5B to 3B by 2070, requiring more energy and opportunities for socioeconomic development.
7.5-10 km
10-12.5 km

## Slide 59: East Africa can deliver Africa’s ~13 GW geothermal potential by 2050; policy reform and regional coordination will determine the pace
Case study: East Africa deep dive
Geothermal Potential and Installed Capacity in East Africa Rift Valley Countries, MW
East Africa Potential
Africa is on track to surpass Europe in geothermal capacity, scaling to 13 GW by 2050 versus Europe’s 5.5 GW.
The East African Rift, one of the world's most active tectonic systems, contains more than 20 GW — roughly 70 to 80% of Africa's geothermal potential — where continuous plate movement generates extraordinarily high heat flow.
With $35 billion in planned investment, Kenya and Ethiopia are positioned to deliver over 90% of Africa’s geothermal development by 2050, anchoring the continent’s clean baseload expansion.
Unlocking this scale-up requires strong policy: de-risking early drilling, harmonizing Rift Valley laws, and investing in cross-border grid integration to turn geology into bankable, scalable clean power.
Kenya leads with 985 MW, while Ethiopia's current ~7.3 MW, backed by an expanding project pipeline, mirrors the Rift Valley's wider geothermal takeoff.
From Barriers to Solutions: Policy Levers for Geothermal Growth in East Africa
Chart: 
 | 7.3 | 985
 | 50 | 10000 | 1000 | 10000 | 500 | 4500
Comoros
Ethiopia
Djibouti
Kenya
Uganda
Tanzania
Installed
Potential
Barriers | Emerging Solution Reform
High upfront costs: Drilling risk and CapEx-intensive exploration. | Regional Geothermal Risk Mitigation Facility and blended finance with KfW, AfDB.
Institutional gaps: Weak regulatory clarity in early-stage markets (Tanzania, Uganda). | KenGen and GDC as regional training hubs and harmonization of EAC geothermal policy.
Technical capacity: Lack of specialized workforce and site modeling data. | UNEP and IGA capacity programs and Kenyan training of 200+ regional engineers.
Environmental and social consent: Local resistance near protected lands’ hot springs. | Early-stage community co-design and geothermal tourism pilots (e.g., Menengai).

## Slide 60: Geothermal represents 43% of Kenya’s 2024 electricity generation; unlocking superhot rock potential will dwarf existing capacity
Kenya’s adoption of geothermal power and favorable policies revolutionized its national electricity mix
Tapping into Kenya’s superhot rock potential could produce 130x Nairobi’s energy demand, far surpassing current hydrothermal capacity
Case study: Kenya
5-7.5 km
7.5-10 km
10-12.5 km
12.5+ km
Excess of 1,209,299 GWh
Ability to power Nairobi
130x over
Equivalent to
643M
barrels of oil
Estimate
Menengai, Kenya
5 SHR wells drilled
Deepest well: 2,196 meters
Hottest well = 400℃
Existing Hydrothermal
Superhot Rock
Kenya’s current national electricity mix
Geothermal comprises 43% of total Kenyan electricity generation, 2024.
1977
2024-25
1982
United Nations permits Kenya Power (KenGen) to take charge of first integration amid 1970 oil crisis.
Kenyan Parliament signs the Geothermal Reources Act, establishing a formal investing, siting, and licensing framework.
Kenya Vision 2030: Government plans rapid industrialization to become middle income by 2030, where the country expects to double geothermal power integration to 1,600 MW.
2018
At the Iceland Geothermal Conference, KenGen presents a case study and validates the wellhead concept as a national fast-track strategy for early revenue production and clean firm power.
2009
GEG brings modular deployment to Africa's geothermal industry by winning the tender for Kenya's first 5.5 MW modular geothermal wellhead facility.
Chart: 
 | 12375 | 63694 | 63694
 | 1209299
2021 Energy Demand
2050 Energy Demand Projection
1% Superhot Rock Potential
1,272,993
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
 | 58 | 58 | 58 | 58 | 128 | 128 | 128 | 128 | 128 | 163 | 198 | 198 | 205.5 | 205.5 | 366.1 | 618.9 | 652.9 | 672.9 | 683.8 | 683.8 | 863.13 | 863.13 | 949.73 | 984.73 | 939.73
939.73
MWh

## Slide 61: Türkiye’s 1.7 GW of geothermal capacity equals 11% of global installed capacity but meets only 1.5% of its own power demand
High geothermal potential and a revised FiT fueled Türkiye’s 2011-2016 geothermal boom
Installed geothermal capacity over time, GW 2000-24
Case study: Türkiye
2005
First national renewable framework establishes feed-in tariffs. Policy introduces guaranteed offtake for renewables, attracting first private developers for geothermal exploration.
2011
2025+
Industry proposes to link FITs to carbon pricing and baseload guarantees. Policy could restore long-term investor confidence and enable new deep-well exploration in Central and East Anatolia. Country aims for 4 GW geothermal power by 2030.
2007
Defines resource ownership by the state, licensing (exploration and operation), reinjection rules, and environmental obligations. It transfers authority to provincial administrations, which accelerate exploration.
2019
Potential YEKDEM Extension and Carbon Market Integration
Presidential Decree No. 3453
National Energy Efficiency and Renewable Strategy 2019-2023
Law No. 6094 (Amendment to 5346)
Geothermal Resources and Natural Mineral Waters Law No. 5686
Renewable Energy Law No. 5346
2021- 2024
Recognizes geothermal as a baseload renewable resource supporting grid stability, resulting in prioritization of geothermal in planning.
Revises feed-in-tariff scheme (geothermal tariff US10.5¢/kWh for 10 years), triggering surge of private financing and foreign interest (2011-2016 boom). Enables bankable PPAs under YEKDEM. Growth continues with the World Bank-Türkiye Development Project in 2016.
Converts FITs from USD to TRY due to TRY devaluation. That limits new investments but keeps the industry stable. Between 2022 and 2025, continues RSM and concessional funding with no new FIT scheme beyond 2025. Industry is focused on efficiency upgrades and binary cycle retrofits.
Chart: 
 | 18 | 15 | 94 | 624 | 1613.188 | 1734.338 | 4000
2000
2030
…
2024
2020
2015
2010
2005
0,02
0,02
0,09
0,62
1,61
1,73
4,00
-4%
+44%
+46%
+21%
+2%
+15%
5-7.5 km
7.5-10 km
10-12.5 km
12.5+ km
Estimate
Existing Hydrothermal
Superhot Rock

## Slide 62: Italy can achieve second ramp-up in geothermal power with FER2 support
Gap between FER1 and FER2 decrees resulted in stagnant installed capacity
Installed geothermal capacity over time, GW 2000-24
Case study: Italy
1999
Liberalizes electricity generation and supply, opening both to competition.
2011
2024-2025
Provides for innovative, high-cost RES with a €35.3B budget, enabling restart of geothermal pipeline.
2010
Updates rules for exploration and exploitation of geothermal energy, which includes classifying resources by temperature, clarifying licensing procedures, and opening the market to new developers.
2016
FER2 (RES2) Decree
FER1 (RES1) Decree
RES-E excl. PV Decree
Legislative Decree 28/2011
Legislative Decree 22/2010
Bersani Decree
2019
Creates core incentives, including bonuses for low-impact/fully reinjected geothermal.
Implements EU RES rules and Autorizzazione Unica streamlined permitting.
To boost renewable adoption, provides incentives to specific technologies (PV, onshore wind, hydro, and residual gas) with a total budget of about €5.8B. Criticized for excluding geothermal, which stalled new developments until the FER2 scheme was introduced.
Chart: 
 | 590 | 671 | 728 | 768 | 771.79 | 771.79 | 1000
2000
2030
…
2024
2020
2015
2010
2005
0,59
0,67
0,73
0,77
0,77
0,77
1,00
+3%
+2%
+1%
0%
0%
+4%
5-7.5 km
7.5-10k m
10-12.5 km
12.5+ km
Estimate
Existing Hydrothermal
Superhot Rock

## Slide 63: World’s No. 2 geothermal market, Indonesia is using policy reforms, private-sector investment to unlock hydrothermal capacity
Indonesia has integrated geothermal energy in its industrial policy and long-term decarbonization goals
Situated on the Pacific Ring of Fire, Indonesia has 356 geothermal sites, 127 active volcanoes, and one of the world’s largest geothermal reserves
Case study: Indonesia
1981-91
Declare geothermal energy a national resource and provide preliminary guidelines for its exploration and development.
2014
Eliminates restrictions on "mining" designation, establishes auction-based working regions, and allows for private and international participation.
2024
Raises targets for renewable energy shares to over 35% by 2034, indicating greater policy support for the growth of geothermal energy.
2060
Presidential Decree No. 22 (1981) and No. 45 (1991)
Geothermal Law No. 21/2014
Electricity Supply Business Plan (RUPTL 2024-2034)
National Net-Zero Commitment
Commits to achieving carbon neutrality for the entire economy by 2060, establishing geothermal as a deployable, low-emission power source for long-term security.
2022
Raises over $20 billion to boost investments in sustainable energy, with geothermal being a crucial baseload technology.
Indonesia Just Energy Transition Partnership (JETP)
2,342.63 MW installed — twice as much as in 2009 (1,187 MW) and an additional 904 MW since 2015 (1,438 MW).
Chart: 
 | 145 | 1000 | 1375 | 2000 | 2250 | 3300
1990
2007
2014
2018
2021
2030 (Projected)
Total Potential = 23.36 GW
Indonesia Geothermal Installed Capacity, MW
0
1-280
281-430
431-575
576-720
721-860
861-1,010
1,010-1,150
1,151-1,300
1,301-1,430
1,431-1,600
MW

## Slide 64: With 12 GW potential, Chilean policy is now steering geothermal from resource mapping to real, scalable power generation
Chile’s geothermal policy evolved from concessions to market incentives, risk finance, and innovation
Chile 2021 vs. 2050 energy demand and 1% geothermal power potential in GWh
Case study: Chile
Chart: 
 | 88015 | 167029 | 167029
 | 11528016
2021 Energy Demand
2050 Energy Demand
1% of Superhot Rock Potential
11,695,045
Excess of 11,360,987 GWh
2000
Introduces Geothermal Concessions Law, the first law for geothermal exploration rights and exploitation concessions.
2008
MiRiG – Geothermal Risk Mitigation Program (IDB + CTF) injects concessional public finance, guarantees, and loans convertible to grants to de-risk high-cost exploratory drilling.
2015
2025
Inaugurates South America’s first geothermal power plant (48 MW) at 4,500 meters in the Atacama Desert, by Enel and ENAP.
2014-15
Electricity tender reforms and structured PPAs produce transparent, technology-neutral contracts, improve auction regulations, and make it possible for geothermal developers to obtain 15- to 20-year PPAs.
5-7.5 km
7.5-10 km
10-12.5 km
12.5+ km
Equivalent to
6.8B
barrels of oil
131x the country’s 2021 electricity consumption
20/25 Renewable Law improves long-term PPA structures and market access for geothermal as firm baseload generation, increases the clean energy objective to 20% by 2025, and modifies power supply tenders.
Introduces mandatory renewable quotas for power providers under the NCRE Mandate (10% by 2024), creating demand and compliance pressure for non-conventional renewables like geothermal.
2013
Issues two new geothermal exploration licenses to Transmark in the Andes, expanding its concession portfolio and signaling continued policy support for scaling geothermal as a firm, decarbonizing energy source.
2017

## Slide 65: Japan’s 23 GW potential remained untapped for decades, but policy reform and local co-creation are driving a cautious revival
Japan is using FiTs, R&D programs focused on closed-loop and superhot potential for its geothermal strategy
Japan Geothermal Installed Capacity, MW
Case study: Japan
1966
Matsukawa plant, Japan's first commercial geothermal facility, starts operations in 1966.
1960- 1990
The 2012 Feed-in Tariff (FiT) and regulatory relaxation for under 7.5 MW projects, along with relaxed national park permitting reforms (2015), open new sites and create the first clear legal path for small-scale and binary geothermal plants.
2021
2025-35
New R&D programs for closed-loop and superhot geothermal pair with policies focused on risk reduction, faster permits, and community consensus to scale by 2035.
2012-15
The 6th Strategic Energy Plan reaffirms geothermal as a key firm renewable alongside nuclear and hydrogen. Sets a 2030 target of ~1.5 GW (1.1% of power) and empowers JOGMEC with subsidies, equity, and loan guarantees, making geothermal officially part of national energy planning.
Observations
Approximately 80% of Japan's geothermal reserves are in national parks and onsen regions, necessitating multi-ministry permissions and extensive coordination, which makes development difficult and slow.
Japan uses only ~2%, or ~520 MW, of its 23 GW potential due to decades of policy, permitting, and community barriers; however, recent reforms and a new target of ~1.5 GW by 2030 signal a slow revival in the sector.
National Parks Law and Hot Spring Act increase environmental regulations; social acceptance and environmental limits become core barriers.
Government leads research and exploration under the New Energy and Industrial Technology Development Organization (NEDO); policy support is concentrated on geological surveys.
1997-2000s
Chart: 
 | 40 | 130 | 230 | 500 | 530 | 520 | 520 | 1500
1970
1980
1990
1995
2000
2010
2024
2035 (Projected)
Japan’s 1990-95 surge reflects the last wave of large plants from its subsidy-driven 1980s pipeline, before permitting and community land-use constraints stalled further expansion.
Incentives rise after 2012, but land-use limits, community resistance, and slow permitting keep capacity flat.
Japan’s new R&D and permitting reforms target risk, speed, and consensus to enable 2035 scale-up.

## Slide 66: Geothermal Power Finance

## Slide 67
Energy Access, Development Needs, and Geothermal’s Role
Developing countries face ongoing challenges in achieving affordable, reliable, and sustainable energy, limiting industrial growth and economic development. Expanding infrastructure, diversifying supply sources and transitioning to low-carbon systems are key priorities.
Geothermal energy offers 24/7, low-cost, carbon-free baseload power, but deployment is constrained by high upfront costs, geological uncertainty, and limited technical capacity.
Technological Cost Reductions in Binary and Flash Geothermal
Both binary and flash geothermal technologies are achieving major cost declines through faster drilling, material efficiency, and plant scaling. Advanced binary systems can reduce CapEx by up to 30%, while flash systems — with monobore wells, 4x faster drilling, and 100 MW plants — cut per-MW costs and timelines dramatically. Such innovations expand geothermal’s geographic reach and competitiveness in emerging economies.
Risk Mitigation, Policy Support, and Financing Models
Early-stage uncertainty remains the key investment barrier. Global programs like World Bank’s ESMAP show that government-led exploration, cost-shared drilling, and fiscal incentives attract private capital. De-risking tools such as GRIF, insurance, and grants, combined with oil & gas expertise in drilling and modular design, could reduce next-gen geothermal costs by up to 80%, achieving ~$40/MWh, competitive with nuclear and PV + storage.
Competitiveness and Industry Spillovers
Geothermal’s LCOEs ($61-$102/MWh) are cheaper than coal and gas and about half the cost of nuclear, with oil & gas technology spillovers accelerating commercialization.
Fervo Energy leverages horizontal drilling and rapid well completion to attract major equity and debt financing, including a $300 million Series E ahead of a planned IPO, advancing geothermal toward commercial bankability and a trillion-dollar clean energy market.
Key messages
Finance

## Slide 68: Conventional geothermal construction costs projected to continue to decline, driven by tech improvements and efficiency gains
Observations
Binary geothermal sees cost reductions through both subsurface and surface improvements.
Conservative: Learning is incremental with limited drilling gains.
Moderate: Introduces faster drilling, reduced material use, and moderate plant scaling (to 40 MW), supported by a 13% learning rate.
Advanced: Accelerates progress with major drilling breakthroughs, larger plants, and advanced surface system efficiency, resulting in up to 30% learning-driven CapEx reduction. As a result, binary systems become increasingly viable across a wider range of geographies.
Flash geothermal sees cost reductions driven by drilling efficiency and plant scale.
Conservative: Only modest gains are expected, with minor improvements in drilling speed and bit durability.
Moderate: Assumes faster drilling, fewer casing stages, and streamlined permitting, leading to more meaningful CapEx savings.
Advanced: Transformational gains, such as 4x faster drilling, monobore well designs, and deployment of 100 MW plants unlock significant cost reductions by cutting timelines, material use, and per-MW development cost.
Cost of construction for both flash and binary geothermal are expected to decline from 2022 to 2050 under conservative to advanced scenarios
Finance
Chart: 
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
 | 2574.3766 | 2372.261 | 2181.5636 | 2001.184 | 1830.1658 | 1667.6734 | 1512.9726 | 1365.4158 | 1224.4287 | 1089.5005 | 960.1745 | 836.0417 | 716.7338 | 601.9185 | 576.3895 | 550.9881 | 525.7137 | 500.5657 | 475.5434 | 450.6462 | 425.8735 | 401.2247 | 376.6991 | 352.2962 | 328.0153 | 303.8557 | 279.817 | 255.8985 | 232.0995
 | 2574.3766 | 2457.7037 | 2350.4021 | 2251.1191 | 2158.7691 | 2072.4686 | 1991.4894 | 1915.2246 | 1843.1633 | 1774.8718 | 1709.9787 | 1648.1638 | 1589.1492 | 1532.6922 | 1502.5633 | 1472.585 | 1442.7567 | 1413.0775 | 1383.5467 | 1354.1635 | 1324.9273 | 1295.8372 | 1266.8926 | 1238.0927 | 1209.4368 | 1180.9242 | 1152.5541 | 1124.3259 | 1096.2389
 | 2574.3766 | 2539.0515 | 2503.903 | 2468.9303 | 2434.1324 | 2399.5085 | 2365.0578 | 2330.7793 | 2296.6721 | 2262.7356 | 2228.9687 | 2195.3706 | 2161.9405 | 2128.6776 | 2095.581 | 2062.6498 | 2029.8834 | 1997.2807 | 1964.8411 | 1932.5637 | 1900.4476 | 1868.4922 | 1836.6965 | 1805.0598 | 1773.5813 | 1742.2601 | 1711.0956 | 1680.0869 | 1649.2333
 | 4933.8723 | 4584.1193 | 4262.0889 | 3964.149 | 3687.3036 | 3429.0567 | 3187.3091 | 2960.2813 | 2746.4531 | 2544.5169 | 2353.3407 | 2171.9392 | 1999.4498 | 1835.1139 | 1803.4189 | 1771.8824 | 1740.5035 | 1709.2815 | 1678.2157 | 1647.3051 | 1616.5492 | 1585.947 | 1555.4978 | 1525.2008 | 1495.0554 | 1465.0606 | 1435.2159 | 1405.5204 | 1375.9733
 | 4933.8723 | 4723.3502 | 4535.9417 | 4367.2459 | 4213.9865 | 4073.6615 | 3944.32 | 3824.4126 | 3712.6896 | 3608.1292 | 3509.8856 | 3417.2515 | 3329.6297 | 3246.5114 | 3207.8134 | 3169.3089 | 3130.9969 | 3092.8765 | 3054.9467 | 3017.2066 | 2979.6551 | 2942.2914 | 2905.1145 | 2868.1235 | 2831.3175 | 2794.6955 | 2758.2566 | 2721.9998 | 2685.9244
 | 4933.8723 | 4886.7497 | 4839.8627 | 4793.2102 | 4746.7909 | 4700.6037 | 4654.6475 | 4608.921 | 4563.4232 | 4518.1529 | 4473.1089 | 4428.2901 | 4383.6954 | 4339.3238 | 4295.1739 | 4251.2448 | 4207.5354 | 4164.0445 | 4120.771 | 4077.714 | 4034.8722 | 3992.2446 | 3949.8301 | 3907.6278 | 3865.6364 | 3823.855 | 3782.2825 | 3740.9179 | 3699.7601
7,000
9,000
2040
2030
2045
2025
2050
10,000
0
5,500
6,000
6,500
9,500
7,500
8,000
8,500
2035
4,871
5,735
6,288
6,015
7,325
8,339
Flash (advanced)
Flash (moderate)
Flash (conservative)
Binary (advanced)
Binary (moderate)
Binary (conservative)
Estimated construction costs, US$/kW

## Slide 69: Next-gen tech is riskier and more equity-heavy, while proven technologies attract more debt through traditional project finance
Finance
Technology
Fervo, U.S. | Rift Valley, Kenya | Sarulla, Indonesia
Next-gen geothermal (EGS, advanced drilling, and fiber optics) | Conventional geothermal (mixture of flash and binary) | Conventional geothermal (flash steam)
Moderate technology risk: While EGS has been de-risked by field pilots like Project Red (TRL 9 in 2024), scaling commercial deployment still carries subsurface and reservoir uncertainty. Medium resource risk: EGS creates its own reservoir, which avoids natural resource uncertainty but introduces engineered subsurface complexity. | Low technology risk: Uses proven conventional technology. High resource risk: In early phases, especially in unexplored or underexplored zones, but borne by the public sector through Kenya’s state-owned GDC, which validates the resource before handing it off to private IPPs. | Low technology risk: Uses proven conventional technology. Low resource risk: Located in a well-characterized field with extensive drilling and historical data.
Long-term PPAs with utilities or corporate, pilot to commercial-scale model. | Utility offtake with donor-backed pricing. | IPP model with 30-year PPA under feed-in tariff, backed by political risk guarantees.
More equity: Early-stage EGS projects are equity-heavy, backed by VC/PE (e.g., Breakthrough Energy, Capricorn). Transitioning toward project finance as risk perception declines. | More debt: GDC-led exploration allows donor-backed debt instruments (e.g., AfDB, AFD, World Bank); equity participation from KenGen and private IPP. | More debt: Classic project finance with concessional and commercial debt (ADB, JBIC, CTF); equity from Medco, Itochu, Kyushu Electric, INPEX.
Frontier tech, higher risk
Proven tech, lower risk
Risk profile
Revenue model
Financing instrument and stakeholder

## Slide 70: Domestic policy support that aims to de-risk geothermal development in the United States is preserved under the Trump administration
IRA, BIL, and OBBBA enhance bankability through tax credits, direct pay, and federal loan support
Emerging risk-sharing programs and public-private partnerships lower risk and crowd in private capital
Finance
Policy | Type of Support | Key Provisions for Geothermal | Impact/Intent
Inflation Reduction Act (IRA) (2022) | Tax credits that improve project economics | 30% ITC or PTC eligibility; direct pay (for tax-exempt entities); transferability of credits; adders (+10% energy communities; +10% domestic content, where met) | First-time inclusion of geothermal; enables monetization of credits and broader investor participation.
Bipartisan Infrastructure Law (BIL) (2022) | Federal R&D, grants, and data to reduce early-stage risk | DOE Geothermal Technologies Office funding; EGS pilot demonstrations; USGS Earth MRI mapping/data; authority for DOE to run field pilots | Focused on early-stage risk reduction: funding exploration, subsurface data, and demonstration wells; supports cost-shared projects to crowd-in private capital
One Big Beautiful Bill Act (OBBBA) (2025) | Credit design plus phase-out policy and domestic supply guardrails | Tightens FEOC rules; strengthens/clarifies domestic content; retains geothermal ITC/PTC runway through 2033 with gradual phaseout; accelerates phaseouts for mature tech (solar/wind) | Protects geothermal’s long credit runway while phasing out mature renewables; encourages domestic supply-chain alignment
Public funds absorb exploration risk.
Partnerships demonstrate viability.
Tax incentives unlock private deployment.
Private Investment Incentivized by Tax Credits
Shared Risk & Market Demonstration
Early-Stage Public Investment
State and local utility partnerships (e.g., Utah FORGE, Calpine DOE pilot) demonstrate technical viability.
Cost-shared drilling grants (DOE, USGS Earth MRI) and federal data programs reduce exploration risk and resource uncertainty.
IRA/OBBBA ITC/PTC and transferability attract developers and tax-equity investors once technical risk is reduced.
Geothermal projects benefit most from policies targeting exploration risk and long payback timelines — areas where solar and wind no longer require subsidy.

## Slide 71: Investors double down on Fervo with equity and debt funding to commercially deploy EGS; total $1.69B raised to date
As Fervo achieved scale-up milestones, the company consistently attracted capital
Fervo lands $206 million in project financing in 2025 (US$M)
Observations
Fervo confidentially filed to go public on January 22, 2026. It would be the first EGS startup to IPO in the United States.
Breakthrough Energy Ventures is a longtime investor that has consistently invested in new rounds, demonstrating conviction in Fervo’s technology.
With technological breakthroughs like horizontal drilling and record-breaking drilling times, Fervo has consistently raised larger rounds and accessed debt financing.
Fervo’s ability to attract project financing is a critical hurdle for a hard tech investment and key to unlocking widespread commercial deployment.
Case study: Fervo Energy
XRL upsized non-dilutive bridge debt financing from $100M to $145.6M.
Breakthrough Energy Catalyst invests $100M of preferred equity.
Mercuria upsized its term loan by $60M for a total of $100M.
2021 – Series B: $28M, led by Capricorn Investment Group
2024 – Series D: $244M, led by Devon Energy
2023 – Series C: $138M, led by DCVC
2019 – Series A: $11M, led by Breakthrough Energy
2024 – Debt: $220M, term loan, letters of credit, project bridge loan
2024 – Series D extension: $135M, corporate equity
2025 – Project finance: $206M, preferred equity, bridge and term loan
2025 – Series E: $460M, led by B Capital Group
January 2026 – Announced IPO
2017 – Grant: Undisclosed, from Stanford TomKat program

## Slide 72: Private and public sector financing was essential for Kenya’s Olkaria III geothermal project, leading to a 16% equity IRR
Observations
First privately financed geothermal project in Africa from field to operations and maintenance
Project returns:
  Equity IRR: 16%
  IRR without DFI support:10%
Factors that led to a 16% IRR:
  Low-cost and long-term debt from DFI
  Donation of wells from KenGen, Kenyan public electric company, saved Ormat $24M, leading to Ormat’s equity IRR increasing from 13% to 16%.
  Refinancing of Ormat equity supported IRR, but delays prevented the project from achieving higher returns.
Project outcomes:
  Estimated 13% lower LCOE and 31% decrease in costs for each geothermal plant
  Reduced Kenya’s emissions by an estimated 2 to 4%
Case study: Olkaria
Olkaria III Geothermal Plant
OPIC Senior Debt $310M
MIGA Risk $55M
DEG + KFW Subordinated $40M
Co-lenders Subordinated $65M
Ormat Project Developer
KPLC Off-taker
Stakeholder | Details
Olkaria III | 110 MW geothermal project in Kenya
Ormat | Experienced project developer and key equity, was a stakeholder at the beginning of the project.
Kenya Power and Lighting Company (KPLC) | Signed 20-year PPA in 1998, at the start of the project.
DFI Banks: DEG and KFW, co-lenders | DEG and KFW Development Bank refinanced Ormat’s equity and provided low-cost, long-term debt.
OPIC | Provided a 19-year senior loan in three tranches. The long-term debt was essential and was OPIC’s first geothermal investment.
MIGA | Multilateral Investment Guarantee Agency (MIGA) provided political risk insurance for equity stakeholder Ormat (2% premium).
1998 – Ormat: $40M equity financing
2009 – DEG & KFW: Refinanced equity for $105M loan
2013 – Olkaria III: Full plant commissioned at 84 MW
2012 – OPIC: Senior loan of $310M
2006 – Ormat: $150M equity financing
2014 – Olkaria III: Full plant commissioned at 110 MW
2016 – Olkaria III: Ormat expansion to 134 MW
1996 – Pre-project: Tender for geothermal
Project Timeline
Olkaria III Project Stakeholders

## Slide 73: Indonesia's Sarulla project's financing success proves bankability of conventional geothermal technology
Case Study: Sarulla Indonesia
Sarulla Project Capital Stack
Observations
Sarulla is one of the largest conventional geothermal projects in the world, financed for $1.6B with a combination of senior debt, mezzanine debt, and sponsor equity.
Mezz lenders paid pari-passu in the event of default due to termination fee of the energy sales contract equaling the senior and mezz debt.
Guarantees: To de-risk the project, the Indonesian government offered a guarantee on the project. JBIC also agreed to a political risk guarantee for the commercial banks if the government did not follow through.
Case study: Sarulla
Chart: 
 | 78
 | 492
 | 250
 | 328
 | 20
 | 80
 | 352
20
Capital Stack
Sponsor Equity
Clean Technology Fund
Canadian Climate fund
Commercial Banks
ADB
JBIC
Pre-operating Revenue
1,600
Sponsors include Medco, Itochu, Kyush, Ormat
Mezzanine Debt
Commercial banks include MUFG, ING, Mizuho, NAB, SMBC, Société Generale
Location: North Sumatra, Indonesia
Details: A conventional geothermal project, built out in three phases across three 110 MW plants for a total of 330 MW.
Construction: Started in 2014 with target completion in February 2018. The third plant was completed a few months after the target date in May 2018.
Offtake Agreement: Signed an energy sales contract with PT Perusahaan Listrik, a state-owned utility, for 30 years of electricity offtake.
Senior Debt
Commercial Banks Senior Debt
Sarulla Ops. Ltd, Geothermal plant
JBIC Senior Debt
ADB Senior Debt
Govt of Indonesia, Guarantee
Medco. 19%, Equity
Inpex 18.25%, Equity
Itochu 25%, Equity
Kyuden 25%, Equity
Ormat 12.75%, Equity
Mezzanine Debt
PLN Off-taker
Pertamina

## Slide 74: Oil & gas expertise transfer can significantly reduce subsurface drilling costs, the largest component of geothermal construction
Next-gen geothermal construction costs are projected to drop ~60-80% by 2050 …
… driven by oil & gas expertise transfer; in the U.S., this can reduce costs by up to 80% of current baseline
Observations
Next-gen geothermal faces high upfront costs, with subsurface drilling accounting for 60 to 80% of total expenses.
Oil & gas expertise in drilling, supply chains, and modular plant design is key to reducing costs, driven by improved site planning, technology spillovers, economies of scale, and surface facility optimization, all areas where O&G capabilities directly apply.
In a low-cost scenario, effective O&G knowledge transfer could cut costs by up to 80%; the medium-cost case assumes more gradual progress and implementation barriers.
Finance: Oil & gas transfer
Chart: 
 | 100 | 93.3333 | 63.3333 | 41.3333 | 27.3333 | 20 | 20
 | 6.6667 | 30 | 22 | 14 | 7.3333
100%
Baseline Cost
7%
Evaluation & Planning
30%
Research
22%
Spillover
14%
Economies of Scale
7%
Surface Facilities
20%
Reduced Cost
14,000 US$/kW
Research and spillover from oil & gas would enhance drilling speed, reliability, and equipment use.
Improvement of site targeting would reduce drilling failures.
Reduction potential comes from modular, standardized plant design.
Chart: 
 | 14000 | 9500 | 7500 | 6500 | 6000 | 5700
 | 14000 | 7000 | 4000 | 3000 | 2500 | 2300
2025
7,500
4,000
2035
2050
Next-gen geothermal construction costs, US$/kW
Medium-Cost Case
Low-Cost Case
Breakdown of geothermal construction potential cost reduction, %

## Slide 75: Geothermal LCOE is on track to compete with hydro, nuclear, and solar PV + storage, through O&G transfer and policy-led de-risking
Observations
Next-gen geothermal costs could drop significantly, enabling power generation at ~US$40/MWh. Both conventional and next-gen geothermal LCOE are on par with nuclear and PV + storage.
Oil & gas expertise in advanced drilling, subsurface exploration, and modular plant design is accelerating cost declines. Solar PV, batteries, and EVs saw similar cost declines through industry spillover and rapid deployment.
Policy support and de-risking tools (e.g., GRIF, insurance, grants) reduce early-stage risk, improve bankability, and crowd in private capital through blended finance and PPPs.
Estimated LCOE (levelized cost of energy) under NREL Advanced scenario, US$/MWh
Finance: Oil & gas transfer
Chart: 
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
 | 71.2824 | 69.6215 | 68.049 | 66.5566 | 65.1367 | 63.783 | 62.4896 | 61.2516 | 60.0646 | 58.9245 | 57.8278 | 56.7714 | 55.7524 | 54.7683 | 54.5704 | 54.3735 | 54.1775 | 53.9826 | 53.7886 | 53.5956 | 53.4035 | 53.2125 | 53.0223 | 52.8332 | 52.6449 | 52.4576 | 52.2713 | 52.0859 | 51.9014
 | 105.6428 | 92.775 | 83.5502 | 76.4939 | 70.8468 | 66.1741 | 62.2071 | 58.7699 | 55.742 | 53.038 | 50.5951 | 48.3663 | 46.3157 | 44.4152 | 44.261 | 44.1077 | 43.9551 | 43.8033 | 43.6522 | 43.5019 | 43.3524 | 43.2036 | 43.0555 | 42.9082 | 42.7616 | 42.6158 | 42.4707 | 42.3263 | 42.1826
 | 68.9255 | 68.9255 | 68.9255 | 68.9255 | 68.9255 | 68.9255 | 68.9255 | 68.9255 | 68.9255 | 66.943 | 64.9604 | 62.9778 | 60.9953 | 59.0127 | 57.4267 | 55.8406 | 54.2545 | 52.6685 | 51.0824 | 50.2894 | 49.4964 | 48.7034 | 47.9103 | 47.1173 | 46.7208 | 46.3243 | 45.9278 | 45.5312 | 45.1347
 | 78.2475 | 78.2475 | 78.2475 | 78.2475 | 77.7901 | 77.3175 | 76.8601 | 76.3875 | 75.9302 | 73.8042 | 73.4078 | 72.9962 | 72.5998 | 72.2034 | 71.807 | 71.4106 | 70.999 | 70.6026 | 70.2062 | 67.4388 | 67.4388 | 67.4388 | 67.4388 | 67.4388 | 67.4388 | 67.4388 | 67.4388 | 67.4388 | 67.4388
 | 87.7439 | 88.6678 | 81.3381 | 74.1573 | 70.7099 | 67.3322 | 64.0217 | 60.7762 | 57.5945 | 54.9084 | 52.2738 | 49.6888 | 47.1529 | 44.6645 | 44.1811 | 43.7004 | 43.2222 | 42.7465 | 42.2731 | 41.8024 | 41.3343 | 40.8684 | 40.4046 | 39.9435 | 39.4847 | 39.0283 | 38.5739 | 38.1221 | 37.6728
0
10
30
40
50
60
70
80
90
100
110
20
45
38
Geothermal - Conventional Flash
Geothermal - Deep EGS Flash
Nuclear - Large Scale
Hydropower
Solar - Utility PV + Storage
67
Advanced projections suggest next-gen EGS may achieve lower costs than conventional geothermal and be competitive with nuclear and PV + storage as early as 2029.

## Slide 76: Modern cumulative investment in geothermal expected to reach $1 trillion a decade before nuclear fission technology
Finance
Chart: 
 | 9.7 | 21 | 31.9 | 48.1 | 73.3 | 109.9 | 159.6 | 219.1 | 283.3 | 343 | 396.3 | 441.8 | 480 | 510.7 | 537.4 | 559.6 | 577.1 | 590.5 | 600.5 | 607.6 | 612.7 | 616.6 | 620 | 623.4 | 626.9 | 630.3
 | 2.1 | 4.2 | 7.4 | 11.8 | 16.9 | 22.1 | 27.2 | 32.8 | 38.5 | 44.2 | 49.5 | 53.9 | 57.8 | 61 | 63.9 | 66.5 | 69.1 | 71.7 | 74.3 | 76.6 | 78.7 | 80.6 | 82.5 | 83.7 | 84.3 | 84.3
 | 14.6 | 15.4 | 17 | 25.7 | 49.5 | 100.7 | 184.1 | 296.3 | 425.6 | 558.8 | 690.9 | 825 | 966.5 | 1110 | 1248.7 | 1372.8 | 1483.9 | 1577.4 | 1657.7 | 1726.9 | 1792.8 | 1854.8 | 1916.6 | 1977.9 | 2039.5 | 2101
2038
2025
2028
2029
2030
2031
2032
2033
2034
2035
2036
2037
2026
2039
2040
2041
2042
2043
2044
2045
2046
2047
2048
2049
2050
2027
Electricty Only
Combined Heat and Power
Industrial Heat
Cumulative Investment Estimate of Geothermal Energy by Application (US$B)
$1T by 2034
Chart: 
 | 5 | 9 | 13 | 17 | 21 | 25 | 57.25 | 89.5 | 121.75 | 154 | 186.25 | 218.5 | 250.75 | 283 | 315.25 | 347.5 | 379.75 | 412 | 444.25 | 476.5 | 508.75 | 541 | 573.25 | 605.5 | 637.75 | 670
 | 60 | 57 | 54 | 51 | 48 | 45 | 92.75 | 140.5 | 188.25 | 236 | 283.75 | 331.5 | 379.25 | 427 | 474.75 | 522.5 | 570.25 | 618 | 665.75 | 713.5 | 761.25 | 809 | 856.75 | 904.5 | 952.25 | 1000
2038
2025
2028
2029
2030
2031
2032
2033
2034
2035
2036
2037
2026
2039
2040
2041
2042
2043
2044
2045
2046
2047
2048
2049
2050
2027
$1T by 2042
Cumulative Investment Estimate of Nuclear Fission Energy by Application (US$B)
Large Reactors
SMRs
Nuclear innovations pushing investor growth, but industry still facing setbacks
Geothermal is emerging and avoids contentious drawbacks of nuclear power
1
Still facing regulatory and safety concerns from the public
2
Low skill transferability from other energy technologies
Applications limited to power generation
3
4
Subject to price shocks of mineral fuels like uranium
5
More expensive to operate
6
No known alternative options for revenue generation
SMRs remain early in development
7
8
Relatively established technology
1
Viewed as a safer baseload power alternative than nuclear
2
Oil and gas engagement certifies large reserve of workforce with applicable knowledge
Applicable to heating and cooling plus electricity
3
4
Immune to price shocks of commodities like uranium
5
Less expensive to operate
6
Potential for critical mineral extraction, providing alternate revenue stream
Technology block generally limited to drilling
7
8
Emerging technology
Potential reasons stunting projections
Potential reasons favoring growth

## Slide 77: Geothermal requires large upfront investment but delivers stable returns and low O&M costs over a 30- to 50-year project life
Observations
Capital Intensity: Geothermal requires the largest upfront investment, with drilling and resource confirmation consuming 60-70% of total CapEx before revenue. Solar and wind projects front-load only ~30%.
Timeline: Development and payback extend across 7-10 years before COD, compared with 2-3 years for solar and wind, 5-7 years for SMRs, and 10-15 years for traditional nuclear.
Returns: Once operational, geothermal delivers steady baseload output for 30-50 years with capacity factors near 85%, far exceeding solar’s and wind’s 20-25 year lifetime and 30-45% capacity factors.
Financing Implications: Longer horizons demand blended finance and government risk sharing, but geothermal’s stable post-COD cash flows make it attractive to infrastructure and pension investors seeking duration.
CapEx, OpEx, and project life ranges for a 100 MW power plant
Finance
Chart: 
 | 80 | 130 | 450 | 400 | 900
 | 40 | 40 | 200 | 300 | 300
Solar
170
650
Geothermal
700
SMR Nuclear
1200
Traditional Nuclear
120
Onshore Wind
CapEx ($M)
OpEx ($M)
Chart: 
 | 1.5 | 3 | 8 | 10 | 12
 | 1 | 2 | 4 | 5 | 6
5
12
15
18
3
Project Lifespan
Chart: 
 | 25 | 20 | 30 | 60 | 60
 | 5 | 5 | 20 | 20
25
50
80
30

## Slide 78: Geothermal Power Deployment

## Slide 79
Geothermal to Meet Growing Energy Demand
U.S. data centers could add 35 to 65 GW by 2030, far exceeding incremental nuclear (~4 GW) and grid-connected geothermal (6 to 8 GW). Behind-the-meter geothermal (~15 GW) can supply data centers directly, bypassing grid and permitting constraints.
Deployment depends on drilling and permitting innovation and applying conventional geothermal, O&G, and geospatial techniques to reduce LCOE.
Industrial and Corporate Drivers
Tech giants (Microsoft, Google, Meta, Amazon) are accelerating deployment through PPAs and site development.
Fervo Energy leverages horizontal drilling, advanced data analytics, and O&G expertise to speed deployment and increase resource efficiency, with corporate demand and energy security driving growth.
Workforce and Cross-Sector Capabilities
Expanding the geothermal workforce via reskilling, O&G talent transfer, and digital automation is critical.
Global geothermal employment grew from 96,000 to 196,000 (2021) but remains small compared with 12.4 million in O&G (2023); the U.S. and EU must expand training to stay competitive with China.
Industrial Decarbonization Potential
Co-locating geothermal with Indonesia’s nickel reserves (40% of global geothermal, 61% of EV nickel) can provide clean heat for refining, cutting upstream emissions and lowering EV lifecycle carbon intensity.
Pilot regions like Sulawesi, Sumatra, and Java can combine industrial decarbonization with local economic and labor development.
Key messages
Deployment

## Slide 80: Geothermal offers reliable, low-footprint baseload energy, though costs and longer timelines may constrain scale-up
Deployment: Baseload power
 | Geothermal | Hydro | Nuclear | Wind | Solar
Resource availability & scalability | Scalable in select locations, high upfront costs, deep drilling needed | Limited scalability due to size (smaller hydro projects more feasible vs. larger dams) | Limited scalability due to high investments and long construction times (SMR easier to scale as modular alternative) | Highly scalable anywhere due to modular deployment | Highly scalable anywhere, due to modular deployment
Costs (LCOE) | $66-$109/MWh | $47/MWh | $141-$228/MWh (new plants) | $37-$86/MWh (onshore), $70-$157/MWh (offshore) | $38-$78/MWh (utility scale)
Capacity factor | 70-90% | Variable (global avg. is around 44%) | ~90% | 38-47% for onshore, 41-50% for offshore | 25-33% for standalone systems
Reliability | Reliable baseload resources | Baseload resource only with reservoir storage | Reliable baseload resources | Intermittent, variable output | Intermittent, energy storage required
Setup time | Moderate timeline, typically 3-5 years | Long timeline, often 5-10 years or more | Longest timeline, often 10+ years due to regulatory & construction complexities | Relatively quick to deploy, often within 1-2 years | Relatively quick to deploy, often within 1-2 years
Technology readiness | Established but room for significant advancements (e.g., EGS) | Mature, limited room for improvement | Established but challenges in cost reduction & public accept. | Mature, ongoing innovations improving efficiency & reducing costs | Mature, ongoing innovations improving efficiency & reducing costs
Land-use footprint efficiency (km2/TWh/year) | 7.5 | 54.0 | 2.4 | 72.1 | 36.9
Despite its higher LCOE and longer development timeline — especially compared to wind and solar — geothermal remains a highly competitive energy source in regions with significant geological activity, offering high reliability and efficient land use.
More desirable
Moderate
More challenging

## Slide 81: Nuclear and geothermal both offer firm, low-carbon power but face distinct financing, technical, and deployment challenges
Non-exhaustive overview of opportunities and challenges
Deployment: Baseload power
Nuclear
Geothermal
Opportunities
Challenges
Provide firm, dispatchable, low-carbon baseload power
EGSs expand resource base
Public resistance around safety, accidents, waste
Co-benefits: heating, desalination, minerals
Long asset lifetimes (with upgrades)
Long permitting and siting processes compared to solar and wind
Potential for distributed/behind-the-meter deployment near load centers
Limited viable siting options (cooling water)
Seismicity concerns from EGS
SMRs with shorter construction timelines
NRC approval cycles drive 10- to 15-year timelines
Smaller project scale, bankability concerns
High upfront CapEx, financing hurdles (risk for investors)
Resource risk and drilling uncertainty
Integration with hydrogen/ammonia production
7- to 10-year development cycle
Waste management and decommissioning costs

## Slide 82: Geothermal power is bringing on new U.S. projects this decade while nuclear holds greater capacity, but the gap is narrowing
Observations
Geothermal
Today’s U.S. geothermal fleet is small (~ 4 MW), but geothermal is bringing new projects online this decade, which drives faster near-term growth.
Future scale depends on technology progress, lower drilling costs, and access to project finance.
As next-generation geothermal expands, the gap with nuclear capacity begins to narrow.
Nuclear
Nuclear holds higher total capacity because of its large legacy fleet.
Near-term nuclear growth is limited, since only one restart is expected before 2030.
New nuclear capacity depends on long development cycles for SMRs and large reactors.
Nuclear’s long-term expansion occurs later in the 2030s, once early SMR projects move into construction.
Installed capacity scenarios for traditional geothermal, next-gen geothermal, existing nuclear, and new nuclear builds in the United States, GW
Deployment: Baseload power
Chart: 
| 2025 | 2028 | 2030 | 2035 | 2040
 | 3.9 | 5 | 6 | 15 | 25
 | 3.9 | 5 | 8 | 25 | 40
 | 3.9 | 5 | 10 | 40 | 60
 | 97 | 97.7 | 94 | 94 | 92
 | 97 | 97.7 | 105 | 115 | 150
 | 97 | 97.7 | 105 | 135 | 210
Geothermal (High)
GW
Geothermal (High)
Nuclear (Low)
Nuclear (Mid)
Nuclear (High)
Geothermal (Mid)
+55%
+926%
Duane Arnold Nuclear Center (Iowa, 2028 target) (600 MW)
First SMRs expected in the early 2030s: TVA’s planned BWRX-300 (300 MW) and Holtec’s 300 MW SMRs at the Palisades in Michigan
Fervo Cape Station (Utah, 2028 target) (400 MW)
DOE target: 35 GW of new capacity by 2035 and 15 GW per year by 2040

## Slide 83: Increasing U.S. energy demand, largely driven by data centers, requires increased baseload supply of power
Projected growth in power demand from U.S. data centers
Incremental firm capacity by 2030
Observations
Data centers could add more than 35 to 65 GW of firm power demand by 2030 in the U.S., equivalent to a large fraction of today’s existing nuclear fleet.
Nuclear restarts and SMRs provide only ~4 GW incremental capacity, which is meaningful but insufficient against projected demand growth.
Grid-connected geothermal adds 6 to 8 GW, but that is also insufficient against projected demand.
Behind-the-meter geothermal (~15 GW) could directly supply data centers, bypassing grid constraints and permitting bottlenecks.
Innovation in drilling and permitting will determine whether geothermal can scale fast enough to complement nuclear in delivering zero-carbon baseload.
Deployment: Data centers
Chart: 
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
 | 5.7078 | 6.8493 | 7.9909 | 9.1324 | 11.4155 | 13.6986 | 17.1233 | 20.5479 | 25.1142 | 29.6804 | 34.2466
 | 66.21
 | 37.1005
High case: +65 GW
Low case: +35 GW
LBL Low Demand 2030 (GW)
Historic Demand (GW)
LBL High Demand 2030 (GW)
Chart: 
 | 4 | 6 | 15
 | 2
Nuclear
Geothermal
Next-Gen Geothermal
New Available GW
8
Nuclear restarts + early SMRs
Grid upside
Behind the meter

## Slide 84: Untapped geothermal potential is uniquely positioned to meet the growing demand for data center power
Observations
Geothermal provides reliable, the clean baseload power required for data centers.
Existing technologies for conventional geothermal, oil and gas drilling, and mineral and geospatial exploration can be modified and improved to optimize geothermal development and decrease LCOE.
Emerging and frontier geothermal technologies will find innovative, cost-effective ways to continue to reduce LCOE.
Geothermal has other potential uses for cooling and water management for data centers.
Potential for Build-to-Suit Data Center Solutions
  Declining LCOE for Next-Gen Geothermal
$75 per MWh for EGS FOAK (unsubsidized) and $120-$150 MWh for ACL FOAK.
McKinsey anticipates a decrease to $45-$75 per MWh for Nth of a kind next-gen geothermal.
Behind the meter solution and decrease energy costs by avoiding transmission and grid interconnection costs.
NREL and the DOE are exploring Cold Underground Thermal Energy Storage to support data center cooling. Geothermal can also support cooling water efficiencies..
Geothermal provides a clean energy baseload resource.
Nuclear is far more capital-intensive and requires far more development time.
Solar and wind are intermittent renewable resources that are not ideal for baseload power.
Geothermal offers 24/7 power that is ideal for baseload power and grid stability.
Offers a high-capacity factor between 70 and 90%.
Global estimated potential of 4,000 PWh/year if next-gen geothermal can unlock resources.
Reliable Baseload Power
  Clean Energy
Deployment: Data centers

## Slide 85: Microsoft, Google, and Meta lead geothermal power investment for data centers, while Amazon sticks to geothermal heating & cooling
Observations
Geothermal strategies vary: Microsoft and Meta target utility-scale, always-on geothermal for data centers; Google combines PPAs with EGS investments; and Amazon focuses on on-site efficiency rather than baseload generation.
Location choices reflect resource and technology maturity: Microsoft and Google invest in established geothermal regions, while Meta uses closed-loop players’ methods to unlock non-traditional sites.
Deployment: Data centers
Microsoft’s major capital investments, i.e., $1 billion project in Kenya with an initial capacity of 100 MW+, geothermal heating and cooling in its Redmond campus, emphasizing large-scale generation in high-potential regions and operational energy efficiency.
Google leverages geothermal energy through power purchase agreements and investments in enhanced geothermal systems, including 115 MW in Nevada and 10 MW in Taiwan, focusing on baseload clean power, geographic expansion, and reducing regulatory barriers.
Amazon primarily employs geothermal heat pumps for heating and cooling in facilities, such as its fulfillment center in Japan, focusing on on-site energy efficiency and renewable energy matching rather than utility-scale power generation.
Meta is developing a 150 MW geothermal plant in New Mexico using advanced geothermal methods to access non-traditional sites, with a focus on scalable, always-on power for data centers and AI workloads.
Microsoft
Google
Meta
Amazon
Microsoft & G42: $1B Digital Initiative in Kenya incl. Geothermal
Microsoft Opens Thermal Energy Center
10-Year Agreement for Geothermal Power Station at Te Huka
May 2023
March 2021
May 2024
Google Signs 10 MW Geothermal Energy Deal in Taiwan
Google Secures 115 MW Geothermal plant in Nevada
Google Unlocks Geothermal with Fervo EGS systems
April 2025
June 2024
October 2024
Meta Touts $1B Investment in Geothermal for Data Centers
Meta Signs Agreement with Sage Energy
June 2025
April 2024
Amazon Unveils Geothermal, Solar- Powered Center in Japan
June 2025
Power
Power
Power
Heating & Cooling

## Slide 86: Google signs first corporate geothermal agreement in Taiwan to power data centers and expand across the Asia-Pacific region
Google and Baseload Capital partner to develop 10 MW of geothermal in Taiwan
Several tailwinds make Taiwan the ideal location for geothermal development
Case study: Taiwan
Google plans to accelerate geothermal across the Asia-Pacific region and utilize its learnings from the Taiwan project.
It partnered with the University of Newcastle to research geothermal energy potential in Australia.
Baseload Capital is a global geothermal developer. Baseload Power Taiwan, a subsidiary, has explored geothermal resources since 2019.
Baseload Power Taiwan is the only geothermal developer in Taiwan. It actively partners with the government to implement regulatory frameworks for geothermal.
Google demonstrated its commitment to geothermal with an equity investment in Baseload Capital.
Net-Zero Commitment | Taiwan aims to be net zero by 2050
Taiwan’s 2023 energy mix was 35% coal, 34% oil, 24% natural gas, 4% nuclear, <2% other renewables, <2% other sources.
Proximity to Pacific Rim | Located near high-potential resources
Taiwan is located along the Pacific Rim, known for its volcanic activity. A 2016 study found that geothermal resources could be up to 160 GWe.
Geothermal Targets | Taiwan targets 6 GW of geothermal
Taiwan established incremental geothermal targets: 20 MW by 2025, 200 MW by 2030, 2 GW by 2040, and 6 GW of geothermal by 2050
Technology Hub | Taiwan as a center for AI Infrastructure
Taiwan announced its 10 Major AI Infrastructure Projects, which is expected to generate $520 billion-plus in economic value.

## Slide 87: XGS signs its first commercial deal, partnering with Meta to develop 150 MW with zero operating water in New Mexico by 2029
Meta and XGS partner to develop a 150 MW geothermal plant to power data centers in New Mexico
New Mexico sets up to unlock next-generation geothermal potential
Case study: Meta – XGS
Meta is seeking clean firm power to support the development of domestic data centers as AI technologies continue to scale.
Partnerships with clean energy innovators like XGS are key to securing energy supply for data center operations in the region. Meta also signed a purchase agreement for a Sage Geosystems planned 150 MW power plant in the Rocky Mountains in 2024.
XGS’s proprietary solid-state, closed-loop system enables the production of geothermal energy with zero operating water use, which is significant in water-scarce regions such as New Mexico.
The project’s first 5 MW are projected to be deployed around 2027, with the remaining by 2029.
Geothermal potential | ~160 MW of potential for next-generation developers
New Mexico has the potential to tap into 160 MW of geothermal energy in the first 4 to 5 km of subsurface.
Skilled workforce | New Mexico has the second-largest U.S. oil and gas industry
The state is equipped with a vast workforce with significant transferrable skills that could help lower costs across all geothermal operations. It currently drills 1,000 wells per year.
Policy support | Financial incentives and 100% clean energy targets
Beyond mentioning geothermal energy in its constitution, New Mexico has a $15 million project development fund, a $0.15 tax credit, and regulations to help govern and grow the industry. The state also has strong renewable portfolio standards, targeting 80% clean energy by 2040 and 100% by 2045.

## Slide 88: Fervo is leading EGS with advanced analytics to improve drilling and development with an emphasis on data center demand
Observations
Fervo’s advanced data analytics enables faster geothermal deployment, demonstrated by its record-breaking drilling and resource temperatures.
The company’s success is attributable to its horizontal drilling technology, from the oil and gas industry. It has also attracted oil and gas talent.
Fervo utilizes real-time data and advanced analytics to assess subsurface characteristics to identify geothermal resources.
Fervo has attracted significant funding traction. The company has gained community buy-in through economic and labor opportunities.
Case study: Fervo Energy
May 2021
Fervo-Google Agreement
Fervo signs a landmark deal with Google to deliver 5 MW of power through a first-of-a-kind geothermal project.
Project to deliver power for Google’s Cloud region in Nevada.
In April 2021, Fervo raised a $28M Series B.
July 2023
Project Red Successful Well Tests
Cape Station targets 400 MW of power starting in 2026 and is fully operational by 2028.
Expected to create 6,600 jobs and generate $437M in wages.
November 2023
Project Red Operational
Project Red begins delivering geothermal power to Google’s data centers just two years after their agreement.
February 2024
Cape Station Drilling Improvements
Cape Station successfully drills 2100 ft. deeper than Project Red.
Fervo demonstrates a 70% reduction in drilling time.
Drilling costs decline significantly, from $9.4M to $4.8M per well.
June 2025
Sugarloaf Well Drilling at Cape Station
Fervo drills to 15,765 feet and 520℉.
Completes in 16 days of drilling, for a 79% reduction in drilling compared to DOE baseline.
An independent report identifies up to 5 GW of development in the Cape Station area.
Fervo completes well tests at its first-of-a-kind commercial pilot in Nevada.
Fervo becomes the first company to drill a horizontal well for commercial geothermal.
It achieves lateral length of 3,250 feet and 191℃.
September 2023
Cape Station Breaks Ground
Cape Station will deliver 100 MW by 2026 and 400 MW by 2028.
Fervo targets first data center cluster in Utah.

## Slide 89: For industrial applications, geothermal energy is viable for temperature applications <200ºC; New Zealand has harnessed this potential since 1957
Temperature requirements and potential geothermal applications for key industrial processes
Temperature (ºC) | Industrial applications | Geothermal application
<100ºC | Food & beverage processing Textile processing Paper processing | GHPs are most competitive for satisfying low-temperature industrial heat demand.
100-200ºC | Paper & chemicals production Auxiliary processes in cement production & food processing | Next-generation geothermal can provide midrange temperatures across a wide geography.
200-400ºC | Petrochemical cracking Cement & steel pre-processing Aluminum smelting | Fuel combustion or direct electricity use will most likely remain necessary.
Geothermal energy suppliers
Geological conditions
250-310ºC downhole temperature range
35 km2 area covered by the geothermal field
350-570 MW estimated available resources
Key industrial processes
Paper & pulp mill
Wood drying
Dairy processing
Supplies various industrial customers in Kawerau
Process steam supplied at pressures of 7-16 bar and process water at 170ºC
~14.8 PJ geothermal energy produced annually
90% less carbon; 0.007 tCO2e/GJ compared with LNG (0.054 tCO2e/GJ)
Ngāti Tūwharetoa Geothermal
Ngāti Tūwharetoa Geothermal (heating)
Eastland Generation, Mercury Energy (power)
Case study: New Zealand

## Slide 90: Geothermal power and geothermal heating & cooling show sectorial flexibility but remain rare in global deployment, despite savings potential
Opportunity Area | Integration Concept | Value Proposition | Locations
District Energy Networks | Supplying heating & cooling and power via geothermal‑driven systems and distribution networks | Enables high total‑energy efficiency in cities, on campuses, in communities | 
Industrial Clusters/ Eco‑Industrial Parks | Using geothermal heat/power for process heating, drying, and cooling in manufacturing or colocated industrial zones | Diversifies revenue, enhances resource utilization, creates industrial symbiosis | 
Tourism & Wellness | Direct‑use geothermal heat for spas, resorts, pools, wellness centers | Monetizes geothermal by‑products, enhances public acceptance of geothermal energy | 
Agriculture & Aquaculture | Geothermal‑heated greenhouses, fish farms, food dehydration using geothermal heat | Enhances year‑round productivity, reduces fossil fuel input, supports food systems | 
Building Energy Systems Data Centers | Geothermal power supply and cooling (or heat reuse) for large thermal loads like data centers or buildings | Enables carbon‑free baseload power, cooling efficiency, and waste‑heat reuse | 
Emerging
Established

## Slide 91: Iceland shows that leveraging heating and cooling provides greater financial security for geothermal power projects
Svartsengi Power Plant x Blue Lagoon enable national power and tourism dollars
Co-ownership unlocks economic co-benefits
Case study: Iceland
1976-78
1989
1993
1999
2008
Constructed in 1976;1 MW of electricity in 1978
1980
Second turbine added
(6 MW)
Three Ormat turbines added (3.6 MW)
Four
Ormat turbines added (4.8 MW)
30 MW turbine installed to power plant 5
30 MW expansion planned for power plant 6
2023
33% expansion planned
1 MW
7 MW
10.6 MW
15.4 MW
45.4 MW
75.4 MW
100.2 MW
Hot runoff water accumulates in proximity of plant
Bathing facilities opened
1987
Blue Lagoon Co. founded
1992
1994-98
Medical clinic established
Spa opens
Skin care and anti-aging products established 2011; Blue Lagoon reports profits 50% higher than HS Orka 2019
2019
Profits from tourism (spa, medicine, etc.)
700K annual visitors
Pays HS Orka through dividends
Project development for geothermal power plants
Heated geothermal water transferred to Blue Lagoon
In 2015, HS Orka received a $2.7M dividend payment.
Blue Lagoon co-ownership built a resilient, diversified business model
Orka Financial Highlights (2015)
Blue Lagoon Impact
Operational Strength
EBITDA: $21M | Gross profit: $15M; FX-adjusted growth of +1% and +7%
Revenue: $5.5M from staff transfer; retail sales +13% YoY.
Net income loss $1.9M driven by $24.7M non-cash derivative loss tied to aluminum prices
Dividend: $2.7M from spa operations
Income from associates: +78% to $8.9M
One-time $2M gain from share issuance
Loan repayments: $17.5M
Continued dividend payouts to shareholders
Power
H&C + Power

## Slide 92: Leveraging oil & gas capabilities can drive down geothermal power costs and accelerate deployment
Deployment: Oil & gas transfer
Problem | Current Challenge | Oil & Gas Synergy | Limitations | Case Example
Resource Identification | Accurate geothermal resource identification and modeling require multi-parameter surface data (seismic, geology, heat flow, permeability). | Oil & gas surface imaging and drilling data reduce exploration risk and improve reservoir targeting. | Legacy O&G datasets often lack thermal gradient resolution or long-term heat recharge data. | Hungary and The Netherlands: Open oil & gas subsurface databases reduce geothermal exploration costs and uncertainty.
Skilled Workforce Needs | Skilled workforce shortages in reservoir engineering and well completion delay project scaling. | Oil & gas professionals have skills that can apply to geothermal exploration, development, and operation. | Current policy frameworks provide limited financial incentives for geothermal workforce transfer. | DOE Geothermal from O&G Initiative: Demonstrates feasibility of cross-sector workforce and skill transfer.
Drilling Costs | Subsurface drilling represents 60 to 80% of total next-generation geothermal CapEx. | Hydrocarbon well technology (e.g., horizontal drilling, multi-stage stimulation) can be directly transferred to EGS. | Geothermal wells require sustained reinjection and higher temperature tolerance than oil & gas operations. | Fervo Energy’s Project Red: Achieved record flow rates by adapting shale fracking and fiber-optic monitoring.
Co-production and Well Repurposing | High initial exploration, drilling, and completion costs can be a limiting factor in geothermal projects. | Co-production or heat extraction from abandoned wells can de-risk geothermal projects. | Wells require a large heat gradient and flow rate, flexible permitting, and proximity to demand. | Zanskar Project (U.S.): AI-driven reservoir modeling revitalized legacy wells, cutting exploration risk by >50%.
Level of shared competencies

## Slide 93: Expanding the geothermal workforce through education, automation, and oil & gas talent transition is essential to compete
Global number of geothermal energy jobs (2018-2023)
Deployment: Oil
Investments in education and training
On-the-job training and apprenticeships
Diversity and inclusion of underrepresented groups
Technology and automation for complex operations
Action implications for geothermal workforce expansion
Chart: 
 | 94 | 99 | 96 | 196 | 152 | 50
 | 7
 | 9
 | 94
2018
2019
2020
2021
2022
9
7
2023
160
+104%
Other
Global geothermal employment more than doubled from 96,000 to 196,000 in 2021. In contrast, oil & gas employed 12.4 million people in 2023 (a 5% annual increase).
China leads in geothermal jobs, while the U.S. and EU must expand technical training and re-skilling to stay competitive.
Next-generation geothermal growth will depend on cross-sector training pipelines and digital automation.
Transition of oil and gas talent and workforce to geothermal energy
Number of jobs in thousands

## Slide 94: While North American land rigs are underutilized, geothermal rigs equipped with over 2,000 horsepower are in short supply
Global land rig supply vs. geothermal 2,000+ HP rigs
Deployment: Oil & gas transfer
Chart: 
 | 1700 | 1350 | 850 | 650 | 200 | 30 | 80
 | 600 | 750 | 1700 | 650 | 550 | 80

0%
20%
40%
60%
80%
100%
APAC
EE& FSU
NA
MENA
Latin America
SS Africa
WE
Oversupply
Demand
Source: Westwood World Land Drilling Rig Market Forecast 2025-2029 (2025)
Chart: 
| 2010 | 2015 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
 | 100 | 100 | 100 | 200 | 300 | 400 | 500 | 600 | 1220 | 1840 | 2460 | 3080 | 3700
 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200
Average land rig supply, demand and utilization by region 2025-2029
Demand and supply forecast of 2,000+ HP rigs for geothermal to supply 10% of U.S. power in 2030
Demand
Supply
Global rig demand is forecast to average 4,704 units between 2025 and 2029, an 18% increase on historical averages, with Asia Pacific leading at 36% (China remains the largest market), followed by Eastern Europe (27%) and North America (17%).
Although North America has the largest fleet, its rigs are underutilized, averaging only 33% utilization.
However, these figures apply to all land rigs — geothermal rigs require special prerequisites to meet operational demands, such as horsepower.
Rigs for EGS need a minimum of 2,000 HP to reach the required depths of 2,000-10,000 meters for EGS drilling.
Only about 5% of the current rig supply meets this horsepower specification.
Most rigs with 2,000+ HP are already used for oil & gas drilling, leading to a constrained supply for EGS drilling that is unlikely to change without a significant shift in demand.
Source: GRC Transactions: Supply Chain Challenges (2012).
Utilization
Need for production shift from general land rigs to geothermal 2,000+ HP rigs

## Slide 95: Traditional oil and gas service companies provide consulting, drilling, and technology to the geothermal industry
Deployment: Oil & gas transfer
Scale | Schlumberger | Baker Hughes | Halliburton
Geothermal-Specific Capabilities | GeothermEx, a Schlumberger subsidiary, involved in 80% of geothermal projects worldwide Resource exploration, development, design, construction, operations, and technical support Equipment: drill bits, fluid control systems, submersible pumps Ground source heat pumps | Geothermal turbines for both steam flashing applications and lower enthalpy Organic Rankine Cycle applications Geothermal drilling solutions (drill bits, mud motors, wellpath controls, etc.) Strategic investing partner in next-gen geothermal Equipment, products, and services on over 1,800 geothermal wells across 25 countries | 70 years of experience on global geothermal projects Consulting, project management, and equipment Subsurface intelligence, well construction and completion, production systems
Partnerships |  |  | 
Achievements and Recent Progress | Selected by U.S. DOD to research geothermal electricity potential of U.S. military sites. Schlumberger will partner with Ormat to provide end-to-end geothermal power solutions. Joint demonstration project in partnership with Ormat to fast-track EGS at existing Ormat site. Mount Ida Geothermal Power Plant (Türkiye): Employed Schlumberger’s electric submersible pump systems, which enabled well stimulation to increase expected output of 10 MW to actual output of 12 MW. | BH’s proprietary geothermal drilling components enabled drilling and operation of the deepest and hottest geothermal well ever drilled in Iceland (15,285 feet, max. temp 426℃). Selected by Fervo to design and deliver equipment for five Organic Rankine Cycle power plants at Fervo’s Cape Station power. Collaborating with Controlled Thermal Resources on 500 MW Hell’s Kitchen project in California. | Engineering and project management support to CeraPhi as it builds it’s first UK geothermal power project. Planning and design of geothermal wells in East Texas for GeoFrame Energy. The geothermal electricity will power lithium extraction. Custom drilling fluid solutions and cement at Fervo’s Cape Station project

## Slide 96: Mineral extraction from geothermal brines before reinjection offers an untapped domestic source for clean energy transition materials
Geothermal brines can be a significant source of critical minerals
Deployment: Critical minerals
Li
Mn, Cu, Ni
REE’s
Geothermal brine chemistry
Mineral extraction opportunity
Reinjected minerals
(status quo)
Li
Mn, Cu, Ni
REEs
Technology integration and compatibility of DLE efficiency and brine chemistry vary across sites.
Mineral recovery may disrupt flow rates, scaling, or reinjection balance.
High CapEx and unclear revenue streams make prioritization difficult.
Challenges
01
02
03
Opportunity
01
Diversify project revenue by co-producing lithium and rare earth elements.
Utilize existing brine reservoirs with proven mineral content.
Deploy emerging direct lithium extraction technologies to monetize brines without disrupting power generation.
02
03

## Slide 97: California’s Salton Sea has one of world's highest lithium brine concentrations, with commercial DLE projects underway
Direct lithium extraction (DLE) potential in Salton Sea:
Over 4 million tons of lithium, enough to support 10,000 GWh of battery capacity.
Existing advantage: Extensive geothermal infrastructure enables rapid DLE scale-up.
Could supply ~40% of global lithium demand if fully developed.
Commercial DLE projects underway:
Hell’s Kitchen: Controlled Thermal Resources
  Potential: 175,000 tons per annum
  Technology: Koch proprietary DLE
  Funding: $285M invested to date
Project ATLiS: EnergySource Minerals (ESM)
  Potential: 20,000 tons per annum
  Technology: ESM proprietary DLE
  Funding: Direct loan up to $1.36B from DOE
Geothermal-Li co-production at Salton Sea could anchor a domestic battery supply chain
Deployment: Critical minerals
1
2
Salton Sea

## Slide 98: Using geothermal energy to process Indonesia's nickel reserves can significantly reduce EV battery lifecycle GHG emissions
Deployment: Critical minerals
Chart: 
 | 66.3
 | 53.2
 | 39.9
 | 30
 | 24.5
 | 13.3
 | 8.9
 | 0
53
9
40
25
13
66
30
Minerals required for NMC EV battery, kg
Geothermal sites
Chart: 
 | 7
 | 3
 | 42
 | 19
 | 4
 | 4
 | 21
21
4
4
19
42
3
7
Minerals (kg)
Emissions
(kg CO2e/kWh)
Opportunity: Geothermal power to decarbonize nickel refining
Challenge: High emissions from nickel-intensive EV battery
Copper
Lithium
Nickel
Manganese
Cobalt
Graphite
Aluminum
Carbon
~40 kg of nickel is required for an average electric vehicle.
61% of all nickel used for EV batteries comes from Indonesia.
40% of global geothermal reserves are also in Indonesia.
Integrating geothermal energy into refining can cut nickel processing emission based on modeled clean-heat substitution.
Potential pilot regions: Sulawesi, Sumatra, and Java, where nickel and geothermal collocate.
Emissions by raw material, kg CO2e/kWh
Nickel contributes 42 kg CO2e/kWh (~40%) of EV battery raw material emissions.
Nickel reserves
Indonesia

## Slide 99: Geothermal power can eliminate upstream nickel emissions and lower EV lifecycle carbon intensity
Battery production dominates EV lifecycle emissions
Replacing fossil energy with geothermal power can cut EV lifecycle emissions by ~25%
Processing and refining steps drive the majority of nickel carbon footprint
Deployment: Critical minerals
Chart: 
 | 14.5 | 30.9
 | 5 | 11.5
 | 3.3 | 0
 | 0 | 3.7
Battery EV
ICE
18
46
Chart: 
 | 14.5 | 30.9
 | 5.3 | 11.5
 | 3.3 | 0
 | 0 | 3.7
Battery EV
ICE
23
46
Chart: 
 | 6.2 | 3.1
 | 25 | 71.5
 | 1 | 0.6
1
HPAL Process
1
3
RKEF Process
32
75
Tons CO2e/vehicle
Car Production
Battery Production
Well to Tank
Tank to Wheel
Mining
Processing
Refining
Car Production
Battery Production
Well to Tank
Tank to Wheel
Address nickel-processing emissions upstream.
Integrating geothermal power into nickel processing cuts 5 tCO2 per EV.
GHG emissions comparison between EV and ICE, tons CO2e/vehicle
GHG emissions by nickel production step mtCO2/ton of nickel
GHG emissions comparison between EV and ICE, tons CO2e/vehicle

## Slide 100: Queue composition (95% variable renewables, <1% firm resources) highlights structural interconnection barriers to geothermal scalability
Observations
Data centers, electrification, and reshoring are pushing load growth 10 times faster than in the previous decade, but the grid has not expanded in parallel.
LBNL finds 2.6 TW of queued capacity vs. 1.28 TW installed — driven overwhelmingly by solar, hybrids, and storage.
Projects took <2 years in 2008, ~3 years in 2015, and nearly 5 years in 2023, with costs rising 44% in the past five years.
Only 20% of projects (2000 to 2018) reached COD; >70% withdrew, often because transmission upgrades triggered by other projects caused cascading restudies.
Outdated lines, limited hosting capacity, and project-by-project upgrade triggers create multiyear delays irrespective of technology.
Recent BLM emergency permitting procedures have fast-tracked geothermal projects, helping offset the long delays created by the interconnection backlog
U.S. interconnection queue by energy sources, cumulative GW​
Deployment: Interconnection
Chart: 
 | 4.6477 | 1.712 | 3.7805 | 6.3889 | 6.6885 | 10.2396
 | 0.4803 | 0 | 2.4674 | 0 | 0 | 12.7252
 | 76.7263 | 2.2233 | 72.5755 | 3.4084 | 13.0785 | 12.8718
 | 0.05 | 2.109 | 0.943 | 0.4284 | 9.6024 | 123.3528
 | 0 | 71.881 | 2.4961 | 69.4526 | 69.603 | 1.4589
 | 0 | 0.1307 | 4.2198 | 1.4587 | 1.5157 | 1.7708
 | 6.1755 | 1.2433 | 6.3243 | 2.1521 | 1.7114 | 4.467
 | 0 | 2.7768 | 77.2033 | 5.4541 | 5.7457 | 5.3171
 | 10.7069 | 6.3093 | 16.546 | 6.457 | 9.993 | 58.5633
 | 214.5888 | 60.9793 | 153.3447 | 111.7873 | 119.8014 | 22.8044
 | 56.2733 | 11.323 | 220.7335 | 25.992 | 47.285 | 189.5991
 | 0 | 134.9305 | 207.5616 | 164.5662 | 198.4069 | 466.7539
2019
2020
2021
2022
2023
2024
733
964
1,443
2,012
2,598
2,290
Hydro
Nuclear
Geothermal
Offshore wind
Coal
Wind (hybrid)
Gas
Wind
Gas (hybrid)
Storage
Other
Storage (hybrid)
Other (hybrid)
Solar (hybrid)
Unknown
Solar

## Slide 101: Geothermal faces structural barriers across permitting, transmission, and interconnection, but new pathways are beginning to unlock deployment
Deployment
02.
01.
03.
04.
05.
Complex, multilayer permitting slows development, with dual federal-state reviews and sensitive-resource checks extending timelines far more than for wind and solar.
High upfront exploration costs increase financial risk, with $5-$10M for site characterization and up to $450M for full next-gen resource confirmation before PPAs are secured.
PPA uncertainty constrains bankability, since geothermal requires large sunk costs before revenue agreements are locked in.
The interconnection queue structurally disadvantages long-lead clean firm resources, with 95% of queued capacity coming from solar, wind, and storage.
Transmission distance and interconnection costs erode project economics, as remote resources face expensive upgrades and long IQ delays.
02.
01.
03.
04.
05.
Behind-the-meter deployment offers a near-term geothermal pathway, allowing industrial loads and data centers to bypass interconnection entirely.
BLM emergency permitting creates faster federal approval routes, with 14-day reviews for select geothermal activities.
Streamlined permitting practices, including tiering, MOUs, and integrated reviews, can materially reduce delays without weakening environmental rigor.
Next-generation geothermal (EGS, closed-loop) expands the viable subsurface resource base, reducing dependence on rare hydrothermal conditions.
Federal tax credits, DOE’s Enhanced Geothermal Shot, plus a goal to reduce EGS costs 90% by 2035 improve project economics, supporting early commercial deployment.
Structural barriers facing geothermal
Emerging pathways that can improve geothermal deployment

## Slide 102: Geothermal power maturity and deployment is in reach as tech investment and policy continue to co-work and de-risk projects
Current state of geothermal heating and cooling vs. electricity generation
Deployment
 | Heating, cooling, and thermal energy storage | Electricity generation
Main stakeholders | Governments, municipalities, real estate developers, industries, energy utilities | Energy utilities, governments, investors, technology firms, industrial users
Scalability | Moderate (local and regional impact) | High (grid-scale impact)
Market momentum | In action (transitions happening now) | First movers
Speed of deployment | Faster (months to a few years) | Slow (5-10+ years)
ROI timeframe | Moderate (5-10 years) | Long (10-30 years)
Industry & policy demand | Strong | Emerging
Funding availability | High (government incentives for urban decarbonization) | Limited (large-scale investments with long return periods)
Risk & uncertainty | Low (proven technology, well-established market) | High (geological risks, high upfront costs)
Technical & regulatory barriers | Low (fewer permits, well-established technology) | High (complicated permits, deep drilling risks)
Conversion efficiency | High (300-500% for heat pump COP) | Low (10-20% for binary plants, 10-15% for flash systems)
Capacity factor | Seasonal, lower utilization in warm climates | High (70-90%), base-load capable
Depth of drilling | Shallow (tens to hundreds of meters) | Deep drilling (1-5 km+), depending on resource
Emerging
Established
Scale & Momentum
Deployment
Policy & Financing
Technology

## Slide 103: Team

## Slide 104
Zacharia Thurston
MS in Sustainability Management
Team Lead | Climate Knowledge Initiative Fellow
Pia Doris Morrow
MS in Sustainability Management
Team Co-lead | Climate Knowledge Initiative Fellow
Sevgi Helin Tilkicioglu
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Heather Hartel
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Stephanie Chen
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Shubhangi Prasad
Master of Public Administration
Climate Knowledge Initiative Fellow
Faradisa Anintya
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Una Oljaca
BA in Economics, Political Sciences, and Government
Climate Knowledge Initiative Fellow
CKI Geothermal Team
Fellows (1/2)

## Slide 105
Thomas Smith
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Leo Gordon
MPA, Columbia SIPA
Climate Knowledge Initiative Fellow
CKI Geothermal Team
Fellows (2/2)

## Slide 106
Hyae Ryung (Helen) Kim
PhD in Sustainable Development
Former Senior Research Fellow
CKI Team Staff, Faculty, and Alumna
Share with attribution: Wagner et al. “Geothermal Power,” Columbia Business School Climate Knowledge Initiative (10 March 2026).

## Slide 107: Appendix

## Slide 108: Glossary (1/2)
CKI Guideline for Geothermal Terms
Baseload power | Electricity supplied consistently over time to satisfy the minimum level of demand
Peaker plant | A power-generation facility that is used only during periods of high electricity demand (peak loads) rather than continuously
Hydrothermal: Conventional geothermal | A geothermal system in which naturally occurring heat, fluid, and rock permeability are present, allowing heat extraction without major engineering of the reservoir
Dry steam power plants | A geothermal plant type in which steam (rather than hot water) from the reservoir is piped directly to a turbine to generate electricity
Flash steam power plants | A geothermal plant type in which high-pressure hot water from underground is brought to the surface, the pressure drops, water “flashes” into steam that drives a turbine, and remaining fluid is often reinjected
Binary cycle power plants | A geothermal plant in which geothermal fluid (often lower temperature) transfers heat to a secondary “working fluid” via a heat exchanger; the working fluid vaporizes and drives a turbine, while the geothermal fluid remains in a closed loop and is reinjected
Next-generation geothermal | An umbrella term for geothermal approaches beyond conventional hydrothermal resources; that is, systems using engineered reservoirs, closed loops, or other technologies to expand geothermal potential
Closed-loop geothermal systems (CLGS) | Geothermal systems in which the working fluid is circulated through sealed loops of pipe drilled into hot rock, extracting heat by conduction rather than relying on natural rock permeability or fluid pathways
Enhanced geothermal systems (EGS) | A method to develop geothermal energy in hot but low-permeability rock by artificially creating or improving the permeability (for example via hydraulic stimulation) so that fluid can circulate and extract heat
Advanced geothermal systems (AGS) | Often used interchangeably with closed-loop systems, geothermal systems that are engineered and do not depend on naturally favorable permeability or hydrothermal fluids
Superhot rock geothermal | Geothermal systems operating at very high temperatures (for example >400°C), often in rock that may reach or exceed super-critical conditions, thus offering a high-potential energy yield per well

## Slide 109: Glossary (2/2)
CKI Guideline for Geothermal Terms
Plasma drilling | A drilling method under development in which plasma (ionized gas) is used to erode or vaporize rock ahead of the drill bit, aiming for faster penetration in very hot or hard rock
Thermal spallation | A drilling technique under development in which rapid heating of rock causes spalling, rapid flaking, or fracturing of the rock surface, to assist borehole advancement in high-temperature conditions
Millimeter-wave drilling (Gyrotron) | A drilling technique under research using high-power electromagnetic waves at millimeter wavelengths (often from a gyrotron) to heat or vaporize rock ahead of the drill, to enable drilling in extreme rock/temperature environments
Laser-assisted drilling | A drilling technique under development in which lasers are used to ablate or weaken rock ahead of the drill bit, thereby improving the drilling rate or reducing bit wear in hard/high-temperature formations
Frontier technologies | Emerging and experimental geothermal technologies beyond current commercial practice, including advanced drilling, novel stimulation techniques, and reservoir-creation methods (please refer to technologies below)
Magma-based geothermal | Geothermal systems that aim to extract heat directly from molten or partially molten rock (magma) or adjacent high-temperature zones; a higher-risk/higher-reward approach in the geothermal field
Geopressured geothermal | Geothermal systems in sedimentary basins where hot fluids are under high pressure (geopressure), sometimes containing dissolved gas (e.g., methane), which can provide combined heat and gas resource potential
Directional drilling | A drilling technique in which the wellbore is steered off vertical (horizontal or angled) to reach target zones of heat, fluid, or permeability that are not directly beneath the surface well pad
Hydraulic fracturing | A stimulation technique in which fluid is injected at high pressure into rock to open or expand fractures, thereby creating or enhancing permeability so that fluid can circulate; used in EGS development