## Slide 1: Geothermal Power Executive Summary
Gernot Wagner, Zacharia Thurston, Pia Doris Morrow, Sevgi Helin Tilkicioglu, Heather Hartel, Stephanie Chen, Shubhangi Prasad, Faradisa Anintya, Una Oljaca, Thomas Smith, Leo Gordon, Ariela Farchi Behar, Hyae Ryung Kim, and Isabel Hoyos
10 March 2026
Cite as: Wagner et al. “Geothermal Power,” Columbia Business School Climate Knowledge Initiative (10 March 2026).

## Slide 2: Geothermal energy technologies span heating & cooling and power generation, with conventional approaches most widely deployed
Geothermal Opportunity
Key pathways for harnessing geothermal energy for heating & cooling and power generation
Conventional/hydrothermal
Underground thermal energy storage
Geothermal heat pumps
Direct-use heat
Borehole thermal energy storage
Aquifer thermal energy storage
Mine thermal energy storage
Advanced geothermal/ closed-loop systems
Enhanced geothermal systems
Next-generation technologies (commercialization <5 years)
Superhot rock
Frontier technologies (commercialization 5+ years)
Geopressured systems
Heating and cooling
Power
Production
Storage
Production
Storage
Cavern thermal energy storage
Pit thermal storage
Reservoir thermal storage
Magma-based geothermal
High-temperature geothermal energy storage
Geomechanical energy storage
Sources: Underground Thermal Energy Storage (Nature, 2012); Pathways to Commercial Liftoff: Geothermal Heating and Cooling (DOE, 2024); The Future of Geothermal Energy (IEA, 2024).
Credit: Sevgi Helin Tilkicioglu, Una Oljaca, Pia Doris Morrow, Isabel Hoyos, Hyae Ryung Kim, and Gernot Wagner. Share with attribution: Wagner et al. "Geothermal Power," Columbia Business School Climate Knowledge Initiative (10 March 2026).

## Slide 3: Global energy demand expected to grow ~10-20% by 2050, largely driven by emerging economies, electrification, and data centers
India, ASEAN*, Africa, and the Middle East will be responsible for ~65-95% demand growth
New data centers and electrification of industry and buildings will drive ~5-10% demand growth
Observations
By 2050, global energy demand is expected to grow ~10 to 20%, with ~65 to 95% of that growth concentrated in emerging economies such as ASEAN, India, and the Middle East — regions that currently rely heavily on fossil fuels for baseload power.
New demand will likely stem from the electrification of industry and buildings, accounting for over half of demand. Data centers (2,500 to 4,500 TWh, or ~5 to 10% of demand), green hydrogen (179 Mtpa, driving ~20% annual power demand growth), and EVs (~10% annual growth, with BEVs dominating car sales) will add to this surge.
To meet such demand, economies will need reliable, non-intermittent baseload solutions for their energy grids.
Opportunity: Power
Chart: 
1990
2000
2010
2020
2030
2040
2050
Chart: 
 | 11.5 | 13 | 20
 | 11.5 | 13 | 20
 | 0.75 | 1 | 10
 | 0.75 | 2 | 6
 | 0.75 | 2 | 8
1
1
2023
1
2
2
2030
2050
27
31
64
+3.5%/ year
Industry
Buildings
H2 and Synfuels
Data Centers
Transport
Global power consumption by sector (thousands of TWh)
Global primary energy demand (million TJ)
India
ASEAN
Africa
Middle East
Rest of World
Latin America
China
North America
OCED Europe
OECD Asia Pacific
~10-20%
Growth

## Slide 4: With vast untapped thermal resources and emerging technological advancements, geothermal power is primed for a breakout decade
Potential of proven oil & gas reserves vs. 1% geothermal resources*, trillion MWh
Projected global geothermal under different scenarios, GW
Historical installed geothermal capacity by country, GW
Opportunity: Power
Chart: 
 | 2793 | 2216 | 2252 | 2133 | 2152 | 2285 | 2274 | 2214 | 2229 | 2382 | 2405 | 2409 | 2592 | 2607 | 2514 | 2542 | 2517 | 2483.3 | 2444.3 | 2555.4 | 2571.9 | 2596.7 | 2648.6 | 2695.8 | 2725
 | 525 | 785 | 785 | 805 | 820 | 850 | 850 | 980 | 1052 | 1189 | 1189 | 1226 | 1336 | 1343.5 | 1403.5 | 1438.3 | 1533.3 | 1808.3 | 1948.3 | 2130.7 | 2130.7 | 2286.05 | 2360.33 | 2597.51 | 2638.8
 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1916.1 | 1916.1 | 1916.1 | 1916.1 | 1928.1 | 1928.1 | 1928.1 | 1928.1 | 1932 | 1951.8 | 1951.8
 | 18 | 18 | 18 | 15 | 15 | 15 | 23 | 23 | 30 | 77 | 94 | 114 | 162 | 311 | 405 | 624 | 821 | 1063.7 | 1282.518 | 1514.688 | 1613.188 | 1676.17 | 1691.338 | 1691.338 | 1734.338
 | 418 | 417 | 372 | 382 | 382 | 437 | 437 | 456 | 578 | 617 | 742 | 742 | 768 | 840 | 966 | 990 | 985 | 985 | 1009 | 1009 | 1043 | 1043 | 1050 | 1050 | 1275.4
 | 843 | 843 | 853 | 953 | 953 | 953 | 953 | 958 | 958 | 958 | 883 | 808 | 833 | 858 | 868 | 898 | 923.5 | 948.5 | 948.5 | 973.5 | 973.5 | 998.5 | 998.5 | 998.5 | 998.5
 | 58 | 58 | 58 | 58 | 128 | 128 | 128 | 128 | 128 | 163 | 198 | 198 | 205.5 | 205.5 | 366.1 | 618.9 | 652.9 | 672.9 | 683.8 | 683.8 | 863.13 | 863.13 | 949.73 | 984.73 | 939.73
 | 172 | 202 | 202 | 202 | 202 | 232 | 422 | 485 | 575 | 575 | 575 | 665 | 665 | 665 | 665 | 665 | 665 | 709.958 | 755.558 | 755.558 | 756.158 | 756.208 | 757.58 | 787.58 | 787.58
 | 590 | 573 | 666 | 707 | 642 | 671 | 671 | 671 | 671 | 695 | 728 | 728 | 728 | 729 | 768 | 768 | 767 | 767.19 | 767.19 | 767.19 | 771.79 | 771.79 | 771.79 | 771.79 | 771.79
 | 533 | 533 | 533 | 535 | 535 | 535 | 532 | 532 | 532 | 535 | 537 | 537 | 512 | 512 | 508 | 516 | 526 | 471.366 | 473.115 | 480.714 | 487.004 | 486.814 | 436.814 | 456.054 | 489.054
 | 144.71 | 144.71 | 144.71 | 162.71 | 165.71 | 165.711 | 165.711 | 165.711 | 165.711 | 165.711 | 165.711 | 217.461 | 217.461 | 217.461 | 217.461 | 217.361 | 206.86 | 206.86 | 206.86 | 261.86 | 261.86 | 258.84 | 262.66 | 262.66 | 262.66
 | 332 | 377.5417 | 423.0833 | 468.625 | 514.1667 | 559.7083 | 605.25 | 650.7917 | 696.3333 | 741.875 | 787.4167 | 832.9583 | 878.5 | 924.0417 | 969.5833 | 1015.125 | 1060.6667 | 1106.2083 | 1151.75 | 1197.2917 | 1242.8333 | 1288.375 | 1333.9167 | 1379.4583 | 1425
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
16
2
2012
2004
2016
2020
2024
United States
Indonesia
Philippines
Turkey
New Zealand
Mexico
Kenya
Iceland
Italy
Japan
Costa Rica
2000
Rest of World
2008
Chart: 
 | 2.55
 | 0
 | 1257
2.55
Proven fossil reserves
1% geothermal resources
Chart: 
 | 2.55
2.55
500x
potential energy
(all geothermal resources)
Chart: 
| 2010 | 2022 | 2023 | 2030 | 2035 | 2040 | 2050
 | 10000 | 15000 | 14850 | 22000 | 31000 | 40000 | 56000
 | 14850 | 25810 | 39630 | 52860 | 83340
 | 14850 | 29000 | 44250 | 59500 | 90000
 | 14850 | 38660 | 61080 | 79630 | 111120
0
10
20
30
40
50
60
70
80
90
100
110
120
Chart: 
 | 2405 | 2409 | 2592 | 2607 | 2514 | 2542 | 2517 | 2483.3 | 2444.3 | 2555.4 | 2571.9 | 2596.7 | 2648.6 | 2695.8 | 2725
 | 1189 | 1226 | 1336 | 1343.5 | 1403.5 | 1438.3 | 1533.3 | 1808.3 | 1948.3 | 2130.7 | 2130.7 | 2286.05 | 2360.33 | 2597.51 | 2638.8
 | 1846.7 | 1846.7 | 1846.7 | 1846.7 | 1916.1 | 1916.1 | 1916.1 | 1916.1 | 1928.1 | 1928.1 | 1928.1 | 1928.1 | 1932 | 1951.8 | 1951.8
 | 94 | 114 | 162 | 311 | 405 | 624 | 821 | 1063.7 | 1282.518 | 1514.688 | 1613.188 | 1676.17 | 1691.338 | 1691.338 | 1734.338
 | 742 | 742 | 768 | 840 | 966 | 990 | 985 | 985 | 1009 | 1009 | 1043 | 1043 | 1050 | 1050 | 1275.4
 | 883 | 808 | 833 | 858 | 868 | 898 | 923.5 | 948.5 | 948.5 | 973.5 | 973.5 | 998.5 | 998.5 | 998.5 | 998.5
 | 198 | 198 | 205.5 | 205.5 | 366.1 | 618.9 | 652.9 | 672.9 | 683.8 | 683.8 | 863.13 | 863.13 | 949.73 | 984.73 | 939.73
 | 575 | 665 | 665 | 665 | 665 | 665 | 665 | 709.958 | 755.558 | 755.558 | 756.158 | 756.208 | 757.58 | 787.58 | 787.58
 | 728 | 728 | 728 | 729 | 768 | 768 | 767 | 767.19 | 767.19 | 767.19 | 771.79 | 771.79 | 771.79 | 771.79 | 771.79
 | 537 | 537 | 512 | 512 | 508 | 516 | 526 | 471.366 | 473.115 | 480.714 | 487.004 | 486.814 | 436.814 | 456.054 | 489.054
 | 165.711 | 217.461 | 217.461 | 217.461 | 217.461 | 217.361 | 206.86 | 206.86 | 206.86 | 261.86 | 261.86 | 258.84 | 262.66 | 262.66 | 262.66
3.5x by 2050 (56 GW)
5.2x by 2050 (83 GW)
5.6x by 2050 (90 GW)
Stated Policies
Announced Pledges
DOE Liftoff
Net Zero Emissions
In 2025, 32 countries had geothermal power, for a total of ~16 GW global capacity, from 3,700 production wells with an average 3 MWh capacity per well.
6.9x by 2050 (111 GW)

## Slide 5: Next-generation drilling unlocks globalized clean energy access, with notable overlap in emerging economies by 2050
Global EGS hotspots concentrated in emerging economies
Potential for next-gen geothermal power capacity by region, GW (IEA projections)
Opportunity: Power
Chart: 
 | 0.05856 | 2.928 | 58.56 | 146.4 | 240 | 300
 | 0.03904 | 1.952 | 39.04 | 97.6 | 160 | 200
 | 0.01952 | 0.976 | 19.52 | 48.8 | 80 | 100
 | 0.015616 | 0.7808 | 15.616 | 39.04 | 64 | 80
 | 0.00976 | 0.488 | 9.76 | 24.4 | 40 | 50
 | 0.01952 | 0.976 | 19.52 | 48.8 | 80 | 100
500
600
400
700
300
800
200
900
100
0
2025
2030
2035
2040
2045
2050
0.1625
8
162
405
664
830
China
United States
India
Southeast Asia
Europe
Rest of the world
5-7.5 km
7.5-10 km
10-12.5 km
12.5+ km
Estimate
United States: 3,400 GW
China: 300 GW
India: 80 GW
Southeast Asia: 64 GW
Europe: 50 GW
Project InnerSpace
IEA
Global next-gen geothermal projections vary. Project InnerSpace’s projections likely reflect greater accuracy of global geothermal potential, driven by superior subsurface data collection. IEA estimates are deliberately conservative, focusing on what is deployable under today’s policy, cost, and financing conditions.
United States: 200 GW

## Slide 6: Geothermal power offers clean baseload capacity to replace retiring coal plants and prevent overreliance on peaker plants
Loss of baseload power leads to overreliance on peaker plants and can drive up costs for consumers
Heavy dependence on intermittent renewables without baseload capacity threatens grid reliability
Opportunity: Power
Fossil energy will plateau despite energy demand increasing.
Grids that are overreliant on wind and solar (intermittent energy) without baseload capacity risk rolling blackouts during periods of low renewable generation.
Cost of generation ($)
Hourly net load (year average) in California
Global final energy consumption for Continued Momentum scenario, by fuel, millions of terajoules
What is baseload?
28,000
26,000
24,000
22,000
20,000
18,000
16,000
14,000
12,000
10,000
0
12am
3am
6am
9am
12am
3pm
6pm
9pm
2020
2018
2019
2017
2016
2015
2014
2013
2012
Increased ramp
Potential overgeneration
Megawatts
Baseload
Mid-load
Peak load
Coal
N. gas
Nuclear
The most common sources of baseload power, chosen for their low LCOE. Gas can be used but has higher OpEx.
Baseload power is the minimum amount of electricity the electrical grid needs at any given time. Runs continuously at a steady output.
Chart: 
 | 24.5 | 25 | 40 | 24.5 | 24.5 | 24.5 | 24.5
 | 100 | 115 | 125 | 120 | 140 | 125 | 105
 | 45 | 77.5 | 110 | 90 | 120 | 110 | 98
 | 35 | 40 | 45 | 37 | 31 | 25 | 21
 | 2 | 8 | 10 | 12 | 16 | 18 | 21
 | 35 | 37.5 | 40 | 50 | 100 | 120 | 150
 | 10 | 11.8333 | 13.6667 | 15.5 | 17.3333 | 19.1667 | 21
1990
2000
2010
2020
2030
2040
2050
Other
Electricty
Hydrogen
Bioenergy
Natural gas
Oil
Coal

## Slide 7: Key barriers limiting geothermal deployment include exploration risks, drilling technology limits, and heat flow variability
Barriers to geothermal achieving global, dispatchable, and cost-competitive clean power
Opportunity: Power
Barrier | Description | Impact on Deployment | Emerging Solutions
Exploration Risk & Cost | High upfront cost for resource identification; drilling success uncertain | Major cost bottleneck; limits financing | AI/geophysical modeling, remote sensing, cheaper slim-hole drilling
Drilling Technology Limits | Conventional rigs struggle with deep/hard rock, high heat, and corrosive fluids | Limits depth/temperature access → limits energy yield | Advanced drilling (plasma, millimeter wave, laser), O&G transfer tech
Reservoir Stimulation & Permeability | Creating or maintaining fluid pathways in hot dry rock is challenging | Determines long-term productivity; EGS sites often fail after testing | Hydraulic shearing, closed-loop systems, supercritical fluid modeling
Materials & Corrosion Resistance | Equipment degradation in harsh conditions (heat, pressure, minerals) | Raises O&M costs and reduces lifetime of wells | High-temp alloys, ceramics, coatings
Power Conversion Efficiency | Efficiency drops at lower temperatures; limited by thermodynamic cycles | Restricts viable sites; reduces energy output | Supercritical CO₂ cycles, binary cycle optimization
Monitoring & Reservoir Management | Hard to track subsurface dynamics and avoid induced seismicity | Safety/regulatory constraints; performance loss over time | Fiber-optic sensing, real-time data analytics, seismic monitoring
Transmission & Integration | Geothermal sites often remote; grid connection costs high | Slows scalability and investment interest | Colocation with industrial heat users, modular systems
Public & Regulatory Challenges | Concerns about seismicity, permitting delays | Adds time and uncertainty to projects | Streamlined EGS permitting frameworks
Major Barriers

## Slide 8: Conventional geothermal energy can utilize all three power plant design methods, each suited to different temperature ranges
Global capacity, %
LCOE, $US/MWh (Conservative estimate, 2030)
TBU
~56
~84
Efficiency, %
20-30
25-35
10-20
30-40
Temperature range, °C
180+
150-200
85-170
180-220
Advantages/ disadvantages
Proven and mature technology
Lower plant complexity
Rare resource availability
Resource depletion risk
Potential emissions
Most common technology
High efficiency
High temperature requirement
Mineral scaling and corrosion
Water management challenges
Lower temperature requirement
Closed secondary loop
Lower efficiency
Higher CapEx and OpEx
Secondary fluid risks
23%
14%
Hydrothermal (conventional)
Dry steam power plants
A
Flash steam power plants
B
Binary cycle power plants
C
19%
Double flash
42%
Single flash
Conventional power generation

## Slide 9: Next-generation technologies enable energy extraction from hot dry rock with little to no natural fluid
Next-gen & frontier power generation
Advanced geothermal (AGS)/ closed-loop systems
Enhanced geothermal systems (EGS)
Superhot rock geothermal
Next-gen technologies
EGS creates or improves permeability in hot dry rock to circulate injected fluid between wells.
Closed-loop geothermal circulates a working fluid in sealed pipes to conductively draw heat from hot rock, with no groundwater contact and no reliance on rock permeability.
Superhot rock geothermal taps ultradeep formations where water becomes a supercritical fluid, enabling vastly higher heat and power output than EGS or AGS systems.
A
B
Definition
Advantages/ disadvantages
Higher thermal efficiency compared to AGS
Potentially higher scale
Seismicity risks
Reservoir uncertainty
Water losses
Geographic flexibility
No brine requirement
No seismic risk
Lower thermal efficiency
Higher CapEx requirements compared to EGS
Much higher energy
Long development time and highest cost requirement
Extreme drilling challenges and equipment limitations
Frontier technologies
C

## Slide 10: Drilling currently drives ~54% of next-gen geothermal LCOE; investments to reduce that share target heat resistance, permeability, and drill-bit life
Emerging technologies aimed at lowering next-generation geothermal drilling costs
Breakdown of projected LCOE components of next-generation geothermal in a low-cost case (US$/MWh)
Drilling technology
High-powered millimeter-wave beams from a gyrotron vaporize rock and drill ultradeep boreholes, bypassing the wear and tear of traditional drilling methods.
Millimeter-Wave Drilling
Directional Steel-Shot Drilling
Repetitive Pulsed Electric Drill (RePED)
High-Pressure Water Jet-Assisted Drilling
A full-scale demonstration drilled 10 feet deep using 100 kW of millimeter-wave power; Quaise also plans to deploy a 1 mW gyrotron within two years to reach commercially viable depths.
Tetra Innovation Institute and NREL partnered to advance the technology, with potential drilling cost reductions of 75% and applications in industries beyond geothermal.
High-voltage electric pulses fracture rock, avoiding mechanical contact. Reduces wear on equipment and is designed to work with existing drilling infrastructure.
Drilling solutions startup Canopus is collaborating with TNO and European partners to test the drill system in the Netherlands, funded by a Dutch subsidy scheme.
Steel-shot particles are released under high pressure to erode rock formations and reduce resistance to further rotary drilling.
ORCHYD combines high-pressure water jets with fluid-driven percussion drilling, aiming to cut drilling costs by 65%. The project received Horizon 2020 funding from the EU in 2021.
High-pressure water jets cut rock into shapes that can be broken apart more easily by fluid-powered percussive hammers.
Chart: 
 | 51 | 25.5 | 22.3
 | 59.9 | 25.5 | 7.5
54%
46%
2025
50%
50%
2035
25%
75%
2050
111
51
30
Drilling costs
Other
Drilling, loop supplies, and installation also comprise 55-65% of conventional geothermal (GHP) costs in the U.S. (2025).

## Slide 11: Four key policy priorities can help scale geothermal power deployment and drive down costs
Observations
Stronger implementation of policy goals could boost new geothermal heat developments 50% by 2030 in the APS compared with the Stated Policies scenario.
Strong policy can also help drive next-generation geothermal cost reductions of up to 80% by 2035.
In the APS, expanding policy support and cost reductions would scale GHP consumption to almost 3,000 PJ — 50% higher than in the Stated Policy scenario (China, U.S., and Europe together account for 80% of this growth).
Almost two-thirds of geothermal power capacity additions between 2024 and 2030 are expected to be policy-driven – primarily tax credits, fixed tariffs, and premiums.
Global policy
Global Collaboration
Global collaboration on geothermal energy – particularly heating and cooling – lags behind other renewables, slowing innovation and increasing risk. Stronger, more large-scale collaboration is a priority.
Workforce Development
Geothermal expansion will require a skilled workforce in engineering, geology, and drilling sectors. Transitioning the oil and gas workforce will streamline geothermal workforce development.
Research & Development
Poor funding infrastructure for geothermal exploration and drilling drives up investment costs and slows technological progress. Strong funding mechanisms will be necessary to speed geothermal deployment.
Risk Mitigation
Geothermal projects have higher predevelopment risks compared with other renewable energy technologies due to complex geological and subsurface conditions. Mitigating risk is critical in lowering project costs.

## Slide 12: Global leaders in deployment are developing policies not only for geothermal power but heating and cooling as well
Observations
Over half of all countries with geothermal policies in place (16 of 31) focus exclusively on power generation.
Regional policy schemes in Latin America and East Africa are not included in this map.
Only eight countries (all in Europe) have adopted geothermal roadmaps for their heating & cooling sectors.
>100 countries have policies in place for solar PV and onshore wind — over 3x as many as for geothermal energy.
Europe is a regional hub for geothermal heating & cooling policies, while China leads on the country level.
Geothermal energy is a priority mitigation option in only 9% of NDCs’ submitted data.
While the risk mitigation-to-remuneration policy ratio is ~1:2 for solar and wind energy, the ratio for geothermal energy is ~1:1 due to high early-stage risk.
Countries with geothermal policies in place, 2024 (risk mitigation and/or remuneration)
Global policy

## Slide 13: Global collaboration favors geothermal power production, leaving room for growth in heating and cooling expansion
Drivers of variable global collaboration on geothermal power versus heat
Power projects tend to be larger and have bigger returns compared to more localized heating projects.
There is a differential global emphasis on electricity access compared to heating access.
The development of EGS has spurred greater collaboration on geothermal power generation.
Scalability of power projects attracts greater private investment.
Global policy
Scale | Power Generation |  | Heating & Cooling | 
Global |  | The Global Geothermal Development Plan (GGDP), launched by ESMAP in 2013 to scale geothermal power, has supported 13 countries and brought three projects online. |  | Although World Bank does not have a dedicated global program for geothermal heating, it has provided one-off investments in district heating in countries including Türkiye and El Salvador.
Regional |  | The GRMF finances geothermal power projects in East Africa, expanding to include heating in 2022; 26 power and 5 direct-use projects have received funding. |  | Geothermica’s €32.5 million Joint Call 2021 aims to accelerate geothermal heating and cooling projects by 2030 through large-scale, commercially viable projects.
Bilateral |  | Japan’s International Cooperation Agency invests in building geothermal power capacity in Latin America and Africa, including over 400 MW of geothermal power plants in Kenya. |  | The German Agency for International Cooperation and the Central American Integration System have cooperated on geothermal heating and cooling in El Salvador, including a pilot geothermal-powered coffee dryer.

## Slide 14: U.S. ranks No. 3 in superhot rock potential, has 12% of total global geothermal potential, and is set to scale with policy support
U.S. geothermal power policy timeline
U.S. 2021 energy demand vs. 1% geothermal power potential, GWh
Case study: United States
1970
Landmark law grants federal authority over geothermal leasing on public lands (via BLM and U.S. Forest Service), enabling competitive leasing with royalties and rentals as part of a broader energy policy to address rising demand and foreign oil dependence.
2009-16
2024-25
IRA incentives repealed but geothermal spared — tax credits phase down after 2033. Global tariffs and U.S. support for tech reshoring boost emerging EGS startups (Fervo, Sage) supplying data centers with baseload power.
2005
Energy Policy Act: Is overhauled, streamlining leasing and permitting and adjusting royalty structures.
2017-21
Trump 2.0: OBBA, Global Tariffs, Domestic Tech Giant Incentives
Biden: Bipartisan Infrastructure Law (2021) + IRA (2022)
Trump 1.0:
Obama Era
Energy Policy Act
Geothermal Steam Act
Chart: 
 | 4374671 | 4374671
 | 31336521
5-7.5 km
7.5-10 km
10-12.5 km
12.5+ km
2021-24
Excess of 31,336,521 GWh
Ability to power NYC
660x over
Majority of U.S. population
High-density population pocket
Provides broad support of renewable energy development, support for DOE funding for EGS; geothermal included in net-zero planning.
Rollbacks in environmental policies broadly ease permitting; renewable incentives are de-emphasized.
DOE’s Geothermal Tech program advances EGS demonstrations.
Modern EGS technology could access ~3,400 GWs of non-superhot rock power in Q4 2025.
35,711,192
Equivalent to
21B
barrels of oil
2021 energy demand (CATF)
1% of superhot rock potential

## Slide 15: OBBBA keeps IRA 45Y and 48E incentives for geothermal power until 2035; foreign entity of concern (FEOC) rules apply after 2026
Case study: United States
Preserved
Inflation Reduction Act (IRA)
One Big Beautiful Bill Act (OBBBA)
Chart: 

Early expiration
All projects onward will be affected by stricter FEOC restrictions.
45V – clean hydrogen: Credit available through 2032 for facilities that start construction. Producer can claim up to $3.0/kg until 10 years after the facility is placed into service. Under OBBBA, the credit is available only if construction starts by December 31, 2027.
Wind and solar: 48E ITC of 6%, incrementable up to 30% and 45Y PTC of ¢0.3/kWh incremental up to ¢1.5/kWh. Facilities must be constructed by July 2026 or placed in service by December 31, 2027.
48E/45Y ‒ geothermal: Preserved in full; sourcing rules apply after 2028. Phaseout set to begin in 2033, through 2035.
Executive Order: Declaring a National Energy Emergency
Cites geothermal heat under the definitions for the terms energy or energy resource, 30 U.S.C. 1606 (a)(3).
Executive Order: Protecting American Energy from State Overreach
States intention to remove illegitimate impediments for the discovery and production of geothermal power.
Secretarial Order: Unleash Golden Era of American Energy Dominance
States intention to focus time, resources, and technologies of the DOE’s R&D toward the development of geothermal.
DOE Office of Hydrocarbons and Geothermal
Supports the development of EGS and superhot technologies through financing and R&D efforts.
Geothermal Power Under Trump Administration
The GTO’s programs are building toward their strategic goal of supplying 60 GW of EGS and hydrothermal resources deployment by 2050.

## Slide 16: Conventional geothermal construction costs projected to continue to decline, driven by tech improvements and efficiency gains
Observations
Binary geothermal sees cost reductions through both subsurface and surface improvements.
Conservative: Learning is incremental with limited drilling gains.
Moderate: Introduces faster drilling, reduced material use, and moderate plant scaling (to 40 MW), supported by a 13% learning rate.
Advanced: Accelerates progress with major drilling breakthroughs, larger plants, and advanced surface system efficiency, resulting in up to 30% learning-driven CapEx reduction. As a result, binary systems become increasingly viable across a wider range of geographies.
Flash geothermal sees cost reductions driven by drilling efficiency and plant scale.
Conservative: Only modest gains are expected, with minor improvements in drilling speed and bit durability.
Moderate: Assumes faster drilling, fewer casing stages, and streamlined permitting, leading to more meaningful CapEx savings.
Advanced: Transformational gains, such as 4x faster drilling, monobore well designs, and deployment of 100 MW plants unlock significant cost reductions by cutting timelines, material use, and per-MW development cost.
Cost of construction for both flash and binary geothermal are expected to decline from 2022 to 2050 under conservative to advanced scenarios
Finance
Chart: 
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
 | 2574.3766 | 2372.261 | 2181.5636 | 2001.184 | 1830.1658 | 1667.6734 | 1512.9726 | 1365.4158 | 1224.4287 | 1089.5005 | 960.1745 | 836.0417 | 716.7338 | 601.9185 | 576.3895 | 550.9881 | 525.7137 | 500.5657 | 475.5434 | 450.6462 | 425.8735 | 401.2247 | 376.6991 | 352.2962 | 328.0153 | 303.8557 | 279.817 | 255.8985 | 232.0995
 | 2574.3766 | 2457.7037 | 2350.4021 | 2251.1191 | 2158.7691 | 2072.4686 | 1991.4894 | 1915.2246 | 1843.1633 | 1774.8718 | 1709.9787 | 1648.1638 | 1589.1492 | 1532.6922 | 1502.5633 | 1472.585 | 1442.7567 | 1413.0775 | 1383.5467 | 1354.1635 | 1324.9273 | 1295.8372 | 1266.8926 | 1238.0927 | 1209.4368 | 1180.9242 | 1152.5541 | 1124.3259 | 1096.2389
 | 2574.3766 | 2539.0515 | 2503.903 | 2468.9303 | 2434.1324 | 2399.5085 | 2365.0578 | 2330.7793 | 2296.6721 | 2262.7356 | 2228.9687 | 2195.3706 | 2161.9405 | 2128.6776 | 2095.581 | 2062.6498 | 2029.8834 | 1997.2807 | 1964.8411 | 1932.5637 | 1900.4476 | 1868.4922 | 1836.6965 | 1805.0598 | 1773.5813 | 1742.2601 | 1711.0956 | 1680.0869 | 1649.2333
 | 4933.8723 | 4584.1193 | 4262.0889 | 3964.149 | 3687.3036 | 3429.0567 | 3187.3091 | 2960.2813 | 2746.4531 | 2544.5169 | 2353.3407 | 2171.9392 | 1999.4498 | 1835.1139 | 1803.4189 | 1771.8824 | 1740.5035 | 1709.2815 | 1678.2157 | 1647.3051 | 1616.5492 | 1585.947 | 1555.4978 | 1525.2008 | 1495.0554 | 1465.0606 | 1435.2159 | 1405.5204 | 1375.9733
 | 4933.8723 | 4723.3502 | 4535.9417 | 4367.2459 | 4213.9865 | 4073.6615 | 3944.32 | 3824.4126 | 3712.6896 | 3608.1292 | 3509.8856 | 3417.2515 | 3329.6297 | 3246.5114 | 3207.8134 | 3169.3089 | 3130.9969 | 3092.8765 | 3054.9467 | 3017.2066 | 2979.6551 | 2942.2914 | 2905.1145 | 2868.1235 | 2831.3175 | 2794.6955 | 2758.2566 | 2721.9998 | 2685.9244
 | 4933.8723 | 4886.7497 | 4839.8627 | 4793.2102 | 4746.7909 | 4700.6037 | 4654.6475 | 4608.921 | 4563.4232 | 4518.1529 | 4473.1089 | 4428.2901 | 4383.6954 | 4339.3238 | 4295.1739 | 4251.2448 | 4207.5354 | 4164.0445 | 4120.771 | 4077.714 | 4034.8722 | 3992.2446 | 3949.8301 | 3907.6278 | 3865.6364 | 3823.855 | 3782.2825 | 3740.9179 | 3699.7601
7,000
9,000
2040
2030
2045
2025
2050
10,000
0
5,500
6,000
6,500
9,500
7,500
8,000
8,500
2035
4,871
5,735
6,288
6,015
7,325
8,339
Flash (advanced)
Flash (moderate)
Flash (conservative)
Binary (advanced)
Binary (moderate)
Binary (conservative)
Estimated construction costs, US$/kW

## Slide 17: Next-gen tech is riskier and more equity-heavy, while proven technologies attract more debt through traditional project finance
Finance
Technology
Fervo, U.S. | Rift Valley, Kenya | Sarulla, Indonesia
Next-gen geothermal (EGS, advanced drilling, and fiber optics) | Conventional geothermal (mixture of flash and binary) | Conventional geothermal (flash steam)
Moderate technology risk: While EGS has been de-risked by field pilots like Project Red (TRL 9 in 2024), scaling commercial deployment still carries subsurface and reservoir uncertainty. Medium resource risk: EGS creates its own reservoir, which avoids natural resource uncertainty but introduces engineered subsurface complexity. | Low technology risk: Uses proven conventional technology. High resource risk: In early phases, especially in unexplored or underexplored zones, but borne by the public sector through Kenya’s state-owned GDC, which validates the resource before handing it off to private IPPs. | Low technology risk: Uses proven conventional technology. Low resource risk: Located in a well-characterized field with extensive drilling and historical data.
Long-term PPAs with utilities or corporate, pilot to commercial-scale model. | Utility offtake with donor-backed pricing. | IPP model with 30-year PPA under feed-in tariff, backed by political risk guarantees.
More equity: Early-stage EGS projects are equity-heavy, backed by VC/PE (e.g., Breakthrough Energy, Capricorn). Transitioning toward project finance as risk perception declines. | More debt: GDC-led exploration allows donor-backed debt instruments (e.g., AfDB, AFD, World Bank); equity participation from KenGen and private IPP. | More debt: Classic project finance with concessional and commercial debt (ADB, JBIC, CTF); equity from Medco, Itochu, Kyushu Electric, INPEX.
Frontier tech, higher risk
Proven tech, lower risk
Risk profile
Revenue model
Financing instrument and stakeholder

## Slide 18: Oil & gas expertise transfer can significantly reduce subsurface drilling costs, the largest component of geothermal construction
Next-gen geothermal construction costs are projected to drop ~60-80% by 2050 …
… driven by oil & gas expertise transfer; in the U.S., this can reduce costs by up to 80% of current baseline
Observations
Next-gen geothermal faces high upfront costs, with subsurface drilling accounting for 60 to 80% of total expenses.
Oil & gas expertise in drilling, supply chains, and modular plant design is key to reducing costs, driven by improved site planning, technology spillovers, economies of scale, and surface facility optimization, all areas where O&G capabilities directly apply.
In a low-cost scenario, effective O&G knowledge transfer could cut costs by up to 80%; the medium-cost case assumes more gradual progress and implementation barriers.
Finance: Oil & gas transfer
Chart: 
 | 100 | 93.3333 | 63.3333 | 41.3333 | 27.3333 | 20 | 20
 | 6.6667 | 30 | 22 | 14 | 7.3333
100%
Baseline Cost
7%
Evaluation & Planning
30%
Research
22%
Spillover
14%
Economies of Scale
7%
Surface Facilities
20%
Reduced Cost
14,000 US$/kW
Research and spillover from oil & gas would enhance drilling speed, reliability, and equipment use.
Improvement of site targeting would reduce drilling failures.
Reduction potential comes from modular, standardized plant design.
Chart: 
 | 14000 | 9500 | 7500 | 6500 | 6000 | 5700
 | 14000 | 7000 | 4000 | 3000 | 2500 | 2300
2025
7,500
4,000
2035
2050
Next-gen geothermal construction costs, US$/kW
Medium-Cost Case
Low-Cost Case
Breakdown of geothermal construction potential cost reduction, %

## Slide 19: Geothermal LCOE is on track to compete with hydro, nuclear, and solar PV + storage, through O&G transfer and policy-led de-risking
Observations
Next-gen geothermal costs could drop significantly, enabling power generation at ~US$40/MWh. Both conventional and next-gen geothermal LCOE are on par with nuclear and PV + storage.
Oil & gas expertise in advanced drilling, subsurface exploration, and modular plant design is accelerating cost declines. Solar PV, batteries, and EVs saw similar cost declines through industry spillover and rapid deployment.
Policy support and de-risking tools (e.g., GRIF, insurance, grants) reduce early-stage risk, improve bankability, and crowd in private capital through blended finance and PPPs.
Estimated LCOE (levelized cost of energy) under NREL Advanced scenario, US$/MWh
Finance: Oil & gas transfer
Chart: 
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
 | 71.2824 | 69.6215 | 68.049 | 66.5566 | 65.1367 | 63.783 | 62.4896 | 61.2516 | 60.0646 | 58.9245 | 57.8278 | 56.7714 | 55.7524 | 54.7683 | 54.5704 | 54.3735 | 54.1775 | 53.9826 | 53.7886 | 53.5956 | 53.4035 | 53.2125 | 53.0223 | 52.8332 | 52.6449 | 52.4576 | 52.2713 | 52.0859 | 51.9014
 | 105.6428 | 92.775 | 83.5502 | 76.4939 | 70.8468 | 66.1741 | 62.2071 | 58.7699 | 55.742 | 53.038 | 50.5951 | 48.3663 | 46.3157 | 44.4152 | 44.261 | 44.1077 | 43.9551 | 43.8033 | 43.6522 | 43.5019 | 43.3524 | 43.2036 | 43.0555 | 42.9082 | 42.7616 | 42.6158 | 42.4707 | 42.3263 | 42.1826
 | 68.9255 | 68.9255 | 68.9255 | 68.9255 | 68.9255 | 68.9255 | 68.9255 | 68.9255 | 68.9255 | 66.943 | 64.9604 | 62.9778 | 60.9953 | 59.0127 | 57.4267 | 55.8406 | 54.2545 | 52.6685 | 51.0824 | 50.2894 | 49.4964 | 48.7034 | 47.9103 | 47.1173 | 46.7208 | 46.3243 | 45.9278 | 45.5312 | 45.1347
 | 78.2475 | 78.2475 | 78.2475 | 78.2475 | 77.7901 | 77.3175 | 76.8601 | 76.3875 | 75.9302 | 73.8042 | 73.4078 | 72.9962 | 72.5998 | 72.2034 | 71.807 | 71.4106 | 70.999 | 70.6026 | 70.2062 | 67.4388 | 67.4388 | 67.4388 | 67.4388 | 67.4388 | 67.4388 | 67.4388 | 67.4388 | 67.4388 | 67.4388
 | 87.7439 | 88.6678 | 81.3381 | 74.1573 | 70.7099 | 67.3322 | 64.0217 | 60.7762 | 57.5945 | 54.9084 | 52.2738 | 49.6888 | 47.1529 | 44.6645 | 44.1811 | 43.7004 | 43.2222 | 42.7465 | 42.2731 | 41.8024 | 41.3343 | 40.8684 | 40.4046 | 39.9435 | 39.4847 | 39.0283 | 38.5739 | 38.1221 | 37.6728
0
10
30
40
50
60
70
80
90
100
110
20
45
38
Geothermal - Conventional Flash
Geothermal - Deep EGS Flash
Nuclear - Large Scale
Hydropower
Solar - Utility PV + Storage
67
Advanced projections suggest next-gen EGS may achieve lower costs than conventional geothermal and be competitive with nuclear and PV + storage as early as 2029.

## Slide 20: Geothermal offers reliable, low-footprint baseload energy, though costs and longer timelines may constrain scale-up
Deployment: Baseload power
 | Geothermal | Hydro | Nuclear | Wind | Solar
Resource availability & scalability | Scalable in select locations, high upfront costs, deep drilling needed | Limited scalability due to size (smaller hydro projects more feasible vs. larger dams) | Limited scalability due to high investments and long construction times (SMR easier to scale as modular alternative) | Highly scalable anywhere due to modular deployment | Highly scalable anywhere, due to modular deployment
Costs (LCOE) | $66-$109/MWh | $47/MWh | $141-$228/MWh (new plants) | $37-$86/MWh (onshore), $70-$157/MWh (offshore) | $38-$78/MWh (utility scale)
Capacity factor | 70-90% | Variable (global avg. is around 44%) | ~90% | 38-47% for onshore, 41-50% for offshore | 25-33% for standalone systems
Reliability | Reliable baseload resources | Baseload resource only with reservoir storage | Reliable baseload resources | Intermittent, variable output | Intermittent, energy storage required
Setup time | Moderate timeline, typically 3-5 years | Long timeline, often 5-10 years or more | Longest timeline, often 10+ years due to regulatory & construction complexities | Relatively quick to deploy, often within 1-2 years | Relatively quick to deploy, often within 1-2 years
Technology readiness | Established but room for significant advancements (e.g., EGS) | Mature, limited room for improvement | Established but challenges in cost reduction & public accept. | Mature, ongoing innovations improving efficiency & reducing costs | Mature, ongoing innovations improving efficiency & reducing costs
Land-use footprint efficiency (km2/TWh/year) | 7.5 | 54.0 | 2.4 | 72.1 | 36.9
Despite its higher LCOE and longer development timeline — especially compared to wind and solar — geothermal remains a highly competitive energy source in regions with significant geological activity, offering high reliability and efficient land use.
More desirable
Moderate
More challenging

## Slide 21: Increasing U.S. energy demand, largely driven by data centers, requires increased baseload supply of power
Projected growth in power demand from U.S. data centers
Incremental firm capacity by 2030
Observations
Data centers could add more than 35 to 65 GW of firm power demand by 2030 in the U.S., equivalent to a large fraction of today’s existing nuclear fleet.
Nuclear restarts and SMRs provide only ~4 GW incremental capacity, which is meaningful but insufficient against projected demand growth.
Grid-connected geothermal adds 6 to 8 GW, but that is also insufficient against projected demand.
Behind-the-meter geothermal (~15 GW) could directly supply data centers, bypassing grid constraints and permitting bottlenecks.
Innovation in drilling and permitting will determine whether geothermal can scale fast enough to complement nuclear in delivering zero-carbon baseload.
Deployment: Data centers
Chart: 
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
 | 5.7078 | 6.8493 | 7.9909 | 9.1324 | 11.4155 | 13.6986 | 17.1233 | 20.5479 | 25.1142 | 29.6804 | 34.2466
 | 66.21
 | 37.1005
High case: +65 GW
Low case: +35 GW
LBL Low Demand 2030 (GW)
Historic Demand (GW)
LBL High Demand 2030 (GW)
Chart: 
 | 4 | 6 | 15
 | 2
Nuclear
Geothermal
Next-Gen Geothermal
New Available GW
8
Nuclear restarts + early SMRs
Grid upside
Behind the meter

## Slide 22: Leveraging oil & gas capabilities can drive down geothermal power costs and accelerate deployment
Deployment: Oil & gas transfer
Problem | Current Challenge | Oil & Gas Synergy | Limitations | Case Example
Resource Identification | Accurate geothermal resource identification and modeling require multi-parameter surface data (seismic, geology, heat flow, permeability). | Oil & gas surface imaging and drilling data reduce exploration risk and improve reservoir targeting. | Legacy O&G datasets often lack thermal gradient resolution or long-term heat recharge data. | Hungary and The Netherlands: Open oil & gas subsurface databases reduce geothermal exploration costs and uncertainty.
Skilled Workforce Needs | Skilled workforce shortages in reservoir engineering and well completion delay project scaling. | Oil & gas professionals have skills that can apply to geothermal exploration, development, and operation. | Current policy frameworks provide limited financial incentives for geothermal workforce transfer. | DOE Geothermal from O&G Initiative: Demonstrates feasibility of cross-sector workforce and skill transfer.
Drilling Costs | Subsurface drilling represents 60 to 80% of total next-generation geothermal CapEx. | Hydrocarbon well technology (e.g., horizontal drilling, multi-stage stimulation) can be directly transferred to EGS. | Geothermal wells require sustained reinjection and higher temperature tolerance than oil & gas operations. | Fervo Energy’s Project Red: Achieved record flow rates by adapting shale fracking and fiber-optic monitoring.
Co-production and Well Repurposing | High initial exploration, drilling, and completion costs can be a limiting factor in geothermal projects. | Co-production or heat extraction from abandoned wells can de-risk geothermal projects. | Wells require a large heat gradient and flow rate, flexible permitting, and proximity to demand. | Zanskar Project (U.S.): AI-driven reservoir modeling revitalized legacy wells, cutting exploration risk by >50%.
Level of shared competencies

## Slide 23: Geothermal faces structural barriers across permitting, transmission, and interconnection, but new pathways are beginning to unlock deployment
Deployment
02.
01.
03.
04.
05.
Complex, multilayer permitting slows development, with dual federal-state reviews and sensitive-resource checks extending timelines far more than for wind and solar.
High upfront exploration costs increase financial risk, with $5-$10M for site characterization and up to $450M for full next-gen resource confirmation before PPAs are secured.
PPA uncertainty constrains bankability, since geothermal requires large sunk costs before revenue agreements are locked in.
The interconnection queue structurally disadvantages long-lead clean firm resources, with 95% of queued capacity coming from solar, wind, and storage.
Transmission distance and interconnection costs erode project economics, as remote resources face expensive upgrades and long IQ delays.
02.
01.
03.
04.
05.
Behind-the-meter deployment offers a near-term geothermal pathway, allowing industrial loads and data centers to bypass interconnection entirely.
BLM emergency permitting creates faster federal approval routes, with 14-day reviews for select geothermal activities.
Streamlined permitting practices, including tiering, MOUs, and integrated reviews, can materially reduce delays without weakening environmental rigor.
Next-generation geothermal (EGS, closed-loop) expands the viable subsurface resource base, reducing dependence on rare hydrothermal conditions.
Federal tax credits, DOE’s Enhanced Geothermal Shot, plus a goal to reduce EGS costs 90% by 2035 improve project economics, supporting early commercial deployment.
Structural barriers facing geothermal
Emerging pathways that can improve geothermal deployment

## Slide 24: Team

## Slide 25
Zacharia Thurston
MS in Sustainability Management
Team Lead | Climate Knowledge Initiative Fellow
Pia Doris Morrow
MS in Sustainability Management
Team Co-lead | Climate Knowledge Initiative Fellow
Sevgi Helin Tilkicioglu
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Heather Hartel
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Stephanie Chen
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Shubhangi Prasad
Master of Public Administration
Climate Knowledge Initiative Fellow
Faradisa Anintya
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Una Oljaca
BA in Economics, Political Sciences, and Government
Climate Knowledge Initiative Fellow
CKI Geothermal Team
Fellows (1/2)

## Slide 26
Thomas Smith
MBA, Columbia Business School
Climate Knowledge Initiative Fellow
Leo Gordon
MPA, Columbia SIPA
Climate Knowledge Initiative Fellow
CKI Geothermal Team
Fellows (2/2)

## Slide 27
Hyae Ryung (Helen) Kim
PhD in Sustainable Development
Former Senior Research Fellow
CKI Team Staff, Faculty, and Alumna
Share with attribution: Wagner et al. “Geothermal Power,” Columbia Business School Climate Knowledge Initiative (10 March 2026).